ZMON V2.00 DOCUMENTATION


MONITOR FUNCTION CALLS:
	These functions are executed by placing the arguments into the
   proper registers and executing a Restart 20H, or by calling location
   F806H.

Arguments:
	A= Function #
	BC= Arg #1
	DE= Arg #2
	HL= Arg #3
	E:HL= Banked memory ptr

Return Values:
	A= Byte
	HL= Word
	BC, DE= Additional values


Function descriptions:

RETURN MONITOR ROM VERSION #
	ENTRY-	A= 0
	EXIT -	HL= BINARY VERSION # IN HUNDREDTHS (X.XX)

***  MEMORY MANAGEMENT  ***
RETURN BANKED MEMORY DATA
	ENTRY-	A= 1
		E:HL= PTR TO DATA LOCATION
	EXIT -	A= DATA FROM LOCATION

STORE BANKED MEMORY DATA
	ENTRY-	A= 2
		E:HL= DATA PTR
		C= DATA TO STORE INTO LOCATION

SELECT MEMORY BANK FOR EXECUTION
	ENTRY-	A= 3
		C= BANK #

SELECT MEMORY BANKS FOR MOVE
	ENTRY-	A= 4
		B= SOURCE BANK #
		C= DESTINATION BANK #

BANK BLOCK MOVE
	ENTRY-	A= 5
		HL= SOURCE PTR
		DE= DESTINATION PTR
		BC= BYTE COUNT
	EXIT -	HL= LAST SOURCE BYTE PTR + 1
		DE= LAST DESTINATION BYTE PTR + 1
		BC= 0

EXECUTE BANK
	ENTRY-	A= 6
		E':HL'= PTR TO EXECUTION CODE


	*** Character I/O Device Functions ***

RETURN CHAR DEVICE VERSION #
	ENTRY-	A= 7
		D= 0
	EXIT -	HL= BINARY VERSION # IN HUNDREDTHS (X.XX)

RETURN CHAR DEVICE PARAMETERS
	ENTRY-	A= 7
		D= 1
		B= DEVICE # {0..15}, -1, -2}
		E:HL= PTR TO LOCATION TO PLACE DATA
	EXIT -	A= 0: DEVICE NOT PRESENT
		  /0: BUFFER CONTENTS (BY OFFSET)
			(0)= 6 CHAR ASCII LOGICAL DEVICE NAME
			(6)= MODE BITS:
				D0= 1: INPUT DEVICE
				D1= 1: OUTPUT DEVICE
				D2= 1: SELECTABLE BAUD RATE
				D3= 1: XON PROTOCOL OK
				D4= 1: XON/XOFF ENABLED
			(7)= BAUD RATE INDEX INITIALIZED TO

EXECUTE SELF TEST IF APPLICABLE
	ENTRY-	A= 7
		D= 2
		B= DEVICE # {0..15}, -1, -2}
	EXIT -	A= 0: OK, /0: ERROR CODE

SET STANDARD CONSOLE DEVICE
	ENTRY-	A= 7
		D= 3
		B= DEVICE # TO SET TO {0..15}, -1, -2}
	EXIT -	A= 0..15: PREVIOUS DEVICE
		   -1: ILLEGAL DEVICE

SET STANDARD LIST DEVICE
	ENTRY-	A= 7
		D= 4
		B= DEVICE # TO SET TO {0..15}, -1, -2}
	EXIT -	A= 0..15: PREVIOUS DEVICE
		   -1: ILLEGAL DEVICE

INITIALIZE CHAR DEVICE
	ENTRY-	A= 7
		D= 5
		B= DEVICE # {0..15}, -1, -2}

SET DEVICE BAUD RATE
	ENTRY-	A= 7
		D= 6
		B= DEVICE # {0..15}, -1, -2}
		C= BAUD RATE INDEX {0: NONE, 1..15}
	EXIT -	A= 0..15: PREVIOUS BAUD RATE INDEX
		   FFH: ILLEGAL BAUD RATE


	*** Disk I/O Driver Functions ***

RETURN DISK DRIVER VERSION #
	ENTRY-	A= 8
		D= 0
	EXIT -	HL= BINARY VERSION # IN HUNDREDTHS (X.XX)

BOOT DISK
	ENTRY-	A= 8
		D= 1
		BC= PHYSICAL DRIVE #
		    BITS 2..0= ROM #
		    3= 0
		    7..4= DRIVE #
		   15..8= CONTROLLER #  
	EXIT -	ERROR, WILL NOT RETURN IF SUCCESSFUL

TEST IOPB.PBSTATO FOR ERROR AND DUMP IOPB IF TRUE
	ENTRY-	A= 8
		D= 2
		E:HL= IOPB PTR
	EXIT -	AF= 0: NO ERROR, /0: ERROR CODE

DISPLAY IOPB ERROR DATA
	ENTRY-	A= 8
		D= 3
		E:HL= IOPB PTR
	EXIT -	AF= 0: NO ERROR, /0: ERROR CODE

EXECUTE IOPB
	ENTRY-	A= 8
		D= 4
		E:HL= IOPB PTR
	EXIT -	AF= 0: NO ERRORS, /0: ERROR CODE


	*** Miscellaneous I/O Driver Functions ***

RETURN MISCELLANEOUS DRIVER VERSION
	ENTRY-	A= 9
		D= 0
	EXIT -	HL= BINARY VERSION # IN HUNDREDTHS (X.XX)

READ CLOCK BUFFER
	ENTRY-	A= 9
		D= 1
		E:HL= PTR TO 13 BYTE BUFFER TO PLACE DATA

WRITE CLOCK BUFFER
	ENTRY-	A= 9
		D= 2
		E:HL= PTR TO 13 BYTE BUFFER TO SET CLOCK FROM

RETURN CLOCK CALENDAR DATA
	ENTRY-	A= 9
		D= 3
	EXIT -	A= DAY
		B= MONTH
		C= YEAR
		L= DAY OF WEEK (0= SUNDAY, 1= MONDAY..)

RETURN CLOCK TIME DATA
	ENTRY-	A= 9
		D= 4
	EXIT -	A= SECONDS
		B= MINUTES
		C= HOURS

RETURN CLOCK REGISTER DATA
	ENTRY-	A= 9
		D= 5
		L= REGISTER #
	EXIT -	A= DATA FROM CLOCK REGISTER

WAIT FOR CLOCK TO CHANGE. DOES NOT RETURN UNTIL CLOCK SECONDS CHANGE.
	NOTE: INSURE BOARD IS IN SYSTEM WITH FUNCTION #7 BEFORE
		INVOKING, OTHERWISE, THE SYSTEM WILL 'HANG'!
	ENTRY-	A= 9
		D= 6

RETURN CLOCK BOARD PRESENT STATUS
	ENTRY-	A= 9
		D= 7
	EXIT -	A= 0: NOT IN SYSTEM, /0: BOARD IN SYSTEM

STOP CLOCK
	ENTRY-	A= 9
		D= 8

START CLOCK
	ENTRY-	A= 9
		D= 9