RBBS/RTPM (BULLETIN BOARD) INSTALLATION

         
         This method can be used to install a standard RBBS,   however
         the TPM II/VALDOCS system should work with little conflict.
         
         If you are using this as a standard RBBS,  evoke  QXBULLA.SYS
         and use that to SYSGEN the RBBS System  on to the LEFT Floppy 
         diskette drive. If you are planning to use a HARD DISK, place
         it on both the LEFT floppy diskette and A: Drive  of the hard
         disk.  Evoke QXBULLB and sysgen to B: Drive (either the RIGHT 
         floppy disk or the hard disk B: Drive, not both).
         
         This version of bulletin board places all files accessible by
         callers on A100:, the ONLY User level callers can have access
         to on the A: Drive. This allows having a normal system setup,
         with all of your popular files located on A0:, where they can
         not be accessed by a caller.
         
         Place the Bulletin Board files at user level A100: before you
         set up any other files on the A: Drive. This will make search
         for the Bulletin Board files much faster.  NOTE: BYE.SYS MUST
         BE ON BOTH A0: AND A100:!  The system accesses the BYE.SYS on
         A0:, the caller uses BYE.SYS at A100:.
         
         Set up of the A: Drive diskette should be done in the follow-
         ing sequence to achieve the best access time:
         
            Drive  Install
         
            A100:  BYE.SYS
            A0:    BYE.SYS, SECRET.CTL, and RUBBSTL.SYS protect all at
                   level <6>
         
                   RUBBSTL.SYS is for the SYSOPerator's use for purges
                   and archiving of message files and is not necessary
                   to operate an RBBS. There is a limit of 200 message
                   records and this program is good house keeping.
         
            A100:  RIBBS.SYS, XMODEM.SYS, BELL.SYS, LIST.SYS,  SD.SYS,
                   DSTAT.SYS, CRCK.COM,  and HOW2USE.DOC. or HELP.
         
                   During LOGON the system will refer to HOW2USE.DOC
                   You can make up your own HELP., and CHAT.COM can be
                   an added enhancement for callers to alert the SYSOP
                   that they want to chat.
         
            A254:  BULLETIN. and INFO.
         
                   These are system bulletins for callers to read when
                   they access the RBBS.  Neither BULLETIN or INFO are
                   necessary for operation. Alterations to BULLETIN or
                   INFO files can be performed by the SYSOP.
         
Š                   Files generated by RIBBS; COUNTERS, SUMMARIES files
                   that contain all messages and history of the users,
                   are also located at this level.
                   
         This RBBS system uses both the A: and B: drives and looks for
         TPM system tracks with modifications on BOTH DRIVES. A: Drive
         TPM System has a modified PIOS module to COLD START with BYE.
         SYS rather than INITIAL.INI. The B: Drive system has modified
         the ICP module to prevent execution of certain commands.
         
         Be sure that you are using a full RS232 modem cable.  BYE.SYS
         performs direct interrogation of the carrier detect line  and
         a 3 wire cable is insufficient.
         
         Anytime the system is RESET, BYE.SYS executes and initializes
         the Smartmodem and  "Waiting for phone to ring...."  displays
         on monitor screen. If the message begins scrolling, the modem
         is either not properly plugged in or not turned "ON".
         
         When the phone rings,  the BYE program receives and tests the
         initial password, then switches the "BOOT" drive to B: Drive.
         The switch is located in the PIOS, at location PIOS+6AH. This
         is 0E86AH in the current version of the system.   That causes
         the modified ICP to be executed on a warm boot.  BYE.SYS then
         "chains" to RIBBS.SYS using the TPM chain function.
         
         RIBBS.SYS now takes control of the system.  Upon EXIT to TPM,
         RIBBS.SYS performs the warm boot and the active ICP is on B:.
         This is the special bulletin board modified version. The user
         exits to what appears to be A0:, but is actually A100:. Users
         may not access any other User Levels on A:.
         
         When BYE is typed, a signoff message is sent,  the system re-
         initializes to wait for another call.  If the carrier is lost
         during operation, an automatic chain to BYE.SYS is made. NOTE
         that there are currently no time-outs in this system.   It is
         possible to have someone not hang up, which leaves the system
         unaccessable or "BUSY".
         
         Anytime the system is waiting for a telephone inquiry,  SYSOP
         may enter a [CTRL] [C] and control will be returned to normal
         keyboard operation.  At that time PIOS is temporarily patched
         so the full TPM-II operation is available.  To set it back up
         as a Bulletin Board, just type BYE.
         
         The SYSOP has extra privleges not available to other callers.
         Type [CTRL] [C] to exit to TPM.   Evoke RIBBS F and log on as
         SYSOP;TWL.  If you respond to the "Function" prompt with [%],
         you can print out a list of callers. If, however your printer
         is attached and "ON" during operation,  logons are printed as
         they occur.