BANK SWITCHING  - Tony Drake    1/83

         Bank switching is a hardware/software technique used in the Kaypro�
         (and other microcomputers) to allow additional memory to be�
         accessible. Under usual conditions, the Z80 microprocessor can�
         directly address 64K (65,536) bytes of memory. When the�
         bank-switch capability has been built in to the computer, as it�
         has in the Kaypro, new segments of memory, called "banks", can be�
         switched in over the top of old segemnts, used for a while, then�
         the old segments can be returned without "forgetting" anything.�
         The Kaypro has one bank of 16K bytes that can be switched in and�
         out. The normal, unswitched bank is called BANK 0. The optional,�
         switched bank is called BANK 1.

         Non-Linear Systems (NLS) did not put user memory in BANK 1. The�
         first 2K bytes consists of preprogrammed, permanent memory (ROM)�
         containing special system routines that are used to control the�
         keyboard, the screen, the disk drives, and the serial and parallel�
         ports. The CP/M operating system uses these routines extensively�
         in running the computer. A programmer can use these routines to�
         his advantage if he wishes to learn how.

         NLS did not put any memory in the next 10K of this bank. A program�
         written to "read" any of this 10K would find it empty.

         The last 4K of this bank contains the video display memory. Any�
         character codes written in this memory automatically show up on�
         the screen in a corresponding position. This is called�
         memory-mapped video. Normally, system routines (in BANK 1) are�
         used to control screen displays, but again, a programmer can write�
         directly to the screen memory if he wishes.

         Switching BANK 1 with BANK 0 is easy to do, but the programmer�
         must not forget which bank is currently "on". The switch is made�
         by turning on bit 7 of the system port. Bits are numbered from�
         right to left, starting with bit 0, so the bank-switch bit is the�
         "highest", or most significant bit (MSB) of the system port. The�
         other bits of the system port are unrelated to bank switching and�
         must not be altered when making the switch. The system port is�
         found at port address 1C (hexidecimal). Using INTEL 8080 Assembly�
         language, the switch to BANK 1 can be made with three�
         instructions:
                 IN   1CH         ;INPUT CURRENT SYSTEM PORT DATA
                 ORI  80H         ;TURN ON HIGH BIT
                 OUT  1CH         ;OUTPUT NEW SYSTEM PORT DATA

         Similarily, in ZILOG Z80 Assembly language:
                 IN   A,(1CH)     ;INPUT CURRENT SYSTEM PORT DATA
                 SET  7,A         ;TURN ON HIGH BIT
                 OUT  (1CH),A     ;OUTPUT NEW SYSTEM PORT DATA

         To switch back to "normal" BANK 0 using INTEL 8080 Assembly�
         language:
                 IN   1CH         ;INPUT CURRENT SYSTEM PORT DATA
                 ANI  7FH         ;TURN OFF HIGH BIT
                 OUT  1CH         ;OUTPUT NEW SYSTEM PORT DATA

         To switch back to "normal" BANK 0 using ZILOG Z80 Assembly�
         language:
                 IN   A,(1CH)     ;INPUT CURRENT SYSTEM PORT DATA
                 RES  7,A         ;TURN OFF HIGH BIT
                 OUT  (1CH),A     ;OUTPUT NEW SYSTEM PORT DATA

         The programmer must be sure that his bank switch instructions are�
         not in the first 16K of memory, since this memory is switched�
         "out" when BANK 1 is switched "in". (With the instructions�
         switched out, the machine won't know how to get back to BANK 0.)

         The program SYSCOPY uses bank switching to copy the system ROM�
         routines out of BANK 1 into normal memory. Here they can more�
         easily be studied by disassembling with DDT.

         The program VIDEO uses bank switching to write directly to the�
         video memory. All hexidecimal codes from 00 to 7F are written to�
         demonstrate the entire displayable character set.