TEAC 55-GFR

D0, D1, D2, D3  These give the drive address in a daisy chain configuration.

U0, U1          Used to select turn-on condition of front bezel light (see

below).

IU              Jumper to make the signal interface terminal 4 be used

for the IN-USE input signal. When strap is removed, the

input circuit is open and the IN-USE signal ineffective.

ML              Selects spindle action according to host command. When

open, spindle rotates only by MOTOR ON input signal. When

jumper is ON motor rotates when (a) MOTOR ON input signal

is TRUE (b) front bezel indicator turns on.

RY/DC           Used to select function of READY/DISK CHANGE signal on

terminal 34. When RY jumper ON signal on terminal 34 functions

as ready signal, and it functions as DISK CHANGE signal when

the DC jumper is ON.

LG              Used to select meaning of HIGH/NORMAL DENSITY input

signal. When on, LOW level of HIGH/NORMAL DENSITY signals

high density mode. When off, LOW level of HIGH/NORMAL DENSITY

signal designates normal density mode.

I and IS        Used to select speed of drive. I strap on: dual speed mode

designated. (360 rpm High Density, 300 rpm Low Density).

Ready state reset once synchronizing with a level change of

the HIGH/NORMAL DENSITY signal. Both I and IS OFF, single

speed mode designated. Speed is 360 rpm regardless of

HIGH/NORMAL DENSITY signal. Both I and IS on, dual speed

mode is activated but FDD remains in ready state, regardless of

level change of HIGH/NORMAL DENSITY signal.

E2              Selects output condition of INDEX and READ DATA pulses. When OFF

pulses are output as in (DIAGRAM NOT SUPPLIED). When ON, output

conditions changed to logical expression as follows:

INDEX: Index hole detection * DRIVE SELECT * Ready state

READ DATA: Read data detection * DRIVE SELECT * Ready State *!Write

FG              Connects FDD frame to DC 0V.

Front Bezel Indicator

Selection         Jumper Combo.                Indicator turn-on condition

1                *        *        *        Drive select

2                IU       *        U1       Drive select + in-use

3                IU       U0       *        In use

4                *        U0       U1       Drive select + ready

5                IU       U0       U1       In use + (drive select * ready)

Notes

Selection

1        Indicator tuns on when DRIVE SELECT signal TRUE

2        Indicator turns on while DRIVE SELECT signal is TRUE or

IN USE signal TRUE

3        Indicator on while IN USE signal TRUE

4        Indicator on when DRIVE SELECT signal TRUE and FDD in ready state.

5        Indicator turns on, on conditions 3 or 4