1
	  		/*****PROGRAM MAGTAP.PAL,   1969*****
	  		/HOWARD SHAPIRO* AND PETER LEMKIN**
	  		/
	  		/
	  		/ **NATIONAL INSTITUTES OF HEALTH
	  		/   BETHESDA, MD. 20014
	  		/
	  		/
	  		/SUBMITTED BY PETER LEMKIN
	  		/
	  		/
	  		/INTRODUCTION:
	  		/-------------
	  		/AN INPUT/OUTPUT DEVICE HANDLER IS GIVEN BELOW FOR THE 
	  		/TU20/TC58 MAGNETIC TAPE DRIVE AND CONTROLLER FOR THE PDP8.
	  		/IT ENABLES THE READING, WRITING, READ-COMPARING, ADVANCING AND
	  		/BACKSPACING RECORDS, AND WRINTING END OF FILES. IT ALSO LETS
	  		/THE PROGRAMMER INTERROGATE THE MAGTAPE CONTROLLER ABOUT THE STATUS
	  		/OF THE DRIVE/CONTROLLER . THE MAGTAPE ROUTINE WAS ORIGINALLY WRITTEN
	  		/BY HOWARD SHAPIRO AND LATER MODIFIED FOR INTER FIELD OPERATION BY
	  		/PETER LEMKIN.
	  		/
	  		/
	  		/
	  		/DESCRIPTION:
	  		/--------------
	  		/THE MAGTAPE INPUT/OUTPUT HANDLER SUBROUTINE FOR THE
	  		/TC58 AND TU20  ON A PDP8 WAS ORIGINALLY
	  		/WRITTEN BY HOWARD SHAPIRO AND MODIFIED BY
	  		/P. LEMKIN.  THE HANDLER ENABLES THE USER TO READ, WRITE 
	  		/READ-COMPARE, SPACE BACKWARD OR FORWARD, REWIND , OR
	  		/WRITE END OF FILE. IT IS ASSEMBLED UNDER PAL10 OR PAL8.
	  		/THE CALLING SEQUENCE IS:
	  		/	JMS MAGTAP
	  		/	N1	/OR # OF WORDS IN READ/WRITE, # RECORDS IN SPACING.
	  		/	N2	/STARTING CORE ADDRESS FOR READ/WRITE
	  		/	N3	/COMMAND....SEE TABLE BELOW
	  		/	N4	/DATA FIELD FOR READ/WRITE 00, 10, OR 20. ETC.
	  		/	NORMAL RETURN
	  		/
	  		/::::::COMMAND TABLE::::::
	  		/	NOP		00
	  		/	REWIND		10
	  		/	READ		20
	  		/	READ-COMPARE	30
	  		/	WRITE		40
	  		/	WRITE END FILE  50
	  		/	SPACE FORWARD   60
	  		/	SPACE BACKWARD  70
	  		/
	  		/
	  		/COMMAND WORD DEFINITIONS:
	  		/------------------------------
	  		/THE COMMAND WORD SPECIFIES WHAT TYPE OF DRIVE AND TAPE FORMAT
	  		/IS TO BE USED IN THE TAPE INSTRUCTIONS. THE FOLLOWING WILL



								2
	  		/ALLOW THE USER TO CONFIGURE THE HANDLER FOR HIS DRIVE.
	  		/SEE THE SMALL COMPUTER HANDBOOK (DEC) 1970 FOR SPECIFICS PP 118,119.
	  		/CURRENTLY THE HANDLER IS CONFIGURED FOR A 9 TRACK, ODD PARITY, 800BPI
	  		/CORE DUMP MODE, UNIT 0, INTERRUPT DRIVEN HANDLER.
	  		/
	  	0003		DENSTY=3 /800=3
	  	0200		CORDMP=200 /0 IF NO COREDUMP
	  	0004		ENBINT=4 /ENABLE INTERRUPT. 0 IF DISABLED.
	  	0400		PARITY=400 /0 IF EVEN, 400 IF ODD.
	  	0000		EXTGAP=0 /100 IF EXTENDED GAP, 0 IF NONE.
	  	0000		UNIT=0 /0 TO 7000 , UNIT #
	  	0001		RINTSO=1 /RUN WITH INTERRUPTS OFF=0, IF ON=1.
	  		/
	  		/THE COMMAND WORD IS THEN CONSTRUCTED.
	  		/
	  	0607		CMDWRD=UNIT+PARITY+CORDMP+EXTGAP+ENBINT+DENSTY
	  		/
	  		/
	  		/
	  		/
	  		/OPERATING INFORMATION:
	  		/-----------------------
	  		/THE USER MUST SUPPLY HIS OWN INTERRUPT ROUTINE IN ORDER
	  		/TO OPERATE WITH THIS PACKAGE IF USED WITH INTERRUPT MODE.
	  		/THIS ROUTINE SHOULD GENERATE A JMS TO SUBROUTINE TINT UPON
	  		/DETECTION OF AN INTERRUPT FROM THE TAPE  UNIT VIA THE 
	  		/MTSF=6701  INSTRUCTION ( SKIP ON TAPE INTERRUPT).
	  		/ THERE ARE 5 ROUTINES OF INTERREST:
	  		/1. SUBROUTINE MAGTAP IS USED TO DO I/O.
	  		/2. SUBROUTINE TNTX IS USED TO TEST THE TAPE STATUS
	  		/   AFTER AN INTERRUPT.
	  		/3. SUBROUTINE TINT IS USED TO SERVICE AN INTERRUPT 
	  		/4. SUBROUTINE WTRDY IS USED TO WAIT UNTIL THE
	  		/   TAPE UNIT IS READY.
	  		/5. SUBROUTINE GOTAPE IS USED BY MAGTAP TO EXECUTE THE TAPE COMMAND.
	  		/
	  		/&
	  	6711	MTCR=6711
	  	6701	MTSF=6701
	  	6721	MTTR=6721
	  	6712	MTAF=6712
	  	6716	MTLC=6716
	  	6722	MTGO=6722
	  	6706	MTRS=6706
	  		/
	  0200	0000	MAGTAP,	 0 /9 TRACK TAPE ROUTINE
	  0201	7200		CLA
	  0202	6214		RDF
	  0203	1235		TAD LCIF
	  0204	3232		DCA LLX
	  0205	4236		JMS WTRDY /WAIT READY
	  0206	7200		CLA /TRANSMIT N1
	  0207	1600		TAD I MAGTAP
	  0210	7041		CIA
	  0211	3700		DCA I WCLOC



								3
	  0212	2200		ISZ MAGTAP
	  0213	7240		STA  /TRANSMITT N2
	  0214	1600		TAD I MAGTAP
	  0215	3701		DCA I CALOC
	  0216	2200		ISZ MAGTAP
	  0217	1600		TAD I MAGTAP /FORM COMMAND WITH N3
	  0220	1234		TAD CCMD /GET MASK
	  0221	3227		DCA TN1 /SAVE COMMAND
	  0222	2200		ISZ MAGTAP
	  0223	1600		TAD I MAGTAP /GET N4 THE BUFFER FIELD
	  0224	3230		DCA TN2
	  0225	6201		CDF 00
	  0226	4252		JMS GOTAPE /EXECUTE
	  0227	0000	TN1,	 0
	  0230	0000	TN2,	 0 /DATA FIELD ARG FOR GOTAPE
	  			IFZERO RINTSO </RUN WITH INTERRUPTS OFF
	  				        JMS WTRDY /WAIT FOR THE TAPE TO FINISH
	  					JMS TINT /FAKE SERVICING IT.
	  					>
	  0231	2200		ISZ MAGTAP
	  0232	6202	LLX,	 CIF 00
	  0233	5600		JMP I MAGTAP /RETURN
	  0234	0607	CCMD,	CMDWRD / COMMAND MASK
	  0235	6202	LCIF,	 CIF 00
	  		/
	  		/
	  		/
	  		/
	  		/SUBROUTINE WTRDY
	  		/IS USED TO WAIT UNTIL THE MAGTAPE IS READY.
	  		/CALLING SEQUENCE:
	  		/	JMS WTRDY
	  		/	NORMAL RETURN /TAPE UNIT READY
	  		/&
	  0236	0000	WTRDY,	 0 /WAIT TAPE READY
	  0237	7200		CLA
	  0240	6214		RDF
	  0241	1235		TAD LCIF
	  0242	3250		DCA WT1
	  0243	6201		CDF 00
	  0244	6711	WTLP2,	MTCR /IS THE CONTROL READY?
	  0245	5244		JMP WTLP2 /NO
	  0246	6721		MTTR /IS THE DRIVE READY?
	  0247	5244		JMP WTLP2 /NO
	  		/YES TO BOTH******
	  0250	6202	WT1,	 CIF 00
	  0251	5636		JMP I WTRDY /RETURN
	  		/
	  		/
	  		/
	  		/
	  		/SUBROUTINE GOTAPE
	  		/IS CALLED BY MAGTAP TO EXECUTE THE TAPE COMMAND.
	  		/CALLING SEQUENCE:
	  		/	JMS GOTAPE 



								4
	  		/	COMMAND 
	  		/	DATA FIELD
	  		/	NORMAL RETURN
	  		/&
	  0252	0000	GOTAPE,	 0 /PERFORM TAPE OPERATION
	  0253	6712		MTAF /CLEAR TAPE CONTROL REGS
	  0254	1652		TAD I GOTAPE /GET COMMAND
	  0255	6716		MTLC /LOAD COMMAND
	  0256	7200		CLA
	  0257	2252		ISZ GOTAPE
	  0260	7200		CLA
	  0261	1652		TAD I GOTAPE /GET DATA FIELD
	  			IFNZRO RINTSO <
	  0262	6001		ION /TURN ON INTERRUPT
	  			>
	  0263	6722		MTGO /GO ALREADY
	  0264	2252		ISZ GOTAPE
	  0265	5652		JMP I GOTAPE /RETURN
	  		/
	  		/
	  		/
	  		/SUBROUTINE TINT
	  		/IS USED TO SERVICE THE MAGTAPE INTERRUPT.
	  		/IT SAVES THE STATUS OF THE MAGTAP  AT THE TIME OF
	  		/INTERRUPT AND CLEARS THE COMMAND AND INTERRUPT REGISTERS.
	  		/CALLING SEQUENCE:
	  		/	JMS TINT
	  		/	NORMAL RETURN
	  		/
	  		/&
	  0266	0000	TINT,	 0 /TAPE SERVICE ROUTINE CALLED
	  0267	7300		CLA CLL
	  0270	6706	TPSRVC,	 MTRS /GET TAPE STATUS
	  0271	3276		DCA TSTAT /STATUSS TO TSTAT
	  0272	6724		6724 /GET COMMAND REG
	  0273	3277		DCA TCOM /COMMAND TO TCOM
	  0274	6712		MTAF /CLEAR STATUS AND COMMAND REGS
	  0275	5666		JMP I TINT /RETURN
	  0276	0000	TSTAT,	 0 /HOLDS LAST STATUS
	  0277	0000	TCOM,	 0 /HOLDS LAST COMMAND
	  0300	7752	WCLOC,	 7752 /WORD COUNT LOCATION
	  0301	7753	CALOC,	 7753 /CURRENT ADDRESS LOCATION
	  		/
	  		/......................................................
	  		/
	  		/
	  		/SUBROUTINE TNTX
	  		/SENSE TAPE CONDITION - THIS ROUTINE IS CALLED BY THE USER
	  		/TO DETECT ERRORS, END OF FILE, BEGINNING OR END OF TAPE.  IN
	  		/ORDER FOR IT TO WORK PROPERLY, AN INTERRUPT MUST HAVE OC-
	  		/CURRED AND HAVE BEEN PROCESSED BY TINT.  HOWEVER, IF TNTX
	  		/IS CALLED WHILE THE TAPE IS STIILL BUSY, IT WILL WAIT FOR
	  		/TAPE TO BECOME READY, BY WHICH TIME AN INTERRUPT SHOULD
	  		/BE FIELDED.
	  		/CALLING SEQUENCE:



								5
	  		/        JMS TNTX
	  		/        N4
	  		/        CONTINUE HERE IF CONDITION HOLDS
	  		/        CONTINUE HEEE IF CONDITION DOES NOT HOLD
	  		/
	  		/ N4 SPECIFIES THE CONDITION SOUGHT AS FOLLOWS:
	  		/    N4     CONDITION
	  		/    ---    -----------
	  		/    0       FLATNESS OF EARTH (NOP)
	  		/    1       READ OR WRITE ERROR
	  		/    2       READ-COMPARE ERROR
	  		/    3       END FILE
	  		/    4       BEGINNING OF TAPE
	  		/    5       END OF TAPE
	  		/
	  		/&
	  0302	0000	TNTX,	 0
	  0303	7200		CLA
	  0304	6214		RDF
	  0305	1235		TAD LCIF
	  0306	3322		DCA TN3 /SAVE RETURN FLD
	  0307	4236		JMS WTRDY /WAIT TAPE READY
	  0310	7200		CLA
	  0311	1702		TAD I TNTX /FORM STATUS MASK ADDRESS
	  0312	6201		CDF 00
	  0313	1324		TAD TN4
	  0314	3325		DCA TN5
	  0315	2302		ISZ TNTX
	  0316	1276		TAD TSTAT /GET STATUS
	  0317	0725		AND I TN5 /AND WITH MASK
	  0320	7450		SNA /SKIP IF CONDITION HOLDS
	  0321	2302		ISZ TNTX /FIX RETURN IF CONDITION DOES NOT HOLD
	  0322	6202	TN3,	 CIF 00
	  0323	5702		JMP I TNTX /RETURN
	  0324	0326	TN4,	 TCOND /MASK LIST BASE ADDR.
	  0325	0000	TN5,	 0 /A OF MASK USED
	  0326	0000	TCOND,	 0 /MASKS FOR SENSE TAPE CONDIYION
	  0327	1616		1616 /READ OR WRITE ERROR
	  0330	1636		1636 /READ-COMPARE ERROR
	  0331	0100		0100 /EOF
	  0332	1000		1000 /BOT
	  0333	0040		0040 /EOT
	  		/HERE ENDETH THE 9 TRACK TAPE PACKAGE
	  		/
	  		/
	  		/............................................
	  			$