ACP Tutorial



 










                        ACP TUTORIAL








                      R. W. Stamerjohn

                         13-MAR-78








          This paper is for oral  presentation  at
          the  Spring,  1978  Decus  Symposium  in
          Chicago, IL on April 26, 1978.  It  will
          also  be published in the proceedings of
          the Symposium.  The paper  is  presented
          here for Monsanto corporate approval.

          The tutorial  deals  with  the  software
          components    of    Digital    Equipment
          Corporation  operating   systems   named
          Ancillary  Control  Processors  (ACP's).
          These  components  are  deeply  involved
          with  the  input/output mechanism of the
          IAS/RSX-11 operating  systems,  however,
          little  is  known  about  their internal
          workings.   The   paper   presents   the
          knowledge  we  have  gained  about ACP's
          while implementing the Monsanto  Digital
          Access Protocol.



ACP Tutorial                                          PAGE 2



1.0  INTRODUCTION [slide 01]


     Some of the  most  frequently  used  components  of  an
IAS/RSX-11   operating  system  are  the  Ancillary  Control
Processors (ACP's).  Yet the concept behind an ACP  and  the
various  ACP's perform and are implemented remain one of the
least understood portions of the  operating  systems.   This
tutorial  will attempt to shed some light on the subject and
provide a starting point for anyone considering implementing
an ACP.

     At Monsanto, we investigated the use of ACP's as a part
of  a  project  called  Monsanto's  Digital  Access Protocol
(MDAP).  The  MDAP  project  will  implement  Digital's  DAP
protocol between a DECsystem-10 and RSX-11M systems.  An ACP
will be used on the RSX-11M systems to provide  remote  file
access from the File Control Services (FCS).

     In this session today, we will present  what  we  haved
learned  about  ACP's.  The discussion will use RSX-11M V3.0
as a basis for any technical details.  While only a  cursory
examination of RSX-11M version 3.1 was made at the time this
presentation  was  prepared,  few  significate  changes  are
expected  in  the  new  release.   Users  of RSX-11D and IAS
should not assume these details will apply to their systems.
While  the  actual ACP's may be similar, our technical focus
will be on the environment an ACP is implemented within, not
the  internal  workings  of  any particular Digital supplied
ACP.

     The format of the session [slide 02] is  basically  the
same  as  the  outline given in the Symposium program guide.
We will first define "ACP" and  outline  the  attributes  of
current  ACP's.   Next,  The  relationship  of an ACP to the
other  IAS/RSX-11  I/O  components  will  be  examined.   In
particular,  the  discussion  will  cover  how  FCS  and the
Digital ACP's interact to  form  a  device  independent  I/O
mechanism.   We  will  then discuss how one determines if an
ACP is the right solution to a problem.

     After a short break, we will begin a discussion on  how
to implement an ACP for a RSX-11M system.  This section will
detail a proposed method  of  implementing  an  user-written
ACP's  that  was  first  discussed  at  the Fall, 1977 Decus
Symposium in San Diego.  This area will not apply to IAS  or
RSX-11D   users.   If  enough  interest  is  generated,  the
discussion will continue at a  Birds-of-the-Feather  session
later this evening.

     During the tutorial, we will pause for questions at the
end  of  each  major topic.  Please hold comments until this
time also.



ACP Tutorial                                          PAGE 3



2.0  PHILOSPHY




2.1  Definition of 'ACP'


     The  first  step  is  to  define  the   mystical   word
"ancillary".   Before  Digital  used  it, the word was not a
part of most vocabularies.  Webster's defines  ancillary  as
either  subordinate or auxiliary.  Digital's use of the word
draws  on  both  definitions.   This  session  will   define
Anillary  Control  Processor  in  the IAS/RSX-11 environment
refers to a task which provides a protocol for  a  class  of
I/O device.



2.2  Attributes of ACP's


     This definition is drawn from the  observed  attributes
of  the  three  ACP's  provided  by  Digital:  the disk file
system (F11ACP), ANSI magtapes (MTAACP) and  the  DDCMP  and
NSP  portions  of DECNET (NT....).  Each of these ACP's have
the following features in common:

     1.  [slide 03] An ACP is implemented  as  a  privileged
         task  and  has all the attributes of a task (stack,
         priority, checkpointablity, task name, etc.)

     2.  [slide 04] An ACP implements a protocol for a class
         of devices [slide 05]:

         1.  F11ACP implements the Files-11 protocol for all
             disks (RK05, RP06, etc.) and DECtapes.

         2.  MTAACP implements the ANSI magtape protocol for
             all   supported  magtape  drives  (TU10,  TU16,
             etc.).

         3.  NT....  implements DECNET protocols for a  wide
             variety   of  communication  interfaces  (DL11,
             DU11, etc.).


     3.  [slide  06]  The  protocol  provided  by  each  ACP
         extends the functionality of the devices in several
         ways [slide 07]:

         1.  The burden of  direct  device  manipulation  is
             removed  from the programmer.  By using an ACP,



ACP Tutorial                                          PAGE 4



             the programmer no longer must deal with  device
             specific I/O requests.

         2.  The burden of direct data manipulation  at  the
             device  level  is  removed from the programmer.
             The ACP strips off  any  data  related  to  its
             protocol  and returns only the items of concern
             to the application.

         3.  The device can be treated as a logical,  rather
             than physical, enity.  In the case of Files-11,
             the programmer deals  with  files  and  records
             versus  physical  disk  blocks.  A corollary of
             this statement is that different devices can be
             treated  the same from the program's viewpoint.
             DECNET's support of asynchronous,  synchronous,
             and   parallel  interface  is  the  most  vivid
             example of this fact.

         4.  The  device  can  be  shared  for  simultaneous
             access.   Each accessing processes is protected
             from the others by the ACP  and  its  protocol.
             The   ACP's  also  synchronize  access  to  the
             physical device.

         5.  The device is  protected  against  unauthorized
             and  destructive  access.   In an appropriately
             managed IAS/RSX-11 system, F11ACP  provides  an
             adequate file protection mechanism.


     4.  [slide 08] An ACP extends the functionality of  the
         IAS/RSX-11   executives,   particularly   the   I/O
         mechanism.  An ACP can  properly  be  considered  a
         part  of the executive;  and in many cases operates
         at the executive level.

     5.  [slide 09] An ACP can  be  enabled/disabled  for  a
         given  device  (mounted/dismounted).  When enabled,
         the device is typically available only for  use  in
         the context of the protocol provided by the ACP.


     In summary [slide 10], this session will define an  ACP
as the following:

     1.  A task....

     2.  which provides a protocol.....

     3.  for a class of I/O devices.

[questions]



ACP Tutorial                                          PAGE 5



3.0  I/O COMPONENTS


     An ACP is one component of the IAS/RSX-11 I/O mechanism
[slide 11], but its functionality is often confused with the
other major  parts:   the  QIO  directive  processing,  File
Control  Services (FCS), and device drivers.  By contrasting
the  role  of  the  ACP  with  the  roles  of  these   other
components,  we  can  gain  a  better  understanding  of the
function of an ACP.

     The begining of all I/O is with the QIO directive.  The
directive  can be issued directly by a program or indirectly
from various run-time systems  (F4POTS)  or  from  the  file
control  services.   In  all cases, the QIO directive is the
only recognized  method  to  request  I/O  service  from  an
IAS/RSX-11  operating  system.   The  action  taken  by  the
executive when a request is issued depends on  the  type  of
request,  the type of device, whether an ACP is used for the
device, and finally, whether the ACP is enabled or  disabled
(mounted/dismounted).  The executive may pass a QIO directly
to the designated device driver.  The driver  then  performs
the  request I/O operation.  However, when an ACP is enabled
for a device, the I/O request  is  typically  passed  to  it
instead.   The  ACP  may  forward the request to the driver,
issue it's own QIO's to service the request, or fulfill  the
function without any device I/O at all.

     The file control services library is the  component  of
the  I/O  mechanism  used  to implement device independence.
The FCS routines examine the device characteristics  or  the
currently assigned device and issue QIO directives dependent
on the device characteristics.  A  task  which  uses  direct
QIO's to perform terminal output cannot use the same code to
output to the disk.  However, if FCS is used to perform  the
output,  this  flexablity  is possible.  The QIO's issued by
FCS to perform the write to the terminal differ  from  those
to a line printer.

     FCS is very much aware of the existence of the Files-11
and magtape ACP's and issues QIO's designed for such device.
The  actual  QIO's  supported  by  these  ACP's  are   quite
different   from   the  normal  device  QIO's  and  are  not
documented by Digital.  In a short while, we will deal  with
the specific relationship between FCS and F11ACP and MTAACP.

     The lowest level of the I/O mechanism  are  the  device
drivers.  A device driver provides basic device services for
a single module  of  a  device.   These  services  typically
related   directly  to  the  method  the  device  physically
performs I/O:   read  data,  write  data,  position  device.
Device drivers require the QIO parameters to be specified in
a basic, often device dependent, form.



ACP Tutorial                                          PAGE 6



     By using an ACP in conjunction with device drivers, the
user  is  allowed  to request logical, rather than, physical
device services.  These logical request are massaged by  the
ACP into the basic, driver specific, I/O request.

     At this stage, we have developed a simplistic  view  of
the  IAS/RSX-11  I/O  mechanism.   The next slide [slide 12]
shows the flow of a simple QIO issued  from  a  task  for  a
particular  device.   The  flow  is thru the executive's QIO
processor to the device driver to the  device.   This  slide
[slide  13]  adds  FCS  to the task.  In this case, the task
makes an I/O request to FCS which  then  issues  the  actual
QIO.   The  last case [slide 14] adds an ACP to the process.
Here, the I/O request from FCS is routed to the ACP  by  the
executive's  QIO processor.  The ACP issue's its own request
to the device driver to satisfy the request.

     In developing the MDAP project, we looked at this slide
with  great interest.  If we could write an ACP that handled
QIO's in a similar fashion to the Files-11 ACP (F11ACP), but
used  DECNET to communicate with a partner on a remote node,
we could  achieve  network  device  and  file  independence.
While  this  statement is not totally true, the ACP approach
is still valid.  The next section will explore this  subject
further and attempt to open the mysteries of FCS and ACP's.

[questions]



ACP Tutorial                                          PAGE 7



4.0  FCS AND ACP'S


     As stated before, the  File  Control  Services  library
(FCS)  is  the  component  of  the  I/O  mechanism  used  to
implement device independence.  When a task uses FCS for its
I/O,  it  does  not  care if the device is a disk, terminal,
line printer, card reader, magtape, or any  other  block  or
record  oriented  device.   The  only  RSX-11M  devices  not
interfaced  to  FCS  are  either  real-time  (LPS,  ICS)  or
communications (DECNET) in nature.

     The FCS library modules can  be  classified  into  four
categories:   parsing, device/file access, input/output, and
device/file control.   The  parsing  routines  are  used  to
set-up the filename block.  The parsing routines also assign
the lun to the specified device and fill  in  FDB  locations
F.RCTL  and  F.VBSZ.   These  locations  are  used  later to
determine the proper QIO request to issue to the device.

     The byte field F.RCTL is filled in with the low byte of
the  first characteristics word (U.CW1).  The most important
bit is bit 0 (FD.REC).  If this bit is  on,  the  device  is
record  oriented,  ie.   not  a disk.  If off, the device is
block-oriented and all records must be handled internally by
FCS.  The next important bit is bit 3 (FD.DIR).  If this bit
is on, the device contains Files-11  directories.   Finally,
bit 5 (FD.SEQ) classifies the device as sequential.

     The device/file access routines examine FD.DIR.  If the
device  has  directories,  ie.   a  disk,  dectape,  or ANSI
maptape,  Files-11  QIO's  are  used  to  access  the  file.
Otherwise,  no  file  access  is required.  The input/output
routines examine RD.REC to determine  the  type  of  I/O  to
perform.    If   the   device   is  record-oriented,  simple
read/write virtual block QIO's are issued for  each  record.
Otherwise,  records  are buffered into blocks and written to
the file.

     FCS provides  the  only  documented  interface  to  the
F11ACP  and  MTAACP.   Knowledge of FCS is very important to
writing your own ACP if the purpose of the ACP is to provide
device/file independence to a non-Digital supported device.

[questions]



ACP Tutorial                                          PAGE 8



5.0  USES FOR USER WRITTEN ACP


     As noted before, the  Digital  supplied  ACP's  perform
many  useful  services  in the RSX-11/IAS operating systems.
As several sites have shown, it is possible to  write  other
ACP's  and  successfully  integrate  them into the operating
systems.  Before continuing with an examination of how  this
is  done for RSX-11M, let use consider possible applications
for user-written ACP's.

     Before continuing, it must be pointed out that  writing
an  ACP is a non-trivial task.  You will probably invalidate
any Digital software warranties and end  up  making  massive
modification  to  the  operating system.  Future releases of
the operating system must be updated for your ACP and  there
is  no guarentee Digital will not completely rewrite the ACP
code.  The advantages of a user-written ACP must be  weighed
against these disadvantages.

     By definition,  an  ACP  implements  an  I/O  protocol.
While  it  would  be  possible to implement an ACP for other
purposes, typically, better solutions could be  found.   The
best  application  for an user-written ACP is to implement a
non-Files-11  file  system,  particularly,  if  the  ACP  is
interfaced  to  FCS  for  device/file independence.  Several
examples come to mind:

     1.  If your  shop  supports  mixed  systems  (RT11  and
         RSX-11M),  an  ACP  could be implemented to support
         the RT-11 file structure.  If  interfaced  to  FCS,
         the  RSX-11M  utilities could be used to access the
         RT-11 disk directly, without the need to FLX  files
         between the two structures.

     2.  If you have a requirement to read foreign magtapes,
         again  an ACP could be written for this task.  This
         is  basically  what   occured   when   MTAACP   was
         introduced by Digital.


     ACP's can also be used to  implement  a  communications
protocol.   Digital  takes  this  approach  with  DECNET.  A
user-written ACP could be used  to  communicate  with  other
computers  via  an established protocol (BYSYNC, SDLC, etc.)
or your own protocol.

     The final example that comes to mind is to  extend  the
functionality  of  a  current Digital device.  One method of
implementing spooling  on  a  RSX-11M  system  would  be  to
implement  a  line-printer  ACP.   This  ACP would intercept
write request to the line-printer and send them  to  a  disk
file.   When the output is terminated, the file is queued to



ACP Tutorial                                          PAGE 9



be printed on the line-printer.

     Notice that in all  examples,  the  user-written  ACP's
extend  functionality, not performance.  If your application
is performance-oriented, a special device driver  or  direct
device access should be considered, not an ACP.

     At Monsanto, we are implementing an ACP  that  is  both
communication  and  file  system  oriented.   Monsanto has a
herichal network, consisting of a DECsystem-10 at  the  top,
and  two  layers  of  RSX-11M  systems  below  it.   We  are
currently working on a  project  to  implement  the  Digital
Access  Protocol  (DAP)  between  our  DECsystem-10  and the
PDP-11's.

     The PDP-11 side will be implemented by  an  ACP.   This
ACP  will be interfaced to FCS on one end and to the Digital
supplied DECNET software on the other.  When  completed,  we
expect  to  have network file independence.  Our programmers
will be able to access remote files using the same  language
syntax used to access local files.

[questions]

     At this time, let us take a 5 minute  break.   When  we
come  back, the discussion will be on how RSX-11M interfaces
to an ACP.  The details presented apply on  to  RSX-11M  and
not to RSX-11D and IAS.

[break]



ACP Tutorial                                         PAGE 10



6.0  MECHANISM'S


     From this point on, the  session  will  deal  with  the
detail's concerning ACP's.  We will first take a look at the
various device tables, concentrating on items which  concern
ACP's.   We  will  then  discuss the environment an ACP must
work in,  looking  at  the  mount  and  dismount  task,  the
executive ACP interface, and some internal ACP processing.

     I have a limited number of copies of this  presentation
and other notes.  The notes are also being placed on the SIG
tape as runoff files.  If anyone is interested in  obtaining
a copy, see me after the session.

     [Because of the detail, the remaining presentation will
be only outlined, not written in full].



6.1  Device Tables


     1.  Overall View [slide 15]

              Mention the various tables  on  the  slide  by
         name but do not make any connection between tables.
         Show which tables  are  always  associated  with  a
         device and which are only present for an ACP.

              Emphasize the flexibilty and latitude you have
         in  setting  up  device tables for an ACP.  Mention
         how each existing ACP uses a different approach and
         the  lack  of  similarity  bewteen  the  VCB's  for
         example.

     2.  Device Driver Tables

         1.  QIO DPB [slide 16]

                  Emphasize that the function code  is  only
             the  high  byte  and  that  all modifiers for a
             particular function must still be the same type
             of  request  (ie.   control).  Also mention the
             required format of a transfer request.

         2.  I/O Packet [slide 17]

                  Emphasize  the  usefulness  of  I.TCB  and
             I.LN2  to  an ACP.  Also discuss I.PRM in terms
             of transfer versus control functions versus ACP
             functions.



ACP Tutorial                                         PAGE 11



         3.  DCB [slide 18]

                  Emphasize function mask bits.  Mention ACP
             functions  must  be  greater than 7.  Reference
             table 4-1  in  Guide  to  Writing  I/O  Driver.
             Describe  order  functions  mask  are  checked:
             legal, control, noop, ACP, and transfer.

         4.  UCB [slide 19]

                  Emphasize U.STS and U.CW1.  In  particular
             mention US.MNT, US.FOR, US.MDM in U.STS and all
             bits in U.CW1, Reference page 4-22 in Guide  to
             Writing  I/O  Driver.   Point  out  how F11ACP,
             MTAACP,   and   NT....    are    differentiated
             internally  by  U.CW1  and how FCS uses DV.REC,
             DV.CCL,  DV.TTY  and  DV.DIR  and   U.CW4   for
             determining  what type of I/O to perform.  Talk
             about U.ACP and U.VCB.

         5.  SCB [slide 20]

                  Mention fork block is  cell,  not  header.
             Can only fork once for any 1 SCB.


     3.  ACP Tables

         1.  VCB [slide 21]

                  Emphasize that only  V.TRCT  is  required,
             all  other  locations  are ACP unique.  Mention
             VCB's created at mount time  and  destroyed  at
             dismount.

         2.  LUT [slide 22]

                  Emphasize importance of  LUT  and  putting
             LUT2 to good use.  Mention lock feature.

         3.  Other Tables

                  Mention what a window is, how  it  typical
             is link to other tables.  Tell about F11ACP and
             its FCB's and NT....  and its CCB's.


     4.  Summary [slide 23]

              Trace through the various links.

         [questions]




ACP Tutorial                                         PAGE 12



6.2  Environment


     1.  MOU Command

         1.  Purpose [slide 24]

                  Explain purpose of MOU task:   ACP  option
             specification,     protocol     initialization,
             protocol verification, and ACP task startup.

                  Explain that using the MOU command is  not
             necessary,   that  an  ACP  could  perform  the
             necessary operation itself when it is initially
             run if written correctly.

         2.  Structure [slide 25]

                  Explain each module's purpose  and  place,
             emphasizing  what  modules  must be added for a
             new  ACP  and  what  modules  must  have   code
             changes.

         3.  Program Flow

             1.  Device Parsing [slide 26]

                      Tell  what  this  process  does:   get
                 command line, parse out device name, assign
                 lun 2 to device, set $MDEV to UCB  address,
                 and  dispatch  on  device  characteristics.
                 Explain how the dispatch is made.

             2.  Option Parsing [slide 27]

                      Tell what these modules typically  do:
                 Allocate  the  VCB  and  any  other storage
                 blocks, set $MVCB and $MVCBL, parse options
                 and set appropriate words in VCB and $MKEY,
                 and   check   for    necessary    multiuser
                 priveledges ($PVTST).

             3.  ACP Startup [slide 28]

                      Tell what these modules typically  do:
                 check  for legal access (label processing),
                 complete table initialization,  and  invoke
                 ACP.

             4.  VID Display [slide 29]

                      Just mention module name ($MDISEP) and
                 how invoked from root.



ACP Tutorial                                         PAGE 13



             5.  Error Handling [slide 30]

                      Just  mention  module  name  ($MOUER),
                 calling  sequence  (R0  = ASCIZ string, and
                 table dealocation.

             [questions]


     2.  DMO Command

              Explain the DMO is fairly  simple.   The  only
         ACP  dependent  code  is if the device is Files-11.
         If not, it constructs a DMO QIO request, queues  it
         di
rectly   to   the   ACP,  increments  the  volume
         transaction count, sets the mark for  dismount  bit
         (US.MDM), and exits.

     3.  Executive ACP Interface

         1.  $DRQIO [slide 31]

                  Explain flow  through  $DRQIO,  mentioning
             points  especially  concerned  with ACP's:  lun
             interlock feature, ACP function  handling,  and
             polish data base.

         2.  $GTPKT [slide 32]

                  Explain  flow  through   $GTPKT,   mention
             points especially concerned with ACP's:  an ACP
             enabled device cannot be attached, an  function
             greater  than  7 for an ACP device is passed to
             the ACP (no matter  what),  and  an  read/write
             virtual  to  an  ACP device is mapped by $MPPKT
             and only sent to the  ACP  if  the  mapping  is
             unsucessful.

         3.  ACP Initialization [slide 33]

                  Explain two entries:  $EXRQP (by priority)
             and $EXRQF (FIFO) and calling parameters.  Note
             that I/O packet is queued to receive queue  and
             that  the normal send process cannot send to an
             ACP.  Also note that these entries can and  are
             used  elsewhere to queue packets to ACP's (MOU,
             DMO, etc.).

         4.  $IODON

                  Note that no special  processing  is  done
             here  for  an ACP, it however uses the I/O done
             processors to terminate a request.



ACP Tutorial                                         PAGE 14



         5.  Task Exit

                  Explain how a  nonzero,  nonlocked  second
             lun  word  is  search  for and IO.CLN issued if
             found.

             [questions]


     4.  Internal ACP Processing

         1.  ACP Mapping [slide 34]

                  Explain  ACP   mapping   and   that   full
             capablilties  of  the  executive and a task are
             available to it.

         2.  State  Switching  [slide  35]  Explain  how  to
             switch from being a task to being a part of the
             executive.

         3.  Dequing and Dispatching I/O Request [slide 36]

                  Show  example  for  proper   dequing   and
             stopping loop.

         4.  Terminating I/O Request

                  Explain that  nothing  fancy  is  involved
             except  decrementing  the transaction count and
             watch for a dismountable state  when  a  marked
             for dismount.

         5.  Issuing Internal QIO's [slide 37]

                  Show example for different ways  to  issue
             QIO's:   regular  directive,  at  $DRQRQ, to an
             ACP.    Also   explain   concept   of    driver
             co-routines.

         6.  Pool Management

                  Show how internal and executive pools  can
             be  managed  and what must be in executive pool
             only (VCB's and windows).  Mention task  header
             usage.


     5.  Summary

         [questions]




ACP Tutorial                                         PAGE 15



7.0  BLUESKYING




7.1  Implementation Hints


     1.  What to print.  List off the important  modules  to
         get  listing  for  but  emphasize  that  everything
         should be listed.

     2.  What to read.  List manuals and important  code  to
         read.

     3.  What to expect.  Point out lack of Digital  support
         and  understanding  for your effort, termination of
         support, problems with future  releases,  bugs  you
         will find.