Files-11 QIO Notes - APR, 78



                          FILES-11 QIO NOTES

     This file documents the various QIO's used by  Files-11  (F11ACP)
and  the  format  of each request.  The material was compiled by Ralph
Stamerjohn, working mostly from an article written by Andrew Goldstein
of Digital in November, 1976.

     The reader is assumed to be a RSX-11/IAS systems programmer.  The
article  is written as a reference guide.  It is not an explanation of
the file I/O mechanism.  No guarentee of accuracy is  implied  by  the
author  or  Digital.   The  material  should  be used with great care.
Improper use will lead to corruption of the file system.



1.0  FILES-11 QIO DPB


     All F11ACP QIO directive parameter blocks have the  same  format.
The following diagram illustrates this format (note only the parameter
fields are different from all other QIO's):

     -------------------------------------------------
     !          Size         !          DIC          ! 
     -------------------------------------------------
     !       Function Code   !       Modifier        ! Q.IOFN Q.IOFN
     -------------------------------------------------
     !       Reserved        !          LUN          !        Q.IOLU
     -------------------------------------------------
     !       Priority        !          EFN          ! Q.IOPR Q.IOEF
     -------------------------------------------------
     !               I/O Status Block                ! Q.IOSB
     -------------------------------------------------
     !                 AST Address                   ! Q.IOAE
     -------------------------------------------------
     !                 FID Pointer                   ! Q.IOPL
     -------------------------------------------------
     !          Attribute List Pointer               !
     -------------------------------------------------
     !   Extend Control      !   Delta Size (High)   !
     -------------------------------------------------
     !          Delta Size (low 16 bits)             !
     -------------------------------------------------
     !   Access Control      !   Window Size         !
     -------------------------------------------------
     !                  FNB Pointer                  !
     -------------------------------------------------

     Each parameter field is used for a  specific  purpose.   The  the
particular  QIO  does  not  require the field is must not be specified
(typically set to zero).  F11ACP checks  range  checks  all  parameter
fields.



Files-11 QIO Notes - APR, 78                                    PAGE 2



2.0  FILES-11 QIO PARAMETERS


     This section will discuss the six parameter words in  a  Files-11
QIO.  While none of the parameters require the FCS data structures, it
is obvious the fields are set up for use in the FCS environment.



2.1  Parameter Word #1 - FID Pointer


     This word contains the address of  a  three  word  block  in  the
issuing  task's  space.  This block is or will become the file ID.  If
the word is zero, no file ID is specified.

     In the FCS environment, this  word  will  typically  contain  the
address  of  the  filename block.  The file ID block has the following
format:

     -------------------------------------------------
     !                   File Number                 !
     -------------------------------------------------
     !               File Sequence Number            !
     -------------------------------------------------
     !                    Reserved                   !
     -------------------------------------------------

     The file number is used by F11ACP has an index to the file header
block in the index file.  The file sequence number is used to maintain
header integrity.  Each time a header block is used for  a  new  file,
the  file  sequence  number  is  inccremented.   The final word has no
current meaning.



2.2  Parameter Word #2 - Attribute List Pointer


     This word contains the  address  of  an  attribute  list  in  the
issuing task's space.  This list controls which file attributes are to
be read or written by F11ACP.  If no attribute list is specified,  the
word is zero.

     File attributes are various fields in  the  file  header.   These
fields  are  documented in Appendix F of the IAS/RSX-11 I/O Operations
Reference Manual (AA-2515C-TC).

     An attribute list consists of  zero  to  six  attribute  entries,
followed  by  a  byte of zero.  Each attribute entry has the following
format:

     .BYTE   <Attribute type>,<N>



Files-11 QIO Notes - APR, 78                                    PAGE 3



     .WORD   <Pointer to 'N' byte buffer>

     The sign of the attribute type determines the  direction  of  the
operation.   If  the attribute type is negative, the attribute is read
from the file  header  to  the  buffer.   If  the  attribute  type  is
positive,  the  buffer  is  written  to  the  file  header  as the new
attribute.  The magnitude of the attribute type and size of the buffer
determine  which  fields  in  the  file  header will be accessed.  The
following table list all valid  read  attribute  types,  valid  buffer
sizes,  and  the  starting  offset  in  the file header.  To write the
attribute, make the sign of the attribute type positive.

     -01,02    Read file owner UIC (H.FOWN).   The  UIC  is  a  binary
               word.   The low byte (H.PROG) is the owner number.  The
               high byte (H.PROJ) is the group number.  Note that  the
               file owner UIC is independent of the directory UIC.

     -01,04    Read file owner UIC, protection (H.FOWN).  The  UIC  is
               returned as described above.  The second word is set to
               the file protection code (see attribute -02,02).

     -01,05    Read  file  owner  UIC,   protection,   characteristics
               (H.FOWN).   The  UIC  and  protection  are  returned as
               described  above.   The  fifth  byte  is  set  to   the
               user-controlled characterics (see attribute -03,01).

     -02,02    Read protection (H.FPRO).  The file protection word  is
               a bit mask with the following format:

               Bit   15       12 11        8 7         4 3         0
                     -----------------------------------------------
                     !   World  !   Group   !   Owner   !  System  !
                     -----------------------------------------------

               Each of the four categories above has four bits.   Each
               bit  has  the  following  meaning  with respect to file
               access:

               Bit        3          2            1          0       
                     -----------------------------------------------
                     !  Delete  !  Extend   !   Write   !   Read   !
                     -----------------------------------------------

               A bit value of zero (0) indicates the  respective  type
               of  access  is allowed to the file.  A bit value of one
               (1) indicates access is denied.

     -02,03    Read   protection,   characteristics   (H.FPRO).    The
               protection  is  returned as described above.  The third
               byte is set to the user-controlled characteristics (see
               attribute -03,01).

     -03,01    Read    characteristics     (H.UCHA).      The     user



Files-11 QIO Notes - APR, 78                                    PAGE 4



               characteristics  is a one byte field containing various
               bit definitions.  The current bits defined  are  listed
               below:

               UC.CON = 200   Logically  continuous  file.   When  the
                              file is extended, this bit is cleared.

               UC.DLK = 100   File improperly closed.  When  ever  the
                              file  is  opened  for write, this bit is
                              set.  It is not cleared until  the  file
                              is  closed  (deaccessed).   This  is the
                              famous lock bit.

               In addition to the user-controlled characteristics, the
               next  byte  in  the  header  is  the  system-controlled
               characteristics.  This byte cannot be  accessed  by  an
               attribute field.  The current bits defined in this byte
               are listed below:

               SC.MDL = 200   File marked for delete.

               SC.BAD = 100   Bad data block in file.

     -04,40    Read record I/O area (U.UFAT).  The first  7  words  of
               this area are a direct copy of the first 7 words of the
               FDB when  the  file  is  opened  (see  Table  A-1,  I/O
               Operations Reference Manual, offsets F.RTYP to F.FFBY).
               The remaining 9 words of this area are not used.  I  do
               not  know  how  this  area  is  defined  in the case of
               RMS-11.

     -05,06    Read filename (I.FNAM).  The filename is stored as nine
               (9) RAD50 characters.

     -05,10    Read filename, type (I.FNAM).  The filename is returned
               as described above.  The type is returned to the fourth
               word (see attribute -06,02).

     -05,12    Read filename, type, version  (I.FNAM).   The  filename
               and  type are returned as described above.  The version
               is returned to thr fifth word (see attribute -07,02).

     -06,02    Read type (I.FTYP).  The type is stored  as  three  (3)
               RAD50 characters.

     -06,04    Read type, version (I.FTYP).  The type is  returned  as
               decsribed above.  The version is returned to the second
               word (see attribute -07,02).

     -07,02    Read version (I.FVER).  The  version  is  stored  as  a
               binary number.



Files-11 QIO Notes - APR, 78                                    PAGE 5



                                        NOTE

                   The filename, type, and version  are  set  when
                   the file is created.  If the file is renamed by
                   PIP, these fields are not changed.



     -10,07   Read expiration date (I.EXDT).  The expiration  date  is
               intended  to  be the time the file becomes eligible for
               deletion.  This feature is not implemented.   The  date
               is  kept  in  ASCII  form in the format day, month, and
               year (2 bytes, 3 bytes, and 2 bytes).

     -11,12    Read statistics block.  The statistics block is defined
               in  Appendix  H  of  the  I/O  reference  manual.  This
               attribute is  not  any  specific  fields  in  the  file
               header, therefore, this attribute cannot be written.

     -12,00    Read entire file header.  The buffer size is assumed to
               be  1000(8) bytes.  This attribute has no corresponding
               write function.

     The magitide of the attribute type determines the  maximun  valid
buffer  size.   Any smaller size is legal.  The sizes listed above are
sufficient to handle the named attributes.  The largest size for  each
attribute is also the largest buffer allowed.



2.3  Parameter Words #3 and #4 - Size/Extend Control


     These two parameters are used to specify how many blocks  are  to
be  allocated  to  a new file or added to an existing file.  The words
are also used to control the type of block allocation.

     The high bit of parameter word #3 (bit 15) controls  whether  the
remaining  fields are used by F11ACP.  If the bit is zero (0), no size
change is desired.  If the bit is one (1), the  remaining  fields  are
processed.

     The high byte of parameter word #3  (extend  control)  determines
the  type  of  allocation  desired.   The  low  byte  of this word and
parameter word #4 form a 24-bit number of blocks  to  allocate  (delta
size).   This  number is the initial file size in the case of a create
and the change in size in the case of an extend.

     The extend control byte consist of various  bit  mask.   The  bit
mask have the following meanings:

     Bit 0     All blocks must be allocated contigously.




Files-11 QIO Notes - APR, 78                                    PAGE 6



     Bit 1     Allocate largest contigious chunk  up  to  delta  size.
               This bit is not examined unless bit 0 is on (1).

     Bit 2     File must end up contigious at operations end.

     Bit 3     Use volume default as delta size.

     Bit 4     Unused.

     Bit 5     Unused.

     Bit 6     Unused.

     Bit 7     Enable extend (see above).



2.4  Parameter Word #5 - Window Size/Access Control


     This word is used to specify the window size (low byte)  and  the
access control (high byte).  The word has is processed if the high bit
(bit 15) is one (1).  If this bit is zero (0), the word is disabled.

     The window size is the number of mapping entries the window is to
hold  at  once.  This is not the window size in bytes.  If the byte is
zero, the volume default is used.

     The access control byte consist of various  bit  mask.   The  bit
mask have the following meanings:

     Bit 0     Lock  file  from  further  accesses  for  write  and/or
               extend.

     Bit 1     Enable daaccess lock.

     Bit 2     Unused.

     Bit 3     Unused.

     Bit 4     Unused.

     Bit 5     Unused.

     Bit 6     Unused.

     Bit 7     Enable access (see above).



Files-11 QIO Notes - APR, 78                                    PAGE 7



2.5  Parameter Word #6 - Filename Block Pointer


     This word contains the address of a  13(10)  word  block  in  the
issuing task's space.  This block is the filename block.  See Appendix
B in the I/O Reference Manual for a description of a  filename  block.
If the word is zero, no filename block is specified.



3.0  FILES-11 QIO FUNCTIONS


     This section will discuss  the  various  functions  processed  by
F11ACP.   This  functions  are normally issued by FCS or RMS, however,
the clever user can use them directly and save  the  overhead  of  the
run-time systems.  At the same time, you also take your life into your
own hands.

     The  following  table  summarizes  the  optional   and   required
parameters for each I/O request.  The key to the table is as follows:

               * = Required parameter.
               O = Optional parameter.
               A = Optional if file already accessed.
               D = May be non-zero, but must be disabled (bit 15 = 0).

If the entry is blank, the parameter must be zero or the I/O  will  be
in  error.   Parmeter  4 is a part of parameter 3 and is not listed in
the table.

     ------------------------------------------
     ! Function ! P 1 ! P 2 ! P 3 ! P 5 ! P 6 !
     ------------------------------------------
     ! IO.ACE   !  *  !  O  !     !  *  !     !
     ------------------------------------------
     ! IO.ACR   !  *  !  O  !     !  *  !     !
     ------------------------------------------
     ! IO.ACW   !  *  !  O  !     !  *  !     !
     ------------------------------------------
     ! IO.CRE   !  *  !  O  !  O  !  D  !     !
     ------------------------------------------
     ! IO.DAC   !  O  !  O  !     !  D  !     !
     ------------------------------------------
     ! IO.DEL   !  A  !     !  O  !     !     !
     ------------------------------------------
     ! IO.ENA   !     !     !     !  D  !  *  !
     ------------------------------------------
     ! IO.EXT   !  A  !     !  *  !     !     !
     ------------------------------------------
     ! IO.FNA   !     !     !     !  D  !  *  !
     ------------------------------------------
     ! IO.RAT   !  A  !  *  !     !     !     !



Files-11 QIO Notes - APR, 78                                    PAGE 8



     ------------------------------------------
     ! IO.RNA   !     !     !     !  D  !  *  !
     ------------------------------------------
     ! IO.WAT   !  A  !  *  !     !     !     !
     ------------------------------------------