NEW CARD READER HANDLER

	TO ALL & SUNDRY:

	I HAVE WRITTEN A NEW CARD-READER HANDLER TO TAKE CARE
OF INPUTS OF ASCII TEXT. IT WILL HANDLE ALL ASCII CODES AND SHOULD
BE INSTALLED VIA THE FOLLOWING STEPS:

1. IF CR11.TSK IS ALREADY IN [3,30] OMIT THE NEXT STEPS AND GO TO
THE INSTALL PHASES.
2. OTHERWISE GET A COPY OF [3,30]CRBR.MAC IN A UIC ON YOUR DISK
FROM THE SYSTEM DEVELOPMENT AND INTERFACE TEST DISK [3,30] AREA
AND A COPY OF CR11.CMD FROM THE SAME PLACE AND PUT ON YOUR DISK.
3. ASSEMBLE AS FOLLOWS:
MAC CR=CRBR
4. TASK BUILD AS FOLLOWS:
TKB @CR11.CMD
5. THIS IS THE INSTALLATION PROCEDURE. ASSUMING YOU BUILT
TASK CR11.TSK USING CR11.CMD WHILE LOGGED IN AS [3,30]:
TYPE THE FOLLOWING WHILE LOGGED IN [1,1]:

UNL CR:
REM CR....
UNL MT:
LOA MT:
DMO SY:
FIX F11ACP
MOU SY:
UNF F11ACP
INS [3,30]CR11
LOA CR:

THE NEW CARD READER WILL NOT HANDLE BINARY (REASSEMBLE WITH A FILE
CONTAINING THE LINE 
BINARY=0
TO PERMIT IT TO)
BUT WHEN A CONTROL CARD WITH A MULTIPUNCH WITH COLUMNS 12,0,2,4, AND 8
IN COLUMN 1 IS PUT AHEAD OF THE DECK, THE HANDLER WILL TRANSLATE ALL
CARD CODES TO THEIR ASCII EQUIVALENTS INCLUDING CR, LF AND OTHER
SPECIAL CHARACTERS. WITHOUT THIS CONTROL CARD, THE HANDLER WILL ACT
EXACTLY AS YOUR OLD ONE DID. THE CONTROL FEATURE SHOULD REMAIN SET
ACROSS ENDFILES. NOTE THAT MOST 029 CODES ARE IDENTICAL TO ASCII
CODES WHERE THE TWO OVERLAP. CARD MULTIPUNCHES THAT HAVE NO ASCII
EQUIVALENTS ARE TRANSLATED TO NULLS (0) ON INPUT. I WILL ALTER THAT
WHEN ANYONE GIVES ME A GOOD REASON TO DO SO.
		GLENN EVERHART
		10/22/1976