PROJECT:        MAC REPLACEMENT PROJECT

   DOC. TYPE:      DESIGN SPECIFICATION
   SUBJECT:        FAST ACCESS OF LARGE DATA AREAS OUTSIDE THE TASK IMAGE
   TITLE:          ACCESSING UNMAPPED REGIONS

   GROUP:          RSX-11M SYSTEM EXTENSIONS
   AUTHOR:         D.B.CURTIS

   DOC NO.:        34.2
   DATE:           15-FEB-79 20:45
   FILE:           largary.RNO


   MODIFIED:  18 JUL 79 23:09



                                                                   PAGE 2
   


   1.0  OBJECTIVES

   This document describes a method of accessing  regions  without  being
   mapped  to  them.   This method allows better utilization of the tasks
   virtual address space.  The method  is  suitable  for  accessing  very
   large (greater than 4K word) areas.

   The method is easy to modify.   Other  documents  describe  additional
   functionality.

   The document is separated into the following major sections:

        1.  discussion -- an overview of the method and a  discussion  of
            its merits and deficiencies.

        2.  detailed plan -- a design for the implementation.




   2.0  DISCUSSION

   This section overviews the method and its  limitations.   It  has  the
   following sub-sections:

        1.  overview of the method

        2.  merits of the method

        3.  deficiencies of the method




   2.1  Overview of the Method

   This method is an easy way of supplementing  the  executive  services.
   One supplementary service allows reasonably rapid access to very large
   shared areas.  The need for  this  service  appears  in  the  RSXMULTI
   project  where the 4K word dynamic area is restrictive, and in the MAC
   REPLACEMENT PROJECT which needs  a  very  large  resident  data  area.
   Typically, this would be satisfied by using the PLAS directives to map
   into the shared data area.  There are advantages and disadvantages  to
   both methods and these are described in section 2.2 and 2.3.

   The method used places code into the  system  pool  and  attaches  the
   illegal  instruction  trap  vector  to  this  code.  This is done by a
   separate task.  Once done, all other tasks may use the facility.



                                                                   PAGE 3
   


   Another task removes the code and returns the system to  its  original
   state.   Typically, the facility would be loaded and the system saved,
   thus, providing the facility at system startup.

   The initial implementation of the facility provides the following:

        1.  transfer a word (on the task's stack) to a specified location
            in the region's area.

        2.  transfer a word from a specified location in a region to  the
            task's stack.

        3.  transfer a block of words from the task's area to the region.

        4.  transfer a block of words from the region to the task area.

        5.  set a value into a block of locations in the region.

   The user is able to specify the region to access.

   The number of words that can be  transferred  is  a  maximum  of  2048
   words.   This  is  because  the  facility runs in the system state and
   therefore task switching is disabled and this could cause unreasonable
   response to real time events.



   2.2  Merits of the Method

   This method has the following advantages over the PLAS method.

        1.  allows the complete addressing space of a task  to  be  used.
            There  no longer is the need to truncate the virtual space of
            the task by 4K words.

        2.  in the case of very large commons with large tasks  there  is
            no  special  code  to  map to and from different areas in the
            common.

        3.  any dynamic region in the system can be accessed without need
            of special privilege.

        4.  as mapping is not done,  it  adds  another  level  of  memory
            resident overlays to the task.

        5.  As an illegal instruction is used, microcoded  PDP-11s  could
            implement the instruction to increase efficiency.




                                                                   PAGE 4
   


   2.3  Deficiencies of the Method

   This method has the following disadvantages with respect to  the  PLAS
   method.

        1.  each access to a particular word of  the  region  takes  much
            longer.  In the PLAS method, an entire chunk of the memory is
            directly accessible by the task.  In the illegal  instruction
            method,  every  access  to  a  word has significant overhead.
            This disadvantage is overcome only  with  very  large  arrays
            with  random accesses or by copying large blocks of memory to
            the task for access and then back to  the  shared  area  when
            done  (paging  of  data).  For MULTI, it may be reasonable to
            copy blocks of dynamic into some smaller array for processing
            and to restore the processed data.


                                        NOTE

                There may be ways to speed up this access.  These may
                be  implemented  later.   One  method  is to keep the
                names of the checked regions  around  in  the  system
                pool  to  speed  the  access protection checks.  This
                would speed the accesses to a given area but slow the
                access  to  new  areas.   Other  optimizations can be
                implemented as the need becomes understood.



        2.  there is no I/O access to the region.




   3.0  DETAILED PLAN

   This section provides a detailed plan of  the  implementation.   There
   are the following subsections:

        1.  Initial Conditions

        2.  Usage (calling sequences)

        3.  system constraints

        4.  ISF -- InStall Function

        5.  RMF -- ReMove Function




                                                                   PAGE 5
   


   3.1  Initial Conditions

   The task that wants access to a region,  must  first  attach  to  that
   region.  This way, the system may check the task/region privileges and
   refuse the task access if the privileges are not compatible.

   The system returns a region ID and this  ID  is  used  to  access  the
   region.  Write attempts to the region are checked for privilege.  Read
|  attempts are not checked.


                                    NOTE

|                 The first  version  does  not  make  the
|                 above  mentioned  privilege  checks.  If
|                 needed, they will be added.





   3.2  Usage (calling sequences)

|  The instruction that starts the system function is:

|  210

   The arguments of the instruction are on  the  stack.   There  are  the
   following types.

        1.  TYPE 0 -- transfer word to user

        2.  TYPE 1 -- transfer word from user

        3.  TYPE 2 -- transfer block of words to user

        4.  TYPE 3 -- transfer block of words from user

        5.  TYPE 4 -- set a block of area to user specified value




                                                                   PAGE 6
   


   Each of these types have the following information on the stack at the
   time  of  the 210 instruction execution.  This information is required
   for each type.  Each type may have other  information  placed  on  the
   stack along with the required information.
|          
|          10(SP) INDEX HIGH PART
|           6(SP) INDEX LOW PART
|           4(SP) REGION ID WORD OBTAINED FROM ATTACH REGION
|           2(SP) RAD50 REPRESENTATION OF "ILL"
|            (SP) TYPE

|  Where the INDEX is a 24-bit byte index into the region.

|  For type 0:

|  no more needed information

|  For type 1:

|  12(SP) VALUE TO BE STORED IN THE REGION

|  For type 2:

|  14(SP) NUMBER OF BYTES TO TRANSFER
|  12(SP) VIRTUAL ADDRESS TO TRANSFER TO 

|  For type 3:

|  14(SP) NUMBER OF BYTES TO TRANSFER
|  12(SP) VIRTUAL ADDRESS TO TRANSFER FROM 

|  For type 4:

|  14(SP) NUMBER OF BYTES TO SET
|  12(SP) VALUE TO SET INTO AREA

|  All cases except type 0 finish the operation with the  stack  cleared.
|  Type  0  returns the value obtained from the area on the stack.  Carry
|  clear implies operation completed successfully.  Carry set implies  an
|  error,  the  stack  is  not  cleared.   The instruction may produce an
|  illegal instruction trap if the arguments are out of order.



   3.3  System Constraints

   The following is a list of implemention constraints.

|       1.  real illegal instructions must still work



                                                                   PAGE 7
   


|       2.  210 with incorrect type is treated as an illegal instruction.

        3.  XDT causes the illegal instruction trap  to  be  reset  every
            time  XDT  executes.   This requires the appropriate table in
            the XDT code to be  ZAPed  to  allow  this  to  run.   It  is
            possible   that   the   ISF  and  RMF  tasks  would  do  this
            dynamically.

        4.  Only attached regions may be accessed ( this does not require
            an APR ).

        5.  access outside the region causes an error.

        6.  adding new functions is made easy.

   The following is a list of optimizations.

        1.  may be able to use the kernal or user data  space  to  access
            the shared area.  This must be able to be conditionalized out
            as it is not compatible with M-PLUS.




   3.4  ISF - InStall Function

   This task is responsible for loading the  specialized  code  into  the
   system  pool.   It also links the illegal instruction interrupt vector
|  to this code.

   Some constraints are:

        1.  If the function is already installed, the ISF task will error
            out.

        2.  if XDT is part of the system, ISF  will  adjust  XDT  to  not
            remap over the illegal instruction interrupt vector.

        3.  some optimizations may be initialized at this time.




   3.5  RMF - ReMove Function

   This task removes the function added by ISF.  It  is  responsible  for
   removing all traces of the function from the system.



                                                                   PAGE 8
   


   4.0  GLOSSARY


        1.  PLAS - Program Logic Address Space
            Name for the standard DEC method of mapping memory.  Used  in
            both the RSX and RT systems.

        2.  M-PLUS - Large version of M.
            A not yet released version of RSX-11M that is to  run  on  22
            bit machines.