SYSTAT - Mark Goegelman
         Johnson and Johnson Products Inc.
	 Medical Research Center
         US Route #1
         New Brunswick, N.J. 08903

         Tel: 201-524-5049

The author welcomes comments and suggestions concerning SYSTAT.

Release 1.0 of SYSTAT has been tested on RSX11M 3.1, 3.2 and MPLUS.
A new release which supports many of the MPLUS bells and whistles
(accounting information and shared hi-seg in particular) is being
debugged and should be available on the FALL 80 DECUS tapes.

Features of release 1.0 (4/15/80):

1. System logo, time, day and date
2. TTY #, privilege indicator, user name, the protection and
   (if not same) the default UIC and all allocated devices.
3. Task name, size, partition name, run priority, most state codes
4. All SET characteristics for a TTY.
5. GEN total in words, system error count, dynamic pool stats,
   and free space on SY: and LB: (see build file)
6. File structure status for all mounted files-11 volumes:
   device name, free space, owner, home block label (disks), and VCB label
7. Misc. switches: Help, All terminals, Remotes only, user Names only,
   a specific terminal, self, Mnemonic definitions, Identify version,
   display Login.txt message of the day, clear screen, Terminal
   characteristics, etc.
8. Continuous SYSTAT with specified sleep time

SYSTAT will attach to your terminal if possible, else break-through
writes will be used.

Some samples:

>SYS C

Status of J & J Research Timesharing at 3:57:49.1 PM on Thursday 7-FEB-80
 
CO0:    #<not logged in> [0,0]
           MTAACP      2.7K   GEN      200.  acp ckp nsd out prv stp
           SHF...      0.4K   SHFPAR   105.  fxd ncp prv stp
           F11ACP      6.3K   FCPPAR   149.  acp cal nsd prv stp
TT0:    $<RESTORE> [2,11] slave MT0:
           AT.T0       8.0K   GEN       65.  mcr prv stp tio wfr
           SLAVE       8.0K   GEN       65.  prv wfr
TT5:    $<SYSTAT DISTRIBUTION> [3,5] DK0: DK1:
           ...SYS      3.1K   GEN      140.  prv
           ...AT.      8.0K   GEN       65.  prv wfr
           CRF...      7.4K   GEN       50.  slv wfr
           ...TKB      31.4K   GEN      50.  wfr
TT6:     <JOANIE DEMKO> [100,105] ti
           ...MAK      9.5K   GEN       50.  ckp out stp tio wfr
TT7:     <JOY TAKEMOTO> [100,112] cts
           ...PIP      8.4K   GEN       50.  wfr
TT12:   $<CCL SOURCES> [1,16]
TT21:    <DORIS PARTYKA> [301,102] remote slave
           TT21       22.4K   GEN       50.
TT22:    <GLENN LEESMAN> [312,100] remote
           ...TEC     18.1K   GEN       50.  wfr

Up: 427:35:04  GEN=133.7K   Syserr=16.  Pool=1434.:3088.:39.  SY0:19641.

>SYS 21AT
TT21:   #<not logged in> [0,0] disabled remote
          speed=300 buf=72. lines=12. hfill=5 term=unknown
          nocrt echo noescseq nohold nolower nola180s nola30s novt05b
          noebc noformfeed nofdx nohht norpa typeahead novfill wrap

>SYS N
TT0:    $<CCL SOURCES>
TT5:    $<MAINTENANCE>
TT6:     <JOAN DEMKO>
TT7:     <JOY TAKEMOTO>
TT21:    <DORIS PARTYKA>
TT22:    <GLENN LEESMAN>

>SYS .
TT5:    $<SYSTAT DISTRIBUTION> [3,5]
           ...SYS    3.1K   GEN      140.  prv
           ...AT.    8.0K   GEN       65.  prv wfr
           CRF...    7.4K   GEN       50.  slv wfr
           ...TKB    31.4K   GEN       50.  wfr

>SYS FV

Device   Free Space     Owner     Volume label

DB0:        28181.      public    RSXM26
DB1:       104895.      public    SYSTEMS
DK0:         3045.      none      DEVBACKUP
DK1:      dismount      free
DK2:          138.      TT7:      SCRATCH
MT0:          512.      TT5:      SYSTAT

>SYS H

SYSTAT (SYS or SY or S) has the following switches:

A  - All terminals (irrespective of login status)
C  - Include CO:
F  - File structure status
G  - General statistics
H  - Help (this text)
I  - Identify SYSTAT version number
L  - Login message of the day
M  - Mnemonics for state codes and TTY characteristics
N  - User names only
R  - Remote terminals only
S  - Short SYSTAT
T  - Terminal characteristics
V  - Volume names for structures mounted and allocated to your TTnn:
     (all volumes if privileged) (the F switch must also be specified)
W  - indicate task sizes in words (default is Kwords)
X  - Clear the screen a la VT52
Zn - continuous SYSTAT with sleep time of n seconds (privileged)
nn - SYSTAT for terminal nn (TTnn:)
.  - SYSTAT for TI: (the issuing terminal)

The syntax is free format with invalid switches (characters) simply ignored.
Example: MCR>S 5ACTX.  All switches are parsed regardless of user privilege.


*** Building SYSTAT ***

The distribution consists of 7 files:

SYSTAT.OLB - Object library of all SYSTAT modules
SYSTAT.DOC - This document
SYSTAT.HLP - Switch HELP file
MNEMONICS.HLP - Mnemonics HELP file
SYSBLD.CMD - Task-build command file
SYSTAT.ODL - Overlay descriptor
LOGO.MAC - Macro source containing installation name.

The command file SYSBLD.CMD contains two global patches used to specify:

- full/half duplex terminal driver
- allow/disallow non-logged in remote SYSTATs (non-logged in execution is
  only possible by patching the MCRDIS module of MCR)
- account file LB:[0,0]RSX11.SYS is sorted by UIC (the ACNT program does
  this automatically in 3.2 and MPLUS and manually in 3.1)
- include/omit user names (First and last names are extracted from the
  system account file.  Specify omit if the search overhead is too large)

- Device name(s) and unit(s) for the general statistics summary line.

See the command file comments for patch specifics.

The file LOGO.MAC contains a PSECT with the text to be placed on the
first line of a SYSTAT.  Edit this file to reflect the name of your
installation.  The taskname of ...SYS will have to be changed for
a 3.1 system (suggest ...STA).

Two HELP files are read by SYSTAT (the H and M switches).  The files
must reside on LB:[1,2] as SYSTAT.HLP and MNEMONICS.HLP.

***

Once these two files have been edited, SYSTAT can be built by typing
TKB @SYSBLD.  Note that SYSTAT must be installed.