CCL -- Console Command Language
                                 RSX11M V4.0
                              V8.0 User's Guide
                                  16-Nov-81





          The normal user interface to an RSX11M operating  system  is
     via  MCR  (Monitor  Console  Routine).   If terminal input is not
     specifically requested by a task, all data, or commands typed  in
     at  a  user's terminal are sent by the terminal driver to MCR for
     decoding.  The MCR  task  (and  its  child  ...SYS)  decode  user
     commands  (ACT,  ABORT,  RUN,  DEV,  etc.).  Tasks installed with
     special names of the form ...XYZ are treated as an  external  MCR
     command.  Hence if a user types:
      
                        XYZ commandline
      
     The  'commandline'  in  its  entirety  (or  at  least  up  to  79
     characters)  is  sent  as  input to the task ...XYZ.  This is the
     conventional  way  of  supplying   most   system   commands   and
     controlling  the  operation  of the RSX11M utility programs.  The
     limitations of this method are that each task must  be  installed
     to  be  treated  as  an  external  MCR  command,  and  each extra
     installed task  uses  valuable  pool  space.   Moreover,  because
     installed  tasks  use  a  critical  system  resource (pool), only
     privileged users are allowed to install and remove tasks from the
     system.   The normal user is restricted to starting tasks via the
     RUN command or using those tasks already installed.

          To alleviate this problem, a user tailorable Console Command
     Language  (CCL)  has  been  implemented which allows each user to
     have a private task control language.  CCL may either be used  as
     an  alternate  CLI  in which case all user typed in command lines
     are passed first to it, and/or it may be used as a catchall  task
     to  which are passed command lines rejected by MCR either because
     they are illegal MCR commands  or  because  the  command  is  not
     recognized  as an external MCR command (a task installed with the
     name ...XYZ).

          If CCL is not used as the terminal's CLI, and a  user  types
     in  a  command line, MCR is given first crack at decoding it.  If
     MCR does not recognize  the  command  (first  three  letters)  as
     either  an  internal  (like SET) or external command, the command
     line is sent to CCL which is installed as  ...CA.,  the  catchall
     task.   CCL  in  turn  checks  to  see if it can find the command
     (command stops at first  space,  comma,  =,  <,  /,  or  carriage
     return).  First, CCL checks its internal command tables to see if
     the command matches.  If a match is not found, CCL then  scans  a
     user  file  USERCCL.CCL to see if the command is present.  If the
     command  is  not  in  the  user  file,   CCL   checks   in   file



                                                                Page 2



     LB1:[1,5]SYSCCL.CCL  to  see  if  the  command  is  a  system CCL
     command.  If the command is not found anywhere, CCL will  attempt
     to  spawn  ...CA2,  a  second  catchall  task.   If ...CA2 is not
     installed, a warning message is printed.  If ...CA2  is  spawned,
     however, CCL will pass the command line on to ...CA2 and exit.

          Each user may have an  individual  CCL  (USERCCL.CCL)  file.
     Instructions  on  how  to  structure  a  CCL file and some worked
     examples are in APPENDIX A.  In APPENDIX  B,  passing  a  command
     line to a task via the RUN command is discussed.

          If CCL is installed as a CLI and if a terminal issues a  SET
     /CLI=TI:CCL,  then  all commands are received by CCL first.  This
     means all MCR commands can be intercepted before they get to MCR.
     If CCL is installed and is being used as a CLI, it first converts
     the command line to upper case, then scans  its  internal  table,
     then  SY:[uic]USERCLI.CCL and finally LB1:[1,5]SYSCLI.CLI to find
     the command.  If it can't find the command, it sends the command,
     as  typed  in,  to  MCR.  CCL knows if is being used as a CLI and
     adjusts its behavior accordingly.  For example, when  used  as  a
     catchall task, CCL can translate a single typed in command into a
     string of MCR commands.  When used as a CLI, only one command  is
     allowed  so  that  the user's CLI will not vanish for an extended
     period of time.  Moreover, single commands  which  would  disable
     the  terminal  cli for periods of time (HEY, %R) are also ignored
     or rejected.





                                                                Page 3



                             System CCL Commands



          A wealth of CCL commands exist to  simplify  the  amount  of
     type  in  a  user  has to do, and to allow the user access to the
     wide variety of RSX utility programs which  are  not  permanently
     installed  in  the  system.   Version  8.0  of  CCL  includes two
     optional  internal  command  sets,  handled  by  DCL  and  $TABLE
     respectively.  The discussion below details the features provided
     by DCL which is conditionally assembled by defining both $DCL and
     $PIP   in   a   conditional  assembly  file,  PRECCLASM.MAC.   An
     alternative/enhancement to DCL has been added to CCL which allows
     CCL  to scan an internal, installer defined table (.PSECT $TABLE)
     of commands.  This command table is enabled by defining $DCLTB in
     PRECCL.MAC,  and  consists of a command list defined in TABLE.MAC
     with the same command set syntax used in the user and system .CCL
     files  (see  APPENDIX A).  The actual layout of the command table
     is  given  in  APPENDIX  E,   and   CCLTABLE.DOC   provides   the
     documentation  for  the  distributed version of TABLE.MAC.  It is
     strongly urged that the internal table file (TABLE.KMS)  be  used
     since support for the hard coded internal parsing will be dropped
     in a future release.

          To simplify the process of  selection  of  the  various  CCL
     configurations a command file (CCLGEN.CMD) is provided which will
     automatically create the entries in PRECCL.MAC,  and  include  or
     not include a variety of internal table files as desired.  To aid
     users in creating an internal CCL table  file  from  a  standard,
     debugged  USERCCL.CCL  or SYSCCL.CCL table file, the command file
     TABLEGEN.CMD is provided.

          A number of  commonly  used  commands  are  built  into  CCL
     (conditionally  assembled by defining $DCL $DCLTB in CCLGEN.CMD).
     The  commands  SORT,  DELETE,  DIRECTORY,  LIST,  PURGE,   SPOOL,
     TRUNCATE, FREE, UIC, POOL, ATS, DLG, SHW, SHQ, HEY are internally
     decoded by CCL either as part of the internal DCL code section or
     from  an  internal table.  Most of these commands are executed as
     PIP file commands and their syntax is,
      
                COMMAND [filespec][,filespec]...
      
     The commands DIR and SORT do not require a file  specifier.   All
     the  other file commands require a file or files to be specified.
     These commands have the following PIP equivalents:
      
     DEL[ete]           filespec                PIP filespec/DE/LD
     DIR[ectory]        [filespec]              PIP [filespec]/LI
     FRE[e]             [ddn:]                  PIP [ddn:]/FR
     LIS[t]             filespec                PIP TI:=filespec
     PUR[ge]            filespec                PIP filespec/PU
     SOR[t]             [filespec/SW]           SRD [filespec/SW]/LI
     SPO[ol]            filespec                PIP filespec/SP



                                                                Page 4



     TRU[ncate]         filespec                PIP filespec/TR
      
     In addition, the user can issue short form  commands  to  display
     certain status information.
      
     ATS  [TTN:]                        ACT [/TERM=TTN:]
     BELL                               Ring terminal bell.
     DLG                                DEV /LOG  Show logged on terms.
     ERASE                              Erases VT52 screen.
     HEY taskname                       Notify user when 'TASKNAME' exits
     IDENT                              Display CCL's version #.
     LIBUIC                             SET /LIBUIC
     NOSCROLL                           Sets VT100 to jump scroll.
     PAGE                               Erases VT100 or TEK 4014 screen.
     SHQ                                QUE /LI   Show spool queue.
     SYS                                SET /SYSUIC
     SCROLL                             Sets VT100 to smooth scroll.
     UIC                                SET /UIC  Show current UIC.
     UIC GRP,MEM                        SET /UIC=[GRP,MEM]
     UIC GRP MEM                                "
      

          All other CCL commands are decoded from the CCL internal  file
     (enabled  by  defining  $DCLTB  in  CCLGEN), or the user and system
     files.  The order of searching for a command match is to check  DCL
     (commands listed above), scan $TABLE which appears just like a file
     to CCL, scan USERCCL.CCL, and  finally,  LB1:[1,5]SYSCCL.CCL.   The
     device  LB1:   is  normally a globally assigned logical device (ASN
     DDu:=LB1:/GBL) and is normally the system device LB0:.  It is coded
     as  LB1:   to allow the user to use CCL commands when the local LB:
     is assigned to  an  alternate  device  for  doing  a  SYSGEN.   The
     assembly  symbol  $LB0  will  enable  CCL  to look for files on LB:
     rather than LB1:  if it is defined (not recomended).


                              System Utilities
      
        Note: Command lines for utilities started by CCL are limited
              to 40-50 characters.  These commands are placed in
      SYSCCL.CCL
      

      
     ACCLOG                     RUN $ACCLOG
      
     ACNT                       RUN $ACNT
      
     BASIC                      RUN $BASIC/INC=4200
      
     BCK                        RUN $RMSBCK
      
     CHKSUM filespec            PAT NL:=filespec/CS,filespec
      



                                                                  Page 5



     CDA DEV:=MM0:/SW           CDA DEV:=MM0:/SW,LB:[1,54]RSX11M.STB/STB
      
     CMP command line           Identical to CMP syntax
      
     CVL command line           Identical to CVL syntax
      
     DMP command line           Identical to DMP syntax
      
     DSP                        RUN $RMSDSP
      
     FLX command line           Identical to FLX syntax
      
     FRG dev:                   Identical to FRG syntax
      
     FTB commandline            Identical to FTB syntax
      
     LBR commandline            Identical to LBR syntax
      
     PAT commandline            Identical to PAT syntax
      
     RNO commandline            Identical to RNO format.
      
     RST                        RUN $RMSRST
      
     SHOW                       @LB:[1,2]SHOW.CMD
      
     SLP @commandfile.SLP       Identical to SLP syntax
      
     VFY commandline            Identical to VFY syntax
      
     VMR                        Identical to VMR syntax
      
     ZAP                        Identical to ZAP syntax


     ^^Privleged System Commands


     ACS DEV:/BLKS=N            Identical to MCR
     ERF                        Identical to MCR
     ERRORS                     @LB:[1,6]ERROR
     LOA(D) DEV:                LOA DEV:/PAR=DRVPAR
     PSE                        Identical to MCR
     SHUTUP                     @LB:[1,2]SHUTDOWN
     SYE                        Identical to MCR
     UFD DEV:[UIC]              Identical to MCR
     UNL(OAD) DEV:              Identical to MCR



                                                                Page 6



                                 Appendix A


                           CCL Command File Format

          When ...CA.  is activated from MCR...  the  program  obtains
     the  command  line from MCR and divides it into units.  The first
     unit is the KEYWORD which is used to select the command from  the
     definition  (.CCL)  files.   The  keywords  are  matched  up to 8
     characters.  The other units become parameters 0 thru  9,  and  A
     thru C.  The alphabetic parameters represent major subsections of
     the command line.  A includes the entire command line  minus  the
     keyword.   B includes all input up to the first space or carriage
     return minus the keyword and any leading switches (see  parameter
     0).  C includes everything from the first space to the end of the
     command line (minus space delimiter).  Parameter 0  includes  any
     leading switches appended to the keyword, continuing to the first
     space (e.g.  BRU/REW, parameter 0 = /REW).  The leading  switches
     may  be  seperated  from  the  keyword by spaces (e.g.  BRU /REW,
     parameter 0 = /REW).  Parameters 1-9 are then assigned, in order,
     to  each  unit  in  the  command line (minus delimiters) that are
     separated by spaces, commas, '=', or  '<'.   Given  this  command
     breakdown:   the  MCR  line includes the KEYWORD and parameter A;
     parameter A includes parameters 0, B, and C;   and  parameters  B
     and C include parameters 1-9.  These parameters are then inserted
     into a new MCR  command  line  under  the  direction  of  a  user
     supplied  template,  and resubmitted to ...MCR.  CCL also has the
     option to prompt for missing parameters, and  will  exit  if  the
     required  input  is  terminated  by  CTRL-Z.   If  the %Q special
     character is  in  a  CCL  command  line,  and  a  required  input
     parameter  default  field  is  null  (ie  %),  CCL will also exit
     without sending the command to MCR.

          At assembly time, an internal  "file"  may  be  included  in
     CCL's  search  for  a  keyword  match.   If  the symbol $DCLTB is
     defined in the conditional assembly file PRECCL.MAC, CCL  expects
     to  find $TABLE.  The MACRO code defining $TABLE is in TABLE.MAC,
     and comprises a list of internal command lines in a form  similar
     to the .CCL file records (see APPENDIX E).  Each internal command
     is preceeded by a 1 word byte  count  followed  by  n  bytes  and
     aligned on the next word boundary.  If the internal search is not
     enabled or a match is not found, CCL  attempts  to  open  a  user
     command  definition  file (SY:USERCCL.CCL) under the user's logon
     UIC.  If present, it is opened and scanned for a  keyword  match.
     If  it is not present or a keyword match is not found, the system
     command  definition  file  (LB1:[1,5]SYSCCL.CCL)  is  opened  and
     scanned.   If  the  command  is  not  found after the scan of the
     system file completes and the keyword  is  terminated  by  a  '?'
     character,  the  files  are  rescanned for a command '?' which is
     called with parameter A redefined to include the entire  original
     MCR  command  (minus  the  '?').  This was added as an additional
     form of help command.  The internal (or system) CCL command  file
     interprets  the  '?' command as 'HELP'.  Hence, PIP?  is the same



                                                                Page 7



     as HELP PIP.  If the keyword did not end with a '?', CCL will try
     to  spawn to ...CA2, the catchall task for CCL.  If ...CA2 is not
     installed, CCL flags the  keyword  as  an  unrecognized  command,
     otherwise,  the  entire  command  line is given to ...CA2 and CCL
     (...CA.) exits.  

          The command definition files have three main types of lines,
      
        1)  beginning '$' - keyword lines (identification line)
        2)  beginning '?' - keyword lines (input querry line)
        3)  beginning '*','+', or '-' lines (action lines).
      

          The command file consists of a keyword  identification  line
     followed by optional input query lines and finally by one or more
     action lines.  The match  procedure  consists  of  comparing  the
     keyword  from  the  command  line with the keyword in the command
     file.  If the minimum  length  of  match  is  satisfied  and  the
     characters  up  to  the  end  of  the  command line keyword match
     characters  in  the  keyword  line,  the  match  is   successful.
     Otherwise  failure  is  signaled  and another '$' keyword line is
     searched for.  When no more keyword lines are found in the  file,
     the  file  is  closed  and  the search has failed in finding that
     command line.
      
     EXAMPLES:
      
        $1111M
        $2811ASSEMBLE
        ?1Filename
        *MAC %1%=LB:[1,1]EXEMC/Ml,[11,10]RSXMC/PA:1,LB:%U%1%
        $1411TYPE
        $2411LIST
        ?BFile
        *PIP TI:=%B%
        $2823COMPARE
        ?1File 1
        ?2File 2
        ?3Output
        *CMP %3?\TI:%%3.SLP%/SL=%1%,%2%
        $5511BUILD
        ?1FILE
        +F4P %1.OBJ;1%=1%
        +TKB %1.TSK;1/CP/FP%=%1%,LB:[1,1]F4POTS/LB
        +PIP %1.OBJ;1%/DE
        *RUN %1%
        $3300ACS
        *INS $ACS/PRM="%1/BLKS\SY:/BLKS%=%2\0.%"/RUN=REM
      
      

          The commands " M file " and "ASSEMBLE FILE"  have  the  same
     effect,  they  create  an object file from the source in [12,10].



                                                                Page 8



     The command ASSEMBLE given without any parameters would result in
     the  prompt  "Filename?"  since the specification for the command
     requires at least one parameter, and it  is  to  prompt  for  one
     parameter  if  it is not present.  The specification ensures that
     "M " is matched by the single character alone,  and  ASSEMBLE  by
     the characters AS ASS ASSE ASSEM thru ASSEMBLE.




                                Keyword Lines


     The keyword line is as follows,
      
        $<m1><m2><mp><ap>KEYWORD
      
                First line of a command set.  There may be many
                keyword lines for the same action line.
      
     where:
      
        <m1>    Minimum number of characters to match.
        <m2>    Maximum number of characters to match.
                (If 0, no check for user KEYWORD > file KEYWORD is
      made).
        <mp>    Minimum number of parameters required.
                If this number of parameters is not present then
                parameters will be prompted for.
        <ap>    Maximum number of parameters to question for if 
                less than <mp> parameters are input.  In the case
                where prompting this number is the highest prompt
                to be requested.
      
             KEYWORD is the command keyword.
      
     The  keyword  consists  of  a  character  string  to  be  matched
     identically  by  the  CCL  processor.  If 'm2' parameter is 0, no
     checking for maximum  keyword  length  will  be  performed.   For
     example,  given two keyword lines $3400DUMP and $3000DUMP, a user
     command of 'DUMPIT', will fail to match the  first  keyword  line
     (DUMPIT  exceeds  maximum  of  4  characters), but will match the
     second keyword line (maximum keyword length  checking  disabled).
     Keywords  may  extend beyond the 9 character limit imposed by the
     single digit parameters m1 and m2 by adding  60  (octal)  to  the
     desired  number  and  entering the corresponding ASCII character,
     e.g.  to  specify  m2  =  11  (dec.)  use  ASCII  character  ';'.
     Terminators for the keyword typed by the user are space, '/', and
     carriage return.







                                                                Page 9



                              Input Query Lines



          The input query line is as follows:
      
        ?<n>QUESTION-TEXT
      
     Where:
      
        <n> is the parameter number (0-9,A-C) (they should be in
      order)
      
     If the correct number of parameters are supplied no questions are
     asked.   If  fewer  parameters  have been supplied then required,
     parameter <n> is checked, and, if it  is  null  (undefined),  the
     question  is  asked  with  the user's response defining parameter
     <n>.  If parameters are skipped then they will only  have  values
     if they were given on the original command line.




                                Action Lines


     The action line is specified as follows:
      
        <#>KEYWORD command-line<+>
      
     where:
      
        <#> is one of '-', '+', or '*'.
        <+> is null or '+'
      

          Action lines come in two varieties.   '-'  lines  are  lines
     which  instruct  the  program to wait for a given task.  The task
     name is an  absolute  name  and  does  not  take  on  a  terminal
     qualified  name  (V4.0 does not have executive task dispatching).
     CCL will issue a connect directive to the specified task  and  if
     the  task  is  found and is active, it will stop itself until the
     task exits.  The format for the wait line is
      
                -<6-char-taskname>
      

          The '*' and '+' command lines differ only in  that  the  '+'
     line  signals  that  further command lines follow in the file.  A
     '*' signals that the command is the last or  only  command  line.
     The  text in the action line is copied except that any parameters
     present may be substituted into the text line.  The action  lines
     consist  of  valid  MCR  commands  which must not involve further



                                                               Page 10



     calls to CCL.  Any action line that is too long to be placed on a
     single line may be continued to the next line by placing a '+' as
     the last character in the action line.  Note:  the '+'  must  not
     be  in  the  middle of a parameter substitution string, rather it
     must stand alone as if it were to be  placed  directly  into  the
     command  line.   Though this facility is provided, it is far more
     likely to exceed the ultimate  MCR  command  line  length  of  79
     characters before running out of action line space.

          Three special fields  in  the  action  line  suspend  direct
     transfer  of  characters  from the action line to the new command
     line:  1) Parameter substitution fields, 2)  Parameter  test  and
     substitute  fields, and 3) Special parameter substitution fields.
     A '%' denotes a substitution argument, and is normally associated
     with  a  parameter number <pn> or special symbol.  Parameters are
     defined by presence of delimiters in  the  original  MCR  command
     line or by response to an input query line.  The comma separating
     the group and member numbers in a UIC field ([g,m]) is treated as
     a  special  case, and not considered a delimiter, thereby placing
     the entire uic within one parameter.

          Parameter  substitution  fields  allow  insertion   of   the
     parameters  0-9,  A-C  into  the  new  command  line by using the
     format:
      
        %<pn><option1><option2><option3>%
      
     where:
      
        <pn>            is the parameter to be substituted (0-9,A-C)
        <option1>       is one of null, '=',' ', or ','
        <option2>       is one of null, or <test-char>text-string
        <option3>       is one of null or _\text=string
      
      

          The  first  optional  element  denotes  a  character  to  be
     inserted before the parameter provided the parameter is not null.
     Only ',' , ' ', or '=' are allowed as preceeding characters.  The
     second  option  denotes  elements  that are to be appended to the
     parameter if the first, test, character did  not  appear  in  the
     parameter.   Typically,  these  are  only those which denote file
     extensions and version numbers.  If the <test-char> is not  found
     in  the body of the parameter, that character and the text string
     following it (up to '%' or '\') are appended  to  the  parameter.
     The  final  option  denotes a text string to be inserted directly
     into the  command  line  if  parameter  <pn>  is  null  (the  '\'
     character is not included).

          The parameter test and substitute field allows the  user  to
     control insertion of text strings into the new command line based
     on the status of a parameter (null or  not  null).   It  has  the
     form:



                                                               Page 11



      
        %<pn>?<string1><_\string2>%
      
     where:
      
        <pn>            is the parameter to test (0-9,A-C)
        ?               Key character to indicate a test field
        <string1>       is one of null or ASCII string
        <_\string2>     is one of null or ASCII string preceeded by 
                        backslash.  If null and %Q is found, CCL will
                        exit without sending a command to MCR.
      

          Encountering the '%<pn>?' field in the  action  line  causes
     CCL to determine if parameter <pn> is null.  If <pn> is null, the
     ASCII string preceeded by '\' and ending with % will be  inserted
     directly  into  the new command line (minus delimiters).  If <pn>
     is not null, any string immediately following the '?' up to a '\'
     or '%' will be inserted into the new command line.  If a required
     input field is defaulted and the default substitution  string  is
     NULL  (ie  \%)  and  the  %Q  (quit)  special  parameter has been
     encountered, CCL will exit without sending a command to MCR.

          Special parameters are '%' followed by a single character:  
      
        %<spec-char>
      
     where:
      
      <spec-char>  is one of '$','%','D','G','M','Q','P','R','T', or
      'U'.
      
     The special parameters are as follows,
      
        
        %$      As the last element in the command line, it  signifies
                that CCL should SPAWN the command to MCR and exit
                (ESCAPE) rather than to stop itsef and wait for exit 
                status.
                Must be the last element of a CCL command.
        %%      Enables the second % to be accepted as a literal.
        %D      A DEBUG switch. When encountered, the expanded 
                command line is printed (up to the %D) at the 
                issuing terminal rather than being sent to MCR.
        %G      The group number of the UIC.
        %M      The member number of the UIC.
        %P      The action line will be printed on TI:
        %Q      Exit without sending a command to MCR if required
                parameter has a NULL default parameter.
        %R      Ring the terminal bell when CCL exits
        %T      The user's terminal ID (Tnn or Vnn where 'nn' is the
                terminal number and 'Tnn' or 'Vnn' are for real 
                terminals and virtual terminals respectively.



                                                               Page 12



        %U      The user's UIC including '[,]'.
      
        Note: the previous release of CCL considered '%A' a special
        parameter.  'A' is now considered a standard parameter, and is
        manipulated via the standard parameter substitution fields
        discussed above.  Also the previous release used the special
        character %B to ring the terminal bell.  This release uses %R.
      
     Examples:
      
        %U      ->      [012,010]
        %G      ->      012
        %M      ->      010
        %T      ->      T14 if TT14:, V1 if VT01:
                        useful for creating multi-terminal tasks
                        (ie BAST2) using INS/TASK=nnn%T.
      
      

          After a CCL command is issued, CCL stops  itself  until  the
     command  is  complete.   When  the task completes it returns exit
     status back to CCL, which in turn passes exit status back to  the
     task which invoked it (such as ...AT.).  If the user wishs CCL to
     exit before the command is  finished,  a  %$  may  terminate  the
     command  in  the command skeleton in the user's (or system's) CCL
     file.  If the users system does not have RPOI$ (chain  directive)
     support,  exit  status  and  MCR  syncronization  will be lost by
     exiting before the MCR command has completed.  (For CCL  (...CA.)
     to  syncronize  correctly  parent/offspring  tasking  support  is
     required.).  However, if RPOI$ is a valid directive, and a %$  is
     found,  CCL  first  tries  chaining  the  command  to MCR.  If it
     succeeds,  the  exit  status  linkage  is  passeded  on  the  the
     offspring  task  and CCL immediately exits (MCR syncronization is
     maintained).  If the RPOI$ directive fails, CCL  tries  to  spawn
     the command to MCR and will immediately exit after the spawn.  In
     this case exit status information and MCR syncronization is lost.
     If a %$ does not terminate the command, the command is spawned to
     MCR and CCL stays in core untill its  offspring  exits  at  which
     point it exits and passes back exit status to its parent.




     From the above examples:

     In ASSEMBLE / M the filename given would normally be a plain name
     e.g.  MCRDIS which would result in (for UIC=[12,10]) 
      
        MAC
      MCRDIS=LB:[1,1]EXEMC/ML,[11,10]RSXMC/PA:1,SY:[012,010]MCRDIS
      
     In LIST or TYPE since the required number of arguments is set  to
     one,  and  the  number of arguments to be prompted for is one the



                                                               Page 13



     results are
      
     TY file            -> PIP TI:=file
     T file.slp         -> PIP TI:=file.slp
     TYPE file,file2    -> PIP TI:=file,file2
     TYPE
     FILE? myfile       -> PIP TI:=myfile
      
     In COMPARE, the minimum number of parameters required is  set  to
     2, but 3 will be prompted for if less then 2 entered:
      
     COMPARE MCRDIS
     File 2? MCRDIS;-1
     Output? <cr>       -> CMP TI:/SL=MCRDIS,MCRDIS;-1
      
     CO MCRDIS,MCRDIS;-1        -> CMP TI:/SL=MCRDIS,MCRDIS;-1
      
     or alternatively with the definition
      
        $2722COMPARE
        ?1Files
        ?2Output
        *CMP %2%%1.SLP%/SL=%1;-1%,%;0%
      
     one then has
     MCR>COM
     Files? INDROT
     Output?            -> CMP INDROT.SLP/SL=INDROT;-1,INDROT;0
     or
     MCR>COM
     Files?INDROT
     Output?TI:         -> CMP TI:INDROT.SLP/SL=INDROT;-1,INDROT;0
      
      however altering this to
      
        $2712COMPARE
        ..........leads to
      
     MCR> COM INDROT    -> CMP INDROT.SLP/SL=INDROT;-1,INDROT;0
     MCR> COM INDROT TI:-> CMP TI:INDROT.SLP/SL=INDROT;-1,INDROT;0
     and
     MCR> COMPARE
     Files?INDROT
     Output?TI:         ->       ditto
      
     Because the number of parameters to prompt for was set  to  2  if
     the required of 1 was not present.  The example line for ACS uses
     an INS  enhancement  described  in  APPENDIX  B.   The  effective
     command lines generated by various ACS commands are,
      
     $3300ACS
     *INS $ACS/PRM="%1/BLKS_\SY:/BLKS%=%2_\0.%"/RUN=REM
      



                                                               Page 14



     ACS                ->ACS SY:/BLKS=0.
     ACS DP:            ->ACS DP:/BLKS=0.
     ACS =498.  ->ACS SY:/BLKS=498.
      
      
     In this example, the '=' delimits a switch value  rather  then  a
     standard  filespec  typ  parameter.   CCL  considers the '=' as a
     valid parameter delimiter thereby assigning the numeric entry  to
     parameter  2  (same  confusion/problem  holds for things like FMT
     /DENS=DOUBLE, etc.) In the first case, parameters  1  and  2  are
     null,  therefore  SY:/BLKS  is  substituted  for  %1%  and 0.  is
     substituted for %2%.  In the second  case,  parameter  1  is  not
     null,  so  DP:   is  inserted  into the command line.  No '/' was
     encountered in parameter 1, so /BLKS  is  added  as  the  default
     extender.   Parameter  2 is null, so 0.  is inserted into command
     line.  In  the  final  case,  parameter  1  is  null,  so  insert
     SY:/BLKS, but parameter 2 is not null, so it is inserted.  
     EXAMPLE:
      
     1.  UIC            ->  SET /UIC
     2.  UIC G,M        ->  SET /UIC=[G,M]
     3.  UIC G M        ->  SET /UIC=[G,M]
      
      
     The following entries in SYSCCL.CCL produce the above syntax.  
                $3300UIC
                *SET /UIC%1?=[%%1%%2,]%
      
       Case 1.  No parameters present so   SET /UIC sent out.
      
       Case 2.  Parameter 1 is not null, so '=[' is inserted, 
                followed by parameter 1, and finally parameter 2
                is preceeded by ',' and trailed by ']' (unless ']'
                was entered as part of parameter 2).
      
       Case 3.  Same as case 2, only space delimits parameter
                1 and 2 rather than comma.
      
      
     EXAMPLE:
      
     DIRECTORY filespec         ==>PIP filespec/BR
      
          The CCL entries to produce this command would be
      
                $3900DIRECTORY
                *PIP %1;*%/BR
      
       Case 1.  The command DIRECTORY would have parameter 1 as 
                null so the MCR command would be  PIP /BR.
      
       Case 2.  The command DIR *.CMD would have appended a ;* 
                since there is no ';' in the command line typed in.  



                                                               Page 15



                So the command is passed back to MCR would be  
                PIP *.CMD;*/BR.
      
       Case 3.  The command DIR *.CMD;1  would have nothing appended 
                since a ';' is found in the input command.  Hence, 
                the command PIP *.CMD;1/BR  would be sent to MCR
                by CCL.



                                                               Page 16



                                 Appendix B


                  Passing Command Lines Via The RUN Command


     Running a task via the RUN filespec facility causes the system to
     RUN  the  task and remove it on exit.  In reality MCR decodes the
     RUN command and then  issues  an  INS  filespec/RUN=REM/TASK=TTn.
     The /RUN=REM switch specifies that the task is to be removed from
     the installed task list when it  exits.   In  a  standard  RSX11M
     system  there  is  no  way  to  pass the task an MCR command line
     unless it is installed as an external MCR command (...XYZ).

          To partially bypass this restriction, a new switch has  been
     added  to  INS (and hence the RUN command), the /CMD switch.  The
     syntax is
      
                RUN filespec/CMD="XXX txt"
      
     where 'txt' is an ASCII command and where XXX  represents  the  3
     character  name  the  task  would  be  invoked with if it were an
     installed MCR command.

          It should be pointed out that a normal MCR command line  may
     be  up  to 80 characters long.  The longest command line possible
     via the RUN command is 53 characters (if filespec is 9 characters
     long).  Adding a /TASK=TSKNAM switch , or a /PRI=N switch further
     decreases the maximum length in a command by 12 and 7  characters
     respectively.   CCL  checks to see if an expanded command line is
     <80  characters  long.   If  not  it  issues  an  error  message.
     However,  when  used  CCL  is  used  with  the RUN command, error
     checking is more  difficult  because  of  the  implicit  /RUN=REM
     switch  which  is automatically inserted into the command line by
     SYS as the command is passed on  to  INS  to  Install,  Run,  and
     Remove  the  task.   If  it  is  desired  to  have CCL do as much
     checking on command line length as  possible,  prototype  command
     lines  in either USERCCL.CCL or SYSCCL.CCL should avoid using the
     RUN command and should replace it with INS filspec/CMD="XXX txt".
     If  INS  sees  the  /CMD switch it will automatically install the
     task as RUN=REM.  This will save 8 characters.


     EXAMPLE:
      
        INS LB:[1,53]DMP/TASK=...DMP/CMD="DMP TI:=3831.ARC/AS"
      

          If command lines are not expected to be long and the task is
     frequently  used  by a large number of users, the CCL command can
     RUN (INS /RUN=REM) the task with a taskname of the  form  ...XYZ.
     This  means  when  the next user goes to use the task, and if the
     first user is still using the task, multiple copies of  the  task



                                                               Page 17



     will  be  created, one for each terminal using the task.  As each
     task exits it will be removed from the installed task list.  This
     cuts  down  somewhat  on  the overhead of looking through the CCL
     command files.  A simple example of this is BASIC on our  system.
     BASIC  is not normally an instaled task, rather when a user types
     BASIC, CCL runs BASIC and installes  it  with  the  name  ...BAS.
     Once  the origional copy of ...BAS is active, multiple copies can
     be created at various terminals.  For tasks  which  require  long
     command  lines (BASIC requires none), this method is not suitable
     and it may be necessary  to  RUN  the  task  without  the  /TASK=
     switch.   This  means  that the task will be run with the name of
     the terminal (TTN).  



                                                               Page 18



                                 Appendix C


                 Passing Variables to Indirect Command Files


     The Indirect File processor (.AT) now supports passing parameters
     on command lines.  One may now type
      
                @CMDFILE PARAM1 PARAM1 PARAM1 PARAM4.....
      
     and have the parameters PARAM1.....PARAM9  transfered  to  string
     variables  P1 to P9 in the indirect file processor.  The variable
     P0 will contain the '@CMDFILE' string.
      
     EXAMPLE:
      
          A powerful example of using this is the BUILD CCL command.
      
        BUILD tsknam,(NO)LIST,(NO)BUILD,(NO)MAP,(NO)YES
      
     This command passes the string variables 
      
                tsknam,(NO)LIST,(NO)BUILD,(NO)MAP,(NO,YES)
      
     to @[1,5]BATCH/NOLI PARM1 PARM2 PARM3 PARM4.  Here tsknam is  the
     name of the FORTRAN IV file to compile, with or without a listing
     (LIST, NOLIST),BUILD or NOBUILD,  determine  whether  or  not  to
     taskbuild  (with  or  without producing a MAP), and able (YES) or
     not able (NO) to be run by other users.  A listing  of  BATCH.CMD
     is  provided  as  a guide to writing complicated command files to
     which CCL passes parameter strings.  Note  in  the  listing  that
     .TESTFILE  is  used to test to see whether or not the source file
     requested exists, and the command file @BATCH creates,  tests  to
     see  if  the  F4P compilation was successful.  If the compilation
     failed the command file terminates gracefully, saving substantial
     time.



                                                               Page 19



                                 APPENDIX D


                     Modifications to CCL for RSX11M V4.0



          CCL   is   highly   modified   for   the    V4.0    release.
     Exit-with-Status  has  been  added.   If a CCL command can not be
     executed (file not found, line too long, etc) a fatal exit status
     of  4 is returned to the indirect file processor.  Because DEC is
     now supporting passing command lines to non-installed  tasks  via
     the  /CMD="CMDLIN"  switch, support for the /PRM="txt" string may
     be dropped.  The SLP file to provide (almost) the old style  /PRM
     switch is included as an optional feature patch on KMSKIT.  It is
     not required for use with  CCL.   However  existing  CCL  command
     files  using  the  /PRM switch will have to be re-written to make
     use of the /CMD switch.

          CCL requires the the SPAWN and STOP  directives.   CCL  also
     requires  the  EXST$  (Exit  With  Status)  directive in order to
     return exit status.   The  RPOI$  directive  is  optionally  used
     instead  of  SPAWN  (where possible) so that CCL can exit at once
     after passing on the command line.  A check is now made to see if
     the  expanded  command  line is too is too large to fit in an MCR
     buffer.  This saves much frustration  when  one  enteres  longish
     commands,  and the tasks reject them at some unknown point in the
     command line.  If CCL detects that the command  is  too  long  to
     pass  on , it warns the user and prints out the offending line up
     to the point at which it overflowed the allowed line length.  

          Since the various PIP, CCL commands seem to be the most used
     and  useful,  these  commands  (  DIR[ectory],  LIS[t], DEL[ete],
     PUR[ge], SPO[ol], and  TRU[ncate],  etc.)  have  been  explicitly
     built  into  CCL's  command  parsing  if  the internal table file
     TABLE.KMS  is  used.   This  speeds  up  command  response  quite
     noticeably.

          Perhaps most importantly, this release of CCL  supports  the
     use  of CCL as an alternate CLI for MCR.  The user wishing to use
     CCL in this way should be sure to create LB1:[1,5]SYSCLI.CCL with
     at  least a dummy entry.  CCL knows whether it is being used as a
     CLI or as the catchall (...CA.) and  will  operate  correctly  in
     either  way.  It will work correctly on systems without alternate
     CLI support, but only  as  a  catchall  task.   To  work  as  the
     catchall  task  it  must  only  be  installed as ...CA.  If it is
     acting as a CLI it uses slightly different names for  its  system
     and  user CLI files (SY:[uic]USERCLI.CCL and LB1:[1,5]SYSCLI.CCL)
     to provide greater flexibility for what  commands  one  wants  to
     search through before defaulting to an MCR command.



                                                               Page 20



                                 APPENDIX E


              Creating/Modifying internal command table, $TABLE





          CCL will search an internal command table prior to  scanning
     the  user  and system .CCL files if the conditional assembly file
     (created by CCLGEN) defines the symbol $DCLTB.  With this  option
     enabled,  the  user  must supply a file defining $TABLE to be the
     start of the internal table  (distributed  in  TABLE.MAC).   This
     command  table  uses the same keyword/query/action line syntax as
     the .CCL files (see APPENDIX A).  Define the  internal  table  as
     follows:
      
     $TABLE::                   ;global definition of Table's start
      address
        .WORD   n               ;insert byte count for keyword line
        .ASCII  /  /            ;define keyword line
        .EVEN                   ;get to word boundary
        .WORD   n               ;define byte count for next line
        .ASCII  /  /            ; etc.
        .EVEN                   ;  etc.
        .WORD   n               ;   etc.
        .....
      
        .WORD   0               ;define end-of-file marker
      

          Great care must be taken in getting the byte counts  correct
     for  the  internal  table.   Incorrect  counts  can  cause CCL to
     malfunction in a wide variety of ways.  The easiest way of making
     a  table is to convert an existing USERCCL.CCL or SYSCCL.CCL file
     to an internal table file using TABLEGEN.CMD.

          Two flavors of internal  tables  are  provided.   The  first
     table,  TABLE.KMS,  should be used if the user wants all the same
     functionality as the origional CCL with the capability of  adding
     more internal commands later.  If this is desired, $DCLX and $PIP
     are not defined and $DCLTB is  defined.   Some  of  the  internal
     commands  can  not  be  created  as  CCL  commands directly (HEY,
     DELAY...) and are  retained  in  the  origional  DCL  section  of
     CCL.MAC.   The  CCL produced in this manner is only a few hundred
     words larger than the last release of CCL and the  user  has  the
     option  of  easily  adding  a  wide  variety  of  new fast lookup
     commands in the internal table.

          A second table file,  TABLE.BIG,  (the  one  created  by  P.
     Sorenson)  has  all  kinds  of  commands  in  it, but not all the
     commands in TABLE.KMS.  The user is urged to examine both  tables



                                                               Page 21



     and use or modifiy either as appropriate.