BATCH SYSTEM USER'S GUIDE
                          BATCH SYSTEM VERSION 2.47
                                  JULY 1982









     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 2
     INTRODUCTION


     Introduction
     ------------

          The batch system is a means by which a program may be put into
     a  queue  of  jobs  waiting  for  execution.  Jobs in the queue are
     executed  as  needed  resources  become  available.   This   system
     provides  reduced  terminal  use  and  better  turnround  for users
     running long jobs.  To use the batch system, a user enters  a  list
     of commands to be processed into a file called the "job description
     file".  A simple job description file might contain only  a  single
     RUN  command.   These  commands can then be queued for execution by
     the batch system.  A later section details how  to  construct  your
     job  description  files,  with  examples.   To  enable users to run
     programs on the batch system in the same form as they  are  run  on
     any  terminal  in  the  normal  fashion, the batch system employs a
     special software construct called the "virtual terminal".   As  the
     name  implies,  this  involves  setting up the software so that the
     RSX-11M Operating System thinks that it is  doing  I/O  to  a  real
     terminal,  when  in fact there is no hardware involved.  To do this
     involves having a virtual  terminal  driver  in  the  system  which
     intercepts  all  requests  that would normally be sent to the usual
     terminal  driver.   The  virtual  terminal  driver's   details   of
     operation  will  normally  be  of  no concern to the user using the
     batch system, since its intervention is completely  transparent  to
     the user.  However, having no terminal keyboard involved means that
     it becomes a little difficult to enter terminal input.  To overcome
     this, the STACK command is provided.  This command puts a batch job
     into direct connection with the virtual  terminal  driver  for  the
     purposes  of entering the equivalent of normal terminal input.  The
     STACK command is easy to use, and is described in detail in a later
     section.

          When a batch job is started by the batch system, the  user  is
     logged  on  to  the virtual terminal (using parameters given by the
     user when the job was submitted) in the same fashion as if the user
     had  logged on at a normal terminal.  The commands contained in the
     job description file are then executed one by one  until  the  last
     command  has  finished processing.  The user is then logged off the
     virtual terminal, and the next user in the batch queue is logged on
     for  his  job  to  run.   System  accounting remains the same as at
     normal terminals,  with  the  exception  that  since  there  is  no
     hardware  involved, there is no charge for connect time.  While the
     batch job is executing, all the output  that  would  normally  have
     gone  to  the terminal is stored on disk by the batch system in the
     "log file".  The log file is created by the  batch  system  with  a
     filetype  of  LOG  and  a version number equal to the number of the
     batch job (see later).  The name of the log file will be  the  same
     as  the  name  of  the job description file.  When the batch job is
     complete, the log file is automatically listed on the line printer.
     The  batch system allows very long jobs to run in short segments by
     resubmitting themselves, so that long programs can run for  several
     days  with  no  user  intervention.  This sort of scheme provides a
     much better turnround for these users, since the  job  can  execute



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 3
     INTRODUCTION


     without tying up a terminal for long periods.  Hence, long jobs can
     run during  the  daytime  instead  of  just  at  night,  which  has
     previously  been  the  case.  Any command that is legal at a normal
     terminal is allowed in a batch job, with a  few  minor  exceptions.
     For  example,  the  SET  commands  that can be used to set terminal
     characteristics, such as SET /LINES=TI:, SET  /BUF  etc.,  will  be
     accepted  but  will  have  no effect.  The BYE command must *never*
     appear in  a  job  description  file.   All  logoff  processing  is
     performed  automatically  by  the  batch system.  If BATMAN detects
     that a BYE command has been issued from within  a  batch  job,  all
     further  processing  for  that  account  will  be  halted.  Also, a
     virtual terminal should never be explicitly referred to in a  batch
     job.   All  input/output  requests  for  the  'terminal'  should be
     directed to the pseudo device TI:, as at a  normal  terminal.   The
     user  has  no control over which batch stream a job will eventually
     execute in, and so explicit use of a virtual terminal  device  name
     and  unit  number  may  be regarded as a privilege violation by the
     virtual terminal driver if it happens to  be  a  different  one  to
     which the job is running on.

          System load is lower when a job is run  in  the  batch  system
     since  a  virtual  terminal  provides no interrupts that have to be
     serviced by the Executive, unlike a normal terminal.

          Although the operation of the batch system appears to be  very
     simple  to  the user, it is in fact rather complex internally.  The
     system consists of several components:

          (i) The BATCH command.  This is  a  normal  MCR  command  that
     allows  users  at  an  interactive terminal to submit jobs into the
     batch queue, and to manipulate them at later  times  if  necessary.
     The BATCH command is the normal user interface to the batch system.

          (ii) The Batch System Queue Manager Program (BATMAN).  This is
     a  system  program which is permanently executing.  Its function is
     to supervise the operation of the batch system, to  start  up  jobs
     and  to generally check that all is well.  Although always running,
     it adds very low overhead to  normal  system  operations.   Another
     function  of  BATMAN  is to supervise the construction of log files
     for each running batch job.  It does this by issuing a read to  the
     virtual  terminal driver.  When a line of output is received by the
     driver from a batch job,  an  Asynchronous  System  Trap  (AST)  is
     effected  within  BATMAN,  which  then  writes  the  line of output
     received into the appropriate log file.  This AST mechanism is used
     to   allow   BATMAN  to  simultaneously  write  log  files  and  to
     start/finish jobs on multiple job queues.   The  inner  details  of
     BATMAN  will  not  normally  be of concern to the user of the batch
     system.  It should be noted that the Batch System Queue Manager  is
     a  different  program  and has no connection with the Print Spooler
     Queue  Manager  program   (QMG...)   described   in   the   RSX-11M
     documentation.

          (iii) The virtual terminal driver itself, and  the  associated



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 4
     INTRODUCTION


     data structures.  The virtual terminal driver was written specially
     for the batch system,  and  has  no  connection  with  the  virtual
     terminal driver described in the RSX11-M I/O Driver's manual.

          (iv) The STACK command, as mentioned above.

          (v) The TAPE command, which allows a batch system job to  load
     a magnetic tape for processing.  The TAPE command is discussed in a
     later section.

          The current structure allows for up to four batch jobs  to  be
     executing  concurrently,  that is, there are four virtual terminals
     available to the batch system onto which it may log users  and  run
     their jobs simultaneously.  If there are more than four jobs in the
     queue, the additional jobs wait until one  of  the  executing  jobs
     finishes  before  the batch system will attempt to log it on to one
     of the virtual terminals.

          Different batch streams have different scheduling limits which
     may  vary  according  to  the  time  of day.  A list of the current
     values is usually posted on the computer room wall.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 5
     INTRODUCTION


     The BATCH command
     --- ----- -------

          To submit a request to the batch system,  the  user  issues  a
     command of the form

          BATCH command-line <CR>

          where "command-line" is a command line containing BAT commands
     (see below), and <CR> represents a carriage return.  Only the first
     three letters of the command name are necessary;  the final "CH" is
     optional.  Alternatively, if several commands are to be issued, the
     following form of the command can be used

     	BAT<CR>
     	BAT>command-line <CR>
     	BAT>command-line <CR>
     	BAT>^Z

          BAT exits when a CTRL/Z is typed in a similar manner to  other
     system  utility programs (PIP, F77, TKB etc.).  CTRL/Z is echoed at
     the terminal as ^Z.  The prompt "BAT>"  is  typed  out  by  BAT  to
     solicit  input.   A line of input may begin with a semi-colon, when
     it is treated as a comment and ignored.  Blank  lines  (entered  by
     pressing RETURN alone) are also ignored.  BAT may also be activated
     by issuing the command

          RUN ...BAT

          In this case, the prompt is produced and BAT waits for  input.
     A  user  may  want  to issue the same sequence of BAT commands on a
     number of different occasions, for example, to submit the same  job
     description file for processing on different days.  To permit this,
     BAT allows commands of the form

          BAT @filespec<CR>

          where "filespec" is  a  standard  RSX-11M  file  specification
     giving  the  name  of  a  file  which  contains  BAT commands.  For
     example, suppose a user wanted to list the batch  queue,  submit  a
     job,  and  then list the batch queue again.  The following might be
     an example of the commands issued

     	BAT /LI
     	BAT BATJOB/PA:PSWD
     	BAT /LI

          Equivalent to this would be

     	BAT<CR>
     	BAT>/LI
     	BAT>BATJOB/PA:PSWD
     	BAT>/LI



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 6
     THE BATCH COMMAND


     	BAT>^Z

          The latter form is recommended for multiple command  requests.
     (Note  that in the above example, there would have been output from
     BAT after each command;  this has been omitted in this example  for
     clarity.) If the file MOBILE.CMD contained the lines

     	/LI
     	BATJOB/PA:PSWD
     	/LI

          then an equivalent procedure to the above example  would  have
     been

          BAT @MOBILE

          Comments  may  be  included  in  indirect  command  files   by
     prefixing  them  with a semicolon in column 1.  An indirect command
     file specifier is also allowed as input to the BAT> prompt;  it  is
     not restricted to the MCR command line as in the example above.

          In using indirect command files in this manner, the  following
     points should be noted:

          1.   If  a  device  is  not  specified  with  the   "filespec"
     parameter,  BAT  assumes that the file is to be found on the user's
     SY:  disk (the system disk in most cases).

          2.   If  a  directory  is  not  specified,  BAT  searches  the
     directory currently in use as the default for the specified file.

          3.  There is no default for the name of the file.

          4.  The filetype defaults to CMD if not specified.

          5.  If a version number is not specified, the  latest  version
     of the file is used.

          6.  Indirect command files may only be nested to  a  depth  of
     one;   that  is,  an  indirect  command file cannot contain another
     indirect command file specifier.  An error message is produced  and
     the  current  scan  is  terminated if an indirect command file at a
     nesting depth of two is detected.

          An error message is generated if the specified file  can't  be
     found,  or if there is a syntax error in the command line.  Because
     of the relative complexity of the batch system, there are  a  large
     number of different error messages that can be produced.  These are
     all  grouped  together  in  a  later  section  together   with   an
     explanation of their meaning and probable cause.

          For example, if the user was running under a UIC of  [304,67],
     and the latest version of file MOBILE.CMD was 17, then



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 7
     THE BATCH COMMAND


          BAT @MOBILE

          is equivalent to

          BAT @SY0:[304,67]MOBILE.CMD;17

          The commands accepted by BAT fall into six classes:

          1.  Commands that submit a job  for  execution  in  the  batch
     system.  The job is added to the list of jobs waiting for execution
     according to the options specified in the command line.

          2.  Commands that remove a previously submitted job  from  the
     batch queue, or cancel a batch job that is already executing.

          3.  Commands to list the contents of the batch queue.

          4.  Commands that can release a previously submitted job  from
     hold  status,  if  it  was  put  in  a  hold  condition when it was
     submitted.

          5.  A further class of commands is available which can only be
     used by a system operator.  These are used to perform various queue
     maintenance functions.  There is only one  command  in  this  class
     that  is  available  to  the general user;  this is the /ID command
     which is described in a later section.  The remaining  commands  in
     this class are not documented in this manual.

          It is not permitted to include commands  from  more  than  one
     class  in the same command line;  doing this results in the command
     being flagged as ambiguous, and ignored.





     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 8
     JOB SUBMISSION COMMANDS


     Job Submission Commands
     --- ---------- --------

          To submit a single job for execution by the batch system,  the
     BAT command takes the form

          BAT filespec/sw1/sw2...

          where  "filespec"  is  the  file  specification  of  the   job
     description  file,  and  /sw1 and /sw2 are switches chosen from the
     list given below.  The same defaults apply to the  job  description
     file  as to an indirect command file, with the execption that there
     is a default filename of "BATCH".  There  are  also  considerations
     pertaining to the use of the version number (see the description of
     the /EV switch below).  At least  one  switch  must  be  specified.
     Each  switch  consists  of  a  slash  followed  by  two characters.
     Certain switches allow their actions to be  nullified  by  negating
     the  switch.   To  negate  a  switch,  two  forms  may be used, for
     example,

          /NOSW

          or

          /-SW

          are both negated forms of the switch /SW.  The  switches  that
     can be negated in this fashion are identified below.

          The following is a list of the switches that can  be  used  to
     control the submission of a job:

      /TL:n

           Specify the time limit of the job.   Here  "n"  is  a  number
           which  gives the time limit in minutes.  It is octal radix by
           default;  to specify decimal, the number should  be  followed
           by  a  decimal point.  The time involved is the CPU time used
           by the job, which means  that  the  job  will  probably  stay
           executing  for  a  period  of  clock  time  that exceeds this
           amount.  If the /TL switch is not used to  specify  the  time
           limit,  a default of 30 minutes will be used.  No job will be
           accepted with a time limit greater than 10  hours  (that  is,
           /TL:600.  or /TL:1130).  The /TL switch cannot be negated.
      /LN:n

           Specify the output limit of the job, that is, the  number  of
           lines  that  can be written to the log file.  The system will
           not adhere to this figure exactly;  a job may be permitted to
           exceed it slightly but will never be aborted before the limit
           is reached.  The line count "n" is octal  radix  by  default;
           to  specify  decimal,  the  number  should  be  followed by a
           decimal point.  If the /LN switch is not used to specify  the



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                       PAGE 9
     JOB SUBMISSION COMMANDS


           line  limit,  a  default  of  2048.   lines (approximately 34
           pages) will be used.  No job will be  accepted  with  a  line
           limit greater than 6144.  (approximately 102 pages).  The /LN
           switch cannot be negated.

      /PA:pswd

           This switch is used to supply the password that will be  used
           to log on your batch job.  If you do not wish to display your
           password on the terminal, omit this switch.   In  this  case,
           BAT will prompt you for the password by typing

           ENTER PASSWORD:

           You can then type in your password.  It will  not  appear  on
           the  terminal, as BAT does a read-with-no-echo, just like the
           HELLO command.  If BAT is to be used from within a batch  job
           to  submit  another  batch  job, you can use the special form
           /PA:*.  This is an indication to BAT to use the same password
           as was used to submit the batch job in which BAT is currently
           running.  This avoids having listings of the  batch  job  log
           files  that  have  your password displayed on them.  The form
           /PA:* is legal only when used in a batch  job.   If  you  are
           using the form of BAT where multiple commands can be typed in
           in response to a prompt, then it is only necessary  to  enter
           the password for the first job that you submit;  BAT uses the
           first password you enter as the password for  all  the  batch
           jobs.   It  is  still legal to specify /PA again if you wish,
           although the new password that you supply  will  be  used  to
           submit all further jobs.  This can be useful if you mis-spell
           your password the first time round.  Note that BAT  does  not
           access  the system account file to check your password (there
           would be no need to type it in if it did), so if you enter  a
           wrong  password, the batch job will fail!  The /PA switch can
           not be negated.

      /EV

           This switch is used to specify an explicit  version  for  the
           job  description  file.   If  this file specification did not
           contain a version number, then this switch  can  be  used  to
           specify  that  the latest version of the job description file
           AS THE DISK CURRENTLY EXISTS is the one to be used to run the
           batch  job.   If you do not specify this switch, then the job
           will  be  started  with  the  latest  version  of   the   job
           description  file AS THE DISK EXISTS WHEN THE JOB IS STARTED.
           This provides the ability to edit the file between submission
           and execution time and still have the right one executed.  An
           explicit  version  number  on  the   job   description   file
           specification in the command line is equivalent to specifying
           /EV, that is, it will be the version  used  to  run  the  job
           however  many  edits  of the job description file you may do.
           The /EV switch may be negated, and the default is /-EV.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 10
     JOB SUBMISSION COMMANDS


      /TR

           Trace job description file execution.  This  switch  has  the
           same meaning as the /TR switch used on indirect command files
           normally  (see  the  Operator's  Procedures  Manual   for   a
           description).  This switch may be negated, and the default is
           /-TR.

      /DE

           Specifying this switch will cause the job description file to
           be  deleted when the job has finished running, providing that
           it  does  not  terminate  abnormally.   This  switch  can  be
           negated, and the default is /-DE.

      /HF:n

           This switch is  used  to  put  the  job  into  hold  for  the
           specified  number  of  minutes.  The default radix for "n" is
           octal.  To specify decimal,  append  a  decimal  point.   Any
           positive  value  less than 32,767 (decimal) may be specified.
           The special values -1 to -7 can be used to put the  job  into
           hold  for  the  specified  number of days (any other negative
           value is illegal).  For  example,  /HF:-2  is  equivalent  to
           /HF:2880.   (or /HF:5500).  A job in hold is not eligible for
           starting until the specified time has elapsed,  even  if  the
           queue  is  idle.   This switch may be negated only in special
           circumstances (see below).  By default a job is not put  into
           a  hold  state,  that  is,  it  is  immediately  eligible for
           execution, when submitted from a normal interactive terminal.
           When  a  job  is submitted from within another batch job, the
           default is /HF:1, that  is,  the  job  is  not  eligible  for
           execution  for  one  minute  after submission.  The intent of
           this is to avoid a great deal of short jobs  from  preventing
           the long ones from ever starting.

      /HU:hh:mm

           This switch is used to put the job into hold until  the  next
           occurrence  of  the  specified  time  of day.  The values are
           assumed to be decimal, and  any  omitted  value  defaults  to
           zero.  For example, /HU holds the job until midnight (as does
           /HU::), /HU::27 holds until 00.27 am, /HU:14  holds  until  2
           pm,  and  /HU:17:46  holds until 5.46 pm.  This switch may be
           negated in special circumstances, when any switch values  are
           ignored.   Obviously it is illegal to use both /HF and /HU to
           submit the same job.  For both /HU and  /HF,  the  batch  job
           will  be  removed  from  the  hold  queue and placed into the
           eligible-for-execution  queue  within  15  seconds   of   the
           specified time elapsing.




     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 11
     JOB SUBMISSION COMMANDS


      /EX

           This switch identifies the job as  an  "express  job".   Such
           jobs  are  immediately eligible for execution (subject to the
           queue being available) regardless of  time  limit,  providing
           that  the  job  has  not also been put into a hold condition.
           Express jobs are executed in the  order  in  which  they  are
           submitted.   They  are  intended  for  system maintenance use
           only, and can only be submitted by privileged users.  If  you
           have  work to do which is very urgent, it can be arranged for
           you to submit jobs into the express class to obtain the  best
           possible  turnround.   This  switch  can  be negated, and its
           default is /-EX.

      /RS

           This switch can be used to specify  that  the  batch  job  is
           restartable.   Any job with the restartable attribute will be
           re-run *from the beginning* should the system crash while the
           job  is running.  If the job has less than approximately 18.2
           minutes left to run this switch will have no effect, that is,
           the  job  will not be considered restartable (the 18.2 minute
           limit is equivalent to 2**16-1 ticks of  a  60-cycle  clock).
           Before using this switch, you should be aware of the possible
           effects on your  files  if  a  job  duplicates  any  previous
           operations.   The  /RS switch can be negated, and the default
           is /-RS, that is, by default a batch job is not  restartable.
           Any  job  that  is  in  the queue but is not yet running will
           always be restored to the queue in  the  event  of  a  crash,
           regardless of its time limit or /RS setting.  In the event of
           a queue restore after a crash, you should be aware that  your
           job  will  be given a different job number than it originally
           had.  There are some considerations pertaining to the use  of
           parameter  lists  (see below) in restartable jobs;  these are
           discussed in the section  on  writing  your  job  description
           files.

      /PM:parm1:parm2:parm3:parm4

                This  switch  allows  you  to   specify   up   to   four
           "parameters"  for  your  batch  job.   A  "parameter" in this
           context is a string of  up  to  10  characters  that  can  be
           substituted at any desired points in the job description file
           when the job is run;  this capability is  discussed  in  more
           detail  in  the section on writing job description files.  It
           allows great  flexibility  in  constructing  job  description
           files  dynamically  at  job  submission  time.   Up  to  four
           parameters may be specified,  and  any  printable  characters
           (except  commas  and  obviously  colons;   spaces are ignored
           also)  are  allowed  in  each  parameter.    Any   characters
           specified  in a parameter beyond the 10th are ignored with no
           warning.  If any parameter field is blank, then it is ignored
           and  any  following parameters are left shifted to take their



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 12
     JOB SUBMISSION COMMANDS


           place.  For example, the  switch  /PM::STRING1?:STRING2!   is
           equivalent   to   /PM:STRING1?:STRING2!   and  specifies  two
           parameters, "STRING1?" and "STRING2!".  Since all spaces  are
           removed  from  the command line by BAT before it is analysed,
           it is not possible to specify a blank parameter using the /PM
           switch.   The  /PM  switch can be negated, and its default is
           /-PM, that is, no parameters will be passed to the job.   You
           should  see  the section on writing job description files for
           information on using parameter lists with  restartable  (/RS)
           jobs.

      /KE

           If this switch is specified at job submission time,  the  log
           file   will   be   created   and  written  in  the  directory
           corresponding to the logon UIC of the user who submitted  the
           job.   After  the  job has finished and the log file has been
           printed by the system (see also /NO below), the log file will
           not  be  deleted,  but  will  remain  in  your  directory for
           whatever functions you wish to perform on  it.   The  default
           for this switch is /-KE, which implies that the log file will
           be created in a system directory, and will be deleted when it
           has  been printed.  It is the users' responsibility to ensure
           that a  log  file  that  is  being  written  in  that  users'
           directory  is  not  tampered with in any way while the job is
           running.  Corruption of the log file in this way is a certain
           way  of  losing any further output from the batch job, and it
           does not guarantee that the job will finish  running  either.
           The  system directory currently in use by the batch system is
           [1,71], but BATMAN sets the protection masks of log files  so
           that  users  will not be granted access to their log files if
           they are to be written to this directory.

      /NO

           If this switch is specified the batch job's log file will not
           be  listed  on  the  line  printer  when the job has finished
           running.   It  makes  sense  to  use  this  switch  only   in
           conjunction  with  the  /KE switch, since users will not have
           access to active log files in the system directory.   If  /NO
           is  specified  and  /KE  is  not,  it  will be ignored with a
           warning message.  The /NO switch  can  be  negated,  and  its
           default is /-NO.

      /IM

           This switch puts the BAT command into  "immediate  mode".   A
           new  version  of the job description file is created (it need
           not exist already).  If a version number is specified and the
           file  does  not  exist, the specified version is created.  If
           the specified version of  the  file  already  exists,  it  is
           overwritten.  BAT then asks for input by typing




     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 13
     JOB SUBMISSION COMMANDS


           ENTER COMMANDS:
           *

               You may enter commands in response to the * prompt.   The
           line of input goes into the file as part of the new job.  On

                receiving a blank line (RETURN  only),  BAT  closes  the
           file  and  submits  the job in the normal fashion.  If an I/O
           error occurs, the file is deleted, the user  is  informed  of
           what has happened, and job submission is not attempted.  This
           can also be achieved by typing CTRL/Z in response  to  the  *
           prompt.  If the job could not be submitted for other reasons,
           for example, the job queue was full, the file is not  deleted
           and  remains  on  the  disk  to be submitted at a later time.
           When a file is created by BAT, it is given an initial size of
           1  block,  and  its size is extended by 1 block increments if
           necessary.  This is a space saving  device,  since  most  job
           description  files are small and the usual initial allocation
           for a new file is 5 blocks.  The /IM switch is  illegal  from
           within  a  batch  job.  It can be negated, and the default is
           /-IM.

          When a job is submitted successfully, the batch system assigns
     it a unique "job number".  The job number is the means by which the
     batch system identifies the job, and it must be known by  the  user
     in  order  to  cancel the job or remove it from hold.  A successful
     job submission is followed by the message

          BAT -- JOB 27 ACCEPTED

          where the job number assigned is given (it is octal).  If  you
     forget  the  number  of  your batch job(s), the batch queue listing
     commands (see later) can be used to find out the  numbers  of  jobs
     that you have in the queue.

          Multiple jobs can be submitted in a  single  command  line  by
     following  the  first  submission  command with a list of other job
     descriptions files, separated by commas.  For example, the command

          BAT JOB1/PA:pswd,JOB2,JOB3

          submits three jobs,  JOB1.CMD,  JOB2.CMD  and  JOB3.CMD.   Any
     switches  that  are specified must follow the first job description
     file specification.  If the above command had been written

          BAT JOB1,JOB2,JOB3/PA:pswd

          then it would have been rejected with a command  syntax  error
     message,  since there were no switches on the first job description
     file to specify its disposition (BAT scans the  command  line  from
     left  to  right).  Any conditions that are set up by switches, such
     as  time  limit,  hold,  delete,  etc.   apply  to  all  other  job
     description  files  specified  in the same command line (but not in



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 14
     JOB SUBMISSION COMMANDS


     subsequent command lines) unless  the  switch  is  explicitly  used
     again  to  alter  those conditions.  If a switch is used again on a
     command line in this manner, then the conditions implied by it also
     apply to any jobs following it on the command line.  For example

          BAT JOB1/PA:pswd,JOB2/TL:45.,JOB3

          This command submits three jobs:  JOB1.CMD with a  time  limit
     of  30 minutes (since /TL was not used on the first job description
     file specification), and JOB2.CMD  and  JOB3.CMD,  both  with  time
     limits of 45 minutes.  A more complex example is

          BAT TEMP1/IM/DE/PA:pswd,JOB3/-IM/PM:XYZ,JOB5/-DE/TL:45./-PM/RS

          Here the BAT command prompts  for  commands  that  are  to  be
     entered in the file TEMP1.CMD.  This job will be submitted, and the
     file TEMP1.CMD will  be  deleted  when  the  job  has  run.   Since
     immediate  mode  is  nullified  on  the second job by virtue of the
     presence of the /-IM  switch,  the  file  JOB3.CMD,  which  already
     exists  (hopefully) is used to submit a second job.  This file will
     also be deleted when the job has run, since /DE was  used  for  the
     first  job  and this condition still holds for the second job.  The
     third job submitted is JOB5.CMD, and this is neither  an  immediate
     mode  command,  nor  will  the job file be deleted when the job has
     run.  JOB5.CMD has a time limit of 45 minutes.  Both TEMP1.CMD  and
     JOB3.CMD  have the default time limit of 30 minutes.  One parameter
     ("XYZ") will be passed to  JOB3;   the  other  jobs  will  have  no
     parameters  passed.  The restartable attribute is attached to JOB5.
     The above example is equivalent to

     	BAT <CR>
     	BAT>TEMP1/PA:pswd/IM/DE
     	BAT>JOB3/DE/PM:XYZ
     	BAT>JOB5/TL:45./RS
     	BAT>^Z

          The number of parameters passed to  each  job  in  a  multiple
     submission command line is determined by the first /PM switch.  For
     example, the command

          BAT JOB1/PM:ONE:TWO:THREE,JOB2/PM:FOUR:FIVE,JOB3/PM:SIX

          passes three parameters to each job, and is equivalent to

     	BAT <CR>
     	BAT>JOB1/PM:ONE:TWO:THREE
     	BAT>JOB2/PM:FOUR:FIVE:THREE
     	BAT>JOB3/PM:SIX:FIVE:THREE
     	BAT>^Z

          If you want to pass a different number of parameters  to  each
     job, they must be submitted on different command lines.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 15
     JOB SUBMISSION COMMANDS


          If one job is  submitted  using  /HF,  and  a  second  job  is
     submitted  on  the  same command line using /HU, or vice versa, the
     first hold condition must be nullified to avoid having the  command
     flagged as ambiguous.  For example, the command

          BAT JOB1/HF:5,JOB2/-HF/HU:13:30,JOB3/-HU/TL:100

          is equivalent to the sequence

     	BAT <CR>
     	BAT>JOB1/HF:5
     	BAT>JOB2/HU:13:30
     	BAT>JOB3/TL:100
     	BAT>^Z

          Note that in this example, BAT would prompt for the  password,
     since  it  was  not specified on the command line.  Also, the third
     job will be submitted with a time limit of 64 minutes, since  octal
     radix  was implied for the time limit by the missing decimal point.
     If the /HU or /HF switches are negated as in this example, then any
     values that may accompany them are ignored.

          The number of jobs that can be submitted on one  command  line
     is  limited  only  by  its length (79(10) characters maximum).  For
     example, the command

          BAT CRUNCH.P64/TL:20./PA:pswd,,,,,DODISJOB.MAN/TL:45.

          will submit the job CRUNCH.P64 once, the  job  BATCH.CMD  four
     times,  and  the  job  DODISJOB.MAN once.  The first five jobs will
     have a time limit of 20(10) minutes, and the sixth job will have  a
     time limit of 45(10) minutes.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 16
     JOB CANCEL COMMANDS


          To remove a job from the batch queue, use the  /CA  switch  in
     the form

          BAT /CA:n

          where "n" is the number of the job  to  be  removed  from  the
     queue.  The job number is octal by default;  this is the radix that
     the job number is given in when the job was submitted.  No filename
     need  (or should) be specified.  If the job is already running, the
     above command alone will not cancel the job.  In this case you need
     to include the /AB subswitch, for example,

          BAT /CA:n/AB

          The default is /-AB, that is, the job will not be  aborted  if
     it  is running.  The two switches can be specified in either order,
     and it is illegal to use /AB alone without /CA, since /AB does  not
     accept the job number as a switch value.  If the job is running and
     a request is made to abort it in this way, the actual  aborting  of
     the job should occur within a period of about 30 seconds.  The user
     will be logged off the virtual terminal, and the log file  will  be
     printed in the normal manner.  Note that it may take BATMAN a while
     to completely terminate the job if it is running at a low  priority
     or  if  system load is high.  The /AB switch will have no effect if
     the job is not running;  it will be ignored.

          To cancel several jobs, either several commands of  the  above
     form  can  be  issued,  or the following form can be used (note the
     separating commas)

          BAT /CA:n,/CA:m,/CA:p,...  etc.

          If /AB is used on any  switch  in  the  above  list,  it  also
     applies to all later switches, for example,

          BAT /CA:16/AB,/CA:21,/CA:37

          is equivalent to

     	BAT <CR>
     	BAT>/CA:16/AB
     	BAT>/CA:21/AB
     	BAT>/CA:37/AB
     	BAT>^Z

          while

          BAT /CA:16/AB,/CA:21/-AB,/CA:37

          is equivalent to

     	BAT <CR>
     	BAT>/CA:16/AB



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 17
     JOB CANCEL COMMANDS


     	BAT>/CA:21
     	BAT>/CA:37
     	BAT>^Z

          A privileged user can cancel or abort any job in  the  system.
     A  non-privileged  user  can  only  cancel  or abort jobs that were
     submitted by him.  If any errors are detected in the command  line,
     such  as  an illegal job number, all commands following the illegal
     one in the same command line are ignored.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 18
     JOB RELEASE COMMANDS


     Job Release Commands
     --- ------- --------

          To remove a previously submitted batch job from  hold  status,
     use the /RL switch in the form

          BAT /RL:n

          where "n" is the job number.  The default radix  for  the  job
     number  is octal;  to specify decimal (which should not normally be
     necessary), append a decimal point.  Note that  this  command  only
     deletes  the  hold  status;   the job is inserted into the queue of
     jobs that are eligible to run according to its time limit and  they
     may  still be a delay in execution while all jobs of a shorter time
     limit are executed.  If there are no other jobs in the  queue  that
     are  eligible  to  run, or the just-released job has a shorter time
     limit than any other job in the queue, then the  job  will  be  the
     next  one  started.  If a batch stream is available to run the job,
     then the just-released job should begin executing within 20 seconds
     and  typically  10 seconds.  Several jobs can be released from hold
     in one command line:

          BAT /RL:n,/RL:m,/RL:p

          A privileged user can delete the hold status of any batch  job
     in the system.  A non-privileged user can delete the hold status of
     only those jobs submitted by him.  If an error is detected  in  the
     command  line, such as an illegal job number, all remaining release
     commands on that command line (if any) are ignored.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 19
     QUEUE LISTING COMMANDS


     Queue Listing Commands
     ----- ------- --------

          The contents of the batch queue can be listed by  issuing  the
     command

          BAT /LI

          The format of the output produced  is  described  below.   The
     listing switch, which cannot be negated, takes two subswitches, /FU
     and /AL, both of which can be negated.  The /FU switch  provides  a
     fuller listing, and can be used on its own, that is,

          BAT /LI/FU

          and

          BAT /FU

          are equivalent, while

          BAT /LI/-FU

          and

          BAT /LI

          are equivalent.  The /AL switch is described below.

          If there are no jobs in the queue (either executing or waiting
     for execution), BAT displays the message

          BAT -- QUEUE IS EMPTY

          otherwise the queue listing is preceded by the text

          JOBS IN QUEUE:  n.

          where "n"  is  the  decimal  number  of  jobs  in  the  queue,
     including  those  job(s)  that are executing.  If the commannd then
     displays the line

          QUEUE IS IN RUNDOWN

          then the queue has been put into the  "rundown  state"  by  an
     operator,  that is, the currently executing jobs will be allowed to
     finish, but no further jobs will be started.   This  is  used,  for
     example,  when  the  system  is being shut down for maintenance.  A
     message may also appear indicating  that  no  new  jobs  are  being
     accepted.   In  this  case, you will not be able to submit any jobs
     into the queue, but all those currently waiting will be allowed  to
     execute.   Following  the initial message(s), there is a line typed
     out for each job of the form



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 20
     QUEUE LISTING COMMANDS


          4.  41 [33,37]        DM0:[33,37]BATJOB.CMD;0

          The first number typed  out  is  the  (decimal)  queue  member
     number.   This  number  gives  the  position  within  the queue for
     starting eligibility.  A zero will appear in  this  field  for  any
     jobs  that  are currently executing, and futhermore these jobs will
     appear at the head of the listing.  Jobs that may be  in  hold  are
     not immediately eligible for execution, and so appear at the end of
     the listing.  Thus a hold job may move several places up the  queue
     when its hold condition expires, depending on its time limit.  Jobs
     that are in hold are not displayed in order of  their  time  limit,
     but  rather  in  the  order  that  they  were  submitted.  Internal
     reordering of hold jobs in the queue occurs when the hold condition
     expires.

          The second number displayed is the (octal) job number assigned
     to  the  job when it was submitted.  This is the number that *must*
     be used to alter the status of any job in the queue, if necessary.

          The third field displayed  is  the  User  Identification  Code
     (UIC)  that will be used to log the user on to the virtual terminal
     when the job is run.  The password that is associated with this UIC
     is  never  displayed  by  the listing commands.  The logon UIC will
     usually, but not always, be the same as the directory in which  the
     job description file is to be found.

          The fourth field is the complete file  specification  for  the
     job description file.  If the version number appears as zero (as in
     the example above), then the latest version of the file as the disk
     exists when the job is started will be the one used to run the job.
     If the version number is non-zero, then either an explicit  version
     number  was given when the job was submitted, or the /EV switch was
     used.  In this case, this version of the job description file  will
     be  used  to  run the job.  If the version number displayed is zero
     and you have more than one version of  the  job  description  file,
     then you can find out which one is running by issuing the command

          PIP filespec/TR

          where  "filespec"  is  the  file  specification  of  the   job
     description  file  with  a  wild  card (*) specified in the version
     number field.  PIP will issue a file open  error  message  for  the
     file that is currently open by the batch system to run the job.

          If the /FU switch was used, all the above information appears,
     but  several fields are appended to the end of the line.  The extra
     information that appears is dependent on the current state  of  the
     job,  and  may  be spread over more than one line, depending on the
     line width of the terminal.  If the  job  is  executing,  then  the
     additional text is similar to

          T=n.M (USED m.mM) VTn:



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 21
     QUEUE LISTING COMMANDS


          The text "VTn:"  indicates  which  batch  stream  the  job  is
     running  in  ("n"  is the unit number of the virtual terminal), and
     the remaining text gives the original time  limit  of  the  job  in
     minutes  and  the  amount  of  CPU  time used by the job so far, in
     minutes rounded down.  If the job is not running,  this  additional
     field is of the form

          T=n.M H=n.nnH EXPR

          where  T=n.M  gives  the  job's  time  limit  in  minutes,  as
     specified  when the job was submitted, H=n.nnH gives the wall clock
     time in hours to one-hundredth of an hour that will  elapse  before
     the  hold  condition expires, and EXPR indicates that the job is in
     the express class.  If either of the last two fields do  not  apply
     (the job may not be express or it may not be in hold), then they do
     not appear.

          For jobs not in execution, the parameter list appears  in  the
     form:

          PM=(parm1,parm2,parm3,parm4)

          This field does not appear if no parameters were passed to the
     job when it was submitted.

          The line limit and count appears in the form:
      
     	LINES=n.
     	LINES=(n./m.)

          Here "n" is the decimal line limit given to the  job  when  it
     was  submitted,  and  "m"  is the number of lines of output already
     done.  Of course, the first form appears for jobs that are  waiting
     for  execution,  and  the  second  form  appears  for jobs that are
     executing.

          The following points should be borne in mind when listing  the
     batch queue:

          (i) At a non-privileged terminal, the  listing  produced  will
     only  include  those  jobs submitted by the user who is issuing the
     listing command.  The initial message that gives the number of jobs
     in  the  queue  is always, however, the total number of jobs in the
     queue, and may be the only output produced if  the  user  does  not
     have  any jobs in the queue.  A non-privileged user may display the
     whole queue by using the subswitch /AL, for example, BAT /FU/AL, or
     BAT /LI/AL.

          (ii) At a  privileged  terminal,  the  listing  produced  will
     include  all the jobs in the queue.  If a privileged user wishes to
     display only jobs submitted by him, then the /-AL subswitch can  be
     used  (for  example  /LI/-AL  or  /FU/-AL)  to  display  only  jobs
     submitted by the user.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 22
     QUEUE LISTING COMMANDS


          (iii) If you wish to find out the job numbers of jobs that you
     have in the queue, use /LI.  To check further the status of jobs in
     the queue, use /FU.

          (iv) The output from a listing command can  be  cancelled  any
     time after the initial message by typing CTRL/O.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 23
     PROGRAM IDENTIFICATION COMMAND


     Program Identification Command
     ------- -------------- -------

          The /ID switch, used on its own as a single command,  provides
     the  version  number  of  the  BAT processor currently in use.  The
     output provided is of the form

          BAT -- BATCH VERSION V2.47

          When new features are added to the system, this version number
     will be incremented.  Users can use this command to find out if new
     features  have  been  implemented.   All  new  features   and   the
     associated  version  number  of  the processor will be described in
     user notices.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 24
     BATCH TEXT MESSAGES


     Batch Text Messages
     ----- ---- --------

          This section contains a list  of  the  informational  messages
     that  are  produced  by  BAT and generally accompany the successful
     execution of a command.  Error messages follow in the next section.
     Each message is of the form

          BAT -- message text

          The following is a list  of  the  possible  strings  that  may
     appear in the "message text" field.  Most are self explanatory, but
     short descriptions of their meanings are included.

     (1)   JOB n REMOVED FROM HOLD

          Job number "n" (octal)  was  successfully  removed  from  hold
     status  by  means  of  the /RL switch and has been entered into the
     relevant job queue.  It is now eligible for execution.

     (2)   JOB n MARKED FOR ABORT

          Job number "n" (octal) has been marked for abort by  means  of
     the  command  /CA:n/AB.  The job will actually be aborted by BATMAN
     within about 15 seconds of the issuance of this  message  (but  see
     the comments on this under the description of the cancel command).

     (3)   JOB n ACCEPTED

          This message accompanies the successful submission of  a  job,
     and  informs  the  user of the job number that has been assigned to
     the job by the batch system.

     (4)   QUEUE IS EMPTY

          A listing command was issued, but there were no  jobs  in  the
     queue, either executing or waiting for execution.

     (5)   QUEUE IS IN RUNDOWN or NO NEW JOBS WILL BE ACCEPTED

          The first message indicates that the system  may  be  shutting
     down  for maintenance.  Currently executing jobs will be allowed to
     finish.  New jobs will be accepted, but none will be started  until
     the  rundown  condition  is  cleared  by  an  operator.  The second
     message indicates that no new jobs will be accepted by the  system,
     but  that  all  jobs in the queue will be allowed to run, including
     those that are currently waiting.

     (6)   JOB n CANCELLED

          Job number "n" (octal) has been deleted from the  batch  queue
     by  means  of  the  /CA:n  command.   The batch system will have no
     further knowledge of the existence of this job.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 25
     BATCH TEXT MESSAGES


     (1)   ** BATCH -- ABORTED BY REQUEST **

          BATMAN inserts this message in your log  file  when  you  have
     requested  the  aborting  of  your  job using /CA:n/AB.  The actual
     program abort message will  contain  the  text  "ABORTED  BY  BATCH
     SYSTEM",  rather  than the usual "ABORTED BY DIRECTIVE OR MCR".  If
     the latter text does appear, then the ABO command from a privileged
     terminal was responsible for the aborting of your program.

     (2)   ** BATCH -- TIME LIMIT EXCEEDED **

          No prizes for guessing what this means.

     (3)   ** BATCH -- SPAWN ERROR **

          This message  indicates  that  an  error  condition  caused  a
     failure  when  BATMAN  tried  to execute a command on behalf of the
     user.  Usually this message will be the only output  produced,  and
     indicated  a  logon  failure that the job had no control over.  Try
     submitting the job again if you get  this  message.   It  will  not
     appear under normal circumstances.

     (4)   ** BATCH -- OUTPUT LIMIT EXCEEDED **

          The job wrote more output lines to the log file than  the  /LN
     switch  (or  the  default) allowed.  The line count is increased to
     30,000 when this happens so that the job can exit in a tidy fashion
     without the automatic logoff sequence being output-limited.

          Note that these messages may appear more than once,  depending
     on how long it takes BATMAN to abort the job.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 26
     BATCH ERROR MESSAGES


     Batch Error Messages
     ----- ----- --------

          This section contains a list of the error messages that may be
     produced  by  BAT,  together  with  a description of their possible
     cause.  Each message is preceded by the text

          BAT --

          If the erroneous command was obtained by BAT  from  within  an
     indirect  command file, then certain of the messages, notably those
     pertaining to an illegal command line format, are also  accompanied
     by  a  message  giving  the command line, or portion of the command
     line, that is in error.  The possible error messages are:

     (1)   COMMAND INPUT ERROR:  CODE n

          This message indicates that  BAT  encountered  an  error  when
     trying  to  get  a  new  command  line.  If the code "n" is zero or
     unity, then  the  error  is  probably  connected  with  an  illegal
     indirect  command  file  specification, such as extra text beyond a
     valid command.  If the error code is negative, it is related to the
     file  system.   An explanation of the meaning of the error code can
     be found by looking in the list of standard FCS error  codes  found
     in  the  back  of  the  I/O  Operations  Manual, Appendix I, or the
     FORTRAN 4-PLUS User's Guide, Appendix C.

     (2)   CAN'T OPEN COMMAND FILE:  FCS n

          An error was detected when  BAT  tried  to  open  an  indirect
     command  file.   The  meaning  of  the  error code (which will be a
     negative decimal number) can be found in  the  list  of  FCS  error
     codes.  The values that will probably be encountered most often are
     -26.  (command file does not exist) and -38.  (file is  locked  due
     to improper closure).  Check that you have correctly spelt the name
     of the command file.

     (3)   MAXIMUM NESTING DEPTH EXCEEDED

          An indirect command  file  specifier  was  detected  within  a
     command  file.   BAT  does  not  allow command file nesting of this
     sort.  The solution to this is to rewrite  the  command  file.   If
     this  would  be  inconvenient  on several occasions, make it known:
     the maximum allowable nesting depth of BAT is  easily  changed,  at
     the expense of about 400 words of core.

     (4)   COMMAND FILE SPECIFICATION ERROR

          The file specification given for an indirect command file  did
     not  conform  to the standard RSX-11M format given at the beginning
     of this document.  Check that all  the  fields  have  been  entered
     correctly, and retype the command line.




     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 27
     BATCH ERROR MESSAGES


     (5)   COMMAND SYNTAX ERROR

          The format of the entered command did  not  conform  to  those
     allowed by BAT.  An example of this sort of error is when a digit 8
     is used in a switch value where an  octal  value  was  expected  (a
     decimal  point  may  be  missing).   This  sort of error is usually
     obvious on examination of the command line.

     (6)   INVALID JOB NUMBER

          Either a job number was missing from a switch which requires a
     job number to be specified, or a zero or negative value was given.

     (7)   CANCEL SWITCH MISSING

          The /AB switch was used on  its  own  without  /CA.   This  is
     illegal since there is no way to specify a job number with /AB.

     (8)   QUEUE IS FULL

          The job that the user is trying to submit cannot  be  accepted
     at the moment because the batch system has reached the limit on the
     number of jobs that can be in the  queue  at  any  one  time.   Try
     submitting the job later.  If the job in question was created using
     the /IM switch, the newly created job file remains on the disk;  it
     is  not  deleted.   The  maximum  allowable  job  queue size can be
     changed by a system command while the system is running, so  if  it
     is important that you have your job in the queue, please enquire in
     the computer room.

     (9)   INVALID TIME LIMIT

          Either the /TL switch was used without a switch value, or  the
     value  given was zero or negative.  Specifying a time limit greater
     than the allowed maximum also causes this message to be displayed.

     (10)  BAD PASSWORD

          The password specified (either by /PA or by the input typed in
     response  to  the ENTER PASSWORD:  prompt) was illegal in some way.
     Check your password and re-enter the command line.

     (11)  COMMAND IS AMBIGUOUS

          This message results either when commands from more  than  one
     class  (see  earlier) are mixed on the command line, or the /HF and
     /HU switches were both used to try to submit the same  job.   Enter
     the command line again in the proper format.

     (12)  INVALID HOLD SPECIFICATION

          For the /HF switch, this message means that either a  zero  or
     negative  value  (other  than -1 to -7) was specified.  For the /HU



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 28
     BATCH ERROR MESSAGES


     switch, this message means that the specified time of  day  doesn't
     exist on the 24 hour clock, for example, /HU:25:30 or /HU:16:-1.

     (13)  PRIVILEGED COMMAND

          This message means that a non-privileged user tried to  submit
     an  express  job.   Only  privileged users can submit express jobs.
     This message will also appear if a  non-privileged  user  tries  to
     issue  one  of  the  batch  system  queue maintenance commands (not
     documented in this manual).

     (14)  NODES EXHAUSTED

          This message means that  BAT  could  not  obtain  a  necessary
     memory  packet from the dynamic storage region (pool) because there
     was insufficient  space  available.   This  is  probably  a  system
     overload  condition,  so  you  are  advised  not  to issue any more
     commands of any sort for a while  until  the  overload  has  eased.
     Don't be surprised if the system crashes shortly after getting this
     message!  Under normal  circumstances  this  situation  should  not
     occur.

     (15)  BAD DIRECTORY STRING

          This message indicates an internal failure in BAT, and  should
     never occur.  If you get this message, please make it known!

     (16)  This error message number reserved for possible future use.

     (17)  ONLY A BATCH JOB CAN DEFAULT THE PASSWORD

          You tried to default the password on a job submission by using
     /PA:*.  This is meaningful only from within a batch job, and cannot
     be used from a normal interactive terminal.

     (18)  CAN'T OPEN JOB DESCRIPTION FILE:  FCS n

          The job description file specified for the submission of a job
     was  corrupted  in  some  way,  or  it did not exist.  The detailed
     nature of the error can be found by consulting a list of FCS  error
     codes.  The most frequently obtained code will be -26., which means
     that the specified file did not exist.

     (19)  IMMEDIATE MODE ILLEGAL WITHIN A BATCH JOB

          You attempted to put BAT into immediate  mode  from  within  a
     batch  job by using the /IM switch.  This is illegal.  This message
     only occurs during batch jobs.

     (20)  I/O ERROR - FILE DELETED:  FCS n

          While compiling a job description file in immediate mode,  BAT
     detected a file-system related error.  The FCS error code gives the



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 29
     BATCH ERROR MESSAGES


     specific cause of the error.  If you decided to cancel an immediate
     mode  job  by  typing CTRL/Z in response to the * prompt, then this
     message indicates that the procedure has been cancelled.   The  FCS
     error  code in this case will be -10 (end of file).  If this is not
     the case, retry the function.  Please enquire in the computer  room
     if the problem persists.

     (21)  JOB n IS RUNNING

          You issued a /RL:n,/TU:n or a /CA:n command (without  the  /AB
     subswitch)  for  a job that was already executing.  These functions
     are not meaningful for jobs that are executing.  If you really want
     to abort an executing job, try the command again and specify /AB.

     (22)  JOB n NOT IN QUEUE

          You issued a /RL:n command, /TU:n command, or either  form  of
     the /CA:n command and specified a job number that did not match any
     of the jobs in the queue.  Check the job number again, possibly  by
     listing  the queue with /LI.  If you are sure that you have the job
     number right, but the job does not appear in the queue, then it has
     already finished running.

     (23)  JOB n IS NOT IN HOLD

          You tried to release a job from hold by using /RL:n,  and  the
     job was not in hold, although it was found in the job queue.

     (24)  PRIVILEGE VIOLATION

          This message indicates that a  non-privileged  user  tried  to
     cancel,  abort or remove from hold a job that he did not submit.  A
     non-privileged user can only alter the status of jobs in  this  way
     if  he is the submitting user, that is, he is logged on to the same
     account that was used to submit the job.

     (25)  This error message withdrwan.

     (26)  WARNING - /NO SWITCH WILL BE IGNORED

          You attempted to submit a job and  specified  the  /NO  switch
     without  specifying  the /KE switch.  You can only prevent spooling
     of the log file if it is written into your own directory.  The  /NO
     switch  is  ignored  and  job  submission continues.  If you really
     intended  the  /NO  function,  cancel  the  job  and  resubmit  it,
     specifying /KE also.

     (27)  UNABLE TO CONSTRUCT PARAMETER LIST

          This message will only appear if  you  specified  a  parameter
     list  by  means  of the /PM switch when submitting a job.  It means
     that BAT was unable to get enough dynamic  memory  to  construct  a
     parameter list, and is probably due to a system overload.  BAT will



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 30
     BATCH ERROR MESSAGES


     not submit the job in this instance.  You can try the command again
     later.   If  the message persists, it is not only fatal to your job
     submission, but to the healthy running of the whole system!

     (28)  CAN'T ACCEPT JOB - SYSTEM CLOSING DOWN

          The batch system is not accepting any more jobs for  the  time
     being.  Any jobs already in the queue will be allowed to run.  Note
     that this is a  different  condition  to  the  'rundown'  condition
     described above.

     (29)  INVALID LINE COUNT SPECIFICATION

          The /LN switch was used and the switch value given  is  either
     larger  than  the  allowed  maximum,  is zero or negative or is not
     specified.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 31
     THE STACK COMMAND


     The STACK Command
     --- ----- -------

          The STACK command is used to enter the equivalent of  terminal
     input  in  a  batch  job.   It is recommended that all users of the
     batch system read any input that they might need from  disk  files.
     However,   if  this  is  not  possible,  or  the  required  program
     modifications are not easy, the STACK command  can  be  used.   The
     operation  of  STACK  (which  can  be  abbreviated  to STA) is best
     described by means of an example.  Suppose that you  had  a  simple
     FORTRAN program to add two integers together:

     	ACCEPT *,I,J
     	TYPE *,I+J
     	STOP
     	END

          If you were running  this  program  at  a  normal  interactive
     terminal, you might type:

     	F77 PROG=PROG
     	TKB PROG=PROG
     	RUN PROG/TASK=PROG

          The program will then pause and wait for you to  type  in  two
     integers.   In  a  batch  job,  you  obviously  cannot  type in the
     required input since there is no hardware terminal involved in  the
     batch system.  Instead, in *advance* of the program's requirements,
     the STACK command is used to inform  the  virtual  terminal  driver
     that  here  is a line of input that the batch job will want to read
     as the equivalent of terminal input some time in the  future.   The
     virtual terminal driver stores the specified data, and transfers it
     directly to the task when it issues a terminal read  request.   The
     job  description  file  for  running  this  simple job in the batch
     system would look something like

     	F77 PROG=PROG
     	TKB PROG=PROG
     	STACK 18,57
     	RUN PROG/TASK=PROG

          When this program executes the ACCEPT statement,  the  numbers
     18 and 57 will be transferred to the program as the variables I and
     J.  Another example (although this is not recommended practice)  is
     in  the  editing of a file in a batch job.  Suppose that you wanted
     to change all occurrences of ABC to XYZ in the  file  TESTEDIT.FTN.
     A batch job description file to do this would look like

     	STACK TESTEDIT.FTN
     	STACK BLOCK OFF&T&PA/ABC/XYZ/
     	STACK EX
     	EDI



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 32
     THE STACK COMMAND


          or, alternatively,

     	STACK TESTEDIT.FTN
     	STACK BLOCK OFF
     	STACK T
     	STACK PA/ABC/XYZ/
     	STACK EX
     	EDI

          These examples should serve to illustrate the use of the STACK
     command.   If  you  should  want  to  delete the stack at any point
     within your job (you might want to construct a new stack  depending
     on  conditions detected by the job), issue the command PIP NL:=TI:.
     This command deletes the entire stack.   The  same  effect  can  be
     accomplished from within a FORTRAN program by the statements

     	999	READ(LUN,2000,END=1000) DUMMY
     	2000	FORMAT(A1)
     		GO TO 999
     	1000	CONTINUE

          where the variable DUMMY is of type BYTE or LOGICAL*1, and the
     logical unit LUN has been assigned to TI:.

          At the end of every batch  job,  the  stack  is  automatically
     purged by BATMAN, so it is not possible to enter data in a stack in
     one job and expect it to be there in a following job.  If a program
     in a batch job asks for terminal input and the stack is empty, then
     the virtual terminal driver sends an end-of-file indication to  the
     task,  just  as  if  the user typed CTRL/Z.  Since typing CTRL/Z in
     edit mode is equivalent to typing EX, and is also used to terminate
     utilities,  this  can  be used to advantage.  For example, consider
     the following FORTRAN program

     10	READ(5,*,END=20) I,J
     	TYPE *,I+J
     	GO TO 10
     20	STOP
     	END

          This program reads a set of integer pairs from  the  terminal,
     and  types  out their sum.  It then loops and repeats the operation
     until CTRL/Z is typed.  A job description file to run this  job  in
     the batch system might look like

     	STACK 18,57
     	STACK 91,567
     	STACK 614,-91
     	RUN PROG

          In this case the looping of the  program  exhausts  the  job's
     stack,  and  the  end-of-file  indication  returned  by the virtual
     terminal  driver  causes  a  graceful  job  exit.    This   example



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 33
     THE STACK COMMAND


     illustrates  that  there  was  no  real  need to stack the final EX
     command in the editing example above, since running off the end  of
     the  stack would accomplish the same result.  You are encouraged to
     use this feature if possible.

          The following points should be borne in mind  when  using  the
     STACK command:

          (i) Only one line can be stacked with a single STACK  command.
     Also, because the command is directed to the system via the Monitor
     Console Routine (MCR), the length of  the  total  command  line  is
     limited to 80 characters.  Any characters that exist on the command
     line beyond this are ignored, although  they  will  appear  in  the
     job's  log  file  up  to a maximum of 132 characters.  At least one
     character must be present in every STACK command line.  Hence it is
     not currently possible to STACK a blank line.

          (ii) Since MCR edits out any redundant tabs  and  spaces,  all
     tabs  will  be  converted to a space and all occurences of multiple
     spaces together will be compressed to a single space.

          (iii) A limit must be imposed on the size of any  job's  stack
     in order to avoid a possible condition where a program looping on a
     STACK command could destroy the system.  This  limit  is  currently
     set  at 132 characters, and so it is guaranteed that a single STACK
     command will never cause a stack overflow.  If you should  want  to
     read  in  more  data  that  the  maximum stack size will allow, you
     should read in this data via a disk file.  The maximum  stack  size
     can be changed if it proves awkward to users.

          (iv) The STACK command is obviously only legal within a  batch
     job.

          (v) Any combination of printable characters is allowed as  the
     parameter to a STACK command.

          (vi) Any input that a program desires to read from  the  stack
     should be read on a unit which is assigned to TI:.

          (vii) If an error condition is detected by the  STACK  command
     (see  below),  a fatal error exit status of 4 is returned.  You can
     detect this and take action accordingly by means of a  construction
     similar to

     		STACK I WANT TO STACK THIS LINE
     		.IF <EXSTAT> EQ 4 .EXIT

          The STACK command can produce four error messages:

     (1)   COMMAND INPUT ERROR

          This message means that either STACK  was  started  by  a  RUN
     command  (RUN  ...STA  or  RUN  $STACK),  in which case there is no



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 34
     THE STACK COMMAND


     command line to transfer to the stack, or  the  user  attempted  to
     stack a blank line.

     (2)   ILLEGAL CONTEXT

          This message is produced when the STACK command is used  at  a
     normal  interactive  terminal.   This  context  is illegal, since a
     stack is maintained by the virtual terminal driver only  for  batch
     jobs.

     (3)   INSUFFICIENT STACK LEFT FOR THIS REQUEST

          This message is produced whenever a STACK command would  cause
     the  stack to exceed its maximum allowable size if the data were to
     be accepted.  The command, and any other STACK  commands  that  may
     follow in the same job, is not accepted.

     (4)   MEMORY ALLOCATION FAILURE

          This message should not normally appear, but  it  indicates  a
     system pool overload condition such that enough memory could not be
     obtained for the length of data specified to link  into  the  job's
     stack  list.  Allocation failures of this sort are usually followed
     by system hangs.  The STACK command will not be  accepted  in  this
     case.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 35
     WRITING JOB DESCRIPTION FILES


     Writing Job Description Files
     ------- --- ----------- -----

          A job description file  is  essentially  an  indirect  command
     file.  The indirect file processor (...AT.) is described in the MCR
     Operations Manual, and all the facilities described  there  can  be
     used  in the batch system.  This section contains a few examples of
     how job description files can be constructed.  A batch job proceeds
     in  a  similar way to a normal terminal session;  login (HELLO) and
     logout (BYE) are performed automatically by the batch  system,  and
     any  commands  that you might normally issue in between are what go
     into the job description file.  You should take care,  however,  to
     ensure  that any command sequences you write will work in the batch
     system, since there is no way of seeing the  output  from  the  job
     until it has finished.  A command file can be given a test run on a
     normal terminal before submission to batch by issuing a command  of
     the form

          @filespec/TR

          where  "filespec"  is  the  file  specification  of  the   job
     description  file  and the /TR switch implies that the command file
     execution should be traced,  that  is,  commands  specific  to  the
     indirect  file  processor  will  be typed out as they are executed.
     When testing your command files at a terminal, you may need to skip
     certain  command  sequences that would normally only execute in the
     batch system, for example, STACK commands.  A system  program,  VT,
     is  provided for this purpose.  VT exits with a exit status of zero
     if it is run on a normal interactive terminal,  and  with  an  exit
     status  of  (n+5)  if  run in the batch system, where n is the unit
     number of the virtual terminal.  The VT program is  stored  in  UFD
     [10,25] and is used with a RUN command.  For example, you could use
     it as follows:

     	; FIND OUT IF WE ARE IN A BATCH JOB
     	.SETT BATCH
     	RUN [10,25]VT
     	.IF <EXSTAT> < 5 .SETF BATCH
     	; SYMBOL "BATCH" WILL BE TRUE IF WE ARE RUNNING IN BATCH,
     	; AND FALSE OTHERWISE.
     	.IFT BATCH STACK FIRST STACKED LINE
     	.IFT BATCH STACK SECOND STACKED LINE

          The task VT can be used in this manner at any  point  in  your
     job  description  files  to  make  them  completely  independent of
     terminal type (real or virtual).

          The simplest form of job is the running of a program which has
     already  been compiled and task-built.  The job description file in
     this case would consist of a single RUN command:

          RUN PROGRAM



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 36
     WRITING JOB DESCRIPTION FILES


          STACK commands can be added to this job to supply any terminal
     input  that the program may require.  If you wanted to run a number
     of different programs in this way, you could  either  write  a  job
     description  file  for  each  one,  or  you  can  use the parameter
     substitution facility provided by  the  /PM  switch  of  BAT.   For
     example,  suppose a job is designed to read in two numbers from the
     terminal  and  produce  some  output.   You  could  write   a   job
     description file (MYJOB.CMD) containing the commands

     	STACK 18,46
     	RUN PROGRAM

          and submit the job with a command such as

          BAT MYJOB/PA:pswd

          or you could write the job description  file  using  parameter
     substitution:

     	.ENABLE SUBSTITUTION
     	STACK 'P1','P2'
     	.SETS NAME "PROGRAM"
     	.IF P3 NE "" .SETS NAME "'P3'"
     	RUN 'P3'

          The same job could then be submitted as

          BAT MYJOB/PA:pswd/PM:18:46

          In this example, wherever the string 'P1' appears,  the  first
     parameter  supplied by the /PM switch is substituted (providing the
     job starts with .ENABLE SUBSTITUTION), and similarly for  'P2','P3'
     etc.   Any parameters which the job uses which were not supplied by
     /PM (like the third parameter in  this  example)  default  to  zero
     length  strings.   More  flexibility  is  given to the above job by
     using the third parameter.  If  the  job  was  submitted  with  the
     command

          BAT MYJOB/PA:pswd/PM:67:-5:NEXTPROG

          then the commands actually executed would be

     	STACK 67,-5
     	RUN NEXTPROG

          Thus the method of  parameter  substitution  can  be  used  to
     submit  a  variety  of  different  jobs  which all use the same job
     description file, but which accomplish different  functions.   More
     complex  jobs  can be written using the .IF directives available to
     the indirect file processor to make decisions within the job  based
     on  parameters  supplied  at  submission  time.  The above job is a
     simple example of this.



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 37
     WRITING JOB DESCRIPTION FILES


          Jobs can easily be written to perform a sequence of steps  and
     then  resubmit themselves to perform further calculation.  This can
     be used when the maximum  allowable  job  time  is  not  enough  to
     complete a calculation, or if you want to use a short time limit to
     get better turnround.  Suppose you have a program which can perform
     500 iterations on a set of data within a certain time, but you want
     to run the calculation to 5000 iterations.  The  program  could  be
     something like

     		OPEN(UNIT=1,NAME='DATA.DAT',TYPE='OLD',FORM=
     		1 'FORMATTED')
     	C READ IN ITERATION COUNT AND VARIABLES
     		READ(1,*) N,X1,X2,X3,X4
     		  .
     		  .
     		perform 500, iterations
     		  .
     		  .
     		N=N+500
     		REWIND 1
     		WRITE(1,*) N,X1,X2,X3,X4
     		CLOSE(UNIT=1)
     		IF(N.GE.4999)STOP
     		CALL EXST(66)
     		END

          This program reads in the data it  needs  from  a  disk  file,
     performs  500  iterations  on  it, writes the new count back to the
     data file and closes  it.   If  there  are  still  less  than  5000
     iterations  done,  the  program  exits  with  an exit status of 66,
     otherwise it will simply STOP (the same as  exiting  with  an  exit
     status  of  1)  if  the  maximum  number  of  iterations  has  been
     performed.  You could  then  submit  the  job  with  a  normal  BAT
     command.  The job description file might look like

     	RUN PROGRAM
     	.IF <EXSTAT> EQ 66. BAT MYJOB/PA:*/TL:120.

          The special variable <EXSTAT> is given the value of  the  exit
     status  of  the  last  program run.  In this example, when the exit
     status is 66., the batch job resubmits itself with a time limit  of
     2  hours.   This  submission/resubmission cycle will continue until
     5000 iterations have been performed, when no further jobs  will  be
     submitted.   The  subroutine EXST used in this example is described
     on page 6-63 of the RSX-11M V3.2 Executive Reference Manual.  Don't
     forget to close your files before you use it!

          There are some points to bear in mind when passing  parameters
     to  a  batch  job that has been given the restartable attribute, as
     mentioned above.  When a job is first started,  BATMAN  passes  the
     parameters  to the job and then deletes the parameter list.  If the
     system crashes while the job is running, a copy of all of  physical
     memory  as  it  existed  at  the  time of the crash is written to a



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 38
     WRITING JOB DESCRIPTION FILES


     magnetic tape.  The batch system has a Crash Queue Restore  program
     (CQR) which reads this magnetic tape and restores the job queues to
     the point that they were when the crash occurred.   Because  BATMAN
     will  have  deleted  the  parameter list, a restartable job will be
     restarted without any parameters, since BATMAN will not  know  what
     they  were.   Consequently,  the  execution  of  the  job  will  be
     uncertain, and will probably fail.  You can check for  job  restart
     by including commands like

          .IF P1 EQ "" .STOP

          at the head of your job description file.  This  command  will
     cause  the  job  to terminate if the first parameter is null, which
     would be the case if a  job  that  originally  had  parameters  was
     restarted.   You  could  also use this command to ensure that a job
     won't do anything disastrous at its initial startup if  you  forgot
     to specify parameters for a job that was expecting some.  Normally,
     a job should not be marked as restartable if parameters are  passed
     to  it,  but the batch system will accept jobs of this sort so that
     you can take alternative action in the job description  file  if  a
     restart  was  made,  for  example,  file  cleanup.   When  a job is
     restarted by the system after a crash, it will have  its  have  its
     original time limit.

          There are some other points to note in connection with  system
     crashes:

          (i) The batch job may have done some more output  between  the
     time  that  BATMAN  last  saved  the  log  file  and when the crash
     occurred.  You should not assume that all that appears in  the  log
     file  is all that the job did.  Any output that may be missing from
     the log file as a result of the crash will always be less than  one
     page in length.

          (ii) If you wanted to keep the log file (/KE) and also  wanted
     it  spooled (/NO was absent), the log file will not be spooled when
     the system is restored after a crash.

          (iii) Log files  written  to  the  system  directory  will  be
     spooled at system restart, but with a different flag page.

          Don't  try  to  submit  jobs  which  attempt  to  do   maximum
     processing  by  simply running off the end of their time limit.  If
     BATMAN detects this and aborts your job while it is writing data to
     a file, you lose the file!



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 39
     THE TAPE COMMAND


     The TAPE Command
     --- ---- -------

          The TAPE command is issued  in  a  batch  job  to  request  an
     operator to load a magnetic tape for use by the job.  It is used in
     place of the usual Allocate/Mount sequence that is used at a normal
     interactive  terminal.   The  TAPE  command  is an indirect command
     file, and its input (the command  line)  is  read  from  the  job's
     stack.  To use the command, place the sequence

     	STACK command-line
     	@LB:[10,25]TAPE

          in the job description file at a  point  before  the  tape  is
     required.   The  "command-line"  is a line of input giving the tape
     parameters to TAPE.CMD, and you should ensure that there is nothing
     else  on  the  job's  stack when you issue the above sequence.  The
     command line format is:

          label/keyword1/keyword2...

          where "label" is the one to six character label of the tape to
     be  loaded,  and  "keyword1","keyword2"  etc  are  keywords used to
     specify other tape  parameters.   The  label  parameter  is  always
     required,  except  in the case where a scratch tape is to be loaded
     (see the /SCRATCH keyword below).  The valid keywords that  may  be
     used are (all of the specified characters are required):

      /DENS=1600


                The tape is to be processed at a density  of  1600  bpi.
           If  this  keyword  is  not specified, a density of 800 bpi is
           used by default.  This keyword is  always  legal  in  a  TAPE
           command.

      /NEW


                This keyword specifies that the tape  "label"  does  not
           exist already and that a blank tape is to be loaded.  The new
           tape will be initialised and mounted ready for  use,  and  at
           the  end  of the job the tape will be placed in the permanent
           tape library.  Thus it is not necessary to initialise a  tape
           interactively in readiness for a batch job if this keyword is
           used.  The label specified in the command  will  be  used  to
           initialise  and  mount  the  tape.   /NEW  is  not  a default
           condition.




     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 40
     THE TAPE COMMAND


      /SCRATCH

                This keyword specifies that a scratch tape  is  required
           for  the  duration  of the batch job only.  A tape label need
           not be specified in this case since it is irrelevant.   If  a
           label  is  used,  it  will  be the one used to initialise the
           tape, else the default label "SCRATC"  will  be  used.   Data
           written  on  scratch tapes is lost at the end of a batch job.
           This keyword is not  a  default,  and  also  it  may  not  be
           specified in the same command as /NEW.

      /READONLY

                If this keyword is specified, the tape will  be  mounted
           without a write-enable ring, so that write access to the tape
           is not allowed.  By default a tape will be mounted  *with*  a
           write-enable ring.  For obvious reasons, it is illegal to use
           this keyword with either /NEW or /SCRATCH.

      /NOMOUNT

                This keyword specifies  that  the  tape  is  not  to  be
           mounted.   It  is  normally  used for privileged system jobs,
           such as those that  perform  a  disk  backup.   This  keyword
           cannot  be  used  with /NEW or /SCRATCH.  It is also legal to
           specify a tape label  longer  than  6  characters  when  this
           keyword  is  used,  since  the  label is then only a means to
           identify the tape reel.

          The algorithm used by  TAPE  when  requesting  a  tape  is  as
     follows:

          (i) If there are any errors  in  the  command  line,  such  as
     invalid  keywords  or  a  label  missing where one is required, the
     batch job will be terminated immediately with an appropriate  error
     message.   Any  commands following TAPE in the job description file
     will not be executed.

          (ii) TAPE tries to allocate the tape drive for private use  by
     the  batch  job.   If the drive was already allocated to the job by
     means  of  an  earlier  TAPE  command,  this  will  be  immediately
     successful,  as  will  also be the case if the drive was available.
     If the tape drive was allocated to another terminal or batch job at
     the  time,  TAPE will cause the batch job to wait until the current
     user of the drive has deallocated it;   the  batch  job  will  then
     proceed  as  normal.  If the drive does not become available within
     60 minutes, TAPE will cause the job to terminate.

          (iii) Once the drive has become  the  private  device  of  the
     batch  job, TAPE will issue a command to the operator's console for
     the tape to be loaded.  The batch job will then wait for the  drive
     to  become online to the system.  It can only be in this state when
     a tape is loaded.  Note that is is also possible for the wait limit



     BATCH SYSTEM USER'S GUIDE   MARCH 1980                      PAGE 41
     THE TAPE COMMAND


     to  expire at this point;  you might have run the job in the middle
     of the night when there was nobody around to load the tape.

          (iv) When the tape is loaded, the tape will be initialised  if
     /NEW  or  /SCRATCH  was  specified  and  mounted  (if  /NOMOUNT was
     absent).  TAPE then exits and passes control back to the batch job,
     which  can then go ahead and use the tape.  If there are any errors
     at this point, for example, the wrong tape was loaded or a hardware
     error occurs, the batch job is terminated.

          The tape drive is automatically deallocated and dismounted  at
     the  end  of  the  job.   If  you  wish to issue more than one TAPE
     command within each job, you should dismount the tape  (using  DMO)
     before the second TAPE command.














                         APPENDIX A

                           INDEX






INDEX                                               PAGE A-2




/AB  . . . . . . . . . . . . . 16
/AL  . . . . . . . . . . . . . 19
/CA  . . . . . . . . . . . . . 16
/DE  . . . . . . . . . . . . . 10
/EV  . . . . . . . . . . . . . 9
/EX  . . . . . . . . . . . . . 11
/FU  . . . . . . . . . . . . . 19
/HF  . . . . . . . . . . . . . 10
/HU  . . . . . . . . . . . . . 10
/ID  . . . . . . . . . . . . . 23
/IM  . . . . . . . . . . . . . 12
/KE  . . . . . . . . . . . . . 12
/LI  . . . . . . . . . . . . . 19
/LN  . . . . . . . . . . . . . 8
/NO  . . . . . . . . . . . . . 12
/PA  . . . . . . . . . . . . . 9
/PM  . . . . . . . . . . . . . 11
/RL  . . . . . . . . . . . . . 18
/RS  . . . . . . . . . . . . . 11
/TL  . . . . . . . . . . . . . 8
/TR  . . . . . . . . . . . . . 10

Abort Job Switch . . . . . . . 16

BATCH Command  . . . . . . . . 3, 5
Batch Error Messages . . . . . 26
Batch System Id  . . . . . . . 23
Batch Text Messages  . . . . . 24

Cancel Job Switch  . . . . . . 16

Error Messages . . . . . . . . 26
Explicit Version Switch  . . . 9
Express Job Switch . . . . . . 11

Hold For Time Switch . . . . . 10
Hold Until Time Switch . . . . 10

Immediate Mode Switch  . . . . 12
Indirect Files . . . . . . . . 6

Job Cancel Commands  . . . . . 16
Job Description Files  . . . . 35
Job Parameters . . . . . . . . 14
Job Release Commands . . . . . 18
Job Submission . . . . . . . . 8

Line  Limit Switch . . . . . . 8
List All Jobs Switch . . . . . 19
List Full Queue Switch . . . . 19
List Queue Switch  . . . . . . 19
Log File Delete Switch . . . . 10



INDEX                                               PAGE A-3



Log File List Switch . . . . . 12
Log File Retention Switch  . . 12

Multiple Job Submission  . . . 13

Parameter Switch . . . . . . . 11
Password Switch  . . . . . . . 9

Queue Listing Commands . . . . 19

Release Job Switch . . . . . . 18
Restartable Job Switch . . . . 11

STACK Command  . . . . . . . . 2, 4, 31
STACK Error Messages . . . . . 33

TAPE Command . . . . . . . . . 4, 39
Terminal Input . . . . . . . . 31
Text Messages  . . . . . . . . 24
Time Limit Switch  . . . . . . 8
Trace Job Switch . . . . . . . 10

Virtual Terminal . . . . . . . 2, 3
VT . . . . . . . . . . . . . . 35