AXIS - MSU CHEMISTRY AXIS DRAWING ROUTINE



                                T. V. Atkinson
                           Department of Chemistry
                          Michigan State University
                            East Lansing, MI 48824



             1.  Introduction

             2.  Common Features

             3.  AXIS Functionality

             4.  Tick Mark Placement

             5.  Tick Mark Lable Format

             6.  Exceptions

             7.  AXIS - Calling Program Interface
























        AXIS.DOC (15-NOV-82)                                    PAGE 2



        1.0  INTRODUCTION


             AXIS is a FORTRAN callable subroutine for drawing a large
        variety  of  axes  on  any graphic device supported by the MSU
        CHEMISTRY graphics routine VECTOR.   The  compiled  object  of
        AXIS is contained in the library MSULIB.OLB.

             A graph is often used to illustrate relationships among a
        set  of  points specified in some original frame of reference.
        Such graphs are constructed by mapping  the  original  set  of
        points  into  a  new  set  of  points  arranged on the drawing
        surface:  a piece of paper  or  a  graphics  terminal  screen.
        Each point drawn is identified by the cartesian coordinates of
        the point in the frame of reference of  the  drawing  surface.
        The  coordinates  of  a  point are given in units of inches or
        centimeters and are relative to  the  origin  of  the  drawing
        surface.   A mathematical function describes how the points in
        the original frame of reference are mapped into the  frame  of
        reference  of  the  drawing  surface.   For  convenience, this
        transformation is divided into two stages.  The first provides
        a  functional  transformation of the data.  The choice of this
        mapping function is the perogative of  the  person  generating
        the plot and will depend on which aspects of the data is to be
        emphasised.
         
                        x' = ax + b                             A.1
         
                        x' = k/x                                A.2
         
                        x' = logm x                             A.3
         
        where x represents one coordinate of the point in the original
        frame  of  reference,  x' is the transformed coordinate in the
        plotting frame of reference, a, b, and k  are  constants,  and
        "logm"  indicates  the  logarithm of a given base.  The second
        transformation is linear and  maps  the  coordinate  onto  the
        physical   drawing   surface.    The   following   is  such  a
        transformation for the x-coordinate.
         
                        x" = cx' + d                             A.4
         
        where x" will be in the space of the drawing surface, c and  d
        are  constants.   For the remainder of this document, only one
        coordinate of the  points  will  be  considered.   The  second
        coordinate  can  be  handled  independently  in  an  analogous
        manner.  In actual fact, one transformation could  be  derived
        to  accomplish  the  mapping  from the logical to the physical
        frames.  The separation into two transformations was done  for
        convenience in this discussion and to more closely reflect the
        internal algorithms used in AXIS.  This discussion will follow
        the  common  practice  of  referring  to the original frame of
        reference as the "logical"  frame.   The  frame  of  reference
        resulting  from  the  application of mapping functions such as
        shown in line A.1, A.2, and A.3 will  be  refered  to  as  the



        AXIS.DOC (15-NOV-82)                                    PAGE 3



        "intermediate"  frame.   Finally,  the  frame  of  the drawing
        surface will be referred to as the "physical" frame.

             An important part of any graph is the axes that help  the
        viewer  identify the points with respect to the original frame
        of reference.  This is accomplished with tick marks which  are
        distributed   along   the  axis  at  points  corresponding  to
        convenient intervals in the original frame of reference.  Each
        axis  drawn  by AXIS consists of a straight line drawn between
        two points defined in  the  physical  space  of  the  plotting
        surface.   The  axis  is embellished with two varieties, major
        and minor, of tick marks which are distributed along the  axis
        in  such  a way as to meter the logical data space.  The major
        tick marks can be labeled with the  logical  value  associated
        with the tick mark.

             This document describes the use  of  AXIS  to  produce  a
        large  variety of axes.  Such a description must take place on
        different levels.  All users will need to know  the  mechanics
        of getting AXIS to produce the desired graphical constructions
        once a program is built and running.  In addition, programmers
        will   need   to   know  how  to  integrate  AXIS  with  their
        programming.  To serve these varied needs, some parts of  this
        document  will focus on the integration of AXIS into a program
        and are of little value to those users who are using  existing
        programming.   These  sections  will  be  marked  (PROGRAMMERS
        ONLY).  In the discussion of AXIS, reference will be  made  to
        the  various  parameters  used  to control the construction of
        axes by AXIS.  Section 7.1 contains the complete list of these
        parameters.



        2.0  COMMON FEATURES


             This section will discuss the axis and tick mark features
        that  are  common  to  all  axes  drawn  by AXIS regardless of
        mapping function.   Figure  A.1  illustrates  many  pertainent
        features  of  axes  drawn by AXIS.  The axis is drawn from one
        point(APBEG(1),APBEG(2)) in the physical space of the  drawing
        surface  to  a  second  point(APEND(1),APEND(2))  also  in the
        physical space.  This inherent directionality of the  axis  is
        utilized  in  the  specification  of some of the tick mark and
        tick mark label attributes.  The right hand side of  the  axis
        is  that  of an observer standing on the beginning of the axis
        and looking towards the end of the axis.  Since the axis is to
        meter  the  logical  data  space that is being mapped into the
        physical drawing space, the logical values of  the  beginning,
        ALBEG,  and  the  end,  ALEND,  must  also  be specified.  The
        independence of the physical and logical direction of an  axis
        can be seen by comparing Figures A.1 and A.2 which differ only
        in the fact that the values  of  ALBEG  and  ALEND  have  been
        interchanged.



        AXIS.DOC (15-NOV-82)                                    PAGE 4





















                                  FIGURE A.1


        In the example shown in Figure A.1 major tick marks were drawn
        at  points  corresponding  to  10,  15,  20, 25, and 30 in the
        logical data space.  Each major tick  interval  is  subdivided
        into  five minor tick intervals by four minor tick marks drawn
        at points corresponding to 9, 11, 12, 13, 14, 16, ...  in  the
        logical data space.


















                                  FIGURE A.2


        All axes used as illustrations in  this  document  were  drawn
        horizontally  from  left  to  right.   This  was done only for
        convenience and should in no way obscure the flexibility  with
        which  AXIS  can  be  used  to  place axes.  The figure at the
        beginning of AXIS.DOC illustrates this flexibility.

             Figure  A.3,  an  enlargement  of  part  of  Figure  A.1,



        AXIS.DOC (15-NOV-82)                                    PAGE 5



        illustrates  several physical aspects of the tick marks common
        to all axes drawn by AXIS.

























                                  FIGURE A.3


        Notice that there are  actually  four  types  of  tick  marks:
        major  ticks  to the right and left of the axis and minor tick
        marks to the right and  left  of  the  axis.   The  lengths(in
        inches)  of  these  tick  marks  are  controlled  by  the four
        parameters TIXLR, TIXLL, TIXSR, AND TIXSL.  Figure  A.4  shows
        the  axis  of  A.1 along with three other variations differing
        only in the values of the four tick mark length parameters.



        AXIS.DOC (15-NOV-82)                                    PAGE 6

























                                  FIGURE A.4


        These four parameters must be positive but can be of any size.
        In  fact,  the  tick  marks  can  extend across the whole data
        plotting surface resulting in "graph paper" (See Figure S.1 in
        SYMPLT.DOC).   The  line  width  of  the  axis, the major tick
        marks, and the minor tick marks,  and  tick  mark  labels  are
        indepently  ajustable  with  the  parameters  contained in the
        array NIB (See section 7.1).  The line patterns of  the  first
        three  of  these  features are controlled with the contents of
        the array  IPATTX  (See  section  7.1).   Finally,  the  space
        between the major tick marks and their labels is controlled by
        the parameter SPACE.



        3.0  AXIS FUNCTIONALITY


             AXIS is capable of  drawing  axes  with  three  different
        mapping  functions:   linear,  reciprocal,  and logarithmic as
        illustrated in Figure A.5.  The choice of mapping function  is
        controlled by the parameter IFUNC.



        AXIS.DOC (15-NOV-82)                                    PAGE 7




































                                  FIGURE A.5


        For linear axes, the  physical  distance  along  the  axis  is
        linearly   related  to  distances  in  the  logical  frame  of
        reference.  For reciprocal axes, the physical  distance  along
        the  axis  is  related  to  the reciprocal of distances in the
        logical  frame  of  reference.   For  logarithmic  axes,   the
        relationship is logarithmic.  Specifically,


                        XT = (XL - ALBEG)                        A.5
         
                        XT = (1.0/ALBEG - 1.0/XL)                A.6
         
                        XT = LOGM(XL) - LOGM(ALBEG)              A.7
         
        where XL is the coordinate of the point in the  logical  frame
        of  reference,  XT  is  the  intermediate  value,  and LOGM(y)
        represents the logarithm of the number "y" with  the  base  of
        the  logarithm  being  BASLOG.   XT will range from 0.0 at the
        begining of the axis to the transformed value of  ALEND.   The



        AXIS.DOC (15-NOV-82)                                    PAGE 8



        axis  is then mapped into the drawing surface in such a way as
        to place the beginning and end of the  axis  on  the  physical
        points  defined for the ends of the axis.  The details of this
        last transformation is of no consequence to this discussion.



        4.0  TICK MARK PLACEMENT




        4.1  LINEAR


             Once ALBEG and ALEND are specified, the placement of  the
        tick marks is governed by the values of the parameters TLFRST,
        TLLAST, DELLTX, and DELSTX.  TLFRST is the value  (in  logical
        units)  at  which  the  first  logical  tick  mark  is  drawn.
        Starting at TLFRST, the major tick marks occur at intervals of
        DELLTX  (logical  units) until the end of the axis.  Note that
        only if TLFRST is equal to ALBEG, will there be a  major  tick
        mark  at the beginning of the axis.  In addition, a major tick
        mark falls at the  end  of  the  axis  only  if  the  distance
        (logical units) between TLFRST and ALEND is an integral number
        of intervals of the length DELLTX.  Each major  tick  interval
        is  subdivided  into minor intervals of length DELSTX (logical
        units).  All minor tick intervals within a  given  major  tick
        interval  will be equal only if DELLTX is an integral multiple
        of DELSTX.  As can be seen in Figure A.1, there does not  have
        to be tick marks, of either kind, at the ends of an axis.

             TLLAST is used to control the role of TLFRST in tick mark
        placement.   If  TLLAST  is  equal  to  0.0, then the value of
        TLFRST is ignored and the  value  of  ALBEG  is  used  as  the
        position of the first major tick mark.



        4.2  RECIPROCAL


             The same considerations apply for  reciprocal  axes  with
        the  exception  that  the  tick  mark intervals will not be of
        equal physical size when drawn.



        4.3  LOGARITHMIC


             The rules governing tick mark placement  is  considerably
        different  for  logarithmic axes.  First, the major tick marks
        are always forced to occur at integral  powers  of  the  base,
        BASLOG.   TLFRST  and  TLLAST  are  ignored.   ALBEG and ALEND



        AXIS.DOC (15-NOV-82)                                    PAGE 9



        provide the primary user control of tick mark placement.   The
        first  major tick mark is placed at the point corresponding to
        the next power of the base along the axis after ALBEG.  DELLTX
        and DELSTX also have different meanings for logarithmic axes.

























                                  FIGURE A.6


        As can be seen in Figure A.6, (IFIX(DELLTX) - 1) powers of the
        base are skipped before the next major tick mark occurs, where
        the  concept  of  the  FORTRAN  function  "IFIX"  is  used  to
        illustrate   that  only  the  interal  portion  of  DELLTX  is
        utilized.  Figure A.6 contrasts this with the use  of  NLABEL.
        Minor  tick  marks  are  not  drawn  unless  the  base  of the
        logarithm is 10, DELLTX = 1, and DELSTX is greater  than  0.0.
        Thus,  DELSTX can be used to turn off minor ticks when base 10
        logaritmic axes are being  generated.   Such  being  the  only
        logarithmic  axis  with  minor ticks.  When those criteria are
        met, the minor tick marks occur at 2, 3, 4, 5, 6, 7, 8, and  9
        times  the value of the next lower major tick mark as shown in
        Figure A.5 and A.6.



        5.0  TICK MARK LABELS


             AXIS labels the major tick marks with the  logical  value
        associated  with  the  tick mark.  The format of the labels is
        chosen by the user from a variety  of  choices.   Essentially,
        the  labels  are  drawn in ways analogous to formatted FORTRAN



        AXIS.DOC (15-NOV-82)                                   PAGE 10



        writes of  decimal  integers,  octal  integers,  decimal  real
        numbers,  or  decimal  real numbers with exponential notation.
        Figure A.7 illustrates some of the choices available.

























                                  FIGURE A.7


        The user chooses the presentation with a string in  the  array
        TLFORM of the following form.
         
                                (fff ... )                       A.7
         
        where "fff ..." is any  valid  FORTRAN  format  for  a  single
        number.   The parentheses must be included in the string.  For
        real formats, the logical value associated with the tick  mark
        is  encoded  into  a  character string according to the format
        contained in TLFORM.  If, however, the format is for a FORTRAN
        integer, the logical value of the tick mark is first converted
        to an integer value.  The resultant integer  is  then  encoded
        into a character string using the format in TLFORM.  In either
        case the string is compressed by removing all  leading  blanks
        and  the  string  is  drawn.   The  placement of the string is
        governed by the parameters IMODE (see Figure  A.8)  and  SPACE
        (see Figure A.3).  Regardless of orientation and placement the
        label string is centered on the line containing the tick  mark
        being annotated.



        AXIS.DOC (15-NOV-82)                                   PAGE 11


























                                  FIGURE A.8



             Since all leading blanks are removed,  many  formats  are
        actually  equivalent.  In the top example in Figure A.7, "I3",
        "I4", "I5", "I6", "I7", ...  would all have produced identical
        results.   Likewise,  "F6.0", "F7.0", "F8.0", "F9.0", "F10.0",
        ...  would all produce axes identical  to  the  third  example
        from  the top in Figure A.7.  In fact, "I8", "O8", "F15.n", or
        "E15.n" will cover the effective range of label  formats.   No
        others  are needed.  The choice of number of decimal places in
        real labels as chosen by the  integer  "n"  in  the  last  two
        formats is the only variations the user need consider.

             The symbol parameters (see  SYMPLT.DOC)  controlling  the
        characters  used  in  the  labels  are  contained in the array
        CPARAM and the fourth element of the array NIB.

             The tick mark labels are drawn with  the  SYMPLT  library
        "0".   The  user  must be careful that the appropriate library
        has been so defined (see SYMPLT.DOC).



        6.0  EXCEPTIONS


             Errors detected by AXIS have the following  general  form
        and are reported by the routine ERRPRT.
         
                ERROR      AXIS: tttttttttttttttt nnnn



        AXIS.DOC (15-NOV-82)                                   PAGE 12



         
        where "ttt ... " is one of the following error message is  and
        "nnnn" is the octal error number.

             1.  "NO ")" in FORMAT"  -  Format  statement  is  missing
                 the right parenthesis.

             2.  "ILLEGAL MODE    "  -  IMODE  is  equal  to  a  value
                 other than 0, 1, 2, or 3.

             3.  "ILLEGAL LOG BASE"  -  BASELOG is less than or  equal
                 to zero.

             4.  "ILLEGAL FUNCTION"  -  IFUNC  is  equal  to  a  value
                 other than 1, 2, or 3

             5.  "ILLEGAL PHYS. AX"  -  The distance between APBEG and
                 APEND is zero.

             6.  "ALBEG = ALEND   "  -  The axis is  of  zero  logical
                 length.

             7.  "ILLEGAL TLFRST  "  -  TLFRST is outside the interval
                 from ALBEG to ALBEG plus DELLTX.




        AXIS.DOC (15-NOV-82)                                   PAGE 13



        7.0  AXIS - CALLING PROGRAM INTERFACE (PROGRAMMERS ONLY)




        7.1  CALLING SEQUENCE

   
   
        SUBROUTINE AXIS (APBEG,APEND,ALBEG,ALEND,TLFRST,TLLAST,TIXLNG,
        1                LPATTX,DELLTX,DELSTX,NLABEL,TLFORM,CPARAM,
        2                ANGLAB,SPACE,NIB,IMODE,IDISAB,IFUNC,BASLOG,
        3                IERR)
  C====================================================================
  C 
  C     TITLE:  AXIS - SUBROUTINE TO DRAW AXES
  C 
  C     AUTHOR: T V ATKINSON
  C             DEPARTMENT OF CHEMISTRY
  C             MICHIGAN STATE UNIVERSITY
  C             EAST LANSING, MI 48824
  C 
  C     DATE:  12-JAN-82
  C 
  C--------------------------------------------------------------------
  C 
  C     ARGUMENT LIST:
  C 
  C     APBEG(2)        ; COORDINATES(X,Y) OF THE BEGINNING
  C                     ; OF THE AXIS.  THE POINT (X,Y)
  C                     ; IS IN PHYSICAL SPACE.
  C 
  C     APEND(2)        ; COORDINATES(X,Y) OF THE END OF THE AXIS. THE
  C                     ; POINT (X,Y) IS IN PHYSICAL SPACE.
  C 
  C     ALBEG           ; LOGICAL VALUE ASSOCIATED WITH THE BEGINNING
  C                     ; OF THE AXIS.
  C 
  C     ALEND           ; LOGICAL VALUE OF ASSOCIATED WITH THE END
  C                     ; OF THE AXIS
  C 
  C     TLFRST          ; LOGICAL VALUE ASSOCIATED WITH THE FIRST
  C                     ; MAJOR TICK MARK.
  C 
  C     TLLAST          ; IF .NE. 0, THEN TLFRST WILL BE USED TO SET
  C                     ; FIRST MAJOR TICK MARK
  C 
  C     TIXLNG(4)       ; REAL ARRAY OF THE LENGTH(PHYSICAL UNITS) OF
  C                     ; OF TICK MARKS: (1) -> TIXLR, (2) -> TIXLL
  C                     ; (3) -> TIXSR, (4) -> TIXSL
  C 
  C     LPATTX(4)       ; INTEGER ARRAY CONTAINING VERSATEC LINE
  C                     ; PATTERN. (1) -> TIXLR, (2) -> TIXLL,
  C                     ; (3) -> TIXSR, (4) -> TIXSL
  C 



        AXIS.DOC (15-NOV-82)                                   PAGE 14



  C     DELLTX          ; LENGTH OF LARGE TICK MARK INTERVALS (LOGICAL
  C                     ; UNITS
  C                     ; FOR LOGARITHMIC AXES, MAJOR TICK MARKS WILL
  C                     ; BE DRAWN AT EVERY DELLTX'TH POWER OF THE
  C                     ; BASE
  C 
  C     DELSTX          ; LENGTH OF SMALL TICK MARK INTERVALS (LOGICAL
  C                     ; UNITS)
  C                     ; FOR LOGARITHMIC AXES, MINOR TICK MARKS WILL
  C                     ; BE DRAWN ONLY FOR BASLOG = 10.0, DELLTX = 1,
  C                     ; DELSTX .GT. 0.  DELSTX SERVES ONLY TO ENABLE
  C                     ; OR DISABLE THE MINOR TICK MARKS.
  C 
  C     NLABEL          ; LABELS WILL BE PLACED ON EVERY "NLABEL'TH"
  C                     ; MAJOR TICK MARKS.
  C 
  C     TLFORM(20)      ; BYTE ARRAY CONTAINING FORMAT
  C                     ; TO BE USED IN GENERATING TICK MARK LABELS.
  C                     ; E, F, G, I, OR O FORMATS WITH FIELDS LESS
  C                     ; THAN OR EQUAL 20 ARE ALLOWED.  THE
  C                     ; FORMAT MUST BE ENCLOSED IN PARENTHESES.
  C 
  C     CPARAM(5)       ; CHARACTER PARAMETERS:
  C 
  C                     ; (1): WIDTH(PHYSICAL UNITS) OF THE SYMBOLS
  C                     ;       USED IN THE TICK LABELS
  C 
  C                     ; (2): HEIGHT(PHYSICAL UNITS) OF THE SYMBOLS
  C                     ;       USED IN THE TICK LABELS
  C 
  C                     ; (3): VERTICAL DISTANCE BETWEEN LINES OF
  C                     ;        SYMBOLS
  C 
  C                     ; (4): HORIZONTAL SPACE BETWEEN SYMBOLS
  C 
  C                     ; (5): SLANT ANGLE(DEGREES) OF THE SYMBOLS
  C                     ;      USED IN THE TICK LABELS
  C 
  C     ANGLAB          ; FOR MODES 2 AND 3 THE TICKMARK LABELS
  C                     ; WILL BE DRAWN AT AN ANGLE OF ANGLAB(DEGREES)
  C                     ; FROM THE AXIS
  C 
  C     SPACE           ; SPACE(PHYSICAL UNITS) BETWEEN MAJOR TICK
  C                     ; MARK AND LABEL
  C 
  C     NIB(4)          ; VERSATEC NIB SELECTION
  C                     ; (1) -> AXIS
  C                     ; (2) -> MAJOR TICK MARKS
  C                     ; (3) -> MINOR TICK MARKS
  C                     ; (4) -> TICK MARK LABELS
  C 
  C     IMODE           ; TICK MARK LABEL PLACEMENT:
  C                     ; =0 -> LABELS WILL BE TO RIGHT OF AND
  C                     ;       PARALLEL TO THE AXIS
  C                     ; =1 -> LABELS WILL BE TO LEFT OF AND



        AXIS.DOC (15-NOV-82)                                   PAGE 15



  C                     ;       PARALLEL TO THE AXIS
  C                     ; =2 -> LABELS WILL BE TO RIGHT OF AND
  C                     ;       PERPENDICULAR TO THE AXIS
  C                     ; =3 -> LABELS WILL BE TO LEFT OF AND
  C                     ;       PERPENDICULAR TO THE AXIS
  C 
  C 
  C     IDISAB          ; DISABLE FLAG (SUM OF THE FOLLOWING):
  C                     ; 1 -> DISABLE DRAWING AXIS
  C                     ; 2 -> DISABLE DRAWING TICK MARK LABELS
  C                     ; 4 -> DISABLE DRAWING TICK MARKS
  C 
  C     IFUNC           ; FUNCTION FLAG
  C                     ; 1 -> LINEAR AXIS
  C                     ; 2 -> RECIPRICAL AXIS
  C                     ; 3 -> LOG AXIS
  C 
  C     BASLOG          ; BASE OF LOGARITHM USED IN LOG AXIS
  C 
  C     IERR            ; ERROR FLAG: =0 -> NO ERROR
  C 
  C====================================================================
  C 
   



        7.2  COMMON AREAS

     
        COMMON/SABORT/LABORT,LDUM(4)
     
                LABORT  L*1     1       Asynchronous flag for
                                        terminating AXIS before
                                        completion. When set
                                        .TRUE. by an AST routine
                                        such as KBCHEK, AXIS will 
                                        abort. A check of LABORT is
                                        made as each tick mark is
                                        processed.
     
                LDUM    L*1     4       NOT USED BY AXIS
     
     
        COMMON/ERROR/LUNEL
     
                LUNEL   I*2     1       Error messages and other
                                        messages from AXIS are made
                                        on the logical unit number 
                                        which is contained in LUNEL
     
     
        In addition, the COMMON areas used by VECTOR and  SYMPLT  must
        be  handled appropriately.  This is true even when AXIS is the
        only MSU graphics routine used  directly  by  the  user.   See



        AXIS.DOC (15-NOV-82)                                   PAGE 16



        VECTOR.DOC  and  SYMPLT.DOC  for  a discussion of these common
        areas.



        7.3  LOGICAL UNIT USAGE


             The only LUN used by AXIS is LUNEL which is utilized  for
        reporting error messages.



        7.4  SAMPLE USE OF AXIS


             The  program  AXIS.TST  illustrates  the   use   of   the
        subroutine  AXIS.   This  program  can be built using AXIS.CMD
        which also uses AXISTKB.CMD.