LA34 SPEED
	----------

The program LA34SPEED.TSK will change the speed of the line attached to
TT2: (the printer port) to that requested in it.

It is distributed with the relevent value set to 5 (300 baud) and may
be changed with ZAP as follows:

	>ZAP
	ZAP>LA34SPEED.TSK/AB
	_4:246/
	5
	_enter new value here

	0	50
	1	75
	2	110
	3	134.5
	4	200
	5	300
	6	600
	7	1200
	10	1800
	11	2000
	12	2400
	13	3600
	14	4800
	15	7200
	16	9600
	17	19200

	_X
	>

	Then 	>RUN LA34SPEED

	which will set the port speed.

The connection to the printer must have the following characteristics:

	Null MODEM	(crossed pins 2 & 3)
	Dataset ready asserted (or you will get PIP error -3 Device not ready)
			(connect pins 5 and 6 together for this)

The connection of pins 7 and 8 together says that the thing is the
console terminal, and BREAK is then active. It is irrelevent to the printer!.