DOCUMENTATION FOR TIDY.COM

	TIDY is a utility that alphabetizes the directory of a disk,
replacing the old disk directory. It is written for H/Z 100
computers operating under Z-DOS (MS-DOS).

Thereafter, the DIR command will read those files in alphabetical 
order. This makes it easier to locate a given file, and harder to
delete similarly named files accidentally.
	The file COMMAND.COM, if it exists, will remain as the first
visible file on the disk. All deleted file entries are moved above the
active files in the directory, so that new files will not become
interspersed amongst the alphabetized ones.
		COMMAND SYNTAX
	TIDY [d[:]]
You will note that TIDY accepts an optional drive parameter. The
colon usually appended to the drive letter is permitted, but not
required.
Examples:
	tidy b	  -->>	Disk in drive B: is alphabetized.
	TIDY	  -->>  Default disk is alphabetized.
Tidy will reply:
	Tidy verified
This means that tidy has checked the new directory on the disk
and found that it reads correctly. In the event that the new
directory has somehow been garbled on the disk, TIDY would
reply:
	Tidy NOT verified
Tidy will try to write and verify the directory once more, before
giving up.
	The current version of TIDY will recognize 5.25" disks of
several kinds and adjust itself to them: Single-sided double density,
Double-sided double density and Double sided, 96 TPI. It automatically
assumes that disks C: and D: are double-sided double density 8"
disks. If they are not, trouble may ensue.
WARNING: 
********* Tidy may be dangerous to single-sided single density
********  8" disks. It cannot recognize that they have a different
********  directory structure from 8" DSDD disks.

Patch to fix TIDY so that it thinks drives C: and D: are SSSD 8".:
DEBUG TIDY.COM
E 35E <RETURN>
1A <SPACE> <SPACE> 80 <SPACE> 0 <SPACE> 10 <RETURN>
W <RETURN>
Q <RETURN>

	Walter Burt
	109 N. Few
	Madison, WI 53703