Disk Save and Compress (DSC)  Tape Formats
        
       	1-April-81
        
        
        
       I. INTRODUCTION
        
       	This note describes what I have learned of the format of DSC produced
       magnetic tapes.  The information presented here is to be considered prelimi-
       nary and subject to revision. The Stand-Alone DSC V2 was used to create test
       tapes for this project.
        
       				Bill Burton
       				Texas Research Institute of Mental Sciences
       				1300 Moursund
       				Houston, Texas  77030
       				(713) 797-1976 ext 501
       

       II. DSC TAPE STRUCTURE
        
       	Basically, DSC tapes are ANSI standard version 1 labeled magtapes.
       Standard version 1 has been superceeded by version 3 (ANSI X3.27-1978).
       Some of the label records are non-conforming or undefined in the version 3
       standard.
        
       	The DSC tape volume consists of ANSI labeled volume and header
       labels surrounding DSC formatted data records.
        
       Record #  Length     Contents
        
       	1	80.	VOL1 label record
       			volume identifier derived from the output file name
       			given in the DSC command line for the first output
       			file.
       			a. Truncated to 4 characters if necessary
       			b. Padded to 4 characters using the character X
       			c. Sequence number, 2 characters
       				01 for first reel of a set
       				02 for second, etc.
       			d. Other information is documented in ANSI Standard
       			   Manual or RSX-11 I/O Operations Manual.
        
       	2	512.	Dummy bootstrap block which produces the message
       			"This volume does not contain a hardware bootable
       			system".
        
       	3	80.	HDR1 label record
       			a. File name specified in DSC command line
       			b. Volume identifier from VOL1 record
        
       	4	80.	HDR2 label record
       			a. An undefined record code (U) is non-standard
       			b. Logical record length 2064 bytes
       			c. Physical record length maximum 2064 bytes
       			d. The character M in byte 37, non-standard
       			e. Buffer offset 00 in bytes 51-52.
        
       	5	Tapemark
        
       	6	1040.	First DSC formatted record, contains
       			a. 8 word (16 bytes) DSC header with code=40
       			b. 512. bytes of DSC Bookkeeping information
       				(documented in section IV)
       			c. 512. byte Files-11 file header for the file
       				(1,1) [0,0]INDEXF.SYS;1
        
       	7. 	1040.	DSC Data record
       			should contain initialization data for disk
       			structure, 2 virtual blocks worth.
        
       	8.	2064.	DSC Data record
       			More initialization information for virtual
       			block 377,177777.
        
       

    
    
    
    
        
       Record #  Length     Contents
        
   	9. & up 528.	(or 1040. or 1552. or 2064.)
       			Contain DSC data records with DSC codes 1, 2, or 4
       			The details of these records are in section III.
       			DSC copies files to the output tape in file-number
       			order.  For each input file on the disk there is
       				1 type 2 record (of unknown function)
       				1 type 4 Files-11 Header record
       				as many type 1 data records as needed to
       				   hold all virtual blocks allocated to the
       				   input file.
        
        
        
       At the end of data from a disk volume, there will be
        
       Record #  Length     Contents
        
       	N	tapemark
        
       	N+1	80.	EOF1 record
       			Identical to HDR1 except bytes 55-60 now contain
       				the number of physical tape records between
       				HDR2 and EOF1.
        
       	N+2	80.	EOF2 record
       			Identical to HDR2 record
        
       	N+3	tapemark
        
       	N+4	tapemark, if this is the end of the tape volume OR
 
       		80.	HDR1 for the next output tape file 
       				created using DSC /AP switch.
        
       If the tape is filled, (ie reaches the End-of-Tape foil marker)
       the EOF1 and EOF2 records will be replaced by EOV1 and EOV2 records.
       The following reel in the set will start with a VOL1 label with
       the output volume name incremented by 1.  The structure of all subsequent
       reels is the same as described above for the first reel, except that data
       records start immediately.  There will be no DSC initialization records
       (6, 7, and 8. above) on subsequent reels.  It is possible for data from a
       disk file to be split across two reels, and the data for a file can be
       separated from its DSC header records or Files-11 header record when
       changing reels.
       

    
    
    
    
       III. DSC DATA RECORD FORMAT
        
       	Within the labeled file, DSC writes its own format records.
   	These records contain:
    
       	a. An 8. word header
       	b. 1, 2, 3, or 4-512. byte logical data blocks.
    
    
        
       DSC header Format
        
       word 1	Length of the data portion of the record, excluding ALL DSC
       		specific information.
        
       word 2	DSC record-type code indicating the type of data in the data 
       		portion of the record.
   	    	code = 1   Disk data record(s), images of input disk blocks
   	    	       2   Prefix information.  I have not fully decoded the
   	    		  data in these records.  May have some filename
   	  	  	  and extent information.
   	    	       4   Files-11 file header (records of code 4 only have
   	    		  one 512. byte data block).
   	    	      40   Special DSC initialization record.
   	    		        a. 512. bytes of initialization information
   	    			   see section IV.
   	    			b. 512. byte Files-11 header for INDEXF.SYS
        
       words 3-4	For type 1 records, these words contain the Virtual Block Number
   		(VBN) of the of the first logical block in the DSC data record.
   		The low order part of the VBN is in word 3, the high-order
       		part is in the low byte of word 4.
   	    	I have not fully understood the use of these words for the
       		second data record for the INDEXF.SYS file.
        
       word 5	The file number this record applies to
        
       word 6	The file sequence number this record applies to.
        
       words 7-8	Always seem to be zero.
        
       

    
    
    
    
    
       IV. DSC INITIALIZATION RECORD
        
       	This record contains the usual 8-word DSC header with a code
       of octal-40 in word 2.  The data portion of the record contains 512.
       bytes of DSC control information plus the 512. byte Files-11 file header
       for (1,1) [0,0]INDEXF.SYS;1
        
       The DSC control information is formatted within the record as follows:
        
       	    Bytes	Contents
        
            1.- 12.	DSC Output name from the command line, ASCII padded with
       			spaces
           13.- 24.	Input device name (e.g. DK1), ASCII, padded with spaces
           25.- 36.	? null
           37.- 48.	Input volume name, ASCII, padded with nulls
           49.- 52.	? null
           53.- 54.	? 1
           55.- 58.	Number of blocks on the input device, binary
           59.- 62.	Number of blocks in use on the device, binary
       			(not including bad blocks)
           63.- 66.	Number of files in use on the device, binary
           67.- 68.	? 
           69.- 70.	? null
           71.- 72.	? Number of blocks allocated to index file
           73.- 74.	? 
           75.- 76.	? 
           77.- 78.	? 
           79.- 80.	?
           81.- 82.	?
           83.- 84.	?
           85.-510.	? null
          511.-512.	checksum
        
       Items marked with ? are items I have not identified.
   

   	V. DSC CODE 2 RECORDS
   	 
   		One of these records preceeds each files-11 file on the DSC tape
   	 
   		DSC header word 1 = 512
   			   word 2 =   2
   			   word 5 =   file number of the files-11 file
   			   word 6 =   file sequence of the files-11 file.
   	 
   		DSC data block, 512. bytes
   			   words 1-3  the string BACKUP
   			   word    5  The number of bytes in the name string
   			   words 6..  The file name string, in the form
   					DDU:[126,342]filename.ext;ver
   				      the UIC 126,342 seems to be constant,regard-
   				      less of what the source or directory uic was.
   	 
   			   word 46.   Number of blocks allocated to the file
   			   word 52.   (same as word 46.)
   			   word 67.   Owning UIC group number
   			   word 68.   Owning UIC member number.
   	 
   		There is some more information, but I have not determined what
   	it is, it was not necessary for restoring files.
    
    
    
    
    
    
       VI. DSC FILES-11 HEADER RECORD
        
       	One of these records immediately follows the DSC code 2 record
       and contains:
        
       	DSC header word 2 = 4  code for files-11 header record
       		   word 5 = files-11 file number for this file
       		   word 6 = files-11 file sequence number for this file.
        
       	The data portion of the record contains the 512. byte files-11
       header block for the file.  It is an exact image of the header as it was
       on the disk, including the map area.