Disk Save and Compress (DSC)  Tape Formats
     
    	1-April-81
     
     
     
    I. INTRODUCTION
     
    	This note describes what I have learned of the format of DSC produced
    magnetic tapes.  The information presented here is to be considered prelimi-
    nary and subject to revision. The Stand-Alone DSC V2 was used to create test
    tapes for this project.
     
    				Bill Burton
    				Texas Research Institute of Mental Sciences
    				1300 Moursund
    				Houston, Texas  77030
    				(713) 797-1976 ext 501
    

    II. DSC TAPE STRUCTURE
     
    	Basically, DSC tapes are ANSI standard version 1 labeled magtapes.
    Standard version 1 has been superceeded by version 3 (ANSI X3.27-1978).
    Some of the label records are non-conforming or undefined in the version 3
    standard.
     
    	The DSC tape volume consists of ANSI labeled volume and header
    labels surrounding DSC formatted data records.
     
    Record Number  Length  Contents
     
    	1	80.	VOL1 label record
    			volume identifier derived from the output file name
    			given in the DSC command line for the first output
    			file.
    			a. Truncated to 4 characters if necessary
    			b. Padded to 4 characters using the character X
    			c. Sequence number, 2 characters
    				01 for first reel of a set
    				02 for second, etc.
    			d. Other information is documented in ANSI Standard
    			   Manual or RSX-11 I/O Operations Manual.
     
    	2	512.	Dummy bootstrap block which produces the message
    			"This volume does not contain a hardware bootable
    			system".
     
    	3	80.	HDR1 label record
    			a. File name specified in DSC command line
    			b. Volume identifier from VOL1 record
     
    	4	80.	HDR2 label record
    			a. An undefined record code (U) is non-standard
    			b. Logical record length 2064 bytes
    			c. Physical record length maximum 2064 bytes
    			d. The character M in byte 37, non-standard
    			e. Buffer offset 00 in bytes 51-52.
     
    	5	Tapemark
     
    	6	1040.	First DSC formatted record, contains
    			a. 8 word (16 bytes) DSC header with code=40
    			b. 512. bytes of DSC Bookkeeping information
    				(documented in section IV)
    			c. 512. byte Files-11 file header for the file
    				(1,1) [0,0]INDEXF.SYS;1
     
    	7. 	1040.	DSC Data record
    			should contain initialization data for disk
    			structure, 2 virtual blocks worth.
     
    	8.	2064.	DSC Data record
    			More initialization information for virtual
    			block 377,177777.
     
    

 
 
 
 
	9. & up 528.	(or 1040. or 1552. or 2064.)
    			Contain DSC data records with DSC codes 1, 2, or 4
    			The details of these records are in section III.
    			DSC copies files to the output tape in file-number
    			order.  For each input file on the disk there is
    				1 type 2 record (of unknown function)
    				1 type 4 Files-11 Header record
    				as many type 1 data records as needed to
    				   hold all virtual blocks allocated to the
    				   input file.
     
     
     
    At the end of data from a disk volume, there will be
     
    Record number	Length	Contents
     
    	N	tapemark
     
    	N+1	80.	EOF1 record
    			Identical to HDR1 except bytes 55-60 now contain
    				the number of physical tape records between
    				HDR2 and EOF1.
     
    	N+2	80.	EOF2 record
    			Identical to HDR2 record
     
    	N+3	tapemark
     
    	N+4	tapemark, if this is the end of the tape volume OR
    		80.	HDR1 for the next output tape file 
    				created using DSC /AP switch.
     
    If the tape is filled, (ie reaches the End-of-Tape foil marker)
    the EOF1 and EOF2 records will be replaced by EOV1 and EOV2 records.
    The following reel in the set will start with a VOL1 label with
    the output volume name incremented by 1.  The structure of all subsequent
    reels is the same as described above for the first reel, except that data
    records start immediately.  There will be no DSC initialization records
    (6, 7, and 8. above) on subsequent reels.  It is possible for data from a
    disk file to be split across two reels, and the data for a file can be
    separated from its DSC header records or Files-11 header record when
    changing reels.
    

 
 
 
 
    III. DSC DATA RECORD FORMAT
     
    	Within the labeled file, DSC writes its own format records.
	These records contain:
 
    	a. An 8. word header
    	b. 1, 2, 3, or 4-512. byte logical data blocks.
 
 
     
    DSC header Format
     
    word 1	Length of the data portion of the record, excluding ALL DSC
    		specific information.
     
    word 2	DSC record-type code indicating the type of data in the data 
    		portion of the record.
	    	code = 1   Disk data record(s), images of input disk blocks
	    	       2   Prefix information.  I have not fully decoded the
	    		  data in these records.  May have some filename
	  	  	  and extent information.
	    	       4   Files-11 file header (records of code 4 only have
	    		  one 512. byte data block).
	    	      40   Special DSC initialization record.
	    		        a. 512. bytes of initialization information
	    			   see section IV.
	    			b. 512. byte Files-11 header for INDEXF.SYS
     
    words 3-4	For type 1 records, these words contain the Virtual Block Number
		(VBN) of the of the first logical block in the DSC data record.
		The low order part of the VBN is in word 3, the high-order
    		part is in the low byte of word 4.
	    	I have not fully understood the use of these words for the
    		second data record for the INDEXF.SYS file.
     
    word 5	The file number this record applies to
     
    word 6	The file sequence number this record applies to.
     
    words 7-8	Always seem to be zero.
     
    

 
 
 
 
 
    IV. DSC INITIALIZATION RECORD
     
    	This record contains the usual 8-word DSC header with a code
    of octal-40 in word 2.  The data portion of the record contains 512.
    bytes of DSC control information plus the 512. byte Files-11 file header
    for (1,1) [0,0]INDEXF.SYS;1
     
    The DSC control information is formatted within the record as follows:
     
    	Bytes		Contents
     
         1.- 12.	DSC Output name from the command line, ASCII padded with
    			spaces
        13.- 24.	Input device name (e.g. DK1), ASCII, padded with spaces
        25.- 36.	? null
        37.- 48.	Input volume name, ASCII, padded with nulls
        49.- 52.	? null
        53.- 54.	? 1
        55.- 58.	Number of blocks on the input device, binary
        59.- 62.	Number of blocks in use on the device, binary
    			(not including bad blocks)
        63.- 66.	Number of files in use on the device, binary
        67.- 68.	? 
        69.- 70.	? null
        71.- 72.	? Number of blocks allocated to index file
        73.- 74.	? 
        75.- 76.	? 
        77.- 78.	? 
        79.- 80.	?
        81.- 82.	?
        83.- 84.	?
        85.-510.	? null
       511.-512.	checksum
     
    Items marked with ? are items I have not identified.


	V. DSC CODE 2 RECORDS
	 
		One of these records preceeds each files-11 file on the DSC tape
	 
		DSC header word 1 = 512
			   word 2 =   2
			   word 5 =   file number of the files-11 file
			   word 6 =   file sequence of the files-11 file.
	 
		DSC data block, 512. bytes
			   words 1-3  the string BACKUP
			   word    5  The number of bytes in the name string
			   words 6..  The file name string, in the form
					DDU:[126,342]filename.ext;ver
				      the UIC 126,342 seems to be constant,regard-
				      less of what the source or directory uic was.
	 
			   word 46.   Number of blocks allocated to the file
			   word 52.   (same as word 46.)
			   word 67.   Owning UIC group number
			   word 68.   Owning UIC member number.
	 
		There is some more information, but I have not determined what
	it is, it was not necessary for restoring files.
 
 
 
 
 
 
    VI. DSC FILES-11 HEADER RECORD
     
    	One of these records immediately follows the DSC code 2 record
    and contains:
     
    	DSC header word 2 = 4  code for files-11 header record
    		   word 5 = files-11 file number for this file
    		   word 6 = files-11 file sequence number for this file.
     
    	The data portion of the record contains the 512. byte files-11
    header block for the file.  It is an exact image of the header as it was
    on the disk, including the map area.