PROLOD release notes
                          --------------------


     PROLOD  is a  system server  task which  is called  via the  POSSUM
library   to   load  device   drivers.    The   task  image   is   named
LB:[ZZSYS]PROLOD.TSK and it is automatically  installed by the system at
boot time.  The installed task name is $LOAD.

     Since PROLOD was not ready for release at the time P/OS version 2.0
was  shipped, a  PROLOD  server has  been provided  with  the file  name
PROLODV2.TSK.  For  P/OS version 2.0  or 2.0A  ONLY, you must  copy this
file to LB:[ZZSYS]PROLOD.TSK to use  loadable drivers.  For P/OS version
3.0 and later, the file is  already included on the distribution kit and
will be automatically installed with the rest of P/OS.

     There is a minor bug with  the PROLODV2.TSK distributed on the P/OS
V3.0  PRODCL2 floppy;  it  is  corrected in  the  task  image with  this
distribution,  and  an  indirect  command  file for  ZAP  to  apply  the
correction to the PROLODV2.TSK distributed on  a P/OS version 3.0 kit is
also included.  The problem is  that the documented feature of assigning
the logical name PROLOD$MSG the equivalence of 0 to cause PROLOD to type
diagnostic  messages on  your terminal  will  not work  on 2.0  systems.
Analysis of the problem shows that it is either a documentation error in
the TLOG$  series of macros,  or a bug  in the TLOG$  macros themselves,
take your  pick.  The bottom line  is that if  you code the source  of a
program using  any of the TLOG$  macros (TLOG$, TLOG$C, or  TLOG$S), and
you place  a zero in  the third field,  which is currently  reserved, as
opposed  to  just  leaving  the  field blank,  the  DPB  generated  when
assembling on  a 3.0 system  will be 10. words  instead of the  9. words
generated on a 2.0 system.  The DPB will be regarded as invalid on a 2.0
system,  and  the  request  will  always fail  with  the  error  IE.SDP,
indicating invalid DIC or DPB size.  PROLOD does not check for the cause
of  the failure;  it  just assumes  the translation  failed  due to  the
absence of  the logical, and skips  typing the output message.   The ZAP
patch  corrects the  DPB to  a 2.0-compatible  DPB, and  then everything
works fine.   By the  way, if you  desire your code  to work  on pre-3.0
systems, the fix currently is to leave  the third field of a TLOG$ macro
blank  instead of  placing  a zero  in  it.   This causes  a  DPB to  be
generated that will work on all versions of P/OS.

     There are  several errors  in the  version 2.0  Tool Kit  "Guide to
Writing an I/O Driver and Advanced Programmer Notes" which could confuse
the driver developer.

    1    The  illustration  of the  KRB  in  figures  4-13 and  4-15  is
         incorrect.  The  first two  words shown  are K.ICSR  and K.SLT.
         These two words are actually located between K.PRM and K.VCT as
         follows:


                        +-------------------------------+
         K.PRM          |   Driver dependent storage    |
                        +-------------------------------+
         K.ICSR         |   interrupt controller CSR    |
                        +-------------------------------+
         K.SLT          |   reserved    | slot number   |
                        +-------------------------------+
         K.VCT/K.CON    |   vector/4    | contrl. index |
                        +-------------------------------+
         .              |               .               |
         .              /               .               /
         .              /               .               /
         .              |               .               |
                        +-------------------------------+


    2    Many of the labels, such as $DAT, described in the manual imply
         the  the device  name is  optional.  It  is not  optional.  The
         label in  the example  mentioned should be  of the  form $xxDAT
         where "xx" is the logical device name associated with the first
         DCB in the driver's database (D.NAM).

    3    The "dev"  argument in  the GTPKT$, DDT$,  and INTSV$  macro is
         described as being optional.  It is not.

    4    The order  of the  last two DDT$  macro arguments  are reversed
         (p4-5).  The correct format is:

              DDT$    dev,nctrlr,iny,inx,ucbsv,new,buf,opt

    5    The sample driver  BMDRV has no "#" characters due  to the text
         preparation method  used.  Also, the following  labels (and any
         references to them) are incorrect:

         Documented as:                Should be:
         -------------                 ---------

         $DAT                          $BMDAT
         $DCB                          $BMDCB
         $END                          $BMEND


    6    The description  of the PROLOD  call is in error.   The correct
         description and format of the argument list follow:

              STATUS,REQUEST,FNAM,FNAMSZ

         where,

         STATUS         The address of an eight word status block

         REQUEST        The address of a word containing a request value
                        corresponding to the  operation to be performed.
                        The defined decimal values are:


                        1. = Load   a   driver   and  bring  online  all
                             associated controllers and units.

                        2. = Unload a driver after successfully bringing
                             all   associated   controllers  and   units
                             offline.


         FNAM           The  address of  a word  which contains  the two
                        ASCII  characters from  which the  actual driver
                        task and  symbol table filenames may  be derived
                        by  PROLOD.  The  derived  name is  of the  form
                        LB:[ZZSYS]xxDRV.TSK   and   LB:[ZZSYS]xxDRV.STB.
                        Both files must be  present to successfully load
                        a driver.

         FNAMSZ         The  size of  the aforementioned  two bytes  (in
                        bytes).


    7    The  CTB  definition  description   was  not  documented.   The
         following macro excerpt describes the CTB:


    ;+
    ; CONTROLLER TABLE (CTB)
    ;
    ; THE CONTROLLER TABLE IS A CONTROL BLOCK THAT CONTAINS A VECTOR
    ; OF KRB ADDRESSES.  THIS VECTOR MAY BE ADDRESSED BY THE CONTROLLER
    ; INDEX TAKEN FROM THE INTERRUPT PS BY $INTSI.
    ;
    ;-


            .ASECT


    .=177754

    L.CLK:'L' .BLKW 8.              ;START OF CLOCK BLOCK (CLK BLK IS
                                    ;OPTIONAL, AND DRIVER DEPENDENT.
                                    ;ALLOCATION OF THESE 8 WORDS IS NOT
                                    ;REQUIRED IN THE DRIVER'S DATABASE
                                    ;UNLESS USED BY THE DRIVER ITSELF)
    L.DID:'L' .BLKW 1               ;HARDWARE DEVICE ID (WORD ALLOCATION
                                    ;ALWAYS REQUIRED. MAY BE 0.)
    L.ICB:'L' .BLKW 1               ;ICB CHAIN FOR THIS CTB
    L.LNK:'L' .BLKW 1               ;CTB LINK WORD
    L.NAM:'L' .BLKW 1               ;GENERIC CONTROLLER NAME (ASCII)
    L.DCB:'L' .BLKW 1               ;DCB ADDRESS OF THIS DEVICE
    L.NUM:'L' .BLKB 1               ;NUMBER OF KRB ADDRESSES IN TABLE
    L.STS:'L' .BLKB 1               ;CTB STATUS BYTE
    L.KRB:'L' .BLKW 1               ;START OF KRB ADDRESSES.


    ;
    ; NOTE: THE SYMBOL $XXCTB:: IS DEFINED  FOR EACH CTB, WHERE THE
    ; SYMBOL IS NOT THE START OF THE CTB, BUT INSTEAD THE START OF
    ; THE KRB TABLE AT THE END OF THE CTB (L.KRB). THE SYMBOL XXCTB (NO"$")
    ; IS GENERATED BY THE DDT$ MACRO AND IS USED TO IDENTIFY THE
    ; WORD IN THE DRIVER WHICH CONTAINS THE ADDRESS OF THE CONTROLLER'S
    ; CTB IN PRIMARY POOL. XXCTB IS REFERENCE BY THE CODE GENERATED IN THE
    ; INTSV$ MACRO WHEN DETERMINING THE UCB ADDRESS.
    ;



    ;+
    ; CONTROLLER TABLE STATUS BYTE BIT DEFINITIONS
    ;-

    LS.CLK='B'1             ;CLOCK BLOCK AT TOP OF CTB (1=YES)
    LS.MDC='B'2             ;MULTIDRIVER CTB. (1=YES)
    LS.CBL='B'4             ;CLOCK BLK LINKED INTO CLK Q (1=YES)
    LS.CIN='B'10            ;CONT. USE COMMON INT TABLE (1=YES)
    LS.NET'B'=20            ;THIS IS DECNET DEVICE.
                            ;ICB LISTHEAD IN K.PRM, L.DCB INVALID (1=YES)




Developer suggestions:

         1 - Before attempting  to load your  device driver, be  sure to
             load and  run XDT, so that  you are prepared to  handle any
             problems which may arise.

         2 - PROLOD attempts to return a meaningful error message to the
             developer if and only if the logical name "PROLOD$MSG" with
             the equivalence  name "0" is defined.   Multiple errors may
             be detected  in the course  of loading and  sanity checking
             the driver and it's database.

         3 - If  your driver  fails  to load,  correct  the problem  and
             reboot.

         4 - Do not depend  on any registers being  preserved by $IODON.
             In particular  this means  R5 may under  some circumstances
             (overlapped I/O completion) be trashed.

The error codes that PROLOD returns as server dependent errors are:

        0.      Illegal request format
      - 1.      File not a valid driver task image
      - 2.      Privileged command
      - 3.      Inconsistent argument length
      - 4.      Illegal request function code
      - 5.      Illegal unit name format specified
      - 6.      Specified unit not found
      - 7.      Illegal controller name specified
      - 8.      Specified controller not found
      - 9.      Failed to offline device
      - 10.     I/O error on input file
      - 11.     Failed to bring device online
      - 12.     Controller already online
      - 13.     Unit already online
      - 14.     File  has illegal STB format
      - 15.     Device not found in system
      - 16.     Illegal device name specified
      - 17.     Database not found in system or driver
      - 27.     Partition/region  not in system
      - 33.     Device not mounted
      - 34.     File not contiguous
      - 35.     Open failure on file
      - 40.     Task image I/O error in file
      - 46.     Partition  too small
      - 50.     Illegal driver task APR usage
      - 51.     Partition/region  is a common
      - 60.     Driver already resident
      - 61.     Driver being loaded or unloaded
      - 62.     Insufficient pool space
      - 63.     Loadable driver support not in system
      - 64.     Driver not loaded
      - 65.     Driver cannot be unloaded, still online
      - 66.     Device  is attached, busy, online and/or mounted
      - 68.     Invalid driver data base at offset  in file
      - 69.     Driver built with wrong executive STB file
      - 70.     Warning - KRB  interrupt vector too high
      - 72.     Warning - KRB  interrupt vector in use
      - 73.     Symbol is undefined in file
      - 74.     Symbol is doubly defined by file
      - 75.     Illegal value for symbol in file
      - 76.     Driver dispatch table is inconsistent
      - 77.     CTB is not supported by driver -- not loaded
      - 78.     Cannot load/unload a pseudo device
      - 79.     Too many symbols of the form in file
      - 80.     CTB does not exist
      - 81.     DCB table for CTB is full
      - 82.     KRB table of CTB will not accept KRB
      - 83.     KRB not in loadable data base
      - 84.     CTB name is a duplicate
      - 85.     Warning - loadable driver larger than 4K
      - 86.     Partition/region is not a common
      - 87.     KRB is not offline
      - 88.     Illegal use of partition or region




The  following  macro  program   illustrates  a  PROLOD  call.   Another
technique for calling PROLOD is the DCL command "LOAD" on version 3.0 or
later systems.


        .TITLE  LOAD - Example PROLOD call

        .mcall  qiow$s,exit$s   ;request system macros
;
; This task requests PROLOD to load the driver XXDRV from LB:[ZZSYS]
;
start:  mov     #loaarg,r5      ;get args for sample call to PROLOD
        call    prolod          ;load the driver
                                ;print status block always
        mov     #stat,r2        ;point to status args
        mov     #fmt,r1         ;output format
        mov     #outbf,r0       ;output buffer
        call    $edmsg          ;format it
        qiow$s  #io.wlb,#5,#5,,,,<#outbf,r1> ;print it
        exit$s                  ;exit

;
; local data
;

loaarg: .word   4               ;four arguments (simple load call)
        .word   stat            ;pointer to eight word status block
        .word   rqst            ;pointer to PROLOD request
        .word   fnm             ;pointer to filename size
        .word   fnmsiz          ;pointer to size (in bytes) of fnm
stat:   .blkw   8.              ;eight word status block
fnmsiz: .word   fnmsz           ;word containing size of fnm
rqst:   .word   1               ;load (and online all) request
fnm:    .ascii  /XX/            ;driver name
                                ;implied filename "LB:[ZZSYS]XXDRV.TSK"
                                ; AND "LB:[ZZSYS]XXDRV.STB"
fnmsz=.-fnm                     ;name extension as this can't be spec'd)

outbf:  .blkb   132.            ;output buffer for status display
fmt:    .asciz  /%Nload request status: %N%8P/ ;output buffer format string
        .even

        .end    start