PROJECT:        MAC REPLACEMENT PROJECT

DOC. TYPE:      TECHNICAL NOTE
TITLE:          Illegal Instruction Code Utility Tasks ISF and RMF
SUBJECT:        New Tasks on [1,54]

GROUP:          SYSTEM EXTENSIONS
AUTHOR:         D.B.Curtis

DOC NO.:        67
DATE:           25-JUN-79 14:20
FILE:           ILLINS.RNO


                    MODIFIED:  19 JUL 79 15:19



                                                                PAGE 2



1.0  INTRODUCTION

This document is a result of document #34.  This document and document
#70 describe the use of the illegal instruction executive functions.



1.1  Objectives

This document describes the use and  structure  of  the  ISF  and  RMF
tasks.   These  tasks  exist  to insert and remove illegal instruction
code from the system pool space.  The document is separated  into  two
sections:

     1.  User Information

     2.  Maintenance Information




1.2  Discussion

The discussion of these tasks is in document #34.



2.0  USER INFORMATION

This section describes how to use the ISF and RMF tasks.  In  general,
these  tasks  are  not to be used!  They exist to simplify the loading
and unloading of the illegal instruction code  into  and  out  of  the
system  pool.   Typically,  the ISF task is run, and the system saved.
This allows the illegal instruction facility to exist upon startup.

Therefore,  you  must  run  these  tasks  at  a  privileged  terminal.
Usually, the tasks will be run only by the system maintenance people.



2.1  ISF - Insert Function

This task inserts code into the system pool space.  The code  inserted
must  be  position  independent (PIC) and stored on disk as a sharable
PIC  library.   This  sharable  library  task  image  must  be   named
"ILLINS.TSK".  ISF first looks for "SY:ILLINS.TSK".  If not found, ISF
will then look for "LB:[1,1]ILLINS.TSK".  If neither files  exist,  an
error message is returned.



                                                                PAGE 3



Once the file is found, space is reserved in the system pool  and  the
code  is loaded into the reserved space.  Then the illegal instruction
trap vector is connected to this code.  If XDT exists, it is  modified
so that it does not overwrite the illegal instruction vector.

Even if 2 concurrent ISF tasks are running, only one will  load  code.
The  other  task will exit with an error.  However, there does exist a
very small window where illegal instructions from other tasks will not
generate an illegal instruction trap.



2.1.1  ISF Errors - ISF may produce the following errors:

     1.  TERMINAL NOT PRIVILEGED

     2.  ATTEMPT TO EXCEED THE 4K LIMIT

         This error message occurs if the code that  is  being  loaded
         into the pool is larger then 4K words.  Since pool space is a
         valuable resource  some  limit  needed  to  be  imposed.   An
         arbitrary 4K word limit was chosen.

     3.  UNABLE TO FIND ENOUGH POOL SPACE

         The limit was not exceeded, but the pool did not have  enough
         contiguous free space to load the code.

     4.  READ ERROR

         The read of code from the file to the pool failed.

     5.  ILLEGAL INSTRUCTION CODE ALREADY INSTALLED

     6.  MISMATCHED COMMON AND FILE NAME

         The file name and common name  must  match.   This  match  is
         performed by the "PAR" taskbuild option.

     7.  NOT A SHARABLE COMMON TASK IMAGE

     8.  PROGRAMMER ERROR

         Something is wrong with the  sharable  task  image.   See  an
         expert.

     9.  COMMON FILE ERROR NUMBER ######

         Some file error.  At next version, the #s will be replaced by



                                                                PAGE 4



         the actual file error number.




2.2  RMF Task

This task resets the illegal instruction trap vector and releases  the
space  to the system pool.  If XDT exists, the ISF XDT modification is
reset.



2.2.1  RMF Errors - RMF will generate the following errors:

     1.  TERMINAL NOT PRIVILEGED

     2.  ILLEGAL INSTRUCTION CODE NOT INSTALLED




3.0  MAINTENANCE INFORMATION

This  section  consists  of  the  extracted  task  headers  and  other
explanatory text.  This information is:

     1.  ISF File Header

     2.  ISF Task Header

     3.  RMF File Header

     4.  RMF Task Header




                                                                PAGE 5



3.1  ISF FILE HEADER



 FILE DESCRIPTION
     THIS TASK INSERTS EXECUTIVE FUNCTIONS INTO THE POOL SPACE
     THE EXECUTIVE FUNCTIONS ARE INVOKED BY THE USE OF ILLEGAL
     INSTRUCTIONS.
 
     THE TASK RMF REMOVES FUNCTIONS
     THE CODE THAT IS INSERTED EXISTS IN A SHARABLE LIBRARY TASK IMAGE
     THE FOLLOWING RESTRICTIONS APPLY:
 
          1) THE CODE MUST BE PIC
          2) THE CODE MUST BE BUILT IN THE SAME MANNER AS A SHARABLE
               LIBRARY AND CANNOT BE LARGER THEN 4K WORDS
          3) THE LIBRARY IS NAMED ILLINS.TSK: THE CURRENT UIC IS
               CHECKED AND THEN THE LB:[1,1] AREA FOR THIS FILE
          4) IF CODE IS ALREADY ATTACHED TO THIS FUNCTION, NOTHING BUT
               AN ERROR MESSAGE OCCURS. THE CODE MUST BE FIRST REMOVED
               BY RUNNING RMF.
 
 
 ASSEMBLE USING:
     =[200,200]RSXMC/PA:1,[X,Y]ILLINS



                                                                PAGE 6



3.2  ISF TASK HEADER

 INPUTS SIDE EFFECTS:
 
    MODIFIED EXTERNALS
     NONE
 
    OTHER SIDE EFFECTS
     CODE IS LOADED INTO THE DYNAMIC POOL, AND LINKED TO THE
     ILLEGAL INSTRUCTION VECTOR (ILV)
 
 STANDARD REGISTER USAGE
 
 THIS TASK DOES THE FOLLOWING:
 BEGIN
   IF NOT PRIVILEGED THEN ERROR1;
   GET-LIBRARY-INFORMATION(,,,);
   IF STATUS NE OK THEN ERROR-ROUTINE;
   IF REQUIRED SPACE GT 4*1024 THEN ERROR2;
   SWITCH STACK
   ALLOCATE SPACE
   SWITCH TO USER STATE
   IF NO SPACE THEN ERROR3;
   SWITCH STACK
   IF ILL-CODE ALREADY LOADED ERROR5
   FILL HEADER
   SWITCH TO USER
   READ CODE INTO SPACE;
   IF ERROR THEN ERROR4;
   IF XDT THEN FIX XDT;
   LINK ILLEGAL-INSTRUCTION-VECTOR TO SPACE;
 END
 
 THE INFORMATION IN THE POOL POINTED TO BY THE ILLEGAL INSTRUCTION
 TRAP VECTER IS OF THE FORM:
 
     ---------------------------
     | ILL (IN RAD50)          |
     |-------------------------|
     | NUMBER OF BYTES IN AREA |
     |-------------------------|
     | ORIGINAL CONTENTS OF ILV|
     |-------------------------|
ILV> |      NOP                |
     ---------------------------
 



                                                                PAGE 7



3.3  RMF FILE HEADER



 FILE DESCRIPTION
 
     THIS TASK REMOVES THE EXECUTIVE FUNCTIONS INSERTED INTO THE POOL
     AND CONNECTED TO THE ILLEGAL INSTRUCTION INTERRUPT BY THE ISF
     TASK.  THE POOL AREA IS DEALLOCATED, THE ILLEGAL INSTRUCTION
     INTERRUPT IS RESET; AND,IF XDT EXISTS, THE MODIFICATION TO XDT IS
     REMOVED.
     
     ASSEMBLE USING:
          =[200,200]RSXMC/PA:1,[X,Y]ILLREM
     



                                                                PAGE 8



3.4  RMF TASK HEADER



  **-START-MAIN ROUTINE
 
 INPUTS:
     NONE
 
 OUTPUTS:
     NONE
 
 SIDE EFFECTS:
 
    MODIFIED EXTERNALS
     XDT VECTOR RESET TABLE IS RESTORED TO ORIGINAL STATE
 
    OTHER SIDE EFFECTS
     THE ILLEGAL INSTRUCTION VECTOR IS RESET TO ITS ORIGINAL VALUE
     AND THE POOL SPACE IS DEALLOCATED FROM THE SYSTEM POOL
 
 STANDARD REGISTER USAGE
 
 THIS TASK DOES THE FOLLOWING:
 BEGIN
   IF NON-PRIVILEGED TASK THEN ERROR1;
   IF ILL FUNCTIONS NOT INSTALLED THEN ERROR2;
   SWITCH STACKS;
   RESET ILLEGAL INSTRUCTION VECTOR
   RESET XDT;
   DEALLOCATE POOL BUFFER
   SWITCH TO USER STACK;
 END
 
 
 THE INFORMATION POINTED TO BY THE ILLEGAL INSTRUCTION VECTOR
     LOOKS LIKE:
 
     ---------------------------
     | ILL (IN RAD50)          |
     |-------------------------|
     | NUMBER OF BYTES IN AREA |
     |-------------------------|
     | ORIGINAL CONTENTS OF ILV|
     |-------------------------|
ILV> |      NOP                |
     ---------------------------
 
 



                                                                PAGE 9



4.0  GLOSSARY