CHAPTER 1

                              Bye Modifications



              SCLI  depends  upon  a  modified  BYE  program  to  re-
         establish  security  when  a  user logs off from a protected
         terminal.  This chapter describes the modifications  to  the
         BYE program.  



         1.1  Overview

              BYE is a priveleged task which handles logout of a user
         from the RSX system.  BYE is activated by the MCR "BYE" com-
         mand, or automatically when the system detects loss of  car-
         rier on a remote line.  


                                     NOTE

              This automatic logout feature  only  functions  on
              lines   which   have  been  set  remote  (MCR  SET
              /REMOTE=TTnn:  command).  It is possible  to  con-
              nect a modem to a non-remote terminal.  If this is
              done, automatic logout will not work on that port.


              For the secure system, BYE is  modified  in  two  ways.
         The first determines that the terminal being logged off is a
         protected terminal (i.e., one known  to  SCLI),  and  estab-
         lishes  SCLI as the command line interpreter for that termi-
         nal.  The second modification causes  bye  to  not  force  a
         protected terminal back to MCR (the normal logout function).

              A third modification included in the source kit is  not
         required by the secure system.  This modification allows all
         terminals to execute SYSLOGOUT.CMD as priveleged terminals. 



         1.2  USRSB

              The major modifications to BYE are implemented  through
         the  USRSB feature of BYE.  BYE will call a user written su-
         broutine (entry point USRSB::), if such a  routine  is  pre-
         sent.  For SECURE, USRSB contains code and data to a) detect

         Bye Modifications                                   Page 1-2
         



         that a protected terminal is being logged out; and b)  reset
         that terminal's CLI to SCLI, rather than the default of MCR.

              USRSB consists of a data PSECT,  the  main  subroutine,
         and  a  subroutine to determine the terminal number from the
         UCB address.  

              PSECT BYEDAT contains a  simple  table,  JMBTBL,  which
         identifies  the  protected terminals.  MACRO "ENT" will con-
         struct a table entry.  A table entry consists of the  termi-
         nal number as an octal integer (word) value, followed by the
         CLI name in RAD50 format.  Each table entry is  three  words
         long.   The  table  must be terminated by a zero word.  Note
         that, as  written,  it  is  not  possible  to  protect  TT0:
         (normally  the  system  console).  Null entries are normally
         left in the table, providing room to ZAP  new  records  into
         the task image.  

              USRSB operation is straightforward.  Routine $WHATT  is
         called  to obtain the tt number of the terminal being logged
         off.  This number is then compared against  the  entries  in
         JMBTBL.   If  no  match is found, the terminal is not a pro-
         tected terminal, and USRSB simply returns.  If  a  match  is
         found,  USRSB issues a SCLI$ directive to set the terminal's
         CLI to that given in  the  table.   If  the  SCLI  directive
         fails, USRSB returns carry set, else carry clear.  


                                     NOTE

              BYE will detect the error return from  USRSB,  and
              cause  the terminal to be left with 'no' CLI - ef-
              fectively disabling the terminal.  


              The other return from USRSB is in R0.  If  R0  is  non-
         zero,  BYE  assumes  that R0 points to an ASCIZ string to be
         printed on the user's terminal.  This feature is  only  used
         if  constant  DBGMSG  is defined in USRSB.  If DBGMSG is de-
         fined, a string is constructed  which  prints  the  terminal
         number,  as  determined by $WHATT, and the string address is
         returned in R0.  This helps debug the $WHATT routine, but is
         otherwise not useful.  


                                     NOTE

              Although this routine was constructed for use with
              the  security system, it is completely possible to
              use it to establish some other CLI on logout for a
              given  terminal.  The only requirement is that the

         Bye Modifications                                   Page 1-3
         



              CLI be installed and 'initialized' under the  name
              contained  in JMBTBL.  It could be used, for exam-
              ple, to force an application CLI to a terminal.



         1.3  BYE.MAC Modifications

              The remaining modifications are to the mainline  module
         BYE.MAC.   A word, SLVFLG, is added to the local data.  This
         flag is used to save the error  return  status  from  USRSB.
         Also,  the  text  the 'time of day' bye messages is altered.
         This is both grinns, and shows that the modified bye  is  in
         fact running.  

              The first modification is at the point at  which  USRSB
         is  called.   SLVFLG  is  cleared  just prior to the call to
         USRSB.  On return from the routine, SLVFLG is incremented if
         carry is set, retaining the error indication for later use. 

              At BYEXIT, BYE has done the preliminary  work,  and  is
         ready  to  actually  log  the  user  off.  BYE enters system
         state, and forces the terminal CLI to MCR, unless the CP.NIO
         and  CP.LGO  bits are set in the CLIDAT buffer.  This buffer
         is filled in with information on the current CLI very  early
         in  BYE's run.  Thus, an un-modified program would not known
         that a different CLI had been  set  by  the  USRSB  routine.
         This  deficiency  is rectified by again calling GCII$ to re-
         fresh the CLIDAT buffer just prior to the switch  to  system
         state.   The  second  call  to  GCII$  occurs after USRSB is
         called, and thus picks up information on the cli established
         by  USRSB.   Since  SCLI  is initialized with the "/LGO" and
         "/QUI" switches, BYE does not switch back to MCR.  The  code
         for this patch is simply copied from that near the beginning
         of BYE.MAC.  

              After returning from system state (at  BYEXT),  several
         QIOs  are  done  to configure the port.  Following this, the
         terminal is set slaved, and SLVFLG checked.   If  SLVFLG  is
         non-zero,  the  port is left slaved.  Otherwise, it is reset
         non-slaved.  Thus, if USRSB was unable to set  SCLI  to  the
         port, it is left slaved, rather than in MCR.  

              The final modification to BYE is not really needed  for
         security.  It does, however, increase the usefullness of the
         SYSLOGOUT.CMD facility dramatically.  In routine CMDFIL, the
         user  is unconditionally set priveleged prior to the call to
         indirect.  This is 'safe', in that the  user's  terminal  is
         slaved  at  this  time.   Of course, access to SYSLOGOUT.CMD
         must be restricted, or non-priv users might cause  mischeif.
         Upon  return from SYSLOGOUT, the terminal is unconditionally

         Bye Modifications                                   Page 1-4
         



         set non-priveleged, and remains so for the remainder of  the
         logout process.  This modification is especially useful in a
         virtual-disk envrionment, where it is  desired  to  dismount
         and deallocate all of the user's virtual disks on logout.  



         1.4  Rebuilding BYE

              BYE must be rebuilt for each installation, since it  is
         a  priveleged task, overmapping the executive.  Two versions
         must be maintained:  one each for M and MPLUS.  USRSB.MAC is
         the  same for either M or MPLUS, but must be edited to prop-
         erly configure the terminal  table  for  each  installation.
         The  remaining  notes  in this section apply directly to the
         MPLUS files in [1,101].  They also apply to the  M  specific
         files in [1,102].

              USRSB is simply assembled (MAC USRSB,USRSB=USRSB).  BYE
         is  re-assembled  with  command file BYEASM.CMD, and rebuilt
         with command file BYE2BLD.CMD.  The taskbuild  files  assume
         device  TK:  points to the 'sysgen work disk'.  It is recom-
         mended that the archives be copied to the sysgen work  disk,
         the site-specific modifications made there, and the task re-
         built on the sysgen work disk.  

              The  primary  account  for  the  BYE  modifications  is
         [1,101].   Files  which  are  specific  to  11M are found in
         [1,102].  To build BYE for M+,  use  the  command  files  in
         [1,101]; for M, the ones in [1,102].

              The source kits contain  COR  files  to  patch  BYE.MAC
         using  SLP.   These correction files apply to MPLUS V2.1"E",
         and to M V4.1"B".  If the release or  update  level  change,
         examine  the  BYE.MAC  source  code for the new version very
         carefully, as the COR files will probably no longer work.  

              If it is necessary to manually apply the patches, use a
         patched  copy of BYE.MAC to locate the patches, and manually
         apply them to the new source using EDT.  All of the  patches
         carry  audit  trail  "JMB219",  making  them easy to locate.
         Once a BYE.MAC has been created for the new release, use CMP
         to create a new COR file.  

              The plant-specific files (such as USRSB.MAC) should  be
         saved on the stdgen disk under the proper uic.  

              It is necessary to modify the taskbuild file  for  BYE,
         in  order to enable USRSB.  Simply comment out the GBLDEF of
         USRSB, and specify USRSB in the input file list.  The  task-
         build file creates a task named BYE2, to help prevent confu-

         Bye Modifications                                   Page 1-5
         



         sion with the unmodified version built by SYSGEN.  


                                     NOTE

                   If an entire STDGEN release is being  genned,
              the  modified  BYE  source should be copied to the
              sysgen work disk, and the correct USRSB.OBJ placed
              in   [1,24]  prior  to  starting  SYSGEN.   Modify
              [1,20]BYEBLD.BLD to reference USRSB.OBJ,  and  let
              SYSGEN build the modified BYE program bye default.
              Having once modified BYEBLD.BLD,  subsequent  gens
              using  the same work disk will automatically build
              the correct BYE.TSK.



         
         





                                   CONTENTS



         1.  Bye Modifications  . . . . . . . . . . . . . . . . . 1-1

             1.1  Overview  . . . . . . . . . . . . . . . . . . . 1-1
             1.2  USRSB . . . . . . . . . . . . . . . . . . . . . 1-1
             1.3  BYE.MAC Modifications . . . . . . . . . . . . . 1-3
             1.4  Rebuilding BYE  . . . . . . . . . . . . . . . . 1-4