VT100 File Listing Utility (VTL)

                               22-September-1983


                            Technical Documentation
                                      by
                                 Robin Miller


VT100 File Listing Utility                                             Page  2
Introduction




     1.0  INTRODUCTION.  

     This  program  is  used  to list file(s) on a VT100 family terminal.
     The file(s) are displayed one screen at a  time  for  easy  viewing.
     Various  commands  can be entered to change listing parameters or to
     position to a particular portion of the file.  Many of the  commands
     are the same as the Digital editor EDT.  Commands can be entered ei-
     ther by using keys on the VT100 keypad, or by entering  commands  to
     the  prompt at the bottom of the screen.  Some of the major features
     of the program are outlined below:  

          1.  Delete the file being displayed.  
          2.  Print the file being displayed.  
          3.  Split screen mode to display two files.  
          4.  CTRL/C detection for aborting searches, etc.  
          5.  Write portions of the file being displayed.  
          6.  Skipping to the next directory when using wildcards.  
          7.  Displaying the file header of the file being displayed. 
          8.  Teco compatible see-all mode.  

     Enhancments requested but not implemented yet:  

          1.  Searching backwards.  
          2.  Backing up to the previous file.  
          3.  Swapping to auxillary file with full screen display.  
          4.  Initialization file to define the keypad keys.  
          5.  /FIND, /RECORD, and /PAGE options at startup.  
          6.  Repetition count for commands.  
          7.  Working message.  


     The  maximum  record  size  that can be displayed is 512 characters.
     All commands have a repetition count of one.  Relative  and  indexed
     files are not supported.  


     2.0  PROGRAM INSTALLATION.  

     There are three files used with this program.  The VTL program writ-
     ten  in Macro-11, the VTLNATIVE program written in Macro-32, and the
     error message file.  These files must be  copied  to  the  following
     directorys:  

          1.  SYS$SYSTEM:VTL.EXE  -  This  is  the main program which can
              be  started   with   either   the   "MCR   VTL"   or   "RUN
              SYS$SYSTEM:VTL" commands.  

          2.  SYS$SYSTEM:VTLNATIVE.EXE  -  This  program  is  used  to do
              the VMS wildcard lookup using the run time library  routine
              LIB$FIND_FILE.   It  is  executed  by  the VTL program from
              compatibility (PDP-11) mode using the unsupported  elephant
              directive.   This  program CAN NOT be started using the RUN
              command.  



VT100 File Listing Utility                                             Page  3
Program Installation


              If  the  native  mode routine is not located in SYS$SYSTEM,
              define the logical name SYS$NORDEN pointing to  the  direc-
              tory  where it resides.  If the routine is not found in ei-
              ther directory, an error is reported to the  terminal,  the
              user  is  prompted,  and  the  program  continues using the
              normal RSX-11M file lookup routines.  

          3.  LB:[1,2]RSX11M.MSG  -  This  file  contains the RSX-11M er-
              ror messages.  If the error message file is not located  in
              LB:[1,2],  the  program  attempts  to  lookup  the  file in
              DUA0:[MILLER].   Unfortunatly,  since  the  error   message
              routine  uses QIO$'s to perform directory lookup, a logical
              name can not be used.  You  can  edit  file  RSXMSG.MAC  in
              routine  GERMSG  to  point  to  any alternate directory you
              want.  You can't specify a sub-directory.  



     3.0  GETTING STARTED.  

     There are three methods of starting the VTL program.   The  sections
     described  below  presume  you  have the following symbol defined in
     your login command file:  

        $ VTL :== $SYS$SYSTEM:VTL

          1.  The  most  common  way  of  starting the program is to pass
              a file specification to the program on  the  command  line.
              When using this method, the file(s) specified are displayed
              and the program exits when  there  are  no  more  files  to
              display.  

              Example:
                $ VTL [ROBIN...]ABC*.DAT

              On  RSX-11M, multiple file specifications separated by com-
              mas can be specified.  

              Example:
                $ VTL DL0:[*]*.CMD,DL1:[*]*.CMD

              The  wildcard  characters  on  RSX-11M  are  limited to the
              asterisk (*) in the UIC, file name, file type,  or  version
              fields.   The  percent sign (%) and the asterisk as used in
              the VAX/VMS example above can not be used.  This may be ad-
              ded in a furture version since RMS on RSX-11M V4.1 now sup-
              ports the same wildcarding that VMS supports.  

          2.  The  second  method  is  to allow the program to prompt for
              the file specification.  Using this method  allows  you  to
              remain in the program until you type CTRL/Z to exit.  After
              starting  the  program,  the  screen  is  cleared  and  the
              "File(s):   "  prompt  is  displayed  at  the bottom of the
              screen.  At this  point,  the  file  specification  can  be
              entered.  



VT100 File Listing Utility                                             Page  4
Getting Started


              Example:
                $ VTL
                (The screen is cleared)
                File(s):

          3.  The  last  method  allows  you  to  use  a  command file as
              input to the program.  The command file contains a list  of
              all  the files to be displayed.  This method is useful when
              using a program such as "DIRECTORY" to  display  all  files
              created since a particular date.  The length of the command
              lines can be up  to  a  maximum  of  256  characters.   The
              continuation  character "-" is allowed at the end of a line
              to continue the command line on the next line.  If the file
              extension  isn't  specified  the default is .CMD on RSX-11M
              and .COM on VAX/VMS.  When the end of the command  file  is
              reached, the program exits.  

              Example:
                $ DIRECTORY/NOHEADER/NOTRAILER/SINCE/OUTPUT=TODAY.COM
                $ VTL @TODAY

     Once  you've  started  displaying  a file, typing the PF2 key on the
     keypad displays the keypad diagram.  There is no other online  help.
     This  document  will  be  converted  to the help file format at some
     point so HELP at DCL level is possible.  


     4.0  STARTUP OPTIONS.  

     There are a number of options which can be specified at startup time
     by  specifying  option  on  the  command  line.   The options can be
     specified anywhere on the command line which allows them to  be  ap-
     pended  to  the  VTL  symbol  defined in your login command file (if
     desired).  

     Options  can not be specified on the command line when using command
     file input.  When using command file input, the options must  reside
     within  the  command  file  or before the command file line within a
     command procedure.  

     All  options  are  preceded  with  a slash "/" and can be negated by
     preceding the option with either a minus sign "-" or  a  "NO".   All
     startup options can be changed after the program is started with the
     "SET"  command.   If  the  option  is  not  followed  by  the   word
     "(default)",  then  the  option must be specified to enable that op-
     tion.  The following are the valid startup options:  

          1.  AVO  -  The  VT100  has the advanced video option.  If your
              VT100 doesn't have the AVO, the terminal can  only  display
              14 lines of 132 column text.  

          2.  BINARY   -  When  displaying  a  binary  file,  the  option
              suppresses escape seqeuences and all control characters  so
              the text within the binary file can be displayed properly. 



VT100 File Listing Utility                                             Page  5
Startup Options


          3.  FEXIT  -  This  controls  whether the program automatically
              displays the next file or exits at the  end  of  file.   If
              enabled, the user must type either "EXIT" or "NEXT" to stop
              displaying the current file.  

          4.  FF  -  This  controls  whether  formfeeds are passed to the
              VT100.  This option is useful when the VT100 has a hardcopy
              attached  to  allow  formfeeds  to skip to the top of a new
              page.  

          5.  HEADER  -  Controls  whether  the  file header is automati-
              cally displayed before displaying the first  page  (screen)
              of  the  file.   The  file  header is displayed in a format
              similar to the "ANALYZE/RMS" DCL command.  

          6.  LINES  -  This  controls  the number of lines to display on
              the screen.  The default number of lines  displayed  is  20
              lines  if  the  file name display is enabled or 22 or it is
              disabled.  When operating over a dialup modem, it is  often
              desirable  to  display  fewer lines.  The command format is
              "/LINES=n" where "n" can be from 5 to 20 (or 22 if the file
              name is disabled).  

          7.  MARK  -  This  command  is  used  to override how often the
              program marks record positions.  These record positions are
              used to quickly reposition to records within the file.  The
              program has 1000 entrys for saving  the  record  positions.
              If this switch is not specified, the following algorithm is
              used to calculate the record marking count:  

                ((blocks_used * records/block)/mark_entrys) = mark_count.
              
              The worst case records/block is based upon the maximum
              record size.
              
                max_record > 256 use (512/32) = 16 records/block.
                max_record > 100 use (512/16) = 32 records/block.
                max_record >  32 use (512/8)  = 64 records/block.
                max_record >  16 use (512/4)  = 128 records/block.
                max_record <  16 use (512/2)  = 256 records/block.

              The mark count is limited to a maximum of 50 records unless
              overridden.  If the file you are displaying has  more  than
              50,000  records,  you  will  want  to specify a mark count.
              Otherwise, all records after 50,000 will have to be skipped
              to  sequentially  from the last record marked.  The command
              format is "/MARK=n".  

          8.  OUTPUT  -  This  allows  you  to specify an output file for
              subsequent write commands.  The output file is  not  opened
              until  the  first  write command is issued, thus errors are
              deferred  until  that  time.    The   command   format   is
              "/OUTPUT=filename".  The output file remains open until the
              CLOSE command is issued or until you exit the program.  



VT100 File Listing Utility                                             Page  6
Startup Options


          9.  NARROW  -  This  forces  all  files  to  be  displayed on a
              narrow (80 column) screen.   Normally  the  maximum  record
              size  within  the  file  is  used  to determine whether the
              screen should be NARROW or WIDE.  

         10.  NAME  (default)  -  This  controls  whether  the  file name
              is displayed at the top of the screen.  Disabling the  file
              name display allows two more lines for the file display.  

         11.  NUMBERS  -  This  controls  whether  the  record  number is
              displayed  along  the  left  hand  margin  preceeding  each
              display  line.  These record numbers are useful when speci-
              fying a range for the write command.  

         12.  PROTECT   (default)   -   The  controls  whether  the  file
              protection is changed before  deleting  a  file  using  the
              DELETE  command.   If  protection  is  disabled,  the  file
              protection is changed to allow deletion before deleting the
              file.   This  is  useful if you want to delete a file whose
              protection is set to read-only which causes  a  "Protection
              Violation" when trying to delete it.  

         13.  QUIET  -  This  controls  whether  bells  are  appended  to
              messages displayed.  If  bells  are  disabled,  then  bells
              within the file are also suppressed.  

         14.  RULER  -  This  controls  whether  a  ruler is displayed on
              the line following the file name line.  If  the  file  name
              display is disabled then the ruler is also disabled.  

         15.  SCREEN  -  This  is  used  to  specify  the  screen display
              width.  It also controls the number of characters displayed
              on  each  line  before the line is truncated.  Specifying a
              screen width overrides the NARROW  or  WIDE  options.   The
              command  format  is  "/SCREEN=n" where the range for "n" is
              from 1 to 512.  

         16.  SCROLL  -  This  controls  whether  both  files  should  be
              scrolled when in split screen mode.  This  is  useful  when
              you  want  to do a visual comparison of two files.  You can
              only scroll in the forward direction using either the  down
              arrow  key,  section,  enter, or the return key.  All other
              commands only affect the active file.  

         17.  SEEALL  -  This  allows  non-printable  characters  such as
              control characters to be displayed.  Control characters are
              displayed as ^char and tabs, carriage return, linefeed, and
              formfeed are displayed by the VT100 graphics HT, CR, LF, or
              FF respectivly.  Escapes are displayed as dollar signs ($). 

         18.  SECTION  -  This  specifies  the  number  of lines advanced
              by the  SECTION  command.   The  default  section  size  is
              normally    (max_lines-(max_lines/5)+1)   where   max_lines
              depends on whether you've specified the /LINES  options  or
              if  the you've disabled the file name display.  The command
              format is "/SECTION=n" where "n" can be any number.  If you


VT100 File Listing Utility                                             Page  7
Startup Options


              specify  zero,  the  section  size  is calculated using the
              algorithm above.  

         19.  TECO  -  This  is  a  sub-option  to  the  SEEALL  command.
              This controls whether control characters are displayed  us-
              ing  the  graphics  character  +/-char instead of the ^char
              format.  

         20.  VERSION   -  This  displays  the  current  version  of  the
              program.  

         21.  WIDE  -  This  forces  all  files to be displayed on a wide
              (132 column) screen.   Normally  the  maximum  record  size
              within  the  file  is  used to determine whether the screen
              should be NARROW or WIDE.  

         22.  WAIT   (default)-   This   controls   whether  the  program
              waits for a response to the prompt "Type any  character  to
              continue:   "  when a file open error occurs when wildcards
              are specified.  If this option  is  disabled,  the  program
              waits three seconds to give the user time to read the error
              message displayed and then continues to open the next file.
              This  option  is  useful  when  doing  a wildcard list of a
              directory which has files protected which normally  results
              in the error "Protection Violation" being displayed.  



     5.0  FILE LISTING COMMANDS.  

     There are a number of commands  available  while  a  file  is  being
     displayed.   The command prompt is displayed on the last line of the
     screen and is constructed from the last record number displayed.  If
     the  file  is positioned at the end of file, then the command prompt
     is preceeded with the string "EOF-".  Commands can also be issued by
     using  various  keys  on  the VT100 keypad.  A keypad diagram can be
     displayed by using the PF2 key.  The  keypad  commands  CAN  NOT  be
     modified by an initialization file such as EDT keys.  The valid com-
     mands are described below:  

          1.  ADVANCE  -  This  command  sets  the  direction to the for-
              ward direction.  

          2.  BOTTOM  -  This  command  positions  to the end of file and
              then displays the last part of the file on the screen.  

          3.  BACKUP  -  This  command  sets  the  direction to the back-
              ward direction.  

          4.  CLOSE  -  This  command  is  used  to  close an output file
              which is open for the WRITE command.  

          5.  DELETE  -  This  command  is  used  to  delete  the current
              file being displayed.  



VT100 File Listing Utility                                             Page  8
File Listing Commands


          6.  EXIT  -  This  command  is used to exit from the program or
              to exit split screen mode when the bottom file  is  active.
              You can also exit by typing CTRL/Z.  

          7.  FIND  -  This  command  is  used  to  find a search string.
              The command format is "FIND search_string".   If  a  search
              string is not specified, you are prompted for one.  

          8.  FNDNXT  -  This  command  is  used  to  find  the  next oc-
              curance of a search string.  If  a  search  string  doesn't
              exist, you are prompted for one.  

          9.  LEFT  -  This  command  moves the margin left if previously
              moved right  with  the  RIGHT  command.   This  command  is
              equivalent  to  the  EDT  SHR (shift screen right) command.
              The command format is "LEFT n" where "n" is from 1 to 512. 

         10.  LINE  -  This  command  is  used  to  advance  or  backup a
              single display line depending of the direction.   The  plus
              sign  or minus sign is used to advance or backup overriding
              the current direction.  

         11.  NDIR  -  This  command  is  used to display the next direc-
              tory or sub-directory when wildcard  directorys  have  been
              specified.  

         12.  NEXT  -  This  command  is  used  to  display the next file
              (if any).  If there are no further files the program exits. 

         13.  PAGE  -  This  command  is  used  to  find  the  next page.
              The formfeed character defines the  start  the  next  page.
              FORTRAN formfeeds and print file formfeeds are not detected
              (future version).  

         14.  PRINT  -  This  command  is  used to spool the current file
              to the line  printer.   On  RSX-11M,  the  file  is  always
              spooled  to  LP0.   On  VAX/VMS,  the  file  is  spooled to
              SYS$PRINT which can be assigned to any line  printer.   The
              file  is  left  open for display after the file is spooled.
              Thus, you must use the NEXT command  to  display  the  next
              file if desired.  

         15.  RIGHT  -  This  command  is  used  to move the margin right
              to display part of the text truncated due to  the  terminal
              width.   This  command  is equivalent to the EDT SHL (shift
              display left) command.  The command  format  is  "RIGHT  n"
              where "n" can be from 1 to 512.  

         16.  REFRESH  -  This  command  is  used  to  refresh the entire
              screen displayed.  The keypad  is  re-enabled  (incase  the
              terminal  was  reset) and the entire screen is redisplayed.
              If two files are displayed in split screen mode, then  both
              files  are  redisplayed.   This  command is used for screen
              refresh instead of CTRL/W used in EDT since CTRL/W  is  not
              recognized by the program.  



VT100 File Listing Utility                                             Page  9
File Listing Commands


         17.  RESET  -  This  command  is  used to reset the select range
              selected by the SELECT command.  

         18.  SELECT  -  This  command  selects  a portion of the file to
              be written.  The lines selected are  displayed  in  reverse
              video just like EDT.  A "WRITE SELECT" command is then used
              to write the selected lines.  When this command  is  issued
              the  current  page  is  automatically selected.  The select
              point starts at the top of the current  page.   Because  of
              this  implementation,  the minimum that can be written is a
              single page.  To write less than a page, enable the  record
              number display and use a "WRITE range" command.  

         19.  SECTION  -  This  command  is  used  to advance or backup a
              section depending on the current direction.  

         20.  SET   -   This  command  is  used  to  change  the  listing
              parameters.  This command is used  to  change  any  of  the
              startup   options   described   early  plus  the  following
              commands;  SET SEARCH EXACT or GENERAL (default), SET TAB n
              (defines the size of a tab, the default is 8).  

         21.  SHOW  -  This  command  is  used  to  display  a particular
              parameter.  Valid keywords for SHOW are:  

                FILE    - Displays the file name.
                HEADER  - Displays the file header.
                KEYPAD  - Displays the keypad diagram.
                MARK    - Displays the record marking count.
                SEARCH  - Displays the search string and general/exact.
                VERSION - Displays the version number.

         22.  SHL - Same as the RIGHT command.  

         23.  SHR - Same as the LEFT command.  

         24.  SPLIT  -  This  command  is  used  to  enter  split  screen
              mode.  If you don't enter a file name on the command  line,
              you  are  prompted for one.  After the file is successfully
              opened, the screen is redisplayed with the  file  specified
              at  the  bottom  of  the  screen.   The "Active" message is
              displayed to the right of the file name to show which  file
              is  currently  active.   If commands to override the screen
              width were not specified (such as NARROW  and  WIDE),  then
              the  screen  width  is controlled by the active file at the
              time the REFRESH command is executed.  

              To  exit  from  split screen mode, make the bottom file the
              "Active" file and then type EXIT or CTRL/Z.  After the bot-
              tom screen is exited, the top file is then redisplayed on a
              full screen.  

         25.  SWAP  -  This  command  is  used  to  swap  between the two
              files displayed in split screen mode.  The "Active" message
              is  displayed  to the right of the active file or the "SHOW


VT100 File Listing Utility                                            Page  10
File Listing Commands


              FILE" command is executed  if  the  file  name  display  is
              disabled.  

         26.  TOP  -  This  command  is  used  to positions to the top of
              the file and displays the first page on the screen.  

         27.  WRITE  -  This  command  is  used to write a portion of the
              active file to an output file.  If an output  file  is  not
              open  or  you didn't specify an output file at startup time
              with the "/OUTPUT=filename" option, you are prompted for  a
              file name.  The range for the WRITE command are descibed in
              a later section.  The default range for the  write  command
              is "WRITE PAGE".  

     If  you  type  the  carriage  return or ENTER key on the keypad, the
     program displays the next page of the file.  A page  is  defined  as
     the  text displayed on the screen as opposed to the text between two
     formfeeds as in EDT.  

     You  can also enter a record number at the command prompt.  This al-
     lows you to skip quickly to a position within  the  file.   This  is
     useful  if  you  don't  know  what  to  search for and don't want to
     repeatedly type the carriage return or section key.  


     5.1  The Range Format.  

     The range for the WRITE command is a subset of the ranges allowed by
     EDT.  The normal range format is:  

        beginning_line:ending_line
                or
        beginning_line THRU ending_line

     The following keywords can be used for the ranges:  

        . - The ending line number on the current page.
        line_number - A line number within the file.
        BEGIN - The beginning line number of the file (line 1).
        BPAGE - The beginning line number on the current page.
        EPAGE - The ending line number on the current page.
        END - The ending line number in the file.
     
        PAGE - The current page displayed.  Same as BPAGE:EPAGE.
        WHOLE - The whole file.  Same as BEGIN:END.
        SELECT - The lines selected by the SELECT command.




VT100 File Listing Utility                                            Page  11
The Output File.


     5.2  The Output File.  

     The output file is created with the file type and file attributes of
     the  active  input file.  This means that if the input file is vari-
     able length with print-file-format, the output file will be the same
     format.   This should be rememebered when writing portions of multi-
     ple input file.  No checking is done to  insure  the  current  input
     file  attributes  are  the same as the output file.  Thus, writing a
     FORTRAN file to an output file created with  print-file-format  will
     not PRINT or TYPE the way you expect after closing the output file. 


     6.0  OUTPUT FORMATTING.  

     Currently, only  implied  (carriage-return)  and  embedded  carriage
     control  files  are  formatted  properly for output to the terminal.
     The first character of each record in FORTRAN files and the sequence
     field used for print-files for carriage control are not interpreted.
     This support will be added in a future version of the program.  


     6.1  Embedded Carriage Control.  

     For files with embedded carriage control  (carriage-return/line-feed
     in the file), scrolling backwards doesn't always backup a section or
     a single page.  This is because a single record may be displayed  on
     several  lines  on  the  screen.   To accuratly display these files,
     display the file in SEEALL mode (this is what  EDT  actually  does).
     Also,  when  scrolling  backwards  through embedded carriage control
     file, the entire screen is redisplayed since this is the only way to
     accuratly redisplay the previous page.  


     7.0  ABNORMAL PROGRAM TERMINATION.  

     If the program aborts abnormally or by your typing  CTRL/Y  to  stop
     it,  a  software  terminal characteristic must be changed.  When the
     program starts, the escape sequence characteristic is enabled.  This
     tells the terminal driver to expect escape sequences.  By having the
     terminal driver interpret the escape sequences, the program  doesn't
     have to do single character reads which results in less system over-
     head (EDT does single character reads).  

     The   following   DCL   command   disables   the   escape   sequence
     characteristic:  

        $ SET TERMINAL/NOESCAPE




VT100 File Listing Utility                                            Page  12
CTRL/Y Detection.


     8.0  CTRL/Y DETECTION.  

     Since this program is written in PDP-11 Macro and runs  in  compati-
     bility  mode,  CTRL/Y  detection is not possible.  If you are in the
     habit of typing CTRL/Y to abort programs, this program should be run
     from  a  command  procedure  which  handles  CTRL/Y  or  disables it
     altogether.  


     9.0  CONTINUATION PROMPT.  

     Whenever  file  open  errors  occur  with  wildcards  active,  after
     displaying  the  file  header,  or  after displaying the keypad, the
     program prompts with the message "Type any  character  to  continue:
     ".   At  this prompt, typing "E" or CTRL/Z will exit the program and
     typing "N" will display the next file.  The "N"ext feature is useful
     if you want to display just the file header (/HEADER option) of each
     file when using wildcards.  


VT100 File Listing Utility                                            Page  13
Index


                                     Index
                                     -----

     Abnormal Program Termination.   . . . . . . . . . . . . . . . .   11

     Continuation Prompt . . . . . . . . . . . . . . . . . . . . . .   12
     CTRL/Y Detection.   . . . . . . . . . . . . . . . . . . . . . .   12

     Embedded Carriage Control . . . . . . . . . . . . . . . . . . .   11

     File Listing Commands . . . . . . . . . . . . . . . . . . . . .    7

     Getting Started . . . . . . . . . . . . . . . . . . . . . . . .    3

     Introduction  . . . . . . . . . . . . . . . . . . . . . . . . .    2

     Output Formatting . . . . . . . . . . . . . . . . . . . . . . .   11

     Program Installation  . . . . . . . . . . . . . . . . . . . . .    2

     Startup Options . . . . . . . . . . . . . . . . . . . . . . . .    4

     The Output File.    . . . . . . . . . . . . . . . . . . . . . .   11
     The Range Format  . . . . . . . . . . . . . . . . . . . . . . .   10