Documentation for CPU Monitor for RSX11-M/M+

        Don Rubin
        S.E.T. Inc.
        9703 Forest Glen Court
        Silver Spring, MD 20910

     The  enclosed  program  is  a  graphic  CPU monitor for
RSX11M/M+.  It requires no  modification  to  the  operating
system  and  adds  little  overhead  to  the system.  It was
created because there is no way to measure CPU  availability
in RSX (the stuff on the RMD system page is garbage, ask the
DEC developers).  

     The program works as follows:  

      .  it  is  installed  at priority 200 (though 50 would
         be OK) 

      .  after  initialization  it  hangs  a  1  second mark
         time and drops to priority 5 at which point  it  is
         higher  than  the  null  task  but lower than every
         other task in the system 

      .  at the low priority it increments a counter 

      .  when   the   mark  time  expires  the  priority  is
         raised and the CPU  availability  is  computed  and
         displayed on a bar graph (VT100) 

      .  the  counter  is  cleared,  another  mark  time  is
         hung, and priority dropped 

      .  program  is  terminated  by  the  user  typing  any
         character on the terminal the  program  is  running
         from 


     In  our  application  we  have a version of the program
which doesn't display the data directly but dumps it into  a
global common for display by another task.  The program must
be calibrated for each particular system.  To calibrate  run
the  program with the command "CPU CALIB" which causes it to
dump calibration values.  Pick the average value (make  sure
the  system  is quiescent at this point).  After calibration
the value may be hard coded into the program or  entered  in
the command line "CPU 115000".  

     The  program  can  be  built  as follows (note, source,
objects and task supplied) 

        f77 cpu=cpu/-wr
        mac mymark=mymark
        mac ast=ast
        tkb cpu/fp=cpu,mymark,ast,lb:[1,1]f4pots/lb
        ins cpu/task=...cpu/pri=200



                                                     Page  2



     The  program  as  supplied displays CPU utilization but
can be changed to show availability by subtracting the util-
ization  from  100  before  display.   I  can answer written
inquires only at the above address.  

                                                        Don
Rubin