Linking Programs "Too Big" for a PDP-11
	                             or
	             How to Break the Rules and Survive

	                         R N Caffin



	                          Abstract

	Imagine you are writing a very large  program  on  a  PDP-11
	under RT-11.  Perhaps a super spreadsheet for instance.  The
	cell-data is stored in a sophisticated database system;  the
	spreadsheet operations are many and varied;  the user inter-
	face is quite complex;  the  data  can  be  reformated  into
	graphical  form;   output  can  be to a variety of different
	devices.  How many subroutines will you have?  How will  you
	link it all together?  It turns out that there is a solution
	in some cases.



	                        Introduction

	Consider a very large  program  such  as  the  one  outlined
	above.   Obviously  it  won't  all fit in the ordinary RT-11
	program memory  space,  so  you  have  to  go  to  overlays.
	Overlaying  is  one  way of getting quart-size programs into
	pint-size spaces.  It involves making different parts of the
	program  appear to occupy the same memory space at different
	times, and can be achieved in several ways.  One way  is  to
	have  the system read different program modules in from disk
	when they are needed, but place them all in the same  physi-
	cal  memory space.  Of course, as you read in one module, it
	overlays or rather overwrites the previous  one.   A  better
	way  is to have all the program modules in extended physical
	memory and move them into active memory when they are  need-
	ed.   The  PDP-11  architecture  contains  a  virtual memory
	mapping system which supports this concept, and  this  paper
	is mainly concerned with the use of virtual overlays.



	                   PDP-11 Memory mapping

	On most PDP-11s the contents of the program counter are  not
	placed  directly  onto  the memory address bus;  rather they
	are fed through a translation table which extends the physi-
	cal  address  from  16  bits to 22 bits (on the Q-bus).  The
	table actually translates only the top few address bits into
	a  another number, so that "pages" of space are moved around
	as units.  The page is 8k bytes, and can be "mapped" to  lie
	anywhere in physical memory.  This is done by putting a map-
	ping value into the appropriate Page Address Register in the
	table.   Given the 16 bit Program Counter, you can only have
	eight pages active or addressable by the PC at any time.

	                                                      Page 2




	To use virtual overlays you store all your program in physi-
	cal  memory,  but broken into pages, so that by altering the
	PAR you can at any stage map the needed routines into active
	memory.  In theory, this allows you to store vast amounts of
	program code in physical memory for immediate access.

	The trouble is, by the time you get your program all  sorted
	out,  you find that you need twelve overlay regions, and the
	PDP-11 has only eight, not all of which may even  be  avail-
	able.   You  could  fold the overlay regions backwards, such
	that region 9 was on top of region 3, and so  on,  but  this
	would violate one of the cardinal rules of the RT-11 and the
	PDP-11 architecture, as spelt out in the  LINKER  documenta-
	tion:   you  would  be destroying the subroutine return path
	and the system would crash.  What to do?  The simplest solu-
	tion  is  to go to a 32-bit machine, and that would normally
	be the best solution.  But suppose you don't have a VAX,  or
	that you must use a PDP-11 for other reasons (all excellent,
	of course):  what can you do?

	Conventional wisdom gives little hope here.  The good  books
	contain  clear  explanations  of  why  you cannot do zig-zag
	through the overlays.  However, if you are prepared to be  a
	bit  adventurous  and  to  ignore, or at least question, the
	official rules, there are ways  to  beat  the  system.   You
	could  write your own linker and overlay handler, and modify
	the compiler as well, but  that  would  leave  you  with  an
	orphan and cost more than a new VAX anyhow.  We discard that
	option.  What else is there which does not require any  mod-
	ifications to the compiler or linker?



	                    The Overlay Problem

	It turns out  that  the  restrictions  which  DEC  place  on
	virtual  overlays are not always true.  There IS a very sim-
	ple way of stacking virtual overlay regions and segments, to
	an  almost  unlimited  extent, which can be used from within
	Fortran.  No Macro code, no patches anywhere, just  Fortran,
	some  imagination,  and a bit more preparation.  The last is
	the key, and is vital.

	Imagine we have a program which has to look like this (never
	mind  why for the moment), and it won't fit into the conven-
	tional overlay technique.  For the  moment  we  will  assume
	that subroutines only get called from one place, but we will
	generalise later on.

	                                                      Page 3



	                      ROOT
	 
	 
	 
	         SUB11        SUB12        SUB13
	 
	 
	 
	       SUB21      SUB22      SUB23      SUB24
	 
	 
	 
	        SUB31        SUB32        SUB33

	Note in particular that each routine is big enough to  be  a
	separate overlay:  they are NOT all simultaneously in active
	memory.  That is, the PARs for the first level  of  overlays
	point  either to SUB11 or SUB12 or SUB13.  [In what follows,
	the reader is invited to first draw in the subroutine  link-
	ages by following the paths outlined below, and then to come
	back and contemplate the problem.  The  author  regrets  the
	limitations of an ASCII printer!]

	The calling path ROOT-SUB11-SUB21-SUB11 is standard.

	The path -SUB11-SUB22-SUB32-SUB22...  is also  standard,  so
	far.

	The path -SUB22-SUB12...  is NOT standard:  it destroys  the
	return path to SUB11.

	The path -SUB12-SUB23...  destroys the path to SUB22.

	The path -SUB23-SUB32-SUB23...  is standard within itself.

	The path -SUB23-SUB13...  destroys the return path to SUB12.

	The path -SUB13-SUB24...  destroys the return path to SUB23.

	The path -SUB24-SUB33-SUB24...  is standard.

	The return paths  SUB13-SUB23-,  SUB23-SUB12-,  SUB12-SUB22-
	and  SUB22-SUB11-  are  all  wiped  out  and will have to be
	restored somehow.



	                   The Secret to Success

	Consider the memory map, not as a linear  space,  but  as  a
	series  of  adjacent  overlay  regions,  each containing 4kW
	words.  Rather than leave such matters to the operating sys-
	tem,  which  is  conventional  wisdom,  we  will take active
	notice of the fact that the PARs point, not  to  the  actual
	routines  in  these  regions,  but  to  the start of the 4kW
	pages, wherever they happen to be in memory.  In particular,

	                                                      Page 4



	we  note  that we are keeping the overlays in "virtual memo-
	ry", which is really genuine physical memory  on  a  PDP-11.
	Imagine we then have to create something like this:  [Again,
	please draw boxes around the  routines  using  the  dots  as
	guides,  then  make  cross  links  similar  to  the previous
	diagram.  The exact linkages don't matter, as long  as  they
	are zig-zag and illegal.]

	 .         .   .         .   .         .
	                                         Each box is a
	    SUB21         SUB22         SUB23    4kW region 
	                                         mapped into
	 .         .   .         .   .         . the address 
	                                         space by a 
	    SUB11         SUB12         SUB13    PAR
	  
	 .         .   .         .   .         .
	 
	    ROOT
	  
	 .         .   .         .   .         .

	The big problem is  the  return  path:   the  wrong  overlay
	regions  are  now  mapped  into  the apparent active address
	space (of 64kB).  Conventional wisdom gives up here, but  we
	can  do  better  than that.  In fact, to fix up the PARs for
	returning, all we have to do is persuade the system to reset
	them.  The PARs were altered when the program asked the For-
	tran Operating Time System (OTS) to alter them so  it  could
	access  a  subroutine.   All we have to do is ask the OTS to
	reset the PARs to where WE know they should be.  That can be
	done  without  any  alterations to the compiler or linker by
	calling a dummy routine in the required page, thus:   [Again
	draw  the  boxs  such that dum21 is inside with SUB21 and so
	on.  Then think of each box as a 4kWd region pointed to by a
	PAR.]

	    .         .     .         .     .         .
	 
	      SUB21           SUB22           SUB23
	 
	  
	        dum21           dum22
	    .         .     .         .     .         .
	 
	      SUB11           SUB12           SUB13
	 
	  
	        dum11           dum12
	    .         .     .         .     .         .
	 
	       ROOT
	  
	    .         .

	The critical thing to understand here is  that  the  overlay

	                                                      Page 5



	region  is in principle a 4kW block of memory containing the
	subroutines, and the PAR just makes  that  page  active,  or
	appear  in  "low"  memory.   Other parts of the OTS sort out
	where inside the page the actual subroutine starts.  You  do
	not need to know where the subroutine starts:  you just need
	to make sure that the right page is in "low" memory  at  the
	time.  The call to the dummy subroutine makes the OTS set up
	the PAR correctly:  after all, it "knows" which PAR is need-
	ed  for  that  subroutine  and what to do to make it active.
	All you have to do is hope that everything is where you left
	it when you altered the PARs, especially the return location
	inside that 4kW block, and this is guaranteed to be so  when
	you  use  virtual overlays.  The code and local data remains
	in memory and is not altered.



	                Basic Implementation Details

	This technique does work:  I have tried it out with  several
	programs,  using the conventional Fortran PRINT statement as
	a tracer, and it runs like  clockwork.   The  code  required
	looks like this:

	        subroutine SUB11()      !This goes in overlay
	         .......                ! region 1
	        call SUB21()
	         .....
	        return
	        end

	        subroutine DUM11X()     !This too goes in overlay
	        return                  ! region 1, with SUB11()
	        end                     !Note it does nothing.

	        subroutine SUB21()
	         .....
	        call SUB12()            !Destroy the return path
	         ........
	        call DUM11X()           !Force OTS to reset PAR
	        return                  ! before returning to SUB11
	        end

	That is, it runs as long as you set it  up  100%  correctly.
	There  is very little room for error with this approach com-
	pared with normal subroutine calls in normal overlays.



	                  The General Return Path

	So far we have considered a subroutine which is called  from
	only  one  place  -  it  knows what to do to get back.  This
	would not normally be the case:  utility subroutines can  be
	called  from  anywhere, many times over.  We would prefer to
	have a general technique, applicable to all sorts of library

	                                                      Page 6



	routines.

	For this to be feasible, we will need to know to  which  PAR
	the  program has to return at any point.  Provision for this
	sort of thing does not exist in the RT-11  Fortran  library,
	but  you will have this information.  You have to design the
	overlay structure to accomodate all the modules:   in  doing
	so   you   will  know  what  overlay  regions  contain  what
	subroutines.  In fact, it is not necessary for you  to  know
	what  PARs  are  used, just the overlay region numbers.  You
	can have the calling  routine  give  the  called  subroutine
	enough information to make the return successfully.

	For the general case you put a dummy routine at the  end  of
	every  overlay  segment.   You include the segment number of
	the calling routine in the subroutine call, and save it in a
	local variable in the called subroutine.  To return, you use
	that segment number  to  select  which  dummy  PAR-restoring
	routine  to call.  This is best done with a single "cleanup"
	routine with a built-in  table.   It  is  probably  best  to
	locate  this  routine  in  the root segment:  this way it is
	always accessible from anywhere.  Thus for  a  program  with
	three  overlay  segments  in each of two overlay regions, we
	might have the following linkage and code (although in prac-
	tice  one  might  have  DUM11  in the same file as SUB11 and
	several routines in each overlay segment, and so on:

	        PROG=PROG,OHANDL//      !The linkage structure
	        SUB11,DUM11/V:1         !Segment 1
	        SUB12,DUM12/V:1         !Segment 2
	        SUB13,DUM13/V:1         !Segment 3
	        SUB21,DUM21/V:2         !Segment 4
	        SUB22,DUM22/V:2         !Segment 5
	        SUB23,DUM23/V:2         !Segment 6
	        //

	              subroutine DUMmn()
	              return
	              end

	      You can see from the code involved that the time taken
	      for  the  OTS overlay handler to juggle the PAR to get
	      DUMmn and for DUMmn to execute  will  be  very  small:
	      roughly  twenty  machine language instructions in all.
	      This is a very small overhead and should deter no-one.
	      The  special Fortran PAR handler is equally simple and
	      brief in execution:

	              subroutine OHANDL(n)
	               
	              if (n.lt.1 .or. n.gt.6) then
	                stop 'OHANDL-F-Invalid region'
	              elseif (n.eq.1) then
	                call DUM11()
	              elseif(n.eq.2) then
	                call DUM12()

	                                                      Page 7



	              elseif (n.eq.3) then
	                call DUM13()
	              elseif (n.eq.4) then
	                call DUM21()
	              elseif (n.eq.5) then
	                call DUM22()
	              elseif (n.eq.6) then
	                call DUM23()
	              endif
	              return
	              end

	The efficiency of this approach  is  made  possible  by  the
	extra time you spend in planning the layout, but this is not
	a run-time cost.  (It  is  only  machine  time  which  costs
	money, after all!  Yours is free.)

	A more complex version of  the  previous  flow  diagram  and
	overlay  map,  involving  multiple calls between the layers,
	has been tested with the  above  overlay  handler  and  does
	indeed  work.  To be sure, this is a somewhat painful way of
	going about things, and yet it requires  no  special  skills
	with  or  patches  to the complex internals of the compiler,
	linker or operating system.  All it requires is a  bit  more
	analysis  of  the  problem  and  some  understanding  of the
	machine and its behaviour.  



	                        Speculation

	It would be possible to modify the compiler and  the  linker
	to  generate  a short-cut version of all this.  The compiler
	could build an automatic call to a macro version  of  OHANDL
	for  a  fix-up  of  the PARs into the code generated for the
	RETURN statement.  The linker could  put  the  dummy  fix-up
	routines into each overlay segment.  This would be very sim-
	ilar to the above but automatic, and perhaps easier and more
	reliable.

	An alternate and far more elegant approach would be for  the
	compiler  and linker to build a look-up table of the regions
	as part of the image and for the  OTS  to  adjust  the  PARs
	according  to  the  table  while  inside  the Fortran RETURN
	statement.  Little change to the compiler and  linker  would
	be required for this:  the segment number could be passed to
	the called subroutine in the high byte of the first word  of
	the  subroutine  argument frame and the table put in the OTS
	data psect.  

	              ------------------------
	        R5 -> |SEGMENT  | no of args |
	              ------------------------
	              | argument 1 address   |
	              ------------------------
	              | argument 2 address   |

	                                                      Page 8



	              ------------------------
	              |argument 3 address    |
	              ------------------------
	              |......................|

	Ommission of the appropriate compiler  and  linker  switches
	would  leave  the  segment number equal to 0, which would be
	recognised as a NO-OP by the OTS.  This  strategy  would  be
	transparent  to  conventional  programs.   Since the segment
	number would be a  byte,  this  technique  would  limit  the
	number  of  overlay  segments  to be less than 256.  This is
	probably quite a reasonable limitation for the  PDP-11.   It
	is interesting to note that DEC reserves this byte for "pos-
	sible future use".  Perhaps they once intended to  implement
	some variant of this scheme?  They may have been deterred by
	some of the problems associated with it, and it is  probably
	a bit late now for them to bother.



	                    Benefits and Dangers

	Variables in Overlays

	You should note this important difference between  disk  and
	virtual  overlays.   When a disk-based overlay is first read
	into memory it is reasonable to assume that all local  vari-
	ables  in  that  part  of the image will be at their initial
	default value (usually zero), and they will  effectively  be
	reset  to the default each time you reload that overlay from
	disk.  This is correct and according  to  the  ANSI  Fortran
	Standard.   But  when  you  keep the routines in virtual, or
	extended, memory, the local variables are in physical memory
	at  the  time  of  subroutine  exit  and stay there.  So you
	should NOT assume that a local  variable  will  be  zero  at
	subroutine entry.  There may well be left over values there.
	The Fortran OTS does NOT check for  this:   it  is  strictly
	your  reponsibility.  At the same time, you should note that
	disk-based overlays will always  lose  old  local  variables
	when  the  overlay  region is overwritten.  Good programming
	practice requires that you never assume the value of an uni-
	tialised  variable  anyhow,  and  this  applies  to ordinary
	subroutines just as much as it applies here.  The  compensa-
	tion  for  this  is  that,  under controlled conditions, you
	should be able to preserve local variables from call to call
	despite  what  the standard says.  The effect is roughly the
	same as the SAVE statement in Fortran 77.  This may well  be
	of use - provided care is exercised!

	A special problem exists with variables stored  in  extended
	memory when you use this extended overlay technique:  passed
	parameters are no longer always reliable:  they can be lost.
	This violates the Fortran standard.  You will have to become
	rather more careful about how you store and pass parameters,
	but  a  very vocal fraction of the computer science has been
	preaching this for years anyhow.

	                                                      Page 9





	Loss of Variables

	Once you violate the  assumptions  which  the  compiler  and
	linker  make  during their operation, you are no longer pro-
	tected by them.  There can be a real danger  if  you  assume
	variables  persist  without adequate cross-checking, or that
	variables are always accessible.  Consider for instance that
	you  have  passed  a local variable X from SUB21 through the
	subroutine call to SUB12, and then to SUB22.  This  variable
	X  is  accessible  from  SUB12, but when SUB22 is called the
	PARs have been altered and the address pointer for X is  now
	pointing  to  some  unknown location within SUB22.  Altering
	the variable could have fatal consequences for  the  program
	if you hit code space:  in any event the results of the cal-
	culation will be incorrect.

	Fortunately, the problem is not insoluble.   If  you  assign
	the  incoming  X  to a local variable Y in SUB12, call SUB22
	with Y, and then remember to  update  X  with  the  returned
	value  of  Y  before you return to SUB21, then all should be
	well.  This has the effect of "moving" the variable into the
	region  containing  SUB12,  such that the address as seen in
	SUB22 is still valid.  


	Use of COMMON

	The continuous reassignment of variables can be  a  nuisance
	and  a  source of mysterious errors.  In many cases it would
	be better to keep such variables in a global  common.   Care
	should  be  exercised  here:   make  sure the common is in a
	stable region!  The root segment is the safest, provided the
	additional  demands on that space don't push it over another
	page boundary and destroy your carefully mapped out  strate-
	gy.

	You can get a lot of storage space with virtual  arrays  and
	avoid  overloading  the  root  area,  but  note that virtual
	arrays cannot be placed in a COMMON block, cannot be  mapped
	with  an  EQUIVALENCE  statement,  and  cannot  be  used  as
	subroutine parameters.  This makes them of limited use here.



	               Flow Diagrams and the Link Map

	It should be fairly obvious now that you will have to design
	your  program with much greater care.  A decent flow diagram
	becomes essential to  ensure  that  things  happen  as  they
	should.   In particular, make sure that you set up the dummy
	calls properly.  But don't worry about it:   you  will  soon
	find  out if you haven't!  You will also need to get used to
	reading the link map, if you aren't  already.   Go  for  the
	bits  you need - they will be fairly obvious, and ignore the

	                                                     Page 10



	great mass of information  about  the  OTS  internals.   The
	region  numbers,  the  partition  and  segment  numbers, the
	module sizes, and the data and variables present are  mainly
	what  you will need.  In the figure below the key parameters
	are in caps in the first segment, and  the  rest  have  been
	reduced to lower case.

	virtual overlay REGION	000001
	----------------------
	 
	partition	000001	SEGMENT 000001
	 $code1	 060002	000336 = 111.   words  (rw,i,lcl,rel,con)
				SUB11@	060002	SUB11X@	060254	
	 $pdata	 060340	000204 = 66.    words  (rw,d,lcl,rel,con)
	 $vars 	 060544	000034 = 14.    words  (rw,d,lcl,rel,con)
	 SEGMENT SIZE = 000576 = 191.   words
	 
	partition	000002	segment 000002
	 $code1	 060002	000336 = 111.   words  (rw,i,lcl,rel,con)
				sub12@	060002	sub12x@	060254	
	 $pdata	 060340	000204 = 66.    words  (rw,d,lcl,rel,con)
	 $vars 	 060544	000034 = 14.    words  (rw,d,lcl,rel,con)
	 segment size = 000576 = 191.   words
	 
	partition	000003	segment 000003
	 $code1	 060002	000132 = 45.    words  (rw,i,lcl,rel,con)
				sub13@	060002	
	 $pdata	 060134	000034 = 14.    words  (rw,d,lcl,rel,con)
	 $vars 	 060170	000010 = 4.     words  (rw,d,lcl,rel,con)
	 segment size = 000176 = 63.    words

	The flow diagram and the link map should also be checked for
	the  correct  storage of variables.  Make sure that they are
	all properly accessible and not hidden by  the  movement  of
	the  PARs.   This can be a bit time-consuming, but is essen-
	tial.

	It may happen that the  root  region  is  just  over  a  4kW
	boundary,  and you will be looking for some way of shaving a
	few words off it.  The compiler and linker conspire  to  put
	any reused OTS modules into the root, but this is not essen-
	tial.  If a particular OTS routine is  only  called  from  a
	couple  of  subroutines,  consider extracting the module and
	linking it into each of those regions.  You will have to use
	the  /D  linker  switch to make the linker behave:  for this
	you should read the manual.



	                       Documentation

	Building the program and doing the final link is  best  done
	under  a  COM file.  This not only gets it right every time,
	once you have got it right, but serves as a key  element  in
	the  overall  documentation.   It  will show what modules go
	where in a very clear and simple manner:  some  comments  in

	                                                     Page 11



	the file would not go astray either.

	Finally, consider the poor maintainer.  You have just creat-
	ed  a  complex  structure.   Unless you explain it on paper,
	no-one will understand it in a  month's  time.   This  means
	comments  in the code explaining why you have shuffled vari-
	ables in that manner, and what the funny useless  subroutine
	calls do;  it should also include an explanation of the gen-
	eral principal as well (a copy of this paper?).  Don't skimp
	on  the  details:  it is quite possible that the next person
	to have to work on the program will be  you,  and  you  will
	have forgotten the details yourself by then.



	                         Conclusion

	The Compiler and the Linker do excellent jobs, but are  con-
	strained in what they can achieve.  Despite the standard DEC
	warnings, it is possible to  reuse  overlay  regions  almost
	without  limit,  provided  you  take full responsibility for
	your actions.  This technique can allow some very large pro-
	grams  to  be  compiled  and  run under TSX+ and RT-11 which
	might otherwise have seemed impossible.

	The cost of this path is greatly increased care on the  part
	of the programmer when designing the program structure, when
	linking the modules, and in  storing  variables,  especially
	those  used  as  passed  parameters.   The  link map will be
	essential reading, along with a detailed flow chart  and  an
	understanding   of  what  routines  access  what  variables.
	Modifications to the program later will be particularly dif-
	ficult  if  you  have  not  documented  the structure of the
	program and how it fits in memory.

	Mention should be made of "swapping' in  the  TSX+  environ-
	ment.   This  OS allows increased use of the standard memory
	space relative to RT-11:  programs may have up  to  64kB  of
	space  if they need it, and they can go into memory-resident
	virtual overlays as well.  It would be  best  if  "swapping"
	was  disabled,  to  ensure  the  modules do stay in physical
	memory and don't get pushed out to the  swap  space  on  the
	disk.   The  danger  is  not  that  great:   the swapped-out
	regions are copied  back  in  when  needed,  with  variables
	retaining their values.

	On the other hand, if there are several users on the  system
	and  swapping  is  disabled,  there  can  be  a problem.  An
	extended memory program requires contigous memory space.  If
	the user is in one 64kB memory block and the next (physical)
	block is also in use, an extended memory program  cannot  be
	loaded  unless  TSX+ can temporarily swap the higher program
	out to disk to create the necessary contiguous memory.   The
	most  common  way  of  experiencing this with a non-swapping
	system is to create a virtual line or job, leave it running,
	and then try to run VTCOM.  The virtual job blocks the memo-

	                                                     Page 12



	ry extension request permanently.

	One solution to some of this is to  load  the  job  at  boot
	time,  via  the  START.TSX  routine or as a realtime program
	perhaps.  This is particularly useful if the program is some
	sort of system utility or data-logging/control program.


	                       Dr R N Caffin
	                    c/- DECUS Australia


	This paper was presented at the DECUS Australia 1989  Sympo-
	sium.








































	symp89