The C Language


                                  Martin Minow






        1.0  introduction              ____________

        This  memorandum  is  an introduction to, and justification for,
        the C programming language.  

        "C  is  a  general-purpose  programming  language.   It has been
        closely associated with the UNIX system, since it was  developed
        on  that  system, and since UNIX and its software are written in
        C.  The language, however, is not tied to any one operating sys-
        tem  or machine;  and although it has been called a "system pro-
        gramming language" because it is useful  for  writing  operating
        systems, it has been used equally well to write major numerical,
        text-processing, and database programs.  

        "C  is a relatively "low level" language.  This characterization
        is not perjorative;  it simply means that C deals with the  same
        sort  of  objects  that  most  computers  do, namely characters,
        numbers, and addresses.  These may be combined and  moved  about
        with the ususal arithmetic and logical operations implemented by
        actual machines.  

        "C  provides  no  operations to deal directly with composite ob-
        jects such as character strings, sets,  lists,  or  arrays  con-
        sidered  as  a  whole.   There is no analog, for example, of the
        PL/I operations which manipulate an entire array or string.  The
        language  does  not define any storage allocation facility other
        than static definition and the stack discipline provided by  the
        local  variables of functions:  there is no heap or garbage col-
        lection like that provided  by  Algol  68.   Finally,  C  itself
        provides no input-output facilities:  there are no READ or WRITE
        statements, and no wired-in file access methods.  All  of  these
        higher-level  mechanisms  must  be provided by explicitly-called
        functions.  

        "Similarly, C offers only straightforward, single-thread control
        flow constructions:  tests, loops,  grouping,  and  subprograms,
        but  not multiprogramming, parallel operations, synchronization,
        or coroutines.  

        "...  Keeping the language down to modest dimensions has brought
        real benefits.  Since C is relatively small, it can be described
        in  a  small space and learned quickly.  A compiler for C can be
        simple and compact.  Compilers are also easily  written;   using
        current  technology,  one can expect to prepare a compiler for a
        new machine in a couple of months, and to find that  80  percent
        of  the  code  of  a  new compiler is common with existing ones.
        This provides a high degree of language mobility." 


        The C Language                                Page 2



        From Kernighan and Ritchie, The C Programming Language.  


        2.0  background              __________

        C was developed at Bell Labs by Dennis Ritchie.  It was based on
        BCPL via the B language (a minimal language for system  program-
        ming).   The  language  has been available for about five years.
        Over 90% of the Unix operating system (and essentially all  UNIX
        applications software) is written in C.  

        The  language is available on PDP-11's (all major operating sys-
        tems, including PDT150's), VAX, GCOS (HIS 6070), OS 370,  Inter-
        data  8/32,  SEL86,  Nova,  Eclipse,  and  on  8080/86  and  Z80
        microcomputers.  On  PDP-11's,  the  compiler  generates  direct
        machine  code.  (The compiler, can be recompiled on an RT11 sys-
        tem).  There are at least three compiler vendors  along  with  a
        version available from Decus.  

        A C language standard was published in 1977.  While the language
        does not define  any  I/O  or  operating-system  conventions,  a
        "portable C library" has been defined to provide necessary func-
        tionality in a machine-independent fashion.  The  Decus  C  com-
        piler  supports  a  run-time  library  that  is portable between
        RSX11, RT11, and either operating system emulated under RSTS/E. 

        The  documentation  available includes a 150 page paperback book
        of excellent quality.  Unix documentation  includes  a  30  page
        reference manual describing the entire language.  

        This  discussion  was  prepared using the UNIX system documenta-
        tion, the discussion of C in the Bell Systems Technical  Journal
        (July-August 1978), and the book by Kernighan and Ritchie quoted
        above.  


        3.0  utilization       of      system/microprocessor             ___________       __      _____________________
             architecture              ____________

        The  language is completely machine-independent.  Operating sys-
        tem interaction is by (separately compiled) functions.  This in-
        cludes all I/O processing.  

        All  variables must be declared prior to use.  A variable may be
        declared "register" type.  If so, the compiler will  attempt  to
        use  hardware registers.  Registers (R0, SP, etc.) cannot be ex-
        plicitly named by C programs.   (It  is  possible,  however,  to
        equate  pointer variables to absolute memory locations, allowing
        C programs access to device registers.) 

        Assembly  language  cannot  be embedded in C programs.  However,
        separately compiled C  and  assembly-language  programs  can  be
        called.  All C programs are re-entrant and the "standard" PDP-11
        calling sequence  is  not  used.   However,  the  Decus  runtime

        The C Language                                Page 3



        library includes an interface subroutine to allow calling a For-
        tran library routine, should this be necessary.  This  allows  C
        programs  running  on  RT11 to access all operating system func-
        tionality.  The subroutine call/return sequence  requires  about
        20  microseconds on a PDP11/70.  C programs can be compiled with
        "profiling" support.  If this is selected, the Decus  C  runtime
        library includes tests for stack overflow and prints "traceback"
        messages if the program aborts.  

        By slightly extending the definition of pointer variables, it is
        possible to address any location in the machine (this is not ex-
        plicitly provided for in the language definition, and may not be
        completely transportable).  Thus, C  programs  can  be  used  as
        device drivers (all UNIX device drivers are written in C).  They
        can also be connected to interrupt vectors (again, not  provided
        for in the language standard).  


        4.0  language functionality              ________ _____________

        C  is  a  typed block-structured language.  All "normal" control
        constructs are included.  The compiler generates reentrant  code
        (reentrancy  is inherent in the language).  There is no language
        construct for coroutines.  

        One  of the most important features of the language is its abil-
        ity to define structures, and  to  manipulate  them  by  use  of
        pointer variables.  In addition, an increment/decrement operator
        is available which allows flexible indexing through a  structure
        or  vector.  Multi-dimensioned arrays are also available.  Also,
        variables may be partitioned into bit fields.  

        While  the  language is typed, it is possible to escape from the
        typing.  This is important when storage must be dynamically  al-
        located from free memory.  The system library contains a storage
        allocation subroutine which returns enough space  to  store  the
        item required.  The allocator is called as follows:  

                struct cell {           /* Define a lisp cell         */
                  struct cell *car;     /* car pointer                */
                  struct cell *cdr;     /* cdr pointer                */
                  int   valtype;        /* What is stored in the cell */
                  union cellval {       /* Cell can store any of:     */
                    int ival;           /* Integer or                 */
                    double rval;        /* Real or                    */
                    struct cell *vlist; /* Value list pointer or      */
                    char *cval;         /* Character string           */
                  } v;                  /* v.ival, etc.               */
                } *head;                /* Head points to a cell      */

                /*
                 * Allocate a cell and initialize it's contents
                 */
                head = (struct cell *)alloc(sizeof cell);

        The C Language                                Page 4



                head->valtype = INTEGER;
                head->v.ival = 123;
                /*
                 * Print value if a cell contains an integer
                 */
                if (head->valtype == INTEGER)
                        printf("%d", head->v.ival);

        The  above  sequence  defines  a  structure and an uninitialized
        pointer to that structure (at compile time).  When  the  program
        is  run,  space  for  the structure is allocated which is of the
        proper size and which is properly aligned  for  the  data  being
        stored.  

        Note  that "sizeof cell" is evaluated at compile-time.  The pro-
        gram body need not be modified if the structure changes,  or  if
        the  number  of  bytes needed to store address pointers or other
        storage units changes.  (This means that programs are transport-
        able  between  PDP11's  (with 16 bit address pointers) and Vax's
        (with 32 bit pointers).  The C "type  cast"  declaration  allows
        the computer to type-check the assignment statements.  

        The  following  example shows how bit fields and PDP-11 hardware
        registers may be defined and manipulated:  

                /*
                 * Define a KW11-P programmable counter
                 */
                struct {
                  struct {              /* Define control-status reg. */
                    unsigned run   : 1; /* Run bit                    */
                    unsigned rate  : 2; /* Rate select (2 bits)       */
                    unsigned mode  : 1; /* Mode                       */
                    unsigned updwn : 1; /* Up/down bit                */
                    unsigned fix   : 1; /* Fix bit (maintenence)      */
                    unsigned inten : 1; /* Interrupt enable           */
                    unsigned done  : 1; /* Device done                */
                                   : 7; /* Unused                     */
                    unsigned error : 1; /* Overrun                    */
                  } csr;                /* All packed in this word    */
                  int csb;              /* Count set buffer           */
                  int cnt;              /* Count                      */
                };

                #define KW11P 0172540   /* Programmable clock address */

                KW11P->csr.rate = 1;    /* Set rate to 10kHz.         */
                KW11P->csb = (-100);    /* Count set to 100 int/sec.  */
                KW11P->csr.run |= 1;    /* Start counting             */

        The  above  shows how device registers might be defined, and how
        the pointer mechanism may be used to access actual machine loca-
        tions.   This (nonstandard) use of pointer variables follows the
        actual coding practices used within the UNIX operating system.  

        The C Language                                Page 5




        Note,  of  course  that  interrupt  handling  would  require  an
        operating-system specific function.  


        5.0  c language characteristics              _ ________ _______________

        C  is  a  typed block-structured language many of whose concepts
        can be traced back to Algol-60.  


        5.1  c control structures              _ _______ __________


                if (<Expression>)
                                <Statement>;
                    else        <Statement>;

                while (<Expression>)
                    <Statement>;

                do <Statement>;
                    while (<Expression>);

                for (<Expression>; <Expression>; <Expression>)
                    <Statement>;

                switch (<Expression>)
                    <Statement>;

                case <Constant Expression>:
                    <Statement>;

                default:

                break;

                continue;

                goto <Label>;

        Wherever <Statement> appears, a multi-statement block may be in-
        cluded.  

        The  switch  statement is used to select which of several state-
        ments (prefaced by case statements)  is  to  be  executed.   The
        default  statement  is  executed if none of the cases are satis-
        fied.  Break exits  the  including  for/while/switch  statement.
        Continue  jumps  to  the  terminating condition of the for/while
        statement.  

        For statements are completely general:  the initial value, test,
        and increment need not be related.  The goto statement is seldom
        needed, and may not exit from (or jump into) a function.  

        The C Language                                Page 6



        5.2  c operators              _ _________

        C  contains  a  rich set of operators, including definitions for
        modulus and arithmetic shifts.  

        One  of the most unique features of C is the increment/decrement
        operator (quite similar to the  PDP11  hardware  functionality).
        For example:  

                x = a++;        /* is equivalent to x = a; a = a + 1; */
                x = ++a;        /* is equivalent to a = a + 1; x = a; */
                x = a--;        /* is equivalent to x = a; a = a - 1; */
                x = --a;        /* is equivalent to a = a - 1; x = a; */

        The increment/decrement operator can be combined with pointers: 

                char x;         /* x is a character                   */
                char *a;        /* a points to a character            */

                x = *a;         /* x is set to what a points to       */
                x = *a++;       /* x is set to what a points to,      */
                                /* and a points to the next character */

                int stlen(s)            /* String length subroutine   */
                register char *s;       /* Pointer to a string        */
                {
                        register int i; /* i gets string length       */

                        for (i = 0; *s++ != NULL; i++);
                        return(i);
                }

                /*
                 * A slightly more efficient string length subroutine is
                 */
                int strlen(s)           /* String length subroutine   */
                register char *s;       /* Pointer to a string        */
                {
                        register char *work;

                        work = s;
                        while (*work)
                                work++;
                        return(work - s);
                }


        Compound expressions (in the Algol 60 sense) are available:  

                printf((s == 1)
                                ? "%d second"
                                : "%d seconds",
                        s);


        The C Language                                Page 7



        prints either "1 second" or "<number> seconds".  

        C is unique in distinguishing between logical and/or (which con-
        trol execution flow) and  arithmetic  and/or  (which  compute  a
        value).   The  compiler  guarantees  left-to-right evaluation of
        logical expressions.  Thus, an if statement can compute a  value
        based on a test which is part of the expression.  

        Object    code    efficiency    is    reasonable   compared   to
        assembly-language.  It is probably good enough  that  individual
        differences  among  programmers will be more important than com-
        piler efficiency.  It is rumoured that PDP-11 C is about 95%  as
        efficient as PDP-11 Bliss.  


        5.3  compile-time capabilities              ____________ ____________

        Compile time capabilities include parameter definition, file in-
        clusion, conditional compilation, and a simple  macro  facility.
        (The  UNIX  philosophy is to provide more sophisticated tools as
        separate packages, rather than by extending  each  language  and
        utility  separately.)  One compile-time operation that should be
        noted is the "sizeof" function which is defined as the number of
        bytes  needed  to  store  its object.  This allows much code in-
        dependence and transportability of C programs.  

        The  Decus  compiler defines symbols that allow the C program to
        be conditionally compiled for RSX or RT11 run-time  characteris-
        tics.   While  this  is not normally needed for application pro-
        grams, several systems programs  (for  example,  those  used  to
        debug the library) require this knowledge.  The run-time library
        also includes global symbol definitions that allow  the  running
        program  to determine which operating system it is running under
        (for example, if it is running on native RT11 or  RT11  emulated
        by RSTS/E).  

        The  Decus  C compiler generates object code that is compatibile
        with the standard operating system linker (task-builder)  It  is
        possible   to   declare   global  variables  and  build  overlay
        libraries.  Note, however, that the "standard" PDP11 calling se-
        quence  (parameter  list  pointed  to  by  R5) is not used.  The
        library contains a very small subroutine to mediate between cal-
        ling sequence conventions thus allowing C programs access to Dec
        library routines.  By use of this subroutine, C programs running
        under  RT11  can  use the standard system library to perform all
        RT11 functions.  

        The  compiler  does  not  produce  listings,  symbol  tables, or
        cross-reference listings.  It is the UNIX  attitude  that  these
        are not needed in an interactive structured-programming environ-
        ment,  and,  where  needed,  are   better   provided   by   more
        sophisticated  tools (such as key-word in context utilities).  A
        cross-reference generator is included with the  Decus  compiler.
        Various  kinds of C debuggers are available under UNIX.  ODT/DDT

        The C Language                                Page 8



        can be used with the Decus compiler.  

        Unfortunately,  the  Decus  compiler  does  not  support several
        features of the language.  It omits floating-point,  bit-fields,
        macros  with arguments and certain kinds of conditional compila-
        tion.  Also, all EIS instructions (multiply, divide, and  shift)
        are done by subroutine calls.  


        6.0  transportability issues              ________________ ______

        Bell Laboratories has developed a "Portable C compiler" which is
        operational on several machines, ranging from System/370 (OS and
        TSS)  to PDP-11's and Nova's.  "Versions are in progress for the
        Intel 8086 and other machines." 

        One  vendor,  Whitesmith's, Ltd., offers compilers for PDP-11's,
        VAX/VMS, 8080, and Z80 computers.  The Whitesmith's package  in-
        cludes   a   "portable   C   library"   implementing   over  100
        system-specific functions.  

        The  Decus compiler runs on all PDP11's including Vax (in compa-
        tibility mode).  The RT11 runtime library allows  compiled  pro-
        grams  (save  images)  to  be moved between RSTS/E emulation and
        native RT11 without relinking.  (This is currently not the  case
        with Fortran IV.) 

        The   C   language   does   not   define  an  I/O  interface  or
        operating-system functionality, such as process synchronization,
        parallel  operation, or process control.  All such functionality
        is provided by (separately compiled) subroutines.  

        This  is  similar in intent to the Fortran ISA extensions avail-
        able on DEC computers.  It is the designer's belief that "making
        these  operations  primitives  of the language is inappropriate,
        mostly because language design is hard enough in itself  without
        incorporating into it the design of operating systems.  Language
        facilities of this sort tend to make  strong  assumptions  about
        the  underlying operating system that may match very poorly what
        it actually does." 

        The  Decus  distribution  includes  RSTS/E and RSX11-M interface
        libraries allowing C programs  full  access  to  the  underlying
        operating  system  functionality.   RT11  operating system func-
        tionality is available by calling  the  "syslib"  library  func-
        tions.  

        The  syntax/semantics  of the language cannot be dynamically ex-
        tended  (as  could   MAD).    However,   a   large   number   of
        special-purpose compilers have been written (in minimal time) by
        writing lexical recognizers that generate C output code.  (There
        is   a   Pascal  to  C  translator,  as  well  as  a  number  of
        data-manipulation languages that operate in this fashion.) 


        The C Language                                Page 9



        Compilers  have  also  been  written (e.g.  for Fortran 77) that
        have a one-pass recognizer that generates an  intermediate  form
        (expression  tree)  identical  to that of the C compiler.  The C
        compiler's code generator may then used to output code from  ei-
        ther language.  


        7.0  support/usability issues              _________________ ______

        The  C language has proven to be an extremely effective tool for
        systems programmers.  "Since C is a relatively  low-level  lang-
        uage,  it is adequately efficient to prevent people from resort-
        ing to assembler, and yet  sufficienctly  terse  and  expressive
        that its users prefer it to PL/1 or other very large languages. 

        "A  language  that doesn't have everything is actually easier to
        program in than some that do.  The limitations of C often  imply
        shorter manuals and easier training and adaptation." 

        Support  for  the  Whitesmith's  product  is  available from the
        vendor.  The primary tutorial is an  excellent  paperback  book,
        written  by  the  language's  designer.  It is, according to the
        Whitesmiths' product specification, an accurate  description  of
        their compiler.  I have not verified this.  

        My  own  experience suggests that programmers learn the language
        in a short time (even without the excellent book).  It  is  very
        easy  to  write  maintainable, reliable, transportable programs.
        (Because C is a low-level language,  maintainable  programs  re-
        quire  that  the programmer take the trouble to include adequate
        documentation.) The Decus library has proven to be  quite  tran-
        sportable between RT11, RSTS/E, RSX11-M, and VMS.