SPECIFICATIONS FOR THE RT-11/TSX-PLUS SERIAL PORT I/O HANDLER (IO.SYS).
  -----------------------------------------------------------------------

			      R. D. BROWNRIGG

ABSTRACT:  A new device handler for the RT-11 and TSX-PLUS operating systems
	   is described.  This handler provides full-duplex input and output
	   to several serial interface ports simultaneously.  Installation
	   instructions and information necessary to communicate with the
	   handler using the MACRO assembly language are detailed.


1.  INTRODUCTION.

The IO handler allows programs to communicate with serial ports under the
RT-11 or TSX-PLUS operating systems.  This may be done either in an output
only manner or by using a two-way communication, in which both output and
input may be achieved concurrently to and from the same port.  Further, the
handler is capable of performing output or I/O to several ports
simultaneously.

This report firstly describes how to install the handler in an RT-11 or
TSX-Plus system, then describes the two means of communicating with the
handler.



2. INSTALLATION REQUIREMENTS.

Before the IO handler can be installed in a user's system, it must be
tailored to suit the hardware available. Further, there are some operating
system considerations which will influence just which hardware can be
considered 'available'.


2.1 Operating System Considerations.

The main operating system consideration to affect the installation of the
IO handler arises from possible conflicts with other handlers designed to
communicate with serial interface I/O ports on the system. For example, if
one wishes to retain the LS (serial printer) handler, a conflict may arise
if the IO handler is configured to communicate with the particular port
assigned to the LS handler. Under the TSX-Plus operating system it is not
possible to have two different handlers accessing the same hardware
interface. This is because all handlers under TSX-Plus are permanently
LOADed, or resident in memory, with their interrupt vectors set up, and
there is no LOAD command, which could modify the interrupt vector for the
device. Under the RT-11 monitors, however, it is usually the case that a
handler is LOADed only when it is required, and therefore it is possible to
have more than one handler capable of accessing a particular device.

Another consideration affecting installation under TSX-Plus is that it is
not possible to use the IO handler to access terminal ports, those serial
interface I/O ports which have been assigned line definitions during the
TSX-Plus SYSGEN process. This is also because the interrupt vectors for the
terminals are set up once and for all when TSX-Plus first starts up.
Finally, there is a difficulty under TSX-Plus if one of the IO ports is
used for a spooled device, such as a serial printer. This configuration
will work in general, the difficulty being that the port being used for
spooling cannot be used as an I/O port. Thus normal .WRITE programmed
requests will behave as expected and be spooled by the operating system,
but .SPFUN programmed requests will not be handled correctly, and are
likely to crash the operating system.


				- 2 -


2.2 Installation Procedure.

Given that a decision has been made as to which serial interface I/O ports
are to be accessible via the IO handler, it remains to modify the handler
to reflect this decision, and then install the handler as part of the
operating system.

There are several parts of the IO handler which may need modifying if an
unusual combination of ports is required to be accessible to the handler.
The most straightforward setup is to specify as being accessible a number
of consecutive ports, starting with the lowest vectored non-console port,
this involving the least amount of modification to the handler. However it
is possible to specify non-consecutive ports, and in any order if desired.
Items within the handler which may need modification in this situation are
the constant specifying the number of ports, the base CSR and vector
addresses, the vector addresses in the vector table, and the register
addresses in the local port tables.

The number of ports accessible to the handler is specified by the constant
PORTS, which must be at least 1 and no greater than 8. The base CSR and
vector addresses are defined by the constants IO$CSR and IO$VEC which by
default are set to octal 176500 and octal 300 respectively. The vector
table is used to associate vectors with their corresponding processor
status values for the single interrupt entry point. The input and output
vectors are specified for each port, in the order in which it is desired to
define them. This then sets up a correspondence between the physical ports
and the handler's unit numbers, the first set of vectors defining port 0,
IO0:, the second set defining port 1, IO1:, and so on. By default the
vectors are defined consecutively from IO$VEC. Finally the local port
tables must also be set up to reflect this same order of port definition.
For each port, the local port table contains one word, initially zero, to
hold the current queue element address, four words which specify the four
register addresses for the port and four words for further port
information. The four register addresses must be set up for each port
required, and the groups of four addresses must appear in the same order as
the corresponding vectors in the vector table. The MACRO source file IO.MAC
has been set up with conditionals so that if the first N ports are to be
accessible to the IO handler, then all the user has to do to select these
ports is to set the constant PORTS to the value N.

Further constants which must be set by the user are the constants TSX and
XM, which set the handler up specially for the TSX-Plus operating system or
the RT-11 XM monitor respectively. If the TSX constant is set to 1 then the
handler's memory management configuration is set up for the TSX-Plus
operating system (irrespective of the setting of the XM constant).
Otherwise if the TSX constant is set to 0, then the XM constant determines
if the handler is configured for the RT-11 SJ and FB monitors (XM = 0) or
the RT-11 XM monitor (XM = 1).


				- 3 -


3.  STANDARD OUTPUT.

The .WRIT(C, E, or W) request behaves in the normal RT-11 manner except that
several .WRIT(C or E) requests to different ports will result in concurrent
output to those ports.

In PASCAL for example, use:

	rewrite(f, 'io3:');	{open port 3 (CSR=176530) for output}
	write(f, data);

In MACRO for example, use the sequence:

	.FETCH	loadaddr, devicename	; if handler not already LOADed.
	.LOOKUP	emtarea, channo, devname
	.WRITC	emtarea, channo, buffaddr, wordcnt, comproutine, blockno

Note that the device name io: is the same as io0:, referring to port zero,
which is usually associated with VECTOR=300 and CSR=176500.


4.  SETTING UP A TWO-WAY COMMUNICATION.

Two-way communication is achieved with the .SPFUN programmed request which
sets up a communication between the handler and the user via a buffer
communication area.  As with standard output, a number of ports may be
active simultaneously.  The MACRO sequence to set up this communication is
as follows:

	.FETCH	loadaddr, devicename	; if handler not already LOADed.
	.LOOKUP	emtarea, channo, devname
	.SPFUN	emtarea, channo, #200, buffaddr, wordcnt, blockno, comproutine

Thereafter all I/O is achieved by the user reading from and writing to the
input and output ring buffers within the main buffer, while manipulating the
appropriate buffer pointers in the buffer communication area.


5.  STRUCTURE OF THE BUFFER.

The buffer referenced by the .SPFUN programmed request to the handler acts
as an interface between the user and the handler.  This buffer may be of any
length up to 20000 bytes (8kB) residing wholly within the user's program.

The first part of the buffer is a communication area which contains various
pointers used by both the handler and the user.  Some of these pointers
point into the user's address space and others point into the handler's
address space (using kernel mode mapping).  The next part of the buffer is
an output ring buffer of a size specified by the user.  The handler
determines this size from the value supplied by the user.  The last part of
the buffer is an input ring buffer of a size similarly specified by the user
and determined by the handler, but not necessarily the same size as the
output ring buffer.  Detail of the buffer contents is shown below:


				- 4 -


offset			data			set by:	   modified by:
      _______________________________________
0     | OG.PTR  next byte from output buf.  |	handler	   handler
      |-------------------------------------|
2     | OP.PTR  next byte to output buffer  |	user	   user
      |-------------------------------------|
4     | A.DIFF  addressing difference	    |   handler	   (read by both)
      |-------------------------------------|
6     | O.BUFL  length of output buffer	    |   user	   (read by handler)
      |-------------------------------------|
10    | O.FULL  output buffer full (byte)   |   user	   reset by handler
11    | O.STAT  output line status (byte)   |   either	   reset by handler
      |-------------------------------------|
12    | IG.PTR  next byte from input buffer |   user	   user
      |-------------------------------------|
14    | IP.PTR  next byte to input buffer   |   handler	   handler
      |-------------------------------------|
16    | I.BUFL  length of input buffer	    |   user	   (read by handler)
      |-------------------------------------|
20    | I.GRN   input length for X-ON	    |   user	   (read by handler)
      |-------------------------------------|
22    | I.RED   input length for X-OFF	    |   user	   (read by handler)
      |-------------------------------------|
24    | I.FULL  input buffer full (byte)    |   handler	   reset by user
25    | I.EXIT  the user is finished (byte) |   either	   (read by handler)
      |-------------------------------------|
26    | I.RESP  respond to X-OFF/X-ON (byte)|   user	   (read by handler)
27    | SPARE			      (byte)|	 -		-
      |-------------------------------------|
30    | I.RBO   # input ring buffer o'flows |   handler	   reset by user
      |-------------------------------------|
32    | I.OVR   # DL11 overrun errors	    |   handler	   reset by user
      |-------------------------------------|
34    | I.FRA   # DL11 frame errors	    |   handler	   reset by user
      |-------------------------------------|
36    | I.PAR   # DL11 parity errors	    |   handler	   reset by user
      |-------------------------------------|
      |					    |
40    | output buffer of length O.BUFL	    |
      |					    |
      |-------------------------------------|
      |					    |
40+   | input buffer of length I.BUFL	    |
O.BUFL|					    |
      |					    |      _______________________________________


NOTES:
	1) If I.RED is zero, then no X-OFF characters are sent by the
	handler when the user buffer becomes full.

	2) Under SJ and FB monitors, A.DIFF will be zero, otherwise the user
	must add A.DIFF to the user's address to arrive at the corresponding
	handler's address.

	3) If IG.PTR is equal to IP.PTR (taking A.DIFF into account), then
	either the buffer is empty, or it is full.  In the latter case,
	I.FULL will be non-zero.


				- 5 -


6.  EXITING FROM A TWO-WAY COMMUNICATION.

To terminate the two-way communication, the byte I.EXIT within the user's
buffer must be set by the user.  If this is not done, then any .EXIT request
will hang, waiting for the I/O to complete.  The MACRO sequence to achieve
this is as follows:

	INCB	I.EXIT
	.WAIT	channo
	.EXIT


7.  ERROR RETURNS.

The completion routine versions of the .WRITEC or .SPFUN request are
recommended since the handler may return from the request immediately if the
port is not available.  The Channel Status Word reflects the error, with the
EOF bit always set if an error has occurred.  The HDERR bit is set if the
error was that the port was already in use by a different job or for a
different function.  If the HDERR bit is not set, this indicates that the
error is a buffer overflow (buffer larger than 8Kb, in XM or TSX-PLUS
systems only).