Programs for testing the speed of CPUs                   Page 1
B. Z. Lederman


                             NOTE

     This  is  a  reduced  version of my original article:
     the original is rather long, and I  thought  that  it
     might  be unwieldy for people to download it over 300
     or 1200 baud lines, especially considering the cost. 



     With  the  introduction of the PDP-11/84, it was suggested
that applications could be moved from 11/70s, but  some  method
of  verifying the speed of the 11/84 was desired and there were
no  published  instruction  times.   I  therefore  wrote   some
programs  which  will  measure  the  speed  at which a CPU will
execute instructions with reasonable accuracy.  

     The method I use is quite simple:  a single instruction is
executed  many  times  (generally  a   minimum   of   1,000,000
executions),  and the time this takes is measured.  Because the
largest single program segment on  a  PDP-11  is  about  32,000
words,  it  is  necessary  to  use  a loop:  a long sequence of
instructions is repeated as many times as  needed  to  get  the
total number of executions wanted.  There is also the effect of
cache:  a short loop will fit  entirely  into  cache  and  will
execute  at the fastest possible speed;  a longer loop will not
all fit into cache, and the effect of the speed of main  memory
can  be  seen.   Finally,  it is necessary to test the speed of
many different instructions (one at a time) to get an  adequate
profile of a given CPU's performance.  

     The   program   S1D.MAC  implements  this  type  of  test.
Although I  have  tried  to  make  it  as  straight-forward  as
possible,  it  should  be  remembered  that this is basically a
diagnostic program,  and  that  it  does  some  things  that  I
normally wouldn't allow in a production program:  specifically,
it treats instruction space as  data,  is  self-modifying,  and
there  are two tables which must be kept in alignment manually.
Sometimes this sort of  thing  is  necessary  in  a  diagnostic
program.   While  modifications  would  be  fairly  easy  for a
programmer with some experience, I  don't  suggest  making  any
changes  unless  you  are  fairly  certain you know what to do.
(The program is not privileged, however, so the worst that  can
happen is the program will abort:  it won't crash your system.) 

     There  are  two  global  equates  at  the beginning of the
program:  $NREP is set to the number of instructions wanted  in
the  loop,  and  $NPAS  is  the  number  of  times  the loop is
executed.  Any combination which will multiply to a large  even
number  will  do, such as 1,000 and 1,000;  3125 and 320;  2500
and 400, or any other suitable combination.  Having the numbers
multiply  out  to  1,000,000  or  10,000,000  isn't  absolutely


Programs for testing the speed of CPUs                   Page 2
B. Z. Lederman


necessary, but it makes it easier to read out  the  times:   at
1,000,000  repetitions  the  time  measured  in  seconds is the
instruction time in micro-seconds.  Because  the  loop  has  to
have  3  instructions  to  form the loop repeat logic, there is
another global called $NREAL which is $NREP minus 3.   As  long
as the loop is reasonably long (several hundred instructions or
more) the effect  of  the  loop  repeat  instructions  will  be
negligible.   I considered making them task build time options,
but it would have made the program far too complicated.   Don't
be  surprised  if  the program takes more time to assemble when
$NREP is large, as it takes more time to fill the ISTRT area.  

     There  are  two tables which must match:  the first starts
at MNTAB, and is a list of mnemonics which print out  when  you
run  the  program to tell you what instruction is being tested.
This must match the set of instructions starting  at  TABLE  if
you  want  to  know  what  is  going on.  The instructions were
placed in their present order after running  the  program  many
times  so  the data comes out in what I feel is the most useful
form, though the instructions could be in any  order.   All  of
the  instructions  are position independent, as they have to be
moved by the program into the execution  area:   testing  other
addressing  modes would be difficult as the addresses would all
have to be adjusted, and I don't believe that  the  information
obtained  would  significantly  improve the comparisons between
machines.  In this program, all instructions are one word long:
another  program  called  S2D.MAC  is identical except that two
word  instructions  are  tested  (actually  instructions   with
addressing  modes  that cause the instruction to be followed by
one word of address information or literal data), and similarly
for  S3D.MAC  which tests three word instructions.  Using three
separate programs makes things very much easier  (for  me,  the
programmer).   There  are also a few special cases:  the BRanch
instructions are set to always branch to the next  instruction,
which  allows  them to be tested even though they are relocated
within the program.  They have been selected so that  one  will
always  branch  and  the  other  will  never  branch:   on many
machines there will be a  difference  in  execution  speed  for
these  two  conditions.   The other special case is the Jump to
SubRoutine instruction:  for this to be tested there must be  a
RETurn  from  Subroutine  instruction  (which  is  in  a  fixed
location), and  the  time  of  execution  really  is  for  both
instructions  together.  As most subroutines end with a return,
this should be a valid test as long as one remembers  that  the
times  obtained  are  for  two instructions.  The data which is
used in the  instructions  is  either  absolute  references  or
loaded  into  registers:   the data for the multiply and divide
instructions may  not  be  the  best  possible  test  of  these
instructions,   but   it   does   work.    Auto-increment   and
auto-decrement addressing modes are difficult to  test  as  the
loop   is   at  least  1,000,000  instructions  long,  and  any


Programs for testing the speed of CPUs                   Page 3
B. Z. Lederman


continuous test would  push  the  register  out  of  addressing
range:   the  only  solution  I  could see was to have the same
instruction do a decrement and increment together, so only  two
addressing  locations  are  used;   this  may  be  seen  in the
MOV -(SP), (SP)+ test.  

     It  should  be  noted that these programs include floating
point processor instructions:   though  it  would  be  easy  to
include  an  assembly  condition  to  include  these  only when
wanted, I haven't been able to get around to  doing  that  yet.
Persons  wishing  to  test machines which don't have FPP should
conditionalize or comment out the FPP instructions:  this would
also  apply  to anyone who does not have EIS instructions (MUL,
DIV,  etc.).   These  programs  do  not   test   FIS   or   CIS
instructions,  because  none  of  the  machines to which I have
access have these instructions.  

     In  the  main  body of the program there is space reserved
beginning at ISTRT:  this is initially filled with  No  OPerate
instructions,  and the program fills this space with one of the
instructions from the TABLE in order  to  test  it's  execution
time.   The  system  directive  GTIM$  (Get  Time) is used just
before the start of the loop and just after the loop to see how
long  it  took:   as  system  time  is  delivered in 0.1 second
intervals, it is necessary to make the test loop long enough to
use  more  time  than  this value.  The fastest 11/70 and 11/84
instructions  are  about  0.3  micro-seconds  long,  so  if   a
1,000,000  instruction  loop  is  used,  the measured times are
about  0.3  seconds,  only  a  little  above  the   measurement
granularity.    Though   this  is  enough  for  an  approximate
comparison, running a 10,000,000 instruction  test  brings  the
shortest  times  up  to  about  3.0 seconds, and gives one more
significant digit of data.   Running  tests  longer  than  this
should  not  be  necessary.   For  slower machines (such as the
PRO-350 and 11/23), 10,000,000 instruction loops are nice but a
little  slow,  and  1,000,000  instruction  loops  are probably
adequate if you don't have much test time available.  

     The  use of the system directive to measure time brings up
several important factors in running these tests, of which  the
first  is  the  amount  of  time it takes to execute the GETIM$
directive.  I measured this on our 11/70 by  having  a  program
issue  several GETIM$ directives sequentially and measuring the
time each directive took to execute with SPM-11:  this  package
from  DEC hooks into the executive and measures time in 0.00001
second intervals (100,000 per second).  The GETIM$  took  about
0.0005 seconds (500 micro-seconds) to execute, which is so much
less than the minimum resolution of 0.1 second that it  can  be
ignored  if  the  loop  is long enough to register at least 0.1
seconds.  A related point is that  when  the  test  program  is
running,  it  should be the only program running, and at a high


Programs for testing the speed of CPUs                   Page 4
B. Z. Lederman


enough priority that it  will  "grab"  the  CPU  more  or  less
exclusively  (the  CPU  will  still  have to service the system
clock if you want the test times).  I have  run  the  tests  on
otherwise  idle  systems, and at a priority of 151 or 152 which
is high enough to be above just about everything except MCR:  I
want  the  test  to  be  below  MCR in case I want to abort it.
While this might make the instructions test a little  slow,  it
is  still  a  valid  comparison between different machines, and
when I  have  compared  the  test  results  obtained  with  the
published  instruction times in the processor handbooks, I have
obtained quite good correlations, indicating that  the  program
is  testing  accurately.   Under these conditions, it should be
possible to run the test either on RSX-11M-Plus, or P/OS (as  I
did),  or  RSX-11M,  or  possibly  on  RSX-11S and obtain valid
results.  The basic program would probably also run on IAS, but
it might be necessary to change the calls to the system library
that format the output messages and the QIOs if  they  are  not
the  same  on IAS.  I've never tried the RSX run-time system on
RSTS/E.  

     I  have  only  been  able  to test 3 machines:  the 11/70,
11/84P and PRO-350.  One of the reasons I am  publishing  these
programs  and  the  results,  and  placed these programs on the
DECUS RSX SIG tape, is the hope that  other  users  with  other
machines  will run the programs and publish the results, so the
user community will have additional data with which comparisons
between  models  of  PDP-11s  may  be  made when choosing a new
system or contemplating an upgrade path.  Also, by testing more
machines,  it  will  be  possible to compare the times with the
published  speeds  in  the  processor  handbooks,  and   obtain
additional  verification  that the speed tests are accurate (or
not, though I have reasonable evidence now that the  tests  are
correct).   I would be very interested in seeing the results of
tests on other CPUs, or suggestions on other instructions which
might be added to the test set.  

     I have also started on a version which will run on the VAX
family of machines but so far the results are rather  variable,
due to my not having "stand-alone" time on the machine, and the
effects of paging, caching, crossing page boundaries, etc.  

     The  following  are  some of the results of timing tests I
have done on several PDP-11 family CPUs, and have been arranged
to  show  the effects of addressing modes.  The category "Basic
Instructions" includes the  TeST,  ROtate  Right,  SWAp  Bytes,
MOVe,  MOVe  Byte, CoMPare, ADD, and BIt Test instructions, all
of which can normally be expected to execute at the same  speed
when  operating  on  registers,  and  did  in fact do so in the
tests.  SWAp Bytes is also used again in one of the  addressing
mode  tests:   in  these  tests  "addr"  is  a symbolic address
reference:  when there are two references to "addr" in the same


PDP-11 CPU instruction timing tests                      Page 5
B. Z. Lederman


instruction they are to two different locations in memory.  The
Branch EQual and Branch Not Equal instructions are used to show
the difference in speed when the branch is taken and when it is
not taken (on some machines these two times differ,  on  others
they  don't):   all other branch instructions should execute at
the same speed under the same circumstances.   Another  special
case is the Jump to SubRoutine instruction:  this also includes
the time for the ReTurn from Subroutine instruction, and so  is
the   time   needed  to  execute  two  instructions.   This  is
reasonable,  as  most  subroutines  conclude   with   the   RTS
instruction.  

     The  reference  to  "Short" and "Long" is to the length of
the instruction sequence:  a short sequence should fit entirely
into  cache  and give the fastest possible CPU times.  The long
sequence does not fit into cache, and shows the effect of  main
memory speed.  All times are converted to micro-seconds.  

                      11/70   11/70  11/84  11/84    PRO-
    Instruction       Short   Long   Short   Long     350

Basic Instructions     0.31   0.91    0.3    0.7     2.38

TST     (R0)           0.76   1.36    0.7    1.3     4.20
CMP     (R0), (R3)     1.06   1.67    1.6    2.1     6.11
MOV    -(SP), (SP)+    1.70   2.55    2.1    2.7     6.50
MOVB   -(SP), (SP)+    2.00   2.86    2.1    2.7     6.51
MUL       R1, R0       3.19   3.81    5.7    6.5    26.64
DIV       R1, R0       1.98   2.59    9.3   10.2     8.96
BEQ     addr           0.31   0.90                   2.38
BNE     addr           0.61   1.21                   2.38
CCC, NOP               0.61   1.21    0.8    1.25    3.23

MOV       #1, R0       0.77   1.95    0.6    1.5     4.07
ASHC      #1, R0       1.38   2.56    2.1    3.1    11.92
MOV   @#addr, R1       1.67   2.42    1.1    2.0     5.49
TST   @#addr           1.67   2.42    1.1    2.0     5.49
SWAB  @#addr           2.03   3.66    1.9    2.9     6.78
MOV     addr, R1       1.43   2.27    1.4    2.3     6.07
TST    2(R0)           1.51   2.26    1.3    2.2     6.11
TST     addr           1.48   2.27    1.3    2.3     6.10
MOV    2(R0), (R3)     1.87   3.52    2.3    3.4     8.12
JSR       PC, (R2)     3.06   3.68                   9.03
JSR       PC, @#addr   3.80   4.63                  10.25



PDP-11 CPU instruction timing tests                      Page 6
B. Z. Lederman


MOV       #1, @#addr   2.04   4.08    1.9    3.2     7.34
MOV   @#addr, @#addr   2.76   4.54    2.4    3.7     8.96
MOV    4(R0), 2(R3)    2.62   4.44    3.0    4.3     9.68
ADD       #1, @#addr   3.02   4.34    2.1    3.5     8.39
ADD   @#addr, @#addr   2.81   4.84    2.7    4.0    10.10
ADD    4(R0), 2(R3)    2.68   4.75    3.2    4.5    10.73

SETF                   1.22   1.83    1.6    2.0     6.14
MULF     AC2, AC0      2.57   2.68   15.4   16.3    61.35
ADDF     AC0, AC1      2.72   2.81   14.3   15.3    72.78
NEGF     AC0           1.22   1.83    4.8    5.4    15.83
ABSF     AC0           1.22   1.83    5.2    5.9    15.99
LDF       R0, AC0      1.22   1.82                  11.47
LDF     (R3), AC0      1.97   2.60                  14.67
LDCIF     R0, AC0      2.27   2.37                  29.14
LDCIF   (R3), AC0      2.27   2.59                  20.47
STCFI    AC0,  R0      2.73   3.36                  36.00
STCFI    AC0, (R3)     3.36   4.17                  37.59

SETD                   1.22   1.82    1.6    2.1     6.13
MULD     AC2, AC0      3.94   4.01   44.4   46.4   215.44
ADDD     AC0, AC1      2.72   2.83   19.2   20.4    98.83
NEGD     AC0           1.22   1.82    5.9    6.5    19.32
ABSD     AC0           1.22   1.82    6.2    7.0    19.29

LDF       #1, AC0      1.81   2.88    3.4    4.4    14.29
LDF   @#addr, AC2      2.72   3.49                  16.06
STF      AC0, @#addr   4.22   5.26    4.0    5.1    11.80
CMPF  @#addr, AC0      2.89   3.49    5.7    6.9    30.40
LDCIF     #1, AC0      2.61   2.89                  42.01
LDCIF @#addr, AC0      2.44   3.18                  25.20
STCFI    AC0, @#addr   3.41   4.89    9.9   11.1    38.24

     The   results   of  these  tests  need  to  be  considered
carefully.  First, I had a limited amount of time on the 11/84,
and  ran the shortest tests:  it would be desirable to run them
again to obtain the same precision as for the 11/70 and PRO-350
tests.   The  times  for  the  MULtiply and DIVide instructions
don't always match the  processor  handbook  values:   this  is
probably  because the data values used are special cases, and a
divide by one is faster on  some  machines  than  a  divide  by
another  number.   The  values  for  the  short loop, where the
entire loop is in cache,  do  match  very  well  the  published
values in the 11/70 processor handbook.  

     It  is  apparent,  however, that the 11/84 certainly comes
very close to the speed  of  an  11/70.   For  some  addressing
modes,  the  11/84  is  faster:  when this is combined with the
larger cache, the net effect is that some other  test  programs
actually  ran  significantly  faster  on  the 11/84 than on the
11/70.  The two cases where the 11/84 is obviously  slower  are


PDP-11 CPU instruction timing tests                      Page 7
B. Z. Lederman


arithmetic  instructions  (MUL,  DIV,  ASHC) where the 11/84 is
slightly slower, and with floating  point  instructions,  where
the  11/84  is  considerably  slower.  How much this affects an
application depends upon how many floating  point  instructions
are  executed:   even  a  program with floating point variables
generally has a relatively low percentage of the total  program
executing  actual  floating  point arithmetic.  A program which
did use floating point heavily (large  matrix  inversion,  fast
Fourier  transforms,  network  analysis, and similar scientific
and engineering applications) would see a reduction in speed on
an 11/84.  

     The  story  does not end here, however.  DEC has announced
an upgraded 11/84A, whose processor  is  supposed  to  run  20%
faster  than  the  machine  I tested, so all of the instruction
times given above can probably be reduced by 20%:   this  would
make  the  11/84 faster than the 11/70 in nearly all instances.
This  machine  will   also   accommodate   a   floating   point
co-processor,   which   is   said  to  execute  floating  point
instructions 5 to 8 times faster than the J-11 CPU:  this would
narrow  or  eliminate  the gap between 11/70 and 11/84 floating
point performance.  

     The times for the PRO-350 are close to but slightly slower
than the times published for an  11/23,  which  uses  the  same
processor.   The  PRO-350  CPU  has  to  do  extra work such as
updating the video screen and keeping the system clock working,
which may account for the difference.  


                  The Effect of Cache Memory.

     Both  the  11/70  and  the  11/84 have cache memory:  this
means that the speed at which instructions will execute depends
upon  the  CPU  having to fetch the instruction from fast cache
memory or relatively slower main memory.  To examine the effect
this  has, the length of the timing loop was varied from a very
small loop (which will fit  entirely  in  cache  and  therefore
execute  at  the maximum CPU speed), to a very large loop which
will not fit into cache, so that the instructions  will  mostly
be  fetched  from  main memory.  By using loops of intermediate
size,  one  can  see  the  effect  of  a  larger  cache.    The
instructions   are   divided  into  three  sets:   single  word
instructions, instructions followed by one word of address, and
instructions  followed by two words of address.  The numbers at
the top of the table give the number of  instructions  in  each
loop.   Though  the tests were run for all instructions, only a
few need be given here to show the effect of cache.  



PDP-11 CPU instruction timing tests                      Page 8
B. Z. Lederman


                           PDP-11/84

                      Length of test loop
Instruction      100    250    500   1000    2500   5000 10000

ROR R0             .3    .3     .3     .3      .3     .4    .8
TST (R0)           .7    .8     .8     .8      .8    1.0   1.3
CMP (R0), (R3)    1.6   1.6    1.6    1.6     1.6    1.8   2.1
MOV -(SP), (SP)+  2.1   2.2    2.2    2.2     2.1    2.3   2.7
MULF AC2, AC0    15.4  15.6   15.7   15.8    15.8   16.1  16.3
MULD AC2, AC0    44.4  45.2   45.5   45.7    45.9   46.1  46.4

Instruction       100   320   400   500   800  1000  2000 10000

ASHC #1, R0       2.1   2.1   2.1   2.1   2.2   2.2   2.2   3.1
MOV @#A, R1       1.1   1.1   1.0   1.0   1.1   1.0   1.1   2.0
STCFI AC0, @#A    9.9  10.0  10.1  10.1  10.2  10.2  10.3  11.1

Instruction    100   125   200   320   400  500  800 1250  2500

MOV #1, @#A    1.9   1.9   1.9   1.9   1.9  1.9  1.9  1.9   3.2
ADD #1, @#B    2.1   2.1   2.1   2.2   2.2  2.2  2.6  2.2   3.5

                    PDP-11/70, Core Memory

Instruction       100    250    500   1000    2500   5000 10000

ROR R0             .3     .3     .3     .4      .8     .9    .9
TST (R0)           .7     .8     .8     .7     1.2    1.3   1.3
CMP (R0), (R3)    1.0    1.1    1.1    1.4     1.6    1.7   1.7
MOV -(SP), (SP)+  1.7    1.7    1.7    2.0     2.5    2.5   2.5
MULF AC2, AC0     2.5    2.6    2.6    2.6     2.6    2.7   2.7
MULD AC2, AC0     3.8    3.9    4.0    4.0     3.9    3.9   3.9

Instruction       100   320   400   500   800  1000  2000 10000

ASHC #1, R0       1.3   1.4   1.4   1.4   2.2   2.2   2.4   2.6
MOV @#A, R1       1.2   1.4   1.5   1.7   2.1   2.2   2.3   2.4
STCFI AC0, @#A    3.3   3.4   3.4   3.4   3.6   3.6   3.6   3.7

Instruction    100   125   200   320   400  500  800 1250  2500

MOV #1, @#A    2.0   2.0   2.0   2.1   2.7  3.5  4.0  4.0   4.0
ADD #1, @#B    2.3   2.3   2.5   3.1   3.5  3.9  4.1  4.1   4.2

     Though the tests showed the effects of the larger cache on
the 11/84, the transition point was shifted  more  twords  long
loops  than I had anticipated.  If I had the opportunity to run
the tests again I would use a longer loop (31,250  instructions
for  the  first  test, 15,625 for the second and 10,000 for the
third) to insure obtaining  the  maximum  execution  times.   I


PDP-11 CPU instruction timing tests                      Page 9
B. Z. Lederman


would   probably  also  run  the  tests  for  10,000,000  total
instructions rather than the 1,000,000 used for the above tests
to  obtain one more significant digit of precision, and I would
not have to run as many tests between the shortest and  longest
loop  as  the  point  at which the effect of cache begins to be
lost can be determined sufficiently well from the above  tests.
It   is   interesting   to   see   what  happens  with  certain
instructions,  especially  floating  point:   the  instructions
which  take the most time to execute suffer least when the loop
is long as the time needed to fetch the instruction from memory
is  only  a small part of the total instruction execution time.
The fastest instructions suffer most, as here the  time  needed
to  fetch  the instruction can be as much as or longer than the
time the CPU needs to actually do the instruction once  it  has
it.