CA - Crossassembler



      1.0  Introduction


           The crossassemblers CAxx uses  the  full  functionality  of
      MACRO 11  in  both  operating  systems  RT11  and RSX11-M.  This
      means, that things like conditional assembling, program sections
      or  the macro feature is possible in the microproccessors assem-
      bly language.  Since the output is object format it is  possible
      to use all the functionality of the Linker or Task Builder.

           Of course there  a  some  restriction.   PDP  11  maschines
      doesn't  like  Hex numbers.  MACRO 11 doesn't accept them and it
      is not able to produce a  listing  with  hexadecimal  addresses.
      Second, since all mnemonics are realized with macros, the assem-
      bly process is a little slow.

           Crossassembler currently realized are:

        CA68    - for 6800
        CA85    - for 8080/8085




      2.0  Assembly process

      The following two lines are neccessary to let the  MACRO 11  as-
      sembler know about the microprocessors mnemonics:

                .MCALL  .OPxx
                .OPxx

      where xx stands for the microproccessor type  (e.g.   .OP85  for
      8080/85).

           In the assembler command line  include  the  macro  library
      OPxx :

        DCL:    MACRO progname+OPxx/lib+....

        MCR:    MAC progname,listname=OPxx/ML,progname

      The macro library can be build:

        DCL:    LIBR/MAC OPxx CAxx

        MCR:    LBR OPxx/CR:::128./DF:MAC=CAxx



CA - Crossassembler                                             PAGE 2



      3.0  Linking/Task Building




      3.1  RT11

      Create a loadable image.  Use the /BOTTOM option  for  the  load
      address:

                LINK/NOBIT/BOT:nnnnnn progname,....

      Use the program SAVBIN for extracting the  code  from  the  .SAV
      file.   For example if you specify /BOT:6000 your code starts at
      block 6 in the .SAV file:

                RUN SAVBIN
                outfile[.DAT]=infile[.SAV]
                Start address (octal): 6000

      Now you have a binary image.

           The program SAVBIN can be built as follows:

                MAC SAVBIN+IOCM/LIB
                LINK SAVBIN,IOCO




      3.2  RSX11-M

      Create a task build command file 'prognameBLD.CMD':

        progname/-HD/-MM,progname=progname,.....
        /
        STACK=0
        PAR=GEN:loadaddr:size
        /

      and build the task:

        TKB @prognameBLD

      where 'size' may be greater than the real size.   Use  the  task
      TSKCO  (task  conversion)  for extracting the code from the .TSK
      file:

                RUN TSKCO
                Enter task image file name [S] : progname[.TSK]
                Output: binary (B) or formatted (F) [S] : B
                Enter output file name     [S] : progname[.DAT]

      The extension .TSK is default and may be omitted.   The  default
      for  the  output  file  extension is .DAT.  If no output file is
      specified and the output is formatted, the output device is  the
      terminal  (TI:).  Formatted output is in Hex either in dump for-


CA - Crossassembler                                             PAGE 3



      mat or in INTEL hex format (one hex byte per line).

           The task TSKCO can be built as follows:

                FOR TSKCO=TSKCO
                FOR ASK=ASK
                TKB @TSKCOBLD


           Of course, the program may also be compiled with FORTRAN IV
      PLUS.



      4.0  Test programs

      A 8085 test program TEST.MAC is  included  in  the  distribution
      kit.   It  has  no  funktion  and is only for demonstration.  It
      calls one subroutine SUBR which is in SUBR.MAC.  For  both  RT11
      and RSX11-M type:

                @TEST