HVPLOT
                                  V01


                     Fortran-compatible library for
                        the joint operation of 
                             HP-GL plotters
                                   &
                        REGIS Graphics Terminals









































                      Dr R N Caffin and S L Hewett
                      CSIRO Div of Textile Physics
                            338 Blaxland Rd.
                           RYDE  2112  N S W
                               Australia

HVPLOT



                                [4mCONTENTS[0m


     Introduction                                1
     HVPLOT Routines                             2
     Number Formats                              4
     Installation                                5
     Control Subroutines                         6
                 Init                            6
                 Ploff                           6
                 Plon                            7
                 Restor                          7
                 Scale                           8
                 Select                          8
     Plotting Subroutines                        9
                 Axis                            9
                 Dir                             9
                 Dirrel                          9
                 Draw                           10
                 Home                           10
                 Jmpch                          10
                 Jump                           10
                 Label                          11
                 LabelA                         11
                 LabelN                         11
                 LabeXY                         11
                 Point                          11
                 Send                           12
                 Size                           12
                 Text                           12
     Error and Digitising Subroutines           13
                 Check                          13
                 Digitz                         13
                 Pread(n)                       14
     Sundry Subroutines                         15
                 PenDn                          15
                 PenUp                          15
                 SetCA                          15
                 SetCS                          15
                 SetIP                          15
                 SetIW                          16
                 SetLT                          16
                 SetLTS                         16
                 SetSA                          16
                 SetSL                          16
                 SetSM                          17
                 SetSR                          17
                 SetSS                          17
                 SetTL                          17
                 SetVS                          17
                 VTclr                          18
                 Scl                            18
                 Pick                           18
                 Tick                           18
                 ATick                          18

HVPLOT



                                [4mINTRODUCTION[0m



          This library of routines has been designed  as  an  integrated
     whole  to  provide  a user with a REGIS graphics terminal and/or an
     HP-GL plotter with a single  Fortran-compatible  graphics  package.
     Suitable terminals include the VT125, VT240, VT241 and their emula-
     tors.  Suitable plotters  include  the  HP7470A,  HP7475A,  HP7550,
     HP7580B,  HP7585B  and the DEC LVP16 (with a strange resemblance to
     the HP7475A).

          The HVPLOT package allows the user to use the same  calls  for
     the  two  devices for most of the common operations such as setting
     up scale factors, drawing  lines  and  labelling,  with  a  runtime
     choice   as   to  which  output  device  shall  be  actually  used.
     Naturally, each device has some calls which  are  peculiar  to  it:
     these calls have no effect when used for the other device.

          Regrettably, this package probably bears  little  relation  to
     any  other  standard graphics language.  There are a number of rea-
     sons for this:  many of the standards  are  archaic  (eg  Calcomp),
     others  are  incredibly complex (eg CORE and GKS), while others are
     just not known to the authors.  The result is a simple set of  com-
     mands which we found useful.

          Two other libraries can be made from HVPLOT, to cater for just
     the  HP-GL  plotters  or for the REGIS terminals.  They are made by
     editing the redundant parts of the modules out  prior  to  compila-
     tion.   The  advantage  of  using one of these packages in place of
     HVPLOT is solely one of memory and disk space.

          As this is the first full release of the  package,  there  are
     bound  to be errors in the software and the documentation.  Neither
     the authors, CSIRO or DECUS can accept any responsibility  for  the
     use  of  this  software  or any consequences.  However, the authors
     would appreciate being informed of any bugs found and of  suggested
     enhancements,  (especially if the code/text is provided!), and will
     try to acknowledge all such contributions.

HVPLOT                                                            Page 2



                               [4mHVPLOT ROUTINES[0m



          The routines available are listed below,  with  a  very  brief
     description  of each.  The chapter on number formats should be con-
     sulted for information on the parameter values.  As a quick  guide,
     most  calls use floating point variables.  In either case, the For-
     tran convention regarding Implicit Integer (I-N) is observed.   The
     chapter on installation should be consulted at the obvious time.

          Far more routines apply to the plotters than to the terminals:
     this  appears to reflect the difference in intelligence and resolu-
     tion between the two devices.  However,  the  terminals  possess  a
     clear  speed advantage.  Try putting the plot on the terminal until
     you are happy with the general  appearance,  then  put  it  on  the
     plotter.



                    CONTROL

     INIT                       To choose (at run time) and initialise
                                the plot device.
     PLOFF                      To turn the device off temporarily
     PLON                       To turn the device back on after a
                                PLOFF
     RESTOR                     Restore system to default state
     SCALE(Xmin,Xmax,Ymin,Ymax) Declare X and Y scales
     SELECT(I)                  Select a pen (on plotter)
     DEVSWT(string)             To optionally switch to the other
                                device.



                    PLOTTING

     AXIS(X0,Y0,Xtick,Ytick)    Draw axes at (X0,Y0) and ticks at *tick
     DIR(Degree)                Define individual character rotation
     DIRREL(Degree)             Define ind. char. rotation relative to
      P1, P2
     DRAW(X,Y)                  Enable writing and draw a line to (X,Y)
     HOME                       Go to BLHC and unload pen if plotter
     JMPCH(Cx,Cy)               To jump a distance defined by char. size
     JUMP(X,Y)                  Disable writing and jump to (X,Y)
     LABEL(String)              Write text at current position
     LABELA(char)               Write char (byte) from alternate char
                                set. See also SETCA,CS,SA,SS
     LABELN(N)                  Write integer in minimum format
     LABEXY(X,Y,Scale,Degree,String) To label the x or y axis
     PENDN                      Enable writing
     PENUP                      Disable writing
     POINT(X,Y)                 To plot a point at (X,Y)
     SEND(String)               To send an arbitrary string to a device
     SIZE(Width,Height)         Define character scale
     TEXT(X,Y,Scale,Degree,String) Put text at (X,Y), to scale and slope

HVPLOT                                                            Page 3






                    ERROR CHECKING and DIGITISING (Plotter Specific)

     CHECK                      Interrogate plotter for error code, if
                                any (plotter only)
     DIGITZ                     Obtain from the plotter the current
                                position
     PREAD1                     Read a single integer from the plotter
     PREAD2                     Read a pair of integers from the plotter
     PREAD3                     Read three integers from the plotter
     PREAD4                     Read four integers from the plotter



                    SUNDRY

     (Plotter Specific)

     SETCA(N)                   Define alternate char. set
     SETCS(N)                   Define standard char. set
     SETIP(IX1,IY1,IX2,IY2)     Redefine the registration points
     SETIW(Xll,Yll,Xur,Yur)     Define a window (Lower Left, Upper
                                Right)
     SETLT(Npatn,Patln)         Define line type and dash lengths
     SETLTS                     Reset line type to continuous
     SETSA                      Select alternate char. set
     SETSL(Slope)               Define character slope 
     SETSM(Char)                Define char. to be drawn at each point
     SETSR(Width,Height)        Define relative character size 
     SETSS                      Select standard char. set
     SETTL(Tplus,Tminus)        Define tick lengths, plus and minus
     SETVS(Speed)               Define pen speed

     (VT125 Specific)

     VTCLR                      Disable and clear the VT125 graphics
                                screen
     SCL(xx,yy,x,y)             To scale from user to VT125 unit 
     PICK(ii,n)                 Move n pixels in direction ii 
     TICK(ii,n)                 Draw n pixels in direction ii
     ATICK(flag)                To draw a tick on axis at current
                                position

HVPLOT                                                            Page 4



                               [4mNUMBER FORMATS[0m



          The HP-GL  plotters  will  accept  either  floating  point  or
     integer  data  for  most commands, while converting internally to a
     special format.  They can also be programmed to scale incoming data
     over a wide range.  The REGIS terminals operate internally in terms
     of pixels, and hence in integer, but they too can  accept  floating
     point  data.  Thus most routines have been written to expect REAL*4
     data.  Scaling for the REGIS terminals has been enabled by  putting
     it in the software:  thus screen formats should be similar for both
     devices when given the same  parameters.   However,  some  vertical
     compression will be noticed with the REGIS terminals as a result of
     the 2:1 raster interlace.

          It should be noted that the plotters usually offer only a res-
     tricted  range  for  the  incoming  data.  The HP7470A plotter, for
     instance, will accept floating point numbers in the range -32768.00
     to  +32767.99  and integers in the same range.  Some floating point
     or integer numbers can only be accepted in the more  limited  range
     -128.0 to +127.99.  Plotting may be done in device units, but it is
     usually more convenient to scale the device to the user's range  of
     data.   For further details, you should consult the manual for your
     plotter.

          The plotter scaling expects floating  point  numbers  for  the
     maxima  and  minima,  but  truncates  these  to integers internally
     before scaling.  Thus it requires a minimum horizontal and vertical
     full-scale  scale  of  1.0  to  avoid  truncation to zero.  It also
     requires a maximum of 64k, obviously.  Exceeding these  values  may
     have  unfortunate  results.   The  terminal  scaling is done by the
     software:  the normal Fortran limits apply.

          Both devices allow the concept  of  a  plot  window,  but  the
     effect  is slightly different in the two cases.  Usually, a plotter
     can be programmed to regard any subset of the legal 2-D  coordinate
     space  as  the  current visible plotting window.  Data outside this
     area is not plotted, although it does  not  cause  an  error.   The
     plotter  manual should be consulted for further details.  The VT125
     on the other hand has a 768x480 visible pixel window onto  a  stor-
     able  768x512  pixel  space,  and  this  visible window, or viewing
     space, can be moved after the data has been sent to  the  terminal.
     It should be noted however that there is a 2:1 mapping in the vert-
     ical:  there are really only 240 distinct  vertical  pixels.   (And
     the  manual is more confusing!).  The plot window is currently only
     implemented for the plotters.

HVPLOT                                                            Page 5



                              [4mCHARACTER STRINGS[0m



          It should be noted that the package is written in Fortran  IV,
     and the string handling facilities in this language are not partic-
     ularly good.  Without some understanding of how strings are handled
     the   user   may  experience  some  difficulties  with  this  area.
     Basically  there  are  two  simple  ways  of  handling  strings  as
     subroutine  parameters  in  Fortran  IV:  either the string and the
     number of characters is passed or the string terminated by  a  null
     character  is  passed.   In the latter case the called routine uses
     the DEC special string length routine LEN(string) to find the posi-
     tion of the first null character in the string.  This latter is the
     technique used in this package.  However,  if  the  user  does  not
     ensure  that  all  strings are terminated by a null the results may
     not be satisfactory.  

          In the subroutines reference is made to a  byte  array  called
     STRING.   This serves as a local reference.  It is given an unknown
     dimension, allowing the user's program to determine the matter.  It
     is  suggested that the use of a string or byte vector in the user's
     program (with the ENCODE statement  where  appropriate  to  convert
     numbers to character strings) and a trailing null be seriously con-
     sidered as a safe way of passing text (and numbers)  for  printing.
     This is shown here:

        BYTE                       string(80)
        . . . .
        x=2.5
        encode(4,1000,string) x
     1000                          format(F4.1)
        string(5)=0
        call label(string)


          However, the user may prefer to pass predefined strings stored
     as  variables.   This can lead to trouble.  The following technique
     is NOT correct by itself:

        REAL                       X(4)
        DATA                       X/' 2.5',' 5.0',' 7.5','10.0'/
        . . . 
        call label(X(2))

     While the individual character strings have been correctly declared
     they are not terminated by nulls, so the LABEL routine can not tell
     how many characters to print.  However, if a COMMON block is  added
     and used as shown below, the system functions:

        REAL                       X(4)
        DATA                       X/' 2.5',' 5.0',' 7.5','10.0'/
        COMMON                     /A,IA/
        DATA                       IA/0/
        . . . 
        A=X(2)

HVPLOT                                                            Page 6



        call label(A)

     The reason is that the variable IA will follow directly after A and
     will  look  to  the  string  routines like the required terminating
     null.

HVPLOT                                                            Page 7



                                [4mINSTALLATION[0m




        [4mRT-11[0m

          In most cases it suffices to build the HVPLOT library  and  to
     make  it  available for subsequent linking.  To do this under RT-11
     you need only to type @HVPLOT and the  command  file  will  do  the
     rest.   You  will also need the PL handler on your system disk, and
     it will need to be installed.  The easiest way of doing this is  to
     type  @PL  and let the command file do the rest.  You should reboot
     the system when PIP prompts you.

          You do not need to LOAD the handler as the INIT  routine  will
     do  this  for  you  it (and it will unload automatically at program
     exit).  It would be nice if the abtio$ bit in the handler could  be
     persuaded  to do it's bit after a C, but I (RNC) don't seem to have
     had much joy with this so far.  Advice is welcome.


        [4mOther Operating Systems[0m

          For use under other operating systems you will  need  to  edit
     the following subroutines:

        INIT, in HV0.FOR, to alter the OPEN and handler LOAD statements
        PLOFF, in HV3.FOR to alter or remove the ILUN and  SPFUN  state-
        ments

     These should be modified  to  suit  your  particular  requirements.
     Note that if you use the CHECK routine you cannot spool the output.
     The same applies to any form of digitising, of course.

          There are three test routines on the distribution:  BOX,  SPI-
     RAL,  and  READIN.   Each  has a .COM file to aid in trying it out.
     The .COM files also illustrate the requirements  for  linking  your
     program  with  the  package (very simple).  The BOX program draws a
     rectangle and writes "Box" in the middle.  It is designed  to  pro-
     vide  a  very  simple  test  of  your system, and to illustrate the
     minimal requirements in setting up a program.  The  SPIRAL  program
     draws  an  annotated  and numbered axis and some data:  this illus-
     trates the various steps required to produce a  full  "axis".   The
     READIN  program  is  for use only with a plotter.  It draws an axis
     and then enters the digitising mode.  It should be studied  with  a
     little  care  if  you  wish  to set up your own digitising program.
     Note in particular that the plotter has to be put into and  out  of
     the digitising mode.

HVPLOT                                                            Page 8



                            [4mSUBROUTINES - CONTROL[0m



          These routines are used for setting up and overall control  of
     the  devices  and  plot  package.   INIT,  SCALE and SELECT must be
     called.


                                    [4mINIT[0m

          The subroutine starts with a request for the  user  to  choose
     which device is required.  The information is held for use in other
     routines and the appropriate device is initialised.  Note  that  if
     you want both devices initialised you must call INIT twice, answer-
     ing "H" once and "V" once.  Switching between the two is done  with
     DEVSWT.

          Initialisation of the plotter and the  plot  package  follows:
     without  this  command  neither  the  plotter nor the terminal will
     function.  The user should note that logical unit 9 is used by  the
     package  for the plotter output.  Since RT-11 does not support mul-
     tiple terminals in the conventional sense, a device handler  called
     PL is supplied with HVPLOT, along with device handler PL.SYS (which
     must be on the system disc)if the plotter is  used  (see  Installa-
     tion).   With  any multi-terminal system, it is probably sufficient
     to attach LUN 9 to a spare terminal port.  On an LSI  11/2  running
     RT11FB  V4.0  or  V5  speeds  up to 4800 baud are easily supported.
     However, 9600 baud during heavy Fortran  floating  point  sometimes
     seems  to be just beyond the limit for an 11/2.  An LSI 11/23 would
     probably be fast enough to support 9600 baud.  Plotting  is  fairly
     continuous  as  the  plotters all have significant internal buffers
     and generally can't keep up with 4800 baud.


                                    [4mPLOFF[0m

     HP-GL plotters:

          Used to turn the plotter OFF  after  a  plot.   It  is  HIGHLY
     recommended that this call be used to avoid problems with unexpect-
     ed interrupts from the plotter.  Not only does it  send  a  "sleep"
     command  to the plotter, but it also disables the interrupts in the
     PL handler.  The first  subsequent  write  to  the  plotter  (which
     should  be  PLON  or INIT) will reactivate the interrupts.  (If you
     have adapted this to run under another O/S, you may need to  delete
     this part of PLOFF.  Advice from anyone doing this is welcome.)

          There does not seem to be any very simple, clean and automatic
     way  under RT-11 of turning off the interrupts for the handler port
     when the program finishes.  There is meant to be, but I  can't  get
     it  to  work  satisfactorily yet.  If you can, let me know, please.
     Consequently, if you don't use this at the end of your program,  it
     is  possible  that, due to noise or other happenstance, the plotter
     could reactivate the interrupts on the port after the  handler  has
     been  "disconnected" from the program or removed from memory.  This

HVPLOT                                                            Page 9



     would most likely ( = "does always") crash the system.

          Note in particular that if it is wished to call HOME as  well,
     this must be done before PLOFF is called.

     REGIS terminals:

          Used to send a REGIS "off" command.   But  note  that  Command
     strings sent to the REGIS terminal in this package switch REGIS on,
     send the command and then switch REGIS off.  This leaves the termi-
     nal in text mode in between calls.


                                    [4mPLON[0m

     HP-GL plotters:

          To turn the plotter back ON after invoking PLOFF.   Note  that
     this  is  the  only  way of doing this, short of calling INIT.  The
     advantage of using PLON is that the  plotter  remembers  all  setup
     commands previously sent plus the current position.

     REGIS terminals:

          Sends a REGIS "on" command string.


                                   [4mRESTOR[0m

     HP-GL plotters:

          This restores some of the plotter functions  to  a  predefined
     state.   The  plotting window size is not altered but the following
     are set.  For further details see the plotter manual.

          Plotting mode . . . . . . . . .Absolute
          Relative character direction   Horizontal
          Line type . . . . . . . . . . .Solid line
          Line pattern length            4% of the distance from P1 to
           P2
          Input window. . . . . . . . . .Mechanical limits of plotter
          Relative character size        Width=0.75% of(P2x-P1x)
                                         Height=1.5% of (P2y-P1y)
                                               (See SCALE) 
          Symbol mode . . . . . . . . . .Off
          Tick length                    tp=tn=0.5% of (P2x-P1x) for
           Y-tick
                                         and 0.5% of (P2y-P1y) for
           X-tick
          Standard character set. . . . .Set 0
          Alternate character set        Set 0
          Character set selected. . . . .Standard
          Character slant                0 degrees
          Mask value. . . . . . . . . . .223,0,0
          Digitise clear                 On
          Scale . . . . . . . . . . . . .Off

HVPLOT                                                           Page 10



          Pen velocity                   38.1 cm/s
          Label terminator. . . . . . . .ETX (ASCII decimal 3)

     REGIS terminals:

          No effect:  returns immediately.


                        [4mSCALE(Xmin, Xmax, Ymin, Ymax)[0m

          Establish the user coordinate system.

          Xmin           The minimum value on the x axis.
          Xmax           The maximum value on the x axis.
          Ymin           The minimum value on the y axis.
          Ymax           The maximum value on the y axis.

          Having scaled the device to the required values,  future  com-
     mands  must be given in terms of this new coordinate system.  Note:
     The top lefthand corner of the paper, as inserted into the  HP7470A
     plotter,  is  roughly  P1, while the bottom righthand corner is P2.
     For further details,refer to the relevant plotter manual.


                                  [4mSELECT(N)[0m

     HP-GL plotters:

          To select and/or store one of the pens.

          N = 0          Stores the currently selected pen.
          N = Odd number Load the lefthand pen on the 7470A.
          N = Even number Load the righthand pen on the 7470A.
          N = 1-6        Loads the appropriate pen on the 7475A.

     REGIS terminals:


          No effect:  returns immediately.

HVPLOT                                                           Page 11



                           [4mSUBROUTINES - PLOTTING[0m



          These routines are used for the majority of the plotting work.


                         [4mAXIS(X0, Y0, Xtick, Ytick)[0m

          To draw the coordinate axis for a graph and put tick marks  on
     the two arms.

          X0, Y0         The Origin of the axes.
          Xtick          The space between ticks on the X axis.
          Ytick          The space between ticks on the Y axis.

          Note that the tick spacings assume that the SCALE routine  has
     been called.  The size of the tick marks can be controlled with the
     SETTL command for the plotter but is fixed for  the  VT125  (unless
     you get into the software).


                                 [4mDIR(Degree)[0m

          To specify the individual  character  rotation  (but  NOT  the
     string  direction).   The  angle  is  in  degrees relative to the X
     direction.  It is in principle possible to do this to the VT125  as
     well,  but  the  results  turn out to be pretty ghastly.  Character
     tilt should be possible in multiples of 45 degrees but only  0  and
     90  degrees  are  catered for at the moment since varying character
     size is not.  The use of this feature is largely confined to  writ-
     ing up the Y-axis, and is done for you.


                               [4mDIRREL(Degree)[0m

     HP-GL plotters:

          As for DIR, but the angle is taken relative to  the  positions
     of  P1  and P2.  Thus alteration of the plot area via P1 and P2 may
     cause the real angles to alter.  Unlike DIR, the overall "image" is
     however preserved.

     REGIS terminals:

          Variable direction lettering is not supported.


                                 [4mDRAW(X, Y)[0m

          To draw a line from the current position  to  a  new  location
     (X, Y).  In the event that (X, Y) is outside the legal plot window,
     the line will go to the edge correctly and the pen will  be  lifted
     while  the  plot  point  is  outside  the window.  If SETSM is also
     called, a character will be plotted at each (X, Y) point given, but
     note  that if the calling program is to operate on either the HP-GL

HVPLOT                                                           Page 12



     plotter or the REGIS terminal at will then SET* subroutines  should
     not  be  used.  It is possible to still send these instructions but
     they have no effect on the terminals.


                                    [4mHOME[0m

          In the case of an HP-GL plotter, this will  position  the  pen
     head  over  the top lefthand corner near P1 for the maximum view of
     the plot, return the pen to its holder  and  turn  off  the  symbol
     mode.   The  effect  for a REGIS terminal is a to put the cursor in
     the top left hand corner of the screen.  Note that this should  not
     be  used as a substitute for PLOFF, but must be called before it if
     it is to be used.


                                [4mJMPCH(Cx, Cy)[0m

     HP-GL plotters:

          To jump a distance related to the size  of  characters.   Used
     for example in positioning labels.

          Cx             The no. of character width spaces.
          Cy             The no. of character height spaces.

          Note  that  the  parameters  are  indeed  real,  not  integer:
     fractions of a character are permitted.  Note also that if the last
     character-writing instruction specified other than a baseline angle
     of  zero,  the height and width values here will be relative to the
     non-zero baseline angle.

     REGIS terminals:

          No effect:  returns immediately.


                                 [4mJUMP(X, Y)[0m

          To move the pen or the terminal cursor to a new  location  (X,
     Y) without drawing.


                                [4mLABEL(String)[0m

          To output a text String (byte array) at the current  position.
     The character set, direction, size, and slant must be predefined if
     default values are not required.  The comments in the  introductory
     chapter  on  character  strings  should  be noted before using this
     routine.  It should also be noted that this  routine  can  be  used
     repetitively.  Consider the writing of a label such as

          'Step Size:  0.200 radians'

     where the '0.200' is actually calculated at run-time.  This can  be
     done  with three calls to LABEL:  one for the 'Step size:', one for

HVPLOT                                                           Page 13



     the number after it has been put into a character string  with  the
     ENCODE  statement,  and one for the 'radians'.  It is not necessary
     to reposition the pen before each  call:   plotting  will  continue
     where the last call left off.


                                [4mLABELA(Char)[0m

          To send one character from the second  character  set  at  the
     current  position  (as  for  LABEL).   The alternate character set,
     direction size and slant must be predefined if default  values  are
     not required.  For further details consult the relevant manuals.


                                  [4mLABELN(N)[0m

          To write  an  integer  number  (which  may  print  as  several
     characters) at the current position.  The character set, direction,
     size and slant must be predefined if the  default  values  are  not
     required.  This is primarily used in numbering tick marks on axes.


                     [4mLABEXY(X, Y, Scal, Degree, String)[0m

          To label the X or Y axis, as appropriate.

          X, Y           The coordinates on axis for start of label.
          Scal           The width of characters to be printed (h=1.5*w)
          Degree         The direction of print of label, (0 or 90.)
          String         The required label (byte array).

          An offset relative to the character size is incorporated  into
     the  subroutine to bring the labelling away from an axis line.  The
     offset is switched depending on whether X or Y is  zero.   If  both
     are non-zero,there is no offset:  for this the routine TEXT is sug-
     gested so that the start location can be chosen.


                                 [4mPOINT(X, Y)[0m

          To plot a point at  location  (X,  Y).   This  is  principally
     intended for the creation of point plots.  

     HP-GL plotters:

          If a character is desired at each point  rather  than  just  a
     point,  use  SETSM  to select the symbol and then just JUMP to each
     point.  The symbol will be plotted automatically.



HVPLOT                                                           Page 14



                                [4mSEND(String)[0m

          A catch-all for unspecified  commands:   whatever  is  in  the
     String  is  sent  to  the device without any modification.  This is
     used with digitising, for instance.


                             [4mSIZE(Width, Height)[0m

          To set the absolute character size in centimetres.

          Width          Width
          Height         Height

     HP-GL plotters:

          If the width value is zero then the size defaults to 0.19  for
     width and 0.27 for height.  Negative parameters will produce mirror
     images.  The range of values  for  width  and  height  is  -128  to
     127.9999, but the high end is meaningless.

     REGIS terminals:

          No effect:  returns immediately.


                      [4mTEXT(X, Y, Scale, Degree, String)[0m

          To output a string at a specified position, size and  baseline
     angle.

          X, Y           The coordinates for the start of the label.
          Scale          The characters width to be used (h=1.5*w).
          Degree         The string baseline slope (plotter only).
          String         The required label (byte array).

     REGIS terminals:

          The degree argument is defaulted to 0.0 when this is used with
     a terminal:  only horizontal text is currently supported.  

HVPLOT                                                           Page 15



                 [4mSUBROUTINES - ERROR CHECKING and DIGITISING[0m



          The HP plotters are usually capable of replying to an  enquiry
     regarding  their  current  error  status  or  position.   The CHECK
     routine is provided for errors, and PREADn is  provided  for  other
     input.


                                   [4mCHECK()[0m

          If this is to be used with the  plotter,  it  must  be  called
     before  PLOFF  is  called.  It will return two error codes, one for
     HP-GL language errors and one for RS232C errors.  If an error  code
     is  non-zero,  it  will  be displayed on the terminal;  if zero, it
     will not be displayed.  A message noting that the  check  has  been
     done  is displayed under all conditions, however.  The error codes,
     as described by the HP manual, mean the following:

     0  No error (not displayed on terminal)
     1  Instruction not recognised
     2  Wrong number of parameters
     3  Out of range parameters, or illegal character
     4  -
     5  Unknown character set
     6  Position overflow
     7  -
     8  Vector received while pinch wheels raised
     9  -
     10 Output instruction received while executing another o/p instr'n.
     11 Invalid byte after <ESC><.> in device control instruction
     12 Invalid byte while parsing (defaults will be used)
     13 Parameter out of range
     14 Too many parameters (excess ignored)
     15 Framing, parity or overrun error
     16 Input buffer overflow

     No corresponding REGIS routines exist but if CHECK is  called  when
     in REGIS mode it returns immediately.


                             [4mDIGITZ(X, Y, Done)[0m

          The HP-GL plotters can return the current position on  demand.
     If  the  optional  fiber  optic sight is put in place of the pen, a
     graph or drawing put in the plotter and the pen moved such that the
     target  is  over the desired position on the paper, the plotter can
     measure that position.  The "enter" key on the plotter is  used  to
     tell the system when the user is ready for the next point.

          The following points should be noted for successful  operation
     of the plotter as a digitiser:

          1.  Do not attempt to store the fiber optic pen in  a  holder:
              the holder will probably be already occupied, and it won't

HVPLOT                                                           Page 16



              fit anyhow.  This means that you  must  unload  the  fiber
              optic  pen  before you tell the plotter to pick up another
              pen too.  You do this with SELECT(0).

          2.  The X and Y parameters are REAL*4 and are in  user  units,
              as  set up by SCALE.  You can modify the routine to return
              plotter units if you wish.

          3.  The Done parameter is LOGICAL*1, and is  false  until  you
              digitise the same point twice, when it becomes true.  This
              is used as a convenient flag for indicating that you  have
              finished digitising.

          4.  The pen should be put down before  you  start  digitising:
              this gives better resolution.

          5.  The plotter should be put  in  digitise  mode  before  you
              start digitising, and should be taken out of digitise mode
              after.

     The test program READIN.FOR can be used as  a  convenient  starting
     point for understanding this function.


                         [4mPREADn(I [,J [,K [,L] ] ])[0m

          The HP plotters  return  data  in  a  known  format,  and  the
     returned  variables  may be obtained in this way.  Typical uses for
     these routines would be the error  checking  mentioned  above  (one
     parameter)  and  digitising  with  the  plotter (three parameters -
     x,y,pen), except that these actually  use  special  optimised  ver-
     sions.

HVPLOT                                                           Page 17



                            [4mSUBROUTINES - SUNDRY[0m



          The calls to subroutines of the form SETxx are used to  define
     or  change  specific  attributes.   For the Plotter, the xx are the
     letters used in the plotter instruction manual,  which  contains  a
     more detailed description of their use.  For the terminals suitable
     mnemonics have been chosen, some of which are the same as  for  the
     plotter:   the VT125 manual allegedly contains more information but
     may prove to be incomprehensible.

     HP-GL Plotters:


                                    [4mPENDN[0m

          To put the pen down at the  current  position.   This  routine
     also forces a rewind or a buffer dump to ensure the buffer is actu-
     ally output to the  device.   This  call  should  not  normally  be
     needed.


                                    [4mPENUP[0m

          To lift the pen while remaining in the current location.   The
     rewind  is  also  executed as in PENDN.  Again, this command should
     not be needed.


                                  [4mSETCA(N)[0m

          To define the alternate character set for the plotter.  N must
     be in the range 0 to 4 to choose one of the five possible character
     sets.  The default value after initialization is 0, the same as the
     main set.


                                  [4mSETCS(N)[0m

          To define which character set is to be used as standard.   For
     the  plotter,  N  must  be in the range 0 to 4 to choose one of the
     five possible character sets.  The default value after  initializa-
     tion is 0.


                          [4mSETIP(Ix1, Iy1, Ix2, Iy2)[0m

          To set the registration points P1 and P2 to  ensure  the  same
     size plot.  The parameters are in plotter units.  The figures quot-
     ed apply to the HP7470A:  see the manuals for other models.   There
     is no checking in the subroutine.

          Ix1, Iy1       The coordinates of P1.
          Ix2, Iy2       The coordinates of P2.


HVPLOT                                                           Page 18



          The range for Y coordinate is the same for both P1 and P2:   0
     <=  Y  <=  7650  .  The range for X coordinate depends on the paper
     setting:  for the plotter set for US paper 0 <= X <= 10300, for  A4
     paper  0  <= X <= 10900.  On power up P1 is set to (250,279) and P2
     is set to (10250,7479).


                          [4mSETIW(Xll, Yll, Xur, Yur)[0m

          This can be used to restrict the area of the plotting surface.
     The  parameters are in plotter units.  On initialisation the window
     is set to the maximum plotting area.

          Xll, Yll       Coordinates of Lower Left of window area.
          Xur, Yur       Coordinates of Upper Right of window area.


                             [4mSETLT(Npatn, Patln)[0m

          To define the type of line to be used when drawing.  The lines
     are specified in the plotter manuals.  Note that line type 0 is NOT
     a simple line:  see SETLTS.

          Npatn          The line pattern number (0 - 6). Default 0.
          Patln          The % length of a pattern. Default is 4%.

          Again , the distance between scaling points is  the  reference
     for the percentage lengths.


                                   [4mSETLTS[0m

          To reset the line type back to a continuous line.


                                    [4mSETSA[0m

          Temporarily selects the predesignated alternate character  set
     for use.  Note that the set remains the "alternate" set.


                                [4mSETSL(Angle)[0m

          This defines the individual (italic) slope of the  characters.
     (To define the slope of a baseline, see DIR.)

          Angle          The tangent of the angle to the vertical.

          Decimal numbers between -128 and 127.99 are accepted.  Using 0
     will  result  in  a  return to vertical which is the default value.
     Note that outside an absolute value of 3 is not very useful.



HVPLOT                                                           Page 19



                                 [4mSETSM(Char)[0m

          To set the symbol to be drawn at each point.  The character is
     centered at the end of the vector.  The default is a null, and this
     can be restored by calling SETSM with a zero for an argument.  This
     routine is quite useful for doing multiple point or vector plots on
     one graph.


                            [4mSETSR(Width, Height)[0m

          The standard size of the characters can be defined relative to
     the chosen scale.

          Width          As a % of the horizontal distance.
          Height         As a % of the vertical distance.

          The size of characters can also be set in absolute terms:  see
     SIZE.


                                    [4mSETSS[0m

          Reselects the standard character set for use.


                            [4mSETTL(Tplus, Tminus)[0m

          Tick marks can be  draw  at  the  current  location  and  this
     routine  is  used  to control the tick size.  Both the positive and
     negative length of the mark can be altered.

          Tplus          The % distance on the positive side
          Tminus         The % distance on the negative side

          The % distances referred to are relative to the X and  Y  axis
     scaling lengths.  The defaults are .5% of the scaling lengths.


                                [4mSETVS(Speed)[0m

          The velocity with which the pen travels can be varied from the
     default  value  38.1cm/s down to .38cm/s.  For transparent film the
     speed should be set at 10cm/sec.

     REGIS terminals:



                                    [4mVTCLR[0m

          To clear the Terminal screen.



HVPLOT                                                           Page 20



                              [4mSCL(xx, yy, x, y)[0m

          Points to be plotted require scaling from user coordinates  to
     screen coordinates.  (This is done for you with the plotter)


                                 [4mPICK(ii, n)[0m

          To move the cursor n pixels in the direction as defined by ii,
     as follows:
     				2
     			      3   1
     			    4   .   0
     			      5   7
     				6


                                 [4mTICK(ii, n)[0m

          To draw n pixels in direction ii, direction as  shown  in  the
     pick routine.


                                 [4mATICK(flag)[0m

          To draw ticks, assumes that the cursor  is  correctly  located
     and draws a small mark,
          if flag = .false. draws horizontally
          if flag = .true.  draws vertically












                                 INDEX


ATICK  . . . . . . . . . . . . . . . 20
AXIS . . . . . . . . . . . . . . . . 11

CHECK  . . . . . . . . . . . . . . . 15

DIGITZ . . . . . . . . . . . . . . . 15
DIR  . . . . . . . . . . . . . . . . 11
DIRREL . . . . . . . . . . . . . . . 11
DRAW . . . . . . . . . . . . . . . . 11

HOME . . . . . . . . . . . . . . . . 12

INIT . . . . . . . . . . . . . . . . 8

JMPCH  . . . . . . . . . . . . . . . 12
JUMP . . . . . . . . . . . . . . . . 12

LABEL  . . . . . . . . . . . . . . . 12
LABELA . . . . . . . . . . . . . . . 13
LABELN . . . . . . . . . . . . . . . 13
LABEXY . . . . . . . . . . . . . . . 13

PENDN  . . . . . . . . . . . . . . . 17
PENUP  . . . . . . . . . . . . . . . 17
PICK . . . . . . . . . . . . . . . . 20
PLOFF  . . . . . . . . . . . . . . . 8
PLON . . . . . . . . . . . . . . . . 9
POINT  . . . . . . . . . . . . . . . 13
PREADn . . . . . . . . . . . . . . . 16

RESTOR . . . . . . . . . . . . . . . 9

SCALE  . . . . . . . . . . . . . . . 10
SCL  . . . . . . . . . . . . . . . . 20
SELECT . . . . . . . . . . . . . . . 10
SEND . . . . . . . . . . . . . . . . 14
SETCA  . . . . . . . . . . . . . . . 17
SETCS  . . . . . . . . . . . . . . . 17
SETIP  . . . . . . . . . . . . . . . 17
SETIW  . . . . . . . . . . . . . . . 18
SETLT  . . . . . . . . . . . . . . . 18
SETLTS . . . . . . . . . . . . . . . 18
SETSA  . . . . . . . . . . . . . . . 18
SETSL  . . . . . . . . . . . . . . . 18
SETSM  . . . . . . . . . . . . . . . 19
SETSR  . . . . . . . . . . . . . . . 19

INDEX



SETSS  . . . . . . . . . . . . . . . 19
SETTL  . . . . . . . . . . . . . . . 19
SETVS  . . . . . . . . . . . . . . . 19
SIZE . . . . . . . . . . . . . . . . 14

TEXT . . . . . . . . . . . . . . . . 14
TICK . . . . . . . . . . . . . . . . 20

VTCLR  . . . . . . . . . . . . . . . 19