The Kermit protocol and the PDP-11


                 Brian Nelson   4-OCT-1985 14:10


Abstract

 This article will describe the  author's  implementation  of  the
Kermit  file transfer protocol for the PDP-11 series under RSTS/E,
RSX11M/M+, P/OS RT11 and TSX+.  This protocol allows many (if  not
most)  types of computer systems to effect, at minimum, error free
file  transfer  with  other  systems   and   microcomputers   over
asynchronous lines.

The first obvious use of  any  program  or  protocol  designed  to
accomplish  file  transfer is to be able to provide the ability to
support file uploads and downloads from superminis such as the VAX
and  PDP-11  to  remote  personal  computers,  such  as the PC and
Rainbow.  Since as of this date (03-Oct-1985) there are  available
over 160 versions of Kermit available for numerous micro, mini and
mainframe configurations, Kermit addresses this need quite well.

Other uses of Kermit are quite numerous.  I routinely  use  Kermit
for  transfering  software  developed  for the PRO/350 on a RSTS/E
11/23+ host as well as using the PDP-11/44 and VAX 11/785 I run at
the University of Toledo for dialing out to other systems, such as
the LCG  Tops  20  system  and  the  LDP  public  domain  library.
Considering  that  there  exists  a  Kermit  for  almost  any  DEC
configuration one can even use Kermit as a poor man's Decnet.   In
my  case,  I have a DMF modem port from the 11/785 and a DZ11 port
from the 11/44 connected to the Gandalf  PACX  front  end  switch,
which  allows  me  to  connect  either  system to any of the other
systems on the PACX, which includes an IBM 370  compatible  system
as well as connecting the VAX to the PDP-11.

With the knowledge that there are Kermit implementations for  most
personal  computers  in  use  it  becomes apparent that the Kermit
standard is well worth looking in to.  A list of versions  running
on Digital hardware follows the article.

The Kermit protocol

The  Kermit  protocol  is  designed   to   operate   over   normal
asynchronous   terminal   lines.    All   data  and  commands  are
transferred with a packet oriented protocol, basically  consisting
of a start of packet character (normally SOH), followed by length,
control, data and checksum fields.  Communications is half duplex,
in  that for every packet sent, the sender must wait for either an
acknowledgement packet (ACK) or a negative acknowledgement  packet
(NAK).   Transmission is in ascii, with no requirements needed for
the transmission of eight bit  characters  or  control  characters
other  than  the  choice  of  control-A for marking the start of a
packet.   All  'control'  characters  imbedded  in  the  data  are
prefixed  to  convert  them  to  printable  characters,  the  same

                                                                Page 2


applying  to   eight   bit   characters   if   required   by   the
characteristics  of  the  line.   Since  there  are many different
implementations of Kermit, the protocol provides  a  mechanism  by
which  the capabilities of two connected Kermits can be negotiated
to allow  for  differences  in  the  level  of  protocol  support.
Examples  of  protocol  features  that  not all Kermits understand
include data compression and transfer of file attributes.
 Rather than to go into more detail about the the Kermit protocol,
the reader should consult the references listed at the end of this
article.

The PDP-11 Kermit-11 implementation

 The author's version of Kermit-11 is written in Macro-11 and  can
run  on  RSTS/E, RSX11M, RSX11M Plus, P/OS and RT11.  The RSTS and
RSX file system interface is via RMS11 version 2, while  the  RT11
interface  attempts to emulate the RMS11 subsystem.  The choice of
Macro-11 for the implementation  language  was  made  for  several
reasons,  one  being  the  availability  of  the  assembler on all
systems and another being speed and compactness of the code.
 RMS11 was used for  RSTS/E  and  RSX  to  provide  a  common  i/o
interface  to  the  host  file system.  Additionally, Bob Denny of
Alisa Systems further extended the RMS interface to support remote
file  access  over  DECNET  with Kermit, allowing commands such as
SEND  NODENAME::[BRIAN.FUBAR]FILE.TYPE  and  other   remote   file
accesses over DECNET.  RMS11 version 2 also provides a very simple
and powerfull means of doing wildcard searching, file renames  and
file deletion via the $PARSE, $SEARCH, $RENAME and $DELETE macros.
Points against RMS basically amount to it's  size,  RMS  is  quite
large  even  if  overlayed.  This is helped by using the segmented
RMSRES available on RSTS/E and RSX11M Plus,  though  there  is  no
remote file access for RMSRES in the current release of Kermit-11.
The other objection to RMS will come from RSTS/E  users,  who  are
used  to  using files that normally lack file attributes.  This is
overcome by the ability of RMS v2 to create stream ascii files.

The RSTS/E Kermit, while it does 'run' under RSX  emulation,  does
NOT use any RSX directives (apart from GTSK$S) to interface to the
executive, as (one) the RSX directive emulation  under  RSTS/E  is
only a small subset of 'real' RSX and (two) there is no need to go
though an additional layer of overhead  to  make  RSTS/E  map  RSX
calls  to native calls.  The 'multiple private delimiters' feature
is used to avoid losing  read  pass  all  (binary)  mode  on  read
timeouts,  as well as setting the link to '8-bit' mode to keep the
terminal driver from stripping the high bit from data received.

The RSX11M/M+ and P/OS versions of Kermit-11, like the RSTS/E  and
RT  versions,  receive  eight bit data assuming no parity is used.
Where parity is a must, Kermit-11 has to use  a  prefixing  scheme
for  eight bit binary data.  Like the RSTS/E version, binary files
are created as FIXED no carriage control files such  as  used  for
task  images.   Note that parity generation is done by software in
Kermit-11.  The P/OS version runs under control of DCL.  The  next
release of Kermit-11, which will be 2.37, will include support for
the PRO TMS (Telephone Management System) option.

                                                                Page 3


 The RT11 and TSX+ version of Kermit-11  maintains  source  module
compatability  with  the RSTS/E and RSX versions.  Each version of
Kermit-11 has it's own source file  to  deal  with  the  operating
system,  for  RSX it is K11M41.MAC, for RSTS/E they are K11E80.MAC
and K1180S.MAC, and for RT11 they are  called  K11RT*.MAC.   Apart
from these specific files, all other source files are shared.  The
RT11 Kermit-11 can use either the version 5.x XL  and  XC  handler
for high throughput, or it can use multiple terminal service to do
all its terminal i/o.  This second option allows the  use  of  any
interface  supported,  including the PDT150 modem port, DL/DLV11's
and DZ/DZV11's.  The drawback is overhead,  the  RT11  MT  service
can't  sustain  a rate much past 1200 baud at most.  This is not a
problem for Kermit, however, due to it's half  duplex  nature  and
the  fact  that  no  packet  received is ever longer than the ring
buffer size.  The only problem is in when Kermit-11 is running  as
a  terminal  emulator  (the Kermit CONNECT command) where the data
coming from the remote host can  easily  overrun  the  executive's
buffer.   A SET RT11 [NO]FLOW command was added to force Kermit-11
to send its own flow control to the host via XON and  XOFF.   TSX+
users  can  connect  to  CL:   for dialing out, the exact means is
documented in the Kermit-11 users guide.  The  disk  i/o  emulates
the RSTS/E and RSX RMS11 version, and each executive directive has
its error codes mapped into an unique global error code, with  the
symbolic  names  corresponding  to  the  nearest RMS11 error name.
Wildcarding is handled, of course, by non  file-structured  access
to  the  directory  on  the desired volume, and supports full RT11
wildcard filenames.

Transmission of file attributes

One of the  optional  features  of  the  Kermit  protocol  is  the
ATTRIBUTE packet.  The attribute packets allow a Kermit program to
send  to  a  receiving  Kermit  information  regarding  the   file
organization,  size,  cluster/retrieval  size,  protection  and so
forth.  There is even a system  dependant  attribute  packet  type
that  can  be  used  to  transfer  things like the RMS11 IFAB (the
RMS/FCS attributes).  One of the things that two Kermits  exchange
before  any  file  transfer  is an information packet, this packet
tells the receiving Kermit about itself.  The last field  in  this
packet,  the CAPAS mask, tells Kermit if the other one can process
attribute packets.  If two  Kermit-11's  are  communicating,  they
will  find that each can do so, and the sender of a file will then
send over attribute packets indicating the need (or lack  of)  for
binary  transmission, based on the file organization, filetype and
protection code (for RSTS/E).  If the sending Kermit-11 is running
on  RSTS/E,  RSX11M/M+  or  P/OS  it  will also send a copy of the
RMS/FCS attributes so the received file will be identical (to  FCS
and/or  RMS)  to  the  copy  on  the sender's system.  Since other
implementations of Kermit may use this  special  system  attribute
packet,  Kermit-11  always  sends  an attribute packet telling the
receiver what hardware and operating system it is running on,  and
thus  will  only use such data if they are compatible.  Of course,
there will be times when a file may be binary and Kermit-11  can't
tell  so,  many Kermit's have a SET FILE BINARY and SET FILE ASCII
to allow the user to override defaults.  Kermit-11 also has a  SET

                                                                Page 4


FILE  AUTO/NOAUTO  to disable it from trying to determine a file's
binary status.

Future directions

With  the  advent  of  packet  switched  networks  and   satellite
communications  the  Kermit  protocol  will  likely be extended to
increase efficiency over such links.  The main problem is the half
duplex  nature  of Kermit, the packet acknowledgements can take up
to several  seconds  in  transit  thus  drastically  reducing  the
throughput.   There are several possibilities under discussion and
a standard should be appearing shortly.

                                                                Page 5


Summary

 This article describes only the PDP-11 Kermit-11  implementation,
for further reading see:


Kermit: A File-transfer Protocol for Universities 
Frank da Cruz and Bill Catchings
BYTE Magazine, June/July 1984

The Kermit Protocol Manual, version 5
Frank da Cruz   April 1984
Columbia University Center for Computing Activities

Information on obtaining Kermit:

KERMIT Distribution
Columbia University Center for Computing Activities 
7th Floor, Watson Laboratory
612 West 115th Street
New York, N.Y.  10025

Kermit is also usually found on the Decus symposia SIG tapes.
Kermit-11 is available from DECUS as number 11-731

Digital hardware that Kermit is currently available for:

                 Operating  Program   
Machine          System     Language     Contributor
     
DEC PDP-11       MUMPS-11   MUMPS-1982   Cornell U
DEC PDP-11       RSTS/E     Macro-11     U of Toledo
DEC PDP-11       RSX-11/M   Macro-11     U of Toledo
DEC PDP-11       RSX-11/M+  Macro-11     U of Toledo
DEC PDP-11       RT-11      Macro-11     U of Toledo
DEC PDP-11       RT-11      OMSI Pascal  U of Toronto
DEC PDP-11       TSX+       Macro-11     U of Toledo
DEC PDP-11       Unix 2xBSD C            Columbia U
DEC PDP-11, ...  Unix V7    C            Columbia U
DEC PDP-8        OS8, RTS8  PAL-8        R. Hippe
DEC Pro-3xx      P/OS       Bliss, Macro Stevens I.T.
DEC Pro-3xx      P/OS       Macro-11     U of Toledo
DEC Pro-3xx      Pro/RT     Macro-11     U of Toledo
DEC Pro-3xx      Venix V1   C            Columbia U
DEC Pro-3xx      Venix V2   C            Columbia U
DEC Rainbow      CPM86      ASM86        Columbia U
DEC Rainbow      MS-DOS     MASM         Columbia U
DEC Rainbow      QNX 1.x    C            Merrell-Dow
DEC VAX          Ultrix-32  C            Columbia U
DEC VAX          VMS        Bliss,Macro  Stevens I.T.
DEC VAX          VMS        C (VAX-11 C) Columbia U
DEC VAX          VMS        Pascal       U of Toronto
DEC VAX, ...     Unix 4xBSD C            Columbia U
DEC VT-180 Robin CPM80      Turbo Pascal Jeff Duncan
DEC VT-180 Robin CPM80 2.2  M80,LASM     ACC

                                                                Page 6


DECmate-II,III   CPM80 2.2  M80,LASM     ACC
DECsystem-10     TOPS-10    Bliss, Macro Stevens I.T.
DECSYSTEM-20     TOPS-20    MACRO-20     Columbia U