This is VFY.DOC
 
    VFY  --  DISK VERIFICATION UTILITY  V01.1  --  PROGRAM DESCRIPTION
 
    Program to VeriFY the VOLUME_ID and OWNER of a disk pack
 
    Author:	LARRY OWENS  -  6/MAR/82
    Last edit:	Larry Owens, 20/Jun/83 - Fix "clean" exit to allow REEnter
    System:	RT-11 v4 (?v3)
 
    The purpose of this utility program is to allow the user to view and/or
    verify the VOLUME_ID and OWNER of a random-access device. This utiltiy
    accepts a standard CSI command line which consists of one input device
    specification and three optional switches. The general command line is:
 
 	*[ddu:][/V][/O][/Q]
    	   1     2   3   4
 
    Where:  1 is the random-access DEVICE specification
 	    2 is the VOLUME_ID VERIFICATION switch
 	    3 is the OWNER VERIFICATION switch
    	    4 is the QUIET MODE switch
 
    You will note that there are no mandatory fields; all four
    of these fields have default values. These defaults are:
 
    1)	The default value for the DEVICE field is "DK:". NOTE: there is no
 	filespec associated with this field. This is because this utility
 	does a non-directory structured open for the device and then reads
 	two 12-byte fields, containing the VOLUME_ID and OWNER data, at a
 	fixed offset from the beginning (absolute block 0) of the device.
 	If the user does specify a filespec in this field it is ignored.
 
    2)	The VOLUME_ID switch requests a verification of the VOLUME_ID data
 	stored on the DEVICE (3) specified. If the VOLUME_ID switch is
 	specified (/V) then this utility will prompt the user for the value
 	to be compared with the data stored on the DEVICE (3) specified. If
 	the two match exactly, then the verification is successful. Otherwise,
 	the verification is not successful, and this utility will output the
 	message "VFY-F-Volume ID Verification Error" followed by a Severe
 	Error type exit. The VOLUME_ID field is 12 characters long and may
 	contain embedded ASCII spaces. If the user does not specify a full
 	12 character value, then this utility will fill the remaining
 	characters with ASCII spaces (this mimics the action of DUP with
 	the INIT/VOLUME command). Note that this implies that a null string
 	specification will be expanded to a value of 12 ASCII spaces (again,
 	just like DUP). If the user specifies more than 12 characters, then
 	the user is informed of the error and reprompted for the value.
 
    3)	The OWNER switch operates just like the VOLUME_ID switch except that
 	it requests a verification of the OWNER data stored on the DEVICE (3)
 	specified. If a verification is not successful, then the message
 	"VFY-F-Owner Verification Error" will be output followed by
    	a Severe Error type exit.
 
    4)	The QUIET switch disables the display of the VOLUME_ID and OWNER data
 	retreived from the input DEVICE (1). The default mode is NOQUIET, in
 	this case the data retreived from the input device is displayed on
 	the console for the user to view. Any warning and/or error messages
 	will always be displayed, regardless of the QUIET (/Q) switch option.
 
    This utility gets its input via .CSISPC and .GTLIN commands, and therefore
    can be run from Indirect Command Files. (Actually this was the original
    intent. I needed a method of verifying disks prior to executing indirect
    commands that resulted in the destruction of data/programs. The Severe
    Error exit stops any .COM process [except if SET ERROR NONE is currently
    in effect].) Like other system utilities, when activated from indirect
    command files, if there is no input-line currently available in the body
    of the indirect command file (i.e. the "^C" option) one will be collected
    from the console terminal.
 
    Examples:	*RK3:/V/O			! Verifies that RK3: has
    		Volume ID ? >DEVELOPMENT	! Volume ID "DEVELOPMENT "
 		Owner     ? >LARRY		! and Owner "LARRY       "
 		Volume ID = "DEVELOPMENT "	! and displays the values
 		Owner     = "LARRY       "	! set for device RK3:
 
    		*DL1:/V				! Verifies that DL1: has
    		Volume ID ? >SYSTEM DISK 	! Volume ID "SYSTEM DISK "
 		Owner     ? >O.C.S. - 005	! and Owner "O.C.S. - 005"
 		Volume ID = "SYSTEM DISK "	! and displays the values
 		Owner     = "O.C.S. - 005"	! set for device DL1:
 
    		*/O/Q				! Verifies that DK: has
    		Owner     ? >LARRY		! OWNER "LARRY       "
 
    		*.NEW=				   ! Generates warning message
 		VFY-W-Output Specification Ignored ! about illegal output spec
 		Volume ID = "DEVELOPMENT "	   ! and displays the values
 		Owner     = "LARRY       "	   ! set for device DK:
 
 		*/Q				! No verification nor display