DIGLIB version 3.2 should be the final release of DIGLIB, but I'm
sure it won't be.  The only changes that forseen will be the addition
of new device drivers and bug fixes.  The bug fixes will be denoted
with a letter following the version number and starting with the
letter A.



                       CHANGES FROM V1.x TO V2

     1.  DIGLIB will no longer die when MAPIT is fed negative numbers
         or zero as the limits of a log axis.  However, the results
         may not be satisfying but "garbage in yields garbage out".

     2.  DIGLIB will no longer die when SCALE is fed negative or zero
         world coordinates for log axes.  Again "garbage in yields
         garbage out".

     3.  MAPIT has been highly modified internally.  It still provides
         the same user interface as before, but now draws things in a
         different order.

     4.  MAPIT will now allow for linear axes to end on non-tickmark
         boundaries.  This is independently controllable for each
         axis.

     5.  MAPIT will optionally reproduce the Y axis at the right of
         the plotting area complete with tick marks, but without tick
         labels.

     6.  MAPIT will optionally reproduce the X axis at the top of the
         plotting area complete with tick marks, but without tick
         labels.

     7.  A new subroutine has been added called MAPSML.  MAPSML is
         MAPIT with most of the versatility of MAPIT commented out.
         The new enhancements to MAPIT have probably caused it to
         grow.  MAPSML is offered to users who don't need the full
         MAPIT and who need space badly.  (Any VAX user using MAPSML
         doesn't know what a VAX is.)

     8.  A new subroutine called MAPSET has been added to DIGLIB.
         MAPSET is quite similar to MAPPRM.

     9.  MAPSIZ, MAPSZ2, PLTBOX, and PLTBX2 now assume 80 lines to the
         screen instead of 40 lines.  The net effect is that the
         characters don't get big until the physical size of the
         graphics device is quite large!

    10.  A new function called GSLENS has been added to DIGLIB.
         GSLENS will return the length of its argument (of string
         type) in virtual coordinates based upon the current character
         size.  This is handy for centering strings and the like.

    11.  To promote the use of RLSDEV, the 4025 and 4027 drivers no
         longer delete the workspace and graphics area on RLSDEV.  It
         is now the users responsibility to do this.

DIGLIB V3.2 RELEASE NOTES                                                 Page 2


    12.  The file LINLAB.ENG contains an alternate linear tick
         labeling package for DIGLIB.  Since LINLAB.ENG uses FORTRAN
         ENCODE statements, the package can't be used with OMSI PASCAL
         programs.  Personally, I wouldn't use it, but if your users
         want tick labels in "scientific notation" and no remote
         exponent, then LINLAB.ENG is for you.

    13.  DIGLIB/RSX and DIGLIB/VAX are now distributed with
         STRINGLIB.OLB!  This library contains subroutine/functions
         for zero byte terminated variable length strings!  They
         behave exactly(?) like their RT-11 SYSLIB counterparts.
         Hopefully, any code that uses the RT SYSLIB string
         subroutines/functions should also work under RSX and VMS!
         The supported subroutines/functions are:  CONCAT, GETSTR,
         INDEX, INSERT, ISCOMP, IVERIF, LEN, PUTSTR, REPEAT, SCOMP,
         SCOPY, STRPAD, SUBSTR, TRANSL, TRIM, and VERIFY.  In
         addition, Hal has included two extra string subroutines that
         have proven very useful.  They are:  SGLUE and STRPBL.  See
         STRINGLIB.DOC for more information on STRINGLIB.

    14.  DIGLIB is now distributed with PURJOY and CONTOR.  These
         subroutines are not documented in DIGLIB.DOC, but have pretty
         good documentation in the code files.  PURJOY is a 3D surface
         drawing subroutine (with hidden line elimination).  CONTOR is
         a contour surface drawing subroutine that has a very similar
         calling sequence to PURJOY.  The test programs TEST3D and
         TESTCN have also been included in the distribution to provide
         a test and demonstration of PURJOY and CONTOR respectively.
         Please note that neither PURJOY nor CONTOR is compiled or
         inserted into DIGLIB by the installation procedure.  If you
         want this done, you must do it manually after the
         installation procedure is complete.  Also, CONTOR will
         produce warning errors under RT-11 (TSX).  These can be
         ignored!

    15.  DIGLIB now has easy bar graph capability with the addition of
         BARGRA.  This subroutine written and donated by Joe Garbarini
         is well documented in the comments at the beginning of the
         file.  Please note that BARGRA is neither compiled nor
         inserted into DIGLIB by the installation procedure.  If you
         want this done, you must do it manually after the
         installation procedure is complete.  Also, note that Hal
         Brand is supporting BARGRA, so do not bug Joe Garbarini about
         bugs!



                       Changes from V2 to V2.1

     1.  The high level clipping mechanism was removed.  The low level
         clipping mechanism was modified to be more general, and so
         now it handles all clipping.  This was simplier and more
         efficient that fixing the bug in the high level clipper.  My
         thanks to Joe Garbarini to bringing this bug (which has
         existed since V1) to my attention.

DIGLIB V3.2 RELEASE NOTES                                                 Page 3


     2.  DIGLIB is now distributed from a VAX without going through a
         PDP-11 intermediate for the RSX and RT/TSX versions.  This
         should allow me to make updates faster!



                       Changes from V2.1 to V3

     1.  MAPIT now allows the caller to suppress the tick mark labels.
         This can be useful when many plots need to be stacked on top
         of each other and the X axis tick labels are unnecessary and
         only clutter the plot.

     2.  The values stored in the common block PLTCLP are slightly
         different, and are no longer used at all by DIGLIB, but are
         still set by MAPIT, MAPSML, and SYAXIS

     3.  The subroutine CURSOR now returns the GIN character as type
         BYTE instead of type INTEGER to be consistant with GSGIN.

     4.  Polygon fill has been added to DIGLIB.  This is supported at
         the lower levels via GSFILL and GSPOLY which work in virtual
         coordinates and provide only solid fill.  DIGLIB V3 provides
         for hardware fill of polygons when available.  The GSFILL
         will use hardware fill when available, and software fill when
         necessary.  A higher level routine, HATCH, does software
         fills for the more general case of multiple polygons, filled
         with lines running at any angle with any spacing.  HATCH can
         use world coordinates or virtual coordinates, and can be
         called multiple times to provide "cross-hatching".

     5.  Several functions were added to DIGLIB to make often
         used/needed constants and parameters easier to access, and to
         make character plotting sequences much easier.  These routine
         are:  GSWDTH, GSHGHT, GSLENS, GSSLEN, GSXLCM, and GSYLCM.
         Note:  GSWDTH and GSSLEN have been removed in V3.1!

     6.  Device drivers written for DIGLIB V3 are not compatable with
         previous versions of DIGLIB and vise-versa.  Sorry about
         that.  However, the changes to make a DIGLIB V2.1 device
         driver compatable with DIGLIB V3 are very simple.  First, the
         device driver must return a error status on IFXN=1
         (Initialize the Device) in YA(1).  The defined error codes
         are given in DRIVRS.DOC.  This allows programs to gracefully
         handle shared devices - and not crash on account of the the
         graphics device driver.  The second difference is that DIGLIB
         V3 drivers return 8 device characteristics words instead for
         7.  The 8th word is described in DRIVRS.DOC.  Making this
         change is optional because the 8th word is defaulted by
         DIGLIB V3.  The third difference has to do with improved
         handling of clipping by DIGLIB.  Now, the second and third
         device characteristics words are directly back-calculated
         from the device resolution and maximum addressable points
         without the need for the fudge factor of 0.5 that was added
         to the maximum addressable point values.

DIGLIB V3.2 RELEASE NOTES                                                 Page 4


     7.  The VAX/VMS graphics terminal device drivers no longer use
         "pass-all" mode.  Thus, hopefully you can always use CRTL/Y
         to kill your image.  (SLIDE/VAX requires DIGLIB V3.)

     8.  The DIGLIB documentation was improved and re-organized.

     9.  DIGLIB grew to requiring two floppys for distribution.

    10.  DIGLIB was modified to be easier to transport to non-DEC
         systems.  The major transportability issues remaining are
         device drivers and the use of "strings".

    11.  Elementary windowing/viewporting was added to DIGLIB.  The
         capability was always there, but it was not easy to use, nor
         was it documented well.  Windowing/viewporting can aid users
         migrating graphics routines from other graphics packages.
         See the subroutine description of GSWNDO for more
         information.

    12.  User selectable line styles were added to DIGLIB.  Now the
         user can override any or all of the 3 broken line styles
         supplied by DIGLIB.  In addition, the construction of line
         styles is now done in absolute coordinates instead of virtual
         coordinates.

    13.  The DIGLIB.NAM file has been dropped.  You can still create
         and use it if you liked it, however, DIGLIB now defines a
         subroutine GSDNAM that returns the device name as a string
         given the DIGLIB device number.  GSDNAM is bundled with
         GSDRVR, and thus provides a more flexable environment,
         especially for those with multiple DIGLIBs or multiple
         GSDRVRs.

    14.  A subroutine called SELDEV is distributed with DIGLIB V3 that
         gives an example of how to use GSDNAM.  SELDEV presents the
         user with a crude menu of the device drivers, gets the user's
         choice, and verifies that the device is available and will
         properly initialize.  This is more important to RSX and VMS
         people, as shared devices, or off-line devices can be
         unavailable.

    15.  A new graphics input mode was added to provide more
         reasonable support for graphics devices that have pointing
         devices with buttons.  The new routines are GSCRSR, GSINPT,
         and GRAFIN.



                       Changes from V3 to V3.1

     1.  The functions GSWDTH and GSSLEN have been removed.  Use only
         GSLENS.

     2.  Alternate (high quality Hershey) fonts have been added to
         DIGLIB/VAX.  The GSFONT subroutine is used to select the
         current font.  (GSFONT is included in the RT/TSX/RSX versions
         of DIGLIB, but does nothing, it is only there for

DIGLIB V3.2 RELEASE NOTES                                                 Page 5


         compatibility.) The alternate fonts are loadable, and are
         loaded the first time they are selected.  GSFONT is capable
         of loading up to 98 fonts (2 thru 99), but the currently
         allocated table space is only adequate for the 9 fonts
         provided with DIGLIB/VAX.  To make the tables larger, just
         change the parameters in GCFONT.CMN.

     3.  MAPIT, MAPPRM, and SYAXIS have all been modified to allow use
         of the alternate fonts.  However, unless the target graphics
         device has around 1000x1000 resolution, use of the alternate
         fonts is not recommended.

     4.  DIGLIB no longer comes in a UNIX version.  Its still
         possible, but the FONT stuff will need work and nobody here
         cares.



                      Changes from V3.1 to V3.2

     1.  Drivers can no longer call GBSENDTTY, but now must call
         GBSENDCHARS instead.  Failure to do so may cause crashes.

     2.  All references to the infamous PLTLIB manual have been
         deleted from the documentation.  I was getting tired of
         explaning how you don't need it!

     3.  Bugs were removed from CONTOR and MAPPRM.

     4.  Version 3.2 was designed for release to NESC and DECUS.