Structured Programming in Macro-11:
                       SUMAC Structured User Macros

                               by Bob Schor

                              February, 1987
                     Updated December, 1988; May, 1989


     The "structured programming" revolution has as its most visible
manifestation the increasing popularity of simple Algol-like languages, of
which the author's favorite is the language Pascal.  These languages all
embody certain key concepts.  At one end is the notion of "top-down
design", in which programs are conceived in large blocks (e.g. inputdata;
performcomputations; writereport); each block, in turn, is broken up into
simpler blocks, which are broken up into still simpler blocks, and so on
until the inner most block is reached whose function it is to perform one
elementary, easily-understood (and debugged!) operation.  At the other end
is the notion of program control, or "GOTO considered harmful", which
structures code in terms of loops (WHILE, REPEAT, FOR), conditional
branches (IF, CASE), procedure and function calls, and sequential
operations.

     A number of attempts have been made to bring some of the benefits of
structured programming, particularly the simple control structure and the
top-down block concept, to the programmer who must interact intimately with
machine hardware, the traditional habitat of the machine language
programmer.  Examples of such languages are C, Modula, and perhaps Ada.
However, these languages are often deeply embedded in specialized
programming environments, and are not included in the typical bundled
software package from the computer's manufacturer.

     What typically is provided, however, is an assembler with the ability
to construct "macros", or "macro-instructions", new user-defined
instructions outside the normal instruction set of the hardware.  By
defining a suitable subset of these macros, it is possible to thereby
define such items as WHILE loops, IF statements, and block structures.

     One such package, designed for the Digital Equipment Corporation
Macro-11 assembler for the PDP-11 series of computers is SUMAC, described
herein.  Versions of this package have been written for the DEC operating
system RT-11 and for the time-sharing system TSX (S&H Computers).  The
macros should largely be compatible with RSX, with the exception of the
terminal output routines.

     The SUMAC package uses standard PDP-11 mnemonics for much of the
sequential coding, so that a program written using these macros retains
much of the appearance of a Macro-11 program.  It will be assumed that the
reader has familiarity with PDP-11 assembly programming, though no
familiarity with writing and using macros themselves will be necessary.
The macros in this package are used to provide a certain amount of


                                - 1 -



Macros for Structured Programming


structure to the assembly program, which is then assembled in the normal
manner (adding that SUMAC is to be used as a supplemental macro library).
Examples will be given below.

     Structured languages like Pascal achieve block structure by use of
PROGRAM, PROCEDURE, and FUNCTION blocks, which have variables local to
their blocks, and which can contain their own (local) PROCEDURE and
FUNCTION blocks.  Such nesting of blocks, and definition of local
variables, are not explicitly provided by this macro package.  Block types
provided are the PROCED and TASK blocks.  The PROCED block is functionally
equivalent to a well-structured procedure, in that it is entered as a
subroutine at the top, and left at the bottom after the final instruction
in the block is executed.  Pascal procedures contain a mechanism for
passing arguments into and out of the routine -- functions, in fact, can be
simply considered procedures which return a value to an external argument.
Two mechanisms exist in SUMAC for passing arguments.  One method uses the
method employed by RT-11 Fortran, in which the argument addresses follow
the subroutine call, and the called routine can look backward to find the
arguments.  Advantage of this method is that it is Fortran-compatible,
meaning that you can call Fortran subroutines using this type of call, as
well as write routines which are called by Fortran.  The other method is to
follow the Pascal route of putting the arguments on the stack.  The
advantage of this method is that procedures can now call themselves (or be
recursive), since the arguments do not live in fixed memory locations; the
trade-off is that stack clean-up procedures are needed.

     The other type of block is the TASK block, which is reserved for
interrupt service routines.  Such a routine can be considered a special
type of procedure -- it is also entered at the top and exited at the
bottom, like a normal routine, but doesn't usually have "arguments" in the
usual sense.  Rather it usually manipulates some global values, such as
filling a buffer, setting and clearing software flags, etc.  Another
difference between normal and interrupt routines is that interrupts occur
asynchronously, that is, they can occur at any time in the program, so they
aren't called from any fixed place.  Thus a mechanism must be found to
return to precisely the spot in the program at which the interrupt
occurred.  The exit from the TASK block automatically takes care of this.

     Within blocks, or within sections of the main program, macros exists
for providing control of program control.  Many of these macros will look
familiar to the Pascal programmer, such as WHILE, REPEAT, IF, ELSE, and
CASE.  The similarities are deliberate, but some differences exist in their
application.

     These program-control macros define a section of code which is to be
executed under a specific set of conditions:  WHILE a condition is true, IF
a condition is true, or REPEATed UNTIL a condition is true.  These macros
define the beginning of the code to be executed; another macro, usually
some form of END (such as ENDIF, ENDCASE, etc.), is required to signal the
end of the block of code.  For example, the IF macro has the form




                                - 2 -



Macros for Structured Programming


        IF      arg1, cond, arg2   ; e.g.     IF      r0, lt, r1
                stmt1
                stmt2
                 ...
                stmtn              ; code to be executed if true
        ENDIF                      ; macro to end block of code
The section of code, which can be ordinary Macro-11 code or further SUMAC
macros, will be executed (if the test specified in the statement is true)
until the ENDIF statement is reached, signalling the end of the block.  If
the test in the IF statement is false, none of the statements between IF
and ENDIF are executed.

     For correct operation, a macro which starts a block (such as IF, CASE,
etc.) must have a corresponding form of END statement.  Although the
present version of the macro package doesn't contain code to specifically
ensure that an ENDIF matches an IF, an UNTIL a REPEAT, some error checking
is built-in.  Blocks declared as PROCED or TASK blocks, which correspond to
procedures (subroutines) and interrupt service routines, do contain code to
check that within the block, there are neither too many nor too few END
macros.  In a well-written structured program, most code will be bracketed
by PROCED ... ENDPROC or TASK ... ENDTASK macros, so most mismatch errors
should be caught.  Two further checks are made.  If the number of END
macros ever exceeds all the previous block-originating macros, an error is
generated.  Finally, an ENDEND macro is provided, which belongs at the end
of the program, to ensure that no ENDs are missing.

     The PDP-11 instruction set contains both word-oriented and
byte-oriented instructions, such as "TST" and "TSTB".  Similarly, both word
and byte versions of several of the macros have been provided (e.g. IF and
IFB).  The byte versions share the same name as the word version, with a
"B" tacked on the end; the operation of the two forms of the macro is the
same, except the byte form expects its operands to be bytes, and will use
PDP-11 byte instructions in dealing with these operands.

     Control blocks which test conditions (such as IF, WHILE, REPEAT/UNTIL)
can have the initial test extended by AND or OR (and byte version) tests.

     A number of macros have been provided as utility macros.  These
include the macros which facilitate Fortran-style subroutine calls and
argument retrieval, along with  macros to convert Fortran array indices
(from 1 .. N bytes, integers, or reals) into an appropriate offset for
indexing into the actual array.  A second set of macros facilitate using
the stack by providing convenient mechanisms for pushing and popping an
arbitrary number of arguments.

     Macros are also provided for debugging and program checking.  This
includes the ENDEND macro mentioned above, which makes sure enough END
macros have been specified.  To permit typeouts of messages, a NOTE and
PNOTE macro are provided.  CHECK will output the value of any variable,
both in octal and as a signed integer.  The ASSERT macro can be used to
make sure that at run time, certain conditions are true -- if the
assertions are ever violated, the false assertion, and the values of the


                                - 3 -



Macros for Structured Programming


variables which caused it to fail, will be output.

     Before getting into a detailed description of the macros and their
usage, a few notes on implementation and addressing mode restrictions.
Most of these macros allow any sensible addressing mode to be used, but
caution should be exercised when using stack addressing (remember some
macros, such as PUSH and POP, change the stack).  Also note that if
auto-increment or decrement modes are used, the registers involved will be
modified when the macro is executed.

     To include the SUMAC package in a Macro-11 program, the macro names
have to be defined using the ".mcall" statement.  This is accomplished by
using the SUMAC macro, which defines the entire package, and initializes
certain internal variables.  The form of this macro, which must be the
first SUMAC macro used in the program, is
        .mcall   SUMAC
        SUMAC

     A recent change (creating version 9.05) was to attempt to ensure that
code generated by SUMAC is "pure", or suitable to be placed in an I-Space
"instruction" program section.  Three of the macros build data tables --
CASE builds a jump table, which is now placed in a data .psect named
$CASE$; NOTE and PNOTE place strings in $TEXT$; FCALL (the FORTRAN call
macro) builds its argument list in $DATA (where F4 normally placed them).
Another minor change in this version was to remove an "illogical" (i.e.
inconsistent) form of the PNOTE macro.

     SUMAC is constantly being maintained and upgraded by Bob Schor.  A
symbol, ".suver", has been added which encodes the current "version" in
decimal (presently, .suver = 905., meaning version 9.05).


                                RT-11 notes

     The macro package can be examined and modified by simply editing
SUMAC.MAC.  Note, however, that any changes to the package must be made
with care to avoid inadvertantly destroying other sections.  Furthermore,
support cannot be offered for changes made without the author's knowledge
and authorization.  The source, when provided, is mainly for the
edification of the advanced system programmer, who may need to know the
internal workings of the package in order to untangle a complex coding
error.

     A few changes were made to Macro-11 when Version 5 of RT-11 was
announced; the two that matter are that lower case characters are now
acceptable in macro definitions, and that the default extension for macro
libraries is ".MLB".  If you choose to use SUMAC with earlier versions of
RT-11, you should take these changes into account.

     The macro library is constructed from the source version by using the
librarian.  To build a stand-alone macro library (the recommended
procedure),


                                - 4 -



Macros for Structured Programming


        LIBRARY/MACRO SUMAC SUMAC
will construct a macro library, SUMAC.MLB from the source SUMAC.MAC (for
RT-11 Version 5 and later).  To now assemble a program, say the
demonstration program SUTEST.MAC using the macro library,
        MACRO SUTEST+SUMAC/LIB
With the RT-11 version 5 indirect command file, one could define an
indirect command which accepts an argument (SUTEST) and executes the above
string.

     Another possibility is to incorporate the structured macros into the
system macro library, SYSMAC.SML.  This procedure is not recommended, as
the contents of this DEC macro library are subject to change, and monkeying
with it is probably not advisable.

     RT-11 version 5 also provides the .library command, which causes
external libraries to automatically be searched.  Thus if SUMAC.MLB is on
device SY:, the Macro directive
        .library        /SY:SUMAC/
will cause SUMAC to automatically be searched for the required macros.
This means that the simple form of the MACRO (or COMPILE )statement will
work, i.e. you can say simply
        MACRO SUTEST
or
        COMPILE SUTEST.

     The message output macros (NOTE, CHECK) make use of the standard RT-11
system macros .TTYOUT and .PRINT.  However, the macros have been coded so
that the user does not have to worry about register saving and restoring
(it is all done internally).


                                 TSX notes

     The macro package for TSX is identical to that for RT-11, and is used
in exactly the same way.  A useful command file for SY: is SUMAC.COM, which
consists of the following --
        COMPILE ^1+SY:SUMAC/LIB
which is just the command required to implement a command suggested above
for automatically invoking the macro package.  Thus you would say
        SUMAC SUTEST
to compile the demonstration program under TSX.

     TSX's real-time features make certain restrictions on interrupt
service routines, namely that they must dispatch through the monitor via an
"RTS PC" rather than directly via an "RTI".  To force this change, the
symbol "$TSX" must be defined as a non-zero quantity.








                                - 5 -



Macros for Structured Programming


                    SUMAC macros, and calling sequences

1.  Enabling macro

SUMAC

     When invoked, this macro will ".mcall" all the rest of the macros in
the package, and will perform necessary initialization.  This macro should
be the first structured macro used in the program.

        .mcall  SUMAC           ;include SUMAC as external library
        SUMAC                   ;initialize macro package

     Note that as of RT-11 Version 5, macro libraries such as SUMAC can be
automatically searched by means of the .LIBRARY command.  Thus if SUMAC.MLB
was located on device SY:,

        .library        /SY:SUMAC/

would cause SY:SUMAC.MLB to be searched for undefined (SUMAC) macro names.


2.  Loop macros

WHILE, WHILEB, ENDWHILE

     The WHILE macro takes up to three arguments, which are used to form a
test which must be true in order to execute the code contained in the block
(i.e. all code between the WHILE and its terminating ENDWHILE macro).  Each
time the block of code is executed, the program will loop back to the
beginning and again test the condition specified by the WHILE macro,
exiting only when the condition is false.  Note that if the condition is
false on entry, the code within the block is never executed.

     The form of the test for the WHILE macro is similar for several of the
other macros, and will be described in detail here.  The most general form
of the macro is illustrated by the three-argument form,

        WHILE   r1, lt, r2

which executes the loop while the relationship between the two arguments is
true, in this case while the contents of r1 are less than those of r2.  The
two-argument form, illustrated by

        WHILE   (sp)+, ne

has an implicit second argument of zero, so the above will execute while
the top value on the stack is non-zero.  Note that this particular example
has a side-effect (dangerous, in general) of changing the value of the
stack pointer, similar to a POP.  Finally, the one-argument form,

        WHILE   cs


                                - 6 -



Macros for Structured Programming



can be used to test a condition code, resulting from some previous
operation.

     Any of the standard PDP-11 branch mnemonics (without the "b") can be
used as the "test" -- "eq", "ne", "mi", "pl", "cs", "vs", "cc", "vc", "lt",
"ge", "le", "gt", "hi", "los", "his", "lo".


FOR, ENDFOR

     This macro defines a counting loop, similar to the Pascal FOR or
Fortran DO statement.  The macro takes three or four arguments, and has the
following form --

        FOR     r0, #1, (r2)

The effect of this loop is to assign to the first argument (which must be
an assignable variable) the value specified in the second argument.  Thus,
in the example above, the number 1 is placed in r0.  Then a (signed)
comparison is made with the third argument (in the example, the value in
r1, the number 1, is compared with the value contained in the address held
in r2).  If the variable is less than or equal to this final value, the
code within the block (i.e. up to the matching ENDFOR macro) is executed,
and the variable (r0) is incremented by 1, tested again, and so on until
the variable exceeds the final value.  Note that if the initial value
exceeds the final value, the loop is never executed.  Also note that within
the loop, the value of the controlled variable (the first argument) is
defined by the loop, and should not be changed within the loop.  At the end
of the loop, however, it should be assumed to be undefined, and its value
unspecified (conforming to often-ignored Pascal and Fortran rules).

     The three-argument form of this macro, illustrated above, uses a
default loop increment of 1.  An optional fourth argument can be used to
specify a different increment, which can be positive or negative.  If a
negative argument is used, the sense of the tests are reversed, so that the
loop executes as long as the controlled loop index (the first argument) is
greater than or equal to the final loop value (argument 3).  Thus to
execute the loop illustrated above, but with the values running backwards,

        FOR     r0, (r2), #1, #-1

is appropriate.


REPEAT, UNTIL, UNTILB

     A REPEAT loop is very similar to a WHILE loop, except that the test is
made at the end of the loop, guaranteeing that the code within the loop
will be executed at least once.  Also, the WHILE loop executes as long as
some condition is true, so that at the end of the loop, you know the
condition is false; at the end of a REPEAT loop, however, the guarding


                                - 7 -



Macros for Structured Programming


condition in the UNTIL clause is true.  The REPEAT macro takes no
arguments; the UNTIL macro takes one to three arguments, analogous to the
WHILE macro.  Thus a typical loop might look like

        REPEAT
                mov     (r1)+, (r2)+    ;move a word
        UNTIL   (r1), eq                ;until 0 encountered

     An additional form of the UNTIL loop is also provided -- if no
arguments are present, the (missing) test will never succeed and the
REPEAT/UNTIL structure will become an endless loop.


3.  Conditional macros

IF, IFB, ENDIF

     The IF macro takes one to three arguments, like the WHILE macro.  If
the test is true, the code block within the macro is executed once; if the
test is false, the code is skipped and not executed.  This macro is
terminated with either the ENDIF, ELSE, ELSIF, or ELSIFB macro (see below).


ELSE

     Using the ELSE macro to terminate an IF block starts another block,
terminated by an ENDIF macro, which contains the code executed if the test
specified by the IF macro is false.  Note that the ELSE macro should be
used when two different actions are required, one if a condition is true,
and another if the condition is false.  If only a single action is
required, a simple IF .. ENDIF block should suffice.  For example, suppose
you wanted to push the larger of two arguments onto the stack.  Then you
might say

        IF      r1, ge, r2
                PUSH    r1      ;r1 >= r2, push larger
        ELSE
                PUSH    r2      ;r2 larger
        ENDIF

Note that the IF macro code is terminated by ELSE, which starts its own
block that is, in turn, terminated by ENDIF.


ELSIF, ELSIFB

     If the first IF fails, code in the ELSE .. ENDIF block will be
executed.  The ELSIF (or ELSIFB) macro combine the ELSE and IF (or IFB)
macros, allowing a test to be included in the ELSE block without another IF
.. ENDIF pair.  The two sections of code below have the same effect.




                                - 8 -



Macros for Structured Programming


        IF      r1, ge, r2                IF      r1, ge, r2
                PUSH    r1                        PUSH    r1
        ELSE
                IF      r1, ge            ELSIF   r1, ge
                        PUSH    r2                PUSH    r2
                ELSE                      ELSE
                        PUSH    #0                PUSH    #0
                ENDIF
        ENDIF                             ENDIF

ELSIF blocks, like IF blocks, can be terminated by ELSE, ENDIF, or another
ELSIF.


IFSTR

     Another specialized version of IF is used for comparing two strings of
characters (bytes).  A string is defined as a sequence of bytes, each of
which is assumed to hold an ascii character.  Strings either have a
specific defined length, or else can be defined as having an unspecified
length, but being terminated with a null (0) byte.  If the strings have a
defined length, then the form of the macro is

        IFSTR   #stra, eq, #strb, #length
                code-if-strings-match
        ELSE
                code-if-strings-do-not-match
        ENDIF

In this example, the strings which start at addresses "stra" and "strb" are
compared byte by byte, for "length" bytes, and if each byte matches, the
first bit of code is executed, otherwise the second is performed. Note that
ELSE code can also be included.  The other form of the macro is

        IFSTR   first, le, second
                code
        ENDIF

which works by assuming that the strings are terminated by nulls.  This
particular example looks at two strings whose first word addresses are
stored in "first" and "second" (note absence of "#") and compares byte by
byte until it reaches the end of the first string.  Note that the end of
the second string itself is not noticed.  The above example can be used to
see if the string pointed to by "first" precedes alphabetically that
pointed to by "second".

     If a negative length is given, or null strings presented, the
comparison will yield equality by default.






                                - 9 -



Macros for Structured Programming


AND, OR, ANDB, ORB

     These macros can be used to extend the IF, WHILE, and UNTIL tests by
adding further conditions.  These tests are processed in the order they are
encountered.  For example, the sequence

        IF      test1
        AND     test2
        OR      test3
        AND     test4

is equivalent to the boolean test

        ((test1 AND test2) OR test3) AND test4


CASE, CASEB, ENDEL, ENDCASE

     The IF macro makes a single test, and can have at most two outcomes.
Occasionally a multi-way branch, similar to the Pascal CASE statement or
the Fortran computed GOTO, is needed.  The CASE macro provides such a
mechanism, more similar to Fortran than Pascal.  The form of the statement
is

        CASE    choice, <opt1, opt2, opt3, ... optn>
        opt1 :          code    ;executed if choice is 1
                ENDEL
        opt2 :          code    ;executed if choice is 2
                ENDEL
         ...
        optn :          code    ;executed if choice is n
                ENDEL
        ENDCASE         ;marks end of entire macro

In this macro, the first argument is the case selector -- it should
evaluate to number between 1 and the total number of case options (note
that there is nothing illegal with using immediate mode addressing, e.g.
CASE  #2, < ... >, except that such a call will always choose the same
option, in this case, the second).  The second argument consists of a list
of addresses, enclosed in angle brackets (to make the macro consider it as
a single argument).  Each address starts a case element which contains
appropriate code for that particular value of the case selector.  Each case
element ends with an ENDEL statement (it is optional, but recommended, for
the final element), and an ENDCASE is used to end the entire CASE macro.
If a null case option is present, for example

        CASE    select, <a, b, , d>

it will be interpreted to mean "do nothing" if selected (in the example
above, if select evaluates to 3, no code will be executed, and the whole
CASE statement up to the ENDCASE will be skipped).  In addition, should the
case selector evaluate to 0, a negative number, or to a number larger than


                                - 10 -



Macros for Structured Programming


the highest option, no option will be selected and the CASE skipped.

     A note of caution -- this macro requires specifying addresses to
define the options.  If you want to use local symbols such as 1$, 2$, etc.
for the option labels, then you must enable a local symbol block around the
CASE statement, as the statement itself generates its own symbols.  For
example,

        .enabl  lsb             ;extend scope of local symbols
        CASE    choice, <1$, 2$, ...>
        1$ :            code
                ENDEL
        2$ :        ...
                ENDEL
        ENDCASE         ;end of CASE macro
        .dsabl  lsb             ;restrict local symbol scope



4.  Block definition macros

PROCED, QUIT, ENDPROC

     The PROCED macro defines a procedure, a set of code which can be
considered as a subroutine, which is called through one of several means at
various points in the program, and which returns to the statement following
the calling statement at its termination.  Methods exists to pass arguments
back and forth across procedure boundaries, but they are not specified by
the PROCED macro; it is the programmer's responsibility to know where and
how arguments are passed, and to program accordingly (see below, the
Fortran-compatible macros; also see the examples in the demonstration
routine).

     The macro has an argument which will be used as a label to define the
entrance to the procedure.  Additional code in the macro causes a box to be
generated in any listing file with the name of the procedure inside it.  An
additional second argument, a string enclosed in angle braces, may also be
specified.  If so, it causes a subtitle to be generated using the procedure
name and the specified string.  Thus

        PROCED  sub, <Demonstration subroutine>
                code
        ENDPROC         ;will expand as RTS PC

will cause the label "sub" to be generated, will make a listing file look
like








                                - 11 -



Macros for Structured Programming


   PROCED sub, <Demonstration subroutine>
   ;
   ;               *************************
   ;               *                       *
   ;               *       sub             *
   ;               *                       *
   ;               *************************
   ;
   sub:
           code
   ENDPROC                 ;will expand as RTS PC

and will create a subtitle of

        sub     Demonstration subroutine

The block defined by the PROCED macro must be terminated by an ENDPROC
macro; when the ENDPROC is encountered, it causes a return to the calling
routine.  In addition, extra code is generated by the PROCED and ENDPROC
macros to make sure that within their confines, there are an equal number
of "starting" (e.g. IF, WHILE, etc.) and "ending" (ENDIF, ENDWHILE) macros.

     Sometimes it is necessary to leave a procedure prematurely, before
reaching the ENDPROC macro.  QUIT forces an immediate exit.  It has no
arguments.


INVOKE

     The INVOKE macro is used to call a procedure defined by PROCED.  Thus
to use the procedure "sub" defined above, you would

        INVOKE  sub
        ;next instruction executed on return from "sub"

which would cause you to begin execution of the "sub" procedure.


TASK, RESUME, ENDTASK

     The other type of code block, the interrupt service routine, is
specified by the TASK macro.  The format for this macro is identical to the
PROCED macro, except that the code within the block is assumed to be an
interrupt service routine, so that the terminal ENDTASK macro generates an
appropriate "RTI" instruction.

        TASK    clock, <Clock service routine>
                code
        ENDTASK         ;will expand as RTI

causes the label "clock" to be defined, sets up an appropriate subtitle,
and causes the listing file to contain


                                - 12 -



Macros for Structured Programming



   TASK    clock, <Clock service routine>
   ;
   ;               *************************
   ;               *                       *
   ;               *       clock           *
   ;               *                       *
   ;               *************************
   ;
   ;>>>>>> Interrupt !! <<<<<<
   ;
   clock:
           code
   ENDTASK                 ;will expand as RTI

     RESUME is used to force a premature exit from an interrupt service
routine, or TASK block.  It is thus analogous to QUIT, above.


LABEL

     This macro is used to generate significant address labels.  It is
called like the PROCED macro, with an address and an optional comment in
angle brackets.  An example of its use would be

        LABEL   start   <Beginning of program>

which would generate an appropriate subtitle, and the following code --

   ;
   ;               *************************
   ;               *                       *
   ;               *       name            *
   ;               *                       *
   ;               *************************
   ;
   name:


HEAD

     This macro generates no code, but makes a nice box heading, with
optional subtitle, similar to the PROCED and TASK macros.  It is useful to
visually mark off sections of programs.  For example, you might want to
have a box labelled "var" to mark the location of variables in the code.

        HEAD    var, <Program variables>

will do just that.  Note that the first argument, "var", is only used to
generate text in the listing file -- no symbol of that name is defined by
the HEAD macro.



                                - 13 -



Macros for Structured Programming




5.  Fortran-compatible subroutine macros


FCALL

     This macro is used to call routines, passing arguments in a manner
compatible with DEC RT-11 and RSX-11 Fortran programs.  The macro should be
used instead of INVOKE to (a) actually call a Fortran sub-program, whether
or not arguments are passed, or (b) to call a Macro sub-program which must
adhere to the Fortran calling conventions (e.g. the sub-program gets called
from Fortran).  Its use is similar to the Fortran CALL statement --

        FCALL   name, <arg1, arg2, ..., argn>

where "name" is the name of the called routine (either an external global
name of a Fortran (or Fortran-compatible) subroutine/function or the name
of a Macro routine, as specified with the PROCED macro.  The arguments, to
be Fortran compatible, must be addresses of arguments (since Fortran only
uses "call-by-reference" for passing arguments). Thus if you wanted a
routine called "add" which adds its arguments together, putting the sum
into the last argument, you would set up the call as follows --

           FCALL   add, <first, second, third>
           ;next instruction goes here
              ...
           HEAD    var, <Variable storage>
   first:  1
   second: 2
   third:  3

The effect would be to add 1+2+3 (assuming the routine "add" is coded
properly; see below), and putting the result into the variable "third",
replacing its value of 3.  Note that if we want to use an array as an
argument, then we pass, as the argument, the address of the first word of
the array.

     A note on using these routines -- the current Fortran implementations
use general register 5 (r5) as a linkage pointer, i.e. a pointer to the
argument list.  Your routine should not modify this register; it is needed
by the other argument macros to access the arguments.  Also note that using
the FCALL macro will overwrite whatever happened to be in r5 when the macro
is invoked.

     A recent upgrade to FCALL allows a more flexible form of argument
passing.  Suppose your Macro routine is both called by, and calls, a
Fortran routine.  Furthermore, suppose the calling Fortran routine passes
in a parameter which, in turn, needs to be passed to the called routine.
You could use GETARG (see below) to get the appropriate argument (or its
address), store it temporarily in the Macro routine, and then build the
appropriate FCALL to the subroutine.  However, since both the passed in


                                - 14 -



Macros for Structured Programming


argument and the argument to the called routine are both addresses, there
is no real need to require intermediate argument storage in the Macro
routine.

     As an example, you write a macro routine MSUB, which is passed two
arguments.  All you want to do with each argument is pass them on, one at a
time, to a fortran subroutine, FSUB.  The old way to do this would be as
follows:

        LABEL   msub, <entry to Macro routine>
                GETARG  1, arg1         ;get arguments (see GETARG, below)
                GETARG  2, arg2         ;note we store address of arguments
                FCALL   fsub, arg1      ;call with first argument
                FCALL   fsub, arg2
        ENDPROC
        arg1:   .word   0               ;address of arguments in calling
        arg2:   .word   0               ;routines

Now, however, you could simply say

        LABEL   msub, <entry to Macro routine>
                PUSH    r5              ;save, will be modified by FCALL
                FCALL   fsub, <2(r5)>   ;call with first passed argument
                POP     r5              ;restore r5
                FCALL   fsub, <4(r5)>   ;call with second argument
        ENDPROC

This second method is faster, shorter, and requires no intermediate storage
of the arguments in transition.

FEXIT

     This macro provides for a Fortran-compatible return from a subroutine,
and hence is equivalent to the Fortran RETURN statement.  It exists in
three forms --

        FEXIT

gives the usual Fortran RETURN; in this form, it is identical to the QUIT
macro (which forces early exit from a PROCED block), and thus also
equivalent to the ENDPROC macro which terminates the PROCED block.  If a
well-structured routine is being written, one with a single entry at its
beginning and a single exit at its end, this macro is unnecessary (see
example below).

        FEXIT   n

provides the equivalent to the (non-standard) RETURN N statement -- it will
return to an address specified by the n-th argument (note -- it is the
user's responsibility to ensure that the n-th argument is a legitimate
address, including that N arguments are actually present).



                                - 15 -



Macros for Structured Programming


        FEXIT   @n

gives the equivalent of the RETURN @N statement, which returns to the
address specified indirectly by the n-th argument, i.e. the argument gives
the address of the return address.  Note that these latter two forms are
highly non-standard, not supported by DEC Fortran, and should rarely (if
ever) be used.


GETARG, PUTARG

     The macro GETARG is used to obtain the values or addresses of
arguments specified in the FCALL macro.  Its use will be illustrated in an
example program below.  It can be used to obtain the value of an argument
(appropriate if the argument represents a variable) or the address of an
argument (since if the argument represents an array, returning the address
gives you the first word address of the array).  To get the value of the
n-th argument,

        GETARG  @n, dest

which gets the value of argument n and stores it in the variable "dest".
Note that "n" is an actual number, i.e. 1, 2, 3, etc., not a variable name.
This is functionally equivalent to

        mov     <value of nth arg>, dest

so that the destination may be specified by any appropriate PDP-11
addressing mode.  To get the address of an argument (i.e. an array first
word address),

        GETARG  n, dest

To illustrate the macro, suppose you want to copy an array from one
argument to another; you would use GETARG to get both array first word
addresses, would save them in index registers, and then copy using those
registers.  Such a routine could be coded as follows:

   PROCED  copy, <Subroutine copy (A, B, N)>
   ;copies N words of array A into array B
           PUSH    <r0, r1, r2, r3>        ;save registers
           GETARG  1, r0                   ;r0 -- pointer to A
           GETARG  2, r1                   ;r1 -- pointer to B
           GETARG  @3, r2                  ;r2 -- number of elements
           FOR     r3, #1, r2              ;for each of N words,
                   mov     (r0)+, (r1)+    ;copy a word from A to B
           ENDFOR
           POP     <r3, r2, r1, r0>        ;restore registers
   ENDPROC                                 ;return (FEXIT not needed)





                                - 16 -



Macros for Structured Programming


PUTARG

     The macro PUTARG is the inverse of GETARG, and serves to return
results into the arguments specified in the FCALL macro.  As with the
GETARG macro, both a "value" and "address" form are available, but in
practice, only the "value" form is likely to be employed.  To save a value
in the n-th argument (assuming that the argument represents a simple
variable),

        PUTARG  src, @n

where, again, "src" can be any appropriate PDP-11 addressing mode.

        PUTARG  src, n

puts the value in "src" into the address specified by the n-th argument.


NUMARG

     This macro determines the number of arguments in the calling routine.
This facilitates writing subroutines which have a variable number of
arguments.  Its use is

        NUMARG  n

which puts in the variable "n" the number of arguments in the corresponding
FCALL macro.  As an example, to code the subroutine "add" which sums all
its arguments, returning the sum in the last argument,

   PROCED  add, <Subroutine add (a, b, ..., sum)>
           PUSH    <r0, r1, r2, r3>        ;save registers
           NUMARG  r0                      ;get number of arguments
           clr     r1                      ;clear sum
           GETARG  1, r2                   ;get address of first arg
           FOR     r3, 1, r0               ;for each argument
                   add     @(r2)+, r1      ;add argument value to sum
           ENDFOR
           mov     r1, @-(r2)              ;result in last argument
   ENDPROC                                 ;and return

Note the use of GETARG to get the address (not the value) of the first
argument, then just accessing the arguments sequentially (remembering that
r2 points to their addresses, so we need to use the "@(r2)+" addressing
mode).  Finally, the result is stored back through the last address
accessed, using the "@-(r2)" mode.








                                - 17 -



Macros for Structured Programming


INDEXB, INDEXW, INDEX4

     If you need to do a lot of computation with Fortran arrays, the INDEX
macro can help provide proper conversion of array indices (which start with
1) into address offsets.  Note that if you are processing an entire array
(as in the example above), an auto-increment address mode is probably more
appropriate.

     Three forms of the macro are provided, one for byte arrays (LOGICAL*1
or character strings), one for word arrays (INTEGER*2), one for real arrays
(REAL*4) -- these take into account the variable amount of storage each
data type requires.  The examples below illustrate the INDEXW form.

        INDEXW  op1, op2

changes the Fortran array index in "op1" into a word offset and stores it
in "op2";

        INDEXW  op1

does the same calculation on "op1", but then replaces this variable with
the address offset.  The following code will clear the seventh element of
the array "buffer" --

        INDEXW  #7, r0                  ;r0 will point to 7th word
        clr     buffer(r0)              ;clear 7th word of array "buffer"


6.  Utility macros

PUSH, PUSHB

     This macro causes its arguments, however many, to be pushed onto the
stack (pointed to by the stack pointer, SP = r6).

        PUSH    <arg1, arg2, ..., argn>

pushes arguments 1, 2, ... n onto the stack, in that order, while

        PUSH

pushes and clears the top of the stack (equivalent to PUSH #0).  The use of
PUSH to save general registers has been illustrated in some of the code
segments above.  After execution of a PUSH (or POP) macro, the carry flag
remains unchanged, allowing its use as an error indicator (e.g. after an
RT-11/TSX EMT).








                                - 18 -



Macros for Structured Programming


POP, POPB

     This macro is the inverse of PUSH, restoring variables from the stack.
Note that if variables are pushed onto the stack in a certain order, they
must be POPped in the inverse order.

        POP     <argn, ..., arg2, arg1>

takes the top "n" arguments and puts them into arguments n, n-1, ... 1 thus
restoring the values saved by a PUSH <arg1, ... argn>.

        POP

simply pops the stack, discarding its top element.


SWAP, SWAPB

     These two macros, which take two arguments, interchange the values
specified by their arguments, either words (SWAP) or bytes (SWAPB). Thus

        IF      r0, lt, r1        ;if r0 smaller,
                SWAP    r0, r1  ;interchange
        ENDIF

will ensure that the contents of r0 are greater than, or equal to, those in
r1.


7.  Debugging and output macros

NOTE

     This macro is used to output an arbitrary string on the system
console.  It can be used to prompt the user for input, provide information,
or output debugging messages (such as "You have just entered subroutine
Add").  This macro involves operating system-specific calls to handle
terminal output.  This macro mimics the Pascal procedure "writeln".

        NOTE    <Hello, world>

causes the message "Hello, world" to be output, while

        NOTE

without a specific string outputs a blank line.








                                - 19 -



Macros for Structured Programming


PNOTE

     To write a "partial note", i.e. to output a string without the final
carriage return and line feed, use the PNOTE macro.  This is equivalent to
the Pascal procedure "write".

        PNOTE   <Hello, >
        NOTE    <world>

will also output the message "Hello, world".  The macro without arguments,

        PNOTE

formally put out a single carriage return; however, for logical
consistency, this form of the macro now puts out a "null" partial note,
thereby doing nothing.


CHECK

     To check on numeric values, use the CHECK macro, which will name its
argument, give its values both in octal and as a signed decimal value, and
output an optional string on the terminal.  For example, suppose r1
contained the address 1000, and at 1000 was stored the number -5.  Then

        CHECK   r1, <Contents of register 1>

will cause the following to be displayed on the console --

        r1 = 1000 (512.) Contents of register 1

while

        CHECK   (r1), <Contents of contents>

will produce

        (r1) = 177773 (-5.) Contents of contents

This macro has been coded so that it will allow any type of argument
involving the stack or general registers.  Thus to examine the state of the
stack, you could say

        CHECK   sp, <Location of stack pointer>
        CHECK   (sp), <Value on top of stack>
        CHECK   2(sp), <Next value on stack>
        CHECK   (sp)+, <Top of stack, discarded>







                                - 20 -



Macros for Structured Programming


ASSERT

     In developing complex procedures, it is sometimes difficult to figure
out what is happening when things go awry.  One method is to use ODT to
step through the procedure, checking critical variables to make sure they
stay within legal bounds.  Another method is to embed such testing code
within the procedure, which can test during run time to make sure variables
obey specified conditions.

     The ASSERT macro provides a simple method for implementing this latter
method.  An example of the use of this macro is

        ASSERT  r0, lt, r1

which will include code to test that r0 is less than r1 whenever the macro
is invoked.  If the assertion is not met, a message of the form

        PROOF = 4.
        r0, lt, r1 -- assertion is false
        r0 = 10 (8.)      r1 = 6 (6.)

The first line gives the value of "proof", a (unique) number assigned to
each assertion (see below).  The assertion is presented, along with the
values which caused it to fail.  If the assertion is met, no message is
output.

     The test in the ASSERT macro can be any of the forms used above for
IF, WHILE, and UNTIL, such as

        ASSERT  (sp), ne        ;assert that top of stack not zero or

        ASSERT  cc              ;assert that the carry is not set

     These macros cause the insertion of extra code to handle the assertion
tests and inform the user of possible violations.  Once the code has been
tested demonstrated correct, the extra code can be conveniently eliminated
without major editing changes.  The actual generation of the assertion code
is governed by a user-defined constant named "proof" -- this constant must
be defined, and set to a value > 0 in order to cause code generation.  Thus
just by changing the line

        PROOF   =       1

to

        PROOF   =       0

the code-generation will be turned off.  Each time an ASSERT macro is
assembled and "proof" is positive, "proof" is incremented, providing a
unique identifier for each assertion to aid in debugging.  These
identifiers appear in the listing next to the ASSERT macro in the form



                                - 21 -



Macros for Structured Programming


   ;
   ;>>>>>> n <<<<<<        This is assertion # n
   ;


ASSERB

     To make an assertion about a byte, use ASSERB instead of ASSERT.
Otherwise, the macros are identical.  "Proof" will also be incremented (if
positive) when ASSERB is assembled.


ENDEND

     Each time an "END" macro is assembled, a test is made to ensure that
it has an appropriate macro (such as IF, WHILE, PROCED, etc.) in front of
it.  The ENDEND macro provides the opposite function -- it ensures that
enough END macros have been included to match all preceding macros.  It is
typically placed as the last macro in the program, and will cause the
generation of an error message if a missing END is detected.


8.  "Invisible" macros for numeric output

      These macros are all "invisible", that is, the user does not need to
directly specify them.  They provide certain bookkeeping functions for the
output routines described in the previous section.  The first two macros,
TYP.8 and TYP.10, which output numeric values, might be useful in a user
program.


TYP.8, TYP.10

     These macros type a number in octal or signed decimal on the console.
They can be called in two fashions --

        TYP.8   x

types the number in x on the console, while

        TYP.8

outputs the contents of r0.  The contents of the registers are not altered
by either of these macros.  In particular, they allow "sp" and "(sp)" as
arguments.









                                - 22 -



Macros for Structured Programming


.TYPER

     This macro does the actual type out of octal or decimal values.  When
first invoked, it builds an internal subroutine ".tysub" which handles the
number-to-character conversion.


A.LABL

     This macro is a part of the assertion macros.  Its function is to
provide an identifying label in listings showing the number of each
assertion.  An example listing could include

           ASSERT  r0, lt, r1
   ;
   ;>>>>>> 12 <<<<<<        This is assertion # 12
   ;


9.  "Invisible" macros for program control

     This group of macros is invoked by many of the block-structuring
macros (IF, WHILE, END, etc.) to handle control block and looping
structure.  You should never need to explicitly invoke them; they are
described here for completeness.


Internal symbols

     The macros work by maintaining some internal symbols, which serve as
stacks, addresses for loop beginning and end, type of comparison, etc. The
symbols all use the "reserved" character "." as the first character, so
they should not interfere with user-defined symbols.

        .1, .2, .3 ...      Labels used to construct control blocks,
                            e.g. forms addresses at beginning and end
                            of WHILE-controlled code.

        .head               Unique (pair) of numbers used to generate
                            labels for control blocks.

        .tail               Symbol often used at end of control blocks
                            to construct final branches.

        .temp               Temporary "scratch" symbol.

        .stk                Depth of internal symbol stack.

        .stk1, .stk2, ...   Internal symbol stack, holds various values
                            for blocks, used to build nested block
                            structure.



                                - 23 -



Macros for Structured Programming


        .br                 Holds branch instruction (e.g. bne, bgt)
                            needed for other macros.

        .nchrs              Used to count characters in output strings.


Internal symbol stack macros

.PUSH, .POP

     Pushes or pops argument using the internal stack.  The argument can be
any value or symbol.


..PUSH, ..POP

     These macro does the actual stack manipulation for .PUSH and .POP.


.TOP

     This macro gets the top element from the stack, without doing a .POP.
The effect is equivalent to a .POP followed by a .PUSH.


Label macros

     Certain macros (such as IF, WHILE, CASE) generate labels, which are a
unique pair of symbols of the form ".n" where n is a number.  Labels are
generated sequentially; .1 and .2 are the first pair of labels.


.LABEL

     This macro generates a label of an appropriate number (its argument)
corresponding to the current program counter.


.ADDR

     This macro generates an address corresponding to a label number.  In
contrast to the .LABEL macro, which defines a symbol equal to the current
value of the PC, the .ADDR macro generates a word (actual code) whose value
corresponds to the address of the corresponding label number.


.GOTO

     This cause a jump to a label.  The argument of the macro gives the
label number.




                                - 24 -



Macros for Structured Programming


.GOBAK
     This is an optimized backwards-branching form of .GOTO, which will use
a branch instruction where possible.


Branching macros

     Several macros require tests, such as "GT", "CC", etc.  Branch
instructions ;corresponding to such tests (e.g. bgt, bcc) will be stored in
the symbol ".br", and will be used in the following macros.


..BR

     Branch to the address represented by the argument.


...BR

     Branch to the label whose number is given by the argument.


.TEST, .TESTB

     Generate code for various tests.  Arguments represent the number of
arguments in the invoking macro, the arguments of the invoking macro, and
the numeric value of the false fork's label, i.e. where to go if the test
fails.


























                                - 25 -