Government of Canada
                                 Ottawa Ontario





















                            FLECS/RT-11 USER'S GUIDE

                          IMPLEMENTATION VERSION 28.01

                                   April 1980


FLECS/RT-11 V28 USER'S GUIDE                                         2



     FORWARD     _______

     This document and the software it describes, are edited  versions
     of  work  performed  by  Mr.Terry Beyer (herein refered to as the
     author) of the University of Oregon.

     COPYRIGHT     _________

     This manual is in  the  public  domain  and  may  be  altered  or
     reproduced without the explicit permission of the author.

     SUPPORT     _______

     Support for the RT-11 implementation of  FLECS  may  be  obtained
     from  the  design  authority  stated  within  this document.  The
     department however, reserves the right to  terminate  support  at
     any time without notice.

     DISCLAIMER     __________

     Although care has been taken to ensure the correct functioning of
     the FLECS system, neither the author nor the University of Oregon
     nor any agency of the Government of Canada shall  be  liable  for
     any  direct  or  indirect,  incidental, consequential or specific
     damages of any kind, or from any cause whatsoever arising out of,
     or in any way connected with, the use or performance of the FLECS
     system or its documentation.

     ACKNOWLEDGEMENTS     ________________

     The author is indebted to many people for assistance of one  form
     or another during the course of this project.  Mike Dunlap, Kevin
     McCoy and Peter Moulton deserve special thanks for  many  helpful
     and  fruitful discussions, suggestions, and encouragements.  I am
     grateful to my wife Kathleen, who assisted in many ways including
     shielding  me  from the harsh reality of JCL and IBM 360 assembly
     language.  Text preparation was adroitly  accomplished  by  Marva
     VanNatta, Allyene Tom, Diane Lane and Kathleen Beyer.

     This project was initiated while the author was working  under  a
     grant provided by the Office of Scientific and Scholarly Research
     of the Graduate School at the University of Oregon.  Work on  the
     project  has  also  been  supported  in part by the Department of
     Computer Science and by the Computing Centre of the University of
     Oregon.


FLECS/RT-11 V28 USER'S GUIDE                                         3



                               TABLE OF CONTENTS



     1.  FLECS OVERVIEW .................................. 04

     2.  FLECS DECISION STRUCTURES ....................... 10

     3.  FLECS LOOP STRUCTURES ........................... 13

     4.  INTERNAL PROCEDURES ............................. 15

     5.  FLECS/RT-11 TRANSLATION DIRECTIVES .............. 18

     6.  OTHER FLECS/RT-11 FEATURES ...................... 21

     7.  RESTRICTIONS .................................... 22

     8.  HINTS TOWARDS A CODING STANDARD ................. 25

     9.  RUNNING THE TRANSLATOR UNDER RT-11............... 27

     10. ERROR HANDLING .................................. 30

     Appendix A - RT-11 INSTALLATION PROCEDURES .......... 33

     Appendix B - FLECS SUMMARY .......................... 37


FLECS/RT-11 V28 USER'S GUIDE                                         4



                            FLECS/RT-11 USER'S GUIDE
                           IMPLEMENTATION VERSION 28



1.   FLECS OVERVIEW     _____ ________


1.1  INTRODUCTION     ____________

     FORTRAN contains four basic mechanisms  for  controlling  program
     flow:  CALL/RETURN, IF, DO and various forms of the GOTO.

     FLECS is a language extension of  FORTRAN  which  has  additional
     control  mechanisms.   These  mechanisms  make it easier to write
     FORTRAN by eliminating much of  the  clerical  detail  associated
     with constructing FORTRAN programs.  FLECS is also easier to read
     and comprehend than FORTRAN.

1.2  SCOPE OF DOCUMENT     _____ __ ________

     This manual is intended to be a brief but  complete  introduction
     to  FLECS and its RT-11 implementation.  It is not intended to be
     a primer on FLECS  or  structured  programming.   The  reader  is
     assumed to be a knowledgeable FORTRAN programmer.

1.3  PORTABILITY     ___________

     For programmers to whom transportability of their programs  is  a
     concern, it should be noted that the FLECS translator source code
     is in the public  domain  and  is  made  freely  available.   The
     translator  was  written with transportablilty in mind and should
     require little effort to move from one machine to another.  Those
     interested  in  moving  FLECS  to  a  machine other than a PDP-11
     running RT-11 should contact:

                           Mr.  Terry Beyer
                           Computing Centre
                           University of Oregon
                           Eugene, Oregon 97409
                           Telephone:  (503) 686-4416


1.4  RT-11 IMPLEMENTATION DESIGN AUTHORITY     _____ ______________ ______ _________

     The RT-11 implementation of FLECS described in this document  may
     be obtained from:

                           National Defence Headquarters
                           Ottawa Ontario Canada
                           K1A 0K4
                           Attention: Mr. G. L. Adams (DACS 2)
                           Telephone: (613) 993-9624


FLECS/RT-11 V28 USER'S GUIDE                                         5



1.5  RT-11 IMPLEMENTATION STANDARDIZATION     _____ ______________ _______________

     As with all "implementations", the RT-11 implementation has  some
     enhancements  which  make  it a little more useable, but slightly
     different from pure FLECS.  Since "local  improvements"  tend  to
     destroy  standardization and hence transportability, the user may
     easily edit out  any  non-standard  features,  should  it  become
     necessary to move any programs to a different system.

1.6  HOW FLECS WORKS     ___ _____ _____

     FLECS is implemented as a  preprocessor  which  translates  FLECS
     programs into FORTRAN programs.  The resulting FORTRAN program is
     then processed in the usual way.  The translator also produces  a
     nicely  formatted  listing of the FLECS program which graphically
     presents the control structures used.

     Diagram 1-1 illustrates the translating process.


                                  Diagram 1-1
                            The Translation Process



          .----------.          .------------.         .-----------.
         .  FLECS   .           ! FLECS      !        . FORTRAN   .
         .  SOURCE  . --------> ! TRANSLATOR ! -----> . SOURCE    .
          .__________.          !____________!         .___________.
                                      !
                                      v
                                .------------.
                                ! INDENTED   !
                                ! LISTING    !
                                !____________!




1.7  RETENTION OF FORTRAN FEATURES     _________ __ _______ ________

     The FLECS translator examines each statement in the FLECS program
     to see if it is either a translation directive (a statement which
     controls translation but does not actually generate  any  FORTRAN
     code)  or  an  extended  statement (a statement which is valid in
     FLECS but not in FORTRAN).

     If it is recognized as  an  extended  statement,  the  translator
     generates the corresponding FORTRAN statements.

     If it is recognized as a translation directive,  the  appropriate
     action  is  performed  (such  as  causing  the  listing  to go to
     top-of-form).


FLECS/RT-11 V28 USER'S GUIDE                                         6



     If however, the statement is not recognized as either an extended
     statement or a translation directive, then the translator assumes
     it must be a FORTRAN statement and passes it  through  unaltered.
     Thus  the  FLECS  system does not restrict the use of FORTRAN, it
     simply provides a set of additional statements which may be used.
     In particular, GOTOs, arithmetic IFs, CALLs, arithmetic statement
     functions, and any other FORTRAN statements,  compiler  dependant
     or otherwise, may be used in a FLECS program.

1.8  CORRELATION OF FLECS AND FORTRAN SOURCES     ___________ __ _____ ___ _______ _______

     One difficulty of preprocessor systems like FLECS is  that  error
     messages  which  come  from  the FORTRAN compiler must be related
     back to the original FLECS source program.

     This difficulty is all but eliminated in the RT-11 implementation
     because  both the FLECS line numbers and the FORTRAN line numbers
     (not to be confused with FORTRAN statement numbers) are placed on
     the listings output by the FLECS translator.

     Since RT-11 FORTRAN compiler errors  are  given  at  the  end  of
     compilation  in  terms  of  the line number, only the one listing
     need be consulted.  There is seldom any need to cross-compare the
     FLECS listing and its associated FORTRAN listing.

     On those rare occasions when cross-comparison  is  required,  the
     programmer may insert sequence numbers in columns 76 to 80 in the
     FLECS  source  program  or  have  the  FLECS  translator  do   it
     automatically  for him.  The sequence numbers are carried through
     to the FORTRAN code and hence FORTRAN errors which are  reported,
     may  be  found  by  manually  tracing  them back from the FORTRAN
     listing to the FLECS source.

1.9  STRUCTURED STATEMENTS     __________ __________

     A basic  notion  of  FLECS  is  the  structured  statement  which
     consists  of  a  control  phrase  and its scope.  FORTRAN has two                      _______  ______          _____
     structured statements, the logical IF and the DO.   For  example,
     in the FORTRAN statement

                           IF (A.GT.B) A=B

     The portion IF (A.GT.B) is the control phrase while  A=B  is  its
     scope.  Similarily, in the FORTRAN program segment

                           DO 100 I=1,10
                           A(I)=B(I)+C
                           L(I)=I-K(I)
                       100 CONTINUE

     the line DO 100 I=1,10 is the control phrase  and  the  remaining
     lines are the scope.

     Each control phrase consists of two parts,  a  keyword  and  some                                                    _______
     additional  information  called  the specification.  In the above                                          _____________


FLECS/RT-11 V28 USER'S GUIDE                                         7



     examples, IF and DO were the keywords.

     Note that in FORTRAN and in FLECS,  not  all  statements  have  a
     scope.   Some such as CALL, the arithmetic IFs and the GOTOs have
     only a control phrase.  These are called simple statements.                                              ______ __________

     The problem with the FORTRAN logical IF  statement  is  that  its
     scope   may   contain  only  a  single  simple  statement.   This
     restriction is eliminated in the case of the DO, but at the  cost
     of  clerical  detail  (having  to stop thinking about the problem
     while a statement number is invented).  Note  also  that  the  IF
     specification   is   enclosed   in   parentheses   while  the  DO
     specification is not.

     In FLECS, there is  a  uniform  convention  for  writing  control
     phrases  and  indicating  their  scopes.   To  write a structured
     statement, the keyword is placed first on a line, followed by its
     specification enclosed in parentheses.  The remainder of the line
     is left blank or may contain one simple statement as its scope.

     If a simple statement  is  included  on  the  same  line  as  the
     structured  statement,  a  single-line  structured  statement  is                                ___________  __________  _________
     created.

     If a simple statement is not included on the  same  line  as  the
     structured  statement,  then  the  scope  is placed on successive
     lines creating a multi-line structured statement.  The  scope  of                      __________ __________ _________
     each  multi-line  structured  statement is terminated with a FIN.
     The following examples illustrate.

                           IF (X.EQ.Y)   !A multi-line IF.
                             U=V+W
                             S=T*G
                             FIN

                           DO (I=1,100)  !A multi-line DO.
                             A(I)=B(I)+C
                             C=C*3.14159
                             FIN   !Note no statement number.

                           DO (I=1,100) A(I)=0   !A single line DO.


     Nesting of structured statements is permitted to any depth.  Here
     is an example of nested structured statements.

                           IF (X.EQ.Y)     !Start of level 1.
                             U=V+W
                             DO (I=1,N)    !Start of level 2.
                               A(I)=B(I)+C
                               C=C*2.14-3.14159
                               FIN           !End of level 2.
                             R=S+T
                             FIN             !End of level 1.


FLECS/RT-11 V28 USER'S GUIDE                                         8



     Since each control phrase must begin on a new  line,  it  is  not
     possible  to  have  a  one-line  structured statement whose scope
     consists of a structured statement.  As an example, the following
     is not valid in FLECS.     __ ___ _____

                           IF (A.EQ.B) DO (I=1,10) C(I)=D(I)


     To achieve the effect desired above, the IF must  be  written  in
     the multi-line form as in the following example.

                           IF (A.EQ.B)
                             DO (I=1,10) C(I)=D(I)
                             FIN


     In  addition  to  IF  and  DO,  FLECS  provides  some  additional
     structured  statements  not  available in FORTRAN.  These will be
     discussed later.

1.10 INDENTED LISTING OF SOURCE LINES     ________ _______ __ ______ _____

     In the examples of multi-line structured  statements  above,  the
     statements  in  the  scope  were  indented  in an "L" shape.  The
     indentation effect helps to reveal the structure of the program.

     The FLECS translator performs this indentation automatically  and
     enhances  the  effect  by  adding trace-back dots which join each
     keyword to its matching FIN.  The following example illustrates.

                           DO (I=1,10)
                           .  A(I)=B(I)
                           .  C(I)=B(I)*3.14159
                           ...FIN

     The rules for indentations are quite  simple  and  uniform.   The
     control phrase of a multi-line structured statement always causes
     indentation of the statements that follow.  Nothing  else  causes
     indentation.   A  level  of indentation (i.e.  a scope) is always
     terminated with a  FIN.   Nothing  else  terminates  a  level  of
     indentation.

     When writing a FLECS program  on  paper,  the  programmer  should
     adopt  the  indentation and line drawing conventions shown above.
     When preparing  a  FLECS  source  program  with  a  text  editor,
     however,  each  line  should  begin  after  a tab character or on
     column 7.  If  the  programmer  attempts  to  introduce  his  own
     indentation by using leading tabs or blanks, the FLECS translator
     will ignore them.


     The correctly indented listing is a tremendous aid in reading and
     working   with   FLECS   programs.    Except  for  the  dots  and
     indentations, the lines appear  exacly  as  they  appear  in  the
     source  program  and  internal  spacing  (as  opposed  to leading


FLECS/RT-11 V28 USER'S GUIDE                                         9



     spacing) is preserved.  There is seldom any need to  refer  to  a
     straight listing of the unindented source.

1.11 COMMENTS     ________

     In order to prevent interruption of  the  trace-back  dots  which
     indicate  the scope, a comment line which contains only blanks in
     columns 2 through 6 will be listed  with  columns  7  through  72
     indented at the then-current level of indentation (as if the line
     were an executable statement).  If however, one or more non-blank
     characters  appear  in  columns  2  through  6, it will be listed
     without indentation.

     As an additional aid to readability, blank lines may be  inserted
     in  the  source  (without a C in column 1) and will be treated as
     empty comments.

     In addition to regular FORTRAN comments as indicated by  a  C  in
     column 1, in-line comments are also supported.  Any text appended
     to a line following an exclamation  mark  (!)  is  treated  as  a
     comment.


FLECS/RT-11 V28 USER'S GUIDE                                        10



2.   FLECS DECISION STRUCTURES     _____ ________ __________

     Structured statements which control the execution of their scopes
     on  the  basis  of  a logical expression test are called decision
     structures.

2.1  IF     __

     The IF statement causes a logical expression to be evaluated.  If
     the  value is true, the scope is executed once and control passes
     to the next statement.  If the value  is  false,  control  passes
     directly to the next statement without execution of the scope.

     Examples:

                           IF (A.GT.B) X=R*COS(A)

                           IF ((T.GT.0).AND.(S.LT.R))
                           .  I=I+1
                           .  Z=0.1
                           ...FIN


2.2  UNLESS     ______

     The  UNLESS  statement   is   functionally   equivalent   to   an
     "IF (.NOT.---)"  statement  but  is  useful  because  it  is more
     readable in most contexts.

     Example:

                           UNLESS (ERROR)
                           .  READ (1,1) A
                           .  WRITE(2,2) A
                           ...FIN


2.3  WHEN/ELSE     _________

     The  WHEN/ELSE  statements   correspond   to   the   IF/THEN/ELSE
     statements  of  ALGOL, PL/1, PASCAL etc.  In FLECS, both the WHEN
     and the ELSE act as structured statements although only the  WHEN
     has  a specification.  The ELSE statement must immediately follow
     the scope of the WHEN.   After  the  specifier  of  the  WHEN  is
     evaluated,  one  and only one of the two scopes is executed.  The
     scope of the WHEN is executed if the expression is true  and  the
     scope  of  the  ELSE  is executed if the expression is false.  In
     either case, control then passes to the next statement  following
     the scope of the ELSE statement.

     Examples:

                           WHEN (X.EQ.0) ANSWER=.FALSE.
                           ELSE          ANSWER=.TRUE.


FLECS/RT-11 V28 USER'S GUIDE                                        11



                           WHEN (GOODANSWER)
                           .  X=R*SIN(THETA)
                           .  CALL EVALU8(X)
                           ...FIN
                           ELSE
                           .  TRIES=TRIES+1
                           .  TYPE *,' PROGRAM-I-Your answer was bad.'
                           ...FIN

     Notes:

     WHEN and  ELSE  always  come  as  a  pair  of  statements,  never
     separately.

     Either the WHEN or the ELSE or both  may  assume  the  multi-line
     form.

     ELSE is considered to be a control phrase, hence cannot be placed
     on the same line as the WHEN.

2.4  CONDITIONAL     ___________

     The CONDITIONAL statement is based on the  LISP  conditional.   A
     list  of  logical  expressions  is evaluated one by one until the
     first  expression  to  be  true  is   encountered.    The   scope
     corresponding  to  that  expression  is executed and control then
     passes to the first statement following the CONDITIONAL.  If  all
     expressions  are  false, no scope is executed.  (See however, the
     note about OTHERWISE below).

     Examples:

                           CONDITIONAL
                           .  (X.LT.-5) U=U+W
                           .  (X.LE..1) U=U-W
                           .  (X.LE.1.) U=U*W
                           ...FIN

                           CONDITIONAL
                           .  (A.EQ.B) Z=1
                           .  (A.LE.C)
                           .  .  Z=2
                           .  .  R=X-4
                           .  ...FIN
                           .  (A.GT.D) Z=Z-1
                           .  (OTHERWISE) Z=0
                           ...FIN

     Notes:

     The CONDITIONAL itself does not possess a  one-line  form.   Each
     element  of  the  CONDITIONAL however, is treated as a structured
     statement and may be in a one-line or a multi-line form.


FLECS/RT-11 V28 USER'S GUIDE                                        12



     The reserved word  OTHERWISE  represents  a  catchall  condition.
     (OTHERWISE) is equivalent to (.TRUE.).

2.5  SELECT     ______

     The SELECT statement is similar to the CONDITIONAL  but  is  more
     specalized.   It  allows  the  specification  to  be  tested  for
     equality to each element in a  list  of  expressions.   When  the
     first matching expression is encountered, the corresponding scope
     is executed and the SELECT statement  terminates.   Any  type  of
     expression  (integer,  real, complex etc.) may be used as long as
     the underlying FORTRAN  system  allows  such  expressions  to  be
     compared with an .EQ.  or .NE.  operator.

     Example:

                           OPCODE=MEMORY(PC)
                           SELECT (OPCODE)
                           .  (JMP) PC=MEMORY(PC+2)
                           .  (ADD)
                           .  .  SRC=MEMORY(PC+2)
                           .  .  DST=MEMORY(PC+4)
                           .  .  MEMORY(DST)=MEMORY(DST)+MEMORY(SRC)
                           .  .  PC=PC+6
                           .  ...FIN
                           .  (NOP) PC=PC+2
                           .  (OTHERWISE) CALL TRAP4(PC)
                           ...FIN

     Notes:

     As in the case of CONDITIONAL, at most one of the elements of the
     SELECT will be executed.

     The catchall OTHERWISE may also be used in  a  SELECT  statement.
     (OTHERWISE)    in    our   example   would   be   equivalent   to
     (OPCODE.EQ.OPCODE).

     The specification of the SELECT is evaluated for each  comparison
     in  the  list.   Lengthy,  time  consuming  or  non-reproduceable
     expressions should be pre-computed, assigned to  a  variable  and
     then the variable used in its place.


FLECS/RT-11 V28 USER'S GUIDE                                        13



3.   FLECS LOOP STRUCTURES     _____ ____ __________

     Loop structures all have scopes which  are  executed  a  variable
     number of times depending on the specified conditions.

     Of the five loops presented, the most  useful  are  the  DO,  the
     WHILE and the REPEAT UNTIL.  To avoid confusion, the REPEAT WHILE
     and  the  UNTIL  loops  should  not  be  used  unless  absolutely
     necessary.

     Except for the DO, the presence of  the  keyword  REPEAT  directs
     that  testing  be  done at the end of the loop.  If REPEAT is not                                    ___
     present then testing is done at the beginning of the loop.

3.1  DO     __

     The FLECS DO loop is functionally identical  to  the  FORTRAN  DO
     loop.   The  only  differences  are syntactical.  In the FLECS DO
     loop, the statement number is omitted from the specification, the
     specification  is  enclosed  in  parentheses and the scope may be
     either single-line or multi-line.

     Examples:

                           DO (I=1,N) A(I)=0.0

                           DO (J=4,62,2)
                           .  B(J)=B(J-1)*B(J-2)
                           .  C(J)=SIN(B(J))
                           ...FIN

     Notes:

     With FORTRAN/RT-11, testing is done at the end of the loop.  As a
     consequence,  all  DO  loops  will  be  executed  at  least  once
     regardless of the specification parameters.

3.1   WHILE       _____

     The WHILE loop causes its scope to be repeatedly executed while a
     specified  condition  is true.  The condition is checked prior to
     the first execution of the scope.  If the condition is false, the
     scope will never be executed at all.

     Examples:

                           WHILE (X.LT.A(I)) I=I+1

                           WHILE (P.NE.0)
                           .  VAL(P)=VAL(P)+1
                           .  P=LINK(P)
                           ...FIN


FLECS/RT-11 V28 USER'S GUIDE                                        14



3.2 REPEAT WHILE    ______ _____

     The REPEAT WHILE is similar to the WHILE loop except that the use
     of  the  REPEAT verb causes the test to be logically moved to the
     end of the loop.  Since the condition is not checked until  after
     the  first  execution  of  the  scope,  the  scope will always be
     executed at least  once.   The  condition  indicates  under  what
     conditions the scope is to be repeated.                                   ________

     Examples:

                           REPEAT WHILE (N.EQ.M(I)) I=I+1


3.3  UNTIL     _____

     The UNTIL loop causes its scope to be repeatedly executed until a
     specified condition becomes true.  The condition is checked prior
     to the first execution of the scope, thus  if  the  condition  is
     initially true, the scope will not be executed at all.

     The UNTIL is functionally equivalent to WHILE (.NOT.---).

     Examples:

                           UNTIL (X.EQ.A(I)) I=I+1


3.5  REPEAT UNTIL     ______ _____

     By using the REPEAT verb, the test can be logically moved to  the
     end  of  the  loop.  The REPEAT UNTIL loop causes its scope to be
     repeatedly executed until a  specified  condition  becomes  true.
     The  condition  is not checked until after the first execution of
     the scope thus the scope will always be executed at  least  once.
     The  condition  indicates under what conditions the repetition of                                                         __________
     the scope is to be terminated.

     Examples:

                           REPEAT UNTIL (END_OF_FILE)
                           .  END_OF_FILE=.TRUE.
                           .  READ (1,1,END=100) A,B,C
                           .  END_OF_FILE=.FALSE.
                     100   .  UNLESS (END_OF_FILE) WRITE(2,2) A,B,C
                           ...FIN


FLECS/RT-11 V28 USER'S GUIDE                                        15



4.   INTERNAL PROCEDURES     ________ __________

     In FLECS, a sequence of statements may be  declared  an  internal                                                              ________
     procedure  and  given  a name.  The procedure may then be invoked     _________
     from any point in the program by simply giving its name.

4.1  INTERNAL PROCEDURE NAMES     ________ _________ _____

     Procedure names may be any string of letters, digits and  hyphens
     (i.e.   minus  signs)  beginning  with a letter and containing at
     least one hyphen.  Internal blanks are  not  allowed.   The  only
     restriction  on  the  length  of  a  name  is  that it may not be
     continued onto a second line.

     Examples of valid internal procedure names:

                           INITIALIZE-ARRAYS
                           GIVE-WARNING
                           SORT-INTO-DESCENDING-ORDER
                           INITIATE-PHASE-3


4.2  INTERNAL PROCEDURE DECLARATIONS     ________ _________ ____________

     A procedure declaration consists of the keyword "TO" followed  by       _________ ___________
     the  procedure  name  and  its  scope.   The  set  of  statements
     comprising the procedure is  called  its  scope.   If  the  scope
     consists  of  a  single simple statement, it may be placed on the
     same line as the "TO"  and  the  procedure  name,  otherwise  the
     statements  of  the  scope  are placed on the following lines and
     terminated with a FIN.  These rules are analogous with the  rules
     for forming the scope of a structured statement.

     Examples:

                           TO DO-NOTHING CONTINUE

                           TO SUMMARIZE-THE-FILE
                           .  INITIALIZE-SUMMARY
                           .  OPEN-FILES
                           .  REPEAT UNTIL (ENDOFFILE)
                           .  .  READ-A-RECORD
                           .  .  WHEN (ENDOFFILE) CLOSE-FILES
                           .  .  ELSE UPDATE-THE-SUMMARY
                           .  ...FIN
                           ...FIN

4.3  REFERENCING AN INTERNAL PROCEDURE     ___________ __ ________ _________

     An internal procedure reference is  a  procedure  name  appearing        ________ _________ _________
     where  an  executable  statement  would be expected.  In fact, an
     internal procedure reference is an  executable  simple  statement                                  __
     and thus may be used in the scope of a structured statement as in
     the last example.


FLECS/RT-11 V28 USER'S GUIDE                                        16



     When control reaches a procedure reference during execution of  a
     FLECS   program,  a  return  address  is  saved  and  control  is
     transferred to  the  first  statement  in  the  procedure.   When
     control  reaches  the  end  of  the procedure's scope, control is
     transferred  back  to  the  statement  logically  following   the
     procedure reference.

     A typical  FLECS  program  consists  of  a  sequence  of  FORTRAN
     declarations:   (e.g.   SUBROUTINE,  INTEGER,  DIMENSION, COMMON,
     etc.) followed by a sequence of executable statements called  the
     body  of  the  program  followed  by the FLECS internal procedure     ____
     declarations if any, and finally the END statement.

     As an example,  a  complete  (but  uninteresting)  FLECS  program
     follows   which   illustrates  the  placement  of  the  procedure
     declarations.  It is shown exacly as it would be  listed  by  the
     FLECS/RT-11  implementation.  Note both the FLECS and the FORTRAN
     line numbers  on  the  left,  the  use  of  blank  lines  by  the
     programmer  and  the  dashed lines generated by the translator to
     separate procedure declarations.

     Example:

          0001     C     Interactive Program to Compute X**2.
          0002     C     A zero input terminates execution.
          0003     
          0004 001       REAL X,XSQ
          0005     
          0006 002       REPEAT UNTIL (X.EQ.0.)
          0007 005       .  GET-A-VALUE-OF-X
          0008 007       .  UNLESS (X.EQ.0.)
          0009 009       .  .  COMPUTE-RESULT
          0010 010       .  .  TYPE *,' X SQUARED = ',XSQ
          0011           .  ...FIN
          0012           ...FIN
          0013     
          0014 011       CALL EXIT
                   
                         --------------------------------------
                   
          0015           TO GET-A-VALUE-OF-X
          0016 012       .  TYPE 10
          0017 013 10    .  FORMAT('$Give me an X?  ')
          0018 014       .  ACCEPT 20,X
          0019 015 20    .  FORMAT(F10.5)
          0020 016       ...FIN
                   
                         --------------------------------------
                   
          0021 017       TO COMPUTE-RESULT XSQ=X*X
          0022     
          0023 019       END



FLECS/RT-11 V28 USER'S GUIDE                                        17



     Notes:

     All internal procedure declarations must be placed at the end  of
     the  program  just prior to the END statement.  The appearance of
     the first "TO" statement terminates the body of the program.  The
     translator expects to see nothing but procedure declarations from
     that point on.  In particular, the translator will reject  FORMAT
     statements;   thus  they  cannot  be  placed  just before the END
     statement  in  the  program.   The  suggested  place  for  FORMAT
     statements  is  at  the  beginning  of  the  program  immediately
     following the data declaration section (i.e.   make  FORMAT  look
     like part of the data declaration).

     The order of internal procedure declarations  is  not  important.
     The  translator  prints an alphabetical procedure cross reference
     table at the end of the listing to assist  in  finding  procedure
     references and declarations.

     Procedure declarations may not be nested.  The following  example
     is not valid in FLECS.        ___ _____

                           TO DO-THE-WHOLE-THING
                           .  A=B+C
                           .  TO DO-PART-OF-THE-THING
                           .  .  B=C+D
                           .  ...FIN
                           ...FIN


     A procedure may  reference  any  other  procedures  but  may  not
     reference itself.

     Dynamic recursion of procedure referencing is not allowed.

     All program variables are global and accessable to the statements
     in any internal procedure or the program body.

     There is no formal mechanism for defining or  passing  parameters
     to  an internal procedure.  When parameter passing is needed, the
     FORTRAN function or subroutine mechanisms should be used.

     The   FLECS   translator   automatically   separates    procedure
     declarations  on  the  listing by dashed lines thus improving the
     aesthetics of the output.

     Do not confuse  internal  procedures  with  FORTRAN  function  or
     subroutine  subprograms.   Internal  procedures  form a part of a
     function or subroutine subprogram, or of course, a main program.


FLECS/RT-11 V28 USER'S GUIDE                                        18



5.   FLECS/RT-11 TRANSLATION DIRECTIVES     ___________ ___________ __________

     The RT-11 implementation of FLECS  allows  the  user  to  specify
     several translation directives that are not available in standard
     FLECS or in FORTRAN/RT-11.  They actually make using FLECS  under
     RT-11 easier.

     Should the programs have to be transported to a different  system
     with  only  standard  FLECS,  the  RT-11  implementation  can  be
     standardized simply by editing  out  any  translation  directives
     used.

     Translation directives are not shown on the listings produced  by
     FLECS, they are only visible in the actual source code.

     Most translation directives start with a "$" in column 1 with the
     first  letter  of  the  specific command in column 2.  All others
     have regular FLECS format.

5.1  $FORTRAN/$NFORTRAN     __________________

     The $NFORTRAN or $NF directive turns off  FORTRAN  output  (which
     speeds  up FLECS processing).  The $FORTRAN or $F directive turns
     it back on again.

     Users should be aware that in most  cases,  turning  off  FORTRAN
     output  will  result  in  FORTRAN  code  which  is incomplete for
     compilation.

5.2  $LIST/$NLIST     ____________

     The $NLIST or $NL directive turns listing output off (to speed up
     FLECS  processing  on  already  debugged  sections of code).  The
     $LIST or $L directive turns the listing back on.

5.3  $PAGE     _____

     The $PAGE or $P directive causes a form-feed to be output to  the
     listing  so  that the user may start appropriate sections of code
     at the top-of-form.

     Note that the FLECS translator never  outputs  form-feeds  except
     when requested by the $PAGE directive.

5.4  $X/$NX     ______

     The $X and $NX directives facilitate the conditional  translation
     of source lines which have an "X" in column 1.

     When $X is invoked, all lines which have an "X" in column  1  are
     translated or are passed through to FORTRAN as appropriate.

     When $NX is invoked, all lines which have a "X" in column  1  are
     totally ignored (not even listed).


FLECS/RT-11 V28 USER'S GUIDE                                        19



     Notes:

     $NX is the default condition at the commencement of translation.

     If an input line is processed with an "X" in column 1  and  there
     is  a  "C" or a "D" in column 2, the "C" or the "D" will be moved
     to column 1 and the statement treated as a comment.

     The use of the FORTRAN debug option (conditional  compilation  of
     lines  with  "D"  in  column 1) is not recommended in FLECS.  The
     line numbering on the listings will be incorrect and may lead the
     user astray.  $X/$NX should be used instead.

5.5  INCLUDE     _______

     The  INCLUDE  directive  is  simular  to  the  INCLUDE  statement
     available  in  FORTRAN  IV PLUS.  It allows source input to to be
     "included" from a secondary input file.

     Format:

                           INCLUDE DEV:FILNAM.EXT

     In the following example, files "COM1.CMB" and "COM2.CMB" contain
     "COMMON /ABC/ A,B,C" and "COMMON /DEF/ D,E,F" respectively.

     The program would be entered via the editor as:

                           PROGRAM MAIN
                           INCLUDE COM1.CMB
                           INCLUDE COM2.CMB
                           <some code here>
                           CALL SUB1
                           CALL SUB2
                           CALL EXIT
                           END

                           SUBROUTINE SUB1
                           INCLUDE COM1.CMB
                           <some code here>
                           RETURN
                           END

                           SUBROUTINE SUB2
                           INCLUDE COM2.CMB
                           <some code here>
                           RETURN
                           END

     Notes:

     INCLUDE statements must begin immediately in column 7 or after  a
     tab character.


FLECS/RT-11 V28 USER'S GUIDE                                        20



     DEV:FILNAM.EXT must be separated from the INCLUDE  keyword  by  1
     and only 1 space.

     A file which is being included may not include another file (i.e.
     INCLUDE nesting is only 1 deep).

     If the device "DEV:" is not given in the file specification, then
     the standard user default device "DK:" is used.

     Inline comments may not be placed on the same line as an  INCLUDE
     statement.

     Use of the INCLUDE is especially usefull when there are  a  large
     number  of  programs  which  reference  the  same  COMMON  block.
     Normally, when changes occur to a  COMMON  block,  every  program
     which references it must be individually edited.  If however, the
     COMMON block is in its own file and INCLUDEd into  the  programs,
     then  only  the one file need be edited.  The common block change
     will be in effect when each program is re-translated.


FLECS/RT-11 V28 USER'S GUIDE                                        21



6.   OTHER FLECS/RT-11 FEATURES     _____ ___________ ________

6.1  EXTENDED VARIABLES     ________ _________

     FORTRAN/RT-11 allows the use of variable names  longer  than  six
     characters   (although   only   the   first  6  are  recognized).
     Unfortunately, variables like "ENDOFFILE" or "VALOFXSQUARED"  are
     not very readable.

     FLECS/RT-11 allows the underscore character "_"  to  be  used  as
     part  of  a  variable  name.   Hence,  the  above examples may be
     written as  "END_OF_FILE"  or  "VAL_OF_X_SQUARED"  which  greatly
     enhances their readability.

     Notes:

     All that the current implementation does to the "_" characters it
     encounters, is to replace them with the character "I".  Hence the
     variable "END_OF_FILE" would be seen in the FORTRAN  compiler  as
     "ENDIOF".

     Users  should  be  careful  that  the  names  of  variables  with
     underscores  in  them  do  not inadvertantly clash with variables
     used  elsewhere.   For  example,  the  variables  "INITIAL"   and
     "IN_T_AGAIN" both work out to be "INITIA".


FLECS/RT-11 V28 USER'S GUIDE                                        22



7.   RESTRICTIONS     ____________

     If FLECS were implemented by a nice  intelligent  compiler,  this
     section  would  be  much  shorter.   Currently  however, FLECS is
     implemented by a sturdy but naive  translator.   Thus  the  FLECS
     programmer must observe the following restrictions.

7.1  STATEMENT NUMBERING     _________ _________

     FLECS must invent many statement numbers in creating the  FORTRAN
     program.   It does so by beginning with 32767 (the largest 16 bit
     integer) and generating successively smaller numbers as it  needs
     them.

     Never use a statement number which is likely to  be  produced  by
     the  translator.   A good rule-of-thumb is to avoid using 5 digit                                                   _____ _____ _ _____
     statement numbers.     _________ _______

7.2  VARIABLE CONVENTIONS     ________ ___________

     The FLECS translator must generate integer  variable  names.   It
     does  so  by  using names of the form "Innnnn" where nnnnn is a 5
     digit number generated similar to the statement numbers mentioned
     in section 7.1.

     Never use a variable of the form "Innnnn" which is likely  to  be
     produced  by  the  translator.   A good rule-of-thumb is to avoid                                                                 _____
     using variables of the form "Innnnn".     _____ _________ __ ___ ____ _________

7.3  TYPE DECLARATIONS___  ____ ____________

     FLECS generates variables of the  form  "Innnnn"  which  must  be
     INTEGER.  Never cause them to be declared as any other type.

     For example  the  declaration  "IMPLICIT  REAL  (A-Z)"  leads  to
     trouble.  Try "IMPLICIT REAL (A-H,J-Z)" instead.

7.4  CONTINUATION LINES     ____________ _____

     The translator does  not  recognize  continuation  lines  in  the
     source  file.   This  doesn't  mean that they can't be used, just
     that the translator doesn't recognize them.

     Pure FORTRAN statements may be continued since each statement and                             ___
     its  continuations  will be passed through the translator without
     alteration (see section 1.6).  Extended FLECS statements however,                                    ________ _____ __________ ________
     may not be continued (including the IF statement).     ___ ___ __ _________

     Note that the FORTRAN/RT-11 convention of a tab,  followed  by  a
     numeric  character denoting a continuation line, may not be used.
     FORTRAN continuation lines must begin in column  6  with  leading     _______ ____________ _____ ____ _____ __ ______  _  ____  _______
     spaces only (i.e.  no leading tabs).     ______ ____ _____  __ _______ _____

     The reasons one might wish to continue a FLECS statement  are  1)
     it  is a structured statement or procedure declaration with a one


FLECS/RT-11 V28 USER'S GUIDE                                        23



     statement scope too long to fit on a line, or 2) it  contains  an
     excessively  long specification portion, or 3) both of the above.
     Problem 1 can  be  avoided  by  going  to  the  multi-line  form.
     Frequently, problem 2 can be avoided when the specification is an
     expression (logical or otherwise), by assigning the expression to
     a  variable  in a preceding statement and then using the variable
     as the specification.

7.5  BLANKS ARE SEPARATORS     ______ ___ __________

     Blanks are meaningful separators in FLECS statements.  Don't  put     ______ ___ __________ __________ __ _____ __________
     them  in  dumb  places like the middle of identifiers or keywords
     and do use them to separate distinct words like REPEAT and UNTIL.         __

7.6  FLECS INDENTATION     _____ ___________

     User indentation  will  be  ignored  by  FLECS;   this  way,  the
     listings will always reveal the true structure of the program (as
     understood by the translator, of course).

7.7  FORMAT STATEMENT PLACEMENT     ______ _________ _________

     As far as the translator  is  concerned,  FORMAT  statements  are
     executable  FORTRAN statements since it doesn't recognize them as
     extended FLECS statements.  Thus, only  place  FORMAT  statements                                       ____  _____  ______  __________
     where an executable FORTRAN statement would be acceptable.     _____ __ __________ _______ _________ _____ __ __________

     It is recomended that FORMAT statements be placed after any  data
     declarations but before the body of the program.

     Don't put them between the end of a WHEN and the beginning of  an
     ELSE or between procedure declarations.

     Incorrect examples:

                           WHEN (FLAG) WRITE (1,1)
                     1     FORMAT(' TITLE:')
                           ELSE LINE=LINE+1


                           TO WRITE-HEADER
                           .  PAGE=PAGE+1
                           .  WRITE (1,1) PAGE
                           ...FIN
                     1     FORMAT(' PAGE:  ',I3)

7.8  RESERVED WORDS     ________ _____

     The translator, being simple-minded,  recognizes  extended  FLECS
     statements by the process of scanning the first identifier on the
     line.  If the identifier is one of the FLECS keywords  (IF,  WHEN
     etc.)  the  line  is  assumed  to be an extended statement and is
     treaded as such.  Thus, FLECS keywords are reserved words and may                             _____ ________ ___ ________ _____ ___ ___
     not be used as variable names.     ___ __ ____ __ ________ _____


FLECS/RT-11 V28 USER'S GUIDE                                        24



     Should it be absolutely necessary, a variable name, say WHEN, may
     be  slipped  past  the translator by embedding a blank within it.
     Thus "WH EN"  will  look  like  "WH"  followed  by  "EN"  to  the
     translator  which  is  blank  sensitive,  but  like "WHEN" to the
     compiler which ignores blanks.

7.9  PARENTHESES AND HOLLERITH CONSTANTS     ___________ ___ _________ _________

     In scanning a parenthesized specification, the  translator  scans
     from  left  to  right to find the right parenthesis which matches
     the  initial  left  parenthesis  of   the   specification.    The
     translator,  however, is ignorant of FORTRAN systax including the
     concept  of  Hollerith  constants  and   will   treat   Hollerith
     parentheses as syntactic parentheses.

     Never place Hollerith constants containing unbalanced parentheses     _____ _____ _________ _________ __________ __________ ___________
     within specifications.     ______ ______________

     If necessary, assign such constants to a variable and  place  the
     variable in the specification.

     Incorrect Example:

                           IF (J.EQ.'(') DO-SOMETHING

     Correct Example:

                           LP='('
                           IF (J.EQ.LP) DO-SOMETHING

7.10 RETURNS,STOPS AND EXITS     _____________ ___ _____

     The FLECS translator will not supply the statements necessary  to
     cause  appropriate  termination of main and subprograms.  Thus it                                                                    __
     is necessary to include the appropriate RETURN, STOP or CALL EXIT     __ _________ __ _______ ___ ___________ _______ ____ __ ____ ____
     statement  prior  to  the  first  internal procedure declaration.     _________  _____  __  ___  _____  ________ _________ ___________
     Failure to do so will result in control entering the scope of the
     first procedure after the body of the program.

     One mistake often made by novice FLECSers is to  put  the  RETURN
     statement   between   the  procedure  declarations  and  the  END
     statement.

7.11  EXCLAMATION MARKS AND UNDERSCORES      ___________ _____ ___ ___________

     Exclamation marks "!" and underscores "_" have  special  meanings
     to  the translator (inline comments and extended variables).  The
     underscore character may not be used in literal  strings  of  the                          ___ ___
     form  '_'  and  both may only use the form "1H!".  The translator
     recognizes the "1H"  and  will  not  action  the  normal  special
     meaning.


FLECS/RT-11 V28 USER'S GUIDE                                        25



8.   HINTS TOWARDS A CODING STANDARD     _____ _______ _ ______ ________

     There have been numerous specifications written on how one should
     go about developing top-down structured programs.  In most cases,
     the points  brought  out  are  no  more  than  good  common-sense
     programming practices.

     As an aid to programmers, the following hints should  be  helpful
     in  writing  good  FLECS  code  which  will  be both readable and
     maintainable.

8.1  MODULARITY     __________

     Each individual program used to implement functions at all levels
     of   the   software   hierarch   should  be  highly  independent,
     single-functioned modules.

8.2  MODULE READABILITY     ______ ___________

     A module should never exceed 200 lines of code and  the  body  of
     the program should be easily readable on one page.

     Implement the body such that the use of internal  procedures  and
     subroutine  calls,  coupled  with the flow-control, makes it read
     almost like pseudo-code.

8.3  USE OF INTERNAL PROCEDURES     ___ __ ________ __________

     Don't go internal procedure crazy.  Novice FLECSers fall  quickly
     in  love  with  them and wind up with one huge, slow to translate
     file.  Use internal procedures only when the routine is  discrete
     to  a  given  program.   Use the call mechanism when a routine is
     referenced from many different programs.  For example:

                           CALL INIT !TO INITIALIZE THE DATA BASE

                       vs. INITIALIZE-THE-DATA-BASE

     Note also that CALLed subroutines may  be  overlayed  (using  the
     nice RT-11 overlay feature) but internal procedures cannot.


8.4  GLOBAL DEFINITIONS     ______ ___________

     All references to centralized assignments and definitions  should
     be coherently generated using the "INCLUDE" statement rather than
     retyping all the required references in each and every program.

8.5  SOURCE FILES     ______ _____

     Each  module  should  be  contained  in  its  own  source   file.
     Subroutines and function subprograms which are called by only one
     module should be included in the same file.


FLECS/RT-11 V28 USER'S GUIDE                                        26



8.6  USE LOGICAL VARIABLES     ___ _______ _________

     FLECS tends to require  the  use  of  flow  control  flags.   Use
     "LOGICAL*1"  data  for  this  purpose  rather  than numeric value
     checking, the result will be more readable.

     Bad example:

                           REPEAT UNTIL (I.EQ.1)
                           .  I=INPUT(DATA)
                           .  UNLESS (I.EQ.1) CALL OUTPUT(DATA)
                           ...FIN
                           END

     Good example: (at least more readable)

                           LOGICAL*1 END_OF_FILE,INPUT
                                
                           REPEAT UNTIL (END_OF_FILE)
                           .  END_OF_FILE=INPUT(DATA)
                           .  UNLESS (END_OF_FILE) CALL OUTPUT(DATA)
                           ...FIN
                           END

8.7  NEVER GOTO     _____ ____

     Never use a "GOTO" statement, there is always  another  way.   If                                            ______
     you  think you must, for the purpose of an "abnormal" exit from a
     loop  (or  something),  then   review   your   basic   structured
     programming.  Set a flag!  Set a flag!  Set a flag!


FLECS/RT-11 V28 USER'S GUIDE                                        27



9.   RUNNING THE TRANSLATOR     _______ ___ __________

     Special care has been taken to ensure  that  this  implementation
     "follows  the  rules" for RT-11 system programs.  It works pretty
     much like you would expect (assuming you have  used  other  RT-11
     programs) and should offer no surprises.

9.1  STARTING THE TRANSLATOR     ________ ___ __________

     FLECS is normally on the system disk "SY:" and  is  started  with
     the KMON command "R".  For example:

                           .R FLECS<ret>

     If FLECS is on the user disk, or some other media, it is  started
     with the KMON command "RUN".  For example:

                           .RU DT1:FLECS<ret>

     Note:  <ret> denotes the "return" key on the keyboard.

9.2  COMMAND STRING INTERPRETOR (CSI) INPUT     _______ ______ ___________ _____ _____

     Control input to the FLECS  translator  is  via  a  standard  CSI
     command of the form:

          [fort-out][,list-out]=flecs-input

     Notes:

     Each field (fort-out, list-out etc.) is a file  specification  of
     the form "DEV:FILNAM.EXT".

     Fields enclosed in square brackets "[]"  indicate  optional  file
     specifications.

     The default device for all file specifications  is  the  standard
     user default "DK:".

     The "flecs-input" file contains the FLECS source code.

     The "fort-out" file, if specified, receives the generated FORTRAN
     source code.

     The  "list-out"  file,  if  specified,  receives   the   indented
     listings.

     The default extension for "fort-out" is ".FOR".

     The default extension for "list-out" is ".LST".

     The default extension for "flecs-input" is ".FLX".



FLECS/RT-11 V28 USER'S GUIDE                                        28



9.3  CSI SWITCHES     ___ ________

     The following switches may be used to enhance the  FLECS  control
     commands.

     /W:n Select  listing  width  n  where  64<=n<=136.   The  default
          listing width is 132.

     /X   Translate all lines with an X in column 1 independant of any                    ___
          conditional  translation  requests made using the $X and $NX
          directives.

     /S   Place the FLECS line numbers into the sequence  position  of
          the  generated  FORTRAN  code.   This is occasionally useful
          when relating the FLECS sources to the FORTRAN sources.

     /F   Generate a FORTRAN file of the same name  and  on  the  same
          device  as  the  FLECS  input  file.   The CSI specification
          "*ABC/F" would be exactly the same as "*ABC=ABC".

     /L   Generate a listing file of the same name  and  on  the  same
          device  as  the  FLECS input file.  The CSI command "*ABC/L"
          would be exactly the same as "*,ABC=ABC".

     /P   Generate a listing on the printer "LP:".   The  CSI  command
          "*ABC/P" is exactly the same as "*,LP:=ABC".

     /T   Generate a listing on the system  console  "TT:".   The  CSI
          command "*ABC/T" is exactly the same as "*,TT:=ABC".

     /I   Indent the source file to produce a new source file that has
          the  same  indentation  as  the  corresponding listing-file.
          This is often useful for editing purposes.  No  output  file
          specifications  may  be  given  with /I;  output goes to the
          file "DK:FLECS.TMP".  Upon completion, the flecs-input  file
          is  renamed  to have the extension ".BAK" and "DK:FLECS.TMP"
          is renamed to the same  name  as  the  original  flecs-input
          files.

     /N   Suppress processing of INCLUDE directives.  This  switch  is
          selected automatically with /I.

9.4  NULL HANDLER     ____ _______

     When no FORTRAN or listing output is requested,  output  goes  to
     the  bit-bucket  device  "NL:".   For  correct operation the null                                                              ___ ____
     device handler "NL:" must be installed.     ______ _______ _____ ____ __ _________

9.5  EXAMPLES     ________

     To translate the file "DK:ABC.FLX"  into  "DK:ABC.FOR"  and  then
     compile  it  into  "DK:ABC.OBJ",  both  of the following examples
     could be used.  Listings are sent to "LP:".


FLECS/RT-11 V28 USER'S GUIDE                                        29



     Example 1

                 .INS NL:          !If not already done.
                 .R FLECS<ret>     !Start the translator.  
                 *ABC,LP:=ABC<ret> !Tell it what to translate.
                 *^C               !Return to KMON via a control C.
                 .R FORTRAN<ret>   !Start the FORTRAN compiler.
                 *ABC,LP:/L:MAP=ABC<ret> !List only the map portion.
                 *^C               !Return to KMON via a control C.

     Example 2


                 .R FLECS<ret>     !Start the translator.  
                 *ABC/P/F<ret>     !Use /P and /F to specify output.
                 .FORT/LIST/SHOW:MAP ABC !High level compile.

9.6  OPERATION UNDER TSX     _________ _____ ___

     Under  the  TSX  time-sharing  executive  for  RT-11  (circa  S&H
     Computer  Leasing , Nashville Tenn.), the FLECS translator may be
     invoked via a pseudo high-level command (assuming FLECS.SAV is on
     SY:).   To  perform the same functions as the examples of section
     9.5, the following commands could be used.

     Example 3


                 .FLECS ABC/P/F  !High level translation.
                 .FORT/LIST/SHOW:MAP ABC !High level compile.


FLECS/RT-11 V28 USER'S GUIDE                                        30



10.  ERROR HANDLING     _____ ________

     This section provides a framework  for  understanding  the  error
     handling  mechanisms  of version 28 of the FLECS translator.  The
     system described below is at an early point in its evolution, but
     has proven to be quite workable.

     The FLECS translator examines a FLECS program on  a  line-by-line
     basis.   As  each line is encountered, it is first subjected to a
     limited syntax analysis followed by a context  analysis.   Errors
     may  be  detected  during  either  of these analyses.  It is also
     possible for errors to go undetected by the translator.

     Note that the occurrence  of  any  major  error  will  cause  the
     translator  to  cease generating any FORTRAN output (although the
     FLECS listing and error logging will of course continue).

10.1 SYNTAX ERRORS     ______ ______

     When a syntax error is detected, the statement  is  ignored.   On                                      ___ _________  __  _______
     the FLECS listing the line number of the statement is overprinted
     with dashes to indicate that the statement has been ignored.  The
     nature of the syntax error is given in a message on the following
     line.

     The fact that a statement has been ignored may, of course,  cause
     some  context  errors  in  later  statements.   For  example, the
     control  phrase  "WHEN (X(I).LT.(3+4)"  has   a   missing   right
     parenthesis.   This  statement  will  be  ignored,  causing  as a
     minimum, the  subsequent  "ELSE"  to  be  out  of  context.   The
     programmer  should  of  course be aware of such effects.  More is
     said about them in the next section.

10.2 CONTEXT ERRORS     _______ ______

     If a statement successfully passes the  syntax  analysis,  it  is
     checked  to  see  if  it is in the appropriate context within the
     program.  For example, an ELSE must appear following a  WHEN  and
     nowhere  else.   If  an  ELSE  does not appear at the appropriate
     point or if it appears at some other point, then a context  error
     has occurred.  A frequent source of context errors in the initial
     stages of development, comes from miscounting the number of  FINs
     needed at some point in the program.

     With the  exception  of  excess  FINs  which  do  not  match  any
     preceding  control  phrase  and  are  ignored  (as  indicated  by
     overprinting the line number), all  context  errors  are  treated
     with a uniform strategy.  When an out-of-context source statement
     is encountered, the translator generates a "STATEMENT(S)  NEEDED"
     message.   It then invents and processes a sequence of statements
     which, if they had been included at that point  in  the  program,
     would  have  placed  the  original  source statement in a correct
     context.  A message is given for each  such  statement  invented.
     The  original  source  statement  is  then processed in the newly
     created context.


FLECS/RT-11 V28 USER'S GUIDE                                        31



     By inventing statements, the translator is not trying to patch up
     the program so that it will run correctly, it is simply trying to
     adjust the local context so that the  original  source  statement
     and  the  statements which follow will be acceptable on a context
     basis.  As in the case of context errors generated by ignoring  a
     syntactically  incorrect statement, such an adjustment of context
     frequently causes further  context  errors  later  on.   This  is
     called propagation of context errors.            ___________ __ _______ ______

     One nice feature of  the  context  adjustment  strategy  is  that
     context  errors  cannot  progagate  past a recognizable procedure
     declaration.  This is because the "TO" declaration is in  context
     only  at  indentation  level 0.  Thus to place it in context, the
     translator must invent enough statements to  terminate  all  open
     control  structures  which  procede the "TO".  The programmer who
     modularizes his program into a  collection  of  relatively  short
     internal  procedures,  limits  the  potential  for propagation of
     context errors.

10.3 UNDETECTED ERRORS     __________ ______

     The FLECS translator is  ignorant  of  most  details  of  FORTRAN
     syntax.   Thus most FORTRAN syntax errors will be detected by the
     FORTRAN compiler not the FLECS translator.   In  addition,  there
     are two major classes of FLECS errors which will be caught by the
     compiler not the translator.

     The first class of undetected  errors  involve  misspelled  FLECS
     keywords.   A  misspelled  keyword  will not be recognized by the
     translator.  The line on which it occurs will be assumed to be  a
     FORTRAN  statement  and will be passed unaltered to the compiler,
     which will no doubt object to it.  For example, a common error is
     to  spell  UNTIL  with two Ls.  Such statements are passed to the
     compiler, which then produces an error message.  The fact that an
     intended  control  phrase  was not recognized frequently causes a
     later context error since a level  of  indentation  will  not  be
     triggered.

     The  second  class  of  undetected  error   involves   unbalanced
     parentheses.   When  scanning  a parenthesized specification, the
     translator is looking for a matching right parenthesis.   If  the
     matching  parenthesis  is encountered before the end of the line,
     the remainder of the line is scanned.  If the remainder is  blank
     or  consists  of a recognizable internal procedure reference, all
     is well.  If neither of the above two cases hold,  the  remainder
     of  the line is assumed (without checking) to be a simple FORTRAN                     _______
     statement which is passed  to  the  compiler.   Of  course,  this
     assumption may be wrong, thus the statement

                           WHEN (X.LT.A(I)+Z)) X=0

     is broken into keyword "WHEN", specification "(X.LT.A(I)+Z)"  and
     FORTRAN  statement  ") X=0".   Needless to say, the compiler will
     object to ") X=0" as a statement.


FLECS/RT-11 V28 USER'S GUIDE                                        32



10.4 FORTRAN/RT-11 OTS ERRORS     _____________ ___ ______

     The FLECS translator is itself a FLECS program and,  at  runtime,
     it  operates  with  the standard FORTRAN/RT-11 object time system
     (OTS).   Occasionally,  the  translator  will  bomb-out  with  an
     appropriate OTS error message.

     Usually, these errors are a result  of  how  you  are  using  the
     system  (like  trying  to  get  a  listing on a non-existant line
     printer), rather than as a result of a programming error.   There
     is  one  case  however, where this is not so;  if an OTS error 28
     (OPEN FAILED FOR FILE) occurs, it could be that the  flecs-input,
     stated  in the CSI command string, could not be found or that the                                                                   ___
     file specification used in an  INCLUDE  statement  could  not  be     ____ _____________ ____ __ __  _______  _________  _____  ___  __
     found.  Mysterious error 28s are usually traced to the latter.     _____

10.5 OTHER ERRORS     _____ ______

     The translator detects a variety of other errors such as multiply
     defined,  or  undefined procedure references.  The error messages
     are self-explanatory (really and truly!!).


FLECS/RT-11 V28 USER'S GUIDE                                        33



A.   INSTALLATION NOTES     ____________ _____

     This appendix  contains  the  information  necessary  to  install
     implementation 28 of the FLECS/RT-11 translator.


A.1  BEFORE YOU START     ______ ___ _____

     Copy the distribution kit to a working disk, you should  not  use
     the original just in case something goes wrong.


A.2  CONTENTS OF THE DISTRIBUTION KIT     ________ __ ___ ____________ ___


     FLECS .DOC - This file.

     FLXDOC.RNO - The RUNOFF version of this file.

     FLXREN.DOC - Implementation release notes.

     FLXMIN.SAV - An executable version of the translator  which  will
                  run   on  a  minimal  RT-11  system  (16KW  with  SJ
                  monitor).  It is fully overlayed,single-buffered and
                  linked against a NHD library.

     FLXREG.SAV - An executable version of the translator  which  will
                  run   on  a  typical  RT-11/PDP-11  system.   It  is
                  minimally  overlayed,  double-buffered  and   linked
                  against an NHD library.

     FLXGEN.COM - A  command  file  for  automatic   translation   and
                  compilation of pre-processor itself.

     FLXHDR.FLX - Header information to be INCLUDEd into  each  source
                  file.

     FLXBLK.FLX - Blockdata for common system parameters.

     FLECS .FLX - Main line source code file.

     FLXIO .FLX - RT-11 I/O interface sources.

     FLXGO .FLX - RT-11 file initialization sources.

     FLXGOS.FLX - Same as FLXGO.FLX but for single buffered I/O.

     FLXANL.FLX - Analyzer sources.

     FLXLST.FLX - Listing generator sources.

     FLXSUP.FLX - Miscellaneous support program sources.

     DATIME.FLX,DATEIN.FLX,TIMEIN.FLX - Date and time entry demo.


FLECS/RT-11 V28 USER'S GUIDE                                        34



A.3  RUNABLE TRANSLATORS DISTRUBUTED     _______ ___________ ___________

     There are two runable versions of the translator included in  the
     distribution  kit, FLXMIN and FLXREG;  the attributes of each are
     discribed in section A.2.

     It may be that one of the distributed versions will satisfy  your
     requirements.   If  this is the case, simply copy the appropriate
     one to SY:FLECS.SAV and you are ready to  go.   If  not,  then  a
     complete  build  will  have  to  be  performed as outlined in the
     following sections.


A.4  INSTALLATION STEPS     ____________ _____

     The following steps outline the installation procedure.

     1 - Select the most useable, distributed runable version  of  the
     translator.   FLXMIN  is  small enough to run on a 16KW SJ system
     but is very slow.  If you have more than 24KW, use FLXREG.

     For the purpose of building a  tailored  translator,  rename  the
     selected translator to "FLECS.SAV".  For example;

                           .COPY FLXREG.SAV FLECS.SAV

     2 - Translate the  .FLX  sources  into  .OBJ  modules  using  the
     supplied FLXMIN and your FORTRAN compiler.

     3 - Link the .OBJ modules to create FLECS.SAV, a version  of  the
     preprocessor tailored for your specific system.

     4 - Test FLECS.SAV by retranslating and compiling the distrubuted
     source files.


A.5  TO COMPILE THE SOURCES     __ _______ ___ _______

     The source files may be translated into the .OBJ modules using  a
     command  file  supplied  for  this  purpose "FLXGEN.COM", or done
     manually.  If done manually, print a  copy  of  "FLXGEN.COM"  and
     "play it by ear".  To use the command file enter:

                           .ASSIGN xxx: DK:
                           .ASSIGN yyy: OUP:
                           .@FLXGEN

     Where "xxx" is the source input device and "yyy"  is  the  target
     device which is to receive the .OBJ modules.  "xxx" and "yyy" may
     be the same device.  FLECS.SAV is sent to SY:.

     Notes

     The source files must be on device 'DK:' so that  INCLUDEd  files                      ____
     may be found.


FLECS/RT-11 V28 USER'S GUIDE                                        35



     There must be at least 250 contiguous free blocks on  the  output
     device for the translation to be successful.

     Example

     If the sources are on a diskette mounted in  DY0:   and  an  RL01
     mounted  in  DL1:   is  to  be  used  for  the  object files, the
     following commands should be entered.

                           .ASSIGN DY0: DK:
                           .ASSIGN DL1: OUP:
                           .@FLXGEN
                           -compilation log given here -
                           *ignore any compilation warnings*

A.6  LINKING FLECS.SAV     _______ _________

     There are numerous ways  in  which  the  object  modules  may  be
     linked, depending on your particular system's configuration.  The
     following examples illustrate.

     1 - FORTRAN library part of SYSLIB and SJ or  FB  is  used  on  a
     system with full memory (28KW).

                           .R LINK
                           *SY:FLECS=OUP:FLECS,FLXSUP,FLXIO/I/C
                           *OUP:FLXBLK/C
                           *OUP:FLXANL/C
                           *OUP:FLXLST/O:1/C
                           *OUP:FLXGO/O:1
                           Library search? $SHORT
                           Library search? <ret>
                           *^C

     2 - FORTRAN library part of SYSLIB and SJ used on a  system  with
     minimum useable memory (or for use under TSX).

                           .R LINK
                           *SY:FLECS=OUP:FLECS,FLXSUP,FLXIO/I/C
                           *OUP:FLXBLK/C
                           *OUP:FLXANL/O:1/C
                           *OUP:FLXLST/O:1/C
                           *OUP:FLXGOS/O:1
                           Library search? $SHORT
                           Library search? <ret>
                           *^C


FLECS/RT-11 V28 USER'S GUIDE                                        36



     3 - FORTRAN library in file "SY:FORLIB.OBJ"  and  SJ  used  on  a
     system with minimum memory (16KB).

                           .R LINK
                           *SY:FLECS=OUP:FLECS,FLXSUP,FLXIO/F/I/C
                           *OUP:FLXBLK/C
                           *OUP:FLXANL/O:1/C
                           *OUP:FLXLST/O:1/C
                           *OUP:FLXGOS/O:1
                           Library search? $SHORT
                           Library search? <ret>
                           *^C

     4 - FORTRAN library in file "SY:FORLIB.OBJ"  and  XM  used  on  a
     system  with  extended  memory (RT-11 V04 and FORTRAN V2.5 only).
     The extended memory support module in file "SY:EXTEND.OBJ".

                           .R LINK
                           *SY:FLECS=OUP:FLECS,FLXSUP,FLXIO/I/V/C
                           *SY:EXTEND/C
                           *OUP:FLXBLK/C
                           *OUP:FLXANL/V:1:1/C
                           *OUP:FLXLST/V:1:2/C
                           *OUP:FLXGOS/V:1:2
                           Library search? $SHORT
                           Library search?  <ret>
                           *^C

     Note:  FLXANL,FLXLST and FLXGO or  FLXGOS  may  be  be  overlayed
     against each other in any disk or virtual scheme.

A.7  TO TEST YOUR FLECS.SAV     __ ____ ____ _________

     To  test  your  tailored  version   of   the   translator,   copy
     "SY:FLECS.SAV" to "DK:FLECS.SAV" and @FLXGEN again.

A.8  DEC SOFTWARE VERSIONS     ___ ________ ________

     The above installation procedure assumes RT-11 V03, RT-11 V03B or
     RT-11 V04.  If an earlier version is used, you will have to enter
     the command files by  hand  (or  edit  them  into  batch  files).
     Subsequent releases after RT-11 V04 should be compatible.

     FORTRAN V02.5 or  FORTRAN  V02.1  with  Software  dispatch  patch
     number  5 installed should be used.  To use an earlier version or
     V02.1 without patch 5, the carriage  control  parameters  of  the
     IASIGN calls in FLXGO.FLX will have to be complimented.


FLECS/RT-11 V28 USER'S GUIDE                                        37



B.   FLECS SUMMARY     _____ _______


B.1  EXTENDED FLECS STATEMENTS     ________ _____ __________

     IF           - Execute the scope if the condition is true.

     UNLESS       - Execute the scope if the condition is false  (i.e.
                    unless the condition is true).

     WHEN/ELSE    - Execute the scope of the WHEN if the condition  is
                    true, else execute the scope of the ELSE.

     CONDITIONAL  - Execute the scope of  the  first  condition  found
                    true.

     SELECT       - Execute the scope of the first element to which  a
                    match is made.

     DO           - Repeat the  scope  for  the  specified  number  of
                    times.

     WHILE        - Execute the scope while a condition is true.

     UNTIL        - Execute the scope while a condition is false (i.e.
                    until it is true).

     REPEAT WHILE - Execute the scope until a condition becomes false.

     REPEAT UNTIL - Execute the scope until a condition becomes true.


B.2  TRANSLATION DIRECTIVES     ___________ __________

     $F/$NF       - Turns FORTRAN output generation on/off.

     $L/$NL       - Turns listing output generation on/off.

     $P           - Causes listing to go to top-of-form.

     $X/$NX       - Turns conditional translation of lines with an "X"
                    in column 1 on/off.

     INCLUDE      - Includes source lines from an alternate  secondary
                    input file.