An RT-11 Application








                          N. A. Bourgeois, Jr.
                      Sandia National Laboratories
                   Systems Engineering Division 1738
                             P. O. Box 5800
                         Albuquerque, NM 87185








                                Abstract


             An application of the RT-11  single-user  operating
        system  is  described.   The  application  involves  the
        development of real time  signal  processing  algorithms
        for  a  dedicated  microcomputer  system.   The hardware
        included in the seven systems  of  this  application  is
        discussed.   Reasons  for the selection of and continued
        use of RT-11 are given.








                                 80j15a


                                                        Page   1
                                                       16 Oct 80


















                This  document  is  issued   by   Sandia
                National  Laboratories, operated for the
                United States Department  of  Energy  by
                Sandia Corporation.


                                 Notice


                This  document  was  sponsored  by   the
                United  States  Government.  Neither the
                United States Government nor the  United
                States  Department of Energy, nor any of
                their  employees,  nor  any   of   their
                contractors,  subcontractors,  or  their
                employees makes any warranty, express or
                implied,  or assumes any legal liability
                or  responsibility  for  the   accuracy,
                completeness   or   usefulness   of  any
                information,   apparatus,   product   or
                process  disclosed,  or  represents that
                its use  would  not  infringe  privately
                owned rights.


                This work was sponsored and funded by:

                    Headquarters, ESD / OCB / Stop 36
                    Hanscom Air Force Base, MA 01731


                                                        Page   2
                                                       16 Oct 80






                              Introduction


             Our groups task at the Sandia National Laboratories
        is  the  development of signal processing algorithms for
        intrusion   detection   applications.    This   includes
        execution both in real time and with recorded data.  The
        ultimate goal is a dedicated microprocessor  system  for
        each  of  these applications.  We are using seven PDP-11
        family machines as tools to achieve this end.

             We selected RT-11 [1] for its fast response and its
        ability  to  operate  on  the  LSI-11  as well as on the
        larger PDP-11 machines.  We plan to continue using RT-11
        and  would  select  it  again  if  we were starting over
        today.



                                Hardware


             During  the  course  of  this  project  our   tools
        (PDP-11'S)  have grown from one PDP-11/10 and one LSI-11
        to one PDP-11/34, one PDP-11/10 and five  LSI-11's.   We
        are currently upgrading the PDP-11/34 to a PDP-11/60 and
        the PDP-11/34 will replace the PDP-11/10.  I  shall  now
        describe these systems as if our present upgrade program
        were completed.

             The two larger machines and three of  the  LSI-11's
        are   permanently   located   in   our  laboratories  in
        Albuquerque.  One LSI-11 is  configured  as  a  portable
        system   and   one  LSI-11  is  installed  in  a  mobile
        laboratory.  The UNIBUS machines have  four  RK05's,  an
        RX02  and 128K words of memory.  The Q-BUS machines each
        have an RX02 and 32K words  of  memory.   The  PDP-11/34
        also  has  an  additional  RX02, a line printer, and two
        nine-track mag tape units.



                              Utilization


             There is consideral overlap in the  utilization  of
        our  computer  systems.  Software development may be and
        is done to some  degree  on  all  machines.   Also,  all
        systems  are  capable  of performing data analysis.  The
        LSI-11's are used  for  data  recording  and  real  time
        playback.


                                                        Page   3
                                                       16 Oct 80


             PDP-11/60.  This system is used primarily for  data
        analysis.   It  is  also  used  for  original  algorithm
        development using recorded data.   There  are  two  work
        stations  tied to this system.  Each station consists of
        a VT52 and a Tektronix 4015 with a 4631 hard copy unit.

             PDP-11/34.    This   is   our   primary    software
        development    system.     Operating   system   software
        maintenance is performed here.  System software for  all
        PDP-11 family machines is supported from this PDP-11/34.
        There are four VT100 work  stations  connected  to  this
        system.

             LSI-11 (Computer room system).  The initial testing
        of  real time implementations of both data recording and
        signal processing algorithms is done on  this  computer.
        I  try  to maintain on this machine at least one each of
        any device that is on any of the other LSI-11's.

             LSI-11 (Dual system).  Testing  of  various  target
        microprocessor systems is accomplished in the laboratory
        with this dual processor system.  One  CPU  is  used  to
        control  and  to deliver one or two channels of recorded
        data in real time to  a  target  microprocessor  system.
        The second CPU monitors the progress of the system under
        test.

             LSI-11 (Portable system).  This system is  packaged
        to  be  airline  checkable.   It  is  used for both data
        acquisition and real time  algorithm  execution  in  the
        field.

             LSI-11 (Mobile system).   A  motor  home  converted
        into  a  mobile  laboratory  houses  this  system.   Its
        primary function is to control and monitor  up  to  four
        target   microprocessor  systems  in  the  field.   Data
        acquisition and real time algorithm  execution  is  also
        accomplished with this machine.



                                Software


             RT-11 is the only DEC disk operating system capable
        of  running on all of our PDP-11 family computers.  Most
        of our data rates are handled with  ease  under  RT-11's
        interrupt   protocol.    On  occasion  we  must  run  an
        interrupt service routine outside of the  system,  which
        incidently, RT-11 does permit.

             A near RT-11 environment is provided on our  larger
        machines  with a time sharing executive [2] from another
        vendor.  Thus, we use essentially the syntax of only one
        operating  system on all of our computers while allowing


                                                        Page   4
                                                       16 Oct 80


        multiple user access to our larger machines.

             Our real time software is all written in  MACRO-11.
        Other application software is done in FORTRAN and PASCAL
        with some even in BASIC.  Our technique is to develop an
        algorithm   using  FORTRAN,  then  to  implement  it  in
        MACRO-11 using integer arithmetic.  Once this real  time
        code  is  proven  both in the lab and in the field it is
        translated into the target microprocessor's language.















































                                                        Page   5
                                                       16 Oct 80






                               References


        1.  "RT-11, Version 4.0 Single-User  Operating  system",
            AE-3393M-TC, Digital Equipment Corporation, Maynard,
            MA, April 1980.

        2.  "General Release Notes for  TSX-Plus  Version  1.4",
            S & H Computer Systems, Inc., Nashville, TN.