BMUX

                    Burroughs Polling Protocol

                           MULTIPLEXOR




                               SAGE

                           division of

                  GENERAL SCIENTIFIC CORPORATION
                        966 Hungerford Dr.
                       Rockville, Md. 20850   

                           301-340-2773



                         TECHNICAL MANUAL


                        TABLE OF CONTENTS


BMUX USAGE INFORMATION
  Startup                                               1-1
  Console Commands                                      1-1
  Initialization of Operations                          1-2
  Status Information                                    1-2
  Suspension of Operations                              1-2

  Exit Procedure                                        1-2
  Configuration of Multiplexor                          1-2
  Console messages to a defined port                    1-4
  Software Problems                                     1-4

BMUX CONSOLE COMMAND SUMMARY
  PROCede                                               2-1
  HALT                                                  2-1
  MESSage##                                             2-1
  STATistics                                            2-1
  EXIT                                                  2-2

SOFTWARE PERFORMANCE REPORT
  SPR                                                   3-1

HARDWARE
  Processor option straping                             4-1
  Ports 0 to 3 option strapping                         4-3
  Ports 4 to 7 option strapping                         4-5
  Ports 8 to 11 option strapping                        4-6
  Ports 12 to 15 option strapping                       4-7

  Ports 16 to 19 option strapping                       4-8
  Ports 20 to 23 option strapping                       4-9
  Disk Controller                                       4-10
  Disk Drive                                            4-11
  Cable Wiring                                          4-12

BMUX MAINLINE LOGIC DOCUMENTATION
  Mainline Logic                                        5-1
  Interrupt Service Logic                               5-2
  Configuration Logic                                   5-2

SYSTEM SOFTWARE EQUATES
  SF1 (Source File 1)                                   6-1

SUPPORT SUBROUTINE DOCUMENTATION
  BTIME                                                 7-1
  GBUFC                                                 7-1
  SAVE                                                  7-1
  STOR                                                  7-2
  READ                                                  7-2

                        TABLE OF CONTENTS



  WRITE                                                     7-2
  FORCE                                                     7-2
  FNDCOM                                                    7-2
  JORSTA                                                    7-3
  REBUF                                                     7-3

  GPCBDA                                                    7-4
  CONWRI                                                    7-4
  PCBSET                                                    7-4
  BOMB                                                      7-4
  CONFDP                                                    7-4

  CONCMD                                                    7-4
  HLTPRO                                                    7-5
  START                                                     7-5
  STDISP                                                    7-5
  MSG                                                       7-5

  PROXIT                                                    7-5
  DISTAT                                                    7-6
  CONCPY                                                    7-6
  Canned Messages                                           7-6
  SF20 Module                                               8-1

  SF30 Module                                               8-1
  SF40 Module                                               8-2
  SF50 Module                                               8-3
  SF60 Module                                               9-1

BMUX DATA STRUCTURE DOCUMENTATION
  CR1-CR5                                                  10-1
  CR6                                                      10-1
  CRTAB                                                    10-1
  TRKSRP                                                   10-1
  CONFLG                                                   10-1

  TRAPA                                                    10-1
  TRDQ2                                                    10-1
  TSP-TEP                                                  10-1
  PSP-PEP                                                  10-2
  SPTR-PEN                                                 10-2

  PRPTR-TWPTR                                              10-2
  HALTFL                                                   10-2
  INIFLG                                                   10-2
  STDFLG                                                   10-2
  SPFUN                                                    10-2

  CCMD                                                     10-2
  ISRTAB                                                   10-2
  DA1-DA8                                                  10-2

                        TABLE OF CONTENTS


  ISRSAV                                                10-2
  CONSAV                                                10-3

  RCSRA-XBUFA                                           10-3
  RCSRI-XBUFI                                           10-3
  WAIT1-NEWSEC                                          10-3
  PAT                                                   10-3
  CUMTAB                                                10-3

  PCB                                                   10-3
  POLTAB                                                10-3
  TTYPE                                                 10-4
  BRTAB                                                 10-4
  PCBDAT                                                10-4

  TWBPCB                                                10-4
  RVITAB-JORST                                          10-4


                      BMUX USAGE INFORMATION

                  General Scientific Corporation
                          Rockville, Md.


1.   STARTUP

          The  BMUX software is normally booted automatically when
     the system is started by either a power-up  sequence  or  the
     depression and lifting of the "RUN" switch on the LSI-11. If,
     for some reason, the console terminal shows a period  (.)  on
     the  current  line,  it is probably awaiting user response to
     the RT-11 console prompt. in this case, enter:

                             RUN BMUX

     and  depress  the  RETURN  key.  This  will  start  the  BMUX
     software.  When the start sequence has run, regardless of the
     cause of its initiation, the BMUX software will announce  its
     readiness by displaying the message:

             **** BMUX INITIALIZED TO HALT MODE ****

     indicating that the console is functional and the software is
     ready for operation.

2.   CONSOLE COMMANDS

          The console terminal (Port 2) can asynchronously  access
     both  the  Burroughs and the multiplexor's control interface.
     If a console command  entry  is  desired,  the  user  of  the
     console  terminal  must  start  the  current  line  with  two
     Control-V's, created by simultaneously depressing the control
     and  "V" keys. The command must immediately follow the second
     control-V and be one of the following:

     A. PROC        Initiates multiplexor operations

     B. STAT        Generates a status  display  for  the  defined
                    trunk(s) and ports

     C. MESS ##     Sends the remainder of the line to Port ##, if
                    defined

     D. HALT        Temporarily suspends multiplexor operations by
                    preventing input by the ports

     E.   EXIT      (must be preceeded by the HALT command) causes
                    the multiplexor software to release control to
                    RT-11 (generally used to run the configuration
                    program)

          Invalid console command entry will  be  denoted  by  the
     appearence  of  either  "!!!!" (invalid command) or "MESS ??"

     (invalid port number). in the case where the  "EXIT"  command
     is  entered  but not preceeded by the "HALT" command, it will
     be ignored.


3.   INITIALIZATION OF OPERATIONS

          Enter the "PROC" console command to begin communications
     operations  between  the  port  terminals  and  the Burroughs
     mainframe.

4.   STATUS INFORMATION

          To examine the status of various ports and the trunk(s),
     use  the  "STAT"  console  command. Remember that the display
     values for traffic (TFC) and errors (ERR)  are  "wrap-around"
     counts.  This  means that an accurate traffic and error count
     over any timeframe is the  absolute  difference  between  the
     last set of values and the current ones. This also applies to
     the values displayed on the "LINK:" line at the  end  of  the
     display.  refer  to  the  BMUX  console  command  summary for
     display element descriptions.

5.   SUSPENSION OF OPERATIONS

          If it is  desired  to  temporarily  block  all  terminal
     access  to the Burroughs cpu, the "HALT" console command will
     return the software to a pseudo-halt-mode  state  similar  to
     that  immediately  after  startup.  In  this  state, the read
     buffers are still active, but port  inputs  (except  for  the
     console)  are  blocked. If a port terminal user attempts data
     entry, the terminal will sound  a  bell  or  similar  audible
     alarm.

6.   EXIT PROCEDURE

          If  it  is  desired  that  the  software  be  completely
     initialized to the startup state, use the "HALT"  and  "EXIT"
     console  commands, in that order. the software will then exit
     to  RT-11  control.  Refer  to  the  startup  procedures  for
     restarting the BMUX software.

7.   CONFIGURATION OF MULTIPLEXOR

          To  change the configuration of the multiplexor, use the
     EXIT sequence  detailed  above.  when  under  RT-11  control,
     enter:

                            RUN BCONF

     and depress the RETURN key.

          The configuration program will now run. The use of  this
     portion of the software will result in the destruction of the
     prior configuration. All ports must be defined, including the

     trunk(s).  The  procedure  of  multiplexor configuration will
     require verification that the prior configuration  is  to  be
     destroyed.  The  user  responds  yes  (Y)  or  no  (N) to the
     destruction message. A response of no (N) will cause an  exit
     without distrubing the prior configuration.

          If a yes (Y)  response  is  entered,  the  program  will
     commence  prompting  for  the  trunk  and port parameters. At
     least one trunk must be defined, or the software will  reject
     definition  of  any  ports.  Port  2,  the  console,  must be
     defined;  or  the  BMUX  software  cannot  be   started   and
     operations cannot commence.

          A trunk definition requires definition of the following:

               A.   Two-character poll address

               B.   6-character owner name

               C.   5-character site name

               D.   3-digit  decimal  line  buffer  size   (1-160.
                    characters)

          A port definition requires definition of the  following:

               A.   Two-character poll address

               B.   6-character owner name

               C.   5-character site name

               D.   3-digit  decimal  line  buffer  size   (1-160.
                    characters)

               E.   2-digit decimal carriage return  delay  (00-20
                    null characters)

               F.   2-digit decimal form feed  delay  (00-20  null
                    characters)

               G.   A yes (Y) or no (N) response  to  cause  input
                    characters  to  be  echoed  by the multiplexor

          There are two  special  input  conditions  that  can  be
     entered for the poll address prompt:

               A.   Two   control-V   characters    (created    by
                    simultaneously  depressing  the  control and V
                    keys)  cause  the  current  port/trunk  to  be
                    "skipped",  with  definition proceeding to the
                    next port/trunk (if any).

               B.   A  control-V  and  an "E" character terminates
                    the  configuration  process  by  setting   the
                    remaining ports to an undefined state.

          After the configuration has been prepared, re-enter  the
     BMUX  software  as  shown  in  the  startup information. This
     process may be done as often as desired, but it disables  the
     operational   capability   of   the  multiplexor  during  the
     configuration procedure.

8.   CONSOLE MESSAGES TO A DEFINED PORT

          If the user of the console terminal  wishes  to  send  a
     message to the user of a defined port, the "MESS" command can
     be utilized  (as  opposed  to  using  the  Burroughs  message
     capability)  by  entering  the  message line in the following
     format:

        (control-V)(control-V)MESS ## (message as desired)

          Where the ## is the port number assigned to the port  as
     shown in the "STAT" display. this capability is convenient in
     that it removes  the  processing  of  the  message  from  the
     Burroughs  mainframe.  It  is  usable  only within the set of
     ports defined by the "STAT" display.

9.   SOFTWARE PROBLEMS

          If a software problem should occur,  the  logic  in  the
     multiplexor  should  indicate  the  situation by displaying a

                      "**** BMUX ABORT ****"

     message  upon  the console terminal. If this happens, certain
     information should be acquired from the system and  the  BMUX
     system  problem report (SPR) should be prepared as completely
     as possible. When this type of situation occurs, the  console
     terminal will then be under DEC "ODT" control. In this state,
     the registers ($0, $1,  $2,  $3,  $4,  $5,  and  $6)  can  be
     examined  by  entering  the  register  name followed by a "/"
     character (ex: $0/ ). When the value has been copied, depress
     the  return  key and go on to the next register. When all the
     registers have been examined and their values entered on  the
     spr  form,  enter  the $6 value, followed by a "/" character.
     This will be some number between  0  and  1000  under  normal
     abort conditions. when the value displayed by the initial "/"
     character has been copied onto  the  SPR  form,  depress  the
     line-feed  (LF)  key  to get the next value (displayed in the
     form: address/value). repeat this process until  the  address
     value  is  1000.  Refer  the form to the appropriate point of
     contact for resolution of the cause of the  abort  condition.






                  BMUX CONSOLE COMMANDS SUMMARY
                  =============================

     Console  commands  for  the BMUX software can be requested at
the console port (PORT NUMBER 02) only!! The format of all console
commands  is  as  follows:  (control-V) (control-V)command(RETURN)

where:

     (Control-V)    is  the simultaneous depression of the control
                    and V keys

     (RETURN)       is  the  depression of the return (or carriage
                    return) key

     COMMAND        is  a  four-character  BMUX  command  from the
                    following table:



               PROC           The processing of I/O will now begin
                                   or resume

               HALT           All inputs (except console commands)
                                   will suspend

               MESS ## (msg)  The   message  (msg)  (whatever  was
                              typed)  will  be  sent  to  port  ##

               STAT           A table of information regarding all
                              ports and  trunks  defined  will  be
                              displayed on the console. The format
                              of the individual table line  is  as
                              follows:



            ##  PP  TT  OWNER  LOC  TFC  ERR  STS  RWQ



          where:    ##        is the BMUX port number

                    PP        is the  port's  two-character  ASCII
                              poll address

                    TT        is the trunk  BMUX  port  number  to
                              which  the  port's  input and output
                              will 'flow' to  and  from  the  host

                    OWNER     is  the  six-character owner or user
                              name


                    LOC       is  the  five-character location for
                              the port

                    TFC       is  the count of lines sent/received
                              on the port

                    ERR       is the count of input errors for the
                              port or any errors in trunk  I/O  or
                              protocol handling

                    STS       is the port's status indication with
                              bit values:

                              1    Input complete

                              2    Output complete

                              4    Need an input buffer

                              8    Statistics count ready

                              16   Console command input

                              R    Appears  if  an input buffer is
                                   active for the port

                              W    Appears  if an output buffer is
                                   active for the port

                              Q    Appears  if there is port input
                                   queued for the host

               The  last  line of the display contains information
          specific to the trunk line(s).  This  line  is  labeled:
          LINK:

               The values contained in the line are:

                    PRO ERR        Count    of   protocol   errors
                                   detected

                    POL ADR        Count of invalid poll addresses
                                   received

                    CONTENTION

                              1    Trunk  1  (port   #0)   is   in
                                   contention

                              2    Trunk  2  (port   #2)   is   in
                                   contention


          EXIT      If preceeded by a 'HALT' command,  causes  the
                    BMUX program to exit to RT-11 control.

                               NOTE

                 If entered inadvertantly, type:

                         RUN BMUX(return)

                  to re-enter the BMUX program.



     Please report any difficulties with  this  software  via  the
BMUX System Problem Report (SPR) form.






   GENERAL SCIENTIFIC CORPORATION          BMUX PROBLEM REPORT

ODT ADDRESS:___________________       RELEASE:______    DATE:______

REPORTING: PERSON:_____________________  COMPANY:__________________

===================================================================

PROBLEM SYMPTOMS:__________________________________________________

___________________________________________________________________

___________________________________________________________________

___________________________________________________________________

___________________________________________________________________

___________________________________________________________________

===================================================================

REGISTERS:                    STACK:


R0_____________________     >>>>>>________________________
                            ^
R1_____________________     ^     ________________________
                            ^
R2_____________________     ^     ________________________
                            ^
R3_____________________     ^     ________________________
                            ^
R4_____________________     ^     ________________________
                            ^
R5_____________________     ^     ________________________
                            ^
R6_________________STACK>>> ^     ________________________

                                  ________________________

                                  ________________________

                                  ________________________

                                  ________________________

                                  ________________________

                                  ________________________



                    HARDWARE CONFIGURATION OF BMUX



          The  BMUX  Multiplexor  is  designed  about  the  LSI-11
          processor,    manufactured    by    Digital    Equipment
          Corporation. The BMUX components are arranged in a 4 x 8
          backplane arrangement as follows:




                                                PROCESSOR LSI-11
     -------------------------          -------------------------

     PORTS 0,1,2,3    DLV11J                 DISK CONTROLLER
     -------------------------          -------------------------

     PORTS 4,5,6,7    DLV11J                 PORTS 8,9,10,11
     -------------------------          -------------------------

     PORTS 16,17,18,19                       PORTS 12,13,14,15
     -------------------------          -------------------------

     PORTS 20,21,22,23                       MEMORY
     -------------------------          -------------------------

     SPARE                                   SPARE
     -------------------------          -------------------------

     SPARE                                   SPARE
     -------------------------          -------------------------

     SPARE                                   SPARE
     -------------------------          -------------------------

          The placement of the component boards  is  critical  and
          should  not be arbitrarily relocated. The jumpers on the
          processor board should be configured as follows:
                       PROCESSOR OPTION JUMPERS


     JUMPER    STATUS    FUNCTION
     ______    ______    ________________________________________________

     W1        R         Resident memory bank 1 not selected

     W2        R         Resident memory bank 2 not selected

     W3        R         Event line (LTC) interrupt enabled

     W4        I         Processor controlled memory refresh disabled

     W5        R         Power up mode 0 selected

     W6        R

     W7        -         Factory configured bias voltage (do not change)

     W8        -         Factory configured bias voltage (do not change)

     W9        I         Disable reply from resident memory

     W10       R         Disable reply from resident memory during refres

     W11       R         Disable on board memory select

         SERIAL LINE INTERFACE JUMPER OPTIONS    Lines 0 to 3




     Label       Jumper         Function Implemented
     _____       ___________    ________________________________________

     A12         X to 1         This arrangement of jumpers A5-A12
     A11         X to 1         implements the octal base device ad-
     A10         X to 1         dress 17650X, which is the assigned
     A9          X to 1         address for channel 0 RCSR. The least
     A8          X to 0         significant digit is decoded on the mod-
     A7          R              ule during operation to address one of
     A6          I              four SLU device registers as follows
     A5          X to 0             X=0,RCSR
                                    X=2,RBUF
                                    X=4,XCSR
                                    X=6,XBUF

     C1          X to 1         These jumpers are used to enable
     C2          X to 1         channel 3 for console operation. Base
                                address must be 176500 (factory con-
                                figured), 176540, or 177500 for the
                                console.

     BREAK       No Jumper      No response to break

     V7          I              This arrangement of jumpers V5-V7
     V6          I              implements the octal "base" vector of
     V5          X to 0         300 with channel 3 at 60 and 64

                 CHANNEL 0
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 0         Parity generation and detection

                 CHANNEL 1
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 0         Parity generation and detection

                 CHANNEL 2
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 3
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection


     N0-3        X to 3         EIA RS-423 AND RS-232C
     M0-3        X to 3         EIA RS-423 AND RS-232C

     R10         22 kohm        Channels 0 and 1, slew rate of 2usec
     R23         22 kohm        Channels 2 and 3, slew rate of 2usec

                               BAUD RATE



     Port        Jump           Description

     0           to N           Trunk 0 set to 9600 bps
     1           to N           Trunk 1 set to 9600 bps
     2                          selected remotely
     3                          selected remotely

         SERIAL LINE INTERFACE JUMPER OPTIONS    Lines 4 to 7

     Label       Jumper         Function Implemented
     _____       ___________    ________________________________________

     A12         X to 1         This arrangement of jumpers A5-A12
     A11         X to 1         implements the octal base device ad-
     A10         X to 0         dress 17564X, which is the assigned
     A9          X to 1         address for channel 0 RCSR. The least
     A8          X to 1         significant digit is decoded on the mod-
     A7          I              ule during operation to address one of
     A6          R              four SLU device registers as follows
     A5          X to 1             X=0,RCSR
                                    X=2,RBUF
                                    X=4,XCSR
                                    X=6,XBUF

     C1          X to 0         These jumpers are used to disable
     C2          X to 0         channel 3 for console operation.

     BREAK       No Jumper      No response to break

     V7          I              This arrangement of jumpers V5-V7
     V6          I              implements the octal "base" vector of
     V5          X to 1         340

                 CHANNEL 0
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 1
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 2
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 3
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

     N0-3        X to 3         EIA RS-423 AND RS-232C
     M0-3        X to 3         EIA RS-423 AND RS-232C

     R10         22 kohm        Channels 0 and 1, slew rate of 2usec
     R23         22 kohm        Channels 2 and 3, slew rate of 2usec

         SERIAL LINE INTERFACE JUMPER OPTIONS    Lines 8 to 11

     Label       Jumper         Function Implemented
     _____       ___________    ________________________________________

     A12         X to 1         This arrangement of jumpers A5-A12
     A11         X to 1         implements the octal base device ad-
     A10         X to 0         dress 17570X, which is the assigned
     A9          X to 1         address for channel 0 RCSR. The least
     A8          X to 1         significant digit is decoded on the mod-
     A7          I              ule durRng operation to address one of
     A6          I              four SLU device registers as follows
     A5          X to 0             X=0,RCSR
                                    X=2,RBUF
                                    X=4,XCSR
                                    X=6,XBUF

     C1          X to 0         These jumpers are used to disable
     C2          X to 0         channel 3 for console operation.

     BREAK       No Jumper      No response to break

     V7          I              This arrangement of jumpers V5-V7
     V6          I              implements the octal "base" vector of
     V5          X to 1         340

                 CHANNEL 0
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 1
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 2
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 3
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

     N0-3        X to 3         EIA RS-423 AND RS-232C
     M0-3        X to 3         EIA RS-423 AND RS-232C

     R10         22 kohm        Channels 0 and 1, slew rate of 2usec
     R23         22 kohm        Channels 2 and 3, slew rate of 2usec

        SERIAL LINE INTERFACE JUMPER OPTIONS    Lines 12 to 15

     Label       Jumper         Function Implemented
     _____       ___________    ________________________________________

     A12         X to 1         This arrangement of jumpers A5-A12
     A11         X to 1         implements the octal base device ad-
     A10         X to 0         dress 17574X, which is the assigned
     A9          X to 1         address for channel 0 RCSR. The least
     A8          X to 1         significant digit is decoded on the mod-
     A7          I              ule during operation to address one of
     A6          I              four SLU device registers as follows
     A5          X to 1             X=0,RCSR
                                    X=2,RBUF
                                    X=4,XCSR
                                    X=6,XBUF

     C1          X to 0         These jumpers are used to disable
     C2          X to 0         channel 3 for console operation.

     BREAK       No Jumper      No response to break

     V7          I              This arrangement of jumpers V5-V7
     V6          I              implements the octal "base" vector of
     V5          X to 1         340

                 CHANNEL 0
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 1
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 2
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 3
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

     N0-3        X to 3         EIA RS-423 AND RS-232C
     M0-3        X to 3         EIA RS-423 AND RS-232C

     R10         22 kohm        Channels 0 and 1, slew rate of 2usec
     R23         22 kohm        Channels 2 and 3, slew rate of 2usec

        SERIAL LINE INTERFACE JUMPER OPTIONS    Lines 16 to 19

     Label       Jumper         Function Implemented
     _____       ___________    ________________________________________

     A12         X to 1         This arrangement of jumpers A5-A12
     A11         X to 1         implements the octal base device ad-
     A10         X to 1         dress 17600X, which is the assigned
     A9          X to 0         address for channel 0 RCSR. The least
     A8          X to 0         significant digit is decoded on the mod-
     A7          R              ule during operation to address one of
     A6          R              four SLU device registers as follows
     A5          X to 0             X=0,RCSR
                                    X=2,RBUF
                                    X=4,XCSR
                                    X=6,XBUF

     C1          X to 0         These jumpers are used to enable
     C2          X to 0         channel 3 for console operation.

     BREAK       No Jumper      No response to break

     V7          I              This arrangement of jumpers V5-V7
     V6          I              implements the octal "base" vector of
     V5          X to 1         340

                 CHANNEL 0
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 1
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 2
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 3
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

     N0-3        X to 3         EIA RS-423 AND RS-232C
     M0-3        X to 3         EIA RS-423 AND RS-232C

     R10         22 kohm        Channels 0 and 1, slew rate of 2usec
     R23         22 kohm        Channels 2 and 3, slew rate of 2usec

        SERIAL LINE INTERFACE JUMPER OPTIONS    Lines 20 to 23

     Label       Jumper         Function Implemented
     _____       ___________    ________________________________________

     A12         X to 1         This arrangement of jumpers A5-A12
     A11         X to 1         implements the octal base device ad-
     A10         X to 1         dress 17604X, which is the assigned
     A9          X to 0         address for channel 0 RCSR. The least
     A8          X to 0         significant digit is decoded on the mod-
     A7          R              ule during operation to address one of
     A6          R              four SLU device registers as follows
     A5          X to 1             X=0,RCSR
                                    X=2,RBUF
                                    X=4,XCSR
                                    X=6,XBUF

     C1          X to 0         These jumpers are used to disable
     C2          X to 0         channel 3 for console operation.

     BREAK       No Jumper      No response to break

     V7          I              This arrangement of jumpers V5-V7
     V6          I              implements the octal "base" vector of
     V5          X to 1         340

                 CHANNEL 0
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 1
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 2
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

                 CHANNEL 3
     E           X to 1          Even parity
     D           X to 1         8 data bits
     S           X to 0         1 stop bit
     P           X to 1         No Parity generation and detection

     N0-3        X to 3         EIA RS-423 AND RS-232C
     M0-3        X to 3         EIA RS-423 AND RS-232C

     R10         22 kohm        Channels 0 and 1, slew rate of 2usec
     R23         22 kohm        Channels 2 and 3, slew rate of 2usec

                            DISK CONTROLLER

          The  MDC11  Disk  Controller  is a peripheral controller
     intended for use in LSI-11 based computer systems. The option
     straps are set as follows:

     Label     Jumper           Function Implemented
     -----     ------           ---------------------------------------

     R0        I                Positioning step time period
     R1        I                set at 40 milliseconds
     Mx        None             1.6 second time out delay
     RD        I                Refresh Disable
     R13       I                Address 13
     173       I                Enable address 173000

     A15       R                Prom address bit 15
     A14       R                Prom address bit 14
     A13       I                Prom address bit 13
     PD        I                Prom Disable
     ER0       I                Enable Prom block 0

     ER1       I                Enable Prom block 1
     ER2       I                Enable Prom block 2
     ER3       I                Enable prom block 3
     A-B       I                A-B
     C-D       I                C-D

     E         R                E
     12M       I                12 Volt supply
     A11       R                Address 11 latched
     5M        I                -5 Volt supply to ROMS
     R-Q       R                R-Q

     B12       R                Base address of minidisk
     B11       R                controller located at 177200.
     B10       R                  Register
     B9        R                    Command-Status (CSR) 177200
     B8        I                    Track (TR)           177202

     B7        R                    Sector               177204
     B6        I                    Data                 177206
     B5        I
     B4        I
     B3        I

     M1        R                Time out delay
     M2        R                set at
     M4        R                1.6 seconds after no user access
     MD        R                Motor disable


                              DISK DRIVE


          The disk utilized is the MPI 51/52 or the Shugart SA400.
     They  are  physically  and  electrically interchangeable. The
     option straps are as follows:

     Label     Jumper           Function Implemented
     -----     ------           ---------------------------------------

     T1        I                Head solinoid with select
     T2        I                Drive select 1 selected
     T3        R                Drive select 2 not selected
     T4        R                Drive select 3 not selected
     T5        I                Drive always selected
     T6        R                Drive 4 not selected
     T7        I                Head solinoid with motor on


                BMUX MAINLINE LOGIC DOCUMENTATION

     The software is divided into three major portions:

     A.   Mainline Logic

     B.   Interrupt Service Logic

     C.   Configuration Logic.

     The  mainline   logic   is   divided   into   two   portions:
Initialization  and  Controller  Logic.  The  initialization logic
presets the operational conditions for the proper  functioning  of
the   controller  portion.  The  controller  handles  all  garbage
collection, I/O start/stop and control interface functions.

     The initialization section does the following:

     A.   Saves the current contents  and  presets  the  interrupt
          vector address contents for the proper interrupt service
          routine entry,

     B.   Reads  the configuration information from disk to preset
          the port- dependent operations  of  the  controller  and
          interrupt service portions of the software,

     C.   Prints an initialization  message  on  the  console  and
          initiates the input process for the console, and

     D.   Presets  flags  to  show  that  the   logic   has   been
          initialized.

     The controller section does the following:

     A.   Starts all read/write I/O sequences for the trunk(s) and
          ports,

     B.   Processes   all   read/write  I/O  completions  for  the
          trunk(s) and ports,

     C.   De-queues  all traffic and messages for the trunk(s) and
          ports,

     D.   Acquires  and releases all buffers from/to the trunk and
          port pools,

     E.   Processes all console control interface commands,

     F.   Maintains (when possible) a  double-read  condition  for
          the trunk(s),

     G.   Journals traffic and error statistics (by trunk/port) to
          a cumulative table, and


     H.   Handles the timer expiration situation for the trunk(s),
          and   the  interrupt  service  logic  resides  with  the
          mainline   logic   and   asychronously   services    the
          transmission/receipt  of  characters by the trunk(s) and
          ports. the trunk read ISR  (interrupt  service  routine)
          works hand-in-hand with the controller section and trunk
          write ISR to provide response to the Burroughs protocol.
          The  port  read/write  ISR's process buffers to/from the
          trunk(s) and ports. Messages from the  console  port  to
          the  other  ports  is picked up by the command processor
          segment of the controller section  and  is  massaged  to
          look like a trunk read completion.

     The buffers pools are separate and homogeneous  in  size  and
structure. Hence the same acquisition/release routines can be used
for both. The trunk read pool is used to supply read  buffers  for
the  trunk  read  ISR,  which  become  port write buffers when the
burroughs has sent a buffer to  a  port  in  a  'select'  protocol
sequence.  The  port  read pool is used to supply read buffers for
the port read ISR, which become trunk-bound write buffers. Console
messages  reside in the port read buffer, but are massaged to look
like a trunk read destined  for  the  specified  port.  These  are
dequeued  by  a  special segment of the mainline's traffic-routing
routines.

     A  third  segment of the software is the configuration logic,
which shares and sets up defined port values in the data structure
segment (SF2) to enable the controller and interrupt service logic
to function as the user desires.

     The  in-core  structure  of the multiplexor and configuration
portions of the software  (low-to-high  memory  adressing)  is  as
follows:

     program stack            program stack
          |                        |
     data structure (SF2)          data structure (SF2)
          |                        |
     buffer pools (SF98, SF99)     configuration logic (SF60)
          |
     initialization and controller (SF10)
          |
     command processing routines (SF12)
          |
     trunk read ISR (SF20)
          |
     port write ISR (SF30)
          |
     trunk read ISR (SF40)
          |
     trunk write ISR (SF50)
          |
     canned messages (SF90)


     These  two software entities cannot co-exist in memory at the
same time.

     Buffer  request  and  release  are  controlled  by two common
routines having separate entry points for Trunk  and  Port  buffer
processing.  These routines maintain pointers for each buffer pool
which denote the start and end of the group of  buffers  currently
active  for  that  pool.  Traffic  scans  will  begin at the start
pointer value and stop when the end pointer value is reached. When
a  buffer  is  requested from the buffer pool, the search is first
made from the buffer immediately following the end  pointer  until
the  start  pointer  value  is reached. If none exist, a search is
made from the  start  pointer  to  the  end  pointer  looking  for
"embedded"  buffers  that  are available for use. When a buffer is
released to either buffer pool, the start and/or end pointers  are
updated  IF  the  buffer was being pointed to by either pointer. A
buffer is active if its Read Queue (RQ) byte is NOT a -1 value. If
the  Write Queue (WQ) byte is NOT a -1 value, the buffer is queued
for transfer to a Trunk or Port. Refer to  the  following  diagram
for  a  sample  condition of the two buffer pools, Trunk and Port.


     In the example, Trunk buffers 4 and 5 are  active  for  Trunk
Read purposes. Due to the positional order of the two, buffer 4 is
probably active  and  buffer  5  is  waiting  for  use  (refer  to
references  to  the  "double-queued" buffers for Trunk reads). The
other Trunk buffers have completed the Trunk Read process and  are
awaiting  (or in the process of) transmission to the specified PCB
terminals: buffer 1 is queued for PCB 2, followed by buffer 3, and
buffer 2 is queued for PCB 3. In the Port buffer pool, buffers are
actively being used for Port Reads: buffer 6 is active for PCB  5,
buffer  11  for  PCB 3, and buffer 12 for PCB 4. Buffers 7-10 have
completed the Port Read process and are awaiting  transmission  to
the  Trunk.  Note that PCB 2 has NO buffer queued in the Port Read
buffer pool. It has probably JUST completed a Read process and the
mainline  has  NOT YET requested a new buffer for the Read process
for PCB 2.

     In  the general flow of buffers, Port Read buffers "feed" the
Trunk Write process, just as Trunk Read buffers  "feed"  the  Port
Write  process.  The  "Traffic  Queues" for each Write process are
loosely held between the start and end pointers of the two  buffer
pools. Traffic dequeuing occurs when a Trunk or Port has completed
its last Write process and is ready to commence another. The Trunk
Write  dequeuing is controlled by the Burroughs requests, however.
It is probably obvious that the Trunk buffer pool stands the  best
chance  of  becoming  "staurated"  due to large "bursts" of output
from the Burroughs processor. This is purely  dependent  upon  the
ability  of  the defined Port PCB's to output the buffers received
from the  Trunk  fast  enough  to  keep  ahead  of  the  Burroughs
transmissions.   The   software   DOES   prohibit  further  buffer
transmittal from the Burroughs when the Trunk buffer pool  becomes
saturated  by  "throttling"  the  transmission  until at least one
Trunk buffer is available for the Read process.


     .TITLE    BMUX -GENERAL SCIENTIFIC CORP.
     .IDENT    /000001/  ;  GAITHERSBURG, MARYLAND
;
;    COPYRIGHT (C) 1979
;
; THIS SOFTWARE IS FURNISHED UNDER A LICENSE FOR USE ONLY ON A SINGLE
; COMPUTER SYSTEM AND MAY BE COPIED ONLY WITH THE INCLUSION OF THE ABOVE
; COPYRIGHT NOTICE AND THE EXPRESSED, WRITTEN PERMISSION OF GENERAL
; SCIENTIFIC CORPORATION.  TITLE TO AND OWNERSHIP OF THIS SOFTWARE SHALL
; REMAIN WITH GENERAL SCIENTIFIC CORPORATION.  COPIES OF THIS SOFTWARE
; MAY NOT BE PROVIDED TO OR OTHERWISE MADE AVAILABLE TO ANY OTHER PERSON
; EXCEPT FOR USE ON A GENERAL SCIENTIFIC CORPORATION SUPPLIED SYSTEM.
;
; THE INFORMATION IN THIS SOFTWARE IS SUBJECT TO CHANGE WITHOUT NOTICE AND
; SHOULD NOT BE CONSTRUED AS A COMMITMENT BY GENERAL SCIENTIFIC CORPORATION.
;
     .LIST
;
;
;
     .PAGE
     .SBTTL    NOTES
;
;    THE FOLLOWING SET OF EQUATES EXPRESSES THE DESIGN PARAMETERS

;    FOR THE BMUX SOFTWARE.  NOT ALL OF THE EQUATES ARE USED IN THE
;    INITIAL VERSION OF THE SYSTEM.  SOME LOCAL EQUATES OCCUR IN SOME
;    OF THE MODULES.  AT A LATER TIME, THESE WILL BE MOVED TO THIS
;    SOURCE FILE.
;
;    ***** IMPORTANT NOTE: *****
;
;    THIS SOURCE FILE ** MUST ** BE ASSEMBLED WITH EVERY OTHER SOURCE
;    FILE, SF2-SF99.
;
;
     .PAGE
     .SBTTL    MACRO CALLS AND DEF'S
;
     .MCALL    .SPND,.TWAIT,.REGDEF,..V2..
;
     ..V2..    ; VERSION 2 MACRO CALLS
     .REGDEF   ;MAKE LIFE EASIER
;
     .PAGE
     .SBTTL    DLV11-J EQUATES
;    THIS SECTION DEFINES THE DLV-11J DEVICE BIT SETTINGS AND REGI
;    DEVICE HARDWARE REGISTER OFFSETS RELATIVE TO THE GIVEN
;    DEVICE'S RCSR ADDRESS.   REFER TO THE DEC LSI-11 PERIPHERALS
;    MANUAL FOR INFORMATION REGARDING THE OPERATIONS OF THE DLV-11J
;    VIA ITS HARDWARE REGISTERS.
;
;
;    RCSR:     READ CHANNEL CONTROL & STATUS REGISTER
;

RCSR=0         ;DEVICE ADR REG OFFSET
R.DONE=200     ;RCVR DONE BIT
R.IE=100  ;INTERRUPT ENABLE BIT
R.RE=1         ;RCVR ENABLE (CLEARS R.DONE)
R.KILL=101     ;RCVR STOP BITS
;
;    RBUF:     READ CHANNEL BUFFER REGISTER
;
RBUF=2         ;DEV ADR OFFSET
;
;    STATUS BIT VALUES FOR RBUF
;
R.ER=100000    ;ERROR BIT
R.OV=40000     ;OVER-RUN ERROR
R.FR=20000     ;FRAMING ERROR
R.PA=10000     ;PARITY ERROR
;
;    XCSR:     TRANSMIT CHANNEL CONTROL & STATUS REGISTER
;
XCSR=4    ;DEV ADR OFFSET
X.RDY=200 ;XMTR READY BIT
X.IE=100  ;INTERRUPT ENABLE BIT
X.BR=1         ;XMTR BREAK (SET TO BREAK XMIT)
;
;    XBUF:     TRANSMIT CHANNEL BUFFER REGISTER
;
XBUF=6         ;DEV ADR OFFSET
;    DATA IS TRANSMITTED BY MOVING A CHARACTER INTO THE LOWER BYTE
;
     .PAGE
     .SBTTL    SYSTEM EQUATES
;
;    THE FOLLOWING VALUES SET THE LIMITS OF THE MULTIPLEXOR'S
;    DESIGN AND DEFINE CERTAIN CRITICAL VALUES, SUCH AS THE PORT
;    CONTROL BLOCK (PCB) NUMBER FOR THE CONSOLE.
;
;
MAXPRT=24.     ;MAX # OF PORTS DEF'D
CONSOL=2  ;PORT # OF CONSOLE DEVICE
CONVEC=60 ;CONSOLE VECTOR
TRKA=0         ;PCB FOR TRUNK A
TRKB=1         ;PCB FOR TRUNK B
STA=MAXPRT     ;STATUS POLL FOR TRUNK A
STB=MAXPRT+1   ; SAME FOR B
STALL=MAXPRT+2 ;BOX STATISTICS POLL PCB #
TRAVEC=300     ;TRUNK A VECTOR
TRBVEC=310     ;TRUNK B VECTOR
CMDL=4         ;LEN OF ASCII CMD IN BYTES
NCMD=6         ;NUMBER OF CONSOLE COMMANDS
CTABL=6        ; LEN OF CMD TABLE ENTRY
TIMOUT=100.    ;10. SECOND MAX TIME-OUT
NUMBUF=54.     ;# BUFFERS IN EACH (OF TWO) POOLS
BUFSIZ=170.    ;SIZE OF DATA PORTION OF BUFFER
BUFLEN=BUFSIZ+6     ;LEN OF EACH BUFFER
     .PAGE

     .SBTTL    CHAR RECOGNITION EQUATES
;
;    THE FOLLOWING EQUATES DEFINE ASCII CHARACTER VALUES OF IMPORTANCE
;
;    TO THE PROCESSING OF THE TERMINAL PORTS, SUCH AS THE RETURN KEY.
;
;    TERMINAL ASCII:
;
ESC=33         ;ESCAPE
CR=15          ;CARRIAGE RETURN
LF=12          ;LINE-FEED
FF=14          ;FORM-FEED
NULL=0         ;NULL
BS=10          ;BACK-SPACE
DEL=177        ;LINE DELETE
SYNC=26        ;SYNC (CMD FLAG CHAR)
;
;
;    THE FOLLOWING VALUES ARE OF SPECIAL IMPORTANCE TO THE PROCESSING
;
;    OF THE BURROUGHS PROTOCOL BY THE MAINLINE AND TRUNK ISR'S, SUCH
;
;    AS THE POL OR SEL CHARACTERS (WHICH INDICATE 'POLL' AND 'SELECT'
;
;    REQUESTS ISSUED BY THE BURROUGHS' LINE CONTROL PROGRAM).
;
;    BURROUGHS ASCII:
;
ENQ=5          ;ENQUIRE
POL=160        ;PORT-TO-B SELECT
SEL=161        ;B-TO-PORT SELECT
CON=7          ;CONTENTION MODE (BELL)
BELL=7
EOT=4          ;END-OF-XMIT
ETX=3          ;END-OF-TEXT
ACK=6          ;ACKNOWLEDGE
NAK=25         ;NEGATIVE ACKNOWLEDGE
SOH=1          ;START OF HEADER
STX=2          ;START OF TEXT
;
RVI=40       ;REVERSE INTERRUPT USED TO STOP OUTPUT FROM HOST (NOT USED)
;
;
     .PAGE
     .SBTTL    PCB DEFINITION
;
;    THE FOLLOWING EQUATES DEFINE THE STRUCTURE AND SOME OF THE DATA
;    CONTENTS OF THE PORT CONTROL BLOCK (PCB).  CURRENTLY, THE P.BAUD
;    AND P.TYPE BYTES ARE NOT USED; DUE TO THE IMPLEMENTATION OF THE
;    DLV-11J DEVICES.
;
;
P.SOU=0        ;PCB INDEX TO POLTAB FOR THIS PORT (-1 IF NOT DEF'D)
P.DST=1   ;PCB INDEX TO POLTAB FOR DESTINATION FROM HERE (OR -1)
P.PST=2        ;PORT STATUS BYTE

;
;    P.PST BIT MEANINGS:
;
PS.RF=1        ;READ FINISHED BIT
PS.WF=2        ;WRITE FINISHED BIT
PS.RB=4        ;READ BUFFER NEEDED BIT
PS.JS=10  ;JOURNAL STATS HOLD WD TO BUFFER BIT
PS.CMD=20 ;PROCESS COMMAND FROM CONSOLE BIT
PS.TQ=40  ;TRAFFIC QUEUED FOR TRUNK BIT
;
P.DELF=3  ;DELAY FLAG (0=>INACTIVE)
;
;    P.DELF BIT MEANINGS:
;
PD.CR=1        ;CR DELAY FLAG
PD.FF=2        ;FF DELAY FLAG
;
P.BAUD=4  ;PORT BAUD RATE (INFO ONLY)
P.TYPE=5  ;PORT TERM TYPE (INFO ONLY)
P.LSIZ=6  ;LINE LENGTH (BYTES)
P.ECHO=7  ;ECHO FLAG  (0=>NO)
P.CRD=10  ;CR DELAY VALUE (0=NONE)
P.FFD=11  ;FF DELAY VALUE (0=NONE)
P.STAT=12 ;STATS FLAG (0=NONE)
;
;    P.STAT BIT MEANINGS:
;
PST.E=1        ;ERROR STATISTICS COLLECTION BIT
PST.T=2        ;TRAFFIC STATISTICS COLLECTION BIT
;
;
P.WIND=13 ;STATS WINDOW (.1 SEC 'TICKS')
P.ERR=14  ;ERROR STATS COUNTER
P.TFC=15  ;TFC STATS COUNTER
P.RST=16  ;READ STATUS BYTE
P.WST=17  ;WRITE STATUS BYTE
;
;    READ/WRITE STATUS BIT SETTINGS
;
PS.DOR=300     ;RD: DATA OVER-RUN ERROR
PS.FRA=240     ;RD: FRAMING ERROR
PS.PAR=220     ;RD: PARITY ERROR
PS.TMO=210     ;WR: TIME-OUT ERROR
PS.OK=1        ;R/W: SUCCESSFUL COMPLETION
;
;
P.RC=20        ;READ CHAR CNT
P.WC=21        ;WRITE CHAR CNT
P.RBFA=22 ;READ BUFFER ADR
P.RBP=24  ;READ BUFFER PTR (CURRENT)
P.WBFA=26 ;WRITE BUFFER ADR
P.WBP=30  ;WRITE BUFFER PTR (CURRENT)
P.SHLD=32 ;STATS HOLD WD (FOR JOURNALING TO CUMULATIVE TABLE)
P.STIM=34 ;STATS WINDOW TIMER
P.WTIM=35 ;WRITE I/O TIMER

P.DC=36        ;DELAY CNTR (0= NO DELAY, ELSE # OF NULL'S)
P.ECH=37  ;ECHO CHAR AWAITING OUTPUT
;
PCBLEN=40 ;LEN OF PCB IN BYTES
;
     .PAGE
     .SBTTL    BUFFER DEF'S
;
;    THE BUFFERS OF BOTH POOLS ARE HOMOGENEOUS IN SIZE AND FLAGS USAGE
;    IN THE F(IN THE FIRST 3 WDS OF EACH BUFFER).  THE FIRST BYTE IS A -1 IF IT
;    IS NOT QUEUED FOR USE AS A READ BUFFER.  THE SECOND BYTE IS A -1 IF
;    IT IS NOT QUEUED TO BE WRITTEN TO A SPECIFIED PORT (PCB NUMBER).
;    THE THIRD BYTE CONTAINS THE READ/WRITE CHARACTER SIZE (MAX 255.).
;    THE FOURTH BYTE CONTAINS A ZERO IF THE BUFFER IS NOT ACTIVELY BEING
;    USED, ELSE IT CONTAINS A 1.  THE FIFTH AND SIXTH BYTES ARE USED TO
;    COMPUTE THE BCC CHARACTER VALUE FOR BUFFERS DESTINED FOR TRANSMISSION
;    TO THE BURROUGHS VIA EITHER TRUNK.
;
;    PORT AND TRUNK READS BEGIN AT THE APPROPRIATE POINTS WITHIN THE BUFFER,
;    SINCE THE BURROUGHS HEADER VALUES ARE PLACED AT THE BEGINNING OF THE
;    PORT READ BUFFER PRIOR TO ITS TRANSMISSION.  BOTH THE ETX AND BCC
;    (COMPUTED) CHARACTERS ARE AFFIXED TO THE END OF THE PORT READ BUFFERS.
;
;    THE BUFFERS ARE MANAGED BY THE DATA LISTHEAD PTRS:
;
;    PST: START OF PORT ACTIVE BUFFERS
;    PEP: END OF PORT ACTIVE BUFFERS
;    TSP: START OF TRUNK ACTIVE BUFFERS
;    TEP: END OF TRUNK ACTIVE BUFFERS
;
;    THE BUFFER POOL(S) ARE COMPLETELY USED WHEN THE START PTR
;    VALUE IS THE SAME AS THE END PTR.
;
;
;
RQ=0 ;READ Q BYTE: -1=AVAIL,ELSE PORT #
WQ=1 ;WRITE Q BYTE: SAME AS RQ
SZ=2 ;R/W CHAR SIZE (MAX 146.)
AFL=3     ;ACTIVE FLAG (0=INACT, 1=ACT)
TDATA=6   ;START OF TRUNK READ
PDATA=10. ;START OF PORT READ DATA
;           IF XM# USED, PDATA SHOULD BE 11.
BCC=4          ;BCC COMPUTATION WD
BAD0=7    ;START OF TWO-BYTE POLL ADR IN HEADER
;         NOTE: AREA FROM TDATA TO PDATA CONTAINS BURROUGHS HDR
;
;
     .LIST


              BMUX Support Subroutine Documentation


1.   BTIME: Trunk Timeout Handler

               This  subroutine  verifys  that  the  Trunk timeout
          message byte is not as yet set. If so, the message  byte
          is  set  to  trigger the Console message indicating that
          this Trunk is not responding to communication  attempts.

2.   GBUFC: Buffer Request Handler

          This subroutine has two entry points:

               GTBUF:    To  request  a  Trunk  read  buffer,  and

               GPBUF:    To request a Port read buffer.

               The   common  routine  processes  the  buffer  pool
          pointers as set by the entry point logic to  locate  and
          allocate a buffer for the Trunk/Port which has requested
          the action. If a  buffer  is  located,  its  address  is
          placed  on  the  top  of  the stack upon return from the
          subroutine. If no available buffers were found,  a  zero
          will  be  returned.  This  routine  processes  the  pool
          starting at the  first  buffer  after  the  current  end
          pointer. If needed, the "search" pointer is reset to the
          top of the buffer  pool  being  examined  (this  is  the
          "wrap-around" case). If scanning from the end pointer to
          the start pointer fails to provide an available  buffer,
          the  scan  will  then  switch to the "embedded" case and
          search from the start pointer to the end  pointer.  Once
          the entire buffer pool is checked, a zero is returned to
          the calling routine to indicate the pool  is  completely
          used.  If a buffer islocated, the end pointer is the set
          to the buffer's address, unless this was  the  "embedded
          case",  to  set  the  limits  for the mainline's traffic
          scan.

               This is an important point, since the start and end
          pointers are the limits for the mainline's dequeuing  of
          traffic for the Trunk and Port write processes.

3.   SAVE:     Register Save Routine

               When  the  routine  to  be  executed  will  destroy
          register contents that are  needed  after  the  routines
          execution,  this  routine is called to save the contents
          of the registers, R0 through R5, on the stack (SP).  The
          RSTOR  subroutine must be called at the logical point to
          restore the registers to their saved values  just  prior
          to exit from the calling routine.

4.   STOR:     Register Restoration Routine

               This routine restores the registers, R0 through R5,
          to the values saved  on  the  stack  (SP)  by  the  SAVE
          routine.  See  usage  note for the SAVE routine for more
          information regarding the application of  this  pair  of
          subroutines.

5.   READ:     Trunk/Port Read Process Initiation Routine

               When   the   mainline   processing   requires   the
          initiation of a new read condition for a Trunk or  Port,
          this   routine  is  called  to  preset  the  appropriate
          pointers and counters  so  the  read  interrupt  service
          routines  can  process the characters received and place
          them in the Trunk/Port's read buffer. Just prior to exit
          from  this  routine,  the  Interrupt  Enable bit for the
          Trunk/Port is set in the appropriate Read Command/Status
          Register (RCSR) to enable interrupt processing.

6.   WRITE:    Trunk/Port Write Process Initiation Routine

               This routine has a special entry point, FORCE, used
          to transmit the Trunk's  Contention  Break  message  (in
          accordance  with  the  Burroughs  protocol).  The entire
          routine functions similarly to the READ routine in  that
          it  sets  up  the appropriate pointers to support output
          character  interrupt  processing   by   the   Trunk/Port
          interrupt  service  routines. In addition to setting the
          Interrupt  Enable  bit  in  the  Trunk/Port's   Transmit
          Command/Status  Register  (XCSR), the FIRST character to
          be transmitted MUST be loaded into the  Transmit  Buffer
          Register  (XBUF) to initiate the transmission process to
          accomplish the Write function.

7.   FORCE:    Burroughs   Protocol   Contention  Break  to  Trunk
          Routine

               Refer   to   the   WRITE   routine  for  processing
          information.  This  routine   is   entered   after   the
          Contention  Break  message  has  been set up to initiate
          communications  on  the  Trunk  line  NOW,  rather  than
          waiting  for  the  next  cyclic  polling  process  to be
          initiated by the Burroughs end of  the  link.  For  more
          information  on  the conditions for initiation, refer to
          the FNDCOM routine description.

8.   FNDCOM:   Traffic Dequeuing (Trunk/Port) Routine

          This routine has two entry points:

               FNDMSG:   Sets  up  Trunk  Write traffic scans, and

               FNDPWB:   Sets up Port Write traffic scans.


               The common logic scans the buffer pool specified by
          the entry point, looking for buffers in the  pool  whose
          Write  Queue  (WQ)  byte  contains the Trunk/Port's Port
          Control Block (PCB) number as found in the PCB's  Source
          (P.SOU) byte.

               If a match  occurs,  the  buffer  address  will  be
          loaded  into the Port's Write Buffer address word in the
          PCB so the Write process can be initiated.

               The  Trunk  is  processed  slightly differently. In
          order for the buffer to be dequeued, the Read Queue (RQ)
          byte  in the buffer MUST match the Dequeue byte (TRKRSP)
          for this Trunk. Otherwise, scanning continues. If a Port
          buffer  is  dequeued  for the Trunk, it is placed into a
          holding array (TWBPCB)  ordered  in  PCB  sequence.  The
          logic  then  determines  if a Break Contention is needed
          for this the Trunk line to transmit the  buffer  to  the
          Burroughs  processor.  If  not,  control  returns to the
          calling routine, and the buffer will be  transmitted  in
          its  proper  sequence.  If a Contention Break is needed,
          the source PCB number from the buffer will be encoded in
          ASCII  and  placed  in  the  Contention Break buffer and
          control given to the FORCE  routine  to  "wake  up"  the
          Burroughs.

9.   JORSTA:   Statistics Journaling Routine

               This  routine  transfers  the  traffic  (P.TFC) and
          error (P.ERR) byte values from the holding word (P.SHLD)
          in  the  PCB into the "wrap-around" word accumulators in
          the Statistics Cumulative array (CUMTAB), ordered in PCB
          sequence.  This  array can be displayed using the 'STAT'
          Console command.

10.  REBUF:    Buffer Release Routine

               This routine returns buffers to  either  pool  upon
          completion   of  the  Trunk/Port  Write  process.  After
          return, it frees enables the dequeuing  of  traffic  for
          the  Trunk  or Port by clearing the Write Buffer Address
          (P.WBFA) word, which allows  the  traffic  dequeuing  to
          resume. The header words of the buffer are reset and the
          the buffer pool pointers (start/end)  are  appropriately
          updated.


11.  GPCBDA:   Device Address Pointers Preset Routine

               When  the mainline logic requires that the Read and
          Transmit Device  Address  Registers  be  accessed,  this
          routine  will  preset the pointer words according to the
          PCB number contained in the PCB's source  byte  (P.SOU).

12.  CONWRI:   Console Message Output Routine

               This routine copies a "canned" message into a Trunk
          read  buffer  and queues it for the Console port's write
          process. If the Trunk read  buffer  pool  is  full,  the
          C-bit  will  be  set  upon  return,  indicating that the
          routine failed to complete the requested action.

13.  PCBSET:   Configuration Preset Routine

               During  initialization  of  the  multiplexor,  this
          routine    is    called    to    find   and   copy   the
          Configuration-dependent data structure from floppy  disk
          to  core.  It  uses  standard RT-11 directives (.LOOKUP,
          .READW  and  .CLOSE)  to  perform   this   action.   The
          Configuration-dependent  area  consists  of  543.  words
          beginning at label "PCB" in the data structure.

14.  BOMB:     Multiplexor Abort Exit Point

               If   software   conditions   develop   which    the
          multiplexor  cannot  handle,  this routine is entered to
          indicate that the condition has occurred and to  provide
          an  opportunity  to examine the software for information
          about  the  condition.   This   routine   "undo's"   the
          initialization  process, prints the abort message to the
          Console, and enters DEC's standard SOFTWARE "ODT" module
          to  provide  the  user  and  maintenance  personel  with
          software tools to aid the examination.



15.  CONFDP: Special Message Dispatcher

          This routine processes special message  conditions  such
     as  Trunk timeout for both possible Trunks. The Trunk timeout
     flag byte is examined to see if a message  is  needed.  Else,
     the routine exits. If a message is needed, the routine copies
     the appropriate Trunk's message into the LAST defined  buffer
     in  the  Port  buffer  pool.  The  timeout  flag byte is then
     incremented until it reaches a timed limit and is reset.  The
     message copied is queued for the Console to indicate that the
     named Trunk line is not supporting  communications.  At  some
     later  point,  other  special  messages  could be added here.

16.  CONCMD: Console Command Decoding Routine

          When a Console command is detected by the Port read ISR,
     the mainline will route it to this routine for  decoding  and
     dispatch.  The  input  buffer is checked against the existing
     command dispatch table (CCMD)  and  the  appropriate  command
     processing  routine is called. If the command is invalid, the
     buffer will be echoed to the console with the console command
     in  error replaced with an error indicator "!!!!" in place of
     the command. Once the  processing  call  has  completed,  the
     buffer will either be released or reused.

17.  HLTPRO: HALT Command Processing Routine

          This  command  is  called  by  the CONCMD routine when a
     'HALT' command is detected. It sets the HALT condition  flag,
     HALTFL,  which  disables  input  from  the  Trunk  and  Ports
     terminals (except for the Console).

18.  START: PROC Command Processing Routine

          This routine is called by  the  CONCMD  routine  when  a
     'PROC'  command  is  detected.  It  clears the HALT mode flag
     (HALTFL), re-initializes the Read process for all Trunks  and
     Ports   defined,   clears   the  Trunk  traffic-queued  table
     (TWBPCB), and arbitrarily  sets  the  Trunk  Contention  mode
     flag(s) to indicate a Contention condition.

19.  STDISP: STAT Command Display Header Routine

          When  the  CONCMD routine detects a 'STAT' command, this
     routine is called. It copies the display header into  a  Port
     read  buffer  and  queues  it  for the Console. To preset the
     remainder of the status display, a flag is set  (STDFLG)  and
     the  PCB  counter  for the display line processor (DISTAT) is
     set for PCB  0  (the  lowest-numbered  PCB  in  the  system).
     Control is then returned to CONCMD.


20.  MSG: Console Message Dispatcher

          When  the  CONCMD routine detects a 'MESS' command, this
     routine is called. The PCB number (02-23)  is  validated  and
     the  buffer  is  queued  for  that Port. If the PCB number is
     invalid, it is replaced in the buffer by the  ASCII  constant
     '??'  to signal an error. In this case, the buffer will begin
     with 'MESS ??' and be echoed upon the Console.

21.  PROXIT: EXIT Command Processing Routine

          Detection of an 'EXIT' command  by  the  CONCMD  routine
     causes  this  routine to be called. If HALT mode is in effect
     (HALTFL set), the routine  will  "un-do"  the  initialization
     process,  print  an EXIT message upon the console, and return
     Console and program control to RT-11. If the EXIT command  is
     entered and the HALT mode flag is not set, it wil be IGNORED.

22.  DISTAT: STAT Display Line Processing Routine

          When a 'STAT' command has been requested by the Console,
     this routine is entered once for every COMPLETE scan  of  ALL
     PCB's  by  the  mainline  logic.  If  the display flag is set
     (STDFLG), the 'buffer-ready' flag (STRDY) is checked. If set,
     the  logic  is awaiting an available Port read buffer. If the
     flag is not set, the NEXT PCB to be  displayed  is  processed
     into  an  intermediate buffer according to the format defined
     by the header line and the  buffer-ready  flag  is  set.  The
     CONCPY  routine  is  then  called  to copy the staging buffer
     (CM16) into a Port read buffer. This process continues  until
     ALL  PCB's  have  been  represented  in  a line of the status
     display. Once this point has  been  reached,  the  Link  line
     (representing  both  possible  Trunks)  is  formatted to show
     protocol errors and conditions.  The  process  is  terminated
     after  this  line  is queued for the Console by resetting the
     display flag, STDFLG.

23.  CONCPY: Console Status Display Buffer Copy Routine

          When a line of status display has been prepared  by  the
     DISTAT routine, this routine is called to acquire a Port read
     buffer, copy the formatted line into it from the staging area
     (CM16),  and  queue  it for output upon the Console terminal.

24.  Canned Messages:

          The system uses various "canned" messages, literal ASCII
     strings used for  display  purposes,  etc.  The  strings  are
     contained in the SF90 and SF12 source modules.




        BMUX Port Interrupt Service Routines Documentation


25.  SF20 Module - Port Read Interrupt Service Processing  Routine

     This routine has six entry points:

          PR0: entry point for the Console;

          PR1: entry point for PCB 3;

          PR2: entry  point  for  PCB's  5,  9,  13,  17  and  21;

          PR3:  entry  point  for  PCB's  6,  10,  14,  18 and 22;

          PR4: entry point for PCB's 7, 11, 15,  19  and  23;  and

          PR5:  entry  point  for  PCB's  4,  8,  12,  16  and 20.

          The multiple entry points each establish  a  pointer  to
     variable-length  table  containing  a LIST of pointers to the
     various Ports' PCB and Device Address  entries.  Upon  entry,
     the  ISR will scan ALL Ports defined in the list to see WHICH
     Port caused the Interrupt to occur. This structured technique
     permits the ISR to be data-driven and the actual logic exists
     only ONCE but processes ALL Read  Interrupts  for  ANY  Port.

          The   Read   ISR   routine   processes  input  character
     interrupts from the terminal Ports, 2 through 23. It  handles
     the following:

          1.   Console command recognition for the Console,

          2.   Blocks  input from ALL terminals EXCEPT the Console
               during HALT mode,

          3.   Backspace and line-deletion conditions,

          4.   Blocks terminal input and sends a BELL character if
               the   terminal's   Trunk   line  is  in  a  timeout
               condition,

          5.   Auto-echo   (if  defined)  of  a  terminal's  input
characters,

          6.   End-of-line    conditions    by    formatting   the
               appropriate header information in  the  buffer  for
               transmission   of   the  buffer  to  the  Burroughs
               processor, and 7.   Detects over-sized line
               situations.

          This routine computes a BCC value, the XOR-ed sum of ALL
     input  characters  that  were  input  for transmission to the
     Burroughs processor.  When  the  full  buffer  is  ready  for

     transmission  to  the Trunk line, a completion status will be
     set into the Read Status byte (P.RST) and a  Read  Completion
     flag  (PS.RF)  set in the Port Status byte (P.PST) of the PCB
     to trigger mainline completion handling.

26.  SF30 Module - Port Write Interrupt Service Processing Routine

               This routine has six entry points:

                    PW0: entry point for the Console;

                    PW1: entry point for PCB 3;

                    PW2:  entry  point  for PCB's 5, 9, 13, 17 and
                         21;

                    PW3:  entry  point for PCB's 6, 10, 14, 18 and
                         22;

                    PW4:  entry  point for PCB's 7, 11, 15, 19 and
                         23; and

                    PW5:  entry  point  for PCB's 4, 8, 12, 16 and
                         20.

          This    multiple-entry   ISR   routine   processes   the
identification of the Port which caused the Interrupt Entry in the
same  manner  as  the  SF20  Port  Read  ISR  logic.  Refer to the
description in that module's discussion for more details.

          The ISR handles the Write buffer character processing to
     complete the Write function for terminal Ports 2 through  23.
     The following conditions are handled by this routine:

          1.   Output character buffer processing;

          2.   Carriage  return (CR) and form feed (FF) delays (if
               defined) by sending the specified number  of  ASCII
               NULL  characters  after the transmission of a CR or
               FF; and

          3.   Write completion handling.

          When the  output  sequence  is  complete,  a  completion
     status  is  placed  in  the Write Status byte (P.WST) and the
     Write Completion flag is set in the Port Status byte  (P.PST)
     of the PCB.

27.  SF40 Module - Trunk Read Interrupt Service Processing Routine

               This routine has two entry points:

                    TR0: entry point for Trunk 0, and

                    TR1: entry point for Trunk 1.

          The ISR entry points for this routine specify the  table
     address  for  the  appropriate  Trunk  PCB and Device Address
     entries. In this manner, the logic appears only ONCE but will
     process Read Interrupts for either of the two Trunk lines (if
     both are defined).

          It is responsible for the following actions:

          1.   Protocol interpretation and response for the  Trunk
               lines,

          2.   Traffic receipt from the Burroughs destined for the
               Ports,

          3.   Protocol verification,

          4.   Poll address verification,

          5.   Oversized line detection, and

          6.   Burroughs-bound  traffic  control  by  coordination
               with the Trunk Write ISR and  the  mainline  logic.

          This  routine  is  the  sole  validator  of the protocol
     messages  from  the  Burroughs.  Invalid  lengths,  bad  poll
     addresses, etc will result in error conditions being noted by
     this routine. If traffic is sent from  or  requested  by  the
     Burroughs  processor,  this routine verifies the poll address
     and request by the processor and attempts to fill  the  same.
     Refer  to  information on the protocol for the Burroughs link
     for specific details. The Burroughs protocol buffers accepted
     by this routine are:

          1.   Message buffers,

          2.   POL requests for Burroughs-bound traffic,

          3.   SEL requests for permission to send a buffer  to  a
               terminal, and

          4.   CON buffers indicating the Burroughs  is  declaring
               the  line  to be in Contention mode (that is, "wake
               me up if you have any traffic").

          This  routine  also  handles completion of Trunk Writes,
     since the buffers sent to the Byrroughs MUST be  acknowledged
     by   the  processor  before  a  Trunk  Write  action  can  be
     considered completed. Read Completions for the Trunk(s) occur
     only  after a buffer has been received for one of the defined
     terminal   Ports.   ALL   reads   on   the    Trunk(s)    are
     "double-queued",  i.e. a second buffer MUST be waiting before
     the receipt of a buffer destined for a Port  is  acknowledged
     by  the  multiplexor. If the multiplexor is in HALT mode or a
     second read buffer does NOT exist (due to Trunk  read  buffer
     pool  usage),  SELect  requests  will NOT be acknowledged. As

     part of the Trunk timeout processing, the receipt of a POL or
     SEL request causes the Contention Break timer condition to be
     canceled.

28.  SF50  Module  -  Trunk  Write  Interrupt  Service  Processing
     Routine

          This routine has two entry points:

               TW0: entry point for Trunk 0, and

               TW1: entry point for Trunk 1.

          The ISR entry points specify  the  appropriate  PCB  and
     Device Address entries for the Trunk to be processed. In this
     fashion, the logic  to  process  either  Trunk  line's  Write
     Interrupts occurs only ONCE.

          This routine merely outputs ALL characters in the  Trunk
     write  buffer and turns off the Interrupt Enable bit when the
     last  character  has  been  transmitted  to   the   Burroughs
     processor. It also clears the Trunk Write Buffer Address word
     (P.WBFA)  in  the  PCB  to  allow   further   Trunk   traffic
     processing.



             BMUX Configuration Module Documentation

29.  SF60 Module - Configuration Generator

          This routine uses standard RT-11 directives for terminal
     and disk I/O to prompt the  user  for  a  definition  of  the
     Trunk(s)  and  Port(s) he wishes to use. After the definition
     has been completed, it is stored on a  mini-floppy  disk  for
     subsequent  retrieval  by  the  multiplexor  PCBSET  routine.

          The minimum configuration consists of a Trunk  (PCB's  0
     or  1) and the Console Port (PCB 2). ALL others are optional.
     The data structure module, SF2, is commonly used by both  the
     Configuration  Generator  and  the  Multiplexor.  The user is
     prompted, starting at PCB 0 and proceeding to PCB 23, for the
     needed information. Refer to the user documentation for order
     and limits upon the  various  prompts  by  the  Configuration
     Generator.  If  a port is NOT defined, its Source (P.SOU) and
     Destination (P.DST) bytes contain a -1 value. The  Statistics
     are  preset  for  each  Trunk or Port defined to collect BOTH
     Error and Traffic counts. All numeric inputs are  assumed  to
     be DECIMAL values. All inputs are validated for size, but the
     SITE and OWNER fields are  validated  for  length  ONLY,  and
     stored AS ENTERED.

          Entry of two Control-V's causes the PCB  to  be  skipped
     UNLESS  it is PCB 2. If a Trunk is NOT defined, the Generator
     will exit after the definition  of  the  first  Port  PCB.  A
     Control-V  and  an ASCII 'E' causes the remaining PCB's to be
     skipped and not defined.



                BMUX Data Structure Documentation

30.  SF2 Module - Data Structure

          The  following  data  elements  comprise  the functional
     control set for both the  Configuration  Genertator  and  the
     Multiplexor.  The  following table provides the item-specific
     information:

          Label:         Description:

          CR1-CR5        These are canned responses used to handle
                         the Burroughs protocol

          CR6            This buffer is sent  to  the  appropriate
                         Trunk  to  break the Contention condition
                         on that Trunk. The proper POLL ADDRESS is
                         first  inserted  after the EOT character.

          CRTAB          This is a table of  the  canned  response
                         addresses.

          TRKSRP         Each byte (0/1) is used by  the  mainline
                         to  scan  for traffic to be placed in the
                         Burroughs-bound table for the PCB  number
                         held in that Trunk's TRKRSP byte. This is
                         used only by the mainline.

          CONFLG         Non-zero  values  in the respective bytes
                         (0/1)  indicate  that  the  corresponding
                         Trunk  line  is  in Contention mode. This
                         acts as  a  communications  mechanism  to
                         relay the receipt of a Contention message
                         by the Trunk Read ISR  to  the  mainline.

          TRAPA          The  Trunk  Read  ISR uses the respective
                         bytes (0/1) to signal to the mainline the
                         PCB  from  which it wants traffic sent to
                         the Burroughs via the Trunk Write process
                         (in response to a POLL).

          TRDQ2          The mainline stores the  address  of  the
                         second   buffer  of  the  "double-queued"
                         buffer pair in the respective words (0/1)
                         for  each  Trunk to signal the Trunk Read
                         ISR that it can accept buffers  from  the
                         Burroughs.  This  "double-queued"  buffer
                         process   prevents   "windows"   in   the
                         monitoring  of  the  Trunk communications
                         from the Burroughs processor.

          TSP-TEP        These  two pointers hold the starting and
                         ending addresses  for  the  active  Trunk
                         buffer  pool  buffers. The buffer request
                         and release routines maintain the  values
                         of the pointers.

          PSP-PEP        Used as TSP and TEP,  but  for  the  Port
                         buffer pool.

          SPTR-PEN       These  scratch  areas  are  used  by  the
                         buffer  request  and  release routines to
                         examine the buffer pools.

          PRPTR-TWPTR    These pointers are used to hold the entry
                         point table addresses for the  Trunk  and
                         Port Read/Write ISR's.

          HALTFL         This byte, if  non-zero,  indicates  that
                         HALT mode is in effect.

          INIFLG         This byte,  if  non-zero,  indicates  the
                         multiplexor is NOT yet initialized.

          STDFLG         If  this  byte  is  non-zero,  the   STAT
                         command  is  processing  lines of display
                         information.

          SPFUN          This  table is used to define the list of
                         special  subroutines  the  mainline  must
                         process between each complete scan of ALL
                         the defined PCB entries.

          CCMD           The  Console  command  decoder  uses this
                         table to identify a valid Console command
                         and  execute  the proper routine for that
                         command.

          ISRTAB         This  table is used during Initialization
                         to establish the Interrupt  Vector  entry
                         addresses  for  Interrupt processing. The
                         Vector  address,  Read  ISR  address  and
                         Write  ISR  address comprise a unit entry
                         in this table.

          DA1-DA8        These  variable-length  tables consist of
                         PCB number/Device Read CSR address  pairs
                         for   the   Trunks/Ports   utilizing  the
                         specified Interrupt Vector  as  entry  to
                         the Read or Write ISR's. Refer to the ISR
                         module    documentation    for    further
                         information.

          ISRSAV         This area is used by  the  Initialization
                         process  to save both the prior Interrupt
                         Vector  contents  and  the  prior  Device
                         Address  contents  before the multiplexor
                         "takes over" for its operations. In ABORT
                         or EXIT conditions, this table is used to
                         reset the Interrupt  Vectors  and  Device
                         Address  Registers  before giving control
                         back to RT-11.

          CONSAV         The   Console   Device  Address  Register
                         contents are also saved in this area  for
                         abort reset.

          RCSRA-XBUFA    This  set  of  Device  Address   Register
                         pointers  is  used SOLELY by the mainline
                         to access a given device  for  Read/Write
                         initiation.

          RCSRI-XBUFI    This  set  of  Device  Address   Register
                         pointers  are used soley by the currently
                         active  ISR  routine   to   process   the
                         interrupt.

          WAIT1-NEWSEC   RT-11 directive scratch areas.

          PAT            Software  maintenance  scratch  area  for
                         absolute patches.

          CUMTAB         Statistics  cumulative  accumulator table
                         (2 words/PCB).

          PCB            Port  Control  Block  table.  This  table
                         defines  the  active   PCB's   that   the
                         multiplexor   must   process.  Being  the
                         Master   control   structure   for    the
                         multiplexor's  operation,  it is much too
                         difficult  to   describe   ALL   of   the
                         interactions   in  this  segment  of  the
                         documentation to any detail. In  general,
                         it  controls  traffic  flow, buffer flow,
                         ISR processing, traffic/error  statistics
                         collection,  Trunk timeout detection, and
                         status coordination between the ISR's and
                         the  mainline. Please refer to the System
                         Equates documentation for PCB
                         definitions.

          POLTAB         This table contains the user-defined POLL
                         ADDRESS  for  each  defined  PCB, 2 ASCII
                         bytes in PCB  order.  Unused  areas  will
                         contain  a  -1  value,  and ASCII control
                         characters  are  not  permitted  by   the
                         Configuration  generator.  This  table is
                         used by the Trunk Read ISR to validate  a
                         POLL  ADDRESS  received  in  a POL or SEL
                         buffer from the Burroughs processor.  The
                         Port  Read  ISR uses this table to define
                         the POLL  ADDRESS  value  in  the  header
                         segment  of  the buffer to be sent to the
                         Burroughs CPU.

          TTYPE          This  table  contains  the  6-byte  OWNER
                         value  entered  by  the  user   via   the
                         Configuration Generator. Undefined values
                         will contain a "******" value.

          BRTAB          The  SITE  values entered by the user via
                         the Configuration  Generator  are  stored
                         here,  5 bytes per PCB in PCB order. If a
                         PCB is not defined, a "*****" value  will
                         appear.

          PCBDAT         This table provides a cross-reference  of
                         PCB   numbers   and  their  corresponding
                         Device Address Register addreses.

          TWBPCB         This table holds buffer addresses, in PCB
                         order, which are to be transmitted to the
                         Burroughs for processing. If no buffer is
                         queued   from   any   given   PCB,    the
                         corresponding  word will be a zero value.

          RVITAB-JORST   Scratch areas for future expansion.