DDDD    SSS   K   K  L      IIIII  BBBB
                    D   D  S   S  K  K   L        I    B   B
                    D   D  S      K K    L        I    B   B
                    D   D   SSS   KK     L        I    BBBB
                    D   D      S  K K    L        I    B   B
                    D   D  S   S  K  K   L        I    B   B
                    DDDD    SSS   K   K  LLLLL  IIIII  BBBB 











                          DSKLIB (Disk Librarian) V02

                                January 6, 1982




    NOTE: THIS PROGRAM IS SUBMITTED as is TO DECUS.  WHILE I WOULD APPRECIATE
    HEARING ABOUT ANY PROBLEMS OR SUGGESTIONS, I CANNOT PROMISE TO RESPOND.

                                                             Joel Berez






                               Copyright (C) 1982
                                Berez Associates
                               64 Jacqueline Road
                               Waltham, MA  02154













                                   CHAPTER 1

                             Introduction to DSKLIB          






          1.1  Purpose of DSKLIB


               RT-11 includes facilities for creating and  maintaining
          multiple  files on a disk device through the use of a direc-
          tory.  A utility is also provided for listing subsets of the
          directory  in  various  formats.   This utility (PIP or DIR)
          makes it easy to find a particular file as long as the  file
          is currently on-line.

               In installations  using  low-capacity  disks,  however,
          there  tend to be many more disks than drives.  At any given
          time, most files will be off-line and  inaccessible  to  the
          RT-11  directory  programs.  Finding a file may require exa-
          mining titles  written  on  disks  for  a  likely  category,
          searching  through previously printed directory listings, or
          mounting disks successively until the right one is found.

               It is of course correspondingly more difficult to  find
          all  copies of a particular file, all files of a given type,
          or even a good place to put a new file.  The problem is com-
          pounded on systems using floppy disks or on development sys-
          tems, which both generally have large  numbers  of  off-line
          disks.    This  is  also  true  of  systems  using  archives
          (pseudo-devices), which can have a large number of  directo-
          ries  that  need to be searched, even though they may all be
          "on-line" at once.

               DSKLIB solves these problems by maintaining  a  single,
          compact directory of files from many disks.  This master di-
          rectory may be kept on-line for easy searching and updating.
          Whenever  files are added or removed from a disk, the master
          directory may be quickly updated.  DSKLIB provides  commands
          for  utilizing  this information to find files on any catal-
          oged disk.


          Introduction to DSKLIB                              PAGE 1-2



          1.2  Configuration Supported




          1.2.1  Software


               DSKLIB is intended to run under any of a family of sim-
          ilar  monitors:   RT-11,  CTS-300, and HT-11.  Specifically,
          DSKLIB has been tested and should properly operate under the
          following  groups of monitors.  In this document, "RT-11 V2"
          will be used to refer to RT-11 V2C, CTS-300 V3.5,  or  HT-11
          V1.   "RT-11 V3" will refer to RT-11 V03, RT-11 V3B, CTS-300
          V4, or CTS-300 V5.  "RT-11 V4" will refer to RT-11 V04.00 or
          CTS-300  V6.   Although  DSKLIB may also operate under other
          versions of these monitors or under other similar  monitors,
          there  is  no  guarantee that it will behave exactly as des-
          cribed herein.

               DSKLIB will also run with TSX under any  of  the  above
          mentioned  monitors that is also supported by TSX.  However,
          due to certain peculiarities of TSX, the  terminal  handling
          characteristics of DSKLIB may not be identical under a given
          monitor with  and  without  TSX.   This  document  describes
          DSKLIB  without  TSX,  but is generally also applicable to a
          TSX environment.

               DSKLIB will run in the background  under  any  monitor.
          In  addition,  it  may be run in the foreground under any of
          the RT-11 V3 or V4 monitors.



          1.2.2  Hardware


               Since no special instructions are used, except  option-
          ally   EIS,   all  PDP-11  processors  are  supported.   EIS
          hardware, if present, may be used to improve performance.

               DSKLIB will run comfortably in 8K words of memory,  not
          counting  the monitor.  More memory may be dynamically used,
          if available, but is generally not necessary.

               At least two disk drives are necessary for DSKLIB to be
          useful.   Up to 10 drives are supported, which may be of any
          type handled by the monitor, and need not all be of the same
          type.

               Any type of terminal may be used,  and  DSKLIB  distin-
          guishes  between  printing  and display terminals when char-
          acters are deleted.  Most output can also be directed  to  a


          Introduction to DSKLIB                              PAGE 1-3



          printer.



          1.3  Terminology


               1.  DRIVE
                   Digit (0 to 9) identifying one  of  the  predefined
                   disk  drives or an explicitly entered device or ar-
                   chive name.  May be any device that is RT-11 direc-
                   tory structured, including DECTAPE.

               2.  ARCHIVE
                   A file that may be accessed by the archive  handler
                   as a pseudo-device (see Section 1.4.3).

               3.  DISK
                   The medium mounted on a drive.  Also refers to  the
                   information  stored in the catalog about a particu-
                   lar disk, identified by the disk number.

               4.  VOLUME
                   Used synonymously with DISK.

               5.  DIRECTORY
                   The area on a disk from which DSKLIB extracts  file
                   information.  Also, a listing of all disks current-
                   ly cataloged.

               6.  ENTRY
                   The block of information in a disk directory  or  a
                   DSKLIB  catalog identifying an RT-11 file or volume
                   and various characteristics.

               7.  FILE
                   Either an RT-11 file or an entry in the DSKLIB  ca-
                   talog.

               8.  CATALOG
                   An RT-11 file created and used by DSKLIB to contain
                   information about a set of disks and their files.

               9.  PRIMARY CATALOG
                   The default catalog used by most DSKLIB commands.

               10. SECONDARY CATALOG
                   Another catalog that may be open at the  same  time
                   as  the  primary.  Some commands optionally use it,
                   but its main purpose is for the MOVE command, which
                   requires two catalogs.

               11. VOLUME ID


          Introduction to DSKLIB                              PAGE 1-4



                   The  twelve  character  identifier  stored  in  the
                   disk's  header  block by DSKLIB or DUP.  DSKLIB de-
                   codes it into disk number and name.   Special  file
                   entries in the catalog contain volume information.

               12. DISPLAY TERMINAL
                   A       terminal       that       supports        a
                   backspace-space-backspace  combination  to  erase a
                   character.

               13. PRINTING TERMINAL
                   Any terminal not fitting the display  terminal  de-
                   finition.

               14. PRINT COLUMNS
                   The number of columns across a line in  which  file
                   entries will be printed.




          1.4  Installation




          1.4.1  Generating and Customizing DSKLIB


               The distribution disk contains all files necessary  for
          installation  of  DSKLIB  for any of the RT-11 monitors sup-
          ported.  The same version of DSKLIB will run under any moni-
          tor,  but  it  may not be linked under RT-11 V2.  Therefore,
          the following instructions,  which  allow  more  flexibility
          under  RT-11  V3  or  V4,  refer  to the monitor under which
          DSKLIB is generated, and not to the one under which it  will
          ultimately be run.



          1.4.1.1  RT-11 V3 and V4 - 

               DLBOPT.MAC contains the options that may be set to cus-
          tomize  DSKLIB.  This file should be edited as desired.  The
          following options exist:

               1.  DEVTAB
                   Ten RAD50 words containing the device names of  the
                   drives  known  to DSKLIB, referenced in the program
                   by digits 0-9.  Physical names are recommended  al-
                   though logical names will also work.


          Introduction to DSKLIB                              PAGE 1-5



               2.  DPBLKS
                   The number of blocks, one to  four,  that  will  be
                   used  in each catalog for pointers for disks catal-
                   oged.  Disks need not be numbered continuously from
                   zero,  but  the  highest number that may be used is
                   equal to DPBLKS*256-3.  Note that this  option  af-
                   fects  the  generation of a catalog, which requires
                   catalogs to be used only with a DSKLIB  having  the
                   same DPBLKS specification.

               3.  PROMPT
                   The character used at the top level  of  DSKLIB  to
                   prompt  for  a  command.   This might be changed to
                   avoid confusion with another program using the same
                   prompt character.

               4.  CATNAM
                   The name of the catalog file that will be automati-
                   cally opened when DSKLIB is first started.

               5.  PRTNAM
                   The default file name that will be opened when out-
                   put  is  directed  to the printer.  May be either a
                   sequential or a file-structured device.

               6.  DEFORD
                   File entries found in a catalog search are  usually
                   sorted  before  printing.  The default order of the
                   five sort keys, from major to minor, may be  speci-
                   fied  here.  When a particular key is selected by a
                   user option, the other four will still  follow  the
                   order given here.

               7.  TRMTYP
                   When DSKLIB is first started, if it  is  unable  to
                   determine  the  terminal  type, it will use the de-
                   fault specified here.

               8.  TT0COL
                   The default number of print columns for  a  type  0
                   (printing) terminal.

               9.  TT1COL
                   The default number of print columns for  a  type  1
                   (display) terminal.

               10. PRTCOL
                   The  default  number  of  print  columns  for   the
                   printer.

               11. PRTLNS
                   The default  number  of  lines  per  page  for  the
                   printer.  Specify zero here to disable paged mode.


          Introduction to DSKLIB                              PAGE 1-6



               12. OWNER
                   A twelve character ASCII string used to  initialize
                   a volume's owner field.


               After DLBOPT.MAC is edited, it should be  assembled  as
          follows  (assuming  all DSKLIB files are on the default dev-
          ice):

                    .MACRO DLBOPT

          The correct version of  DSKLIB  must  be  selected  for  the
          hardware to be used.  If EIS support is desired:

                    .RENAME DSKLIB.EOB DSKLIB.OBJ

          If EIS hardware is not present, or is not to be used:

                    .RENAME DSKLIB.NOB DSKLIB.OBJ

          Then DSKLIB must be linked using:

                    .LINK DLBOPT,DSKLIB/EXE

          The result will be the utility  program,  DSKLIB.SAV,  which
          will run in the background.

               It is also possible to link DSKLIB for foreground oper-
          ation:

                    .LINK DLBOPT,DSKLIB/EXE/FORE

          To run DSKLIB in the foreground, it will be necessary to al-
          locate workspace:

                    .FRUN DSKLIB/N:n

          The number n must be at least (DPBLKS+4)*1000 octal.   Extra
          space  may  be  allocated for large searches in multiples of
          1000.



          1.4.1.2  RT-11 V2 - 

               Since DSKLIB may not be  linked  under  RT-11  V2,  two
          linked  versions  are provided, one with EIS support and one
          without it.  To select EIS support:

                    .R PIP
                    *DSKLIB.SAV=DSKLIB.ESV/R
                    *^C



          Introduction to DSKLIB                              PAGE 1-7



          If EIS hardware is not present, or is not to be used:

                    .R PIP
                    *DSKLIB.SAV=DSKLIB.NSV/R
                    *^C

               DSKLIB.SAV is now ready to use, with the options preset
          as  shown  in  the distributed DLBOPT.MAC file.  However, if
          desired, options 1, 4, 5, and 12 may be changed using PATCH:

                    .R PATCH

                    FILE NAME--
                    *DSKLIB
                    *(loc)/  (old value)   (new value)
                    *E


               The following locations may be  examined  and/or  modi-
          fied.  Unless otherwise specified, all locations are RAD50.

                    1000/    (device name for drive 0)
                    1002/    (device name for drive 1)
                    ...
                    1022/    (device name for drive 9)
                    1024/    (default catalog device)
                    1026/    (first half of default catalog name)
                    1030/    (last half of default catalog name)
                    1032/    (default catalog type)
                    1034/    (default printer device)
                    1036/    (first half of default printer file name)
                    1040/    (last half of default printer file name)
                    1042/    (default printer file type)
                    1044/    (first two characters of owner name in
           ASCII)
                    1046/    (third and fourth characters)
                    ...
                    1056/    (eleventh and twelveth characters)



          1.4.2  Auxiliary Programs


               Two small programs are included  with  DSKLIB  in  both
          .SAV  and  source  form.   These utilize a feature in DSKLIB
          that allows programs to chain to it and pass commands.

               UA causes DSKLIB to do an Update with the  All  option.
          It  is useful for quickly updating the cataloged information
          for all disks currently on-line.

               DLBCOM takes a command line  and  passes  the  text  to


          Introduction to DSKLIB                              PAGE 1-8



          DSKLIB.   It  is  intended  for  calling DSKLIB from command
          files (not available under RT-11 V2).  The line may end with
          a "Q" to exit from DSKLIB and continue the command file.  If
          DSKLIB runs out of text before exiting or if some error  oc-
          curs, it will begin accepting input from the terminal.

               Both of these programs expect DSKLIB  to  be  found  as
          SY:DSKLIB.SAV.   They  may be reassembled to use a different
          name, if necessary.  UA might also be changed to pass a dif-
          ferent line of text.



          1.4.3  Archive Handler


               Also included with DSKLIB are files  used  to  maintain
          archives:   the  archive handler, an archive definition pro-
          gram, and documentation describing their use.  Archives  are
          pseudo-devices  which may be created as files on larger dev-
          ices and used to conveniently partition and organize files.

               They can be extremely useful  by  themselves  and  work
          particularly  well  when  used  in  conjunction with DSKLIB.
          However, since the archive handler, which  runs  only  under
          RT-11  V4,  must  perform certain operations that are beyond
          normal RT-11 support, it is not supported by  Berez  Associ-
          ates and must be used at your own risk.













                                   CHAPTER 2

                                DSKLIB Operation          






          2.1  Initialization


               The first thing required to use DSKLIB is the  creation
          of  a  catalog,  preferably  the default catalog.  If at all
          possible, the default catalog should reside, along with  the
          DSKLIB  program, on a permanently mounted disk, probably the
          system disk.  All disks that are part of  normal  operations
          should be cataloged here.

               Where there are logically two or more groups  of  disks
          that  are not normally used together, it may be desirable to
          have one catalog for each group.  A group might consist, for
          example, of all disks owned by a particular department, per-
          son, or project;  all MUBASIC-related disks;  or  a  set  of
          backup  disks.   In such cases, there is often a system disk
          for each group.  The group catalog would then reside there.

               The Create command in DSKLIB is used to create a  cata-
          log  file.   Each disk to be cataloged there must be given a
          suitable volume id containing a volume  name  and  a  unique
          (for that catalog) number.  The Volume ID Change command may
          be used.  Alternatively, DUP (INIT/VOL:ONLY)  may  be  used.
          In  the  latter  case,  the format required is ###nnnnnnttt,
          where ### is the zero-filled disk number, nnnnnn is the  vo-
          lume name, and ttt is the volume type.

               Once the disks are given numbers and  names,  they  may
          all  be  cataloged using the Update command.  This completes
          the initialization procedure.


          DSKLIB Operation                                    PAGE 2-2



          2.2  Catalog Maintenance


               Keeping the DSKLIB catalog up to date  simply  requires
          using  the  Update command for each disk whose directory has
          changed (files added, deleted, or replaced) since  last  ca-
          taloged.  There are three commonly used methods for ensuring
          that the catalog remains current.  Any  of  these,  or  some
          variation,  may  be used, depending upon individual require-
          ments.

               Each modified disk may be cataloged just  before  being
          dismounted.  The disks remaining on-line could be cataloged,
          possibly using the All and/or Rchive options of  Update  (or
          the UA program), at the end of each day or work session.

               Alternatively, all disks used during some  time  period
          may  be  kept  together.   Then they could be cataloged in a
          batch before returning them to the main library.

               A third technique, where completely up to date informa-
          tion is not essential, is to simply recatalog all disks on a
          periodic basis or whenever appropriate.

               Occasionally it may be necessary to change the size  of
          the  catalog.  If the catalog becomes full, an error message
          will be displayed.  The catalog  could  also  be  needlessly
          large  after  a number of disks are Expunged.  The Size com-
          mand may be used at any time to  determine  current  catalog
          size and percentage utilization.

               The catalog may be expanded by extending the file  with
          DUP  (RT-11 V3 or V4) or PIP (RT-11 V2).  It may be expanded
          or contracted in DSKLIB by creating a new catalog of the de-
          sired  size  and  using Move with the All option to transfer
          the information from the old one to the new one.



          2.3  Normal Usage


               Using DSKLIB to find files is  quite  easy.   When  the
          program  is  first started, it does a number of things auto-
          matically.  Under RT-11  with  multi-terminal  support  (not
          available under RT-11 V2), DSKLIB will determine the type of
          terminal in use from the monitor.  It will also get the ter-
          minal  width.  In the absence of multi-terminal support, the
          defaults specified at DSKLIB generation time will be used.

               At this time DSKLIB will attempt to  open  the  default
          catalog.   If  that  catalog is not found, a message will be
          displayed.


          DSKLIB Operation                                    PAGE 2-3



               Once the program initialization  is  completed,  DSKLIB
          will  display  the  command  prompt character and wait for a
          command.  Commands are invoked by typing a single character.
          A  question  mark (?) may be typed to get a list of all com-
          mands.  The Help command may be used for a concise  descrip-
          tion of a command and its arguments.

               Anytime input is requested, a ^C may be typed to return
          to the command level.  This is especially useful for exiting
          from a command inadvertantly entered.  (Under  RT-11  V2  it
          will  also be necessary to REENTER DSKLIB.) During long com-
          mands, two ^Cs will cause a return to command level.  (Under
          RT-11 V2, this must be followed by REENTER.)

               A few commands may be particularly useful  when  DSKLIB
          is  first  started.  If the default catalog was not found or
          if a different one is desired, the Open Catalog command  may
          be  used to open the proper catalog file.  The Terminal Type
          command may be used to change  the  current  terminal  type.
          The  Width  of  Terminal  command  may be used to change the
          number of columns that will be  used  for  printout.   (This
          number may be overridden by a Find option.) The Printer File
          command may be used at any time to  change  the  destination
          for printer output.

               The most powerful command and the one that will be most
          frequently  used is Find.  The Find command searches the ca-
          talog for files matching the given specification and  prints
          those  file  entries in a specified format.  Besides finding
          existing files or volumes, Find may also be used to find su-
          itable places to put files, or just to count files and total
          sizes.

               Although entries may be grouped in various  numbers  of
          columns and rows per page, the entries themselves are always
          printed in a standard format.  For example:

                    35 LIBCAT.DLB  100 17-May-79

          A file named LIBCAT.DLB (probably a catalog) exists on  disk
          number 35.  It is 100 blocks long and was created on May 17,
          1979.  If the file had been protected (under RT-11 V4),  the
          entry would have been followed by a "P".

               A volume id entry looks like a file entry but is inter-
          preted  differently.   If  the  above  example were a volume
          entry, it would represent disk number 35, named  LIBCAT.DLB.
          The disk would have 100 free blocks remaining, and an Update
          would last have been done for it on May 17, 1979.

               The Directory and List commands are  special  forms  of
          the Find command that find particular entries.


          DSKLIB Operation                                    PAGE 2-4



               Finally, the Quit command is used to exit  neatly  from
          DSKLIB.  If a new catalog was created and is still open, the
          Abort command may be used to exit without  making  the  file
          permanent.  DSKLIB may be restarted after a Quit or an Abort
          using KMON's REENTER command.  The last opened primary cata-
          log  will  be reopened and the terminal characteristics will
          remain unchanged.  (Note that a ^C under RT-11 V2 acts  like
          the  Abort  command, unless it is followed by the KMON CLOSE
          command.  In the latter case, it is equivalent to  the  Quit
          command.)













                                   CHAPTER 3

                                DSKLIB Commands          




               Each command will be described in  the  following  sec-
          tions.   The  command format is shown first and then a deta-
          iled description is given.

               In the command format, text enclosed in angle  brackets
          is  typed  by  the  user.   Everything  else is displayed by
          DSKLIB.  Within the angle brackets, uppercase text is  typed
          exactly  as shown.  Lowercase words represent parameters en-
          tered:

               1.  <num>
                   A positive integer, preceded by a number  sign  (#)
                   or  an  equal sign (=) prompt, terminated by a car-
                   riage return.

               2.  <file name>
                   Standard RT-11  format  file  name  (dev:name.typ),
                   preceded by a "named:" prompt, terminated by a car-
                   riage return (after any switches).  A  <file  name>
                   may  be  followed by one or more <switch>es.  Note:
                   the Find command has a special format.

               3.  <switch>
                   An option name, which may be abbreviated to two  or
                   more characters.  A slash (/) must be typed preced-
                   ing the switch.  Any <file name> may be followed by
                   <switch>es.   /HELP  will  always list the ones al-
                   lowed for that command.

               4.  <command>
                   The first character of a command name, preceded  by
                   the  command  prompt  (colon, unless changed by the
                   generation option).

               5.  <digit>
                   A number between zero and nine following  a  number
                   sign (#) prompt.



          DSKLIB Commands                                     PAGE 3-2



               A colon following an argument in angle  brackets  shows
          the default value if no text is typed preceding the carriage
          return.  A vertical bar represents a choice between two  op-
          tions.  Square brackets enclose optional arguments.



          3.1  Abort


                    :<A>bort
                     Are you sure? <Y>es|<N>o

               Exits from DSKLIB like the Quit command.  However, if a
          new  catalog  file had been created and not yet closed, that
          file will be purged.  If it had the  same  name  as  another
          file, the original file will not be deleted.



          3.2  Create Catalog


                    :<C>reate catalog named: <file name>; size=<num>
                     Overwrite existing catalog? <Y>es|<N>o

               Creates a new catalog file with the specified name  and
          Opens  it.   Any  RT-11  directory  structured device may be
          used.  The default file type is DLB.



          3.2.1  Arguments


               The size given is the number of blocks in the new  file
          and  must  be  between  DPBLKS+2 and 512, inclusive.  On the
          average, the number of blocks required in a catalog file for
          F  files  on  V  volumes is [(F+V)/6+V/2]/8+DPBLKS+1.  Extra
          blocks should also be allocated for expansion.

               The "overwrite existing catalog" message will be  given
          if the new catalog replaces a file with the same name.  A No
          response will abort the operation.  A Yes will continue, but
          the  old  file  will  not actually be replaced until the new
          file is closed either by a Quit or an  Open/Create  for  the
          same catalog type (primary or secondary).

               Whether the new catalog is overwriting an existing  one
          or  not,  until the file is closed, the Create may be undone
          by the Abort command.


          DSKLIB Commands                                     PAGE 3-3



          3.2.2  Switches


               /SECONDARY catalog
                    Opens the new file as the secondary catalog.  This
                    would  be used when creating a new catalog to Move
                    disks to.

               /HELP
                    Lists switches allowed.



          3.3  Directory of Disks


                    :<D>irectory of disks

               Displays the volume entries of all disks in the primary
          catalog,  sorted  by  disk  number.   This  is equivalent to
          ":Find file named:  /VOLUME/DISK" except that the sorting is
          slightly different and it may be faster.



          3.4  Expunge Disk


                    :<E>xpunge disk #<num>

               Removes all of the entries associated with  the  speci-
          fied disk from the primary catalog.  This might be done if a
          disk is being removed from the library, if  the  number  has
          been changed, or if the disk has been Moved to another cata-
          log.



          3.5  Find File


                    :<F>ind file named: <file name:*.*>[<switch>...]

               Finds files (entries) in the catalog and lists them  on
          either  the  terminal or printer.  The number of files found
          and their total sizes are displayed on the terminal  at  the
          end of the listing.


          DSKLIB Commands                                     PAGE 3-4



          3.5.1  File Name Format


               The file name format allowed is  an  extension  of  the
          format used by the file utilities (PIP, DIR) of RT-11 V3 and
          V4, which is itself an extension of the format used by RT-11
          V2.   The format is name.type, where "name" contains zero to
          six characters and "type" contains zero to three characters.
          The dot is required only if a type is given.

               The characters may be any allowed in a file name (A  to
          Z, 0 to 9) and the special characters, asterisk (*) and per-
          cent (%).  A percent will match any  single  character  (in-
          cluding a space) in a file name.  An asterisk will match any
          series of zero or more characters.   Any  arbitrarily  hairy
          combination  of  these characters is allowed, as long as the
          length restrictions are not exceeded.  For example:

                    LIBCAT.DLB

          Finds files named LIBCAT.DLB.

                    FILE%.DAT

          Matches names such as FILE1.DAT, FILED.DAT, or FILE.DAT.

                    *.SAV
                    .SAV
                    *%*%*%.SAV

          These are all equivalent and will find all files whose  type
          is  SAV.  (A missing name or type is equivalent to an aster-
          isk.)

                    *A%B*.*C*

          Finds all files with an A and a B  somewhere  in  the  name,
          separated by one character, and a C anywhere in the type.



          3.5.2  Find Switches


               Although a file  name  may  always  be  followed  by  a
          switch, the switch is specifically shown in the Find command
          format to emphasize its importance.  One  or  more  switches
          are frequently used with Find to control the entry selection
          criteria and the output format.


          DSKLIB Commands                                     PAGE 3-5



          3.5.2.1  Switch Arguments - 

               A number of switches for the Find  command  require  an
          argument.   Each  switch  requiring an argument must be fol-
          lowed by a single space before the argument, even if the ar-
          gument  is  not entered, but completely defaulted.  The type
          of argument is specified in parentheses in the  switch  des-
          cription:

               1.  (number)
                   A nonnegative decimal integer.  If not entered, de-
                   faults to zero.

               2.  (date)
                   This is a superset of  the  standard  RT-11  format
                   date  (dd-mmm-yy).   This  date  is  generalized to
                   allow the three parts (day, month, and year) to  be
                   entered  in any order prefered, as long as they are
                   separated by dashes.  Furthermore, any or all parts
                   may  be  omitted  and will default according to the
                   following algorithm.

                   Consider the date components ordered from lowest to
                   highest  importance (day, month, year).  Unless all
                   lower order components  are  missing,  any  missing
                   component  will default to the corresponding compo-
                   nent of the current date.  If all lower order  com-
                   ponents  are  missing,  a component that is present
                   will refer to all dates within that component.  For
                   example,  if  only  "May" is specified, all days in
                   May of this year will be used.  Also, a  completely
                   missing date defaults to today's date.




          3.5.2.2  Switches - 

               /NAME sort
                    Sorts entries by file name.  This is the  default,
                    unless modified by the generation option.

               /TYPE sort
                    Sorts entries by file type.

               /DATE sort
                    Sorts entries by file date.

               /FILESIZE sort
                    Sorts entries by file size.

               /DISK number sort
                    Sorts entries by disk number.


          DSKLIB Commands                                     PAGE 3-6



               /REVERSE sort
                    Sorts entries in reverse order.

               /VOLUME id entries
                    Finds volume id entries instead of file entries.

               /LESS than (number)
                    Only selects entries whose  sizes  are  less  than
                    (number).   May  be used with /GREATER to select a
                    range of sizes.

               /EQUAL to (number)
                    Only selects entries  whose  sizes  are  equal  to
                    (number).

               /GREATER than (number)
                    Only selects entries whose sizes are greater  than
                    (number).   May  be  used  with  /LESS to select a
                    range of sizes.

               /BEFORE (date)
                    Only selects entries whose dates are earlier  than
                    (date).  May be used with /SINCE or /DURING to se-
                    lect a range of dates.

               /DURING (date)
                    Only selects entries  whose  dates  are  equal  to
                    (date).   Remember  that (date) may specify an en-
                    tire month or year.  May be used with  /BEFORE  or
                    /SINCE to select a range of dates.

               /SINCE (date)
                    Only selects entries whose dates are later than or
                    equal  to  (date).   May  be  used with /BEFORE or
                    /DURING to select a range of dates.

               /ONLY disk (number)
                    Selects entries  from  the  specified  disk  only.
                    This  more-or-less allows the functions of the DIR
                    program (PIP, for RT-11 V2) to be duplicated with-
                    out the need for the disk to be on-line.

               /PRINTER
                    Sends output to the printer instead of the  termi-
                    nal.   The  output will automatically be formatted
                    into pages.

               /LINES per page (number)
                    If /PRINTER is also used, overrides  default  page
                    length.   Furthermore,  if (number) is zero, paged
                    mode will be disabled.   Otherwise,  forces  paged
                    mode  for  the  terminal  using the specified page
                    length.  (number) should not include lines skipped


          DSKLIB Commands                                     PAGE 3-7



                    by the form-feed at the end of each page.

               /COLUMNS per line (number)
                    Overrides  line  width  default  for  terminal  or
                    printer.

               /QUIET
                    Finds entries, but only displays totals.  This  is
                    faster than typing a ^O to see just the totals.

               /SECONDARY catalog
                    Finds entries from the secondary catalog,  instead
                    of the primary.

               /HELP
                    Lists switches allowed.



          3.5.2.3  Switch Examples - 

                    /DURING 77

          Finds all files created during 1977.

                    STOCK/DUR 77/SINCE JUL-77

          Finds files named "STOCK" (any type) created during the last
          six months of 1977.

                    /VOL/EQ 480

          Assuming all disks are RX01 floppies,  this  will  find  all
          completely empty disks.

                    /QUIET

          Shows total number of files and blocks used.

                    /VO/QU

          Shows total number of disks cataloged and  total  number  of
          free blocks available.

                    TELNET.MAC/DATE/REV

          Used to find most recent version of specified file.

                    .BAS/SINCE APR/GR 50

          Might be used to find some BASIC program  if  the  name  has
          been  forgotten,  but it is known that the file is more than
          50 blocks large and was created no  earlier  than  April  of


          DSKLIB Commands                                     PAGE 3-8



          this year.

                    .SAV/PR

          List all SAV files on the printer.



          3.6  Help


                    :<H>elp for command:<command>

               Displays a brief description of the  specified  command
          along with the command and argument format, as shown here.



          3.7  List Disk


                    :<L>ist disk #<num>

               Lists cataloged entries for a disk.  First  the  volume
          id  entry  is  shown.   Then the file entries are displayed,
          sorted according to the default sequence.  This  command  is
          basically  equivalent  to  "Find  file  named:  /VOLUME/ONLY
          <num>" followed by "Find file named:  /ONLY <num>."



          3.8  Move Disk


                    :<M>ove disk #<num:All>

               For this command to operate, a catalog must  have  been
          previously  Opened  or  Created  with the /SECONDARY switch.
          (As for most commands, it is assumed that a primary  catalog
          is  open.) All entries for the specified disk will be copied
          from the primary catalog to the secondary.

               The entries moved will not be deleted from the  primary
          catalog.   If  that is desired, Expunge should be used after
          Move.

               Typing a carriage return without a disk number will se-
          lect  the All option.  All disks in the primary catalog will
          be individually moved to the secondary.  This option is use-
          ful  for  expanding or contracting a catalog.  A new catalog
          should be created (with /SECONDARY) of the desired size  and
          then all disks are Moved to it with this option.


          DSKLIB Commands                                     PAGE 3-9



          3.9  Open Catalog


                    :<O>pen catalog named: <file name>

               Opens an existing catalog as either the primary or sec-
          ondary.  Closes any previously open catalog of the same type
          (primary or secondary).  A previously Created catalog  would
          become permanent at this point.



          3.9.1  Switches


               /SECONDARY catalog
                    Opens the new file as the secondary catalog.  This
                    would be used to Move disks to.

               /HELP
                    Lists switches allowed.



          3.10  Printer File


                    :<P>rinter file named:<file name>

               Redirects printer output from the default file (or last
          one  given  with  this command) to the new one.  <file name>
          may be on a sequential or a file-structured device.  In  the
          latter case, each time Find is used with the Printer option,
          the file will be reopened and  any  previous  file  will  be
          lost.



          3.11  Quit


                    :<Q>uit

               Exits from DSKLIB  after  closing  any  open  catalogs.
          Closing a newly created catalog makes the file permanent and
          deletes any older file with the same name.  If that  is  not
          desirable, use the Abort command.


          DSKLIB Commands                                    PAGE 3-10



          3.12  Size of Catalog


                    :<S>ize of catalog ...

               Lists information about the primary catalog,  including
          its  name, size in blocks, and percentage utilization.  Note
          that a newly created catalog will be more than 0%  full  be-
          cause of the blocks used for header information (DPBLKS+1).

               The space used in a catalog is not necessarily contigu-
          ous.  This has the effect that although a catalog may be ex-
          panded by extending the file, it may not  be  contracted  by
          truncating  blocks  from the end, even though it may be only
          partially full.



          3.13  Terminal Type


                    :<T>erminal type is printing|display

               Changes the terminal type and shows the new one.  Since
          there are only two types, this command simply toggles to the
          other one each time it is used.  It also sets the number  of
          print  columns  to  the default assciated with this terminal
          type (a generation option).

               DSKLIB handles the two terminal types differently  only
          when  characters typed are deleted.  On a printing terminal,
          the deleted character is echoed.  On a display terminal,  it
          is erased.  Typing a ^U is always equivalent to individually
          deleting all previously typed characters.



          3.14  Update


                    :<U>pdate from drive
           #<digit>|<A>ll|<F>ile|<R>chives

               Copies directory information from the  specified  drive
          into the primary catalog.  The digit identifies a predefined
          disk drive.  Typing an "A" instead of a  digit  invokes  the
          All option, which does an Update for every drive in DSKLIB's
          list.

               The File option will give the standard "named:"  prompt
          and  may  be  used to specify either a device name or a com-
          plete file name.  The former is used for specifying  devices
          that  were not predefined to DSKLIB.  The latter may be used


          DSKLIB Commands                                    PAGE 3-11



          for archive files or for images of small devices  that  have
          been  backed-up  to a larger device (using COPY/DEVICE/FILES
          under RT-11 V4).

               The Rchives option does an Update for all archives cur-
          rently  defined  to  the archive handler.  It is also a nice
          way of simply determining which archives are defined.



          3.15  Volume ID Change


                    :<V>olume id change for drive #<digit>|<F>ile
                    from #nnn; named: ffffff.ttt; owner: xxxxxxxxxxxx
                    to #<num:nnn>; named: <file name>

               Displays volume number, name, and owner for the disk on
          the  specified drive and allows them to be changed.  As with
          the Update command, a file name (or  device)  may  be  given
          instead  of  a  drive  number.   "nnn" is the current volume
          number, "ffffff.ttt" is the volume name  (in  standard  file
          name  format),  and  the  x's  are the contents of the owner
          field.

               For convenience, if a new number  is  not  entered,  it
          will  default  to  the old one, so that only the volume name
          will be changed.



          3.15.1  Switches



               /OWNER field set
                    Sets the volume owner field to the text  specified
                    during  DSKLIB generation.  This might be used the
                    first time the volume name and number are set.

               /RT11A format
                    Initializes volume header block in the format used
                    by RT-11 V3 and V4.  This can be done to V2-format
                    disks to avoid the  warning  message  that  DSKLIB
                    would otherwise display whenever the volume id was
                    changed.

               /HELP
                    Lists switches allowed.


          DSKLIB Commands                                    PAGE 3-12



          3.16  Width of Terminal


                    :<W>idth of terminal (in columns) #<digit>

               Changes the default number of  columns  for  file  name
          printing.   This  number  is only relevant for the terminal.
          The default for the printer may only be set at DSKLIB gener-
          ation  time.   Either default may be overridden for the Find
          command through a switch.













                                   CHAPTER 4

                                DSKLIB Messages          




               The messages displayed by DSKLIB in standard RT-11 for-
          mat  indicate  various  operational problems.  Generally the
          cause  is  clear  and  the  solution   is   straightforward.
          Sometimes, however, the problem will not be obvious.

               Many of these messages can be caused by hardware errors
          or  RT-11  bugs.  If these are suspected, the standard tests
          should be  run,  including  rebooting  the  system,  running
          hardware diagnostics, etc.

               If the cause of the problem cannot be  readily  traced,
          and programs other than DSKLIB are not failing, there may be
          reason to suspect a DSKLIB bug.  In this case, a description
          of  the  problem should be sent to Berez Associates, 64 Jac-
          queline  Road,  Waltham,  MA  02154.   A  printed  copy   of
          DLBOPT.MAC  as  modified should be included.  The version of
          DSKLIB in use should be specified, which can be obtained  by
          running  DSKLIB  and typing a carriage return to its command
          prompt.   It  is  desirable,  particularly  if  the  bug  is
          catalog-related,  to  include  a  machine-readable  copy  of
          DSKLIB and the catalog in use, preferably on a floppy disk.



          4.1  Informational Messages


               These messages do not require any particular action  by
          the user, but are informative only.



          4.1.1  Message Descriptions



          ?DSKLIB-I-Cannot attach console terminal
               Although an RT-11 monitor with  multi-terminal  support
               is being used, DSKLIB could not attach the console ter-


          DSKLIB Messages                                     PAGE 4-2



               minal to get its characteristics.   It  is  in  use  by
               another job.  DSKLIB will use its standard terminal de-
               faults.

          ?DSKLIB-I-Insufficient memory for all file entries
               There was not enough memory to hold all  entries  found
               by  the  Find  command.  (Each entry requires 6 words.)
               All entries found so far will be  sorted  and  printed,
               and  then  the search will continue.  See Section 4.3.2
               for further details.

          ?DSKLIB-I-No disk mounted
               The Update command accessed a drive that  had  no  disk
               mounted.  For Update All, the drive will be skipped and
               the Updates will continue.

          ?DSKLIB-I-Skipping bad chain
               This message from the Move command indicates  that  bad
               data  have  been  found  in the catalog for the current
               disk.  Although this disk cannot be moved, a  Move  All
               will  continue with subsequent disks.  For this reason,
               Move All is useful for recovering as  much  information
               as possible from a damaged catalog.



          4.2  Warning Messages


               These messages warn of some adverse condition that  has
          not  yet  caused a problem but may later if the condition is
          not corrected.



          4.2.1  Message Descriptions


          ?DSKLIB-W-Disk not RT11A initialized
               This message from the Volume id  change  command  warns
               that  the  target  disk has not been initialized in the
               format used by RT-11 V3 and V4.  If the command is  al-
               lowed  to  continue,  important information may be des-
               troyed.  Unless the disk has  been  initialized  by  an
               RT-11  V2  monitor,  which makes it downward compatible
               with the new format, the command should be  aborted  by
               typing  ^C.   Normally  a V2-format disk should be com-
               pletely upgraded to the new  format  using  the  /RT11A
               switch.

          ?DSKLIB-W-No date set
               The system date has not been set.  This date is used by
               Update  and by the date switches of Find.  Particularly


          DSKLIB Messages                                     PAGE 4-3



               if an Update will be done, Quit should be used to  exit
               to  KMON, the date should be set with the DATE command,
               and DSKLIB may be REENTERed.



          4.3  Error Messages


               These messages describe fatal  errors.   Generally  the
          particular  command in use is aborted and control returns to
          DSKLIB command level.



          4.3.1  Read/Write Failures


               A number of errors are caused by read or write failures
          from  or to a disk.  Such an error might be an indication of
          a hardware problem or an RT-11 software problem.   It  might
          also be simply that the disk is not properly mounted.

               A read failure might be caused by a bad  block  on  the
          disk.  A badly formatted disk could cause either a read or a
          write failure.   A  write  failure  could  be  caused  by  a
          write-protected disk or drive.

               If a DSKLIB bug is suspected, it should be reported  to
          Berez Associates (see above).



          4.3.2  Insufficient Memory


               A number of messages  indicate  the  unavailability  of
          sufficient  main memory (or "core") to complete the command.
          The available memory depends upon the physical  memory  con-
          figured in the hardware and the amount used by the software.

               To free enough memory for a command, examine  the  cur-
          rent  software configuration.  Significant amounts of memory
          are used by setting the USR NOSWAP, by having a  second  job
          in  the  FB  monitor, by using the FB monitor instead of SJ,
          and by LOADing device handlers.

               In DSKLIB, setting DPBLKS to 4, compared to 1, will use
          3  more  blocks of memory (and 3 more blocks in each catalog
          file).  Accessing devices  with  non-resident  handlers  re-
          quires DSKLIB to load the handlers into dynamically acquired
          memory.


          DSKLIB Messages                                     PAGE 4-4



          4.3.3  Message Descriptions


          ?DSKLIB-F-Archive handler not available
               The Update Rchives command cannot be  executed  because
               either  the  system does not include an archive handler
               (AR:) or the handler has not been initialized.

          ?DSKLIB-F-Bad catalog
               The file Opened is not recognized as a DSKLIB  catalog.
               Possibly  it  is  a  catalog created by an incompatible
               version of DSKLIB.

          ?DSKLIB-F-Bad date
               An improperly formatted date argument was  given  to  a
               switch that required a date.

          ?DSKLIB-F-Bad device name
               The specified physical or logical device  name  is  not
               recognized  by  RT-11.   This  may also come from a bad
               specification for one of the default file names.

          ?DSKLIB-F-Bad disk chain
               Bad data have been found in the catalog for the current
               disk.   This indicates that some damage has occurred to
               the catalog file, which should normally  never  happen.
               To  recover  as  much  data  as possible, a new catalog
               should be Created and a Move All from the  old  catalog
               should be done.  If this problem then recurs and cannot
               be traced to hardware or system software failure, a bug
               report should be sent to Berez Associates (see above).

          ?DSKLIB-F-Bad disk number
               An Update could not be done because  the  mounted  disk
               contained  a  bad disk number.  After ensuring that the
               correct disk is mounted, Volume ID Change can  be  used
               to set the number.

          ?DSKLIB-F-Bad file name
               An improperly formatted file name was either  typed  or
               found  on  a disk by Update.  In the case of the Update
               command, after ensuring that the correct disk is mount-
               ed,  Volume  ID  Change  can  be used to set the volume
               name.

          ?DSKLIB-F-Bad number
               An improperly formatted number was typed.

          ?DSKLIB-F-Bad number of columns
               Entries can be printed in one to nine  columns,  inclu-
               sive.  Any other number specified is illegal.


          DSKLIB Messages                                     PAGE 4-5



          ?DSKLIB-F-Catalog full
               There is not enough space left in the catalog  to  per-
               form the current operation.  The catalog may be expand-
               ed as described in Section 2.2.

          ?DSKLIB-F-Catalog not found
               The specified catalog file was not found.  This message
               can either come from the Open command or from the auto-
               matic Open when DSKLIB is started.

          ?DSKLIB-F-Catalog not open
               After  certain  errors,  the  primary  catalog  may  be
               closed.   This  message  for  the secondary catalog may
               also  indicate  that  a  secondary  catalog  was  never
               opened.  The appropriate catalog should be Opened.

          ?DSKLIB-F-Catalog write failure
               An error occurred while trying to write data  into  the
               catalog file.  See Section 4.3.1 for further details.

          ?DSKLIB-F-Device handler not found
               This indicates an RT-11 system failure.   A  good  file
               name  was  specified,  but  RT-11  could  not  load the
               handler.

          ?DSKLIB-F-Disk directory read failure
               The Update command could not read the directory of  the
               disk  on  the  specified  drive.  See Section 4.3.1 for
               further details.

          ?DSKLIB-F-Disk number too high
               The specified disk number is higher  than  the  highest
               disk  number  allowed  for this version of DSKLIB.  See
               the DPBLKS option in Section 1.4.1.1.

          ?DSKLIB-F-Disk read failure
               Some unspecified read failure  occurred.   See  Section
               4.3.1 for further details.

          ?DSKLIB-F-Disk write failure
               Some unspecified write failure occurred.   See  Section
               4.3.1 for further details.

          ?DSKLIB-F-Drive access failure
               The Update command could not  open  a  channel  to  the
               specified  drive.   This might indicate that the drive,
               as defined in DEVTAB at DSKLIB  generation  time,  does
               not  exist.   It  also  might mean that the handler for
               this device is not installed in the current monitor.

          ?DSKLIB-F-File name missing
               A device name was given without a file name for  a  di-
               rectory structured device.


          DSKLIB Messages                                     PAGE 4-6



          ?DSKLIB-F-Illegal switch
               A switch was used that is not defined for this command.
               The /HELP switch lists all legal switches, if any.

          ?DSKLIB-F-Insufficient free core for move
               The Move command requires enough main  memory  to  hold
               all  entries for each disk that it moves (approximately
               48 entries per block of memory).  See Section 4.3.2 for
               further details.

          ?DSKLIB-F-Missing date argument
               No date was supplied to a switch that required one.  To
               default the date to the current date, follow the switch
               by a single space.

          ?DSKLIB-F-Missing numeric argument
               No number was supplied to a switch that  required  one.
               To  default  the number to zero, follow the switch by a
               single space.

          ?DSKLIB-F-Nonexistent disk
               The specified disk  is  not  defined  in  the  catalog.
               Either it was never cataloged or it has been Expunged.

          ?DSKLIB-F-Not enough memory available
               When DSKLIB is started, it tries to obtain  memory  for
               buffer  space  (DPBLKS+4 blocks).  If the memory is not
               available, DSKLIB cannot be executed and will return to
               KMON.  See Section 4.3.2 for further details.

          ?DSKLIB-F-Not enough memory for device handler
               Not enough memory  is  available  to  load  a  required
               non-resident  device  handler.   See  Section 4.3.2 for
               further details.

          ?DSKLIB-F-Not enough room for file
               A catalog file could not be Created with the  specified
               size  due to lack of space on the disk.  In may only be
               necessary to squeeze the disk to get enough  contiguous
               space for the file.

          ?DSKLIB-F-Number too high
               A disk number larger than 999 was given to  the  Volume
               ID Change command.  There is only room for three digits
               in the volume id format for DSKLIB.

          ?DSKLIB-F-Printer file open failure
               The printer file could not be opened.  Check  the  name
               specified  at  generation time or with Printer File and
               ensure that this device is available for use.

          ?DSKLIB-F-Printer file write failure
               Output to the printer file failed.


          DSKLIB Messages                                     PAGE 4-7



          ?DSKLIB-F-Size too large for bit map
               For the Create command,  the  file  size  specified  is
               larger  than  the  maximum number of blocks that can be
               utilized by DSKLIB (currently, 512 blocks).

          ?DSKLIB-F-Size too small
               For the Create command,  the  file  size  specified  is
               smaller  than  the  minimum required, which is DPBLKS+2
               blocks.

          ?DSKLIB-F-Undefined drive number
               No device name was given in DEVTAB at  generation  time
               for this drive number.