PROGRAM NAME
	prom.sav	Special prom burning program

SYNOPSIS
	run prom
	*device[/opt1[/opt2...]]=device[/opt1[/opt2...]]

FUNCTION
	The user enters his command after the * prompt.
	The prom program transfers information between
	any two of the following devices.
	The device on the left is the destination.
	The device on the right is the source.
	
DEVICES
	There are three choices for devices
	(1)	filename	/* DDD:NNNNNN.EEE normal file name*/
	(2)	P		/* Prom burner */
	(3)	A		/* Internal memory*/

	Using these devices most transfers between the prom burner
	and files may be made.

OPTIONS
	File Options
	------------
	START:nn      starting byte in file
	COUNT:nn      number of bytes to read
	COLUMNS:nn    number of columns
	BASE:nn       base of data
	AND           not working yet
	TITLES:nn     base of titles
	               0 = no titles
	ECHO          shows memory contents
	HIGH          not working yet
	LOW           not working yet
	WORDS         not working yet
	NAME          not working yet

	Prom Options
	------------
	P:nn          number of bytes
	START:nn      starting byte
	ECHO          echo prom replies
	TYPE:nn       type of prom
	               0 2716
	               1 2516
	               2 2758
	               3 2508
	               4 2532
	               5 2732
	               6 MCM68764

	Memory Options
	--------------
	A:nn          number of bytes
	START:nn      starting byte
	ECHO          shows memory contents

FILE FORMAT
	The file format is as following:
	title1	value1,1 value1,2 ......value1,N<CR><LF>
	title2	value2,1 value2,2 ......value2,N<CR><LF>
	title3	......				<CR><LF>
	.......
	titleM	valueN,1 valueM,2 ......valueM,N<CR><LF>

	N is the number of columns in the file.
	The base of titles and values may be specified.
	The number of columns may be specified.
	The titles may be omitted.

HELP
	Typing any portion of the word HELP after the prompt
	will provide information on options.

SERIAL PORT
	Connect prom burner to port 1.(console is port 3)
	the serial port can work at 1200 or 300 baud.
	The special serial port handler LQ: must be
	installed on that port.

EXAMPLE
	r prom
	*p=dm5:file.rom/col:1/base:2