MTED

     Author:  Steve C. Cribbs				June 1984
              Atomic Energy of Canada Limited
              Pinawa, Manitoba
              Canada  R0E 1L0

     MTED was written to allow dynamic redefinition of use for the RT-11
multi-terminal ports.  Although RT-11 permits a program to blindly use
a device handler, interrupt service routine or directly address the
vectors and registers that control a multi-terminal serviced port, it is
a foolish practice that destroys the monitors integrity.  Once the port's
CSR and vectors have been modified, the monitor has lost control of the
device.  Further use of the port as a terminal may hang or corrupt the
system.  Of course, proper service is restored when the computer is
re-booted.

     The Multi-Terminal Enable/Disable utility (MTED) can be used to
inform the monitor that the port is unavailable, turn off input interrupts,
and to also preserve the necessary vector linkage to the monitor's 
terminal service code.  When terminal access through the port is again
desired, MTED can restore proper linkage.  Like the RESORC utility, MTED
can be used to indicate terminal availability, but in addition MTED also
returns information through the systems User Error Byte.  This last
feature is very useful to tasks executed through command files.

     MTED provides an asterisk ("*") prompt as do DIGITAL's utilities
and is terminated by the CONTROL_C sequence.  It responds to four
commands:  DISABLE, ENABLE, LIST, and HELP.  Single character command
abbreviations are recognized.  The first three commands accept a list
of numeric arguments indicating the multi-terminal port numbers to be
acted upon.  Argument lists may be separated with either space or comma
characters.  The LIST command with no arguments displays a table of
CSR and vector addresses for all enabled ports.  Information saved
through the DISABLE command is written into "SY:MTED.SAV", thus this
program should be run from the system device.

     MTED reports errors for the following conditons:

     - specification of an illegal multi-terminal number;

     - attempts to disable:
               - an already disabled port;
               - a port in use by another job;
               - the job's own console;

     - attempts to enable an already enabled port.