Smart Mailer
                              User's Guide









                               March 1985








        OPERATING SYSTEM AND VERSION:  RSTS Version 7.2 or later
                                       Micro/RSTS 1.0 or later  
                                       VMS Version 3.5 or later 

        SOFTWARE VERSION:              Smart Mailer  Y1.1       















         digital equipment corporation . maynard, massachusetts





                                                First Printing, May 1983
                                                     Revised, March 1985


The information in this document is subject to change without notice and
should   not   be   construed  as  a  commitment  by  Digital  Equipment
Corporation.  Digital Equipment Corporation  assumes  no  responsibility
for any errors that may appear in this document.

The software described in this document is furnished under  license  and
may be used or copied only in accordance with the terms of such license.

No responsibility is assumed for the use or reliability of  software  on
equipment that is not supplied by Digital or its affiliated companies.


       Copyright (c) 1983, 1985 by Digital Equipment Corporation
                          All Rights Reserved.


                           Printed in U.S.A.






The following are trademarks of Digital Equipment Corporation:

     DEC                      DIBOL               RSX
     DECalc                   MASSBUS             UNIBUS
     DECmate                  PDP                 VAX
     DECsystem-10             P/OS                VMS
     DECSYSTEM-20             Professional        VT
     DECUS                    Rainbow             Work Processor
     DECwriter                RSTS                digital (logo)





                                    CONTENTS


                                                                    Page


CHAPTER 1       Introduction

        1.1     Overview of Smart Mailer Functionality . . . . . . . 1-1
        1.2     Overview of Smart Mailer Structure . . . . . . . . . 1-3
        1.2.1     File Structure . . . . . . . . . . . . . . . . . . 1-3
        1.2.2     Program Structure  . . . . . . . . . . . . . . . . 1-4
        1.3     Getting Help . . . . . . . . . . . . . . . . . . . . 1-5
        1.4     General Guidelines . . . . . . . . . . . . . . . . . 1-5
        1.4.1     Data Entry Conventions . . . . . . . . . . . . . . 1-5
        1.4.2     Choosing an Output Device  . . . . . . . . . . . . 1-7
        1.4.3     Structure of the Menus . . . . . . . . . . . . . . 1-9
        1.5     Getting Started  . . . . . . . . . . . . . . . . .  1-11
        1.5.1     Logging On/Off the Computer  . . . . . . . . . .  1-11
        1.5.2     Starting Smart Mailer  . . . . . . . . . . . . .  1-11
        1.5.3     Choosing a Mailing List  . . . . . . . . . . . .  1-13
        1.5.4     Main Menu  . . . . . . . . . . . . . . . . . . .  1-14
        1.5.5     Transferring to Another Mailing List . . . . . .  1-15


CHAPTER 2       Creating a New Mailing List

        2.1     Mailing List Parameters  . . . . . . . . . . . . . . 2-2
        2.2     Mailing List Categories  . . . . . . . . . . . . . . 2-6
        2.3     Walk Through . . . . . . . . . . . . . . . . . . . . 2-9


CHAPTER 3       Updating Mailing List Addresses

        3.1     Explanation of Address Fields  . . . . . . . . . . . 3-2
        3.2     Walk Through . . . . . . . . . . . . . . . . . . . . 3-6
        3.2.1     Adding an Address  . . . . . . . . . . . . . . . . 3-7
        3.2.2     Changing an Address  . . . . . . . . . . . . . .  3-12
        3.2.3     Displaying an Address  . . . . . . . . . . . . .  3-18
        3.2.4     Removing an Address  . . . . . . . . . . . . . .  3-19


CHAPTER 4       Sublist Definition

        4.1     Sublist Definition Format  . . . . . . . . . . . . . 4-2
        4.2     Walk Through . . . . . . . . . . . . . . . . . . . . 4-5
        4.2.1     Creating a Sublist Definition  . . . . . . . . . . 4-6
        4.2.2     Updating a Sublist Definition  . . . . . . . . .  4-11
        4.2.3     Printing a Sublist Definition  . . . . . . . . .  4-14
        4.2.4     Displaying a Sublist Definition  . . . . . . . .  4-15
        4.2.5     Removing a Sublist Definition  . . . . . . . . .  4-16
        4.2.6     Show All Sublist Definitions . . . . . . . . . .  4-18

                                  iii

                                CONTENTS


CHAPTER 5       Displaying a Mailing List or Sublist

        5.1     Walk Through . . . . . . . . . . . . . . . . . . . . 5-2


CHAPTER 6       Printing a Mailing List or Sublist

        6.1     Sorting a Mailing List . . . . . . . . . . . . . . . 6-2
        6.2     Walk Through . . . . . . . . . . . . . . . . . . . . 6-3


CHAPTER 7       Creating a List Document File

        7.1     Walk Through . . . . . . . . . . . . . . . . . . . . 7-2


CHAPTER 8       Category Definitions

        8.1     Walk Through . . . . . . . . . . . . . . . . . . . . 8-2
        8.1.1     Updating a Category Definition . . . . . . . . . . 8-4
        8.1.2     Printing a Category Definition . . . . . . . . . . 8-7
        8.1.3     Displaying a Category Definition . . . . . . . . . 8-9


CHAPTER 9       Report Mailing (Sub)list Statistics

        9.1     Walk Through . . . . . . . . . . . . . . . . . . . . 9-1


CHAPTER 10      Advanced Topics

        10.1    PRESORTing Addresses . . . . . . . . . . . . . . .  10-1
        10.1.1    PRESORT Rules  . . . . . . . . . . . . . . . . .  10-1
        10.1.2    PRESORT Statistics . . . . . . . . . . . . . . .  10-3
        10.1.3    PRESORT References . . . . . . . . . . . . . . .  10-7
        10.1.4    Use of Non-First Class Mail PRESORT  . . . . . .  10-7
        10.2    Sublist Definitions  . . . . . . . . . . . . . . .  10-8
        10.3    Printing Labels  . . . . . . . . . . . . . . . . . 10-11
        10.3.1    Label Parameters . . . . . . . . . . . . . . . . 10-13
        10.3.2    Lining Up Labels . . . . . . . . . . . . . . . . 10-17
        10.4    Creative Uses of the Smart Mailer System . . . . . 10-18
        10.4.1    Types of Information . . . . . . . . . . . . . . 10-18
        10.4.2    Types of Forms . . . . . . . . . . . . . . . . . 10-19


GLOSSARY


INDEX





                                   iv

                                CONTENTS


FIGURES

        1-1     Output Device Menu . . . . . . . . . . . . . . . . . 1-8
        1-2     Screen Dialog Flow . . . . . . . . . . . . . . . .  1-10
        1-3     Smart Mailer Introduction Screen . . . . . . . . .  1-12
        1-4     Enter Mailing List Name Screen . . . . . . . . . .  1-13
        1-5     Main Menu  . . . . . . . . . . . . . . . . . . . .  1-14
        2-1     Enter Mailing List Name Screen . . . . . . . . . . . 2-9
        2-2     Confirming Mailing List Name . . . . . . . . . . .  2-10
        2-3     Mailing List Parameter Screen  . . . . . . . . . .  2-10
        2-4     Category Initialization Screen . . . . . . . . . .  2-12
        3-1     Update Menu  . . . . . . . . . . . . . . . . . . . . 3-6
        3-2     Add an Address Screen  . . . . . . . . . . . . . . . 3-7
        3-3     Specify an Address ID Screen . . . . . . . . . . .  3-12
        3-4     Change an Address Screen . . . . . . . . . . . . .  3-14
        3-5     Display an Address Screen  . . . . . . . . . . . .  3-18
        3-6     Remove an Address Screen . . . . . . . . . . . . .  3-19
        4-1     Sublist Definition Menu  . . . . . . . . . . . . . . 4-5
        4-2     Naming Your Sublist Screen . . . . . . . . . . . . . 4-6
        4-3     Sublist Definition Screen  . . . . . . . . . . . . . 4-7
        4-4     Example - Sublist Definition Update Screen . . . .  4-11
        4-5     Example - Sublist Definition Display Screen  . . .  4-15
        4-6     Example - Sublist Definition Remove Screen . . . .  4-16
        4-7     Show All Sublist Definitions Screen  . . . . . . .  4-18
        5-1     List Selection Menu  . . . . . . . . . . . . . . . . 5-2
        5-2     Display Sort Menu  . . . . . . . . . . . . . . . . . 5-4
        5-3     Example - Display of Addresses Sorted by Primary ID  5-5
        6-1     List Selection Menu  . . . . . . . . . . . . . . . . 6-3
        6-2     Print Sort Menu  . . . . . . . . . . . . . . . . . . 6-5
        6-3     Output Format Menu . . . . . . . . . . . . . . . . . 6-7
        6-4     Sample - Short Listing . . . . . . . . . . . . . . . 6-8
        6-5     Sample - Full Listing  . . . . . . . . . . . . . . . 6-9
        6-6     Sample - Label Printing  . . . . . . . . . . . . .  6-10
        6-7     Output Device Menu . . . . . . . . . . . . . . . .  6-10
        6-8     PRESORT Menu . . . . . . . . . . . . . . . . . . .  6-12
        6-9     Label Menu . . . . . . . . . . . . . . . . . . . .  6-13
        7-1     List Selection Menu  . . . . . . . . . . . . . . . . 7-2
        7-2     Sort Menu  . . . . . . . . . . . . . . . . . . . . . 7-4
        7-3     Generating a List Document File Screen . . . . . . . 7-5
        8-1     Category Definition Menu . . . . . . . . . . . . . . 8-2
        8-2     Category Update Screen . . . . . . . . . . . . . . . 8-4
        8-3     Output Device Menu . . . . . . . . . . . . . . . . . 8-7
        8-4     Example - Category Definition Display Screen . . . . 8-9
        9-1     List Selection Menu  . . . . . . . . . . . . . . . . 9-1
        9-2     Report Menu  . . . . . . . . . . . . . . . . . . . . 9-3
        9-3     Example - Total Addresses Report Screen  . . . . . . 9-4
        9-4     Output Device Menu . . . . . . . . . . . . . . . . . 9-5
        10-1    Example - PRESORT Menu . . . . . . . . . . . . . .  10-4
        10-2    Sample - PRESORTed Labels  . . . . . . . . . . . .  10-6
        10-3    Label Menu . . . . . . . . . . . . . . . . . . . . 10-13
        10-4    Example - Label Parameters . . . . . . . . . . . . 10-15



                                   v

                                CONTENTS


TABLES

        2-1     Parameter Definitions  . . . . . . . . . . . . . . . 2-2
        2-2     Category Initialization Type Codes . . . . . . . . . 2-7
        3-1     State Abbreviations  . . . . . . . . . . . . . . . . 3-5
        4-1     List of Comparisons  . . . . . . . . . . . . . . . . 4-3
        6-1     Sorting Order  . . . . . . . . . . . . . . . . . . . 6-2
        10-1    Label Format . . . . . . . . . . . . . . . . . . . 10-12
        10-2    Label Parameters for Typical Label Sizes . . . . . 10-16















































                                   vi

                                                                        


PREFACEPREFACE


Intended AudienceIntended Audience

    _____ ______ ______ _____The Smart Mailer User's Guide is written for individuals  who  will  use
the system for their everyday use.


Structure of this DocumentStructure of this Document

Chapter 1 gives a complete overview of Smart Mailer functionality,  file
structure,  program  structure,  data entry conventions, output devices,
structure of menus, logging on to a  computer,  starting  Smart  Mailer,
choosing  a mailing list, Main Menu, and transferring to another mailing
list.

Chapter 2 explains how to  create  a  new  mailing  list  and  describes
mailing  list  parameters and mailing list categories.  A "Walk Through"
is included which describes each screen that is displayed when  creating
a    new   mailing   list:    Parameters   Definitions,   and   Category
Initialization.

Chapter 3 describes updating an existing mailing list.   An  explanation
of  address fields and a table of valid state abbreviations is included.
A "Walk Through" is included which describes options that are  available
from  the  Update  Menu:   Adding,  Changing/Displaying, and Removing an
Address.

Chapter 4 explains what a sublist definition is and shows the format  of
a  sublist  definition.   A  "Walk  Through" is included which describes
options that are available from the Sublist Definition Menu:  Update (or
Create), Print, Display, Remove, and Show All Sublist Definitions.

Chapter 5 describes  displaying  a  mailing  list  or  sublist  and  the
difference  between displaying and printing addresses.  A "Walk Through"
is included which explains what options  are  available  from  the  List
Selection Menu:  All Addresses in a Mailing List, Sublist, and Temporary
Sublist.

Chapter 6 describes how to print addresses on a  printing  device  using
paper  or  labels.   This  chapter is pretty lengthy because of the many
options available with Smart Mailer.

Chapter 7 explains creating a Word Processor List Document  File,  which
can  be  used  as a List Document with the List Processing function on a
word processing system.

Chapter 8 explains the options available from  the  Category  Definition
Menu:  Update, Print, and Display the Category Definitions.






                                  vii

 


Chapter 9 describes the new Report option which allows  users  to  print
statistics on mailing lists and sublists.

Chapter 10 covers some  advanced  material.   The  chapter  covers  more
Postal   PRESORTing   procedures,  using  complex  sublist  definitions,
changing label parameters, and suggestions for creative  uses  of  Smart
Mailer.


Conventions Used in this DocumentConventions Used in this Document

   Convention                           Meaning

UPPERCASE WORDS         Uppercase  words  and letters  used in  examples
AND LETTERS             indicate that you should type the word or letter
                        exactly as shown.

  RUN                                                               bold$ RUN                   All user input in examples is  printed  as  bold
                        text.

$_File:                 All output that the system prints or displays is
                        printed as regular text.

<RETURN> or <SP>        A symbol indicates that you press a key  on  the
                        terminal keyboard.

                        <RETURN> is the key labeled RETURN.
                        <SP> is the space bar.

<CTRL/x>                <CTRL/x> indicates that you must hold  down  the
                        key  labeled  CTRL  while you press another key.
                        For example, <CTRL/C>,  <CTRL/Y>,  or  <CTRL/Z>.
                        In  examples, this control key sequence is shown
                        as ^C, ^Y, or ^Z, because that is how the system
                        echoes control key sequences.

Unless otherwise noted, all numeric values are  represented  in  decimal
notation.

Unless otherwise specified, you terminate your answers by  pressing  the
<RETURN>  key.   This  will  signal  the  computer  that  your answer is
completed.


Associated DocumentsAssociated Documents

For information on installing Smart Mailer and using  the  Smart  Mailer
                        ____ _____ ______ ______ _________ _____     ___Utility,  refer  to the RSTS Smart Mailer System Manager's Guide, or VAX
_____ ______ ______ _________ _____Smart Mailer System Manager's Guide.  For special notes on  the  current
                                        ____ _____ ______ _______ _____version  of  Smart Mailer, refer to the RSTS Smart Mailer Release Notes,
   ___ _____ ______ _______ _____or VAX Smart Mailer Release Notes.  For information on  your  particular
operating system, refer to your operating system documentation.


                                  viii






                               Chapter 1
                              Introduction



Welcome to Smart Mailer!Welcome to Smart Mailer!

1.1  Overview of Smart Mailer Functionality

Smart Mailer is a software application tool that enables you to maintain
mailing lists and generate address labels.  Its features include:


User InterfaceUser Interface

There is an easy menu-driven user interaction.

There is extensive on-line help text, where the help is  geared  to  the
particular situation.

Smart Mailer has easy movement between menus and functions.

Most questions have default (suggested) answers.

The system can be customized to meet your requirements.


Mailing List MaintenanceMailing List Maintenance

Smart Mailer has the ability to maintain one or more independent mailing
lists that can be accessed by everyone or restricted to personal use.

Mailing List entries can  include  name,  3  address  lines,  city/town,
state/country, zip code, a counter, a comment, two separate identifiers,
and up to 6 separate categories of related information.

IntroductionIntroduction                                                    Page 1-2


Address SelectionAddress Selection

Addresses may be extracted from a master list  which  meet  user-defined
requirements.

The list of requirements can be labeled and  stored  with  each  related
mailing list.

The addresses may be sorted by any of the address fields.

A special sorting may be requested  to  take  advantage  of  U.S. Postal
Presorting discount postal rates.


Major FunctionsMajor Functions

Update

        The mailing lists can  be  created  and  maintained  by  adding,
        removing and changing individual addresses.

Display

        The addresses, category definitions, and sublist definitions can
        all be displayed on the video screen.

Listings

        The addresses, category definitions, and sublist definitions can
        all be printed on any printing device.

Labels

        The addresses can be printed on a wide variety  of  label  sizes
        and types; multiple labels across a page; with test printing and
        special messages on each label as options.

List Processing interface

        Smart Mailer can generate a List  Document  file  for  use  with
        Digital word processors to produce personalized letters.

IntroductionIntroduction                                                    Page 1-3


1.2  Overview of Smart Mailer Structure

This section describes the structure of the Smart Mailer files.  It also
describes  the two programs that make up Smart Mailer - the Smart Mailer
program itself, and the Smart Mailer Utility.



1.2.1  File Structure

There are three different types  of  files  associated  with  the  Smart
Mailer system.  The first two are referred to as the Screen File and the
Parameter File.  The last, and most important is the Mailing List  File.
The  typical  user  will  only need to deal with the Mailing List Files.
The other two files are only of a concern to  the  System  Manager  when
installing or modifying the Smart Mailer system.

    System Screen FileThe System Screen File contains most of the information displayed to the
user  on  the terminal video screen, including the help messages.  There
is only one Screen File that is used by all Smart  Mailer  users.   This
file is created when the Smart Mailer system is installed, and then left
alone.

    System Parameter FileThe System Parameter File contains information that is  unique  to  your
computer  system.  For example, the number and type of printers that are
connected to your computer system are listed  in  the  System  Parameter
File.  These printers are used by Smart Mailer users to print labels and
listings.  In this way, Smart Mailer uses the System Parameter  File  to
satisfy  your  particular  requirements.  Like the Screen File, there is
only one System Parameter File which is used by all Smart Mailer  users.
It  is  created  when Smart Mailer is installed.  Whenever the situation
changes (such as a new printer being  attached),  the  System  Parameter
File may be changed to reflect the new information.

  Mailing List FileA Mailing List File contains names, addresses and  related  information.
There  may  be  one Mailing List File, or there may be many Mailing List
Files.  For example, every user can have their own separate Mailing List
File,  or as another example, there can be only two files - one file for
customers and one file for suppliers.  Depending  on  how  each  Mailing
List  File  is set up, users can be allowed or restricted from accessing
each others files.  For example, the System Manager can set up a  common
Mailing List File so that it can be accessed by anyone.

There are three kinds of information stored in each Mailing  List  File.
The  first  type  of  information is the Mailing List Parameters.  These
differ from the System Parameters  in  that  they  relate  only  to  the
specific  Mailing  List where they are stored.  For example, one Mailing
List Parameter specifies how each address is to  be  identified.   Users
can identify each address with a user-specified identification tag, such
as social security number, or Smart Mailer itself can  assign  a  unique
number  to the address.  These parameters are defined only once for each
Mailing List File, when the Mailing List File is created.  These Mailing
List Parameters are described in detail in Chapter 2.

IntroductionIntroduction                                                    Page 1-4


The second type of information stored in a  Mailing  List  File  is  the
definition  of  any  associated  sublists.   Each  Mailing  List File is
considered a 'master' list from which the user can extract or select out
certain  addresses  to  form a 'sublist'.  These sublists are not stored
separately; they are always extracted from the entire Mailing List  when
they  are  needed.   The information on how the addresses are chosen for
each sublist is stored within each Mailing List File.   For  example,  a
sublist  might be defined as 'all students majoring in Chemistry'.  This
definition can be stored with a college's  Mailing  List  File  and  the
addresses  matching  the definition extracted when needed.  There may be
no sublist definitions for any given Mailing List File, or there may  be
many sublist definitions.  The topic of sublist definitions is described
in Chapter 4 - Sublist Definition.

The third and most important type of information  stored  in  a  Mailing
List  File  is  the  names, addresses and related information.  For each
name, the Mailing List stores the address  information  (address  lines,
city,  state,  zip),  category  information,  a counter and any remarks.
Category information is related information such  as  class,  major  and
financial  aid  status (for students), or last purchase date, and credit
limit (for customers).  The labels of these categories (such  as  major)
are stored with the Mailing List Parameters.  The particular information
for each name (such as Chemistry) is stored with the  name  and  address
information.



1.2.2  Program Structure

There are two programs associated with the Smart Mailer system.  One  is
Smart  Mailer  itself.   The  other  is  the  Smart Mailer Utility.  The
typical user will only use Smart Mailer.  The Smart Mailer Utility  will
normally be used by the System Manager.

The Smart Mailer program forms the heart  of  the  system.   It  is  the
software  program  which  maintains  the names and addresses, and prints
them out on labels.  The rest of this User's Guide describes the use  of
Smart Mailer.

    Smart Mailer UtilityThe Smart Mailer Utility is used by the System  Manager  to  modify  the
System Parameter File, to create Mailing List Files, and to compress and
extend Mailing List Files.  The System  Manager's  Guide  describes  the
Smart Mailer Utility in detail.

IntroductionIntroduction                                                    Page 1-5


1.3  Getting Help

                                                          ?Whenever you want help in using Smart Mailer, simply type ?   and  press
<RETURN><RETURN>.   Smart  Mailer  will  then  display help information for that
particular part of Smart Mailer.  Depending on the point  at  which  you
     ?type ?, Smart Mailer either shows you a single help message line, or one
                                                                       ?or more full screens of help information.  For example, if  you  type  ?
to  the  first  field  name when adding an address to your Mailing List,
Smart Mailer shows you information on what each address field means.  If
           ?you  type  ?   at any other field name in that same screen, Smart Mailer
shows you a single line message describing that particular field name.

In general, the help text gives you information on what  the  prompt  or
question  means,  what answers are acceptable (e.g., only S, F or L), or
what range of answers are acceptable (e.g.,  between  1  and  10  labels
across a page), and/or what the implications of each answer are.

1.4  General Guidelines

This section gives information on  general  guidelines  to  follow  when
using  the Smart Mailer system.  The first part describes how to respond
to Smart Mailer prompts and how to move between menus.   The  next  part
describes  how  to  choose an output device for listings or labels.  The
last part describes the organization and structure of the  Smart  Mailer
menus.   These  menus provide the user with options from which to choose
Smart Mailer functions.



1.4.1  Data Entry Conventions

The Smart Mailer system  interacts  with  you  by  a  set  of  menu  and
'fill-in-the-blank'  screens.   In  the  case of the menu screens, Smart
Mailer presents you with a list of choices.  Smart Mailer then positions
the  cursor to the right of the prompt "Select option:".  You may select
one of the choices by typing the letter  corresponding  to  the  desired
function,  and  then press <RETURN>.  In most cases, a default answer is
already provided and displayed at the  cursor  position.   This  default
answer  represents  the  most  common choice and is intended to make the
system easier to use.   To  accept  the  default  answer,  simply  press
<RETURN>.

IntroductionIntroduction                                                    Page 1-6


In the case where you are  providing  a  set  of  information  to  Smart
Mailer,  the  system  displays  a 'fill-in-the-blank' screen.  This is a
display where there are a set of field names followed by spaces for  the
answers.  For example, when prompting you for address information, Smart
Mailer will show you a screen with the field names such  as  "Name"  and
"Address  line", followed by spaces for your answers.  Smart Mailer will
position the cursor to the field name that is to be filled in, and  show
you  how  long  the  answer  can be (how many characters) by a series of
underscores.  As with any entry,  after  typing  in  the  answer,  press
<RETURN>.   If  there  is no information (e.g., no zip code), just press
<RETURN> to go to the next field name.

Whenever appropriate, Smart Mailer  will  offer  a  default  (suggested)
answer.  To accept the default answer, simply press <RETURN>.  To change
a default answer, simply type over it with the correct  information  and
press  <RETURN>.   To  eliminate  a default answer (change it to blank),
simply press the space bar once, then press <RETURN>.  In  other  words,
typing  any  character  in  place of a default answer will overwrite the
entire default answer.  The one exception to this general rule is a date
answer.  The default for a date field is today's date.  If you type just
the day (e.g., 15), then Smart Mailer will automatically fill in today's
month and year.  Or if you type in the day and the month (e.g., 15-OCT),
then Smart Mailer will fill in today's year.  This is intended to reduce
the amount of typing and make the system easier to use.

Smart Mailer is designed with certain conventions.   One  convention  is
that  to continue on within the system, you usually press <RETURN>.  For
example, when shown a list of label  parameters  (label  height,  width,
etc.), you have the option of changing any of them.  If they do not need
to be changed, or when you are done,  you  simply  press  <RETURN>,  and
Smart  Mailer continues on to the next step.  Another convention is that
       ENDtyping END usually moves you back to the previous screen,  or  completes
                                           ENDwhat  you  are doing.  For example, typing END at the Main Menu puts you
out of Smart Mailer.  (Note that pressing <CTRL/Z>, that is, typing  'Z'
                                                                   ENDwhile  holding  down  the  key labeled CTRL, is the same as typing END).
Another convention is the use of <CTRL/C>.  If you press <CTRL/C>, Smart
Mailer aborts whatever function it is currently in.  For example, if you
are at a menu, Smart Mailer terminates the session.  This  <CTRL/C>  key
should  ONLY  be used as a PANIC BUTTON and not on a regular basis.  You
may lose whatever you were doing.  For example, if  you  are  adding  an
address, that address may be lost.

IntroductionIntroduction                                                    Page 1-7


1.4.2  Choosing an Output Device

Whenever you request output from Smart Mailer, it offers you a choice of
where to send the output, that is, a choice of which device to print the
information on.  Smart Mailer presents you with your choices by using  a
menu.  The first choice in the menu is always the option of having Smart
Mailer send the information to a file.  If you choose this option, Smart
Mailer  then  asks  you  to  specify  the  name of the file.  Unless you
specify otherwise, the file will be put in your account.   If  you  send
information  to a disk file, you can later use operating system commands
to print the information wherever you want (e.g., for the RSTS operating
               QUE LP0:=filenamesystem  type,  QUE LP0:=filename,  or  for  the VAX/VMS operating system
      PRINT filenametype, PRINT filename).  You should delete the file when you are finished
                                                     PIP filename/DEwith  it  (e.g., for the RSTS operating system type, PIP filename/DE, or
                                       DEL filenamefor the VAX/VMS operating system type, DEL filename).

The other options available  from  this  printer  device  menu  will  be
different  for each installation.  For example, a large company may have
5 different printing devices  (e.g.,  two  regular  printers,  a  Letter
Quality  Printer, and two hardcopy terminals), but a small company might
have only one printer.  The System Manager responsible for Smart  Mailer
will  have  set  up  this  information  during installation of the Smart
Mailer system (and may update it periodically), so the  choices  offered
to you reflect the printers that are at your site.

In general, there are two  different  ways  of  sending  information  to
different  printing  devices.   You can either send the information to a
printer directly, or you can  send  the  information  to  the  operating
system,  which  will  send  it to the printer when the printer is ready.
Following the instructions of the System Manager, Smart Mailer may  send
the  information  directly  to  the  printer.  If this is the case, then
depending on the amount of information and the speed of the printer, the
printing  may  take  a long time to complete.  You see the results being
printed out immediately, but you  can  not  do  anything  else  at  your
terminal until Smart Mailer is finished producing the printout.

The other case is where Smart Mailer lets the  operating  system  handle
the  printing (in the background).  If the System Manager has set up the
printer so that information can be queued, then Smart Mailer  creates  a
temporary  file,  puts the information in the file, then sends it to the
operating system with instructions to  print  it  when  the  printer  is
available,  and  to erase it when the printing is done.  This means that
it may take longer to get your printout if there are other files in  the
queue  to be printed before yours, but the printing does not tie up your
terminal.  (Also, printers that are set  up  for  a  queue  are  usually
faster printers than those that are not).  Once Smart Mailer has created
the temporary file with the information, then you  can  terminate  Smart
Mailer, or continue on with another Smart Mailer function.

IntroductionIntroduction                                                    Page 1-8


When you choose a printer, Smart Mailer tells you what type of  printing
will  be  done.   If it gives you a message that the information will be
'sent to' the device, then it will print it directly.  If it  says  that
the  information will be 'queued to' the device, then it will send it to
the operating system to be printed.  In both  cases,  there  will  be  a
message  shown  such  as, "generating labels...  please wait".  You must
wait until Smart Mailer indicates it  is  ready  for  more  instructions
before  going on to anything else.  DO NOT turn the terminal off, or try
to log off.

Figure 1-1 is an example of the Output Device Menu.

------------------------------------------------------------------------


                       Output Device Menu




                D  =   Disk file output:

                1  =   Main Printer







                END =  Return to the previous menu



                       Select option:

------------------------------------------------------------------------


Figure 1-1:  Output Device MenuFigure 1-1:  Output Device Menu


IntroductionIntroduction                                                    Page 1-9


1.4.3  Structure of the Menus

When you start the Smart Mailer  system,  it  displays  an  Introductory
Screen  that  introduces Smart Mailer and asks you if you want help.  If
you ask for help, then  Smart  Mailer  shows  you  one  or  more  screen
displays with help information.

The next screen asks you which Mailing List you want to work  with.   If
you  ask for a new Mailing List, Smart Mailer leads you through a set of
menu screens which ask questions relative to creating a new Mailing List
                                           ENDFile.   If you make a mistake, simply type END to go back to the Mailing
List name question.  If you ask for an existing Mailing List, then Smart
Mailer shows you the Main Menu.

Since the default file type of a Mailing List  File  is  .MLF,  you  can
refresh  your  memory  of  what  Mailing  List Files you already have by
listing all files with the .MLF file type.   This  can  easily  be  done
using  the  RSTS  or VAX/VMS operating system command 'DIR *.MLF' before
starting Smart Mailer.  This procedure assumes that you  have  used  the
convention  of  naming  your Mailing List files with a file type of .MLF
(this is recommended).

The Main Menu shows you all the major functions that  Smart  Mailer  can
perform.  When you choose a function, Smart Mailer will lead you through
the set of questions necessary to perform that function.  Then  it  will
generally  return  to  the  Main  Menu.   One  exception is when you are
adding, changing or removing an address.  In  that  case,  Smart  Mailer
assumes  that  you  want to continue that same operation and prompts you
for more.  In that way, you can add a series of addresses without having
to  choose  'Update  the  Mailing  List', then 'Add an Address' from the
menus for each address.

Figure 1-2 shows the organization of the menu screens.

IntroductionIntroduction                                                   Page 1-10



                                                        INTRODUCTION
                                                             |
                                                          MAILING
                                                           LIST
                                                           NAME
                                                             |
          ---------------------------------------------------|
          | NEW MAILING LIST                                 |
          |                                                MAIN
       DEFINE                                              MENU
     PARAMETERS                                              |
          |                 ---------------------------------------------------------------------------------------------------
     INITIALIZE             |      |      |             |             |               |                  |                    |
     CATEGORIES           UPDATE   |  CATEGORIES     SUBLIST     LIST DOCUMENT     DISPLAY             PRINT                REPORT
          |                 |      |----->|       |---->|             |               |                  |                    |
        MAIN                |      |  CATEGORY    |  SUBLIST        WHICH           WHICH              WHICH                WHICH
        MENU                |      |    MENU      |   MENU         SUBLIST?        SUBLIST?           SUBLIST?             SUBLIST?
                            |      | D,P  |       | S   |             |               |                  |                    |
                            |      |------| U     |-----|           SORT            SORT            PRINT SORT              REPORT
                            |      |  CATEGORY    |  SUBLIST        MENU            MENU           ----MENU                  MENU
                            |      |   UPDATE     |   NAME?           |               |            |      |                   |
                            |      |------|       |     |       LIST DOCUMET        MAIN           |      |            OUTPUT DEVICE
                            |                     |D,P,R|          MENU             MENU       OUTPUT     |                 MENU
                            |                     |-----|             |                        FORMAT     |                   |
                            |                     |     | U         MAIN                        MENU      |                 MAIN
                            |                     |  SUBLIST        MENU                          |       | PRESORT         MENU
                         UPDATE                   | DEFINITION                                    |       |
                          MENU                    |-----|                                         |       |
                            |                                                                     |       |
      |------------|--------------|--------------|                                                OUTPUT DEVICE
      | A     |--->| C       |--->| D       |--->| R                                           |-------MENU--------|
|---->|       |    |         |    |         |    |                                             |       |           |
|    ADD      |  WHICH       |  WHICH       |  WHICH                                      LIST |       | LABEL     | PRESORT
|  ADDRESS    | ADDRESS?     | ADDRESS?     | ADDRESS?                                         |       |           |
|     |       |    |         |    |         |    |                                             |       |        PRESORT
|-----|       | CHANGE       | DISPLAY      |  REMOVE                                          |       |         MENU
              | ADDRESS      | ADDRESS      |  ADDRESS                                         |      LABEL        |
              |----|         |----|         |----|                                             |      MENU---------|
                                                                                               |       |
                                                                                               |      MAIN
                                                                                               |------MENU





Figure 1-2:  Screen Dialog FlowFigure 1-2:  Screen Dialog Flow


IntroductionIntroduction                                                   Page 1-11


1.5  Getting Started

Depending on the version of your operating system, the following logging
on/off  examples  may  be  different  on  your  computer.  Refer to your
operating system documentation for more information on login procedures.



1.5.1  Logging On/Off the Computer

RSTS or Micro/RSTSRSTS or Micro/RSTS

                        HELLO <RETURN>To log in on RSTS, type HELLO <RETURN>.

Continue by typing your User ID  <RETURN>  and  the  Password  <RETURN>.
User  ID  is  also known as an account number ([nnn,ppp]).  For security
reasons, the password does not echo (i.e., you  can  not  see  what  you
type).   The  operating  system  verifies the information and begins the
session.

                                 BYE/F <RETURN>To log off the RSTS system, type BYE/F <RETURN>.


VAXVAX

                        <RETURN>To log in on VAX, press <RETURN>.

Continue by typing your User ID <RETURN> and the Password <RETURN>.  For
security reasons, the password does not echo (i.e., you can not see what
you type).  The operating system verifies the information and begins the
session.

                                LOG <RETURN>To log off the VAX system, type LOG <RETURN>.



1.5.2  Starting Smart Mailer

RSTS or Micro/RSTSRSTS or Micro/RSTS

You can start Smart Mailer by typing  SMAIL  <RETURN>  (if  your  System
Manager has installed the SMAIL CCL).  Otherwise, you can run SMAIL from
the appropriate account by typing:


                      RUN [nnn,ppp]SMAIL <RETURN>                      RUN [nnn,ppp]SMAIL <RETURN>

Where: nnn,ppp is the Smart Mailer account.

VAXVAX

                                                       SMAIL <RETURN>You can start Smart Mailer on the VAX system by typing SMAIL <RETURN>.

After you have started Smart  Mailer,  the  system  displays  the  title
screen  and  asks  if  you want instructions on how to use Smart Mailer.
Refer to Figure 1-3 for a display of this screen.

IntroductionIntroduction                                                   Page 1-12



------------------------------------------------------------------------



                              Smart Mailer




                              Version  Y1.1
                            Copyright  1983
                    by Digital Equipment Corporation





         Do you want instructions on how to use Smart Mailer?

         Type Y for Yes, or N for No, then press the RETURN key.

------------------------------------------------------------------------


Figure 1-3:  Smart Mailer Introduction ScreenFigure 1-3:  Smart Mailer Introduction Screen


     YType Y for instructions on how to use Smart Mailer.

The instruction screens explain some of the terms used by  Smart  Mailer
and  by this book.  In addition, the instruction screens outline some of
the special keys available to you during your Smart Mailer session.

                                                             <RETURN>After you are familiar with the introductory material, press <RETURN> to
go to the next screen, which will ask you to choose a Mailing List.

                                ENDTo terminate Smart Mailer, type END at  the  Main  Menu.   Smart  Mailer
returns you to the monitor level where the operating system displays the
system prompt (for example, READY or $).

IntroductionIntroduction                                                   Page 1-13


1.5.3  Choosing a Mailing List

After you start Smart Mailer you will have to specify the  name  of  the
mailing  list  you  would like to create or update.  Refer to Figure 1-4
for a display of the screen.

------------------------------------------------------------------------



   Type the name of the mailing list you want to create or update
   (The maximum number of characters in a name is nine).

   You may also type an entire file specification instead of just
   a mailing list name.  Type '?' for help.






    Type the name of the mailing list:

------------------------------------------------------------------------


Figure 1-4:  Enter Mailing List Name ScreenFigure 1-4:  Enter Mailing List Name Screen


If you specify a mailing list that exists,  Smart  Mailer  displays  the
Main  Menu and you may choose any option from that menu.  If you specify
a mailing list that does not exist, Smart Mailer displays the  following
messages:

        That mailing list does not exist.

        Please press RETURN to create a new list with that name,
        or type END to choose another mailing list name:

             <RETURN>If you press <RETURN>, Smart Mailer will create a new mailing list  with
                                    ENDthe  name  specified.   If you type END, Smart Mailer displays the Enter
Mailing List Name screen and you  may  type  the  name  of  an  existing
mailing list.

Refer to Chapter 2 for instructions on how to create a new Mailing List.

IntroductionIntroduction                                                   Page 1-14


1.5.4  Main Menu

The Main Menu shows you all the major functions that  Smart  Mailer  can
perform.  When you choose a function, Smart Mailer will lead you through
the set of questions necessary to perform that function.  Then  it  will
return to the Main Menu.



------------------------------------------------------------------------

                          Smart Mailer Main Menu


              U   =    Update (or display) an address

              S   =    Sublist  Definitions - update, print, display

              D   =    Display a Mailing (Sub)List on the screen

              P   =    Print a Mailing (Sub)List, paper or labels

              W   =    Word Processing List Document creation

              C   =    Category Definitions - update, print, display

              T   =    Transfer to use another Mailing List

              R   =    Report Mailing Sub(list) Statistics

              END      Finished using Smart Mailer

                       Select option:

------------------------------------------------------------------------


Figure 1-5:  Main MenuFigure 1-5:  Main Menu


IntroductionIntroduction                                                   Page 1-15


1.5.5  Transferring to Another Mailing List

The Transfer option enables you to work on another mailing list  without
reentering  Smart  Mailer.   When  you  select this option from the Main
Menu, Smart Mailer displays the Enter Mailing List Name screen (refer to
Figure 1-4 for a display of this screen).  Once you type the name of the
mailing list, you will be using that new mailing list until you go  back
to  the Main Menu and select another mailing list.  This option does NOT
allow you to transfer names or addresses from another mailing list.

                                           TTo transfer to another mailing list, type  T  at  the  "Select  option:"
prompt  of  the  Main  Menu.   If  you specify another mailing list that
exists, Smart Mailer will display the Main Menu and you may  choose  any
option  from  that  menu.  If you specify another mailing list that does
not exist, Smart Mailer displays the following messages:

        That mailing list does not exist.

        Please press RETURN to create a new list with that name,
        or type END to choose another mailing list name:

             <RETURN>If you press <RETURN>, Smart Mailer will create a new mailing list  with
                                    ENDthe  name  specified.   If you type END, Smart Mailer displays the Enter
Mailing List Name screen and you  may  type  the  name  of  an  existing
mailing list.

Refer to Chapter 2 for instructions on how to create a new mailing list.






                               Chapter 2
                      Creating a New Mailing List



There are two ways to create a Mailing List File to contain mailing list
addresses.   The  easiest way is to give Smart Mailer the name of a file
that does not already exist.  Smart Mailer will  then  automatically  go
through the procedure of creating a new file.  (It will first ask you to
confirm this action).  This method of creating Mailing List Files should
be reserved for trying out Smart Mailer, or for small mailing lists.

The other way of creating a Mailing List File is to use the Smart Mailer
Utility.   This is the preferred method because it is more flexible, and
generates a file that stores information more efficiently.  For example,
the  Smart  Mailer  Utility  can  create a file that is almost any size,
where Smart Mailer always creates a file that is the  same  size.   Both
methods create files with the same format.  The Smart Mailer Utility can
also extend and compress any existing Mailing List File.  Refer  to  the
____  _____  ______  ______  _________  _____    ___ _____ ______ ______RSTS  Smart  Mailer  System  Manager's  Guide or VAX Smart Mailer System
_________ _____Manager's Guide for a full description of the Smart Mailer Utility.

This chapter describes how to create a new Mailing List File using Smart
Mailer.   By  following  the  procedure outlined in this chapter you can
initialize a file to contain the addresses in  the  mailing  list.   You
initialize  a  Mailing List File by defining the kind of information you
want to store.  This information includes such things as the  definition
of  categories  you  want to keep for each address, and whether you want
address fields to default to the previous address's  information.   When
you  are  done telling Smart Mailer how to set up the file, Smart Mailer
initializes the file and then  displays  a  message  that  the  file  is
created.

Once your Mailing List File is ready you can  add  addresses  to  it  by
following  the directions given in the next chapter on "Updating Mailing
List Addresses".

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-2


2.1  Mailing List Parameters

By using Mailing List Parameters you can  customize  each  mailing  list
enabling  you  to  sort, retrieve, and store address information to your
specifications.  Unlike System Parameters which  are  stored  separately
and  apply  to  everyone using Smart Mailer, Mailing List Parameters are
unique to each Mailing List File.  You can accept the  parameter  values
shown or you can change any or all of them.

Table 2-1 shows  the  parameter  definitions.   A  description  of  each
parameter follows Table 2-1.



Table 2-1:  Parameter DefinitionsTable 2-1:  Parameter Definitions


             Parameter                 Possible Responses         

1. System generated Primary ID          1 (Consecutive Numbers)
                                        2 (Address Hash)
                                        3 (User Defined)

2. System generated Alternate ID        Y (yes), N (no)

3. Alternate ID Character Mix           0-10, 0-10
   Last Name, First Name                Sum must equal 10
                   
4. Use Last Address as Default          Y (yes), N (no)
   For Next Address

5. Validate state and zip codes:        Y (yes), N (no)


Parameter DefinitionsParameter Definitions

Primary IDPrimary ID

        Smart Mailer uses the Primary ID to store and  retrieve  address
        information.   By  answering  1  to the Primary ID prompt, Smart
        Mailer specifies this ID automatically when adding addresses  to
        the  Mailing  List  (it numbers addresses sequentially).  If the
        Primary ID is defined as type 1, users cannot change it.

        Because the Primary ID must be unique for each address,  if  you
        choose  to  specify  User-defined  Primary  ID (3), take care to
        choose a unique numbering scheme; Social  Security  Number,  for
        example.  Smart Mailer does a search of existing Primary ID's to
        ensure that any new ID added  is  not  already  there.   If  the
        Primary ID is defined as type 2 or 3, users can change the ID if
        it is a duplicate.  When the Primary ID field is selected as the
        field  to  change,  the  system defined value (if applicable) is
        displayed as the default.

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-3


        A new Primary ID type (2),  called  a  'system  defined  address
        hash', has been added.  The ID type is selected when the mailing
        list  is  created.   The  'hashed'  Primary  ID   is   generated
        automatically  each  time a record is added, and consists of the
        following characters from the mailing list record:

        Characters 1-5   First 5 characters of Zip Code.
                         Zeroes if Zip Code is blank.

        Characters 6-7   First 2 characters of last name.

        Character 8      4th character of last name or 3rd
                         character of last name if there is
                         no 4th character.

        Character 9      First character of first name.

        Characters 10-16 - taken from the last 2 address lines above the
        City, State, and Zip Code.

        If address line 3 is blank:        If address line 3 is blank:

        Characters 10-12 First 3 characters of address line 1
                         (except spaces, "The" and  ".")

        Characters 13-16 First 4 characters of address line 2
                         (except spaces, "." and  ",")

        If address line 3 has information:        If address line 3 has information:

        Characters 10-12 First 3 characters of address line 2
                         (except spaces, "The" and  ".")

        Characters 13-16 First 4 characters of address line 3
                         (except spaces, "." and  ",")

        There are several advantages to the new ID type.  First, records
        are  stored  in  Zip Code order, so selecting and sorting by the
        Zip Code is more efficient.

        A second advantage is that duplicate  records  can  be  detected
        before they are added to the file.  If a new record has the same
        Primary ID as an existing record, Smart Mailer allows  the  user
        to take appropriate action.  Users can view the existing record,
        if desired, and then  choose  to  replace  it,  cancel  the  new
        record, or alter the ID of the new record.  Another advantage of
        the hashed ID is that it is easy to locate addresses  that  must
        be changed.

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-4


Alternate IDAlternate ID

        The system generated Alternate ID is a combination of characters
        from  the first and last name, specified by your response to the
        Character Mix prompt.  By answering yes to the system  generated
        Alternate  ID  prompt,  the  system will assign the Alternate ID
        automatically.  Note that you can override  a  system  generated
        Alternate  ID when entering an address.  If you choose to assign
        the Alternate ID yourself, you may choose up  to  10  characters
        for  each  address.   When the Alternate ID field is selected as
        the field to change, the system defined value (if applicable) is
        displayed as the default.

Alternate ID Character MixAlternate ID Character Mix

        The ID mix determines how the system generated Alternate  ID  is
        formed.   If,  for example, the ID mix is 5 5, Smart Mailer uses
        the first five characters from the last and first names for  the
        ID.

        If you are planning to  sort  on  last  name,  first  name,  for
        example,  take  care  to  specify enough letters in each name to
        provide the best sort.  The default for Alternate  ID  character
        mix  is  6  4;  or  the  first  six  characters of the last name
        followed by the first four characters of the first name.

             Using two different character mixes: 

             Name                    Alternate ID       Alternate ID
                                      (Mix 5 5)          (Mix 9 1)

             Thomas Jones            JONESTHOMA         JONES    T

             Theodore Jones Jr.      JONESTHEOD         JONES    T

             Thea Joneson            JONESTHEA          JONESON  T

        Note that when forming the Alternate ID,  Smart  Mailer  ignores
        titles  such as Mr.  and MD.  as long as they end with a period.
        This means that initials should be  entered  as  J D Smith  (not
        J. D. Smith)  for  the initial of the first name to be used in a
        system generated Alternate ID.

        For  names  such  as  La Croix  and  St. Hilaire,  Smart  Mailer
        considers  the  first  word  as a middle name.  Therefore, it is
        better to use the convention of either a period  with  no  space
        (ST.HILAIRE),  upper  and lower case (LaCroix), or just no space
        (LACROIX), so that the Alternate ID will use the full last name.
        Names with hyphens (Fawcett-Maker) and apostrophes (O'Toole) are
        acceptable,  but  may  generate  Alternate   ID's   with   those
        characters (- and ') in them.

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-5


Use Last Address as Default For Next AddressUse Last Address as Default For Next Address

        Smart Mailer will prompt for each city, state, and zip code with
        the  information from the previously entered address.  This is a
        shortcut for a set of addresses that are similar,  or  from  the
        same  general area.  You can, of course, override the default if
        the next address has different information.

        If you do not want Smart Mailer to use the  last  address  as  a
        default  for  the  next  address,  you  will  have  to  type the
        information for each city, state, and zip code when  you  add  a
        new address.

Validate state and zip codesValidate state and zip codes

        Smart Mailer will check to see if you have entered a valid  U.S.
        state  abbreviation.  Refer to Table 3-1 in Chapter 3 for a list
        of the valid state abbreviations.  Smart Mailer will also  check
        to   see  if  you  have  entered  the  correct  form  (xxxxx  or
        xxxxx-xxxx) for U.S.  zip codes.  It will not check  to  see  if
        the  zip  code  matches the state or that the zip code is valid.
        If you type an invalid state or  zip  code,  Smart  Mailer  will
        display a warning message.

        If you have mostly foreign addresses or non-address information,
        you  may  not want Smart Mailer to warn you of invalid states or
        zip codes.

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-6


2.2  Mailing List Categories

Smart Mailer enables you to define six fields for collecting specialized
information  called  categories.  A category is related information that
you want associated  with  a  particular  mailing  list.   The  category
information  (such  as  Hire  Date)  is stored with the name and address
information.

Category labels are a maximum of ten characters and can consist  of  any
printable  character.   Sample  labels  include  Occupation,  Hire Date,
Salary, etc.

Category type codes describe the kind of information you are  collecting
for  each  category.  Refer to Table 2-2 for examples and definitions of
these type codes.

It is not necessary to assign all six  categories  before  you  use  the
mailing list.  Remember, however, that once you do assign categories, if
you change a previously assigned category label or type  code,  all  the
addresses in the list before the change may have inappropriate data.

Likewise,  if  you  add  a  category  after  you  have   added   address
information,  all  the  addresses  in the list prior to the new category
addition may have no information in the new category field.

You can change, display, or add  new  category  definitions  anytime  by
using  the  Category  option (C) from the Main Menu.  Refer to Chapter 8
for  more  details  on  updating,  displaying,  or   printing   category
definitions.

You can change, display or add category information for any  address  by
using the Update Address option (U) from the Main Menu.

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-7


Table 2-2:  Category Initialization Type CodesTable 2-2:  Category Initialization Type Codes


Type Code              Definition                   Examples   

   A     Alphanumeric; default type code            Plumber
         Any combination of printable characters.   $32,000.
                                                    #317

   N     Numeric                                    32000
         Numbers only (no $ , - . characters)       230
         If you want to assure that the user        5280
         types numbers only, assign a numeric       89
         type code.

   D     Date; defaults to today's date             23-JUN-82 
         You must type all dates in the standard    01-OCT-79     
         format shown.                              02-JAN-00

         Use the following month abbreviations:
 
               JAN       MAY       SEP
               FEB       JUN       OCT
               MAR       JUL       NOV
               APR       AUG       DEC

   Y     Y (yes) or N (no).  If you want to         Y, N
         assure that the user types a Y or N.
         This is used when you have a label such
         as Customer? and you want to define
         whether he/she is or is not a customer.

   C    Coded (C).  If you specify a category       (see the following
        field as coded, Smart Mailer treats each     examples)
        character position independently.
        Comparisons are made on a character by
        character basis and a wild card character
        (such as %) can be used in sublist
        definitions.  Coded categories allow
        the user to pack more information in the
        category field, and give the user greater
        control over sublist selection.  

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-8


Example 1:Example 1:

The user sends out catalogs 4 times a  year  but  does  not  send  every
catalog  to  all addresses in the mailing list.  A coded category can be
set up (called CATALOGS) to store  this  information  in  the  following
manner.  The first character indicates whether the customer receives the
Spring catalog, the second shows whether the Fall catalog is  sent,  and
so  forth  for  Winter,  and  Christmas.  So a customer that only gets a
Christmas catalog would have a category value of NNNY (N = no, Y = yes).
A sublist for the Fall catalog mailing would look like:

    line 1:    CATALOGS  is  %Y%%

(assuming that % is used as the wild card character - this is set  by  a
parameter in the Smart Mailer Parameter File).

A sublist of regular customers, who receive all catalogs except for  the
Christmas catalog could be extracted by:

    line 1:    CATALOGS  is  YYYN

Example 2:Example 2:

Another way of using the coded characters is to set up a system where  S
means Spring, F means Fall, W means Winter, and C means Christmas.  Then
a customer with  codes  SFW  gets  all  catalogs  except  the  Christmas
catalog.   And  a  sublist  for  sending out the Fall catalog would look
like:

    line 1:      CATALOGS  is  F
    line 2:   or CATALOGS  is  %F
    line 3:   or CATALOGS  is  %%F
    line 4:   or CATALOGS  is  %%%F

Example 3:Example 3:

For a user who manages three magazines, coded categories could be set up
to  indicate when the subscriptions expire, and how many renewal notices
have been sent.  A  customer  subscribing  to  Creative  Nest  Building,
Popular  Skiing,  and  Purple  Thumb might have categories EXPIRES = ABC
(meaning the subscriptions expire in January, February, and  March)  and
NOTICES  =  010  (meaning  that  the  customer has been sent one renewal
notice  for  Popular  Skiing).   A  sublist  of  all   customers   whose
subscription  to  Purple  Thumb  expires in April and who have been sent
more than one renewal notice would be:

    line 1:       EXPIRES  is    %%D
    line 2:  and  NOTICES  above %%1

Creating a New Mailing ListCreating a New Mailing List                                     Page 2-9


2.3  Walk Through

This section describes the flow through Smart Mailer for initializing  a
Mailing List File, showing each screen, describing the logical flow, and
explaining any questions, prompts or messages that have not already been
explained in the previous sections.

This section of Smart Mailer assumes that you have already  logged  onto
the  system and read the instruction screen.  If you have not done this,
refer to the "Getting Started" section of Chapter 1.

After you have read the instruction screen, Smart  Mailer  displays  the
following screen:


------------------------------------------------------------------------

   Type the name of the mailing list you want to create or update.
   (The maximum number of characters in a name is nine).

   You may also type an entire file specification instead of just
   a mailing list name.  Type '?' for help.






    Type the name of the mailing list:

------------------------------------------------------------------------


Figure 2-1:  Enter Mailing List Name ScreenFigure 2-1:  Enter Mailing List Name Screen


To create a new Mailing List File, specify the name of  a  mailing  list
that  does  not  already  exist.   You  must  press  <RETURN> after each
response.

                                                           RESUMEFor example, to create a mailing list called RESUME, type  RESUME.   All
examples throughout this manual will be referencing this mailing list.

If you type more than nine characters,  Smart  Mailer  will  accept  it.
However,  it will not use more than six characters for that Mailing List
File name.  For example, if you enter ORDERFORM  for  the  name  of  the
mailing list, Smart Mailer will name that file as "ORDERF.MLF", dropping
off any extra characters.  The ".MLF" extension is the default extension
for a Mailing List File name.

If this Mailing List File does not already exist, Smart  Mailer  assumes
that you want to create a new mailing list, but asks you to confirm this
with the following screen:

Creating a New Mailing ListCreating a New Mailing List                                    Page 2-10


------------------------------------------------------------------------

       That mailing list does not exist.


       Please press RETURN to create a new list with that name,
       or type END to choose another mailing list name:

------------------------------------------------------------------------

Figure 2-2:  Confirming Mailing List NameFigure 2-2:  Confirming Mailing List Name


You can perform one of the following actions:

              END      o  Type END to choose another Mailing List File name.

               <RETURN>      o  Press <RETURN> to assure Smart Mailer that you want to create a
         new Mailing List File.

Since  the  mailing  list  is  new,  Smart  Mailer  asks  for  parameter
definitions  and  category  initialization.   Refer to Section 2.1 for a
list of valid responses and descriptions to the  parameter  definitions.
Smart  Mailer  displays  the  Mailing  List Parameter Screen as shown in
Figure 2-3.


------------------------------------------------------------------------

                    Mailing List Parameter Screen


      1 =  Primary ID:                                    1
                1 = Consecutive Numbers
                2 = Address Hash
                3 = User Defined

      2 =  System generated Alternate ID:                 Y

      3 =  Alternate ID char mix - last name, first name: 6   4

      4 =  Use last address as default for next address:  Y

      5 =  Validate state and zip codes:                  Y

    Type the number of the parameter you want to redefine;
    then the parameter value(s).
    Press RETURN to continue to the next screen.
    Type END to go back.

                           Select option:

------------------------------------------------------------------------

Figure 2-3:  Mailing List Parameter ScreenFigure 2-3:  Mailing List Parameter Screen


Creating a New Mailing ListCreating a New Mailing List                                    Page 2-11


You can perform one of the following actions:

              END      o  Type END to go back to the Enter Mailing List Name display.

              ?      o  Type ?  to display help messages for the Mailing List Parameter
         Screen.

               <RETURN>      o  Press <RETURN>  to  accept  all  the  default  values  for  the
         parameters.

      o  Type the  number  of  the  parameter  definition  you  want  to
         redefine and then type the new value.

The following section discusses how to change parameter values.

You must press <RETURN> after each response.  If you want to redefine  a
parameter  value,  type the number of the parameter you want to redefine
and the cursor will move to that parameter value.  Type the new value.

For example, to change your Alternate ID character mix from 6 4 (default
value) to 5 5, follow these steps:

              3     1.  Type 3.

              5     2.  Type 5.

              5     3.  Type 5.

The cursor is then positioned at the "Select option:"  prompt  to  allow
you to change another parameter value.  You may change another parameter
value or press <RETURN> to accept the parameter values displayed.

If you enter an invalid response to the parameter  value,  Smart  Mailer
displays  an  error message and will reprompt you for the correct value.
Type the correct value.

After you define the parameters,  Smart  Mailer  displays  the  Category
Initialization  screen as shown in Figure 2-4.  Refer to Section 2.2 for
a description of what a category is and a list of the valid  type  codes
for categories.

Creating a New Mailing ListCreating a New Mailing List                                    Page 2-12


--------------------------------------------------------------------------------

                         Category Initialization


                           label       type

          Category 1    undefined       A
          Category 2    undefined       A
          Category 3    undefined       A
          Category 4    undefined       A
          Category 5    undefined       A
          Category 6    undefined       A


    Type the label of each category (for example, Occupation), press RETURN,
    then type the kind of the information to be stored in the category - either
    Alphanumeric (A) - the default, or Numeric (N), Date (D), Yes/No (Y),
    Coded (C).

    Simply press RETURN to take the default for any answer.  Type '?' for help.
    Do NOT use labels such as NAME, CITY or STATE - these are already there.
    (note:  You may not back up to the previous menu at this point.)

--------------------------------------------------------------------------------


Figure 2-4:  Category Initialization ScreenFigure 2-4:  Category Initialization Screen


The cursor is positioned at Category 1 "label".  The default values  for
the type codes are alphanumeric (A).

Smart Mailer does not allow you to back up from this screen because  you
are  now  half  way through creating the file.  If you change your mind,
simply continue on, then delete the file as you would any other file.

You can perform one of the following actions:

              END      o  Type END to go back to Category 1 "label".

               ?      o  Type  ?   to   display   help   messages   for   the   Category
         Initialization Screen.

                <RETURN>      o  Press  <RETURN>  or  at  each  "label"  and  "type"  to   leave
         categories undefined.

      o  Type the label of the category you want to define and  enter  a
         type code to be associated with that category.

The following section discusses how to define categories.

Creating a New Mailing ListCreating a New Mailing List                                    Page 2-13


You must press <RETURN> after  each  response.   To  define  categories,
enter  the  name  you want for the category label (e.g., Occupation) and
then enter a valid type code (e.g., A (Alphanumeric)) to  be  associated
with that label.

If you make a mistake when entering your category labels or type  codes,
type END before you finish with category initialization and Smart Mailer
will move the cursor back to Category 1 "label".  If you have a  change,
type  over  the  label  and/or type code where the change is to be made.
Press <RETURN> to skip the  labels  and  type  codes  you  have  defined
correctly.

If you made a mistake when defining your categories and you did not type
END before you finished defining categories, you can make changes to the
categories by selecting the Category Definitions  option  (C)  from  the
Main Menu.  Updating category definitions is discussed in Chapter 8.

For  example,  to  define  Category  1  as  Occupation  and  assign   an
Alphanumeric value for the type code, follow these steps:

              Occupation     1.  Type Occupation.

               <RETURN>     2.  Press <RETURN> (Alphanumeric is the default value).

The cursor moves to the next category.  Define another category or press
<RETURN> at each "label" and "type" to skip the rest of the categories.

After you define categories for your new Mailing List File, Smart Mailer
confirms  the  Mailing  List  File  creation by displaying the following
message:

        Finished creating Mailing List File called RESUME.MLF

If you specified an extension for your mailing list, that  extension  is
displayed instead of the ".MLF" extension.

If you are finished with this mailing list and you do not  want  to  add
                       ENDany  addresses,  type  END  at  each screen displayed until Smart Mailer
returns you to monitor level where the  operating  system  displays  the
system prompt.






                               Chapter 3
                    Updating Mailing List Addresses



                                               addingThis chapter describes the basic operations of adding a new  address  to
                      changing      displayingyour  mailing  list,  changing  or  displaying  an existing address, and
removingremoving an obsolete address.  It explains in detail each  component  of
an address.

The concept of address identifiers (ID's) is important.  Each  name  and
                         Primary  IDaddress  has  a  unique  Primary  ID, such as social security number, or
                                     Alternate IDaccount number.  It may also have an Alternate ID, which may or may  not
be unique.  How these identifiers are defined is set up when the file is
created.  (See Chapter 2, "Creating a Mailing List").  When you want  to
change, display, or remove an existing address you refer to it using one
of its identifiers.

Smart Mailer always prompts you for the name of the  mailing  list  when
you  start.  Refer to Figure 1-4 for a display of the Enter Mailing List
Name screen.  You must enter the name of a mailing list.  If the mailing
list  name exists, Smart Mailer displays the Main Menu.  Refer to Figure
1-5 for a display of the Main Menu.  If you want  to  update  a  mailing
list, you may type 'U' or press <RETURN> to accept the default answer at
the Main Menu.  Smart Mailer then displays the Update  Menu.   Refer  to
Section 3.2 for a display of the Update Menu.

The following section gives an explanation of address fields and a table
of the valid state abbreviations.

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-2


3.1  Explanation of Address Fields

When adding an address, make sure you use the same conventions for every
address  in  the  Mailing  List  File.  For example, if you start adding
names and addresses in all upper case characters,  use  all  upper  case
characters for all addresses in the Mailing List File.  This will ensure
consistency when it comes time to print, display, or  update  a  mailing
list.

A brief explanation of each address field is given below:

Name:Name:

        Type the name of the addressee (up to 30 characters) as you want
        it to appear on the label.

Address line 1:Address line 1:

        Type the first line of the address (up to 30  characters).   For
        example, type the street address, P.O. Box, or company name.

Address line 2:Address line 2:

        Type the second line of the address (up to 30 characters).   For
        example, type a c/o line.

Address line 3:Address line 3:

        Type a third line of the address (up  to  30  characters).   For
        example, type a building number or room number.

City/Town:City/Town:

        Type the name of the city or town  of  the  address  (up  to  30
        characters).

State/Country:State/Country:

        Type the standard abbreviations for the state  (2  letters),  or
        you  may  type  the  name  of a country (e.g., Canada).  Use the
        standard state abbreviations  as  listed  at  the  end  of  this
        section in Table 3-1.  You may type up to 12 characters.

        If you  type  invalid  state  abbreviations  and  you  have  the
        "Validate state and zip codes" parameter set to "Yes" (Y), Smart
        Mailer displays a warning message.  If you have  this  parameter
        set  to "No" (N), Smart Mailer will not check to see if they are
        valid.  If  you  press  <RETURN>  to  skip  entering  the  state
        information, Smart Mailer will not display a warning message.

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-3


Zip code:Zip code:

        Type the zip code (up to 10 characters).  All United States  zip
        codes  are  five  digits  (xxxxx)  or 5 digits with hyphen and 4
        digits (xxxxx-xxxx).  The xxxxx-xxxx is the new 9-digit zip code
        for the United States.

        Zip codes that are not for the United States are nonstandard and
        may  contain  alphanumeric  characters.  These zip codes are for
        foreign countries.  Only United States zip  codes  are  eligible
        for the presorted postal rate.  For more information on PRESORT,
        refer to Section 10.1.

        If you type an invalid form for  zip  codes  and  you  have  the
        "Validate state and zip codes" parameter set to "Yes" (Y), Smart
        Mailer displays a warning message.  If you have  this  parameter
        set  to "No" (N), Smart Mailer will not check to see if they are
        valid.  If you press <RETURN> to  skip  entering  the  zip  code
        information, Smart Mailer will not display a warning message.

Category DefinitionsCategory Definitions

        If you defined  any  categories  during  initialization  of  the
        Mailing List File, the label you typed for each category will be
        displayed when  Smart  Mailer  displays  the  "Add"  an  Address
        screen.    If   you   did   not  define  every  category  during
        initialization of the Mailing List  File,  the  categories  that
        were  not  defined  will  be displayed as "undefined" when Smart
        Mailer  displays  the  "Add"  an  Address  screen.    For   more
        information on Category Definitions, refer to Section 2.2.

Counter:Counter:

        Smart Mailer displays the counter as 0 for each new  address  in
        the  mailing  list.   This  counter is used to keep track of how
        many times this address has been printed  on  labels.   You  may
        change  this  default when adding the address, or you may update
        the counter when updating the address.  The range of the counter
        is  0  to  9999.  If you try to decrement or increment a counter
        outside of that range, the counter will be set to  either  0  or
        9999  (respectively).  The system actually allows you to enter a
        counter with negative  or  fractional  numbers  (-9,  6.4),  but
        converts them to non-negative integers (0, 6).

Remarks:Remarks:

        You may type up to 65 alphanumeric characters.   You  would  use
        this  for  any  comments  you may want to be associated with the
        address.

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-4


Primary ID:Primary ID:

        If this mailing list  has  the  Primary  ID  defined  as  system
        generated (1), you can not change it.  If the Primary ID is user
        defined (3), or a system  defined  address  hash  (2),  you  can
        change it if it is a duplicate Primary ID.  If the Primary ID is
        user defined, you must assign a unique ID to this address (up to
        16 characters).  For example, type the social security number of
        the person.  This Primary ID will identify  the  addressee  when
        you  update  the  mailing list, print the mailing list, or print
        labels.

Alternate ID:Alternate ID:

        If this mailing list has a system generated Alternate  ID,  then
        it  will  be made up of a combination of the first and last name
        of the addressee.  It may  always  be  changed  by  typing  over
        whatever  is  there.   You  may  assign a combination of letters
        and/or numbers to this  address  (up  to  10  characters).   For
        example,  you  may type the last name of the addressee.  You may
        also leave it blank.  Unlike the Primary ID,  the  Alternate  ID
        does not have to be unique; there may be duplicates.  If you use
        Alternate IDs, Smart Mailer can print addresses in  that  order.
        For more information on Alternate IDs, refer to Chapter 2.

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-5


Table 3-1:  State AbbreviationsTable 3-1:  State Abbreviations


STATE          ABBREVIATION        STATE          ABBREVIATION

Alabama             AL             Missouri            MO
Alaska              AK             Montana             MT
Arizona             AZ             Nevada              NE
Arkansas            AR             New Hampshire       NH
California          CA             New Jersey          NJ
Colorado            CO             New York            NY
Connecticut         CT             North Carolina      NC
Delaware            DE             North Dakota        ND
Georgia             GA             Ohio                OH
Florida             FL             Oklahoma            OK
Hawaii              HI             Oregon              OR
Idaho               ID             Pennsylvania        PA
Illinois            IL             Rhode Island        RI
Iowa                IA             South Carolina      SC
Indiana             IN             South Dakota        SD
Kansas              KS             Tennessee           TN
Kentucky            KY             Texas               TX
Louisiana           LA             Utah                UT
Maine               ME             Virginia            VA
Maryland            MD             Vermont             VT
Massachusetts       MA             Washington          WA
Michigan            MI             Wisconsin           WI
Minnesota           MN             West Virginia       WV
Mississippi         MS             Wyoming             WY



               OTHER                    ABBREVIATION

          District of Columbia               DC
          Guam                               GU
          Puerto Rico                        PR
          Virgin Islands                     VI

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-6


3.2  Walk Through

This section describes the flow through  Smart  Mailer  for  updating  a
Mailing List File, showing each screen, describing the logical flow, and
explaining any questions, prompts, or messages  that  have  not  already
been explained in the previous section.

This section of Smart Mailer assumes that you have already  logged  onto
the  system, read the instruction screen, typed the name of your mailing
list, and the Main Menu is displayed.  If you have not done this,  refer
to Chapter 1, Sections 1.5 through 1.5.4.

                                                                    UTo add, change, display or remove addresses in a mailing list, type U at
the  "Select  option:"  prompt  of  the  Main  Menu.  The Update Menu is
displayed as shown in Figure 3-1.


------------------------------------------------------------------------

                               Update Menu


                      A    =   Add a new address

                      C    =   Change an address

                      D    =   Display an address

                      R    =   Remove an address

                      END      Return to the Main Menu


                               Select option:

------------------------------------------------------------------------


Figure 3-1:  Update MenuFigure 3-1:  Update Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the Update Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (A).

      o  Type the letter associated with the option you want to perform.

The following sections discuss these options in detail.

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-7


3.2.1  Adding an Address

                        ATo add an address, type A at the "Select option:" prompt of  the  Update
Menu.   Smart  Mailer displays the "Add" an Address screen.  A sample is
shown in Figure 3-2.


------------------------------------------------------------------------

Add                                                    Type '?' for help


  1 Name:
  2 Address line 1:
  3         line 2:
  4         line 3:
  5 City/Town:
  6 State/Country:
  7 Zip code:

  8 Occupation
  9 undefined
 10 undefined
 11 undefined
 12 undefined
 13 undefined
 14 Counter:
 15 Remarks:

 16 Primary ID:        1
 17 Alternate ID:

------------------------------------------------------------------------


Figure 3-2:  Add an Address ScreenFigure 3-2:  Add an Address Screen


The cursor is positioned at the "Name:" field.

The Primary ID is displayed if you accepted the system generated Primary
ID  (1)  when you created the mailing list.  The Primary ID is displayed
when the cursor is displayed at the Alternate ID field if 'address hash'
(2) was chosen when you created the mailing list.

The category  labels  are  displayed  if  you  have  defined  them.   If
categories are not defined, Smart Mailer displays them as "undefined".

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-8


You can perform one of the following actions:

              END      o  Type END to go back to the Update Menu.

              ?      o  Type ?  when the cursor is positioned at the "Name:" field  for
         Smart Mailer to display help messages for all the fields in the
         "Add" an Address screen.

              ?      o  Type ?  when the cursor is positioned at any other field (e.g.,
         "Address line 1:") and Smart Mailer displays a single line help
         message for that field.

               <RETURN>      o  Press <RETURN> to skip entering information for a field and  go
         to the next field.

      o  Type information for the field.

               <LINEFEED>      o  Press <LINEFEED> at any category field  to  indicate  that  all
         data  has  been  entered  for  this address.  This provides the
         convenience of skipping over undefined categories.

Certain address fields may have a default answer.  These fields are  the
city/state/zip  fields  (may  be  defaulted to the previous values), any
categories defined as date information (defaulted to today's date),  the
counter  (defaults  to  zero),  and  the  Alternate ID (may default to a
combination of first and last name characters).  These  default  answers
will be shown when the cursor is positioned at that field.  In all cases
you may either accept the suggested answer by pressing <RETURN>,  change
it by typing over it, or remove it by pressing the space bar once before
pressing <RETURN>.

The following section discusses how to add an address.

Updating Mailing List AddressesUpdating Mailing List Addresses                                 Page 3-9


For example, to add the following address:

        Robert Fuller
        14 River St.
        P.O. Box 375
        Marlboro, MA  01752
        Occupation:  Engineer

follow these steps:

              Robert Fuller     1.  Type Robert Fuller.

              14 River St.     2.  Type 14 River St..

              P.O. Box 375     3.  Type P.O. Box 375.

               <RETURN>     4.  Press <RETURN> to skip "Address line 3:" field.

              Marlboro     5.  Type Marlboro.

              MA     6.  Type MA.

              01752     7.  Type 01752.

              Engineer     8.  Type Engineer.

               <RETURN>                                       <LINEFEED>     9.  Press <RETURN> for each undefined category, or press <LINEFEED>
         at  first  undefined  category  and  the  cursor  moves  to the
         Alternate ID field.

               <RETURN>    10.  Press <RETURN> to accept counter default value.

               <RETURN>    11.  Press <RETURN> to skip "Remarks:" field.

               <RETURN>    12.  Press <RETURN> to accept system generated Alternate ID.

         (Primary ID is system generated in this example.)


Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-10


When you are finished entering an address, Smart Mailer  allows  you  to
change  information  in  the  address  before it is added.  Smart Mailer
displays the following prompt:

      -  Change which line (1-17):
         Press RETURN to accept.

         You can perform one of the following actions:

                  END          <RETURN>          o  Type END or press <RETURN> to accept  the  address  as  is.
             Smart Mailer will redisplay a blank "Add" an Address screen
             so you can add another address.

          o  Type the number of the field  you  have  changes  in.   The
             cursor  moves  to  the  field specified.  Type over the old
             information with the changed information.

                  <CTRL/C>          o  Type <CTRL/C> to return to the "Name:" field.  You can then
             re-enter  the address information, or, type <CTRL/Z> or END
             to return to the previous menu without adding  the  address
             to the Mailing List file.

                                        NOTE                                        NOTE

                 The use of <CTRL/C> in this case is  an  exception;                 The use of <CTRL/C> in this case is  an  exception;
                 in general, <CTRL/C> terminates the program.                 in general, <CTRL/C> terminates the program.




Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-11


The following section discusses how to change information in an address.

For example, let's change Robert Fuller's address from "14 River St." to
"14 River Rd.".  To change this information, follow these steps:

              2     1.  Type 2.  The cursor moves to "Address line 1:".

              14 River Rd.     2.  Type 14 River Rd..

         You can also perform one of the following actions at step 2.

                   <RETURN>          o  Press <RETURN> if you changed your mind and do not want  to
             change  the information for the field and Smart Mailer will
             keep the old information.

                                                  <RETURN>          o  Press the space bar once, then press <RETURN> if  you  want
             to erase the information in the field.


When you are finished changing the field selected, the cursor will  move
down  to the "Change which line (1-17):" prompt again.  If you have more
changes to the address, follow the same procedure  as  described  above.
                   <RETURN>Otherwise,  press  <RETURN>  and  Smart  Mailer  stores that address and
clears the screen so you can add another address.

If you accepted all the default Mailing  List  parameter  values,  Smart
Mailer  displays  the  "Add" an Address screen for the next address with
information of the previous address in the "City/Town:",  "State:",  and
"Zip code:"  fields  and  displays  the  next  sequential number for the
"Primary ID" field.

To fill up our sample Mailing List, add the following addresses:

        Roberta Fullerton               John Doe
        146 Main St.                    10 Any St.
        Maynard, MA  01754              Hudson, MA  01749
        Occupation:  Data Prep          Occupation:  Plant Mgr.

                                              ENDWhen you are finished adding addresses, type  END  when  the  cursor  is
positioned at the "Name:" or "Change which line (1-17):" prompt.

                                                      ENDIf you want to terminate Smart Mailer continue typing END for every menu
displayed  until  Smart  Mailer  returns  you to monitor level where the
operating system displays the system prompt.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-12


3.2.2  Changing an Address

If you are going to use your mailing list for any amount  of  time,  you
will need to update it.  People move, change names, jobs, and so forth.

                           CTo change an address, type C  at  the  "Select option:"  prompt  of  the
Update  Menu.  Smart Mailer displays the Specify an Address ID screen as
shown in Figure 3-3.

Specify an Address IDSpecify an Address ID

Whenever you choose to change or display addresses in your mailing list,
Smart  Mailer requires that you enter the Primary or Alternate ID of the
address you want to change or display.


------------------------------------------------------------------------

                  Specify an Address ID



                  P    =    Primary ID

                  A    =    Alternate ID


    Type the ID code (P or A) of the ID that you want to use to
    identify the address to display or change.  Then type the ID.
    Or type END to return to the Update Menu.


                      Select option:

------------------------------------------------------------------------


Figure 3-3:  Specify an Address ID ScreenFigure 3-3:  Specify an Address ID Screen


The cursor is positioned at the "Select option:" prompt.

To tell Smart Mailer which address needs to be changed,  you  must  type
either the Primary or Alternate ID of the address you have changes in.

You can perform one of the following actions:

              END      o  Type END to go back to the Update Menu.

              P      o  Type P to identify the address by Primary ID.  If you type 'P',
         Smart  Mailer  moves  the cursor to the Primary ID field.  Type
         the Primary ID of  the  address  you  want  to  change.   Every
         Primary ID is unique.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-13


              A      o  Type A to identify the address by Alternate ID.   If  you  type
         'A',  Smart  Mailer moves the cursor to the Alternate ID field.
         Type the Alternate ID of the address you want  to  change.   If
         you  cannot  think  of  the complete Alternate ID, you may type
         just the first part of it.  You may  have  duplicate  Alternate
         ID's.   Refer  to  the  "DUPLICATE  ALTERNATE ID'S" section for
         details of the prompts displayed.

If you type an ID  that  does  not  exist,  Smart  Mailer  displays  the
following message and prompts you for another ID.

        An address with that ID does not exist.

If you type an ID that exists, Smart Mailer  displays  the  "Change"  an
Address screen with address information (Figure 3-4).

The following examples discuss how to select an address  by  Primary  or
Alternate ID.

For example, to change John Doe's address by Primary  ID,  follow  these
steps:

              P     1.  Type P to select the address by Primary ID.

              3     2.  Type 3 because that is the  Primary  ID  associated  with  this
         address (following the examples in this guide).

         Smart Mailer displays the "Change" an Address screen  as  shown
         in Figure 3-4.

You could also change John Doe's address by Alternate ID.  To change his
address by Alternate ID, follow these steps:

              A     1.  Type A to select the address by Alternate ID.

              DOE<SP><SP>JOHN<SP>     2.  Type DOE<SP><SP>JOHN<SP>  because  that  is  the  Alternate  ID
         associated  with  this  address (Alternate ID character mix was
         changed to 5 5).

         Smart Mailer displays the "Change" an Address screen  as  shown
         in  Figure  3-4  except  the  "<--- selected by" is next to the
         Alternate ID field.

If you have other addresses with the same  Alternate  ID,  Smart  Mailer
does not display the "Change which line (1-17):" prompt first.  Refer to
the "DUPLICATE ALTERNATE  ID'S"  section  for  details  of  the  prompts
displayed.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-14


------------------------------------------------------------------------

Change                                                 Type "?" for help


  1 Name:               John Doe
  2 Address line 1:     10 Any St.
  3         line 2:
  4         line 3:
  5 City/Town:          Hudson
  6 State/Country:      MA
  7 Zip code:           01749

  8 Occupation:         Plant Mgr.
  9 undefined
 10 undefined
 11 undefined
 12 undefined
 13 undefined
 14 Counter:            0
 15 Remarks:

 16 Primary ID:         3               <--- selected by
 17 Alternate ID:       DOE  JOHN

                Change which line (1-17):
                Press RETURN to accept.

------------------------------------------------------------------------


Figure 3-4:  Change an Address ScreenFigure 3-4:  Change an Address Screen


The cursor is positioned at the "Change which line (1-17):" prompt.

If there is only one address with that ID,  Smart  Mailer  displays  the
following prompt:

      -  Change which line (1-17):
         Press RETURN to accept.

         You can perform one of the following actions:

                   <RETURN>         END          o  Press <RETURN> or type END and Smart  Mailer  displays  the
             Specify  an  Address  ID  screen  so you can choose another
             address.

          o  Type the number of the field you have  changes  in.   Smart
             Mailer moves the cursor to the field selected.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-15


                  <CTRL/C>          o  Type <CTRL/C>  to  return  to  the  previous  menu  without
             updating the address.

                                        NOTE                                        NOTE

                 The use of <CTRL/C> in this case is  an  exception;                 The use of <CTRL/C> in this case is  an  exception;
                 in general, <CTRL/C> terminates the program.                 in general, <CTRL/C> terminates the program.


             You can perform one of the following actions:

              o  Type  over  the  old  information  with   the   changed
                 information.

                       <RETURN>              o  Press <RETURN> if you changed your mind and do not want
                 to  change  the  information  for  the  field and Smart
                 Mailer will keep the old information.

                                                       <RETURN>              o  Press the space bar once, then press  <RETURN>  if  you
                 want to erase information in the field.

                 Once you perform one of the above actions, Smart Mailer
                 displays  the  "Change which line (1-17):" prompt again
                 so you can change another field in this address.



The following section discusses how to change John Doe's  "Address  line
1:" from "10 Any St." to "10 Ruth Rd.".

To change this address, follow these steps:

              2     1.  Type 2.

              10 Ruth Rd.     2.  Type 10 Ruth Rd..

If you have more changes to the address, follow the  same  procedure  as
described above.  Otherwise, press <RETURN> and Smart Mailer stores that
address and displays the Specify an Address ID screen again so  you  can
choose  another address to change.  When updating addresses, the default
response to the "Specify an Address ID" screen is your previous  choice.
This makes updating several addresses easier.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-16


Duplicate Alternate ID'sDuplicate Alternate ID's

You may have addresses with duplicate Alternate  ID's  in  your  mailing
list.   For example, Roberta Fullerton and Robert Fuller would both have
an Alternate ID of "FULLEROBER".  Also, specifying just a portion of the
Alternate  ID  could  give  you  more  than one address that matches the
specified ID portion.  For example, if you type "JON" as  the  Alternate
ID  and  you  have  James Jones and Henry Joneston in your mailing list,
that will cause you to have duplicate Alternate ID's.

If you enter an Alternate ID for which there is more than  one  matching
address,  Smart  Mailer  will  first  try to determine which address you
want.  Smart Mailer displays the "Change" an Address screen as shown  in
Figure  3-4  except  the  "Change  which  line  (1-17):"  prompt  is not
displayed first.  Instead, Smart Mailer displays the following prompts:

      -  (There is at least one other address with this Alternate ID.)
         Is this the address you want?

         You can perform one of the following actions:

                  Y          o  Type Y if this is the correct  address,  and  Smart  Mailer
             displays  the  "Change which line (1-17):" prompt.  You may
             now change address information.

                         Y             If you type Y  and  you  are  displaying  addresses,  Smart
             Mailer displays the "When through with address ...    Press
             RETURN" prompt.

                  N          o  Type N if this is not the correct address, and Smart Mailer
             displays the following prompt:


      -  Do you want to see the next matching address?

         You can perform one of the following actions:

                  N          o  Type N if you do not want to see the next address and Smart
             Mailer displays the Specify an Address ID screen so you can
             choose another Primary or Alternate ID.

                  Y          o  Type Y to display the next address with that Alternate  ID.
             Smart Mailer displays the next address.

             However, if this is the last address  with  that  Alternate
             ID, the following prompt is displayed:

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-17


              -  (There are NO more addresses with that Alternate ID.)
                 Is this the address you want?

                 You may perform one of the following actions:

                          Y                  o  Type Y and Smart Mailer displays the "Change  which
                     line  (1-17):"  prompt.  You may now change address
                     information.

                                 Y                     If you type Y and  you  are  displaying  addresses,
                     Smart   Mailer  displays  the  "When  through  with
                     address ...    Press RETURN" prompt.

                          N                  o  Type N and Smart Mailer  displays  the  Specify  an
                     Address ID screen so you can choose another Primary
                     or Alternate ID.




                                               ENDIf you are finished updating addresses,  type  END  at  the  Specify  an
Address ID screen and Smart Mailer displays the Update Menu.

                                            ENDIf you want to terminate Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-18


3.2.3  Displaying an Address

Sometimes you may want to  display  an  address  in  your  mailing  list
without changing any information.

                            DTo display an address, type D at  the  "Select option:"  prompt  of  the
Update  Menu.   Smart  Mailer displays the Specify an Address ID screen.
Refer to the "SPECIFY AN ADDRESS ID"  section  of  this  chapter  for  a
display and details of this screen.

After you specify the Primary or Alternate ID of the address you want to
display,  Smart Mailer displays the "Display" an Address screen as shown
in Figure 3-5.


------------------------------------------------------------------------

Display


  1 Name:               John Doe
  2 Address line 1:     10 Ruth Rd.
  3         line 2:
  4         line 3:
  5 City/Town:          Hudson
  6 State/Country:      MA
  7 Zip code:           01749

  8 Occupation:         Plant Mgr.
  9 undefined
 10 undefined
 11 undefined
 12 undefined
 13 undefined
 14 Counter:            0
 15 Remarks:

 16 Primary ID:         3               <--- selected by
 17 Alternate ID:       DOE  JOHN


When through with address ...                         Press RETURN

------------------------------------------------------------------------

Figure 3-5:  Display an Address ScreenFigure 3-5:  Display an Address Screen


                                                    <RETURN>When you are through reading  the  address,  press  <RETURN>  and  Smart
Mailer  displays  the  Specify  an  Address  ID  screen again so you can
display another address.

                                            ENDIf you want to terminate Smart Mailer, type END at each screen displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-19


3.2.4  Removing an Address

Periodically cleaning up your mailing list enables Smart Mailer to  work
more efficiently.  Whenever you can, remove obsolete addresses from your
list with this option.

                           RTo remove an address, type R  at  the  "Select option:"  prompt  of  the
Update Menu.

Smart Mailer requires that you type the Primary ID associated  with  the
address.   Typing  the  Primary  ID  ensures that the correct address is
removed because every Primary ID is unique.  Refer to Figure 3-6  for  a
display of the Remove an Address screen.


------------------------------------------------------------------------

                        Remove an Address






     Enter the Primary ID of the address you want to remove,
     or type END to return to the Update Menu:

------------------------------------------------------------------------


Figure 3-6:  Remove an Address ScreenFigure 3-6:  Remove an Address Screen


You can perform one of the following actions:

              END      o  Type END to return to the Update Menu.

      o  Type the complete Primary  ID  for  the  address  you  want  to
         remove.

If you specify a Primary ID that does not exist, Smart Mailer displays a
message stating the address does not exist and reprompts you for another
Primary ID.

Updating Mailing List AddressesUpdating Mailing List Addresses                                Page 3-20


If you specify a Primary ID  that  exists,  Smart  Mailer  displays  the
address associated with that Primary ID and the following prompt:

      -  Type REMOVE to delete this address:

         You may perform one of the following actions:

                  REMOVE     remove          o  Type REMOVE (or remove) to  delete  the  address  from  the
             mailing list.

             Smart Mailer displays a message confirming that the address
             has  been  removed  and then displays the Remove an Address
             screen again.

          o  Type anything other than 'REMOVE' (or 'remove')  and  Smart
             Mailer will NOT remove the address.

             Smart Mailer displays a message warning  that  the  address
             has  not  been  removed  and  then  displays  the Remove an
             Address screen again.


The following example discusses how to remove John  Doe's  address  from
the mailing list.

To remove John Doe's address, follow these steps:

              3     1.  Type 3.

              REMOVE     2.  Type REMOVE.

If you have more addresses to delete from the mailing list,  go  through
                                                    ENDthe  same  procedure  as  above.   Otherwise,  type END to return to the
Update Menu.

                                             ENDIf you are finished using Smart Mailer, type END at each menu  displayed
until  Smart  Mailer  returns  you  to  monitor  level  where the system
displays the system prompt.






                               Chapter 4
                           Sublist Definition



This section describes the  use  of  sublist  definitions  within  Smart
Mailer.   Smart Mailer allows you to maintain one or more mailing lists,
each contained within a Mailing List File.  You can think of these lists
as master lists from which sublists can be selected.

   sublistA  sublist  is  a  set  of  names  and  addresses  that   meet   certain
qualifications.   For  example, if you had a mailing list that contained
all the names of the subscribers to your magazine, then you could select
all those people whose subscription is ending next month.  This could be
done by setting up your mailing list with a category called 'ExpireDate'
which  indicates when their subscription expires.  Then you can instruct
Smart Mailer to select all people  whose  'ExpireDate'  is  between  the
first  day  of  next month and the last day of next month, and print out
labels for them.

Each name chosen from the mailing list for the sublist must meet  a  set
                                                                 sublistof requirements.  This set of requirements is referred to as the sublist
definitiondefinition.  For  example,  if  the  mailing  list  is  a  list  of  all
employees,  and the sublist is the list of all people eligible to retire
this year, then the sublist definition may consist of two requirements -
that each person is 55 or older, and has been employed for 10 years.

Smart Mailer does NOT remove the names selected from  the  mailing  list
for  the  sublist.   Each  time  the  sublist is requested, Smart Mailer
examines every name in the Mailing List File to determine  if  it  meets
the  requirements.  Then it copies the necessary information and uses it
for whatever function you have chosen.  So every time  you  choose  that
same  sublist,  the  names and addresses in that sublist reflect all the
changes made to the master list.

The Main Menu offers you the sublist definition function  -  to  create,
remove,  display,  update,  or  show  sublist definitions.  Smart Mailer
stores all sublist definitions  with  the  corresponding  mailing  list.
This  means  that  the  definition  can  be used repeatedly to select an
updated copy of the sublist.

Sublist DefinitionSublist Definition                                              Page 4-2


When you want to use a sublist (as opposed to dealing with  the  sublist
definition),  you  should  choose  whatever function you want to perform
with that sublist.  For example, if you want to print out a list of  all
potential  retirees,  then  you choose the Print function.  Smart Mailer
then asks if you want to print  the  entire  mailing  list,  or  just  a
sublist.   This  choice  is  also  available  from  the Display and Word
Processor List Document creation options from the Main Menu.

4.1  Sublist Definition Format

The Sublist Definition format is as follows:

    FIELD NAME    COMPARISON    VALUE(S)

Examples:

    JOB TITLE         IS        TEACHER
    HIRE DATE       BETWEEN     01-JAN-73 AND 31-DEC-73
    SALARY         NOT BELOW    $20,000

For more detailed examples, refer to Section 10.2

Field NamesField Names

Fields are names of data against which you can  compare  values;.   They
include  standard address fields such as Primary or Alternate ID and zip
code, as well as user-defined categories, such as Job Title.

Specify the name of the field that contains data  you  want  to  compare
against.

ComparisonsComparisons

Comparisons determine how Smart Mailer compares the information  in  the
specified  field of each address to the specified VALUE.  Refer to Table
4-1 for a list of all possible comparisons.

Sublist DefinitionSublist Definition                                              Page 4-3


Table 4-1:  List of ComparisonsTable 4-1:  List of Comparisons


                        Mathematical
Comparison              Definition              Meaning

IS (Default)            Field = Value           When you use IS, the
                                                system rejects any 
                                                address that has
                                                information in that
                                                field that is not equal
                                                to the value you type.

                              /IS NOT                  Field = Value           When you use IS NOT, the
                                                system accepts all 
                                                addresses that do not
                                                contain the value you
                                                type.

ABOVE                   Field > Value           When you use ABOVE, the
                                                system accepts values
                                                starting with the next
                                                number or letter.

                              _NOT ABOVE               Field < Value           When you use NOT ABOVE,
                                                the system accepts all
                                                values up to, and
                                                including the stated
                                                value.

BELOW                   Field < Value           When you use BELOW, the
                                                accepts all values up
                                                to, but NOT including
                                                the stated value.

                              _NOT BELOW               Field > Value           When you use NOT BELOW,
                                                the system accepts all
                                                values above, and 
                                                including the stated
                                                value.

                               _       _BETWEEN                 Value1 < Field < Value2 When you use BETWEEN,
                                                the system selects all
                                                values between the two
                                                values, including those
                                                values stated.

NOT BETWEEN             Field < Value1          When you use NOT
                              or                BETWEEN, the system
                        Field > Value2          selects values either
                                                below the first value
                                                or above the second
                                                value.

Sublist DefinitionSublist Definition                                              Page 4-4


ValuesValues

Smart Mailer uses user-specified values to test  the  contents  of  each
address.   Smart  Mailer  performs  this  test  for  each address in the
mailing list.

Values can be alphanumeric (A), numeric (N), date  (D),  or  yes/no  (Y)
fields  depending  on  the  field  name.   In the case of category field
names, you define the data type (A, N, D, Y) during initialization.

ConnectorsConnectors

Connectors relate one requirement with the next.  There are two types of
connectors:  AND, OR.  Smart Mailer asks you to specify a connector when
you want two or more conditions to be met.

AND

The AND connector sets forth more than one condition  that  the  address
must  meet before it is included in the sublist.  For example, ALTERNATE
           ANDID BELOW N AND ZIP CODE IS 02199 would yield a  sublist  of  all  people
with  names  starting  with  a  letter  between  A  and M, who live in a
particular area of Boston.

AND is the default connector.

OR

The OR connector sets forth either/or conditions  that  an  address  may
                                                                      ORmeet  before it is included in the sublist.  For example, STATE IS MA OR
            ORSTATE IS NH OR STATE IS ME would yield a sublist of people who  live  in
either Massachusetts, New Hampshire or Maine.

When a sublist definition has three or more conditions, you can  specify
                                                      ANDboth  connectors.   For  example, SAT SCORE ABOVE 600 AND GRADE AV ABOVE
    OR3.0 OR PARENT IS ALUMNA, would yield all prospective students with  good
scores, and all children of alumnae regardless of their qualifications.

Sublist DefinitionSublist Definition                                              Page 4-5


4.2  Walk Through

This section describes the flow through Smart Mailer  for  dealing  with
sublist  definitions,  showing each screen, describing the logical flow,
and explaining any questions, prompts, or messages that have not already
been explained in the previous sections.

This section of Smart Mailer assumes that you have already  logged  onto
the  system,  read  the  instruction  screen,  entered  the name of your
mailing list, and the Main Menu is displayed.   If  you  have  not  done
this, refer to Chapter 1, Sections 1.5 through 1.5.4.

To  create,  update,  print,  display,  remove  or  show   all   sublist
definition(s),  type  S at the "Select option:" prompt of the Main Menu.
The Sublist Definition Menu is displayed as shown in Figure 4-1.


------------------------------------------------------------------------

                        Sublist Definition Menu


              U    =   Update (or create) a sublist definition

              P    =   Print a sublist definition

              D    =   Display a sublist definition

              R    =   Remove a sublist definition

              S    =   Show all sublist definitions


              END      Return to the Main Menu



                       Select option:

------------------------------------------------------------------------


Figure 4-1:  Sublist Definition MenuFigure 4-1:  Sublist Definition Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

Sublist DefinitionSublist Definition                                              Page 4-6


You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages  for  the  Sublist  Definition
         Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (U).

      o  Type the letter associated with the option you want to perform.

The following sections discuss these options in detail.



4.2.1  Creating a Sublist Definition

                                     UTo create a sublist definition, type U at the "Select option:" prompt of
the  Sublist  Definition Menu.  Smart Mailer prompts you for the name of
your sublist as shown in Figure 4-2.

If you choose a sublist that does not exist, Smart  Mailer  assumes  you
want to create a new sublist.

If you want to create a sublist just for  the  duration  of  your  Smart
Mailer  session,  you  may  do  so by creating a Temporary Sublist.  The
mechanics of defining the sublist are the same.  The only difference  is
in naming the sublist.


------------------------------------------------------------------------

                Enter the name for this sublist:

------------------------------------------------------------------------


Figure 4-2:  Naming Your Sublist ScreenFigure 4-2:  Naming Your Sublist Screen


Sublist DefinitionSublist Definition                                              Page 4-7


You may perform one of the following actions:

              END      o  Type END to go back to the Sublist Definition Menu.

               <RETURN>      o  Press <RETURN> to create a temporary sublist.

         Smart Mailer takes the  <RETURN>  key  to  mean  Temporary  and
         displays  the  Sublist  Definition  screen  with  the  name  of
         "Temporary".

         After you terminate the Smart Mailer session, you cannot recall
         the Temporary sublist definition.  Because of the nature of the
         temporary sublist definition, you  can  only  specify  one  per
         Smart Mailer session.

      o  Type the name of a sublist you want to create.

         Smart Mailer displays the Sublist Definition  screen  with  the
         sublist name you specified.

For example,  to  create  a  sublist  definition  named  Marlboro,  type
MARLBOROMARLBORO.   Smart Mailer displays the Sublist Definition screen as shown
in Figure 4-3.


------------------------------------------------------------------------

                          Sublist Definition
                          name: MARLBORO
      FIELD NAME                                       COMPARISON

 1 = Primary ID     11 = Name                          a =  is
 2 = Alternate ID   12 = Addr line 1                   b =  is not
 3 = Counter        13 = Addr line 2                   c =  above
 4 = Zip code       14 = Addr line 3                   d =  not above
 5 = Occupation     15 = City/town                     e =  below
 6 = undefined      16 = State/country                 f =  not below
 7 = undefined                                         g =  between
 8 = undefined                                         h =  not between
 9 = undefined
10 = undefined
------------------------------------------------------------------------

                Select a FIELD NAME (1-16):


------------------------------------------------------------------------


Figure 4-3:  Sublist Definition ScreenFigure 4-3:  Sublist Definition Screen


Sublist DefinitionSublist Definition                                              Page 4-8


Note "MARLBORO"  next  to  "name:"  is  the  name  of  the  sublist  you
specified.  If you created a temporary sublist (pressed <RETURN> for the
sublist name), "TEMPORARY" is displayed next to "name:".

When the Sublist Definition screen is displayed, Smart  Mailer  displays
the following prompts one at a time:

      -  Select a FIELD NAME (1-16):

         Type the number associated with the FIELD NAME that you want to
         define.

      -  Select a COMPARISON (a-h):

         Type the letter associated with the COMPARISON that you want to
         make.

      -  Specify a value for comparison:

         Type the value you want to compare.  Type  two  values  if  the
         comparison that you chose is 'between' or 'not between'.

For example, to create a sublist definition with all addresses that have
a  zip  code of 01752 (Marlboro zip code) and an Occupation of Engineer,
follow these steps:

              4     1.  Type 4.

               <RETURN>     2.  Press <RETURN> to accept the default answer (a = is).

              01752     3.  Type 01752.

The following is a sample  of  the  sublist  definition  line  you  just
created.

line  1:           Zip code     is      01752

Sublist DefinitionSublist Definition                                              Page 4-9


After you define the first line of the sublist definition, the following
prompts are displayed:

      -  Select the number of the line to add/update/remove:
         (or type END to terminate the definition)

         Smart Mailer displays the next sequential line  number  as  the
         default  because  it  assumes  you  want to add another sublist
         definition line.

         Creating a sublist definition is like creating an address - you
         can  also update it at the same time.  Refer to the "Updating a
         Sublist  Definition"  section  for  details  on  updating   and
         removing a sublist definition line.

                  END          o  Type END if you are finished with this  sublist  definition
             and  Smart  Mailer  returns  you  to the Sublist Definition
             Menu.

                   <RETURN>          o  Press <RETURN> to  accept  the  default  answer  (add  next
             sublist definition line) and Smart Mailer displays the next
             prompt.


      -  Select a word to connect to the next line (AND/OR):

         Smart Mailer displays "AND" as the default for this prompt.

         This prompt connects one sublist  definition  line  to  another
         sublist definition line.  Choosing AND means the next condition
         MUST be met.  Choosing OR means the next condition MAY be met.

         You can perform one of the following actions:

                   <RETURN>          o  Press <RETURN> to accept the default answer (AND).

                  OR          o  Type OR.

         Smart Mailer then asks you to define another sublist definition
         line.  Define the next sublist definition line by answering all
         the prompts as you did previously.

               END         Type  END  at  the  "Select  the  number   of   the   line   to
         add/update/remove:"  prompt when you are done to go back to the
         Sublist Definition Menu.


Sublist DefinitionSublist Definition                                             Page 4-10


For example, you already defined sublist definition line 1 (zip code  is
01752).   Now  you  can  define sublist definition line 2 (Occupation is
Engineer).  To define the occupation line, follow these steps:

               <RETURN>     1.  Press <RETURN> to accept the default line number (2).

               <RETURN>     2.  Press <RETURN> to accept the default connector (AND).

              5     3.  Type 5 for Occupation.

               <RETURN>     4.  Press <RETURN> to accept the default comparison (a = is).

              Engineer     5.  Type Engineer.

You have just created a sublist definition that will  extract  addresses
in  your mailing list that have a zip code of 01752 and an Occupation of
Engineer.

The following is a display of the sublist definition you just created.

line  1:           Zip code     is      01752
line  2:     and Occupation     is      ENGINEER

Smart Mailer displays up to 6 lines of sublist definitions and then  the
screen  scrolls  either up or down depending on what line you are at and
what line you want to display (e.g., if you  have  7  lines  of  sublist
definitions and you are currently at line 7, the screen displays lines 2
through 7.  If you want to display line 1 when you are at line 7, type 1
at  the "Select the number of the line to add/update/remove:" prompt and
the screen displays lines 1 through 6).  You may have up to 30 lines  of
sublist requirements for one sublist.

If you continue using Smart Mailer and you choose the Sublist Definition
Menu  option  again  from  the  Main  Menu, Smart Mailer defaults to the
current sublist when the "Enter the name for this  sublist:"  prompt  is
redisplayed.   Press  <RETURN>  to  accept  the default sublist or enter
another sublist name.  If you press <RETURN> when  the  default  sublist
name  is  displayed,  it  assumes  that you want to do something (print,
update, display) to that sublist.  If you want  to  create  a  temporary
                                                               TEMPORARYsublist and the name of an existing sublist is displayed, type TEMPORARY
at the "Enter the name of this sublist:" prompt.

                                            ENDIf you are finished with Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Sublist DefinitionSublist Definition                                             Page 4-11


4.2.2  Updating a Sublist Definition

You can change a sublist definition by adding, updating, or  removing  a
sublist  definition  line.   One  line  represents  one  requirement  or
condition to be met.

                                                              UTo add, update, or remove a sublist  definition  line,  type  U  at  the
"Select  option:"  prompt  of the Sublist Definition Menu.  Smart Mailer
prompts you for the name of the sublist.

Once the sublist  name  is  typed,  the  Sublist  Definition  screen  is
displayed (Figure 4-4).

The following is an example of the sublist you defined in  the  previous
section.


------------------------------------------------------------------------

                          Sublist Definition
                          name: MARLBORO
      FIELD NAME                                       COMPARISON

 1 = Primary ID     11 = Name                          a =  is
 2 = Alternate ID   12 = Addr line 1                   b =  is not
 3 = Counter        13 = Addr line 2                   c =  above
 4 = Zip code       14 = Addr line 3                   d =  not above
 5 = Occupation     15 = City/town                     e =  below
 6 = undefined      16 = State/country                 f =  not below
 7 = undefined                                         g =  between
 8 = undefined                                         h =  not between
 9 = undefined
10 = undefined
------------------------------------------------------------------------
line  1:           Zip code     is      01752
line  2:       and Occupation   is      ENGINEER


        Select the number of the line to add/update/remove: 3
        (or type END to terminate the definition)

------------------------------------------------------------------------


Figure 4-4:  Example - Sublist Definition Update ScreenFigure 4-4:  Example - Sublist Definition Update Screen


Note "MARLBORO" next to "name:" is the sublist name you specified.   The
next  sequential  number  is  displayed  as  the default for this prompt
because Smart Mailer assumes you want to add another sublist  definition
line.   Refer  to  the  previous  section  for details on adding another
sublist definition line.

Sublist DefinitionSublist Definition                                             Page 4-12


You can perform one of the following actions:

              END      o  Type END to go back to the Sublist Definition Menu.

              ?      o  Type ?  to display a one line help message for this prompt.

               <RETURN>      o  Press <RETURN> to add the next sublist definition line.

      o  Type the number of the sublist  definition  line  you  want  to
         update, add, or remove.

If you have two or more sublist definition lines and  you  type  a  line
number  that exists, Smart Mailer assumes that you want to either update
or remove that line and displays the following prompt:

      -  Type REMOVE to remove the line; or press RETURN to update it.

         You can perform one of the following actions:

                   <RETURN>          o  Press <RETURN> and  Smart  Mailer  displays  the  following
             prompts  with  the  previously  assigned  values  for  that
             sublist definition line.

              -  Select a word to connect to the next line (AND/OR):

                 This prompt is not displayed if you  select  the  first
                 line (which does not have a connector).

              -  Select a FIELD NAME (1-16):

              -  Select a COMPARISON (a-h):

              -  Specify value(s) for comparison.

                 You may  change  any  of  the  defaults  by  specifying
                 different  values  for each prompt or press <RETURN> at
                 each prompt to accept the defaults.


                  REMOVE     remove          o  Type REMOVE (or remove) and Smart Mailer clears the sublist
             definition  line  specified  and  displays  the "Select the
             number of the line to add/update/remove:" prompt.   If  you
             remove  a line, Smart Mailer erases that line and moves any
             subsequent lines up.

         You can add, update, or remove another sublist definition  line
         by going through the same procedure.


Sublist DefinitionSublist Definition                                             Page 4-13


                                  NOTE

        If you have only one sublist  definition  line  and  you
        type  1  at  the  "Select  the  number  of  the  line to
        add/update/remove:" prompt, Smart  Mailer  assumes  that
        you  want  to  update that line and does not display the
        "Type REMOVE to remove the  line;  or  press  RETURN  to
        update it" prompt.  This is because you may not remove a
        sublist definition with the Update option.  You must use
        the "Remove a Sublist Definition" option.

As an example of updating a  sublist  definition,  you  have  a  sublist
definition  (MARLBORO)  that  extracts people in the mailing list with a
                  andzip code of 01752 and Occupation of Engineer.  Now you decide  you  want
                                                        orall people in the mailing list with a zip code of 01752 or an Occupation
of Engineer.

You will not have to update the first sublist  definition  line  because
the  zip  code  is  not changing, but you will have to change the second
sublist definition line because you have to change the connector  value.
To do this, follow these steps:

              2     1.  Type 2 and press <RETURN> to update.

              OR     2.  Type OR.

                <RETURN>     3.  Press  <RETURN>  to  accept  the  default  answer  (FIELD  NAME
         "Occupation").

               <RETURN>     4.  Press <RETURN> to accept the default answer (COMPARISON "is").

               <RETURN>     5.  Press <RETURN> to accept the default answer ("ENGINEER").

Now you have a sublist definition that will extract all  people  in  the
mailing  list  who  live  in  Marlboro  (regardless  of  occupation) and
everyone who is an Engineer (regardless of where they live).

You may update, add or remove another sublist definition line  by  going
                                    ENDthrough  the same procedure or type END at the "Select the number of the
line to add/update/remove:" prompt to go back to the Sublist  Definition
Menu.

                                            ENDIf you are finished with Smart Mailer, type END at each screen displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Sublist DefinitionSublist Definition                                             Page 4-14


4.2.3  Printing a Sublist Definition

After you have defined a couple of sublists, you might want to print the
sublist  definitions  so  that  you  have  a  listing as a guideline for
creating new sublist  definitions,  or  to  store  with  the  associated
sublist listing.

                                    PTo print a sublist definition, type P at the "Select option:" prompt  of
the  Sublist  Definition Menu.  Smart Mailer prompts you for the name of
the sublist.

Once you have entered the name of the sublist, Smart Mailer displays the
Output  Device  Menu.  Refer to Section 1.4.2 for a complete description
of the Output Device Menu.

If you specify the name of a sublist that does not exist,  Smart  Mailer
displays  a message stating that the sublist name does not exist.  Smart
Mailer then reprompts you for another sublist name.

The listing will be printed on the device you selected.  However, if you
requested  a disk file, the listing will be created on disk but will NOT
be printed.  You may print a disk file like you would any other file.

Smart Mailer then returns to the Sublist Definition  Menu  and  you  can
choose another option.

                                            ENDIf you are finished with Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Sublist DefinitionSublist Definition                                             Page 4-15


4.2.4  Displaying a Sublist Definition

After you have defined a couple of sublists, you might want to display a
sublist  definition  so  you  can  see what sublist definition lines you
have.

                                      DTo display a sublist definition, type D at the "Select option:"  of  the
Sublist  Definition  Menu.  Smart Mailer prompts you for the name of the
sublist.

Once the name  is  typed,  the  Sublist  Definition  Display  screen  is
displayed  (Figure  4-5).   The  following  is an example of the sublist
definition you defined in the previous sections.


------------------------------------------------------------------------

                          Sublist Definition

Sublist name:  MARLBORO                         Date:  27-JAN-83
Mailing List:  RESUME.MLF                       Time:  15:33


line  1:           Zip code     is      01752
line  2:        or Occupation   is      ENGINEER






When through reading the display ...                    Press RETURN

------------------------------------------------------------------------


Figure 4-5:  Example - Sublist Definition Display ScreenFigure 4-5:  Example - Sublist Definition Display Screen


If you specify the name of a sublist that does not exist,  Smart  Mailer
displays  a message stating that the sublist name does not exist.  Smart
Mailer then reprompts you for another sublist name.

If the sublist definition has more than 16 lines, Smart Mailer will show
you  the  first  16 lines then wait for you to read them before clearing
the screen to show you the rest of the definition.

      <RETURN>Press <RETURN> when you are finished viewing the sublist definition  and
Smart  Mailer  returns  to the Sublist Definition Menu so you can choose
another option.

                                            ENDIf you are finished with Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Sublist DefinitionSublist Definition                                             Page 4-16


4.2.5  Removing a Sublist Definition

                                     RTo remove a sublist definition, type R at the "Select option:" prompt of
the  Sublist  Definition Menu.  Smart Mailer prompts you for the name of
the sublist.

Once the sublist  name  is  typed,  the  Sublist  Definition  screen  is
displayed  (Figure  4-6).   The  following  is an example of the sublist
definition you defined in the previous sections.


------------------------------------------------------------------------

                          Sublist Definition

Sublist name:  MARLBORO                         Date:  27-JAN-83
Mailing List:  RESUME.MLF                       Time:  15:33


line  1:           Zip code     is      01752
line  2:        or Occupation   is      ENGINEER







When through reading the display ...                    Press RETURN

------------------------------------------------------------------------


Figure 4-6:  Example - Sublist Definition Remove ScreenFigure 4-6:  Example - Sublist Definition Remove Screen


Note "MARLBORO" next to "Sublist name:" is the name of the  sublist  you
specified and "RESUME.MLF" is the name of your mailing list.

If you specify the name of a sublist that does not exist,  Smart  Mailer
displays  a message stating that the sublist name does not exist.  Smart
Mailer then reprompts you for another sublist name.

Sublist DefinitionSublist Definition                                             Page 4-17


                                                       <RETURN>When you have read the sublist definition lines, press <RETURN> and  the
following prompt is displayed:

      -  Type REMOVE to delete this sublist definition:

         You can perform one of the following actions:

                  REMOVE     remove          o  Type REMOVE (or remove) to delete  the  sublist  definition
             and  Smart  Mailer  displays  a message confirming that the
             sublist definition has been  removed.   Smart  Mailer  then
             returns to the Sublist Definition Menu.

          o  Type anything other than 'REMOVE' (or 'remove')  and  Smart
             Mailer  will not remove the sublist definition and displays
             the following message:

              -  The sublist definition will NOT be removed Press RETURN

                           <RETURN>                  o  Press <RETURN> and  Smart  Mailer  returns  to  the
                     Sublist  Definition Menu and you may choose another
                     option.




                                            ENDIf you are finished with Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Sublist DefinitionSublist Definition                                             Page 4-18


4.2.6  Show All Sublist Definitions

Occasionally you might want to display all  sublist  definitions  for  a
particular mailing list so you can see what sublist definition lines you
have defined for each sublist definition.

                                                              STo show all sublist definitions for  a  mailing  list,  type  S  at  the
"Select option:" prompt of the Sublist Definition Menu.

The following screen is displayed:


------------------------------------------------------------------------

                        Display of all Sublist Definitions
                        for Mailing List File:  RESUME.MLF







                                                        Press RETURN

------------------------------------------------------------------------


Figure 4-7:  Show All Sublist Definitions ScreenFigure 4-7:  Show All Sublist Definitions Screen


Note that "RESUME.MLF" is the name of your mailing list.

      <RETURN>Press <RETURN> and Smart Mailer displays the  first  sublist  definition
for  the  mailing  list  you  specified.   They  will  be  shown, sorted
alphabetically by sublist name.

This option displays the sublist definition screen the same way  as  the
Display  option  except  you do not have to keep specifying each sublist
definition name.

                                                    <RETURN>Once you have read one sublist  definition,  press  <RETURN>  and  Smart
                                    <RETURN>Mailer  displays  another.   Press  <RETURN>  after reading each sublist
definition until there are no more.

             ENDYou may type END if you do  not  want  to  continue  displaying  sublist
definitions and Smart Mailer returns to the Sublist Definition Menu.

When Smart Mailer reaches  the  end  of  your  sublist  definitions,  it
returns  to  the  Sublist  Definition  Menu  and  you can choose another
option.

Sublist DefinitionSublist Definition                                             Page 4-19


If you do not have any sublist definitions for the mailing  list,  Smart
Mailer displays the following message:

   There are no sublist definitions for this Mailing List.  Press RETURN

      <RETURN>Press <RETURN> and Smart Mailer returns to the Sublist Definition Menu.

                                            ENDIf you are finished with Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.






                               Chapter 5
                  Displaying a Mailing List or Sublist



This chapter describes how to display addresses on the terminal  screen.
When  Smart  Mailer  displays addresses on the screen, it only shows you
certain address fields.  This is done to display one address  per  line,
in  a  condensed format for easy viewing.  For a complete listing on the
entire contents of each  address,  including  category  information  and
comments, you can request that the addresses be printed.

You may choose to display the entire mailing list, or just a portion  of
the  mailing  list  (a  sublist).   If  you  just  want  a  sublist, the
definition of the sublist requirements should already  exist  (refer  to
Chapter 4, Sublist Definition).

Difference Between Displaying and Printing AddressesDifference Between Displaying and Printing Addresses

When displaying addresses, you are offered the  choice  of  sorting  the
addresses by Primary or Alternate ID.  Both of these sorts are done very
quickly, so that you will not have to wait long  to  see  the  addresses
displayed.

Displaying allows you to see what addresses are in  a  mailing  list  or
sublist.   You  may  want  to  display  a mailing list or sublist before
printing them to make sure you will be printing the  correct  addresses.
The  format  of  the  display will match the format of a short printout.
That is, only the Primary and Alternate ID's, the name, state,  and  zip
codes will be displayed.

Printing a mailing list or sublist allows  you  to  print  addresses  on
labels  or  paper.   You  may  print  the  contents of a mailing list or
sublist to see  what  addresses  and  Primary  and  Alternate  ID's  are
associated  with  that  mailing list.  This helps when you want to print
addresses on labels but do not know the ID's  of  the  addresses.   When
printing  a  mailing  list  or  sublist, you are offered more choices of
sorting your addresses.  For more details on printing, refer to  Chapter
6.

Displaying a Mailing List or SublistDisplaying a Mailing List or Sublist                            Page 5-2


5.1  Walk Through

This section describes the flow through Smart Mailer  for  displaying  a
mailing  list  or  sublist,  showing each screen, describing the logical
flow, and explaining any questions, prompts, or messages that  have  not
already been explained in the previous sections.

This section of Smart Mailer assumes that you have already  logged  onto
the  system, read the instruction screen, typed the name of your mailing
list, and the Main Menu is displayed.  If you have not done this,  refer
to Chapter 1, Sections 1.5 through 1.5.4.

                                                        DTo display addresses in a mailing list or sublist, type D at the "Select
option:"  prompt of the Main Menu.  The List Selection Menu is displayed
as shown in Figure 5-1.


------------------------------------------------------------------------

                         List Selection Menu


                  A  =   All addresses in a mailing list

                  S  =   Sublist name:

                  T  =   Temporary sublist

                  END    Return to the previous menu


                         Select option:

------------------------------------------------------------------------


Figure 5-1:  List Selection MenuFigure 5-1:  List Selection Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the List Selection Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (A).

      o  Type the letter associated with the option you want to perform.


Displaying a Mailing List or SublistDisplaying a Mailing List or Sublist                            Page 5-3


                                           STo display a sublist of  addresses,  type  S  at  the  "Select  option:"
prompt.  The cursor will be positioned after the "Sublist name:" prompt.
Type the name of your sublist (MARLBORO).

If you do not have  an  existing  sublist,  Smart  Mailer  displays  the
following message:

        Sublist xxx does not currently exist.
        Do you wish to go back to create that sublist definition (Y/N)?

You can perform one of the following actions:

               Y      o  Type  Y  to  create  that  sublist  definition.   Smart  Mailer
         displays  the  Sublist Definition Menu.  Refer to Chapter 4 for
         more details on sublist definitions.

              N      o  Type N and Smart Mailer returns to the List Selection Menu.

                                                     TTo display a temporary sublist of  addresses,  type  T  at  the  "Select
option:"  prompt.   If  a temporary sublist does not exist, Smart Mailer
displays a similar message to  above.   Refer  to  Chapter  4  for  more
details on sublist definitions.

Displaying a Mailing List or SublistDisplaying a Mailing List or Sublist                            Page 5-4


After you select the type of list, Smart Mailer displays the  Sort  Menu
as shown in Figure 5-2.


------------------------------------------------------------------------

                                  Sort Menu



Sort mailing list by ...


                 P   =   Primary ID

                 A   =   Alternate ID


                 END     Return to the previous menu



                         Select option:

------------------------------------------------------------------------


Figure 5-2:  Display Sort MenuFigure 5-2:  Display Sort Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the Sort Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (P).  Smart  Mailer
         sorts the addresses by Primary ID.

              A      o  Type A to sort the addresses by Alternate ID.

Smart Mailer displays the following message while it  is  selecting  the
addresses:

        working ... please wait.

Displaying a Mailing List or SublistDisplaying a Mailing List or Sublist                            Page 5-5


When Smart Mailer displays the addresses, it will look similar to Figure
5-3.


------------------------------------------------------------------------

                        Short Address Listing


Sublist Name:  MARLBORO                         Date:  07-FEB-83
Mailing List:  RESUME.MLF                       Time:  09:13
Sorted by:     Primary ID

Primary ID      Alter. ID       Name               State   ZIP Code
--------------- --------------- ---------------    ------- ---------

         1      FULLEROBER      Robert Fuller      MA      01752







        Task completed, total selected addresses = 1

        When through reading the display ...           Press RETURN

------------------------------------------------------------------------


Figure 5-3:  Example - Display of Addresses Sorted by Primary IDFigure 5-3:  Example - Display of Addresses Sorted by Primary ID


Smart Mailer displays the Sublist  name  (e.g.,  MARLBORO)  if  'S'  was
specified  in  the List Selection Menu.  If 'S' was not specified, Smart
Mailer will not display the "Sublist name:".  Smart Mailer displays  the
Mailing List File name (e.g., RESUME.MLF), the date and time the mailing
list is displayed, and what type of sort was selected (i.e., Primary  or
Alternate  ID's).   Smart  Mailer displays the Primary ID, Alternate ID,
Name, State, and Zip Code for the addresses in the chosen  list.   Smart
Mailer  also  displays  the total number of addresses that were selected
when it reaches the end of the addresses.

Smart Mailer displays addresses one screen at a time.  If  you  want  to
see  more  addresses,  press  <RETURN>  and  Smart  Mailer displays more
addresses with the following column headings displayed  on  the  top  of
your terminal screen:

Primary ID      Alternate ID    Name            State   ZIP Code
--------------- --------------- --------------- ------- -------------

Displaying a Mailing List or SublistDisplaying a Mailing List or Sublist                            Page 5-6


                                                ENDYou can quit looking at the addresses by typing END at the "When through
reading  the  display ...  Press RETURN" prompt and Smart Mailer returns
to the Main Menu.

When Smart Mailer reaches the end of  the  addresses,  it  displays  the
message:

        Task completed, total selected addresses = n

        When through reading the display ...    Press RETURN

The "n" signifies a number of the total selected addresses.

When you are finished looking at your addresses, press <RETURN>.   Smart
Mailer returns to the Main Menu.

                                            ENDIf you are finished with Smart Mailer, type END at each  menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.






                               Chapter 6
                   Printing a Mailing List or Sublist



This chapter describes how to print the addresses on a  printing  device
using  paper  or labels.  For detailed information on printing addresses
on labels, refer to Section 10.3.  You can request a short listing which
contains  a  limited amount of information from each address (similar to
the display of addresses at the terminal).  Or, for a  complete  listing
of  the  entire contents of each address, including category information
and comments, you can request that the full address be printed.  If  you
request  labels,  then Smart Mailer prints only the name, address lines,
city/state/zip fields, and optionally one  other  piece  of  information
from  the  address  (Primary  ID,  Alternate  ID, counter, or a category
value).  It can also print a  special  message  across  all  the  labels
(e.g., Address Correction Requested).

You may choose to print the entire mailing list, or just  a  portion  of
the  mailing  list  (a  sublist).   If  you  just  want  a  sublist, the
definition of the sublist requirements should already  exist  (refer  to
Chapter 4, Sublist Definition).

When printing addresses, you are offered several choices of how to  sort
your  addresses.  Sorting addresses by Primary ID's or Alternate ID's is
relatively fast; any other sorting will take longer.  One of the sorting
options  is  to  sort  the addresses according to rules published by the
Post Office (PRESORT) to qualify for lower postal rates.

You may be given several choices for printing devices.  The choices  are
dependent  on  your particular computer system.  Refer to the section on
"Choosing an Output Device" in the first chapter for more information.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-2


6.1  Sorting a Mailing List

You can sort your selected addresses  on  any  one  of  several  address
fields.   In  addition,  the  PRESORT  algorithm  enables  you  to  sort
according to Post Office rules  to  qualify  for  special  bulk  mailing
rates.  Refer to Section 10.1 for more details.

When sorting, Smart Mailer puts fields beginning  with  <SPACES>  first,
then  numbers,  and  then letters (uppercase and lowercase).  For a more
complete definition of the sorting order, refer to Table 6-1.



Table 6-1:  Sorting OrderTable 6-1:  Sorting Order

        <SPACE>
        Special characters      (!"#$%&'()*+,-./)
        Digits                  (0123456789)
        Special characters      (:;<=>?@)
        Letters                 (A-Z)
        Special characters      ([\]^_`{|}~)

For example, these fields are sorted in Smart Mailer order.

        #5 Main St
        12 Main St
        926 Main St
        92A Main St
        Main St


If you are sorting on any parameter other than Primary or Alternate  ID,
the  sort  can  take a considerable amount of time depending on the size
and complexity of the mailing list or sublist.  However,  the  speed  of
sorting  large  and/or complex mailing lists or sublists is considerably
faster than the previous version of Smart Mailer.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-3


6.2  Walk Through

This section describes the flow through Smart Mailer  for  printing  all
addresses  in a mailing list or sublist, showing each screen, describing
the logical flow, and explaining any  questions,  prompts,  or  messages
that have not already been explained in the previous sections.

This section of Smart Mailer assumes that you have already  logged  onto
the  system, read the instruction screen, typed the name of your mailing
list, and the Main Menu is displayed.  If you have not done this,  refer
to Chapter 1, Sections 1.5 through 1.5.4.

                                           PTo print a mailing list or sublist,  type  P  at  the  "Select  option:"
prompt  of the Main Menu.  The List Selection Menu is displayed as shown
in Figure 6-1.

List SelectionList Selection


------------------------------------------------------------------------

                         List Selection Menu



                  A  =   All addresses in a mailing list

                  S  =   Sublist name:

                  T  =   Temporary sublist

                  END    Return to the previous menu



                         Select option:

------------------------------------------------------------------------


Figure 6-1:  List Selection MenuFigure 6-1:  List Selection Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-4


You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the List Selection Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (A).

      o  Type the letter associated with the option you want to perform.

                                      STo print a sublist of addresses, type S at the "Select option:"  prompt.
The  cursor  will  be positioned after the "Sublist name:" prompt.  Type
the name of your sublist (e.g., MARLBORO).

If you do not have  an  existing  sublist,  Smart  Mailer  displays  the
following message:

        Sublist xxx does not currently exist.
        Do you wish to go back to create that sublist definition (Y/N)?

You can perform one of the following actions:

               Y      o  Type  Y  to  create  that  sublist  definition.   Smart  Mailer
         displays  the  Sublist Definition Menu.  Refer to Chapter 4 for
         more details on sublist definitions.

              N      o  Type N and Smart Mailer returns to the List Selection Menu.

                                                     TTo print a temporary  sublist  of  addresses,  type  T  at  the  "Select
option:"  prompt.   If  a temporary sublist does not exist, Smart Mailer
displays a similar message to  above.   Refer  to  Chapter  4  for  more
details on sublist definitions.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-5


SortingSorting

After you have selected the the desired option from the  List  Selection
Menu, the Print Sort Menu is displayed as shown in Figure 6-2.


--------------------------------------------------------------------------------

                            Print Sort Menu

Sort mailing list by ...


       P   =  Primary ID                    C   =  Counter
       A   =  Alternate ID
                                            1   =  Occupation
       N   =  Name                          2   =  undefined
       L1  =  Address Line 1                3   =  undefined
       L2  =  Address Line 2                4   =  undefined
       L3  =  Address Line 3                5   =  undefined
       T   =  Town/City                     6   =  undefined
       S   =  State/Country                    
       Z   =  Zip Code                      PRE =  US Postal PRESORT sorting

                                            END =  Return to the previous menu



                            Select option:

--------------------------------------------------------------------------------


Figure 6-2:  Print Sort MenuFigure 6-2:  Print Sort Menu


Note that options "1 through 6" are the categories for the mailing list.

The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the previous menu.

              ?      o  Type ?  to display help messages for the Print Sort Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (P).

      o  Type the code(s) associated with the type of sort you  want  to
         perform.   You  can  specify  up to 3 sort keys.  Multiple sort
         options are separated by commas.   For  example,  if  you  type
         "T,1", the address will be sorted by Town/City, and within each
         Town/City by the information stored in Category 1.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-6


Provided that you meet certain qualifications set by  the  Post  Office,
you  can  presort  your  mail  and take advantage of lower postal rates.
Smart Mailer's PRESORT option makes the assumption that if you choose to
presort  that  you  want to print labels and does not display the Output
Format Menu.

After you choose PRESORT, Smart Mailer selects addresses  and  validates
their  state  zip  codes.   Note  that  you must use the two digit state
abbreviations  listed  in  Chapter  3,  Table  3-1  to  presort.    Only
U.S. addresses are eligible for the presorted postal rate.

After Smart Mailer finishes selection and validation,  it  displays  the
total  number  of  addresses,  listing  the  number  of valid as well as
invalid addresses.  For the invalid addresses, Smart  Mailer  lists  the
reasons  that  they  are  unacceptable  and  allows you to terminate the
PRESORT function.

For more information on PRESORT, refer to the "PRESORT" section of  this
chapter and Section 10.1.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-7


Output FormatOutput Format


After you type an option at the Print Sort Menu, Smart  Mailer  displays
the Output Format Menu as shown in Figure 6-3.

You may print a short or full listing of a  mailing  list,  sublist,  or
temporary sublist.  A short listing contains the following fields:

     o  Primary ID

     o  Alternate ID

     o  Name

     o  State/Country

     o  Zip Code

A full listing contains all fields, including  categories  and  comments
for a mailing list, sublist, or temporary sublist.


------------------------------------------------------------------------

                      Output Format Menu



                S  =  Short listing

                F  =  Full listing

                L  =  Label printing

                END   Return to the previous menu



                      Select option:

------------------------------------------------------------------------


Figure 6-3:  Output Format MenuFigure 6-3:  Output Format Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-8


You can perform one of the following actions:

              END      o  Type END to return to the previous menu.

              ?      o  Type ?  to display help messages for the Output Format Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (S).

      o  Type the letter associated with the type of listing you want to
         print.

After you type the letter associated with the type of listing you  want,
Smart Mailer displays the following prompt:

        Lines per page:  66

This new enhancement to Smart Mailer allows you to specify the number of
lines  per  page  when  requesting  Short  or  Full  listings or address
distribution reports.  If you select Label printing  (L),  Smart  Mailer
displays the Label Menu after the Output Device Menu.


Figure 6-4 is a sample printout of the short listing, sorted by  Primary
ID for all addresses in the "RESUME.MLF" mailing list.



                             Short Address Listing              Page   1 

                                                                Date:  08-Mar-83
Mailing List:  RESUME.MLF                                       Time:  10:01
Sorted by:     Primary ID


Primary ID       Alter. ID  Name                          State       Zip Code
---------------- ---------- ----------------------------- ----------- ----------

               1 FULLEROBER Robert Fuller                 MA          01752     
               2 FULLEROBER Roberta Fullerton             MA          01754     



Total printed addresses =  2



Figure 6-4:  Sample - Short ListingFigure 6-4:  Sample - Short Listing


Printing a Mailing List or SublistPrinting a Mailing List or Sublist                              Page 6-9


Figure 6-5 is a sample printout of the full listing, sorted  by  Primary
ID for all addresses in the "RESUME.MLF" mailing list.




                                                       Full Address Listing                                        Page   1 

                                                                                                                   Date:  08-Mar-83
Mailing List:  RESUME.MLF                                                                                          Time:  10:01
Sorted by:     Primary ID

                                                                  -------------------------- Categories ---------------------------
Primary ID        Name & Address                 Alter. ID  Count Occupation undefined  undefined  undefined  undefined  undefined
----------------  ------------------------------ ---------- ----- ---------- ---------- ---------- ---------- ---------- ----------

               1  Robert Fuller                  FULLEROBER     0 Engineer                                                         
                  14 River Rd.                  
                  Marlboro, MA   01752     

               2  Roberta Fullerton              FULLEROBER     0 Data Prep                                                        
                  146 Main St.                  
                  Maynard, MA   01754     



Total printed addresses =  2


Figure 6-5:  Sample - Full ListingFigure 6-5:  Sample - Full Listing


Printing a Mailing List or SublistPrinting a Mailing List or Sublist                             Page 6-10


Figure 6-6 is a sample of the labels printed, sorted by Primary  ID  for
all addresses in the "RESUME.MLF" mailing list.



Robert Fuller                    Roberta Fullerton                
14 River Rd.                     146 Main St.                     
Marlboro, MA   01752             Maynard, MA   01754              


Figure 6-6:  Sample - Label PrintingFigure 6-6:  Sample - Label Printing





Output DeviceOutput Device


------------------------------------------------------------------------

                       Output Device Menu




                D  =   Disk file output:

                1  =   Main Printer







                END =  Return to the previous menu



                       Select option:

------------------------------------------------------------------------


Figure 6-7:  Output Device MenuFigure 6-7:  Output Device Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                             Page 6-11


You can perform one of the following actions:

              END      o  Type END to return to the previous menu.

              ?      o  Type ?  to display help messages for the Output Device Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (D).

      o  Type the code associated with the type of printer you  want  to
         select.

When you choose a printer, Smart Mailer tells you what type of  printing
will  be  done.   If it gives you a message that the information will be
'sent to' the device, then it will print it directly.  If it  says  that
the  information will be 'queued to' the device, then it will send it to
the operating system to be printed when the printer is available.

You must wait  until  Smart  Mailer  indicates  it  is  ready  for  more
instructions before going on to anything else.  DO NOT turn the terminal
off, or try to log off.

After you specify the printer, Smart Mailer lets you know it is  working
by displaying the following message:

        generating listings... please wait.
or
        generating labels... please wait.

Note that the printing operation can take anywhere from a few seconds to
a  number  of hours depending on:  total number of addresses, percentage
of addresses meeting the sublist requirements, printer  speed,  type  of
listing, type of computer, and number of other computer users.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                             Page 6-12


PresortPresort

                                          PREThe PRESORT Menu is displayed if you type PRE from the Print  Sort  Menu
and  after  Smart  Mailer  sorts  the addresses by zip code and presorts
them, but before any labels are generated.  Figure 6-8 is  a  sample  of
the PRESORT Menu.


--------------------------------------------------------------------------------

                              PRESORT Menu

              A  210   Direct pieces
              B  360   City/SCF pieces
              C   43   Residual pieces
              D  570   pieces that qualify for lower postage rate (A+B)
              E  613   pieces that count toward the minimum       (A+B+C)
              F    7   pieces that are invalid for PRESORT


              1    =   Print all the addresses

              2    =   Print only valid addresses     (see E above)

              3    =   Print only invalid addresses   (see F above)


              END      Return to the Main Menu


                       Select option (1,2,3):

--------------------------------------------------------------------------------


Figure 6-8:  PRESORT MenuFigure 6-8:  PRESORT Menu


The cursor is positioned at the "Select option (1,2,3):" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the PRESORT Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (1).

      o  Type the number associated with the option you want to perform.

Refer to Section 10.1 for more details on PRESORT.

Printing a Mailing List or SublistPrinting a Mailing List or Sublist                             Page 6-13


Label PrintingLabel Printing

            L                              PREIf you type L at the Output Format Menu or PRE at the Print  Sort  Menu,
Smart Mailer displays the Label Menu.

Note that the defaults that appear on  your  display  are  set  by  your
System Manager, and therefore, may not match the display shown.  If your
company uses one standard label, use the default  values  and  continue.
If  you  do have to change the default values, note that your values are
valid for the duration of the Smart Mailer session.  As soon as you  end
the session, Smart Mailer defaults back to the System Manager's values.


--------------------------------------------------------------------------------

                              Label Menu

     1  =   Test print sample labels               Y
     2  =   Extra info on labels (P,A,C,1-6)
     3  =   Special label message
     4  =   Increase/Decrease/Reset counters
     5  =   Number to incr/dec/reset counters      0
     6  =   Number of copies of labels             1
     7  =   Number of labels across a page         2
     8  =   Number of spaces at left margin        0
     9  =   Number of char.s per address line     30
    10  =   Number of char.s between left edges   33
    11  =   Number of address lines per label      7
    12  =   Number of lines between top edges      9

    END =   Return to the Main Menu

    If the information on each line is correct, press RETURN.  If you want
    to add or change any information, type the number for that option.

                         Select option:

--------------------------------------------------------------------------------


Figure 6-9:  Label MenuFigure 6-9:  Label Menu


Printing a Mailing List or SublistPrinting a Mailing List or Sublist                             Page 6-14


Before trying to print the mailing list or sublist on labels, you should
check  that  the labels are aligned properly.  If the first parameter is
                                                     1No, specify that you want to test print  by  typing  1  to  the  "Select
option:"  prompt.   The  cursor moves to line 1.  Change the response to
              Yyes by typing Y.  Smart Mailer will display the following prompt on your
terminal:

        Please check the alignment of sample test labels.
        Do you want another sample written?

Check the alignment of the labels on the printer you specified.  If  the
labels  are  off,  type 'Y' to this prompt and use the ruler provided on
the back page of this manual to measure how  many  characters  you  must
adjust.   Smart  Mailer  will  redisplay the Label Menu and you may make
adjustments by redefining the parameter settings.  Refer to Section 10.3
for detailed descriptions of the parameter settings.

If you change a parameter setting, Smart Mailer checks to  see  if  your
change  is  reasonable  and/or correct.  If it is not, Smart Mailer will
display a warning or error message (e.g., Answer is  less  than  MINIMUM
value).

Smart Mailer can not generate labels with a parameter that is under  the
MINIMUM.   Smart  Mailer  will  produce  labels with parameters that are
outside the SAFE limits, but may not produce reasonable results.   Refer
to  Section  10.3  for  more  details  on the SAFE, MINIMUM, and MAXIMUM
limits of the parameter settings.

                                  <RETURN>After you make adjustments, press <RETURN> and Smart  Mailer  will  test
print  the labels again and redisplay the "Please check the alignment of
sample test labels.  Do you want another sample written?"  prompt.   You
may  want  to  print  two  sets to check the vertical adjustment between
labels.  Smart Mailer will continue asking this  question  until  yotype
                     N'N'.   When you type N, Smart Mailer prints the addresses on the printer
you selected and will display the following messages:

        generating labels... please wait.

        task completed, total labels printed = n

"n" is the number of labels generated.

                                             ENDIf you are finished using Smart Mailer, type END at each menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.






                               Chapter 7
                     Creating a List Document File



This chapter describes how to create  a  Word  Processor  List  Document
File.   This option is very useful if you have a Digital word processing
system and you want to generate personalized form letters for  addresses
in a mailing list or sublist.

Generating a List Document File allows you to choose certain  fields  in
your mailing list to be included in a Form Letter on the word processing
system.

This List Document File  will  extract  address  information  from  your
mailing  list for the fields you specify.  You may use this file as your
"List Document" for List Processing on the word processing system.

After you create your List Document File using  Smart  Mailer,  you  may
have  to  use a word processing system to convert the file from standard
file format to word processor format.  After you convert your file,  you
may  create  a  Form  Letter  and  Selection  Specification  on the word
processor.  Then use the List Processing option on the word processor to
generate personalized letters.

For more information on Form Letters, Selection Specifications, and List
Processing, refer to your word processor manual.

Creating a List Document FileCreating a List Document File                                   Page 7-2


7.1  Walk Through

This section describes the flow through Smart Mailer for creating a List
Document  File,  showing  each  screen, describing the logical flow, and
explaining any questions, prompts, or messages  that  have  not  already
been explained in the previous sections.

This section of Smart Mailer assumes that you have already  logged  onto
the  system, read the instruction screen, typed the name of your mailing
list, and the Main Menu is displayed.  If you have not done this,  refer
to Chapter 1, Sections 1.5 through 1.5.4.

                                     WTo create a List Document File, type W at the "Select option:" prompt of
the  Main Menu.  The List Selection Menu is displayed as shown in Figure
7-1.


------------------------------------------------------------------------

                         List Selection Menu



                  A  =   All addresses in a mailing list

                  S  =   Sublist name:

                  T  =   Temporary sublist

                  END    Return to the previous menu



                         Select option:

------------------------------------------------------------------------


Figure 7-1:  List Selection MenuFigure 7-1:  List Selection Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

Creating a List Document FileCreating a List Document File                                   Page 7-3


You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the List Selection Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (A).

      o  Type the letter associated with the option you want to perform.

                                       STo select a sublist of addresses, type S at the "Select option:" prompt.
The  cursor  will  be positioned after the "Sublist name:" prompt.  Type
the name of your sublist (e.g., MARLBORO).

If you do not have  an  existing  sublist,  Smart  Mailer  displays  the
following message:

        Sublist xxx does not currently exist.
        Do you wish to go back to create that sublist definition (Y/N)?

You can perform one of the following actions:

               Y      o  Type  Y  to  create  that  sublist  definition.   Smart  Mailer
         displays  the  Sublist Definition Menu.  Refer to Chapter 4 for
         more details on sublist definitions.

              N      o  Type N and Smart Mailer returns to the List Selection Menu.

                                                     TTo select a temporary sublist  of  addresses,  type  T  at  the  "Select
option:"  prompt.   If  a temporary sublist does not exist, Smart Mailer
displays a similar message to  above.   Refer  to  Chapter  4  for  more
details on sublist definitions.

                       <RETURN>For our example, press <RETURN> to select all addresses in  the  mailing
list.

Creating a List Document FileCreating a List Document File                                   Page 7-4


After you specify the type of list you want, Smart Mailer  displays  the
Sort Menu as shown in Figure 7-2.


------------------------------------------------------------------------

                                  Sort Menu



Sort mailing list by ...


                 P   =   Primary ID

                 A   =   Alternate ID


                 END     Return to the previous menu



                         Select option:

------------------------------------------------------------------------


Figure 7-2:  Sort MenuFigure 7-2:  Sort Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the Sort Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (P).  Smart  Mailer
         sorts the addresses by Primary ID.

              A      o  Type A to sort the addresses by Alternate ID.

After you specify the type of sort you want, Smart Mailer  displays  the
following message while it is selecting the addresses:

        working ... please wait.

Creating a List Document FileCreating a List Document File                                   Page 7-5


Smart Mailer displays the Generating a  List  Document  File  screen  as
shown in Figure 7-3.


------------------------------------------------------------------------

                     Generating a List Document File

       Name of List Document File: 

       Enter Y to include the address field in the List Document File

       Name                 N                 Occupation           N
       Address Line 1       N                 undefined            N
       Address Line 2       N                 undefined            N
       Address Line 3       N                 undefined            N
       City/Town            N                 undefined            N
       State/Country        N                 undefined            N
       Zip Code             N                 Counter              N
                                              Remark               N
                                              Primary ID           N
                                              Alternate ID         N


     (Type ? for help.  Type END to return to Sort Menu.)

------------------------------------------------------------------------


Figure 7-3:  Generating a List Document File ScreenFigure 7-3:  Generating a List Document File Screen


The cursor is positioned at the "Name of List Document File:" prompt.

The categories that are defined in your mailing list are displayed.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Sort Menu.

              ?      o  Type ?  to display help messages for this screen.

      o  Type the name of the List Document File you want to create.

                                                                 RESUMEFor example, to create a List Document File called RESUME, type  RESUME.
Smart Mailer's default extension for this file is ".DOC".  If you do not
include an extension for this List  Document  File,  Smart  Mailer  will
default to the ".DOC" extension.

Creating a List Document FileCreating a List Document File                                   Page 7-6


If you type more than nine (9) characters, for the  name  of  your  List
Document  File,  Smart  Mailer will accept it.  However, it will not use
more than nine (9) characters for that List Document File name.

If you specify a file that already exists,  Smart  Mailer  displays  the
following message:


        That output file already exists.    Press RETURN


This message is displayed for the RSTS and Micro/RSTS  versions.   If  a
file  already  exists  on  VMS,  this message is not displayed; instead,
another version of the List Document File is created.

      <RETURN>Press <RETURN> and Smart Mailer  will  reprompt  you  for  another  List
Document File name.

After you specify the name of file, the cursor moves down to the  "Name"
field.

You can perform one of the following actions:

              Y      o  Type Y at each field you want to include in this List  Document
         File.  You must say yes to at least one field.

               <RETURN>      o  Press <RETURN> to skip any field you do not want in  this  List
         Document  File  (N  is  the default answer for all the fields).
         Pressing <RETURN> accepts the default answer.

              END      o  Type END and the cursor goes  back  to  the  beginning  of  the
         screen.


Creating a List Document FileCreating a List Document File                                   Page 7-7


For example, to create a List Document File  which  includes  the  name,
address  lines,  city/town,  state/country,  zip  code,  and  Primary ID
fields, follow these steps:

              Y     1.  Type Y for the "Name" field.

              Y     2.  Type Y for the "Address Line 1" field.

              Y     3.  Type Y for the "Address Line 2" field.

              Y     4.  Type Y for the "Address Line 3" field.

              Y     5.  Type Y for the "City/Town" field.

              Y     6.  Type Y for "State/Country" field.

              Y     7.  Type Y for "Zip Code" field.

               <RETURN>     8.  Press <RETURN> to skip each category field.

               <RETURN>     9.  Press <RETURN> to skip the "Counter" field.

               <RETURN>    10.  Press <RETURN> to skip the "Remark" field.

              Y    11.  Type Y for the "Primary ID" field.

               <RETURN>    12.  Press <RETURN> to skip the "Alternate ID" field.


When you finish selecting which fields you want  in  the  List  Document
File, Smart Mailer confirms that the List Document File is being created
and displays a running sum of the total selected addresses.

The following is an example of the message displayed  with  the  example
given above.

        Creating List Document File RESUME.DOC ... Please wait

        Addresses Printed = xxx

        Task completed, total selected addresses = 2

After creating the List Document File, Smart Mailer returns to the  Main
Menu.

                                             ENDIf you are finished using Smart Mailer, type END at the  Main  Menu  and
Smart  Mailer  returns  you  to monitor level where the operating system
displays the system prompt.

Creating a List Document FileCreating a List Document File                                   Page 7-8


The following is an example  of  the  List  Document  File  (RESUME.DOC)
created in the example:

                                  NOTE                                  NOTE

        In the new version of Smart Mailer,  three  fields  have        In the new version of Smart Mailer,  three  fields  have
        been  added  to the List Document file:  <TITLE>, <FIRST        been  added  to the List Document file:  <TITLE>, <FIRST
        NAME>, and <LAST NAME>.  These fields  are  included  in        NAME>, and <LAST NAME>.  These fields  are  included  in
        the  List  Document  File  whenever the user selects the        the  List  Document  File  whenever the user selects the
        <NAME> field while generating a list document.        <NAME> field while generating a list document.


Note that Smart Mailer considers the first word in the name field to  be
a  title if it ends with a period.  In the following examples, Mr., Ms.,
Hon.  and J.  are treated as titles; but Miss and  Sir  are  treated  as
first names.

   Mr. John Doe            Sir Walter Smith
   Ms. Sarah Brown         Hon. Austin Philbin
   Miss Andrea Safer       J. D. Smith

The following is an example  of  the  List  Document  File  (RESUME.DOC)
created in the example:

<NAME>Robert Fuller
<TITLE>
<LAST NAME>Fuller
<FIRST NAME>Robert
<ADDRESS LINE 1>14 River Rd.
<ADDRESS LINE 2>P.O.Box 375
<ADDRESS LINE 3>
<CITY/TOWN>Marlboro
<STATE/COUNTRY>MA
<ZIP CODE>01752
<PRIMARY ID>               1
<>

<NAME>Roberta Fullerton
<TITLE>
<LAST NAME>Fullerton
<FIRST NAME>Roberta
<ADDRESS LINE 1>146 Main St.
<ADDRESS LINE 2>
<ADDRESS LINE 3>
<CITY/TOWN>Maynard
<STATE/COUNTRY>MA
<ZIP CODE>01754
<PRIMARY ID>               2
<>

A blank line is inserted between list document records (as shown).

Creating a List Document FileCreating a List Document File                                   Page 7-9


We specified that we wanted all three address  lines  included  in  this
List Document File, but some of the addresses may not have three address
lines.  Therefore, if you include all three address lines in  your  Form
Letter, you may have blank lines in the letter when it is created.

You must type the complete field name when creating your Form Letter  on
a word processing system.  For example, you must type the following:

<NAME>
<TITLE>
<LAST NAME>
<FIRST NAME>
<ADDRESS LINE 1>
<ADDRESS LINE 2>
<ADDRESS LINE 3>
<CITY/TOWN>
<STATE/COUNTRY>
<ZIP CODE>
<OCCUPATION>
<COUNTER>
<REMARK>
<PRIMARY ID>
<ALTERNATE ID>

Refer to the word processing documentation for help in  converting  this
List  Document  File  and a description of the Form Letter and Selection
Specification used with the List Processing option.






                               Chapter 8
                          Category Definitions



                                                  categoryEach Mailing List can have up to 6 categories.  A category is a piece of
information  associated  with each name and address.  For each different
Mailing List, you can choose different categories.  Each category has  a
label   (a   name  up  to  10  characters  long),  and  type  (character
information, numeric information, dates, or  Yes/No  values)  associated
with  it.   Normally, these categories are defined at the same time that
the Mailing List is created.

If you want to change the information stored in a category for any name,
you can use the 'Update an Address' function from the Main Menu.

If you want to change the label or the type of information stored  in  a
category,  you can use the 'Category' function from the Main Menu.  THIS
SHOULD BE DONE WITH CARE.  If you add a category to an existing  Mailing
List  by defining its label and type, understand that any existing names
in that Mailing List will probably not  have  any  information  in  that
category.   Changing  the label on an existing category can be harmless.
For  example,  changing  'PAY'  to  'SALARY $'  makes  the  label   more
meaningful.   But  changing  'RECVD DATE' to 'SHIP DATE' can potentially
cause problems.  Problems can occur because the category information for
existing names and addresses may not match the new category label.  Even
more problems occur if you  change  the  category  type.   For  example,
changing  the  type  of  information  in  'PHONE NUM'  from  numeric  to
alphanumeric, allows you to store phone numbers with hyphens imbedded in
them.  But it does not change existing phone numbers.

To summarize, the ability to change category definitions is provided  as
a  useful technique, but it should be used knowing what the implications
are.  Smart Mailer does NOT change, or even check  existing  information
to  make  sure  that it matches the new definition.  In general, changes
should be made to define previously undefined categories, or  to  modify
labels.  Be careful when changing the type of an existing category.

Category DefinitionsCategory Definitions                                            Page 8-2


8.1  Walk Through

This section describes the  flow  through  Smart  Mailer  for  updating,
printing,  and  displaying  category  definitions,  showing each screen,
describing the logical flow, and explaining any questions,  prompts,  or
messages that have not already been explained in the previous section.

This section of Smart Mailer assumes that you have already  logged  onto
the  system, read the instruction screen, typed the name of your mailing
list, and the Main Menu is displayed.  If you have not done this,  refer
to Chapter 1, Sections 1.5 through 1.5.4.

                                                        CTo update, display, or print category definitions, type C at the "Select
option:"  prompt  of  the  Main  Menu.   The Category Definition Menu is
displayed as shown in Figure 8-1.


------------------------------------------------------------------------

                           Category Definition Menu



                  U    =   Update the category definitions

                  P    =   Print the category definitions

                  D    =   Display the category definitions

                  END      Return to the Main Menu




                           Select option:

------------------------------------------------------------------------


Figure 8-1:  Category Definition MenuFigure 8-1:  Category Definition Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

Category DefinitionsCategory Definitions                                            Page 8-3


You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for  the  Category  Definition
         Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (U).

      o  Type the letter associated with the option you want to perform.

The following sections discuss these options in detail.

Category DefinitionsCategory Definitions                                            Page 8-4


8.1.1  Updating a Category Definition

The Update option enables you to add  new  category  information  or  to
correct/change  the existing labels and type codes.  Be careful when you
are updating the label and type of the category.  Refer to the beginning
of this chapter for details of problems that may occur when you change a
label or type code.

                                                     UTo change or add  new  category  definitions,  type  U  at  the  "Select
option:"  prompt  of  the  Category  Definition  Menu.   A sample of the
Category Update screen is displayed as shown in Figure 8-2.


------------------------------------------------------------------------

                           Category Update


                           label       type

                 1  =   Occupation      A
                 2  =   undefined       A
                 3  =   undefined       A
                 4  =   undefined       A
                 5  =   undefined       A
                 6  =   undefined       A


    Type the number of the category to be updated.
    Then type the label for that category, followed by a RETURN,
    then type the type code of that category (A = Alphanumeric,
    N = Numeric, D = Date, Y = (Yes/No), or C = Coded
    Press RETURN to leave any option unchanged.


                           Select option:

------------------------------------------------------------------------


Figure 8-2:  Category Update ScreenFigure 8-2:  Category Update Screen


The cursor is positioned at the "Select option:" prompt.

The category labels are displayed if you defined  them.   If  categories
are  not  defined,  Smart Mailer displays them as "undefined".  The type
code that is associated with the label is displayed, as well as the type
code default values (A) of undefined categories.

Category DefinitionsCategory Definitions                                            Page 8-5


You can perform one of the following actions:

              END      o  Type END to return to the Category Definition Menu.

              ?      o  Type ?  to display help messages.

               <RETURN>      o  Press <RETURN> to return to the Category Definition Menu.

      o  Type the number associated with the category label or type code
         you want to add or update.

When you type the number associated with the category you want to add or
update,  the  cursor  is positioned at "label".  Enter the name you want
for the category label and press <RETURN>.  The cursor moves to  "type".
Type  the  type  code  that  belongs  with the category definition.  The
cursor returns to the "Select option:" prompt.

The following section discusses how to add new category definitions.

For example, we will add the following category definitions:

        Salary          A (Alphanumeric)
        Phone No.       A (Alphanumeric)
        Date Rcvd       D (Date)
        Interested      Y (Yes/No)
        Catalog         C (Coded)

We already have one category definition defined, so we will  select  the
second category.

Category DefinitionsCategory Definitions                                            Page 8-6


To add these category definitions, follow these steps:

              2     1.  Type 2.

              Salary     2.  Type Salary.

               <RETURN>     3.  Press <RETURN> to accept the default answer (A).

              3     4.  Type 3.

              Phone No.     5.  Type Phone No..

               <RETURN>     6.  Press <RETURN> to accept the default answer (A).

              4     7.  Type 4.

              Date Rcvd     8.  Type Date Rcvd.

              D     9.  Type D (date type code).

              5    10.  Type 5.

              Interested    11.  Type Interested.

              Y    12.  Type Y.

              Catalog    13.  Type Catalog.

              C    14.  Type C.

If you select a defined category definition and then decide you  do  not
want  to  redefine either the "label" or "type", press <RETURN> when the
cursor is positioned at "label" or "type" and Smart  Mailer  will  leave
the  current  value  in  that  field  and return to the "Select option:"
prompt.

If you select a category that is already defined  and  then  decide  you
want  to  leave the "label" or "type" blank, press the space bar once at
"label" and "type" and Smart Mailer will leave that  "label"  or  "type"
blank.

When you are finished updating/adding your category  definitions,  press
<RETURN>  at the "Select option:" prompt and Smart Mailer will return to
the Category Definition Menu.

                                             ENDIf you are finished using Smart Mailer, type END at each menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Category DefinitionsCategory Definitions                                            Page 8-7


8.1.2  Printing a Category Definition

                                                     PTo print a listing of the category definitions, type P  at  the  "Select
option:"  prompt of the Category Definition Menu.  Smart Mailer displays
the Output Device Menu as shown in Figure 8-3.


------------------------------------------------------------------------

                       Output Device Menu




                D  =   Disk file output:

                1  =   Main Printer







                END =  Return to the previous menu



                       Select option:

------------------------------------------------------------------------


Figure 8-3:  Output Device MenuFigure 8-3:  Output Device Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the previous menu.

              ?      o  Type ?  to display help messages for the Output Device Menu

               <RETURN>      o  Press <RETURN> to accept the default answer (D).

      o  Type the code associated with the type of printer you  want  to
         select.


Category DefinitionsCategory Definitions                                            Page 8-8


When you choose a printer, Smart Mailer tells you what type of  printing
will  be  done.   If it gives you a message that the information will be
'sent to' the device, then it will print it directly.  If it  says  that
the  information will be 'queued to' the device, then it will send it to
the operating system to be printed when the printer is  available.   See
Section 1.4.2 for more information on the Output Device Menu.

You must wait  until  Smart  Mailer  indicates  it  is  ready  for  more
instructions before going on to anything else.  DO NOT turn the terminal
off, or try to log off.

After you specify the printer, Smart Mailer lets you know it is  working
by displaying the following message:

        Listings will be queued to device xx
or
        Listings will be sent to device xx

The Output Device Menu enables you to output to disk or  to  a  printer.
Note that if you write to disk, Smart Mailer stores the information, but
does not produce a listing.  If you  specify  a  printer,  Smart  Mailer
produces a listing of the current category definitions.

On completion, Smart Mailer returns you to the Category Definition Menu.

                                             ENDIf you are finished using Smart Mailer, type END at each menu  displayed
until  Smart  Mailer  returns  you  to monitor level where the operating
system displays the system prompt.

Category DefinitionsCategory Definitions                                            Page 8-9


8.1.3  Displaying a Category Definition

                                                              DTo display the category definitions for a mailing list, type  D  at  the
"Select  option:"  prompt of the Category Definition Menu.  Smart Mailer
displays the categories for the mailing list specified.

Figure 8-4 displays the category definitions for  the  'RESUME'  mailing
list with categories defined in previous sections of this manual.


------------------------------------------------------------------------

                                                Date:  07-FEB-83
Mailing List:  RESUME.MLF                       Time:  09:13

                                label           type

               Category 1:      Occupation      A
               Category 2:      Salary          A
               Category 3:      Phone No.       A
               Category 4:      Date Rcvd       D
               Category 5:      Interested      Y
               Category 6:      Catalog         C




When you are done reading the display ...               Press RETURN

------------------------------------------------------------------------


Figure 8-4:  Example - Category Definition Display ScreenFigure 8-4:  Example - Category Definition Display Screen


The Category Definition Display screen displays the Mailing  List  name,
date  and  time  the  display  was requested, and a list of all category
labels and type codes.

      <RETURN>Press <RETURN> when you are done viewing this screen  and  Smart  Mailer
returns to the Category Definition Menu.

                                             ENDIf you are finished using Smart Mailer, type END at each menu  displayed
until  Smart  Mailer  returns  you  to  monitor level were the operating
system displays the system prompt.






                               Chapter 9
                  Report Mailing (Sub)list Statistics




This chapter describes a new option that has been  added  to  the  Smart
Mailer  Main  Menu  to provide the user with statistics on mailing lists
and sublists.

9.1  Walk Through

This section describes the flow through  Smart  Mailer  for  printing  a
Statistics  Report  on  a  mailing list or sublist, showing each screen,
describing the logical flow, and explaining any questions,  prompts,  or
messages that have not already been explained in the previous sections.

This section of Smart Mailer assumes that you have already  logged  onto
the  system, read the instruction screen, typed the name of your mailing
list, and the Main Menu is displayed.  If you have not done this,  refer
to Chapter 1, Sections 1.5 through 1.5.4.

                                                                RTo print a statistics report on a mailing list or sublist, type R at the
"Select  Option:"  prompt  of the Main Menu.  The List Selection Menu is
displayed as shown in Figure 9-1.


------------------------------------------------------------------------

                         List Selection Menu



                  A  =   All addresses in a mailing list

                  S  =   Sublist name:

                  T  =   Temporary sublist

                  END    Return to the previous menu



                         Select option:

------------------------------------------------------------------------


Figure 9-1:  List Selection MenuFigure 9-1:  List Selection Menu


The cursor is positioned at the "Select option:" prompt.

Report Mailing (Sub)list StatisticsReport Mailing (Sub)list Statistics                             Page 9-2


You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the List Selection Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (A).

      o  Type the letter associated with the option you want to perform.

                                       STo select a sublist of addresses, type S at the "Select option:" prompt.
The  cursor  will  be positioned after the "Sublist name:" prompt.  Type
the name of your sublist (e.g., MARLBORO).

If you do not have  an  existing  sublist,  Smart  Mailer  displays  the
following message:

        Sublist xxx does not currently exist.
        Do you wish to go back to create that sublist definition (Y/N)?

You can perform one of the following actions:

               Y      o  Type  Y  to  create  that  sublist  definition.   Smart  Mailer
         displays  the  Sublist Definition Menu.  Refer to Chapter 4 for
         more details on sublist definitions.

              N      o  Type N and Smart Mailer returns to the List Selection Menu.

                                                     TTo select a temporary sublist  of  addresses,  type  T  at  the  "Select
option:"  prompt.   If  a temporary sublist does not exist, Smart Mailer
displays a similar message to  above.   Refer  to  Chapter  4  for  more
details on sublist definitions.

                           <RETURN>For  our  example,  press  <RETURN>  to  select  all  addresses  in  the
RESUME.MLF Mailing List File.

After you specify the type of list you want, Smart Mailer  displays  the
Report Menu as shown in Figure 9-2.

Report Mailing (Sub)list StatisticsReport Mailing (Sub)list Statistics                             Page 9-3


------------------------------------------------------------------------

                               Report Menu


                1   =   Report total addresses in this
                        Mailing (Sub)List

                2   =   Report address distribution by first
                        N digits of Zip Code.  N = 1,2,3,4 or 5

                                  Select N: _


                END     Return to Main Menu



                        Select Option: 1

------------------------------------------------------------------------


Figure 9-2:  Report MenuFigure 9-2:  Report Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the Main Menu.

              ?      o  Type ?  to display help messages for the Report Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (1).

              2      o  Type 2 if you want an address distribution report.

         The cursor is positioned at the "Select N:" prompt.

         You can perform one of the following actions:

                  ?          o  Type ?  to display a help message for this prompt.

          o  Type the number of Zip Code digits to use  in  the  address
             distribution  report.   The  report will list the number of
             addresses in each Zip Code area, using 1 to 5 digits of the
             Zip Code.


After you specify the number of Zip Code digits to use  in  the  address
distribution report, Smart Mailer displays the followng prompt:

Report Mailing (Sub)list StatisticsReport Mailing (Sub)list Statistics                             Page 9-4


        Lines per page:  66

This prompt allows you to specify the number of lines per page  for  the
report.  The default is 66.

If you select option 1 (report total addresses), Smart  Mailer  displays
the Total Address Report as shown in Figure 9-3.


------------------------------------------------------------------------

                           Total Addresses Report

                                                        Date:  21-Mar-85
Mailing List:  RESUME.MLF                               Time:  02:27 PM

------------------------------------------------------------------------



            Total addresses = 3









When through reading the display ...                        Press RETURN

------------------------------------------------------------------------


Figure 9-3:  Example - Total Addresses Report ScreenFigure 9-3:  Example - Total Addresses Report Screen


If you specified a sublist name in the List Selection Menu, Smart Mailer
displays the sublist name above the mailing list name on this screen.

      <RETURN>Press <RETURN> when you are done viewing this screen  and  Smart  Mailer
returns to the Smart Mailer Main Menu.


If you select option  2  (report  address  distribution),  Smart  Mailer
displays the Output Device Menu as shown in Figure 9-4.

Report Mailing (Sub)list StatisticsReport Mailing (Sub)list Statistics                             Page 9-5


------------------------------------------------------------------------

                       Output Device Menu




                D  =   Disk file output:

                1  =   Main Printer







                END =  Return to the previous menu



                       Select option:

------------------------------------------------------------------------


Figure 9-4:  Output Device MenuFigure 9-4:  Output Device Menu


The cursor is positioned at the "Select option:" prompt.

You must press <RETURN> after each response.

You can perform one of the following actions:

              END      o  Type END to return to the previous menu.

              ?      o  Type ?  to display help messages for the Output Device Menu.

               <RETURN>      o  Press <RETURN> to accept the default answer (D).

      o  Type the code associated with the type of printer you  want  to
         select.

When you choose a printer, Smart Mailer tells you what type of  printing
will  be  done.   If it gives you a message that the information will be
'sent to' the device, then it will print it directly.  If it  says  that
the  information will be 'queued to' the device, then it will send it to
the operating system to be printed when the printer is available.

You must wait  until  Smart  Mailer  indicates  it  is  ready  for  more
instructions before going on to anything else.  DO NOT turn the terminal
off, or try to log off.

Report Mailing (Sub)list StatisticsReport Mailing (Sub)list Statistics                             Page 9-6


After you specify the printer, Smart Mailer lets you know it is  working
by displaying the following messages:

        Selecting addresses to sort ... please wait
        Total addresses = 3
        Sorting addressses ... please wait
        generating reports ... please wait.
        task complete

After the task is complete, Smart Mailer displays the Smart Mailer  Main
Menu.

                                             ENDIf you are finished using Smart Mailer, type END at the  Main  Menu  and
Smart  Mailer  returns  you  to  monitor level were the operating system
displays the system prompt.

Note that the printing operation can take anywhere from a few seconds to
a  number  of hours depending on:  total number of addresses, percentage
of addresses meeting the sublist requirements, printer  speed,  type  of
listing, type of computer, and number of other computer users.


The following example shows a page from an Address  Distribution  Report
using  the  sample  RESUME.MLF  Mailing List File.  The report lists the
number of addresses in each 5 digit Zip Code area.





                            Address Distribution Report         Page   1

                                                                Date:  20-Mar-85
Mailing List:  RESUME.MLF                                       Time:  01:35 PM
Address Distribution by first 5 digits of Zip Code.


     Zip : Total         Zip : Total         Zip : Total         Zip : Total    
   -------------       -------------       -------------       -------------
   01749 :     1       01752 :     1       01754 :     1    

                                                 Zip Codes  01749   to   01754

Total addresses  =        3

Report Mailing (Sub)list StatisticsReport Mailing (Sub)list Statistics                             Page 9-7


The next example shows  an  Address  Distribution  Report  on  the  same
mailing  list,  but  this time address totals are grouped by the first 3
digits of the Zip Code.


                            Address Distribution Report         Page   1

                                                                Date:  20-Mar-85
Mailing List:  RESUME.MLF                                       Time:  01:36 PM
Address Distribution by first 3 digits of Zip Code.


     Zip : Total         Zip : Total         Zip : Total         Zip : Total    
   -------------       -------------       -------------       -------------
   017__ :     3    

                                                 Zip Codes  017__   to   017__

Total addresses  =        3







                               Chapter 10
                            Advanced Topics



This  chapter  covers  some  advanced  material.   Depending   on   your
situation,  you  may  not  need this information in your everyday use of
Smart Mailer.

The material covers more Postal  PRESORTing  procedures,  using  complex
sublist  definitions,  changing  label  parameters,  and suggestions for
creative uses of Smart Mailer.

10.1  PRESORTing Addresses

10.1.1  PRESORT Rules

The information given in this section  referring  to  PRESORT  rules  isThe information given in this section  referring  to  PRESORT  rules  is
given  to help you, BUT it should not be relied on.  The Post Office maygiven  to help you, BUT it should not be relied on.  The Post Office may
issue revised rules at any time and they should  be  contacted  for  theissue revised rules at any time and they should  be  contacted  for  the
current  status.  You must contact the Post Office to obtain a permit tocurrent  status.  You must contact the Post Office to obtain a permit to
use PRESORT, and to learn the appropriate method  of  packaging  PRESORTuse PRESORT, and to learn the appropriate method  of  packaging  PRESORT
mail.   The  following information is believed to be correct at the timemail.   The  following information is believed to be correct at the time
this document was written.  But again - please refer  to  official  Postthis document was written.  But again - please refer  to  official  Post
Office regulations for current rules.Office regulations for current rules.


The Post Office describes PRESORTed mail in the following way:


        "First-Class letter mail  in  volumes  of  500  pieces  or  more
        qualifies for a postage rate three cents per piece less than the
        regular letter rate if it is presorted and prepared according to
        specific  requirements.   The  rate  for properly presorted post
        cards is one cent less than the regular post card  rate.   Those
        pieces which are necessary to meet the 500 piece minimum volume,
        but can not be presorted and prepared as prescribed are residual
        mail and must be paid at the full First-Class letter rate or the
        full First-Class post card rate." (from the Information Guide on
        PRESORT First-Class mail)

Advanced TopicsAdvanced Topics                                                Page 10-2


There are several requirements that you must meet before you can qualify
for  a  PRESORT  postal rate discount.  Some of these requirements, like
size and weight of letters, must  be  met  by  yourself.   Others,  like
sorting  by  zip  code,  you  can request Smart Mailer to help you meet.
When you request PRESORTing, Smart Mailer will

      o  check if your chosen addresses are valid,

      o  determine  whether  you  have  the  minimum  number  of   valid
         addresses for PRESORT,

      o  sort those addresses by zip code,

      o  combine the sorted addresses into batches of similar zip  codes
         (according to Post Office rules),

      o  combine addresses that can not be separated as in the  previous
                              residual         step into a separate residual section,

      o  then print out the valid addresses (and optionally the  invalid
         addresses)  on  labels  that  are separated by break labels (if
         requested) indicating the Post Office specified groupings.


Advanced TopicsAdvanced Topics                                                Page 10-3


10.1.2  PRESORT Statistics

The following message is an example of what Smart Mailer will  tell  you
after you request PRESORT:



        Total selected addresses = 620

   Of these 613 are valid addresses for PRESORT;  7 are invalid.
   bad zip code = 5, blank city = 2, bad state code = 0


This represents the first step in the process where Smart Mailer  checks
to see if your addresses are proper.  If, for example, your addresses do
not have the hyphen in their 9-digit zip codes, then your addresses  are
not valid for PRESORT.  Or as another example, if you have 600 addresses
and 150 of them represent foreign addresses,  then  only  450  would  be
valid addresses for PRESORT.

If you have less than the minimum (500), then  Smart  Mailer  tells  you
that  and  lets  you terminate the PRESORTing, before it actually starts
the sorting.  This avoids wasting time in a situation where you  do  not
want  the  final  results.  You can then go back and correct any invalid
addresses, use another sublist with more addresses, or just  do  regular
labels.

Assuming you DO have  enough  labels  (or  you  just  want  to  continue
anyway),  Smart  Mailer  will sort the addresses for PRESORT and asks if
you want break labels printed and displays the following message:

        Should break labels be printed?


                                          <RETURN>If you want break labels generated, press <RETURN>  (Y  is  the  default
                         Nanswer); otherwise, type N and break labels will not be generated.

Advanced TopicsAdvanced Topics                                                Page 10-4


Figure 10-1 is an example of the PRESORT display that Smart Mailer shows
you after it has PRESORTed the addresses:


--------------------------------------------------------------------------------
                              PRESORT Menu

              A  210   Direct pieces
              B  360   City/SCF pieces
              C   43   Residual pieces
              D  570   pieces that qualify for lower postage rate (A+B)
              E  613   pieces that count toward the minimum       (A+B+C)
              F    7   pieces that are invalid for PRESORT


              1    =   Print all the addresses

              2    =   Print only valid addresses     (see E above)

              3    =   Print only invalid addresses   (see F above)


              END      Return to the Main Menu


                       Select option (1,2,3):

--------------------------------------------------------------------------------


Figure 10-1:  Example - PRESORT MenuFigure 10-1:  Example - PRESORT Menu


Smart Mailer shows you how your addresses are sorted and  grouped.   The
number  of  invalid  addresses  (see F above) you have already been told
about before in the previous message.   All  others  count  toward  your
minimum  number,  but  the pieces that do not qualify for PRESORT (see C
above), do not qualify for the lower postage rate.  If you asked to have
multiple copies of the addresses, each copy counts as a separate piece.

The statistics are meant to help you decide which addresses to print  on
labels.   You can print any of these sets of addresses.  You may want to
print   the   invalid   addresses   because    they    represent    real
non-U.S. addresses,  or  because  you  want  to see them so that you can
correct them.

Advanced TopicsAdvanced Topics                                                Page 10-5


The  following  definitions  explain  the  meaning  of   the   different
statistics listed in the display.


Direct pieces:Direct pieces:

        The number of pieces that can be sorted  into  a  direct  group.
        Each  direct  group  must  have  10 or more pieces with the same
        5-digit zip code.

City/SCF pieces:City/SCF pieces:

        The number of pieces that can be  sorted  into  a  city  or  SCF
        group.  Each City/SCF group must have 50 or more pieces with the
        same 3-digit zip code prefix.

Residual pieces:Residual pieces:

        The number of pieces that have valid state abbreviations and zip
        codes,  but do not meet the requirements for direct, city or SCF
        pieces.  Residual pieces do not qualify for  the  lower  postage
        rate, but do count towards the 500-piece PRESORT minimum.

Pieces that qualify for the lower postage rate:Pieces that qualify for the lower postage rate:

        The total number of direct and city/SCF pieces.

Pieces that count toward the minimum:Pieces that count toward the minimum:

        The total number of direct, city/SCF, and residual pieces.

Pieces that are invalid for PRESORT:Pieces that are invalid for PRESORT:

        The number of pieces that have invalid  state  abbreviations  or
        zip codes, or any other errors.


When Smart Mailer prints PRESORTed labels, it also prints  break  labels
(if  requested)  which  indicate  the groupings into which the addresses
have been sorted.  This should make it  easier  for  you  to  affix  the
required Post Office stickers.

Figure 10-2 is a sample of PRESORTed labels which include break labels:

Advanced TopicsAdvanced Topics                                                Page 10-6


**************************       John Q. Public
**************************       123 Main Street
DIRECT PIECES:         210       Maynard, MA  01254
Zip Code:    01254



Jane Smith                       Susan Jones
12 Elm Street                    3 Maple Street                     
Boston, MA   01254               Apt. 14
                                 Boston, MA   01254


.
.
.


Thomas Andy, Jr.                 **************************       
c/o Mrs. Andy                    **************************       
54 Elm Street                    UNQUALIFIED PIECES:      5       
Oakwood, CA   55987                                               



      
Ann Parker                       Tom Anderson
11 Concord Street                10 Main Street
New Glasgow                      Billerica, MA   
Nova Scotia, CANADA



Robert Fund                      
12 Rose Lane                     
East Boston,   02128             

.
.
.



Figure 10-2:  Sample - PRESORTed LabelsFigure 10-2:  Sample - PRESORTed Labels


Advanced TopicsAdvanced Topics                                                Page 10-7


10.1.3  PRESORT References

The following references  represent  the  currently  known  publications
published by the Post Office that explain the use of PRESORT:

___________ _____ __ _______ ___________ _____ ___ ___ ____ ____Information Guide on PRESORT First-Class Mail, Pub 61, June 1981

________ ___________ ___ _______ _____ _____ _____ ___ ____ ___ ____Computer Programming for PRESORT First Class Mail, Pub 232, Oct 1980

________ ____ ______ _____Domestic Mail Manual (DMM)

________ ___ ____ ___ ____ ______ __________ ___ __National Zip Code and Post Office Directory, Pub 65

_ ______ ____ ________ __ ____ _______ ________ ___ ___A Bottom Line Estimate of your Presort Savings, Pub 231

____ __ _______Memo to Mailers



10.1.4  Use of Non-First Class Mail PRESORT

Although Smart Mailer is designed to implement PRESORT  for  First-Class
Mail,  you  may be able to use part of it for non-First-Class Mail.  For
example, third class bulk mailings have similar regulations.  Both  need
to  be sorted by zip code (although the groupings are somewhat different
and the minimum number of pieces is lower).

Please refer  to  official  Post  Office  regulations  for  the  current
official implementation rules.

Advanced TopicsAdvanced Topics                                                Page 10-8


10.2  Sublist Definitions

A sublist definition defines how Smart Mailer is to check  each  address
in  a  Mailing List to determine if the address belongs in that sublist.
                                                         lineA sublist definition can have up to 30 lines, where each line represents
one condition that may (or must) be met before an address is included in
the sublist.  Each line defines a comparison that is to be made  between
the  contents of an address field and a user specified value or range of
values.  An address field is one part of the address, such as zip  code,
or  a  category  such as Job Title.  The address field is referred to by
its name (Job Title).  The actual comparison is done on the contents  of
the address field (Janitor) for each address.

When you request a sublist, Smart Mailer checks every  address  in  your
Mailing  List to determine if it meets the requirements.  Therefore, the
sublist is always as up-to-date as the Mailing List.

Rules Used to Evaluate Requirement LinesRules Used to Evaluate Requirement Lines

When determining if an  address  belongs  in  a  sublist,  Smart  Mailer
evaluates  each requirement line for that address.  The way Smart Mailer
checks each requirement line for validity is described below.

There are five different kinds of data - Alphanumeric, Numeric, Date and
             numericYes/no.  For numeric data, the comparison is straight-forward.  Is means
                                         dateequal to; above means greater than.  For date data, there is  a  similar
analogy.   Above means after; below means before.  Making comparisons on
alphanumericalphanumeric data is a little more subtle.  Above means that the address
field comes after the specified value in the Smart Mailer sorting order.
You can refer to Table 6-1  for  a  more  complete  explanation  of  the
sorting  order,  but  basically,  blanks come before numbers, which come
                        Yes/nobefore letters.   With  Yes/no  data,  the  only  comparisons  that  are
                                                       codedreasonable  are the IS or the IS NOT comparisons.  For coded data, refer
to Table 2-2 and the examples that follow that table.

When doing BETWEEN (or NOT BETWEEN) comparisons, the second  value  must
be  higher than (greater than, after) the first value.  For example, you
may not request Alternate  ID's  between  M  and  A.   You  may  request
Alternate  ID's  between  A  and M.  The two values may be the same, but
that is the same as using the easier IS (or IS NOT) comparison.

When the length of alphanumeric address field  information  matches  the
length  of  the  specified  value,  then the comparison is easy to make.
When the lengths are unequal, then Smart Mailer checks whether  the  two
items match up to the length of the user-specified value.

The system matches the exact string given in the sublist criteria.   For
example, ZIP CODE IS 017 will only choose addresses that have a Zip Code
of 017.  To choose addresses that have a Zip Code starting with 017  you
need to request ZIP CODE BETWEEN 01700 and 01799.  This is more flexible
than the stated method, since it means that you  can  request  addresses
that  match  exactly,  not just start with a sequence.  For example, you
can request the address with Primary ID of 5 and not get  all  addresses
with  a Primary ID starting with 5.  This allows you to extract customer
number 5 and not also get numbers 52 and 517.

Requesting Alternate ID's that are not S (ALTERNATE ID is  not  S)  will
give you all Alternate ID's that do not begin with S.

Advanced TopicsAdvanced Topics                                                Page 10-9


Rules for Evaluating Multi-line Sublist DefinitionsRules for Evaluating Multi-line Sublist Definitions

When there is only one line in  a  sublist  definition,  the  way  Smart
Mailer  checks  for a match is straight-forward.  The comparison must be
true for every address chosen.

If there are two comparison lines in the definition, then the  situation
is  somewhat  more  complex.   If the connector between the two lines is
AND, then both comparisons must be true.  If the connector  between  the
two  lines  is OR, then either comparison may be true for the address to
be included.

For more complex definitions, that is definitions  with  three  or  more
lines,  Smart  Mailer  follows  two  rules for determining if there is a
match.  The first rule is that Smart Mailer checks pairs of  lines  that
refer  to  the  same  field first.  The second rule is that Smart Mailer
starts at the first line then checks the next line, then the next and so
on,  each  line in turn.  (This means that there is top-down precedence.
The AND operator does NOT have precedence over the  OR  operator).   For
example,

           HIRE DATE        BELOW     01-JAN-73
      or   SALARY           ABOVE     $40,000
      and  JOB TITLE        IS        MANAGER


would generate a sublist of all the managers who have either  been  with
the company for a long time, or who make a large salary.

As another example,

           WAGE TYPE        IS       HOURLY
      and  JOB TITLE        IS       CLERK
      or   JOB TITLE        IS       TECHNICIAN


would generate a sublist of all hourly workers who are either clerks  or
technicians.   In  this  case,  lines  2 and 3 are checked before line 1
because the fields are the same (JOB TITLE).

In the example,

           JOB TITLE        IS       TECHNICIAN
      and  WAGE TYPE        IS       HOURLY
       or  JOB TITLE        IS       CLERK


This is not the same as the previous example.  In this case, lines 1 and
2  are checked before line 3 because the lines with the same fields (JOB
TITLE) are not listed together.  This example would generate  a  sublist
of all hourly technician, and all clerks (regardless of wage type).

Advanced TopicsAdvanced Topics                                               Page 10-10


Empty SublistEmpty Sublist

In certain situations, you may find that a sublist has no  addresses  in
it.   This  is  usually caused by some type of mistake.  First make sure
that you are using the right Mailing List.  Otherwise, check the sublist
definitions for criteria that are impossible to meet.

Smart Mailer does a limited  amount  of  checking  when  you  enter  the
sublist  definition.   For  example,  Smart  Mailer will warn you if you
specify that a field must be two  different  things  at  the  same  time
(e.g.,  JOB  TITLE  is  DENTIST  and JOB TITLE is DOCTOR).  It will also
check that when looking for a range of values, that the upper  limit  is
greater  than  the  lower  limit.   But  not all combinations that would
produce an empty list can be anticipated.   Neither  does  Smart  Mailer
check  all  addresses  when  the  sublist  is  defined - only when it is
actually used.  In fact, you can define sublists before  there  are  any
addresses defined.

Advanced TopicsAdvanced Topics                                               Page 10-11


10.3  Printing Labels

This section describes in detail the label parameters, the format of the
labels  and the label output.  For a description of how to use the Smart
Mailer menus to print a set of labels see Chapter 6.

Label parameters allow you to change settings  for  different  types  of
labels.   The  label  parameters  allow  you  to adjust for each type of
label.  You may test print the labels to see if  you  have  the  correct
settings  for  the  type of label and correct alignment of labels in the
printer.  The test print parameter will print one row of  labels  across
the page so that you can see if all your settings are correct.

If they are not correct, you may  make  adjustments  by  redefining  the
parameter  settings.   The default settings for the label parameters are
defined by the System Manager.  As long as you  stay  in  Smart  Mailer,
when  you  select  another  set  of labels, the default values for these
label parameters will match those parameters that you just used.  If you
terminate  Smart  Mailer  after you have redefined these parameters, the
default settings will go back to the System Manager's values.

Advanced TopicsAdvanced Topics                                               Page 10-12


Table 10-1 shows  the  address  format  used  to  print  labels.   If  a
particular address line is blank, then the address will be compressed so
there are no imbedded blank lines.



Table 10-1:  Label FormatTable 10-1:  Label Format


Line 1:  User-defined Message (Left-justified)
Line 2:  Extra Information    (Right-justified)
Line 3:  Name
Line 4:  Address Line 1
Line 5:  Address Line 2
Line 6:  Address Line 3
Line 7:  City, State   Zip code




The following are examples of addresses as printed by Smart Mailer (with
and without special messages and extra information):


Address Correction Requested          Please renew today! exp:
                   011-55-0169                              01-JUL-83
Johnny Smith                          Pauline Anderson
c/o Mr. James Smith                   54 Elmwood Drive
123 East 12th Street                  Columbus, OH   44896
Apt 12A
New York, NY   12386

Merry Christmas !!                    Marion Willow
Mary Anne Murphy                      RFD 2
45 Main St                            Thorndike, ME   10766
New Glascow
Nova Scotia, Canada



Advanced TopicsAdvanced Topics                                               Page 10-13


10.3.1  Label Parameters

Smart Mailer can generate labels in almost any format that you may want.
The  parameters  for  the  different  types, sizes, shapes and number of
labels are defined by the Label Menu (Figure 10-3).


--------------------------------------------------------------------------------

                              Label Menu

     1  =   Test print sample labels               Y
     2  =   Extra info on labels (P,A,C,1-6)
     3  =   Special label message
     4  =   Increase/Decrease/Reset counters
     5  =   Number to incr/dec/reset counters      0
     6  =   Number of copies of labels             1
     7  =   Number of labels across a page         2
     8  =   Number of spaces at left margin        0
     9  =   Number of char.s per address line     30
    10  =   Number of char.s between left edges   33
    11  =   Number of address lines per label      7
    12  =   Number of lines between top edges      9

    END =   Return to the Main Menu

    If the information on each line is correct, press RETURN.  If you want
    to add or change any information, type the number for that option.

                         Select option:

--------------------------------------------------------------------------------


Figure 10-3:  Label MenuFigure 10-3:  Label Menu


A description of each of the menu items is given below.

         Test print sample labels     1.  Test print sample labels

         You may answer Y or N to this question depending on whether you
         want  Smart  Mailer  to  print  a  row  of sample labels before
         printing the actual addresses.  Smart Mailer will  continue  to
         print  a  row  of  labels  until  you  are  satisfied  with the
         alignment of the labels and the format of the labels.

         Extra Info on labels     2.  Extra Info on labels

         You may type P (Primary ID), A (Alternate ID), C (Counter),  or
         1-6  (Category  number associated with label) if you want Smart
         Mailer to print any one of the  above  (right-justified)  above
         the name on the label of each address.

Advanced TopicsAdvanced Topics                                               Page 10-14


         Special label message     3.  Special label message

         You may type in a message (up to 30 characters) that  you  want
         Smart Mailer to print at the top of every label.  If there is a
         default message, and you do not want any message,  then  simply
         press  the space bar once before you press <RETURN>.  This will
         eliminate the existing message.

         Increase/Decrease/Reset Counters     4.  Increase/Decrease/Reset Counters

         You may answer I, D, R or blank to this question, where I means
         Increase, D for Decrease, R for Reset or blank for no change to
         the counters.  If you want to change the counter, type I, D  or
         R  to  affect  the  counter by the amount specified in the next
         parameter.  All addresses printed (NOT all those in the Mailing
         List  if  you  requested  a  sublist)  will have their counters
         affected in the same way.  This allows you to keep track of how
         often addresses have been printed (e.g., how often you sent out
         late notices).  You can change individual counters by using the
         Update option from the Main Menu.

         Number to Increase/Decrease/Reset Counters     5.  Number to Increase/Decrease/Reset Counters

         Type the number by which you want the counters  changed.   This
         number  is  ignored  if the answer to the previous parameter is
         blank (i.e., no change).  If you are typing multiple copies  of
         labels, the counter will still be affected only by this number.

         (SAFE upper limit = 99)

         Number of copies of labels     6.  Number of copies of labels

         This is the number of copies of  each  address  that  you  want
         Smart  Mailer  to  print.   Smart Mailer prints each set of the
         same address together.  That is, it does NOT print each address
         once, and then go back and do it all over again.

         (MINIMUM = 1, SAFE upper limit = 5)

         Number of labels across a page     7.  Number of labels across a page

         This is the number of labels that can be printed across a  page
         of labels.

         (MINIMUM = 1, SAFE upper limit = 5)

         Number of spaces at left margin     8.  Number of spaces at left margin

         This is the number of spaces to leave at the left margin before
         starting to print the address information.

         (SAFE upper limit = 20)

Advanced TopicsAdvanced Topics                                               Page 10-15


         Number of characters per address line     9.  Number of characters per address line

         This is the number of characters that can fit across a label.

         (MINIMUM = 10, SAFE lower limit = 30, SAFE upper limit = 65)

         Number of characters between left edges    10.  Number of characters between left edges

         This is the number of characters between the left edge  of  one
         label and the left edge of the label beside it.

         (MINIMUM = 11, SAFE lower limit = 33, SAFE upper limit = 70)

         Number of address lines per label    11.  Number of address lines per label

         This is the number of address lines that can fit on a label.

         (MINIMUM = 2, SAFE lower limit = 5, SAFE upper limit = 20)

         Number of lines between top edges.    12.  Number of lines between top edges.

         This is the number of lines between the upper edge of one label
         and the upper edge of the label below it.

         (MINIMUM = 3, SAFE lower limit = 7, SAFE upper limit = 21)


Figure 10-4 shows the  relationship  between  certain  label  parameters
(numbers 8 to 12).




















        8 - Number of spaces at left margin
        9 - Number of characters per address line
       10 - Number of characters between left edges
       11 - Number of address lines per label
       12 - Number of lines between top edges
        

Figure 10-4:  Example - Label ParametersFigure 10-4:  Example - Label Parameters


Advanced TopicsAdvanced Topics                                               Page 10-16


Where applicable, Smart Mailer checks the  parameter  values  to  ensure
that  the answers are both possible to implement, and reasonable.  Smart
Mailer can not generate labels  with  a  parameter  that  is  under  the
MINIMUM.   Smart  Mailer  will  produce  labels with parameters that are
outside the SAFE limits, but may not  produce  reasonable  results.   In
some  cases, Smart Mailer will check the combination of parameters.  For
example, if the product of the number of  characters  per  address  line
times the number of labels across the page, plus the number of spaces at
the left margin is greater than the maximum length of  the  print  line,
then Smart Mailer will display an error message.

Label Parameters for Typical Label SizesLabel Parameters for Typical Label Sizes

Table 10-2 gives the correct settings for a few  standard  label  sizes.
It  is  assumed  the  printer  is set up to print 10 characters per inch
(horizontally) and 6 lines per inch (vertically).



Table 10-2:  Label Parameters for Typical Label SizesTable 10-2:  Label Parameters for Typical Label Sizes


                                Label Size
                        4" x 1-7/16"    3-1/3" x 15/16"
                        ------------    ---------------

Characters per              38                33
Address Line

Characters between          41                36
Left Edges of Labels

Number of Address            8                 5
Lines per Label

Number of Lines              9                 6
Between Top Edges

Advanced TopicsAdvanced Topics                                               Page 10-17


10.3.2  Lining Up Labels

If you asked to have a test printing of the labels,  Smart  Mailer  will
print  a  row  of  address templates which indicate the placement of the
largest possible address.  It will be printed for as many labels as  you
have requested across the page.

This is the template form:

   L ---------- TOP ----------- R    L ---------- TOP ----------- R
   L                            R    L                            R
   L                            R    L                            R
   L                            R    L                            R
   L                            R    L                            R
   L                            R    L                            R
   L -------- BOTTOM ---------- R    L -------- BOTTOM ---------- R


Once the template is printed, you can realign the labels in the printer,
and/or  readjust  the label parameters.  You can have Smart Mailer print
the sample test templates as many times as you wish before Smart  Mailer
actually  starts  printing  the entire set of labels.  In fact, to check
the vertical alignment, it  is  recommended  that  you  print  two  test
patterns.

Advanced TopicsAdvanced Topics                                               Page 10-18


10.4  Creative Uses of the Smart Mailer System

This section is intended to start you thinking about the different  ways
Smart  Mailer  can  be  useful  to  you.   We  encourage you to use your
imagination.



10.4.1  Types of Information

Smart Mailer can be used for things  other  than  just  addresses.   You
could use it for parts inventory or as a general label maker.

Parts InventoryParts Inventory

To use Smart Mailer for parts inventory, you could define  your  address
fields as follows:

Name:                   Suppliers Company Name
Address Line 1:         Suppliers Address
Address Line 2:
Address Line 3:
City/Town:              Suppliers City/Town
State/Country:          Suppliers State/Country
Zip Code:               Suppliers Zip Code
Category 1:             QTY ORDERD
Category 2:             QTY RECEVD
Category 3:             QTY SHIPED
Category 4:             PRICE
Category 5:             STORGE LOC
Category 6:             DATE EXPCT
Counter:
Remarks:                Part Description
Primary ID:             PART NUMBER
Alternate ID:           PART NAME


General Label MakerGeneral Label Maker

Smart Mailer can be used to produce labels for almost any purpose.   For
example,  if  you  enter  a name as 'Company Confidential' or 'Fragile -
Contains Glass', then you can produce an unlimited number of labels with
those messages.

Advanced TopicsAdvanced Topics                                               Page 10-19


Library RecordsLibrary Records

Smart Mailer can be used to keep track of your personal library records.
For example, you could define your address fields as follows:

Name:                   Person Borrowing Book
Address Line 1:         Person's Address
Address Line 2:
Address Line 3:
City/Town:              Person's City/Town
State/Country:          Person's State/Country
Zip Code:               Person's Zip Code
Category 1:             LOAN DATE
Category 2:             TELEPHONE
Category 3:             RETURNED
Category 4:             PRICE
Category 5:             CATLOG NO.
Category 6:             
Counter:
Remarks:                Book Title
Primary ID:             System Generated
Alternate ID:           System Generated



10.4.2  Types of Forms

Smart Mailer can print information on anything that can be loaded into a
printer.   In  addition to standard paper and labels, you might consider
letterhead, rolodex cards, post cards, index cards, preprinted forms, or
envelopes.   For example you might try printing addresses on one side of
a set of post cards, then turning them over,  reloading  them  into  the
printer,  and  print  a  message,  using  a special address like the one
below:

          name:  Come to our semi-annual sale!
address line 1:  XYZ Store is slashing prices
address line 2:  on computers now thru Dec 1st
address line 3:  123 Main St, Anytown, USA


                                GLOSSARY                                GLOSSARY




Address FieldAddress Field           One  piece  of  information  contained   in   an
                        address,  such as zip code.  Every address field
                        has a maximum length.  Any field  may  be  blank
                        except for the Primary ID.

AlphanumericAlphanumeric            A contraction of alphabetic and numeric; the set
                        of  characters  that  compose  text; letters and
                        numbers.  Special characters are also considered
                        alphanumeric.

Alternate IDAlternate ID            A ten character field which  provides  a  second
                        means  of  identification  of mailing addresses.
                        The  system   generated   composition   of   the
                        Alternate ID is determined by the character mix.
                        Duplicate Alternate IDs can exist on  the  file.
                        Any Alternate ID can be changed.

CCLCCL                     Concise Control Language; an abbreviated way  to
                        call  a  RSTS  system  program and to provide it
                        with input of a single command line.

CharacterCharacter               An  element  in  a  set  of  symbols.   A  human
                        readable symbol can be a letter, A-Z, number 0-9
                        or  a  special  symbol.   Some  machine-readable
                        symbols  such  as  a  tab or carriage return are
                        "non-printing" because they cannot be  displayed
                        on a terminal or printer.

Character MixCharacter Mix           Determines the composition of the  Alternate  ID
                        if  it is system generated.  The mix can include
                        the first part of both the first and last names,
                        but  the  sum  of  the number of characters from
                        each  must  always  equal  10.   If   the   user
                        specifies  the  Alternate ID, then the character
                        mix is not used.

ComparisonComparison              Used as part of the sublist  definition.   Valid
                        comparisons are Is (default), Is Not, Above, Not
                        Above,  Below,  Not  Below,  Between,  and   Not
                        Between.

ConnectionConnection              Joins two or more sublist definition requirement
                        lines.   Valid  connectors are And (default) and
                        Or.

GlossaryGlossary


CounterCounter                 A field (0-9999) in each address  which  enables
                        you  to  track  the  number  of  times  you have
                        printed  a  given  label.   You  can   increase,
                        decrease,  or  reset the counter of each address
                        printed via the Label Menu every time you  print
                        labels.

Date FieldDate Field              Defaults to today's date.  The date field format
                        is DD-MMM-YY (e.g., 01-JAN-83)

DefaultDefault                 The answer that is suggested by Smart Mailer  as
                        being  the  most  common or the expected answer.
                        You may accept this default answer  by  pressing
                        <RETURN>.

DeviceDevice                  A machine attached to a computer usually used to
                        perform input and output operations.

Fixed SpacingFixed Spacing           Ten or twelve characters per inch  depending  on
                        if  the printer is producing pica or elite type.
                        (See Variable Spacing.)

HardcopyHardcopy                Computer output printed on paper, such as from a
                        line printer.  Also called listing or printout.

ListingListing                 Computer output printed on paper, such as from a
                        line printer.  Also called hardcopy or printout.

LoginLogin                   The process of gaining access  to  the  computer
                        system; an identification procedure.

LogoutLogout                  The process of ending a computer session.

MonitorMonitor                 A  master  control  program  that  oversees  the
                        computer  users, schedules operations, allocates
                        resources, and performs input and output.

NonqueuableNonqueuable             A printer that can only handle one print request
                        at  a  time.   A printer is nonqueuable if it is
                        already printing and you get  a  message  saying
                        the  printer  is  busy.   Wait  and try to print
                        later.  (See Queuable.)

NumericNumeric                 A field which allows numbers only.  If you  type
                        a  dollar  sign,  comma,  decimal  point, or any
                        other  non-numeric  character,  the  answer   is
                        invalid and you must retype the data.

GlossaryGlossary


Operating SystemOperating System        A  master  control  program  that  oversees  the
                        computer  users, schedules operations, allocates
                        resources, and performs input and output.

OutputOutput                  The act  of  producing  results,  the  processed
                        data.   For example, when your terminal displays
                        the contents of a  file,  the  terminal  is  the
                        output device, the file contents are the output.

ParameterParameter               A parameter is a variable that can  be  set  (or
                        reset) by the user (or the System Manager) which
                        affects the way Smart Mailer works.  It is  used
                        to tailor the system for the individual needs of
                        the users.

PresortPresort                 A  mailing  option  which  is  offered  by   the
                        U.S. Postal  Service  enabling you to save money
                        when mailing in bulk.

Primary IDPrimary ID              Main identifier of each mailing  address.   Once
                        assigned,  you  cannot  change  the  Primary ID.
                        Each Primary  ID  must  be  different.   If  the
                        system   generates  the  Primary  ID,  numbering
                        begins  at  a  number  assigned  by  the  System
                        Manager   and   continues  sequentially.   Every
                        Primary ID  (including  a  user-defined  ID)  is
                        verified to assure that it is different from all
                        the ID's of the other addresses.

PromptPrompt                  A symbol or message  indicating  the  system  is
                        waiting to receive input from you.

QueuableQueuable                A printer that allows you to send it information
                        to  print and enables you to continue processing
                        while it is printed.   Many  print  requests  to
                        print  information  can  be  'queued up' to wait
                        until   the   printer   is   available.     (See
                        Nonqueuable.)

<RETURN><RETURN>                A key on the terminal that ends a line that  you
                        type and inputs it to the computer.

SoftwareSoftware                A set of programs that controls the operation of
                        a computer system.

SublistSublist                 A list which  Smart  Mailer  extracts  from  the
                        entire  mailing  list,  based  on  user  defined
                        criteria.  A sublist  only  exists  when  it  is
                        being used.  It is not stored.  Every time it is
                        needed it is recreated from the  master  Mailing
                        List by using the sublist definition.

GlossaryGlossary


Sublist DefinitionSublist Definition      The specific criteria which enables Smart Mailer
                        to extract a sublist.

Temporary SublistTemporary Sublist       A one-time sublist definition which  extracts  a
                        sublist  during the current Smart Mailer session
                        only.  Once the session is over,  the  temporary
                        sublist definition is gone.

ValueValue                   Address  fields  are   compared   against   user
                        specified  values  to  determine  if  an address
                        meets the sublist qualifications.

Variable SpacingVariable Spacing        A  variable  number  of  characters   per   inch
                        depending  on  the  combination  of  letters and
                        their spacing.  (See Fixed Spacing.)

                                 Index                                 Index


                                 INDEX



            -A-            -A-                       Conventions
                                        Data Entry, 1-5
Address                               Create
  Adding, 3-7                           List Document File, 7-1, 7-2
  Changing/Updating, 3-12               Mailing List, 2-1
  Displaying, 3-18                      Sublist Definition, 4-6
  Removing, 3-19                      Creative Uses of Smart Mailer,
Address Fields                            10-18
  Description of, 3-2
                                                  -D-Address ID                                        -D-
  Specify, 3-12
Advanced Topics, 10-1                 Display
  PRESORT, 10-1                         Address, 3-18
    References, 10-7                    Category Definition, 8-9
    Rules, 10-1                         Mailing List, 5-1
    Statistics, 10-3, 10-5              Sublist, 5-1
  Sample Labels, 10-6                   Sublist Definition, 4-15
  Sublist Definition                    Total Addresses Report, 9-4
    Rules, 10-8                       Display and Print Addresses
  Sublist Definition                    Difference Between, 5-1
      (Multi-line)                    Duplicate Alternate ID, 3-16
    Rules, 10-9
                                                  -F-Alternate ID, 2-4                                 -F-
  Character Mix, 2-4
  Duplicates, 3-16                    Files
                                        Smart Mailer, 1-3
 
            -C-            -C-
                                                  -G-                                                  -G-
Category
  Description of, 2-6, 8-1            General Guidelines, 1-5
  Initialization Screen, 2-12         Getting Help, 1-5
  Initialization Type Codes, 2-7      Getting Started, 1-11
  Labels, 1-4, 2-6
Category Definition
                                                  -I-  Displaying, 8-9                                 -I-
  Menu, 8-2
  Printing, 8-7                       Introduction, 1-1
  Updating/Adding, 8-4                Introduction Screen, 1-12











                                Index-1

                                 Index                                 Index


            -L-            -L-                       Menus (Cont.)
                                        List Selection, 5-2, 6-3, 7-2,
Label, 10-11                                9-1
  Format Table, 10-12                   Main Menu, 1-14
  Menu, 6-13, 10-13                     Organization of Menu Screens,
  Parameters, 10-13                         1-10
    Description of, 10-11               Output Device, 1-8, 6-10, 8-7,
    for Typical Label Sizes,                9-5
        10-16                           Output Format, 6-7
  Printing, 6-13, 10-11                 PRESORT, 6-12, 10-4
Labels                                  Print Sort, 6-5
  Lining Up, 10-17                      Report, 9-3
List Document File                      Sort, 5-4, 7-4
  Creating, 7-1, 7-2                    Statistics Report, 9-3
List Selection                          Structure of, 1-9
  Menu, 5-2, 6-3, 7-2, 9-1              Sublist Definition, 4-5
Log On/Off, 1-11                        Update, 3-6
 
                                                  -N-                                                  -N-
            -M-            -M-
                                      Naming
Mailing List                            Mailing List, 2-9
  Categories, 1-4, 2-6                  Sublist, 4-6
  Category Initialization, 2-12
                                                  -O-  Choosing, 1-13                                  -O-
  Confirming Name, 2-10
  Creating, 2-1                       Output Device
  Displaying, 5-1                       Choosing, 1-7
  Enter Name, 1-13, 2-9                 Menu, 1-8, 6-10, 8-7, 9-5
  Files, 1-3                          Output Format Menu, 6-7
  Parameter Definitions, 2-2
                                                  -P-  Parameter Screen, 2-10                          -P-
  Parameters, 1-3, 2-2
  Printing, 6-1, 6-3                  Parameter Definitions, 2-2
  Sorting, 6-2                        Parameter Screen, 2-10
  Statistics Report, 9-1              Parameters
  Sublist Definition, 1-4, 4-1          Label, 10-11, 10-13, 10-16
  Transfer to Another, 1-15             Mailing List, 1-3, 2-2
  Updating, 3-1                       PRESORT
Main Menu, 1-14                         Addresses, 6-6, 10-1
Menus                                   Menu, 6-12, 10-4
  Category Definition, 8-2              Non-First Class Mail, 10-7
  Label, 6-13, 10-13                    References, 10-7











                                Index-2

                                 Index                                 Index


PRESORT (Cont.)                       Statistics Report
  Rules, 10-1                           Menu, 9-3
  Statistics, 10-3, 10-5              Structure of
Primary ID                              Menus, 1-9
  Description of, 2-2                 Sublist
  Sort Address by, 5-5                  Description of, 4-1
Print                                   Displaying, 5-1
  Category Definition, 8-7              Empty, 10-10
  Labels, 10-11                         Naming, 4-6
  Mailing List, 6-1, 6-3                Printing, 6-1, 6-3
  Sublist, 6-1, 6-3                     Statistics Report, 9-1
  Sublist Definition, 4-14            Sublist Definition, 4-1
Print Sort                              Comparisons, 4-2
  Menu, 6-5                             Comparisons Table, 4-3
Program Structure, 1-4                  Connectors, 4-4
                                        Creating, 4-6
            -R-            -R-                         Description of, 4-1, 10-8
                                        Displaying, 4-15
Remove                                  Field Names, 4-2
  Address, 3-19                         Format, 4-2
  Sublist Definition, 4-16              Menu, 4-5
Report                                  Printing, 4-14
  Mailing List Statistics, 9-1          Removing, 4-16
  Menu, 9-3                             Rules, 10-8, 10-9
  Sublist Statistics, 9-1               Show All, 4-18
                                        Updating/Adding, 4-11
            -S-            -S-                         Values, 4-4
 
                                                  -T-Smart Mailer                                      -T-
  Files, 1-3
  Functionality, 1-1                  Transfer to Another Mailing List,
  Starting, 1-11                          1-15
  Structure, 1-3
  Utility, 1-4
                                                  -U-Sort                                              -U-
  Description of, 6-2
  Menu, 5-4, 7-4                      Update
Sorting                                 Menu, 3-6
  Print Sort, 6-5                     Update/Add
Sorting Order, 6-2                      Category Definition, 8-4
Specify Address ID, 3-12                Sublist Definition, 4-11
Starting Smart Mailer, 1-11           Update/Change
State Abbreviations, 3-5                Address, 3-12

                            Back Cover Ruler





















<blank page for back cover ruler artwork>