<LF>
177110	000027	    'S	? 'D
177110	000030	    'Y	? 'M
177110	000031	    '0	? '1
177110	000032	    ':	? <LF>
177110	000033	    '[	? <LF>
177110	000034	    '0	? '0
177110	000035	    '0	? '0
177110	000036	    '1	? '2
177110	000037	    ',	? <LF>
177110	000040	    '0	? '2
177110	000041	    '1	? '5
177110	000042	    '3	? '4
177110	000043	    ']	? ^C		;uparrow C - not CTRL/C for ONLPAT



The following assumes that SY0:[1,13] is the TYPE device/account.   If  not,
substitute  the device/account you selected in the previous step in place of
the "SY0:[1,13]'s" below.  


Move the TYPE help message file to the TYPE account by
 
PIP SY0:[1,13]*.*<40>/MO:1536=TYPE.HLP
 
("/MO:1536" is a special mode that places the file at the top  of  the  TYPE
account's directory.) 


Create the 'No Ready' program by
 
SWITCH BASIC					-if necessary
NEW NREADY
10 V$=SYS(CHR$(5%))
20 END
COMPILE SY0:[1,13]<40>/MO:1536


Create the run-time system invoking program by

(It is assumed that the CCL UT runs the program $UTILTY.)
 
PIP SY0:[1,13]TYPE.TYP<104>/MO:1536=NL:/RTS:TYPE
 
PIPing TYPE.TYP from the null device (NL:) creates a zero block  file  which
is  only used to call TYPE.RTS.  Eliminate SY0:[1,13]TYPE.TYP from any auto-
matic process that kills zero length files.  



Erskine College TYPE                                                  Page 4
Installation Notes


If you have used the SET option of the RSTS init code  to  set  any  or  all
KB:'s  and/or LP:'s PRIV and you want non-privileged users to type to one of
these privileged devices from some other KB:, change  TYPE.TYP's  protection
code to <232> by typing
 
PIP SY0:[1,13]TYPE.TYP<232>/RE
 
Leave TYPE.TYP's protection code <104> (as established in the previous step)
if  you  have  not set KB:'s or LP:'s PRIV or you do not want non-privileged
users sending data  anywhere  other  than  to  their  own  terminal  or  any
non-privileged KB:/LP:.  


Add the following to your running system and to your start up files:
 
UT
ADD TYPE
CCL TY-PE=SY0:[1,13]TYPE.TYP;0
EXIT
 
If you choose not to use the CCL "TY-PE", you can use something else such as

UT CCL WR-ITE=SY0:[1,13]TYPE.TYP;0 





Erskine College TYPE                                                  Page 5



            * * * *  T Y P E   U S E R ' S   G U I D E  * * * *



If TYPE's CCL alone is typed, a help message is printed.  



1.0  File specs - some examples

 
TY JUNK.TXT		-will print the file JUNK.TXT
 
TY *.TXT		-will print all files with extension .TXT
 
TY .TXT			-same as TY *.TXT
 
TY REPORT.*		-will print files named REPORT with any extension
 
TY REPORT		-same as TY REPORT.*
 
TY REPORT.		-will print the file REPORT. (null extension)
 
TY INFO??.LST		-will print INFOA.LST, INFO24.LST, INFO.LST, etc.
 
TY *.*			-will print all files in the current account
 
TY JUNK.LST,JUNK.TXT	-will print JUNK.LST 1st followed by JUNK.TXT
 
TY *.LST, *.TXT		-will print all .LST files then all .TXT files
 
TY [100,2]FILE.TXT	-will print FILE.TXT from account [100,2] if its
			 protection code allows transfer



2.0  /F - form feed 1st

/F simply sends a form feed (ASCII 12.) before the file's data is  transmit-
ted  and  it places additional form feeds between files.  This allows one to
use one form for LOGIN, for a catalogue of files,  etc. then  to  have  TYPE
move  to  the  top of a clean form before printing begins.  (This requires a
terminal that knows what to do with a form feed!) 



3.0  /S - form feed after 1st file

/S is the same as /F except that it does not output a form feed  before  the
first  file.  This switch is useful when you are using a LA50 connected to a
VT220's printer port.  


Erskine College TYPE                                                  Page 6
User's Guide


4.0  /P - VT220 printer port

/P turns on a VT220's printer port, sends the file(s), and  then  turns  off
the  printer port.  Note:  If you use CTRL/C to halt TYPE, it will not auto-
matically turn oTYPE  DOC[.050001]TYPE  .DOC[.050001] 	  X1í˜€4¿|HÞï þÿÿ[ú«4ÿ;ßïöëÿÿÝûÿIßkûÿ(Ÿ«ûÿ&ûÿ'(	«á«ôÑk
ß«Hûÿ&ú«PïŠú«`ï‚ßï®ëÿÿŸ«
ûÿüÐ\žËàïR™rP �P2PPzPP{�PPP÷PP2P~ûÿ®ñ�ÿÿÿÿ\ÐÿŸ«ûÿªŸ«$ûÿ ûÿ�Ð\Ã\T‘D«á �0D«áó	\ìÎ~ûÿŠŸ«
ûÿhûÿi)	«ô«á+Ô\Â	^(	«ánÂ
^(
ïëÿÿn°«pÀ\Ð^«tú«xÿYÀ\^úË€ÿÐ\ßïÎêÿÿÝûÿ!ßkûÿŸ«ûÿþûÿÿÐVÕk<Ý\ÝûÿñžFË×ïË°<�Ë´ßË¬ûÿÇûÿÌÖ\À�VÑVkÆ”úË¤ÿ—1`þ@ÐïlüÿÿP ABCDEFGHIJKLMNOPQRSTUVWXYZ$.?0123456789<@<¼SÐ¬TÐ¬
UÔQÕS><„PÑP�ÿùÐ�å¹P×S'{�@PRP�B¯ …×S{(PRP�B¯’…×S�@¯‰…¾@@Œ˜("@$$Ø#0$è#$8$%˜$%(%è$!@"FORRTLLIBRTL7-./%

<=2&?'-@O{[lP}M]\Nk`Kaðñòóôõö÷øùz^L~no|ÁÂÃÄÅÆÇÈÉÑÒÓÔÕÖ×ØÙâãäåæçèéJàZ_my�‚ƒ„…†‡ˆ‰‘’“”•–—˜™¢£¤¥¦§¨©ÀjÐ¡???????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????ÿ\	\\\\

\\\\\-\\\\\
\\\\\\\\\\\\\\\\ \\\\\\\\\[.<(+!&\\\\\\\\\]$*);^-/\\\\\\\\|,%_>?\\\\\\\\\`:#@'="\abcdefghi\\\\\\\jklmnopqr\\\\\\\~stuvwxyz\\\\\\\\\\\\\\\\\\\\\\{ABCDEFGHI\\\\\\}JKLMNOPQR\\\\\\\\STUVWXYZ\\\\\\0123456789\\\\\ÿ	


- !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNOPQRSTUVWXYZ[\]^_`ABCDEFGHIJKLMNOPQRSTUVWXYZ{|}~€�‚ƒ„…†‡ˆ‰Š‹Œ�Ž��‘’“”•–—˜™š›œ�žŸ ¡¢£¤¥¦§¨©ª«¬­®¯°±²³´µ¶·¸¹º»¼½¾¿ÀÁÂÃÄÅÆÇÈÉÊËÌÍÎÏÐÑÒÓÔÕÖ×ØÙÚÛÜÝÞßÀÁÂÃÄÅÆÇÈÉÊËÌÍÎÏðÑÒÓÔÕÖ×ØÙÚÛÜÝþÿ@ïgïgï†h<ïi|ï¿o<ïËm<ï4p<ï’p<ïêk|ïZn<ïÁl
ïfr
ï†rï“wïšx<ï¯x<ïµx<ï¦xïÞº<ïæºï…w@ï]¿@ï¿@ï–¿ïfÉïjÉïnÉïrÉïŠÉüïúÎüï�Ñüï]æïéï¦êïZêïæìüïîïòîïöîïïïeð@ïñ@ïÚð|ï>ñ
ï†ñ|ï
òüïÆò|ïÒýïÑv<ïHÿïï¢|ï€	ï‚	|ï®	ï´	|ïxïz|ï
	ï	|ïzï€ït
ïf
ïrï’ïÎ<ïòï&ïüï^ ü@ïâ&ü@ïŽ'üï*/üïV,ï"?ïLhï:hïÒmïBmüïz|ï¼zï±{üïäxüï`yüï²~|ïf�ïN‚|@ï@ƒ|@ïÍ‚|@ïƒüïôƒüïÝƒüïÆƒ<ïn�ïs�<ïê�ïó�|ïÅŽï	�|ïˆ�ï¸�|ïeŽïpŽ|ïuŽï€Ž|ï-Žï-Ž@ïš›ï§›üïî›|ï‚±üïæ±<ï¾²üï2³üï†»ïš»üï€»ïÖ»üïr¾ï�¾|ïªÂ|ïÃüïªÃïZÈïÉüïRÄïMÆüïšÉï ÉüïÊï
Ê|ïžÓï³ÓüïÔïÔüïšÔüïÙï ÙüïnÛïtÛüïÞÛüïºÜüïBÞ|ï·xï±yüïÞvüïZw|ïJ=|ïR>|ïJ?ï†
ïÎnïÎnï–aïäa|ï–bï²dïºdüïfff the VT220 printer port.  (TYPE, as distributed,  contains
code that works if the VT220 is in VT52 mode.) 



5.0  /R - no "Ready"

This switch makes TYPE not print "Ready" once it is done.  If this switch is
omitted,  a "Ready" or other system prompt will appear after the text on the
last form.  



6.0  /x - x copies

TYPE will print x copies of all files specified if it finds a slash (/) fol-
lowed by a single digit 2 to 9.  Note the following examples:
 
TY JUNK.TXT/3        -will print 3 copies of JUNK.TXT
 
TY A.LST,B.LST/2     -will print 2 copies of A.LST then 2 copies of B.LST



7.0  /N - name 1st

/N tells TYPE to preface each copy of each file with the name of the file.  



8.0  /Q - query mode

When the /Q switch is used, TYPE prints each file name that it finds to pro-
cess  followed  by  a  question  mark.   IF  a  Y is typed by the user, TYPE
proceeds to print that file.  If any other character is  typed,  TYPE  skips
that file and presents any additional files it finds to process.



9.0  /B - binary mode

The /B switch makes TYPE send the data in a file to a user's terminal in bi-
nary mode.  This is useful when punching a paper tape on an (antique) termi-
nal when you want tab characters to stay tabs and not to be translated  into
a  series  of  spaces,  etc.  This mode is also useful when you want to send
text that contains ESCape sequences to a terminal.  /B automatically sets /R
(no "Ready").  


Erskine College TYPE                                                  Page 7
User's Guide


10.0  Directed output

TYPE opens "KB:" for output.  You can direct TYPE's  output  to  some  other
terminal  (KBn:) or to a line printer (LPn:).  The following command directs
TYPE's output to the line printer (LP0:):  

ASSIGN LP:KB 

    NOTE:  TYPE V7.7 cannot determine that an output device is off-line.
    --------------------------------------------------------------------

To direct TYPE's output to KB2:, enter 

ASSIGN KB2:KB 

Use the DEASSIGN command to release either assignment.  



11.0  All done

TYPE sends a series of three bells to signal "all  done"  except  in  binary
mode (/B).  



12.0  Some perhaps strange but expected happenings

 
TY XX.LST,XX.LST/9	-prints 18 copies of XX.LST
 
TY YY.LST/25		-prints 2 copies of YY.LST, 2nd digit is ignored
 
TY ZZ.LST/3/5		-prints 5 copies of ZZ.LST, earlier /3 is ignored
 
TY A.LST/2,B.LST/3	-prints 3 copies of A.LST only, "/" terminates
			 file spec scan.  Switches must be last!
 
 
If WORK.BAC has a protection code with bit 6 set such as <104> (run only),
 
TY WORK.BAC		-prints nothing.
 
 
If RIDICU.LAS has a file size greater than 65,535 blocks,
 
TY RIDICU.LAS		-will not work properly.  No attempt has been
			 made to treat this as an error.
 
ASSIGN DM0:KB		-Is not allowed for obvious reasons!
TY <anything>