rint head".  Zero is the
		right hand margin.  DDHORC is left hand margin
17	DDHORC	device's line width plus one


		DDSTS	Device Characteristics Flags

bit	symbol	description

 8	DDPRVO	ownership requires privlege
 9	DDRLO	read priveges are never given for this device
10	DDWLO	write privileges are never given for this device
11	DDNET	device exists elsewhere in a DECNET network
12		unused
13	DDAUX	device can use KMC11 bridge blocks
14	DDAUXA	device is currently bridged to a KMC11
15	DDSTAT	not used by monitor.  Cleared each time the device is closed.
		Can be used by the driver


		DDCNT Device flags

bit	symbol	description

8-12		unused
13	DDCONS	device is owner's console terminal
14	DDUTIL	temporarily assigned to FIP
15	DDASN	explicitly assigned by job in DDJBNO




			Keyboard DDB's

offset	symbol	description

 0	DDIDX	driver index
 1	DDSTS	status and access control byte  (See general DDB)
2-5		see general DDB
 6	DDCNT	init count and assignment control (See general DDB)
 8	DDFLAG	device specific flags (See below)
10	DDBUFC	BCB (Buffer Chain Block) for output.  See DDB offset 10
16-17		see general DDB
18	TTINPT	BCB (Buffer Chain Block) for input.  See DDB offset 10
24	TTMODE	mode (See below)
26	TTDLMC	delimiter counter
27	TTPDLM	terminal's private delimiter
28	TTCHAR	terminal's characteristics (See below)
30	TTINTF	terminal's interface flag (See below)
32	BCB (Buffer Chain Block) for type ahead.  See DDB offset 10.
38	echo control field size and mode
	bits 1-6 are field size and bit 7 is mode (0 = keypunch)
39	paint character and field active flag
	bits 8-14 are paint character and bit 15 indicates the field is active

		Bits in DDFLAG
	
bit	name		description
 0	TTLFRC		on after Force/Broadcast; off on ^C
 1	TTNBIN		output next in binary mode
 2	TTRSX1		Current RSX mode low order bit
 3	TTDDT		DDT sub-mode
 4	TAPE		tape mode
 5	NOECHO		not echoing
 6	LCLCPY		local copy
 7	TT2741		2741 type terminal
 8	TTRSX2		current RSX mode high order bit
 9	TTHUNG		terminal "hang" pending
10	TTDFIL		delay fill to next character
11	TTMSG		processing incoming message
12	RUBOUT		processing rubouts
13	TTSXOF		send XOFF as soon as possible
14	TTXOFF		an XOFF was sent
15	TTSTOP		output temporarily stopped

		Bits in TTMODE
	
bit	name		description
 0	TTBIN		binary input mode
 1	TTTECO		teco mode
 2	TTCRLF		no auto cr/lf mode
 3	TTECTL		echo control mode
 4	TTGARD		guarded terminal mode
 5	TTPCOL		check incoming XON/XOFF
 6	TTFMS		FMS mode
 7	TTTECS		TECO scope mode
 8	TTESEQ		Escape sequence mode
9-15			reserved




		Bits in TTCHAR

bit	name		description
 0	TTGAG		do not broadcast/force to terminal
 1	TTBRK		do not equate "break" with ^C
 2	TTXANY		do XON on any character
 3	TTFUNC		disable special function characters
 4	TTESC		terminal has real escape
 5	TTSCOP		scope type terminal
 6	TTESCI		allow incoming escape sequences
 7	TTLCOU		allow lower case output
 8	TTPODD		desired parity is odd
 9	TTPRTY		check and send with parity
10	TTUPAR		prefix controls with uparrow
11	TTSYNC		stop output if XOFF received
12	TTXON		sending XOFF will stop input
13	TTFORM		hordware form feed/vertical tab exist
14	TTTAB		hardware horizontal tab exists
15	TTLCIN		allow lower case input

		Values in TTINTF

bit		meaning
0-7	INTFAC	Interface type code (INTFAC)
		 0	KL11
		 2	DC11
		 4	DL11
		 6	DE11
		 8	PK11
		10	DJ11
		12	DH11
		14	DZ11
8-11	TTSUBL	sub-line number
 12	TTRDRN	reader run control
 13	TTHPRT	hardware parity
 14	TTMODM	modem control
 15	TTMUX	multiplexor
DDB   DOC[.050021]DDB   .DOC[.050021]	  X1í˜€4¿|HÞï þÿÿ[ú«4ÿ;ßïöëÿÿÝûÿIßkûÿ(Ÿ«ûÿ&ûÿ'(	«á«ôÑk
ß«Hûÿ&ú«PïŠú«`ï‚ßï®ëÿÿŸ«
ûÿüÐ\žËàïR™rP �P2PPzPP{�PPP÷PP2P~ûÿ®ñ�ÿÿÿÿ\ÐÿŸ«ûÿªŸ«$ûÿ ûÿ�Ð\Ã\T‘D«á �0D«áó	\ìÎ~ûÿŠŸ«
ûÿhûÿi)	«ô«á+Ô\Â	^(	«ánÂ
^(
ïëÿÿn°«pÀ\Ð^«tú«xÿYÀ\^úË€ÿÐ\ßïÎêÿÿÝûÿ!ßkûÿŸ«ûÿþûÿÿÐVÕk<Ý\ÝûÿñžFË×ïË°<�Ë´ßË¬ûÿÇûÿÌÖ\À�VÑVkÆ”úË¤ÿ—1`þ@ÐïlüÿÿP ABCDEFGHIJKLMNOPQRSTUVWXYZ$.?0123456789<@<¼SÐ¬TÐ¬
UÔQÕS><„PÑP�