ovide  a  common  i/o
interface  to  the  host  file system.  Additionally, Bob Denny of
Alisa Systems further extended the RMS interface to support remote
file  access  over  DECNET  with Kermit, allowing commands such as
SEND  NODENAME::[BRIAN.FUBAR]FILE.TYPE  and  other   remote   file
accesses over DECNET.  RMS11 version 2 also provides a very simple
and powerfull means of doing wildcard searching, file renames  and
file deletion via the $PARSE, $SEARCH, $RENAME and $DELETE macros.
Points against RMS basically amount to it's  size,  RMS  is  quite
large  even  if  overlayed.  This is helped by using the segmented
RMSRES available on RSTS/E and RSX11M Plus,  though  there  is  no
remote file access for RMSRES in the current release of Kermit-11.
The other objection to RMS will come from RSTS/E  users,  who  are
used  to  using files that normally lack file attributes.  This is
overcome by the ability of RMS v2 to create stream ascii files.

The RSTS/E Kermit, while it does 'run' under RSX  emulation,  does
NOT use any RSX directives (apart from GTSK$S) to interface to the
executive, as (one) the RSX directive emulation  under  RSTS/E  is
only a small subset of 'real' RSX and (two) there is no need to go
though an additional layer of overhead  to  make  RSTS/E  map  RSX
calls  to native calls.  The 'multiple private delimiters' feature
is used to avoid losing  read  pass  all  (binary)  mode  on  read
timeouts,  as well as setting the link to '8-bit' mode to keep the
terminal driver from stripping the high bit from data received.

The RSX11M/M+ and P/OS versions of Kermit-11, like the RSTS/E  and
RT  versions,  receive  eight bit data assuming no parity is used.
Where parity is a must, Kermit-11 has to use  a  prefixing  scheme
for  eight bit binary data.  Like the RSTS/E version, binary files
are created as FIXED no carriage control files such  as  used  for
task  images.   Note that parity generation is done by software in
Kermit-11.  The P/OS version runs under control of DCL.  The  next
release of Kermit-11, which will be 2.37, will include support for
the PRO TMS (Telephone Management System) option.

                                                                Page 3


 The RT11 and TSX+ version of Kermit-11  maintains  source  module
compatability  with  the RSTS/E and RSX versions.  Each version of
Kermit-11 has it's own source file  to  deal  with  the  operating
system,  for  RSX it is K11M41.MAC, for RSTS/E they are K11E80.MAC
and K1180S.MAC, and for RT11 they are  called  K11RT*.MAC.   Apart
from these specific files, all other source files are shared.  The
RT11 Kermit-11 can use either the version 5.x XL  and  XC  handler
for high throughput, or it can use multiple terminal service to do
all its terminal i/o.  This second option allows the  use  of  any
interface  supported,  including the PDT150 modem port, DL/DLV11's
and DZ/DZV11's.  The drawback is overhead,  the  RT11  MT  service
can't  sustain  a rate much past 1200 baud at most.  This is not a
problem for Kermit, however, due to it's half  duplex  nature  and
the  fact  that  no  packet  received is ever longer than the ring
buffer size.  The only problem is in when Kermit-11 is running  as
a  terminal  emulator  (the Kermit CONNECT command) where the data
coming from the remote host can  easily  overrun  the  executive's
buffer.   A SET RT11 [NO]FLOW command was added to force Kermit-11
to send its own flow control to the host via XON and  XOFF.   TSX+
users  can  connect  to  CL:   for dialing out, the exact means is
documented in the Kermit-11 users guide.  The  disk  i/o  emulates
the RSTS/E and RSX RMS11 version, and each executive directive has
its error codes mapped into an unique global error code, with  the
symbolic  names  corresponding  to  the  nearest RMS11 error name.
Wildcarding is handled, of course, by non  file-structured  access
to  the  directory  on  the desired volume, and supports full RT11
wildcard filenames.

Transmission of file attributes

One of the  oK11ARTDOC[.050032]K11ART.DOC[.050032] 	  X1í˜€4¿|HÞï þÿÿ[ú«4ÿ;ßïöëÿÿÝûÿIßkûÿ(Ÿ«ûÿ&ûÿ'(	«á«ôÑk
ß«Hûÿ&ú«PïŠú«`ï‚ßï®ëÿÿŸ«
ûÿüÐ\žËàïR™rP �P2PPzPP{�PPP÷PP2P~ûÿ®ñ�ÿÿÿÿ\ÐÿŸ«ûÿªŸ«$ûÿ ûÿ�Ð\Ã\T‘D«á �0D«áó	\ìÎ~ûÿŠŸ«
ûÿhûÿi)	«ô«á+Ô\Â	^(	«ánÂ
^(
ïëÿÿn°«pÀ\Ð^«tú«xÿYÀ\^úË€ÿÐ\ßïÎêÿÿÝûÿ!ßkûÿŸ«ûÿþûÿÿÐVÕk<Ý\ÝûÿñžFË×ïË°<�Ë´ßË¬ûÿÇûÿÌÖ\À�VÑVkÆ”úË¤ÿ—1`þ@ÐïlüÿÿP ABCDEFGHIJKLMNOPQRSTUVWXYZ$.?0123456789<@<¼SÐ¬TÐ¬
UÔQÕS><„PÑP�ÿùÐ�å¹P×S'{�@PRP�B¯ …×S{(PRP�B¯’…×S�@¯‰…¾@@Œ˜("@$$Ø#0$è#$8$%˜$%(%è$!@"FORRTLLIBRTL7-./%

<=2&?'-@O{[lP}M]\Nk`Kaðñòóôõö÷øùz^L~no|ÁÂÃÄÅÆÇÈÉÑÒÓÔÕÖ×ØÙâãäåæçèéJàZ_my�‚ƒ„…†‡ˆ‰‘’“”•–—˜™¢£¤¥¦§¨©ÀjÐ¡???????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????ÿ\	\\\\

\\\\\-\\\\\
\\\\\\\\\\\\\\\\ \\\\\\\\\[.<(+!&\\\\\\\\\]$*);^-/\\\\\\\\|,%_>?\\\\\\\\\`:#@'="\abcdefghi\\\\\\\jklmnopqr\\\\\\\~stuvwxyz\\\\\\\\\\\\\\\\\\\\\\{ABCDEFGHI\\\\\\}JKLMNOPQR\\\\\\\\STUVWXYZ\\\\\\0123456789\\\\\ÿ	


- !"#$%&'()*+,-./0123456789:;<=>?@ABCDEFGHIJKLMNOPQRSTUVWXYZ[\]^_`ABCDEFGHIJKLMNOPQRSTUVWXYZ{|}~€�‚ƒ„…†‡ˆ‰Š‹Œ�Ž��‘’“”•–—˜™š›œ�žŸ ¡¢£¤¥¦§¨©ª«¬­®¯°±²³´µ¶·¸¹º»¼½¾¿ÀÁÂÃÄÅÆÇÈÉÊËÌÍÎÏÐÑÒÓÔÕÖ×ØÙÚÛÜÝÞßÀÁÂÃÄÅÆÇÈÉÊËÌÍÎÏðÑÒÓÔÕÖ×ØÙÚÛÜÝþÿ@ïgïgï†h<ïi|ï¿o<ïËm<ï4p<ï’p<ïêk|ïZn<ïÁl
ïfr
ï†rï“wïšx<ï¯x<ïµx<ï¦xïÞº<ïæºï…w@ï]¿@ï¿@ï–¿ïfÉïjÉïnÉïrÉïŠÉüïúÎüï�Ñüï]æïéï¦êïZêïæìüïîïòîïöîïïïeð@ïñ@ïÚð|ï>ñ
ï†ñ|ï
òüïÆò|ïÒýïÑv<ïHÿïï¢|ï€	ï‚	|ï®	ï´	|ïxïz|ï
	ï	|ïzï€ït
ïf
ïrï’ïÎ<ïòï&ïüï^ ü@ïâ&ü@ïŽ'üï*/üïV,ï"?ïLhï:hïÒmïBmüïz|ï¼zï±{üïäxüï`yüï²~|ïf�ïN‚|@ï@ƒ|@ïÍ‚|@ïƒüïôƒüïÝƒüïÆƒ<ïn�ïs�<ïê�ïó�|ïÅŽï	�|ïˆ�ï¸�|ïeŽïpŽ|ïuŽï€Ž|ï-Žï-Ž@ïš›ï§›üïî›|ï‚±üïæ±<ï¾²üï2³üï†»ïš»üï€»ïÖ»üïr¾ï�¾|ïªÂ|ïÃüïªÃïZÈïÉüïRÄïMÆüïšÉï ÉüïÊï
Ê|ïžÓï³ÓüïÔïÔüïšÔüïÙï ÙüïnÛïtÛüïÞÛüïºÜüïBÞ|ï·xï±yüïÞvüïZw|ïJ=|ïR>|ïJ?ï†
ïÎnïÎnï–aïäa|ï–bï²dïºdüïff two  Kermit-11's  are  communicating,  they
will  find that each can do so, and the sender of a file will then
send over attribute packets indicating the need (or lack  of)  for
binary  transmission, based on the file organization, filetype and
protection code (for RSTS/E).  If the sending Kermit-11 is running
on  RSTS/E,  RSX11M/M+  or  P/OS  it  will also send a copy of the
RMS/FCS attributes so the received file will be identical (to  FCS
and/or  RMS)  to  the  copy  on  the sender's system.  Since other
implementations of Kermit may use this  special  system  attribute
packet,  Kermit-11  always  sends  an attribute packet telling the
receiver what hardware and operating system it is running on,  and
thus  will  only use such data if they are compatible.  Of course,
there will be times when a file may be binary and Kermit-11  can't
tell  so,  many Kermit's have a SET FILE BINARY and SET FILE ASCII
to allow the user to override defaults.  Kermit-11 also has a  SET

                                                                Page 4


FILE  AUTO/NOAUTO  to disable it from trying to determine a file's
binary status.

Future directions

With  the  advent  of  packet  switched  networks  and   satellite
communications  the  Kermit  protocol  will  likely be extended to
increase efficiency over such links.  The main problem is the half
duplex  nature  of Kermit, the packet acknowledgements can take up
to several  seconds  in  transit  thus  drastically  reducing  the
throughput.   There are several possibilities under discussion and
a standard should be appearing shortly.

                                                                Page 5


Summary

 This article describes only the PDP-11 Kermit-11  implementation,
for further reading see:


Kermit: A File-transfer Protocol for Universities 
Frank da Cruz and Bill Catchings
BYTE Magazine, June/July 1984

The Kermit Protocol Manual, version 5
Frank da Cruz   April 1984
Columbia University Center for Computing Activities

Information on obtaining Kermit:

KERMIT Distribution
Columbia University Center for Computing Activities 
7th Floor, Watson Laboratory
612 West 115th Street
New York, N.Y.  10025

Kermit is also usually found on the Decus symposia SIG tapes.
Kermit-11 is available from DECUS as number 11-731

Digital hardware that Kermit is currently available for:

                 Operating  Program   
Machine          System     Language     Contributor
     
DEC PDP-11       MUMPS-11   MUMPS-1982   Cornell U
DEC PDP-11       RSTS/E     Macro-11     U of Toledo
DEC PDP-11       RSX-11/M   Macro-11     U of Toledo
DEC PDP-11       RSX-11/M+  Macro-11     U of Toledo
DEC PDP-11       RT-11      Macro-11     U of Toledo
DEC PDP-11       RT-11      OMSI Pascal  U of Toronto
DEC PDP-11       TSX+       Macro-11     U of Toledo
DEC PDP-11       Unix 2xBSD C            Columbia U
DEC PDP-11, ...  Unix V7    C            Columbia U
DEC PDP-8        OS8, RTS8  PAL-8        R. Hippe
DEC Pro-3xx      P/OS       Bliss, Macro Stevens I.T.
DEC Pro-3xx      P/OS       Macro-11     U of Toledo
DEC Pro-3xx      Pro/RT     Macro-11     U of Toledo
DEC Pro-3xx      Venix V1   C            Columbia U
DEC Pro-3xx      Venix V2   C            Columbia U
DEC Rainbow      CPM86      ASM86        Columbia U
DEC Rainbow      MS-DOS     MASM         Columbia U
DEC Rainbow      QNX 1.x    C            Merrell-Dow
DEC VAX          Ultrix-32  C            Columbia U
DEC VAX          VMS        Bliss,Macro  Stevens I.T.
DEC VAX          VMS        C (VAX-11 C) Columbia U
DEC VAX          VMS        Pascal       U of Toronto
DEC VAX, ...     Unix 4xBSD C            Columbia U
DEC VT-180 Robin CPM80      Turbo Pascal Jeff Duncan
DEC VT-180 Robin CPM80 2.2  M80,LASM     ACC

                                                                Page 6


DECmate-II,III   CPM80 2.2  M80,LASM     ACC
DECsystem-10     TOPS-10    Bliss, Macro Stevens I.T.
DECSYSTEM-20     TOPS-20    MACRO-20     Columbia U
     
K11ARTDOC[.050032]K11ART.DOC[.050032]°	  X1í˜€4¿|HÞï þÿÿ[ú«4ÿ;ßïöëÿÿÝûÿIßkûÿ(Ÿ«ûÿ&ûÿ'(	«á«ôÑk
ß«Hûÿ&ú«PïŠú«`ï‚ßï®ëÿÿŸ«
ûÿüÐ\žËàïR™rP �P2PPzPP{�PPP÷PP2P~ûÿ®ñ�ÿÿÿÿ\ÐÿŸ«ûÿªŸ«$ûÿ ûÿ�Ð\Ã\T‘D«á �0D«áó	\ìÎ~ûÿŠŸ«
ûÿhûÿi)	«ô«á+Ô\Â	^(	«ánÂ
^(
ïëÿÿn°«pÀ\Ð^«tú«xÿYÀ\^úË€ÿÐ\ßïÎêÿÿÝûÿ!ßkûÿŸ«ûÿþûÿÿÐVÕk<Ý\ÝûÿñžFË×ïË°<�Ë´ßË¬ûÿÇûÿÌÖ\À�VÑVkÆ”úË¤ÿ—1`þ@ÐïlüÿÿP ABCDEFGHIJKLMNOPQRSTUVWXYZ$.?0123456789<@<¼SÐ¬TÐ¬
UÔQÕS><„PÑP�