P M L    U S E R S   G U I D E


                      P o r t a b l e   M a t h   L i b r a r y


                                     Version 1.1


                                  February 10, 1983




                                     by Fred Fish


                                       G.A.C.A.

        PML --- C Portable Math Library                                 Page 2
        Introduction



        1.0  INTRODUCTION




        1.1  Document structure


             This document describes the PML library, a mathematical  function
        library for C programs.  It contains the following major sections:

             o  Introduction to the document (this section).

             o  A module description section which is  automagically  produced
                from  documentation  in  each  module's source code by the DEX
                (Documentation Extractor) task and "runoff", a text formatting
                program.

             o  An index also produced from information in the source code.




        1.2  Design Considerations


             In writing this library many tradeoffs had to be considered.  The
        primary  design  goal  was  transportability.  It was desired that the
        final library be easily transportable among a wide class of  machines.
        As  of this release, the library has been used with only minor modifi-
        cations on a DECSYSTEM-20 (a 36 bit machine), a VAX-11/780 under  com-
        patibility mode, and various PDP-11's.

             This portability was achieved by careful isolation of machine de-
        pendencies  and  parameterization of the environment (see references).
        The only assumption made is that the C compiler  can  generate  proper
        code for the four basic operations (+,-,/,*).

             Even though efficiency was considered to be of only secondary im-
        portance,  the final routines compared favorably with an informal test
        "race" against the DECSYSTEM-20 FORTRAN, which has optimized  assembly
        language  library routines.  The PML library routines seldom took more
        than twice as long as the FORTRAN library, and many were close  enough
        to call a draw.

             There are currently only four highly machine  dependent  routines
        in  the Portable Math Library.  When transporting the library to a new
        machine, these should be the only ones in which recoding is necessary.
        These routines, written in machine targeted C, are:

             o  dscale --- scale a double precision floating point number by a
                specified power of two.  Equivalent to multiplication or divi-

        PML --- C Portable Math Library                                 Page 3
        Introduction



                sion by a power of two,  depending  upon  sign  of  the  scale
                value.

             o  dxexp --- extract exponent of double precision floating  point
                number and return it as an integer.

             o  dxmant --- extract mantissa of double precision floating point
                number  and  return  it  as  a double precision floating point
                number.

             o  dint --- discard fractional part of double  precision  number,
                returning  integer  part  as a double precision floating point
                number.


             The entire Portable Math Library is built upon  six  "primitives"
        which compute their values from polynomial approximations.  All others
        can be defined in terms of the primitives  using  various  identities.
        The  primitives  are (1) datan, (2) dexp, (3) dln, (4) dsin, (5) dcos,
        and (6) dsqrt.  Strictly speaking, only one of dsin and dcos could  be
        chosen  as a primitive and the other defined with an appropriate iden-
        tity.  In this implementation however, dsin and dcos  call  themselves
        recursively, and each other, to perform range reduction.



        1.3  Error Handling


             No assumptions are made about whether the four  basic  operations
        are  done by hardware or software.  Any overflows or underflows in the
        basic operations are assumed to be handled by the environment,  if  at
        all.  Pathological cases in the library routines are trapped internal-
        ly and control is passed to an error handler routine  "pmlerr"  (which
        may be replaced with one of the user's choosing) for error recovery.

             The default error handler is conceptually similar to the one used
        by DEC for the FORTRAN compilers.  It contains an internal table which
        allows  various  actions  to  be  taken  for  each  error  recognized.
        Currently  each  error  has a corresponding flag word with three bits,
        each bit assigned as follows:

             o  CONTINUE --- If the bit is set control is returned to the cal-
                ling  routine after completion of error processing.  Otherwise
                the task exits with an error status.

             o  LOG --- If the log bit is set then an error warning message is
                written  to the standard error output channel prior to exiting
                or continuing.  If reset, no message is given.

             o  COUNT --- If the count bit is set then the  task's  PML  error
                count  (internal to the error handler) is incremented.  If the

        PML --- C Portable Math Library                                 Page 4
        Introduction



                total error count exceeds the maximum allowed  then  the  task
                exits  with  error status.  If the count bit is reset then the
                error is ignored with respect to the error count and  exit  on
                limit.


             The default conditions in the error handler  for  all  errors  is
        that  the  CONTINUE, LOG, and COUNT bits are all set.  The error limit
        is set at 10.  These values can be changed  by  suitably  editing  the
        header file "pml.h" and <pmluser.h>.

             The error handler responses can also be changed  dynamically  via
        the following routines:

             o  PMLSFS --- Sets the specified bits in  the  specified  error's
                flag  word.   For  example, "pmlsfs(NEG_DSQRT,CONTINUE | LOG)"
                sets the CONTINUE and  LOG  bits  for  the  "double  precision
                square root of a negative number" error.  The COUNT bit is not
                affected.   The  manifest  constant  values  are  defined   in
                <pmluser.h>.

             o  PMLCFS --- Clears the specified bits in the specified  error's
                flag  word.   For  example, "pmlcfs(NEG_DSQRT,CONTINUE | LOG)"
                clears the CONTINUE and LOG bits  for  the  "double  precision
                square root of a negative number" error.  The COUNT bit is not
                affected.   The  manifest  constant  values  are  defined   in
                <pmluser.h>.

             o  PMLLIM --- Changes the task's PML error limit to the specified
                value and returns the previous value.

             o  PMLCNT --- Returns the current value of the  PML  error  count
                and resets it back to zero.




        1.4  Function Names


             In general, FORTRAN naming conventions  were  followed  since  no
        other  more  obvious convention was apparent.  There is one strong ex-
        ception however, and that is the natural logarithm functions  use  the
        generic name "ln" while the logarithm to the base 10 functions use the
        name "log".  This is consistent with the normal usage in virtually all
        modern  mathematical  and  engineering texts.  How FORTRAN came to use
        "log" and "log10" respectively is beyond me.  This  usage  has  bitten
        many a starting FORTRAN programmer.




        PML --- C Portable Math Library                                 Page 5
        Introduction



        1.5  Installation


             As part of the installation kit, some simple minded testing  pro-
        grams  are  provided.   They  are by no means exhaustive tests or ones
        that carefully check possible trouble areas.   They  are  intended  to
        provide  a  quick  and dirty way of verifying that no gross errors are
        inadvertently incorporated in the library as a result of  improvements
        or  bug  fixes,  and  that the installation is successful.  Future re-
        leases may incorporate more extensive test  routines  and  suggestions
        are solicited.



        1.6  Bugs


             On the subject of bugs, all exterminators are encouraged to noti-
        fy the author of any problems or fixes so that they can be incorporat-
        ed into the next release and renegade versions of the library  can  be
        minimized.  Contact:


                         Fred Fish
                         1346 W 10th Place
                         Tempe, Arizona 85281

                         (602) 894-6881   (home)
                         (602) 932-7000   (work @ GACA)

             Those users with strong numerical analysis backgrounds or experi-
        ence  may  be  able  to suggest better methods for some of the library
        routines.  Many of the higher level routines are simple minded  imple-
        mentations of identities, and may not be nearly as stable as some more
        obscure methods.



        1.7  Transporting To Other Machines


             To transport the Portable Math Library to a processor other  than
        the PDP11 or DECSYSTEM-20, do the following:

             o  Define the machine dependent parameters in "pml.h".

             o  implement the four machine dependent modules listed  previous-
                ly, possibly by using the current versions as a guide.

             o  Compile the rest of the library modules and the  testing  rou-
                tines.   Then link and run the testing routines to verify suc-
                cessful installation.

        PML --- C Portable Math Library                                 Page 6
        Introduction



             o  Repeat as required.


        PML --- C Portable Math Library                                 Page 7
        Runtime modules



        2.0  RUNTIME MODULES


             The PML modules are documented on the following pages.   All  the
        rest of this section was produced by the DEX (documentation extractor)
        utility directly from the source files.  Thus the information reflects
        the current state of the runtime modules.

        PML --- C Portable Math Library                                 Page 8
        CABS



        2.1  Double precision complex absolute value




                                       ********
                                       * CABS *
                                       ********




        DESCRIPTION:

                 Computes double precision absolute value of a  double  preci-
                 sion  complex  argument,  where  "absolute value" is taken to
                 mean magnitude.  The result replaces the argument.


        USAGE:

                 double cabs(z)
                 COMPLEX *z;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes CABS(z) where z = (x) + j(y) from:

                         CABS(z) = DSQRT(x*x + y*y)


        PML --- C Portable Math Library                                 Page 9
        CACOS



        2.2  Complex double precision arc cosine





                                      *********
                                      * CACOS *
                                      *********




        DESCRIPTION:

                 Computes double precision complex arc cosine of a double pre-
                 cision complex argument.  The result replaces the argument.


        USAGE:

                 cacos(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex arc cosine of Z = x + j y from:

                    CACOS(z) = -j * CLN(z + j * CSQRT(1-z*z))


        PML --- C Portable Math Library                                Page 10
        CADD



        2.3  Double precision complex addition





                                       ********
                                       * CADD *
                                       ********




        DESCRIPTION:

                 Computes double precision complex result of addition of first
                 double  precision  complex argument with second double preci-
                 sion complex argument.  The result replaces the  first  argu-
                 ment.   Note  that the complex addition function is so simple
                 that it would not normally be called as a function but simply
                 done "inline".  It is supplied mostly for completeness.


        USAGE:

                 double cadd(z1,z2)
                 COMPLEX *z1;
                 COMPLEX *z2;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes CADD(z1,z2) from:

                         1.      Let z1 = a + j b
                                 Let z2 = c + j d

                         2.      Then CADD(z1,z2) = (a + c) + j (b + d)


        PML --- C Portable Math Library                                Page 11
        CASIN



        2.4  Complex double precision arc sine





                                      *********
                                      * CASIN *
                                      *********




        DESCRIPTION:

                 Computes double precision complex arc sine of a double preci-
                 sion complex argument.  The result replaces the argument.


        USAGE:

                 casin(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex arc sine of Z = x + j y from:

                    CASIN(z) = -j * CLN(CSQRT(1-z*z) + j*z)


        PML --- C Portable Math Library                                Page 12
        CATAN



        2.5  Complex double precision arc tangent





                                      *********
                                      * CATAN *
                                      *********




        DESCRIPTION:

                 Computes double precision complex arc  tangent  of  a  double
                 precision  complex  argument.   The result replaces the argu-
                 ment.


        USAGE:

                 catan(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex arc tangent of Z = x + j y from:

                    CATAN(z) = -j/2 * CLN( (j+z) / (j-z) )


        PML --- C Portable Math Library                                Page 13
        CCOS



        2.6  Complex double precision cosine





                                       ********
                                       * CCOS *
                                       ********




        DESCRIPTION:

                 Computes double precision complex cosine of a  double  preci-
                 sion complex argument.  The result replaces the argument.


        USAGE:

                 ccos(z)
                 COMPLEX *z;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-12


        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex cosine of Z = x + j y from:

                         1.      R_CCOS = DCOS(x) * DCOSH(y)

                         2.      I_CCOS = -DSIN(x) * DSINH(y)

                         Then    CCOS(z) = R_CCOS + j I_CCOS


        PML --- C Portable Math Library                                Page 14
        CCOSH



        2.7  Complex double precision hyperbolic cosine





                                      *********
                                      * CCOSH *
                                      *********




        DESCRIPTION:

                 Computes double precision complex hyperbolic cosine of a dou-
                 ble  precision complex argument.  The result replaces the ar-
                 gument.


        USAGE:

                 ccosh(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex hyperbolic cosine of Z = x + j y from:

                    CCOSH(z) = 0.5 * ( CEXP(z) + CEXP(-z) )


        PML --- C Portable Math Library                                Page 15
        CDIV



        2.8  Double precision complex division





                                       ********
                                       * CDIV *
                                       ********




        DESCRIPTION:

                 Computes double precision complex result of division of first
                 double  precision complex argument by second double precision
                 complex argument.  The result replaces the numerator.


        USAGE:

                 double cdiv(numerator,denominator)
                 COMPLEX *numerator;
                 COMPLEX *denominator;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes CDIV(znum,zden) from:

                         1.      Let znum = a + j b
                                 Let zden = c + j d

                         2.      denom = c*c + d*d

                         3.      If denom is zero then log error,
                                 set r_cdiv = maximum floating value,
                                 i_cdiv = 0, and go to step 5.

                         4.      r_cdiv = (a*c + b*d) / denom
                                 i_cdiv = (c*b - a*d) / denom

                         5.      Then CDIV(znum,zden) = r_cdiv + j i_cdiv

        PML --- C Portable Math Library                                Page 16
        CDIV



        2.9  Complex double precision exponential





                                       ********
                                       * CEXP *
                                       ********




        DESCRIPTION:

                 Computes double precision complex  exponential  of  a  double
                 precision complex argument.


        USAGE:

                 cexp(z)
                 COMPLEX *z;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-13


        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex exponential of Z = x + j y from:

                         1.      R_CEXP = DEXP(x) * DCOS(y)

                         2.      I_CEXP = DEXP(x) * DSIN(y)

                         Then    CEXP(z) = R_CEXP + j I_CEXP


        PML --- C Portable Math Library                                Page 17
        CLN



        2.10  Complex double precision natural logarithm





                                       *******
                                       * CLN *
                                       *******




        DESCRIPTION:

                 Computes double precision complex natural logarithm of a dou-
                 ble  precision complex argument.  The result replaces the ar-
                 gument.


        USAGE:

                 cln(z)
                 COMPLEX *z;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-13


        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex natural logarithm of Z = x + j y from:

                         1.      R_CLN = DLN(CABS(z))

                         2.      I_CLN = DATAN2(x,y)

                         Then    CLN(z) = R_CLN + j I_CLN

        PML --- C Portable Math Library                                Page 18
        CLN



        2.11  Double precision complex multiplication





                                      *********
                                      * CMULT *
                                      *********




        DESCRIPTION:

                 Computes double precision complex result of multiplication of
                 first double precision complex argument by second double pre-
                 cision complex argument.  The result replaces the first argu-
                 ment.


        USAGE:

                 double cmult(z1,z2)
                 COMPLEX *z1;
                 COMPLEX *z2;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes CMULT(z1,z2) from:

                         1.      Let z1 = a + j b
                                 Let z2 = c + j d

                         2.      r_cmult = (a*c - b*d)
                                 i_cmult = (a*d + c*b)

                         3.      Then CMULT(z1,z2) = r_cmult + j i_cmult


        PML --- C Portable Math Library                                Page 19
        CRCP



        2.12  complex double precision reciprocal





                                       ********
                                       * CRCP *
                                       ********




        DESCRIPTION:

                 Computes double precision complex reciprocal of a double pre-
                 cision complex argument.  The result replaces the argument.


        USAGE:

                 crcp(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex reciprocal of Z = x + j y from:

                         1.      Compute denom = x*x + y*y

                         2.      If denom = 0.0 then flag error
                                 and return MAX_POS_DBLF + j 0.0

                         3.      Else CRCP(z) = (x/denom) + j (-y/denom)


        PML --- C Portable Math Library                                Page 20
        CSIN



        2.13  Complex double precision sine





                                       ********
                                       * CSIN *
                                       ********




        DESCRIPTION:

                 Computes double precision complex sine of a double  precision
                 complex argument.  The result replaces the argument.


        USAGE:

                 csin(z)
                 COMPLEX *z;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-12


        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex sine of Z = x + j y from:

                         1.      R_CSIN = DSIN(x) * DCOSH(y)

                         2.      I_CSIN = DCOS(x) * DSINH(y)

                         Then    CSIN(z) = R_CSIN + j I_CSIN


        PML --- C Portable Math Library                                Page 21
        CSINH



        2.14  Complex double precision hyperbolic sine





                                      *********
                                      * CSINH *
                                      *********




        DESCRIPTION:

                 Computes double precision complex hyperbolic sine of a double
                 precision  complex  argument.   The result replaces the argu-
                 ment.


        USAGE:

                 csinh(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex hyperbolic sine of Z = x + j y from:

                    CSINH(z) = 0.5 * ( CEXP(z) - CEXP(-z) )


        PML --- C Portable Math Library                                Page 22
        CSQRT



        2.15  Complex double precision square root





                                      *********
                                      * CSQRT *
                                      *********




        DESCRIPTION:

                 Computes double precision complex square  root  of  a  double
                 precision  complex  argument.   The result replaces the argu-
                 ment.


        USAGE:

                 csqrt(z)
                 COMPLEX *z;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-12


        RESTRICTIONS:

                 The relative error in the double precision square root compu-
                 tation  is  10**(-30.1)  after  three applications of Heron's
                 iteration for the square root.

                 However, this assumes exact arithmetic in the iterations  and
                 initial  approximation.   Additional  errors may occur due to
                 truncation, rounding, or machine precision limits.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home



        PML --- C Portable Math Library                                Page 23
        CSQRT



        INTERNALS:

                 Computes complex square root of Z = x + j y from:

                         1.      ROOT = DSQRT((DABS(x) + CABS(Z)) / 2)

                         2.      Q = y / (2 * ROOT)

                         3.      If x >= 0 then
                                 CSQRT(Z) = (ROOT,Q)

                         4.      If x < 0 and y >= 0 then
                                 CSQRT(Z) = (Q,ROOT)

                         5.      If x < 0 and y < 0 then
                                 CSQRT(Z) = (-Q,ROOT)


        PML --- C Portable Math Library                                Page 24
        CSUBT



        2.16  Double precision complex subtraction





                                      *********
                                      * CSUBT *
                                      *********




        DESCRIPTION:

                 Computes double precision complex result  of  subtraction  of
                 second  double  precision  complex argument from first double
                 precision complex argument.  The result  replaces  the  first
                 argument.   Note  that the complex subtraction function is so
                 simple that it would not normally be called as a function but
                 simply  done  "inline".   It is supplied mostly for complete-
                 ness.


        USAGE:

                 double csubt(z1,z2)
                 COMPLEX *z1;
                 COMPLEX *z2;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes CSUBT(z1,z2) from:

                         1.      Let z1 = a + j b
                                 Let z2 = c + j d

                         2.      Then CSUBT(z1,z2) = (a - c) + j (b - d)


        PML --- C Portable Math Library                                Page 25
        CTAN



        2.17  Complex double precision tangent





                                       ********
                                       * CTAN *
                                       ********




        DESCRIPTION:

                 Computes double precision complex tangent of a double  preci-
                 sion complex argument.  The result replaces the argument.


        USAGE:

                 ctan(z)
                 COMPLEX *z;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex tangent of Z = x + j y from:

                         1.      Compute CCOS(z)

                         2.      If CCOS(z) = 0 + j0 then the
                                 result is MAX_POS_DBLF + j0

                         3.      Else CTAN(z) = CSIN(z) / CCOS(z)


        PML --- C Portable Math Library                                Page 26
        CTANH



        2.18  Complex double precision hyperbolic tangent





                                      *********
                                      * CTANH *
                                      *********




        DESCRIPTION:

                 Computes double precision complex  hyperbolic  tangent  of  a
                 double  precision  complex argument.  The result replaces the
                 argument.


        USAGE:

                 ctanh(z)
                 COMPLEX *z;


        REFERENCES:



        RESTRICTIONS:



        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes complex hyperbolic tangent of Z = x + j y from:

                    CTANH(z) = (1 - CEXP(-2z)) / (1 + CEXP(-2z))


        PML --- C Portable Math Library                                Page 27
        DABS



        2.19  Double precision absolute value





                                       ********
                                       * DABS *
                                       ********




        DESCRIPTION:

                 Returns absolute value of double precision number.


        USAGE:

                 double dabs(x)
                 double x;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 28
        DACOS



        2.20  Double precision arc cosine





                                      *********
                                      * DACOS *
                                      *********




        DESCRIPTION:

                 Returns double precision arc cosine of double precision  flo-
                 ating point argument.


        USAGE:

                 double dacos(x)
                 double x;


        REFERENCES:

                 Fortran IV-plus user's guide, Digital Equipment Corp.  pp  B-
                 1.


        RESTRICTIONS:

                 The maximum relative error for the  approximating  polynomial
                 in DATAN is 10**(-16.82).  However, this assumes exact arith-
                 metic in the polynomial evaluation.  Additional rounding  and
                 truncation errors may occur as the argument is reduced to the
                 range over which the polynomial approximation is  valid,  and
                 as  the polynomial is evaluated using finite-precision arith-
                 metic.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home



        PML --- C Portable Math Library                                Page 29
        DACOS



        INTERNALS:

                 Computes arccosine(X) from:

                         (1)     If X = 0.0 then DACOS(X) = PI/2.

                         (2)     If X = 1.0 then DACOS(X) = 0.0

                         (3)     If X = -1.0 then DACOS(X) = PI.

                         (4)     If 0.0 < X < 1.0 then
                                 DACOS(X) = DATAN(Y)
                                 Y = DSQRT[1-(X**2)] / X

                         (4)     If -1.0 < X < 0.0 then
                                 DACOS(X) = DATAN(Y) + PI
                                 Y = DSQRT[1-(X**2)] / X


        PML --- C Portable Math Library                                Page 30
        DACOSH



        2.21  Double precision hyperbolic arc cosine





                                      **********
                                      * DACOSH *
                                      **********




        DESCRIPTION:

                 Returns double precision hyperbolic arc cosine of double pre-
                 cision floating point number.


        USAGE:

                 double dacosh(x)
                 double x;


        REFERENCES:



        RESTRICTIONS:

                 The range of the ACOSH function is all real  numbers  greater
                 than  or equal to 1.0 however large arguments may cause over-
                 flow in the x squared portion of the function evaluation.

                 For precision information refer to documentation of the  flo-
                 ating point library primatives called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes DACOSH(X) from:

                         1.      If X < 1.0 then report illegal

        PML --- C Portable Math Library                                Page 31
        DACOSH



                                 argument and return zero.

                         2.      If X > DSQRT(MAX_POS_DBLF) then
                                 set X = DSQRT(MAX_POS_DBLF and
                                 continue after reporting overflow.

                         3.      DACOSH(X) = LN [X+DSQRT(X**2 - 1)]


        PML --- C Portable Math Library                                Page 32
        DASIN



        2.22  Double precision arc sine





                                      *********
                                      * DASIN *
                                      *********




        DESCRIPTION:

                 Returns double precision arc sine of double precision  float-
                 ing point argument.


        USAGE:

                 double dasin(x)
                 double x;


        REFERENCES:

                 Fortran IV-plus user's guide, Digital Equipment Corp.  pp  B-
                 2.


        RESTRICTIONS:

                 For precision information refer to documentation of the  flo-
                 ating point library primatives called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes arcsine(X) from:

                         (1)     If X = 0.0 then DASIN(X) = 0.0

                         (2)     If X = 1.0 then DASIN(X) = PI/2.

        PML --- C Portable Math Library                                Page 33
        DASIN



                         (3)     If X = -1.0 then DASIN(X) = -PI/2

                         (4)     If -1.0 < X < 1.0 then
                                 DASIN(X) = DATAN(Y)
                                 Y = X / DSQRT[1-(X**2)]


        PML --- C Portable Math Library                                Page 34
        DASINH



        2.23  Double precision hyperbolic arc sine





                                      **********
                                      * DASINH *
                                      **********




        DESCRIPTION:

                 Returns double precision hyperbolic arc sine of double preci-
                 sion floating point number.


        USAGE:

                 double dasinh(x)
                 double x;


        REFERENCES:



        RESTRICTIONS:

                 The domain of the ASINH function  is  the  entire  real  axis
                 however  the  evaluation  of x squared may cause overflow for
                 large magnitudes.

                 For precision information refer to documentation of the  flo-
                 ating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes DASINH(X) from:

                         1.      Let XMAX = DSQRT(MAX_POS_DBLF - 1)

        PML --- C Portable Math Library                                Page 35
        DASINH




                         2.      If X < -XMAX or XMAX < X then
                                 let X = XMAX and flag overflow.

                         3.      DASINH(X) = LN [X+DSQRT(X**2 + 1)]


        PML --- C Portable Math Library                                Page 36
        DATAN



        2.24  Double precision arc tangent





                                      *********
                                      * DATAN *
                                      *********




        DESCRIPTION:

                 Returns double precision arc tangent of double precision flo-
                 ating point argument.


        USAGE:

                 double datan(x)
                 double x;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-3

                 Computer Approximations, J.F.  Hart et al, John Wiley & Sons,
                 1968, pp.  120-130.


        RESTRICTIONS:

                 The maximum relative error for the  approximating  polynomial
                 is  10**(-16.82).   However, this assumes exact arithmetic in
                 the polynomial evaluation.  Additional rounding  and  trunca-
                 tion errors may occur as the argument is reduced to the range
                 over which the polynomial approximation is valid, and as  the
                 polynomial is evaluated using finite-precision arithmetic.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home



        PML --- C Portable Math Library                                Page 37
        DATAN



        INTERNALS:

                 Computes arctangent(X) from:

                         (1)     If X < 0 then negate X, perform steps
                                 2, 3, and 4, and negate the returned
                                 result.  This makes use of the identity
                                 DATAN(-X) = -DATAN(X).

                         (2)     If argument X > 1 at this point then
                                 test to be sure that X can be inverted
                                 without underflowing.  If not, reduce
                                 X to largest possible number that can
                                 be inverted, issue warning, and continue.
                                 Perform steps 3 and 4 with arg = 1/X
                                 and subtract returned result from
                                 pi/2.  This makes use of the identity
                                 DATAN(X) = pi/2 - DATAN(1/X) for X>0.

                         (3)     At this point 0 <= X <= 1.  If
                                 X > DTAN(pi/12) then perform step 4
                                 with arg = (X*DSQRT(3)-1)/(DSQRT(3)+X)
                                 and add pi/6 to returned result.  This
                                 last transformation maps arguments
                                 greater than DTAN(pi/12) to arguments
                                 in range 0...DTAN(pi/12).

                         (4)     At this point the argument has been
                                 transformed so that it lies in the
                                 range -DTAN(pi/12)...DTAN(pi/12).
                                 Since very small arguments may cause
                                 underflow in the polynomial evaluation,
                                 a final check is performed.  If the
                                 argument is less than the underflow
                                 bound, the function returns x, since
                                 ATAN(X) approaches ASIN(X) which
                                 approaches X as X goes to zero.

                         (5)     DATAN(X) is now computed by one of the
                                 approximations given in the cited
                                 reference (Hart).  That is:

                                 DATAN(X) = X * SUM [ C[i] * X**(2*i) ]
                                 over i = {0,1,...8}.

                                 Where:

                                 C[0] =  .9999999999999999849899
                                 C[1] =  -.333333333333299308717
                                 C[2] =  .1999999999872944792
                                 C[3] =  -.142857141028255452
                                 C[4] =  .11111097898051048

        PML --- C Portable Math Library                                Page 38
        DATAN



                                 C[5] =  -.0909037114191074
                                 C[6] =  .0767936869066
                                 C[7] =  -.06483193510303
                                 C[8] =  .0443895157187
                                 (coefficients from HART table #4945 pg 267)


        PML --- C Portable Math Library                                Page 39
        DATAN2



        2.25  Double precision arc tangent of two arguments





                                      **********
                                      * DATAN2 *
                                      **********




        DESCRIPTION:

                 Returns double precision arc tangent of two double  precision
                 floating point arguments ( DATAN(Y/X) ).


        USAGE:

                 double datan2(x,y)
                 double x;
                 double y;


        REFERENCES:

                 Fortran 77 user's guide, Digital Equipment Corp.  pp B-4.


        RESTRICTIONS:

                 Note that the argument usage is exactly the  reverse  of  the
                 common  FORTRAN  usage where DATAN2(x,y) computes DATAN(x/y).
                 The usage here is less confusing than remembering that  x  is
                 really y and y is really x.

                 For precision information refer to documentation of the other
                 floating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home



        PML --- C Portable Math Library                                Page 40
        DATAN2



        INTERNALS:

                 Computes DATAN(Y/X) from:

                         1.      If X = 0 then
                                 DATAN(X,Y) = PI/2 * (SIGN(Y))

                         2.      If X > 0 then
                                 DATAN(X,Y) = DATAN(Y/X)

                         3.      If X < 0 then DATAN2(X,Y) =
                                 PI*(SIGN(Y)) + DATAN(Y/X)


        PML --- C Portable Math Library                                Page 41
        DATANH



        2.26  Double precision hyperbolic arc tangent





                                      **********
                                      * DATANH *
                                      **********




        DESCRIPTION:

                 Returns double precision hyperbolic  arc  tangent  of  double
                 precision floating point number.


        USAGE:

                 double datanh(x)
                 double x;


        REFERENCES:



        RESTRICTIONS:

                 The range of the ATANH function is -1.0  to  +1.0  exclusive.
                 Certain  pathological  cases  near  1.0 may cause overflow in
                 evaluation of 1+x /  1-x,  depending  upon  machine  exponent
                 range and mantissa precision.

                 For precision information refer to documentation of the other
                 floating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes DATANH(X) from:


        PML --- C Portable Math Library                                Page 42
        DATANH



                         1.      If X <= -1.0 or X >= 1.0
                                 then report argument out of
                                 range and return 0.0

                         2.      DATANH(X) = 0.5 * DLN((1+X)/(1-X))


        PML --- C Portable Math Library                                Page 43
        DCOS



        2.27  Double precision cosine





                                       ********
                                       * DCOS *
                                       ********




        DESCRIPTION:

                 Returns double precision cosine of double precision  floating
                 point argument.


        USAGE:

                 double dcos(x)
                 double x;


        REFERENCES:

                 Computer Approximations, J.F.  Hart et al, John Wiley & Sons,
                 1968, pp.  112-120.


        RESTRICTIONS:

                 The DSIN and DCOS routines are interactive in the sense  that
                 in the process of reducing the argument to the range -PI/4 to
                 PI/4, each may call the other.  Ultimately one or  the  other
                 uses a polynomial approximation on the reduced argument.  The
                 DSIN approximation has a maximum  relative  error  of  10**(-
                 17.59)  and  the  DCOS  approximation  has a maximum relative
                 error of 10**(-16.18).

                 These error bounds assume exact arithmetic in the  polynomial
                 evaluation.   Additional  rounding  and truncation errors may
                 occur as the argument is reduced to the range over which  the
                 polynomial  approximation  is valid, and as the polynomial is
                 evaluated using finite-precision arithmetic.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.

        PML --- C Portable Math Library                                Page 44
        DCOS



                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes DCOS(X) from:

                         (1)     Reduce argument X to range -PI to PI.

                         (2)     If X > PI/2 then call DCOS recursively
                                 using relation DCOS(X) = -DCOS(X - PI).

                         (3)     If X < -PI/2 then call DCOS recursively
                                 using relation DCOS(X) = -DCOS(X + PI).

                         (4)     If X > PI/4 then call DSIN using
                                 relation DCOS(X) = DSIN(PI/2 - X).

                         (5)     If X < -PI/4 then call DCOS using
                                 relation DCOS(X) = DSIN(PI/2 + X).

                         (6)     If X would cause underflow in approx
                                 evaluation arithmetic then return
                                 sqrt(1.0 - X**2).

                         (7)     By now X has been reduced to range
                                 -PI/4 to PI/4 and the approximation
                                 from HART pg. 119 can be used:

                                 DCOS(X) = ( P(Y) / Q(Y) )
                                 Where:

                                 Y    =  X * (4/PI)

                                 P(Y) =  SUM [ Pj * (Y**(2*j)) ]
                                 over j = {0,1,2,3}

                                 Q(Y) =  SUM [ Qj * (Y**(2*j)) ]
                                 over j = {0,1,2,3}

                                 P0   =  0.12905394659037374438571854e+7
                                 P1   =  -0.3745670391572320471032359e+6
                                 P2   =  0.134323009865390842853673e+5
                                 P3   =  -0.112314508233409330923e+3
                                 Q0   =  0.12905394659037373590295914e+7
                                 Q1   =  0.234677731072458350524124e+5
                                 Q2   =  0.2096951819672630628621e+3
                                 Q3   =  1.0000...
                                 (coefficients from HART table #3843 pg 244)



        PML --- C Portable Math Library                                Page 45
        DCOS



                 **** NOTE **** The range reduction  relations  used  in  this
                 routine  depend  on  the final approximation being valid over
                 the negative argument range in addition to the positive argu-
                 ment  range.   The  particular approximation chosen from HART
                 satisfies this requirement, although not explicitly stated in
                 the text.  This may not be true of other approximations given
                 in the reference.


        PML --- C Portable Math Library                                Page 46
        DCOSH



        2.28  Double precision hyperbolic cosine





                                      *********
                                      * DCOSH *
                                      *********




        DESCRIPTION:

                 Returns double precision hyperbolic cosine of  double  preci-
                 sion floating point number.


        USAGE:

                 double dcosh(x)
                 double x;


        REFERENCES:

                 Fortran IV plus user's guide, Digital Equipment Corp.  pp B-4


        RESTRICTIONS:

                 Inputs greater  than  LN(MAX_POS_DBLF)  result  in  overflow.
                 Inputs less than LN(MIN_POS_DBLF) result in underflow.

                 For precision information refer to documentation of the  flo-
                 ating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes hyperbolic cosine from:

                         DCOSH(X) = 0.5 * (DEXP(X) + DEXP(-X))

        PML --- C Portable Math Library                                Page 47
        DCOSH



        2.29  Double precision exponential





                                       ********
                                       * DEXP *
                                       ********




        DESCRIPTION:

                 Returns double precision exponential of double precision flo-
                 ating point number.


        USAGE:

                 double dexp(x)
                 double x;


        REFERENCES:

                 Fortran IV plus user's guide, Digital Equipment Corp.  pp B-3

                 Computer Approximations, J.F.  Hart et al, John Wiley & Sons,
                 1968, pp.  96-104.


        RESTRICTIONS:

                 Inputs greater  than  LN(MAX_POS_DBLF)  result  in  overflow.
                 Inputs less than LN(MIN_POS_DBLF) result in underflow.

                 The maximum relative error for the  approximating  polynomial
                 is  10**(-16.4).   However,  this assumes exact arithmetic in
                 the polynomial evaluation.  Additional rounding  and  trunca-
                 tion errors may occur as the argument is reduced to the range
                 over which the polynomial approximation is valid, and as  the
                 polynomial is evaluated using finite-precision arithmetic.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home

        PML --- C Portable Math Library                                Page 48
        DEXP



        INTERNALS:

                 Computes exponential from:

                         EXP(X)  =       2**Y  *  2**Z  *  2**W

                 Where:

                         Y       =       INT ( X * LOG2(e) )

                         V       =       16 * FRAC ( X * LOG2(e))

                         Z       =       (1/16) * INT (V)

                         W       =       (1/16) * FRAC (V)

                 Note that:

                         0 =< V < 16

                         Z = {0, 1/16, 2/16, ...15/16}

                         0 =< W < 1/16

                 Then:

                         2**Z is looked up in a table of 2**0, 2**1/16, ...

                         2**W is computed from an approximation:

                                 2**W    =  (A + B) / (A - B)

                                 A       =  C + (D * W * W)

                                 B       =  W * (E + (F * W * W))

                                 C       =  20.8137711965230361973

                                 D       =  1.0

                                 E       =  7.2135034108448192083

                                 F       =  0.057761135831801928

                         Coefficients are from HART, table #1121, pg 206.

                         Effective multiplication by 2**Y is done by a
                         floating point scale with Y as scale argument.


        PML --- C Portable Math Library                                Page 49
        DFRAC



        2.30  Double precision fractional portion





                                      *********
                                      * DFRAC *
                                      *********




        DESCRIPTION:

                 Returns fractional portion of double precision number as dou-
                 ble precision number.


        USAGE:

                 double dfrac(x)
                 double x;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        RESTRICTIONS:


        PML --- C Portable Math Library                                Page 50
        DINT



        2.31  Double precision integer portion




                                       ********
                                       * DINT *
                                       ********




        DESCRIPTION:

                 Returns integer portion of double precision number as  double
                 precision number.


        USAGE:

                 double dint(x)
                 double x;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        RESTRICTIONS:

                 The current DEC-20 C system treats  double  as  float.   This
                 routine  will  need to be modified when true double precision
                 is implemented.


        PML --- C Portable Math Library                                Page 51
        DLN



        2.32  Double precision natural log




                                       *******
                                       * DLN *
                                       *******




        DESCRIPTION:

                 Returns double precision natural log of double precision flo-
                 ating point argument.


        USAGE:

                 double dln(x)
                 double x;


        REFERENCES:

                 Computer Approximations, J.F.  Hart et al, John Wiley & Sons,
                 1968, pp.  105-111.


        RESTRICTIONS:

                 The absolute error in the approximating polynomial is  10**(-
                 19.38).   Note  that  contrary  to DEC's assertion in the F4P
                 user's guide, the error is absolute and not relative.

                 This error bound assumes exact arithmetic in  the  polynomial
                 evaluation.   Additional  rounding  and truncation errors may
                 occur as the argument is reduced to the range over which  the
                 polynomial  approximation  is valid, and as the polynomial is
                 evaluated using finite-precision arithmetic.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home



        PML --- C Portable Math Library                                Page 52
        DLN



        INTERNALS:

                 Computes DLN(X) from:

                         (1)     If argument is zero then flag an error
                                 and return minus infinity (or rather its
                                 machine representation).

                         (2)     If argument is negative then flag an
                                 error and return minus infinity.

                         (3)     Given that x = m * 2**k then extract
                                 mantissa m and exponent k.

                         (4)     Transform m which is in range [0.5,1.0]
                                 to range [1/sqrt(2), sqrt(2)] by:

                                         s = m * sqrt(2)

                         (4)     Compute z = (s - 1) / (s + 1)

                         (5)     Now use the approximation from HART
                                 page 111 to find ln(s):

                                 DLN(s) = z * ( P(z**2) / Q(z**2) )

                                 Where:

                                 P(z**2) =  SUM [ Pj * (z**(2*j)) ]
                                 over j = {0,1,2,3}

                                 Q(z**2) =  SUM [ Qj * (z**(2*j)) ]
                                 over j = {0,1,2,3}

                                 P0 =  -0.240139179559210509868484e2
                                 P1 =  0.30957292821537650062264e2
                                 P2 =  -0.96376909336868659324e1
                                 P3 =  0.4210873712179797145
                                 Q0 =  -0.120069589779605254717525e2
                                 Q1 =  0.19480966070088973051623e2
                                 Q2 =  -0.89111090279378312337e1
                                 Q3 =  1.0000

                                 (coefficients from HART table #2705 pg 229)

                 (5)     Finally, compute DLN(x) from:

                                 DLN(x) = (k * dln(2)) - dln(sqrt(2)) + dln(s)


        PML --- C Portable Math Library                                Page 53
        DLOG



        2.33  Double precision common log





                                       ********
                                       * DLOG *
                                       ********




        DESCRIPTION:

                 Returns double precision common log of double precision  flo-
                 ating point argument.


        USAGE:

                 double dlog(x)
                 double x;


        REFERENCES:

                 PDP-11 Fortran IV-plus users guide,  Digital  Equip.   Corp.,
                 1975, pp.  B-3.


        RESTRICTIONS:

                 For precision information refer to documentation of the  flo-
                 ating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes DLOG(X) from:

                         DLOG(X) = DLOG(e) * DLN(X)


        PML --- C Portable Math Library                                Page 54
        DMAX



        2.34  double precision maximum of two arguments





                                       ********
                                       * DMAX *
                                       ********




        DESCRIPTION:

                 Returns maximum value of two double precision numbers.


        USAGE:

                 double dmax(x,y)
                 double x;
                 double y;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 55
        DMIN



        2.35  double precision minimum of two arguments





                                       ********
                                       * DMIN *
                                       ********




        DESCRIPTION:

                 Returns minimum value of two double precision numbers.


        USAGE:

                 double dmin(x,y)
                 double x;
                 double y;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 56
        DMOD



        2.36  Double precision modulo





                                       ********
                                       * DMOD *
                                       ********




        DESCRIPTION:

                 Returns double precision modulo of two double precision argu-
                 ments.


        USAGE:

                 double dmod(value,base)
                 double value;
                 double base;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 57
        DPOLY



        2.37  Double precision polynomial evaluation





                                      *********
                                      * DPOLY *
                                      *********




        DESCRIPTION:

                 Evaluates a polynomial and returns double  precision  result.
                 Is  passed  a  the  order  of the polynomial, a pointer to an
                 array of double precision polynomial coefficients (in ascend-
                 ing order), and the independent variable.


        USAGE:

                 double dpoly(order,coeffs,x)
                 int order;
                 double *coeffs;
                 double x;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Evalates the polynomial using recursion and the form:

                         P(x) = P0 + x(P1 + x(P2 +...x(Pn)))


        PML --- C Portable Math Library                                Page 58
        DSCALE



        2.38  Scale a double precision number by power of 2





                                      **********
                                      * DSCALE *
                                      **********




        DESCRIPTION:

                 Adds a specified integer to a double precision number's expo-
                 nent,  effectively  multiplying  by a power of 2 for positive
                 scale values and divided by a power of 2 for  negative  scale
                 values.


        USAGE:

                 double dscale(value,scale)
                 double value;
                 integer scale;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 This routine is highly machine dependent.  As  such,  no  at-
                 tempt  was  made  to make it general, hence it may have to be
                 completely rewritten  when  transportation  of  the  floating
                 point library is attempted.

                 For the DECSYSTEM-20 the double precision word format is:

                 WORD N  =>      SEEEEEEEEMMMMMMMMMMMMMMMMMMMMMMMMMMM
                 WORD N+1 =>     XMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM

                 For the PDP-11 the double precision word format is:

                 WORD N =>       SEEEEEEEEMMMMMMM
                 WORD N+1 =>     MMMMMMMMMMMMMMMM

        PML --- C Portable Math Library                                Page 59
        DSCALE



                 WORD N+2 =>     MMMMMMMMMMMMMMMM
                 WORD N+3 =>     MMMMMMMMMMMMMMMM

                 Where:          S =>    Sign bit
                                 E  =>   Exponent
                                 X  =>   Ignored (set to 0)
                                 M  =>   Mantissa bit

                 DSCALE extracts the exponent, shifts it into the lower  order
                 bits,  adds  the scale value to it, checks for exponent over-
                 flow or underflow, shifts it back into the high bits, and in-
                 serts it back into the value.

                 NOTE:  On the DECSYSTEM-20, the exponent for negative numbers
                 is complemented.  This is not true for the PDP-11.


        PML --- C Portable Math Library                                Page 60
        DSIGN



        2.39  Transfer of sign




                                      *********
                                      * DSIGN *
                                      *********




        DESCRIPTION:

                 Returns first argument with same sign as second argument.


        USAGE:

                 double dsign(x,y)
                 double x;
                 double y;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 61
        DSIN



        2.40  Double precision sine





                                       ********
                                       * DSIN *
                                       ********




        DESCRIPTION:

                 Returns double precision sine of  double  precision  floating
                 point argument.


        USAGE:

                 double dsin(x)
                 double x;


        REFERENCES:

                 Computer Approximations, J.F.  Hart et al, John Wiley & Sons,
                 1968, pp.  112-120.


        RESTRICTIONS:

                 The DSIN and DCOS routines are interactive in the sense  that
                 in the process of reducing the argument to the range -PI/4 to
                 PI/4, each may call the other.  Ultimately one or  the  other
                 uses a polynomial approximation on the reduced argument.  The
                 DSIN approximation has a maximum  relative  error  of  10**(-
                 17.59)  and  the  DCOS  approximation  has a maximum relative
                 error of 10**(-16.18).

                 These error bounds assume exact arithmetic in the  polynomial
                 evaluation.   Additional  rounding  and truncation errors may
                 occur as the argument is reduced to the range over which  the
                 polynomial  approximation  is valid, and as the polynomial is
                 evaluated using finite-precision arithmetic.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.

        PML --- C Portable Math Library                                Page 62
        DSIN



                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes DSIN(X) from:

                         (1)     Reduce argument X to range -PI to PI.

                         (2)     If X > PI/2 then call DSIN recursively
                                 using relation DSIN(X) = -DSIN(X - PI).

                         (3)     If X < -PI/2 then call DSIN recursively
                                 using relation DSIN(X) = -DSIN(X + PI).

                         (4)     If X > PI/4 then call DCOS using
                                 relation DSIN(X) = DCOS(PI/2 - X).

                         (5)     If X < -PI/4 then call DCOS using
                                 relation DSIN(X) = -DCOS(PI/2 + X).

                         (6)     If X is small enough that polynomial
                                 evaluation would cause underflow
                                 then return X, since SIN(X)
                                 approaches X as X approaches zero.

                         (7)     By now X has been reduced to range
                                 -PI/4 to PI/4 and the approximation
                                 from HART pg. 118 can be used:

                                 DSIN(X) = Y * ( P(Y) / Q(Y) )
                                 Where:

                                 Y    =  X * (4/PI)

                                 P(Y) =  SUM [ Pj * (Y**(2*j)) ]
                                 over j = {0,1,2,3}

                                 Q(Y) =  SUM [ Qj * (Y**(2*j)) ]
                                 over j = {0,1,2,3}

                                 P0   =  0.206643433369958582409167054e+7
                                 P1   =  -0.18160398797407332550219213e+6
                                 P2   =  0.359993069496361883172836e+4
                                 P3   =  -0.2010748329458861571949e+2
                                 Q0   =  0.263106591026476989637710307e+7
                                 Q1   =  0.3927024277464900030883986e+5
                                 Q2   =  0.27811919481083844087953e+3
                                 Q3   =  1.0000...
                                 (coefficients from HART table #3063 pg 234)


        PML --- C Portable Math Library                                Page 63
        DSIN



                 **** NOTE ****   The range reduction relations used  in  this
                 routine  depend  on  the final approximation being valid over
                 the negative argument range in addition to the positive argu-
                 ment  range.   The  particular approximation chosen from HART
                 satisfies this requirement, although not explicitly stated in
                 the text.  This may not be true of other approximations given
                 in the reference.


        PML --- C Portable Math Library                                Page 64
        DSINH



        2.41  Double precision hyperbolic sine





                                      *********
                                      * DSINH *
                                      *********




        DESCRIPTION:

                 Returns double precision hyperbolic sine of double  precision
                 floating point number.


        USAGE:

                 double dsinh(x)
                 double x;


        REFERENCES:

                 Fortran IV plus user's guide, Digital Equipment Corp.  pp B-5


        RESTRICTIONS:

                 Inputs greater  than  LN(MAX_POS_DBLF)  result  in  overflow.
                 Inputs less than LN(MIN_POS_DBLF) result in underflow.

                 For precision information refer to documentation of the  flo-
                 ating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes hyperbolic sine from:

                         DSINH(X) = 0.5 * (DEXP(X) - DEXP(-X))

        PML --- C Portable Math Library                                Page 65
        DSINH



        2.42  Double precision square root





                                      *********
                                      * DSQRT *
                                      *********




        DESCRIPTION:

                 Returns double precision square root of double precision flo-
                 ating point argument.


        USAGE:

                 double dsqrt(x)
                 double x;


        REFERENCES:

                 Fortran IV-PLUS user's guide, Digital Equipment Corp.  pp  B-
                 7.

                 Computer Approximations, J.F.  Hart et al, John Wiley & Sons,
                 1968, pp.  89-96.


        RESTRICTIONS:

                 The relative error is 10**(-30.1) after three applications of
                 Heron's iteration for the square root.

                 However, this assumes exact arithmetic in the iterations  and
                 initial  approximation.   Additional  errors may occur due to
                 truncation, rounding, or machine precision limits.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home



        PML --- C Portable Math Library                                Page 66
        DSQRT



        INTERNALS:

                 Computes square root by:

                         (1)     Range reduction of argument to [0.5,1.0]
                                 by application of identity:

                                 sqrt(x)  =  2**(k/2) * sqrt(x * 2**(-k))

                                 k is the exponent when x is written as
                                 a mantissa times a power of 2 (m * 2**k).
                                 It is assumed that the mantissa is
                                 already normalized (0.5 =< m < 1.0).

                         (2)     An approximation to sqrt(m) is obtained
                                 from:

                                 u = sqrt(m) = (P0 + P1*m) / (Q0 + Q1*m)

                                 P0 = 0.594604482
                                 P1 = 2.54164041
                                 Q0 = 2.13725758
                                 Q1 = 1.0

                                 (coefficients from HART table #350 pg 193)

                 (3)     Three applications of Heron's iteration are
                         performed using:

                                 y[n+1] = 0.5 * (y[n] + (m/y[n]))

                                 where y[0] = u = approx sqrt(m)

                 (4)     If the value of k was odd then y is either
                         multiplied by the square root of two or
                         divided by the square root of two for k positive
                         or negative respectively.  This rescales y
                         by multiplying by 2**frac(k/2).

                 (5)     Finally, y is rescaled by int(k/2) which
                         is equivalent to multiplication by 2**int(k/2).

                         The result of steps 4 and 5 is that the value
                         of y between 0.5 and 1.0 has been rescaled by
                         2**(k/2) which removes the original rescaling
                         done prior to finding the mantissa square root.


        PML --- C Portable Math Library                                Page 67
        DTAN



        2.43  Double precision tangent





                                       ********
                                       * DTAN *
                                       ********




        DESCRIPTION:

                 Returns tangent of double precision floating point number.


        USAGE:

                 double dtan(x)
                 double x;


        INTERNALS:

                 Computes the tangent from tan(x) = sin(x) / cos(x).

                 If cos(x) = 0 and sin(x) >= 0, then returns largest  floating
                 point number on host machine.

                 If cos(x) = 0 and sin(x) < 0, then returns smallest  floating
                 point number on host machine.


        REFERENCES:

                 Fortran IV plus user's guide, Digital  Equipment  Corp.   pp.
                 B-8


        PML --- C Portable Math Library                                Page 68
        DTANH



        2.44  Double precision hyperbolic tangent




                                      *********
                                      * DTANH *
                                      *********




        DESCRIPTION:

                 Returns double precision hyperbolic tangent of double  preci-
                 sion floating point number.


        USAGE:

                 double dtanh(x)
                 double x;


        REFERENCES:

                 Fortran IV plus user's guide, Digital Equipment Corp.  pp B-5


        RESTRICTIONS:

                 For precision information refer to documentation of the  flo-
                 ating point library routines called.


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 Computes hyperbolic tangent from:

                         DTANH(X) = 1.0 for X > DTANH_MAXARG
                                  = -1.0 for X < -DTANH_MAXARG
                                  =  DSINH(X) / DCOSH(X) otherwise


        PML --- C Portable Math Library                                Page 69
        DXEXP



        2.45  extract double precision numbers exponent





                                      *********
                                      * DXEXP *
                                      *********




        DESCRIPTION:

                 Extracts exponent from a double precision number and  returns
                 it as a normal length integer.


        USAGE:

                 int dxexp(value)
                 double value;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 This routine is highly machine dependent.  As  such,  no  at-
                 tempt  was  made  to make it general, hence it may have to be
                 completely rewritten  when  transportation  of  the  floating
                 point library is attempted.

                 For the DECSYSTEM-20 the double precision word format is:

                 WORD N  =>      SEEEEEEEEMMMMMMMMMMMMMMMMMMMMMMMMMMM
                 WORD N+1 =>     XMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM

                 For the PDP-11 the double precision word format is:

                 WORD N =>       SEEEEEEEEMMMMMMM
                 WORD N+1 =>     MMMMMMMMMMMMMMMM
                 WORD N+2 =>     MMMMMMMMMMMMMMMM
                 WORD N+3 =>     MMMMMMMMMMMMMMMM


        PML --- C Portable Math Library                                Page 70
        DXEXP



                 Where:          S =>    Sign bit
                                 E  =>   Exponent
                                 X  =>   Ignored (set to 0)
                                 M  =>   Mantissa bit



        PML --- C Portable Math Library                                Page 71
        DXMANT



        2.46  Extract double precision number's mantissa





                                      **********
                                      * DXMANT *
                                      **********




        DESCRIPTION:

                 Extracts a double precision number's mantissa and returns  it
                 as a double precision number with a normalized mantissa and a
                 zero exponent.


        USAGE:

                 double dxmant(value)
                 double value;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        INTERNALS:

                 This routine is highly machine dependent.  As  such,  no  at-
                 tempt  was  made  to make it general, hence it may have to be
                 completely rewritten  when  transportation  of  the  floating
                 point library is attempted.

                 For the DECSYSTEM-20 the double precision word format is:

                 WORD N  =>      SEEEEEEEEMMMMMMMMMMMMMMMMMMMMMMMMMMM
                 WORD N+1 =>     XMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMMM

                 For the PDP-11 the double precision word format is:

                 WORD N =>       SEEEEEEEEMMMMMMM
                 WORD N+1 =>     MMMMMMMMMMMMMMMM
                 WORD N+2 =>     MMMMMMMMMMMMMMMM
                 WORD N+3 =>     MMMMMMMMMMMMMMMM

        PML --- C Portable Math Library                                Page 72
        DXMANT



                 Where:          S =>    Sign bit
                                 E  =>   Exponent
                                 X  =>   Ignored (set to 0)
                                 M  =>   Mantissa bit


        PML --- C Portable Math Library                                Page 73
        PMLCFS



        2.47  Clear specified PML error handler flags





                                      **********
                                      * PMLCFS *
                                      **********




        DESCRIPTION:

                 Clear the specified PML error handler flags for the specified
                 error.   Two  or  more flags may be cleared simultaneously by
                 "or-ing" them in the call, for example "LOG | CONTINUE".  The
                 manifest  constants for the flags and error codes are defined
                 in <pmluser.h>.


        USAGE:

                 pmlcfs(err_code,flags)
                 int err_code;
                 int flags;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 74
        PMLCNT



        2.48  Get PML error count and reset it to zero





                                      **********
                                      * PMLCNT *
                                      **********




        DESCRIPTION:

                 Returns the total number of PML  errors  seen  prior  to  the
                 call, and resets the error count to zero.


        USAGE:

                 int pmlcnt()


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 75
        PMLERR



        2.49  Portable Math Library error handler





                                      **********
                                      * PMLERR *
                                      **********




        DESCRIPTION:

                 Provides a sample PML error handler.  Does not use any avail-
                 able  hardware  "traps" so is machine independent.  Generally
                 only called internally by the other PML routines.

                 There are currently three flags which  control  the  response
                 for specific errors:

                 (1)  LOG      When set an error message is sent
                               to the user terminal.

                 (2)  COUNT    When set the error is counted
                               against the PML error limit.

                 (3) CONTINUE  When set the task continues
                               providing the error count has not
                               exceeded the PML error limit.

                 Each of these flags can be  set  or  reset  independently  by
                 "pmlsfs" or "pmlcfs" respectively.


        USAGE:

                 pmlerr(err_code)
                 int err_code;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 76
        PMLLIM



        2.50  Set Portable Math Library error limit





                                      **********
                                      * PMLLIM *
                                      **********




        DESCRIPTION:

                 Sets the PML error limit to the specified value  and  returns
                 it  previous  value.  Does not affect the current error count
                 (which may be reset to zero by a  call  to  "pmlcnt").   Note
                 that  the  default  error limit is set at compile time by the
                 value in "pml.h".


        USAGE:

                 int pmllim(limit)
                 int limit;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home


        PML --- C Portable Math Library                                Page 77
        PMLSFS



        2.51  Set specified PML error handler flags





                                      **********
                                      * PMLSFS *
                                      **********




        DESCRIPTION:

                 Set the specified PML error handler flags for  the  specified
                 error.   Two  or more flags may be set simultaneously by "or-
                 ing" them in the call, for example  "LOG  |  CONTINUE".   The
                 manifest  constants for the flags and error codes are defined
                 in <pmluser.h>.


        USAGE:

                 pmlsfs(err_code,flags)
                 int err_code;
                 int flags;


        PROGRAMMER:

                 Fred Fish
                 Goodyear Aerospace Corp, Arizona Div.
                 (602) 932-7000 work
                 (602) 894-6881 home









                                      APPENDIX A

                                      REFERENCES




             1.  P.  A.  Fox, A.  D.  Hall, and N.  L.  Schryer, The PORT  Ma-
                 thematical Subroutine Library, ACM Transactions on Mathemati-
                 cal Software, Vol 4, No.  2, June 1978, pp 104-126.

             2.  Brian Ford, Parameterization of  the  Environment  for  Tran-
                 sportable  Numerical Software, ACM Transactions on Mathemati-
                 cal Software, Vol 4, No.  2, June 1978, pp 100-103.








                                        INDEX



        CABS  . . . . . . . . . . . . . . . 8
        CACOS . . . . . . . . . . . . . . . 9
        CADD  . . . . . . . . . . . . . . . 10
        CASIN . . . . . . . . . . . . . . . 11
        CATAN . . . . . . . . . . . . . . . 12
        CCOS  . . . . . . . . . . . . . . . 13
        CCOSH . . . . . . . . . . . . . . . 14
        CDIV  . . . . . . . . . . . . . . . 15
        CEXP  . . . . . . . . . . . . . . . 16
        CLN . . . . . . . . . . . . . . . . 17
        CMULT . . . . . . . . . . . . . . . 18
        complex functions . . . . . . . . . 8, 9, 10, 11, 12, 13, 14, 15, 16,
                                            17, 18, 19, 20, 21, 22, 24, 25, 26
        CRCP  . . . . . . . . . . . . . . . 19
        CSIN  . . . . . . . . . . . . . . . 20
        CSINH . . . . . . . . . . . . . . . 21
        CSQRT . . . . . . . . . . . . . . . 22
        CSUBT . . . . . . . . . . . . . . . 24
        CTAN  . . . . . . . . . . . . . . . 25
        CTANH . . . . . . . . . . . . . . . 26

        DABS  . . . . . . . . . . . . . . . 27
        DACOS . . . . . . . . . . . . . . . 28
        DACOSH  . . . . . . . . . . . . . . 30
        DASIN . . . . . . . . . . . . . . . 32
        DASINH  . . . . . . . . . . . . . . 34
        DATAN . . . . . . . . . . . . . . . 36
        DATAN2  . . . . . . . . . . . . . . 39
        DATANH  . . . . . . . . . . . . . . 41
        DCOS  . . . . . . . . . . . . . . . 43
        DCOSH . . . . . . . . . . . . . . . 46
        DEXP  . . . . . . . . . . . . . . . 47
        DFRAC . . . . . . . . . . . . . . . 49
        DINT  . . . . . . . . . . . . . . . 50
        DLN . . . . . . . . . . . . . . . . 51
        DLOG  . . . . . . . . . . . . . . . 53
        DMAX  . . . . . . . . . . . . . . . 54
        DMIN  . . . . . . . . . . . . . . . 55
        DMOD  . . . . . . . . . . . . . . . 56
        document topics . . . . . . . . . . 2
        DPOLY . . . . . . . . . . . . . . . 57
        DSCALE  . . . . . . . . . . . . . . 58
        DSIGN . . . . . . . . . . . . . . . 60
        DSIN  . . . . . . . . . . . . . . . 61
        DSINH . . . . . . . . . . . . . . . 64
        DSQRT . . . . . . . . . . . . . . . 65

        INDEX                                                         Page I-2




        DTAN  . . . . . . . . . . . . . . . 67
        DTANH . . . . . . . . . . . . . . . 68
        DXEXP . . . . . . . . . . . . . . . 69
        DXMANT  . . . . . . . . . . . . . . 71

        machine dependent routines  . . . . 49, 50, 58, 69, 71
        machine independent functions . . . 25
        machine independent routines  . . . 8, 9, 10, 11, 12, 13, 14, 15, 16,
                                            17, 18, 20, 21, 22, 24, 26, 27, 28,
                                            30, 32, 34, 36, 39, 41, 43, 46, 47,
                                            51, 53, 54, 55, 56, 57, 60, 61, 64,
                                            65, 67, 68, 73, 74, 75, 76, 77
        math libraries  . . . . . . . . . . 8, 9, 10, 11, 12, 13, 14, 15, 16,
                                            17, 18, 19, 20, 21, 22, 24, 25, 26,
                                            27, 28, 30, 32, 34, 36, 39, 41, 43,
                                            46, 47, 49, 50, 51, 53, 54, 55, 56,
                                            57, 58, 60, 61, 64, 65, 67, 68, 69,
                                            71, 73, 74, 75, 76, 77

        PMLCFS  . . . . . . . . . . . . . . 73
        PMLCNT  . . . . . . . . . . . . . . 74
        PMLERR  . . . . . . . . . . . . . . 75
        PMLLIM  . . . . . . . . . . . . . . 76
        PMLSFS  . . . . . . . . . . . . . . 77

        trigonometric functions . . . . . . 28, 32, 36, 39, 43, 61, 67







                                       CONTENTS


             1.0  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . .   2
                  1.1   Document structure . . . . . . . . . . . . . . . .   2
                  1.2   Design Considerations  . . . . . . . . . . . . . .   2
                  1.3   Error Handling . . . . . . . . . . . . . . . . . .   3
                  1.4   Function Names . . . . . . . . . . . . . . . . . .   4
                  1.5   Installation . . . . . . . . . . . . . . . . . . .   5
                  1.6   Bugs . . . . . . . . . . . . . . . . . . . . . . .   5
                  1.7   Transporting To Other Machines . . . . . . . . . .   5
             2.0  RUNTIME MODULES  . . . . . . . . . . . . . . . . . . . .   7
                  2.1   Double precision complex absolute value  . . . . .   8
                  2.2   Complex double precision arc cosine  . . . . . . .   9
                  2.3   Double precision complex addition  . . . . . . . .  10
                  2.4   Complex double precision arc sine  . . . . . . . .  11
                  2.5   Complex double precision arc tangent . . . . . . .  12
                  2.6   Complex double precision cosine  . . . . . . . . .  13
                  2.7   Complex double precision hyperbolic cosine . . . .  14
                  2.8   Double precision complex division  . . . . . . . .  15
                  2.9   Complex double precision exponential . . . . . . .  16
                  2.10  Complex double precision natural logarithm . . . .  17
                  2.11  Double precision complex multiplication  . . . . .  18
                  2.12  complex double precision reciprocal  . . . . . . .  19
                  2.13  Complex double precision sine  . . . . . . . . . .  20
                  2.14  Complex double precision hyperbolic sine . . . . .  21
                  2.15  Complex double precision square root . . . . . . .  22
                  2.16  Double precision complex subtraction . . . . . . .  24
                  2.17  Complex double precision tangent . . . . . . . . .  25
                  2.18  Complex double precision hyperbolic tangent  . . .  26
                  2.19  Double precision absolute value  . . . . . . . . .  27
                  2.20  Double precision arc cosine  . . . . . . . . . . .  28
                  2.21  Double precision hyperbolic arc cosine . . . . . .  30
                  2.22  Double precision arc sine  . . . . . . . . . . . .  32
                  2.23  Double precision hyperbolic arc sine . . . . . . .  34
                  2.24  Double precision arc tangent . . . . . . . . . . .  36
                  2.25  Double precision arc tangent of two arguments  . .  39
                  2.26  Double precision hyperbolic arc tangent  . . . . .  41
                  2.27  Double precision cosine  . . . . . . . . . . . . .  43
                  2.28  Double precision hyperbolic cosine . . . . . . . .  46
                  2.29  Double precision exponential . . . . . . . . . . .  47
                  2.30  Double precision fractional portion  . . . . . . .  49
                  2.31  Double precision integer portion . . . . . . . . .  50
                  2.32  Double precision natural log . . . . . . . . . . .  51
                  2.33  Double precision common log  . . . . . . . . . . .  53
                  2.34  double precision maximum of two arguments  . . . .  54
                  2.35  double precision minimum of two arguments  . . . .  55
                  2.36  Double precision modulo  . . . . . . . . . . . . .  56
                  2.37  Double precision polynomial evaluation . . . . . .  57
                  2.38  Scale a double precision number by power of 2  . .  58





                  2.39  Transfer of sign . . . . . . . . . . . . . . . . .  60
                  2.40  Double precision sine  . . . . . . . . . . . . . .  61
                  2.41  Double precision hyperbolic sine . . . . . . . . .  64
                  2.42  Double precision square root . . . . . . . . . . .  65
                  2.43  Double precision tangent . . . . . . . . . . . . .  67
                  2.44  Double precision hyperbolic tangent  . . . . . . .  68
                  2.45  extract double precision numbers exponent  . . . .  69
                  2.46  Extract double precision number's mantissa . . . .  71
                  2.47  Clear specified PML error handler flags  . . . . .  73
                  2.48  Get PML error count and reset it to zero . . . . .  74
                  2.49  Portable Math Library error handler  . . . . . . .  75
                  2.50  Set Portable Math Library error limit  . . . . . .  76
                  2.51  Set specified PML error handler flags  . . . . . .  77

        A.0  REFERENCES  . . . . . . . . . . . . . . . . . . . . . . . . . A-1


        INDEX  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . I-1