HOL - Contiguous Block Report Utility
		=====================================

			   User's Guide
			   ============

     HOL  is  a small task aimed to give the user detailed information
     on how fragmented his disks are. For any given FILES-11 device it
     will  list  out  all (or optionally just those over a given size)
     the  contiguous  'holes'  on  that  device, giving starting block
     number  (in octal) and size (in decimal), and the total number of
     free blocks for the device.

     HOL may be invoked either by:-

          HOL <DDn:> </nnnn>
     or
          RUN $HOL
          HOL> <DDn:> </nnnn>

     Where  DDn: is a valid Files-11 device (the n and : are optional)
     which defaults to SY: if omitted, and nnnn is an optional decimal
     number (up to 9 digits) specifying a minimum size for the 'holes'
     to be listed.
     The output appears on LUN 2 which may be redirected to a printer.
     HOL may produce one of the following error messages:

     1.   HOL - FALURE ON READING BITMAP.SYS

          An  error occurred trying to read the file BITMAP.SYS on the
          device specified. Most probably the device is not mounted.

     2.   HOL - ILLEGAL DEVICE

          The device specified does not exist on the system, or is not
          a valid Files-11 disk.

     3.   HOL - BAD SWITCH

          The  user typed a slash (/) in his commandline, but followed
          it with something other than a valid decimal number.

     4.   HOL - COMMAND ERROR

          The  command  line  specified did not fulfill the conditions
          laid down above.




		HOL - Contiguous Block Report Utility
		=====================================

			   System Guide
			   ============

     The  task  consists of one simple module. This first gets the MCR
     command  line  -  prompting  the  user  for  input if one was not
     specified  - and parses it to determine the device to be checked,
     and,  if specified, the minimum hole size to be reported. It then
     assigns  a  LUN(1)  to  this  device,  checks that it is a valid,
     mountable,  Files-11  disk  and opens the file [0,0]BITMAP.SYS on
     it.  It  then  reads  through  the  file  checking  each  bit and
     calculating  the  size of each hole. It then checks to see if the
     hole is greater than the minimum requested (if one was specified)
     and,  if so, prints out the block number of the start of the hole
     and the size of the hole.

     The program is built by means of the command file HOL.CMD.  It is
     a  non-privileged  task  that  uses 3 units and has a taskname of
     ...HOL.