Program TALK


          Documentation and User's Guide

















          J. Yambor and N. Bewtra


          Computer Sciences Corporation


          Silver Spring, Maryland

















          Prepared for


          Goddard Space Flight Center


          under Technical Direction of


          Bob Turkelson







                                                                    PAGE 2


                                                                          









     1.0  Introduction








               TALK is a terminal emulation program which enables a PDP-11


          user  running  under the RSX-11M operating system to communicate


          with a remote host computer.  The program  usually  operates  in


          "terminal"  mode which allows the user to talk to the host as if


          the PDP-11 were invisible.  The program also has the  capability


          of bi-directional file transfers.





               Throughout this document the "host" refers to the  computer


          with  which  the  TALK program is communicating - not the one on


          which TALK is running.











          1.1  System Requirements








                    The PDP-11 must be running under  (at  least)  version


               3.2 of RSX-11M with the full duplex terminal driver.







          Program TALK Documentation                                PAGE 3


                                                                   12/2/81









     2.0  Operation Details








               Once TALK has been initiated, the user is prompted to enter


          the  channel  number.   This  is  the  number  of  the interface


          connected to the host computer.  A control-Z input at this  time


          will terminate the program.





               At this point, TALK is in "terminal"  mode - that  is,  any


          characters typed will be sent directly to the host computer, and


          all characters from the host computer will be displayed  on  the


          terminal.





               There are a number of  control  characters  which  are  not


          transmitted  from  the  keyboard  to  the  host  computer.   The


          control-S (^S) and control-Q (^Q) characters are used to suspend


          and  resume (respectively) the processing of characters from the


          host.  The control-B (^B) character  instructs  the  program  to


          transmit   a   "break"  character  to  the  host.   During  file


          transfers, a control-O (^O) character alternately  suspends  and


          resumes  the  terminal  echoing of characters being transmitted.


          The control-W (^W) character  instructs  the  program  to  enter


          command input mode.  In this mode, the user is prompted to enter


          an alphabetic character specifying one of a  number  of  program


          commands  which  are not specified by control characters.  These


          commands are outlined in the next section.











     2.1  Command Descriptions








               Commands  entered  from  "command  input  mode"  are   used


          primarily to control file transfers.  There are also commands to


          display  the  command  menu,  send  to  the  host  the   control


          characters  which  are intercepted by TALK in terminal mode, and


          exit the TALK program.  Commands are accepted in both upper  and


          lower case.  A carriage return gets the user out of this mode if


          he does not wish to enter a command at this time.











          2.1.1   A -  Initiate file transfer to host








                    This  command  coordinates  a  number  of   operations


               necessary  to  transfer  a  text file to the host computer.


               The user is prompted for the desired host file name as well


               as  the  local file name.  Redirected input mode is entered


               and a command is  sent  to  the  host  to  begin  the  file


               transfer.   When  the  end-of-file  is  reached,  the <EOF>


               character is transmitted  to  the  host  to  terminate  the


               transfer and redirected input is cancelled.  TALK currently







          Program TALK Documentation                                PAGE 4


                                                                   12/2/81









               supports file transfers in this manner to  one  of  several


               host  configurations:   the  Sigma 9 CP-V Operating System,


               the  PDP-11  RSX-11M  Operating  System,  or  the   VAX/VMS


               Operating   System.   The  desired  host  configuration  is


               specified when the program is assembled,  by  defining  the


               appropriate  symbol  in  the TALK prefix file ( see section


               3.1).











          2.1.2   B -  Initiate file transfer from host








                    This  command  performs  a  function  similar  to  the


               previous  command,  but  is used to transfer files from the


               host computer.  The same general procedure is used,  except


               that  the transfer is terminated by the receipt of the host


               computer's monitor prompt as the  first  character  in  any


               line.  Although this may occasionally cause problems, files


               can always be transfered in a "manual" mode  if  necessary.


               During file transfers, <CR>, <LF>, and <DEL> characters are


               not transfered to the output file.











          2.1.3  C -  Transmit the break command character to the host








                    This command will transmit to  the  host  the  control


               character  defined as the TALK break character for entering


               command mode.











          2.1.4  D -  Pause








                    This command allows the user  to  interrupt  TALK  and


               communicate  with  the  Monitor  Console  Routine (MCR).  A


               message is displayed on  the  terminal  indicating  how  to


               restart  TALK and a "STOP" directive is issued to the task.


               The program resumes execution  when  the  user  issues  the


               "UNSTOP" command to MCR.











          2.1.5  E -  Change EOR character








                    The user is prompted to enter  a  new  EOR  character.


               The  EOR  character  is used to delimit records in both the


               redirected input and output modes.  If an EOR character  is


               recieved  from  the  host  and the input is redirected, the







          Program TALK Documentation                                PAGE 5


                                                                   12/2/81









               next record from the input file is sent to the host.  Also,


               in  redirected  input mode, an EOR character is appended to


               each record sent to the  host.   If  an  EOR  character  is


               recieved  from  the  host and the output is redirected, the


               buffer  containing  all  characters  recieved   after   the


               previous EOR is written to the output file.





                    The default EOR character is a carriage return.  











          2.1.6   I -  Enter redirected input mode








                    In this mode, the terminal is disconnected as an input


               device,  and  data  is  transmitted  to  the  host  from  a


               specified file.  The redirected file is transmitted  record


               by record to the host on an EOR prompt basis.





                    Redirected input mode continues until the end of  file


               is reached, a read error occurs (including reading a record


               longer than INBSIZ, a symbol defined  in  the  TALK  source


               file), or it is cancelled explicitly by breaking to command


               mode and entering the command to cancel redirect input.





                    The default filename, TLKIN.,  is  used  if  the  user


               enters no filename when prompted.





                    If the input is already redirected, this command  will


               be ignored.











          2.1.7  J -  Exit redirected input mode








                    If the input is currently redirected, the  input  file


               is  closed,  and the terminal is reconnected to the host as


               an input device.  This command will be ignored if the input


               is not redirected.











          2.1.8  K -  Transmit the "break" control character to the host








                    This command simply transmits  the  control  character


               which  is  used as the command to transmit a "break" to the


               host.







          Program TALK Documentation                                PAGE 6


                                                                   12/2/81









          2.1.9  M -  Display the command menu








                    This  command  will  display  the  menu  of  available


               commands on the terminal and reissue the prompt for command


               input.











          2.1.10  O -  Enter redirected output mode








                    In this mode, everything sent to the terminal from the


               host  computer  will  also  be  copied to a specified file.


               Records are terminated by EOR characters  or  by  exceeding


               the buffer size, OFBSIZ ( defined in the TALK source file).


               Redirected output files have the  "list"  carriage  control


               attribute and can be editted normally.





                    Redirected  output  mode   continues   until   it   is


               explicitly  cancelled  by  breaking  to  command  mode  and


               entering the command to cancel redirected output.





                    The default filename, TLKOUT., is  used  if  the  user


               enters no filename when prompted.





                    If the output is already redirected, this command will


               be ignored.











          2.1.11  P -  Exit redirected output mode








                    If the output is  currently  redirected,  any  partial


               record  is  written  to  the  output  file  and the file is


               closed.  This command will be ignored if the output is  not


               redirected.











          2.1.12  Q -  Transmit a control-Q (^Q) to the host








                    This command simply transmits the ^Q character to  the


               host,  since  this character would otherwise be intercepted


               by TALK as a command to  restart  the  processing  of  host


               characters.







          Program TALK Documentation                                PAGE 7


                                                                   12/2/81









          2.1.13  S -  Transmit a control-S (^S) to the host








                    This command simply transmits the ^S character to  the


               host,  since  this character would otherwise be intercepted


               by TALK as  a  command  to  halt  the  processing  of  host


               characters.











          2.1.14  X -  Exit redirected input and/or output mode








                    This command exits any redirected mode  (input  and/or


               output) currently in effect.











          2.1.15  Z or ^Z -  Exit from TALK








                    This command will close any  redirected  input  and/or


               output  files  and terminate the program.  In addition, the


               port will be disconnected.  If desired, TALK  may  then  be


               rerun,  and  communication  with  the  host  will continue.


               Exiting from TALK will allow local file preparation without


               dropping  the  communications  line or logging off the host


               computer.







          Program TALK Documentation                                PAGE 8


                                                                   12/2/81









     3.0  Program Notes














          3.1  Parameter and Code Modifications








                    Program command codes and  I/O  buffer  sizes  may  be


               easily  changed.   These parameters are defined in the data


               definition area of the macro source code and  in  the  TALK


               prefix and system definition files.





                    The vector and CSR addresses for  each  port  must  be


               defined  in  the  appropriate  tables.  See the TALK system


               definition file (TALKSYS.MAC) for instructions on how to do


               this.   The  system  definition  file also contains symbols


               which define the host computer  for  which  TALK  is  being


               used.   If a version of TALK is desired to communicate with


               a PDP-11 RSX-11M system or a VAX/VMS  system,  comment  out


               the  definition of the symbol SIGMA9 and remove the comment


               indicator (;;;) from the definition of the symbol RSX11  or


               VAX.





                    The QSIZET or QSIZEP parameters should be increased if


               the  queue  overflow  message is displayed on the terminal.


               Currently, the port queue size is 600  characters  and  the


               terminal queue size is 200 characters.





                    The INBSIZ and OFBSIZ parameters  are  the  input  and


               output buffers sizes for the redirected files.  The current


               buffer sizes are 133 bytes for  input  and  133  bytes  for


               output.





                    In addition to the system definition  file,  there  is


               also  a  TALK prefix file (TALKPRE.MAC).  This file defines


               some macros and symbols which  are  also  needed  by  TALK.


               When  assembling  TALK,  the  prefix  file  and  the system


               definition file should be assembled along with  the  source


               modules  into the resulting object modules.  A command file


               (TALK.CMD) is provided with TALK to perform  the  necessary


               assembly and taskbuild operations.











          3.2  General








                    Should  TALK  be  abnormally  terminated,   the   user


               terminal  will  have  the  no-echo,  binary input, and full


               duplex characteristics set.







          Program TALK Documentation                                PAGE 9


                                                                   12/2/81









     4.0  Program Design








               On an abstract level, TALK is a simple  program.   Separate


          queues  are  used  for  characters  from  the  port and from the


          terminal.  Characters from the terminal are handled  by  an  AST


          routine, which queues the character and indicates that something


          is in the queue.  Port  characters  are  handled  in  a  similar


          manner through an "interrupt service routine" (ISR) via hardware


          interrupts.  The "connect to interrupt vector" directive (CINT$)


          is used.





               When both of the queues are empty, TALK waits for an  event


          flag  to be set by one of the interrupt routines.  This prevents


          the program from  competing  for  the  CPU  when  there  are  no


          characters  to be processed.  Once a character appears in one of


          the queues, both queues are processed until empty.





               Most prompted input from the terminal (EOR and file  names)


          are  entered  when the program is in a special mode.  Instead of


          being sent to the host, characters received from the terminal in


          this mode are buffered to create an input string.  By reading in


          this fashion, the unsolicited input feature need not  be  turned


          off, and host characters may be processed while typing input.





               The following sections contain the Program Design  Language


          (PDL) code for the TALK program modules.







          Program TALK Documentation                               PAGE 10


          TALK PDL Source Code                                     12/2/81









     4.1  PDL Source Code





          TALK


           


                initialize file i/o package


                CALL CNPRT - connect port terminal


                if


                  connect error


                then


                  EXIT


                else


                  CALL ATTDEV( TERMINAL ) - AST attach user terminal - read no echo


                  CALL CONTRL - handle all characters on queue


                  CALL DCNPRT - disconnect the port


                  CALL DETDEV( TERMINAL ) - detach user terminal - read with echo


                  if


                    redirected input


                  then


                    CALL CANINP - cancel redirected input


                  fi


                  if


                    redirected output


                  then


                    CALL CANOUT - cancel redirected output


                  fi


                fi


                stop







          Program TALK Documentation                                               PAGE 11


          TALK PDL Source Code                                                     12/2/81









          AST -- unsolicited character interrupt handler


           


                if


                  queue full


                then


                  indicate queue overflow


                else


                  put character on queue


                  if


                    pointer off queue


                  then


                    reset back of queue pointer


                  fi


                fi


                return from interrupt







          Program TALK Documentation                                               PAGE 12


          TALK PDL Source Code                                                     12/2/81









          PTINTR -- port interrupt routine for character receive


           


                disable interrupts


                if


                  queue has overflowed


                then


                  set error flag


                else


                  move character to back of port queue


                  if


                    "back of queue" pointer is at its limit


                  then


                    reset it to the front


                  fi


                fi


                set flag to indicate port data


                if


                  event flag needs to be set


                then


                  set event flag indicating presence of something in the queue


                fi


                enable interrupts


                return







          Program TALK Documentation                                               PAGE 13


          TALK PDL Source Code                                                     12/2/81









          CONTRL


           


                while


                  .TRUE.


                do /* Loop forever */


                  if


                    port queue processing has not been suspended


                  then


                    wait for a signal that there is something in a queue


                    if


                      the port queue is not empty


                    then


                      if


                        the port queue has overflowed


                      then


                        WRITE 'QUEUE OVERFLOW' message to terminal


                      else


                        CALL PRTIN( CHARACTER ) - process a port character


                        if


                          the port queue is getting full


                        then


                          CALL PSLEEP to put the host to sleep


                        fi


                      fi


                    fi


                  fi


                  while


                    there is something in the terminal queue


                  do


                    if


                      terminal queue has overflowed


                    then


                      WRITE 'QUEUE OVERFLOW' message to terminal


                    else


                      CALL TRMIN( CHARACTER ) - process a user terminal character


                      if


                        wish to exit program


                      then


                        return


                      fi


                    fi


                  od


                  if


                    port queue processing is not suspended


                  then


                    if


                      port queue is empty


                    then


                      if


                        host is asleep


                      then


                        CALL PAWAKE - to wake up the host


                      fi







          Program TALK Documentation                                               PAGE 14


          TALK PDL Source Code                                                     12/2/81









                      if


                        there is a record to be sent to port


                      then


                        CALL XFERP to transmit it


                      fi


                    fi


                  fi


                od







          Program TALK Documentation                                               PAGE 15


          TALK PDL Source Code                                                     12/2/81









          PRTIN( CHARACTER )


           


                if


                  a command is being sent to the host


                then


                  echo the character


                  if


                    the character is a <cr>


                  then


                    reset the command flag


                  fi


                else


                  if


                    input is redirected


                  then


                    if


                      character is a prompt for next file read


                    then


                      indicate a record is to be sent to port


                    fi


                  fi


                  echo the character


                  if


                    output is redirected


                  then


                    if


                      character is not <DEL>, <CR>, or <LF>


                    then


                      if


                        TALK is helping with file transfer


                      then


                        if


                          the first character in the line is a monitor prompt


                        then


                          CALL CANOUT - to cancel redirected output


                          return


                        fi


                      fi


                      move character to output file buffer


                    else


                      if


                        CHARACTER is EOR


                      then


                        CALL WRTBUF - to write a record to the output file


                      fi


                    fi


                  fi


                fi


                return







          Program TALK Documentation                                               PAGE 16


          TALK PDL Source Code                                                     12/2/81









          TRMIN( CHARACTER )


           


                case in the process of


                / building a file name /


                  CALL BUILD( CHARACTER ) - build file name


                / changing the EOR character


                  CALL ENTEOR( CHARACTER ) - change EOR character


                / entering a command /


                  CALL CMDIN( CHARACTER )


                else


                  case CHARACTER of


                  / enter "command input mode" command /


                    CALL BREAK


                  / transmit break command /


                    CALL SNDBRK


                  / suspend port queue processing command /


                    CALL PSLEEP


                    set "suspend" flag


                  / resume port queue processing command /


                    clear "suspend" flag


                  / suspend/resume terminal echo command /


                  if


                    TALK is helping with file transfer


                  then


                    toggle the echo flag


                  fi


                  else


                    if


                      not redirected input


                    then


                      WRITE CHARACTER to port


                    fi


                  esac


                esac


                return







          Program TALK Documentation                                               PAGE 17


          TALK PDL Source Code                                                     12/2/81









          CMDIN


           


                if


                character is control-Q or control-S


                then


                  return


                fi


                if


                  character is lower case


                then


                  convert character to upper case


                fi


                if


                  not legal command character


                then


                  report error to user


                  CALL BREAK - to prompt for new command


                else


                  case  command to


                  / transmit control character /


                    CALL SENDPR( control character )


                  / initiate file transfer to host /


                    CALL RDIHLP


                  / initiate file transfer from host /


                    CALL RDOHLP


                  / display the command menu /


                    CALL MENU - to display the menu


                    CALL BREAK - to prompt for command


                  / cancel redirected input and/or output /


                    CALL PAWAKE to wake up the host


                    CALL CANINP


                    CALL CANOUT


                  / cancel redirected input /


                    CALL CANINP


                  / cancel redirected output /


                    CALL CANOUT


                  / change EOR character /


                    CALL ASKEOR - to prompt for new EOR character


                  / exit program /


                    set exit flag


                  / redirect input /


                    CALL REDINP


                  / redirect output /


                    CALL REDOUT


                  esac


                  clear command flag


                  CALL PAWAKE - to wake up the host


                fi


                RETURN







          Program TALK Documentation                                               PAGE 18


          TALK PDL Source Code                                                     12/2/81









          BREAK


           


                CALL PSLEEP - to put the host to sleep


                indicate that port queue processing is suspended


                indicate command mode is in effect


                issue the prompt to enter a command


                RETURN


























          MENU


           


                WRITE the command menu to the terminal


                RETURN







          Program TALK Documentation                                               PAGE 19


          TALK PDL Source Code                                                     12/2/81









          RDIHLP


           


                prompt for destination file name


                set flag to indicate that a redirected input command is being built


                initialize the command length, file name length,


                    and their respective pointers


                set flag to indicate that TALK is helping with a file transfer


                RETURN


























          RDOHLP


           


                prompt for source file name


                set flag to indicate that a redirected output command is being built


                initialize the command length, file name length,


                    and their respective pointers


                set flag to indicate that TALK is helping with a file transfer


                return







          Program TALK Documentation                                               PAGE 20


          TALK PDL Source Code                                                     12/2/81









          PSLEEP


           


                if


                  port output not already suspended


                then


                  case


                  / host is SIGMA9 /


                    send an <ESC> H to suspend output


                  / host is RSX11M system /


                    send a ^S to suspend output


                  esac


                fi


                return


























          PAWAKE


           


                clear flag indicating suspended output


                case


                / host is SIGMA9 /


                  send an <ESC> to resume host output


                / host is an RSX11M system /


                  send a ^Q to resume host output


                esac


                return







          Program TALK Documentation                                               PAGE 21


          TALK PDL Source Code                                                     12/2/81









          SNDBRK


           


                set the "transmit break" bit in the transmit CSR


                issue "mark time" directive to wait for one tick (1/60 second)


                    and then execute AST routine CLRBRK


                if


                directive status word indicates failure


                then


                  clear the "transmit break" bit in the CSR


                fi


                return


























          CLRBRK


           


                clear the "transmit break" bit in the transmit CSR


                pop the stack


                return from AST







          Program TALK Documentation                                               PAGE 22


          TALK PDL Source Code                                                     12/2/81









          REDINP


           


                if


                  not redirected input


                then


                  indicate that we are building an input file name


                  initialize file name pointer


                  CALL ASKNM - prompt user to enter a file name


                fi


                return


























          REDOUT


           


                if


                  not redirected output


                then


                  indicate that we are building an output file name


                  initialize file name pointer


                  CALL ASKNM - prompt user to enter a file name


                fi


                return







          Program TALK Documentation                                               PAGE 23


          TALK PDL Source Code                                                     12/2/81









          CANINP


           


                if


                  redirected input


                then


                  CALL CLSFLE( type = INPUT ) - close redirected input file


                  turn off redirected input indicator


                fi


                if


                TALK is helping with file transfer


                then


                  clear terminal echo flag


                  CALL SENDPR( <EOF> )


                fi


                clear help flag


                return


























          CANOUT


           


                if


                  redirected output


                then


                  if


                    output file buffer is not empty


                  then


                    CALL WRTBUF - write output buffer to redirected output file


                  fi


                  CALL CLSFLE( type = OUTPUT ) - close redirected output file


                  turn off redirected output indicator


                  clear help flag and terminal echo flag


                fi


                return







          Program TALK Documentation                                               PAGE 24


          TALK PDL Source Code                                                     12/2/81









          ASKNM


           


                WRITE 'Enter file name:' to user terminal


                initialize file name length to zero


                return







          Program TALK Documentation                                               PAGE 25


          TALK PDL Source Code                                                     12/2/81









          BUILD( CHARACTER )


           


                if


                  CHARACTER is a DEL


                then


                  erase last character written on the terminal


                  delete last character placed in file name buffer


                else


                  if


                    CHARACTER is a CR


                  then /* End of file name */


                    send a <CR> to the terminal


                    if


                      building a host file name


                    then


                      append any trailer to the command string


                      if


                        transferring file to host


                      then


                        CALL REDINP


                      else


                        CALL REDOUT


                      fi


                    else /* building a local file name */


                      CALL OPNFLE - to open file


                      turn off build file name indicator


                      if


                        TALK is helping with file transfer


                      then


                        CALL SNDCMD( command string )


                      fi


                    fi


                  else


                    echo CHARACTER on user terminal


                    if


                      file name is longer than legal name


                    then /*Error, stop building file name */


                      WRITE 'File name is too long' to user terminal


                      turn off build file name indicator


                    else


                      place CHARACTER at the end of file name buffer


                    fi


                  fi


                fi


                return







          Program TALK Documentation                                               PAGE 26


          TALK PDL Source Code                                                     12/2/81









          OPNFLE


           


                prepare file name buffer


                if


                  want to open an input file


                then


                  open input file


                  if


                    not open error


                  then


                    turn on redirected input indicator


                    WRITE message indicating that input is redirected


                    if


                      TALK is not helping with a file transfer


                    then


                      indicate that there is a record to be transfered


                    fi


                  else


                    WRITE ' File open error' to user terminal


                    clear help flag


                  fi


                else


                  open output file


                  if


                    not open error


                  then


                    turn on redirected output indicator


                    WRITE message indicating that output is redirected


                  else


                    WRITE 'FILE OPEN ERROR' to user terminal


                    clear help flag


                  fi


                fi


                return







          Program TALK Documentation                                               PAGE 27


          TALK PDL Source Code                                                     12/2/81









          SNDCMD


           


               get address and length of command


               until  


                 all characters are sent


               do


                 CALL SENDPR( command character )


               od


               return


























          ASKEOR


           


                WRITE 'Enter new EOR character' to user terminal


                turn on change EOR character indicator


                return


























          ENTEOR( CHARACTER )


           


                echo CHARACTER to user terminal


                replace EOR by CHARACTER


                turn off change EOR character indicator


                return


























          CLSFLE( TYPE )


           


                close file of type = INPUT or OUTPUT


                return







          Program TALK Documentation                                               PAGE 28


          TALK PDL Source Code                                                     12/2/81









          XFERP


           


                READ RECORD from redirected input file


                if


                  not end of file and not read error


                then


                  append an EOR character to RECORD


                  until


                    end of record


                  do


                    send a character to port


                    if


                      host is RSX11M system


                    then


                      wait for host to echo the character


                    fi


                  od


                else


                  CALL CANINP - stop redirected input


                fi


                return


























          WRTBUF


           


                WRITE output buffer to redirected output file


                return







          Program TALK Documentation                                               PAGE 29


          TALK PDL Source Code                                                     12/2/81









          CNPRT


           


                set up DPB for terminal read/write


                until


                  legal channel specified


                do


                if


                  channel not specified in the TALK invocation


                then


                  prompt for and read in channel number


                  if


                    error on read


                  then


                    indicate error


                    return


                  fi


                fi


                od


                connect to interrupt vectors


                if


                no errors on connecting


                then


                  report successful connect


                else


                  report failure to connect


                  set carry to indicate failure


                fi


                return







          Program TALK Documentation                                               PAGE 30


          TALK PDL Source Code                                                     12/2/81









          ATTDEV( DEVICE )


           


                save DEVICE characteristics


                set new DEVICE characteristics


                attach DEVICE with unsolicited character AST


                return


























          DETDEV( DEVICE )


           


                detach DEVICE


                set DEVICE characteristics


                return







          Program TALK Documentation                               PAGE 31


          TALK PDL Source Code                                     12/2/81









     5.0  Building TALK








               A command file  (TALK.CMD)  is  provided  with  TALK  which


          performs  the  assembly and/or taskbuild operations necessary to


          build the program.  This command file  should  be  used,  rather


          than  performing  the  operations  manually,  to insure that the


          required options are specified.