PIN - Procedure Interpreter
                         ===========================

                                Users' Guide
                                ============

          The Indirect Command File Processor (AT.) is an  exceptionally
     flexible  and  useful  program.  Unfortunately it is also very big,
     and for the user who only wishes to use it to do  compilations  and
     taskbuilds (or suchlike) sequentially on a small system can be very
     inefficient  in  terms  of  system   resources.    PIN   (Procedure
     INterpreter)  is  a  task  1/4 to 1/6 the size of the Indirect File
     processor which is used  identically  to  ...AT.   to  control  the
     assembly and taskbuild process during program development.  It does
     not recognize the special ...AT.  commands  but  only  accepts  one
     line  MCR  type  commands (and a very limited number of special PIN
     commands).  If during the execution of any command a fatal error is
     encountered, PIN will cease execution of the command file and allow
     the user to correct the problem - the  command  line  creating  the
     error  is  displayed.   By  default,  other  command  lines are not
     displayed.  PIN assumes that the command file given to it will have
     the extension .PRC (For PRoCedure), but if a different extension is
     explicitly used, PIN will use that name in looking for the  command
     file.  

          PIN is invoked by typing
        
                        PIN procedure_file
        or
                        #procedure_file
      
     where <procedurefile> is a  commandfile  (default  extension  .PRC)
     containing  ordinary  MCR  commands  and,  optionally,  special PIN
     commands.  The second form of  the  PIN  command  (via  the  #)  is
     available  only  if  a  system  has installed a SLP patch to MCRDIS
     (MCR...) and indicates that the procedure file  is  to  be  SPAWNED
     directly to MCR rather than indirectly to MCR via ...AT.

          PIN allows a small number of internal commands,  specified  in
     the commandfile, as follows:-
      
         $COW    - Continue on Warning Exit status (the default).
         $DE     - delete the .CMD file on closing.
         $EOW    - Exit on Warning status.
         $NODE   - do not delete the .PRC file on closing (the default).
         $NOTR   - do not print each command.
         $TR        - print each command as it is executed.
      
     Initially PIN starts out with $COW, $NOTR, and $ NODE.



                                                                  Page 2



                             PIN Error Messages
                             ==================

          PIN may report one of the following error messages:-

          1.  PIN - Syntax error

              The commandline contained less than four characters - i.e.
              no commandfile was specified.

          2.  PIN - Illegal file name

              PIN could not  parse  the  specified  file.   Correct  the
              filename and respecify the line.

          3.  PIN - File open error

              PIN could  not  open  the  specified  file.   Correct  the
              problem and submit the line.

          4.  PIN - No such file

              The specified commandfile does not  exist.   Resubmit  the
              line specifying a valid filename.

          5.  PIN - Spawn failure

              The Spawn directive failed - probably because it  was  not
              included  in  the  System  Generation.  PIN cannot operate
              without the Spawn Directive.

          6.  PIN - Stop for Event Flag failed

              The 'Stop for Event  Flag'  directive  failed  -  probably
              because it was not included in the System Generation.  PIN
              cannot operate without the Stop for Event Flag Directive.

          7.  PIN - WARNING, Exit with non-fatal error

              A command spawned by PIN resulted in  a  'non-fatal'  exit
              status (2).  PIN prints out the current line and continues
              unless $EOW has preceeded the occurence of the error.

          8.  PIN - FATAL, Exit with severe error

              A command spawned by PIN resulted in a 'fatal' exit status
              (4).  PIN prints out the current line and exits.

          9.  PIN - Procedure file read error

              An error was detected while reading the command  procedure
              file.  Check the file and resubmit it if necessary.



                                                                  Page 3



          10. PIN - Procedure file close error

              An error was detected while closing the command  procedure
              file.  Check the file to determine the cause of the error.

          11. PIN - Only single line, valid MCR commands allowed

              A command line was detected  that  was  not  a  valid  MCR
              command   line,  nor  an  internal  command.   Remove  the
              offending line and resubmit the commandfile.

          12. PIN - Unknown internal command

              A  command  line  was  detected  that  started  with  a  $
              (indicating an internal command) but which did not contain
              a valid internal command.  Correct the offending line  and
              resubmit the commandfile.




                         PIN - Procedure INterpreter
                         ===========================


                          System Instalation Guide
                          ========================

          PIN is very  simple  in  construction.   It  obtains  the  MCR
     command  line  using GCML$, parses the filename given via CSI$1 and
     opens the file for read.  It then reads each record in the file and
     checks  to  see  if it is an internal command and if not (and it is
     valid for MCR) spawns it to  MCR,  checking  the  exit  status  and
     acting  accordingly.  When all commands are processed it closes the
     file and exits.

          It   handles   all   the   internal   commands    by    simply
     setting/clearing  action flags which are tested when required.  PIN
     is a non-privileged task with a taskname of ...PIN, using  2  units
     (Unit 1 is assigned to SY:  and Unit 2 to TI:).  PIN is built using
     the command file PIN.CMD.  By default it builds  with  FCSRES.   If
     your  system  does  not  have  FCSRES,  PIN.CMD should be edited to
     remove references to FCSRES.  A HELP file PIN.HLP exists and can be
     added to the HELP files on LB:[1,2] (or LB1:[1,2]).

          An alternate version of PIN  which  uses  direct  file  access
     QIO's  to  F11ACP rather than calls to FCS was submitted on the RSX
     Spring 81 symposium tape by  Phil  Stephensen-Payne.   For  systems
     which  do  not have an FCSRES it will build a small, 2Kw version of
     PIN.  He also adds a $CH switch to allow chaining from one PIN .PRC
     file  to  another.   While  his version looks very good, and in all
     probability works as well as this version, the  PIN  supplied  with
     KMSKIT  will continue to use FCS/FCSRES.  There are several reasons



                                                                  Page 4



     for this.  First, using the GCML/CSI$1  interface  guarantees  that
     PIN  can parse and open the procedure file no matter what DEC does.
     DEC might change or modify F11ACP to add new  functionality.   This
     happended  in  V4.0  with MTAACP.  The QIO calls required to access
     files on tape changed and existing programs which did all file  I/O
     on  the  QIO level ceased to work.  Second, if FCS is used for file
     I/O, PIN is migratable to a VAX system.  Third, using FCS,  PIN  is
     easily  upgraded  to  using either BIG-Buffering or Multi-Buffering
     for applications that require very high throughput for commands.