FILE:PLOT.DOC
	THIS FILE IS TO PROVIDE DOCUMENTATION
FOR THE PLOT ROUTINE WRITTEN FOR DOUG PHILLIPS BY JEFF
HAMILTON.
 
	PLOT.OLB CONTAINS:
		BOTTOM
		CLEARF
		CLEARI
		CLEARB
		ELMNTF
		ELMNTI
		GET
		GRID
		FLPLOT
		LABELX
		LABELY
		LIMITF
		LIMITI
		LINEX
		LINEY
		LOAD
		LOADI
		OFF
		ON
		PLOTFL
		PLOTIN
		SIDE
		TOP
		WHERXY
		ZTICK
 
	TO USE PLOT.OLB USE THIS:
TKB  A.TSK,A.MAP=A.OBJ,B.OBJ,...,DK1:[1,54]PLOT.OLB
	THIS WILL LINK THE PLOT SUBROUTINES WITH YOUR TASK.
 


	HERE IS AN EXAMPLE PROGRAM USING SOME OF THE SUBROUTINES
CONTAINED IN PLOT.OLB.
 
	PROGRAM FFTPLT
C
C	SET UP A PARAMETER FOR EASY CHANGING
C
	PARAMETER ISIZE=1024
	BYTE FILE(80)
	COMPLEX CRRAY(ISIZE)
	DIMENSION ARRAY(ISIZE),ERRAY(ISIZE),B(2),LIM(4)
	DIMENSION LIMITX(2),IK(2),LL(2),C(2),D(2),ALIM(2)
C
C	FIND OUT THE NAME OF THE DATA FILE TO BE USED
C
	TYPE *,'ENTER NAME OF FILE TO BE USED'
	ACCEPT 100,NCH,(FILE(I),I=1,NCH)
100	FORMAT(Q,80A1)
C
C	TURN ON PLOTTER
C
	CALL ON(2)
C
C	FIND THE OUTSIDE LIMITS OF THE PLOTTING AREA
C
	CALL GET(LIM)
C
C	DRAW THE GRID WITH FOUR PLOTTING REGIONS
C
	CALL GRID(LIM,-10,4)
C
C	LOAD THE COMPLEX ARRAY WITH DATA FROM THE DATA FILE
C
	CALL LOADC(CRRAY,ISIZE,FILE,1,1,ISTAT)
C
C	CHECK FOR PROPER COMPLEATION
C
	IF(ISTAT.EQ.1)GO TO 5
	CALL EXIT
C
C	GET ARRAYS TO BE PLOTTED
C
5	DO 10,J=1,ISIZE
	ARRAY(J)=REAL(CRRAY(J))
10	ERRAY(J)=AIMAG(CRRAY(J))
C
C	GET THE MAXIMUM AND MINIMUM OF THE REAL ARRAY
C
	CALL LIMITF(ARRAY,ISIZE,B)
C
C	SET UP THE LIMITS FOR THE ARRAY SIZE
C
	LIMITX(1)=1
	LIMITX(2)=ISIZE
C
C	GET VALUES TO BE PRINTED ON THE BOTTOM OF THE PLOT.
C
	ALIM(1)=1.
	ALIM(2)=FLOAT(ISIZE)
C
C	PLOT THE REAL ARRAY IN THE FIRST PLACE ON THE PLOTTER
C
	CALL PLOTFL(1,4,B,ARRAY,ISIZE,LIM,LIMITX)
C
C	DRAW A TICK AT THE ZERO POINT FOR REFERENCE
C
	CALL ZTICK(LIM,4,1,B)
C
C	LABEL THE PLOT SO WE KNOW WHAT IT IS
C
	CALL SIDE(LIM,'REAL DATA',9,4,1)
C
C	LABEL THE Y LIMITS OF THE PLOTTED ARRAY
C
	CALL LABELY(LIM,B,3,4,1,1.)
C
C	PLOT THE IMAGINARY ARRAY IN THE SECOND PLOTTING REGION.
C
	CALL PLOTFL(2,4,B,ERRAY,ISIZE,LIM,LIMITX)
C
C	DO ZERO TICK MARK
C
	CALL ZTICK(LIM,4,2,B)
C
C	LABEL THE SIDE
C
	CALL SIDE(LIM,'IMAG DATA',9,4,2)
C
C	LABEL THE LIMITS
C
	CALL LABELY(LIM,B,3,4,2,1.)
C
C	DO THE FFT
C
	CALL FFT(CRRAY,ISIZE,1)
C
C	LOAD THE PLOTTING ARRAYS
C
	DO 20, J=1,ISIZE
	ARRAY(J)=REAL(CRRAY(J))
20	ERRAY(J)=AIMAG(CRRAY(J))
C
C	FIND THE LIMITS OF THE REAL FFT
C
	CALL LIMITF(ARRAY,ISIZE,C)
C
C	FIND THE POSITION OF THE MAXIMUM FOR LATER USE
C
	CALL ELMNTF(ARRAY,ISIZE,IK)
C
C	FIND TWO POINTS ON EITHER SIDE OF THE MAXIMUM
C
	LL(1)=IK(2)-10
	LL(2)=IK(2)+10
C
C	PLOT THE REAL FFT IN THE THIRD POSITION 
C
	CALL PLOTFL(3,4,C,ARRAY,ISIZE,LIM,LIMITX)
C
C	DO ZERO TICK MARK
C
	CALL ZTICK(LIM,4,3,C)
C
C	DRAW A LINE ACROSS THE MAXIMUM ABOUT HALF WAY UP
C
	CALL LINEX(LIM,4,3,C,C(2)/2.,LIMITX,LL)
C
C	LABEL THE PLOT
C
	CALL SIDE(LIM,'REAL FFT',8,4,3)
C
C	LABEL THE LIMITS
C
	CALL LABELY(LIM,C,3,4,3,1.)
C
C	FIND THE LIMITS OF THE IMAGINARY FFT
C
	CALL LIMITF(ERRAY,ISIZE,D)
C
C	PLOT THE IMAGINARY FFT IN THE FOURTH POSITION
C
	CALL PLOTFL(4,4,D,ERRAY,ISIZE,LIM,LIMITX)
C
C	DO THE ZERO TICK MARKS
C
	CALL ZTICK(LIM,4,4,D)
C
C	LABEL THE PLOT
C
	CALL SIDE(LIM,'IMAG FFT',8,4,4)
C
C	LABEL THE LIMITS
C
	CALL LABELY(LIM,D,3,4,4,1.)
C
C	LABEL THE BOTTOM OF THE PLOT SO WE CAN TELL HOW MANY POINTS
C	THERE IS.
C
	CALL LABELX(LIM,ALIM,1,1.)
C
C	DRAW A LINE DOWN THE MIDDLE OF THE FFT PLOTS BECAUSE
C	THEY ARE JUST MIRRORS OF THEMSELVES.
C
	CALL LINEY(LIM,4,3,C,ISIZE/2,LIMITX,C)
	CALL LINEY(LIM,4,4,D,ISIZE/2,LIMITX,D)
C
C	WRITE THE FILE NAME ON THE BOTTOM OF THE PLOT SO
C	WE WILL KNOW WHERE THE DATA CAME FROM.
C
	CALL BOTTOM(LIM,FILE,NCH)
C
C	WRITE OUR NAME ON THE TOP SO THEY WILL KNOW WHO
C	DID THIS GREATJOB.
C
	CALL TOP(LIM,'FFTPLT',6)
C
C	TURN PLOTTER OFF
C
	CALL OFF
	END


	BOTTOM
	THE SUBROUTINE BOTTOM WILL ENABLE THE USER TO PRINT A STRING
ON THE BOTTOM OF THE PLOT.
 
	FORM:		CALL BOTTOM(LIM,ARRAY,ISIZE)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			BYTE ARRAY
			DIMENSION ARRAY(ISIZE)
 
	A STRING ARRAY IS WRITTEN ON THE BOTTOM OF THE PLOT SO AS
TO NOT INTERFER WITH THE OUTPUT FROM LABELX.  THERE ARE ISIZE
CHARACTERS.  THE DEFAULT SIZE FOR THE CHARACTERS ARE USED
UNLESS THERE ARE TOO MANY; WHERE AUTO SCALING COMES INTO
EFFECT TO MAKE THEM FIT.


	CLEARF
	THE SUBROUTINE CLEARF WILL SET ALL THE ELEMENTS OF
A FLOATING POINT ARRAY TO ZERO.
 
	FORM:		CALL CLEARF(ARRAY,ISIZE)
 
	WHERE:		DIMENSION ARRAY(ISIZE)


	CLEARI
	THE SUBROUTINE CLEARI WILL SET ALL THE ELEMENTS OF
A INTEGER ARRAY TO ZERO.
 
	FORM:		CALL CLEARI(IRRAY,ISIZE)
 
	WHERE:		DIMENSION IRRAY(ISIZE)


	CLEARB
	THE SUBROUTINE CLEARB WILL SET ALL THE ELEMENTS OF
A BYTE ARRAY TO OCTAL ZERO.
 
	FORM:		CALL CLEARB(ARRAY,ISIZE)
 
	WHERE:		BYTE ARRAY
			DIMENSION ARRAY(ISIZE)


	ELMNTF
	THE SUBROUTINE ELMNTF WILL RETURN THE ARRAY ELEMENT
POSITION WHERE THERE IS THE MAXIMUM AND MINIMUM VALUES OF THE ARRAY.
 
	FORM:		CALL ELMNTF(ARRAY,ISIZE,IK)
 
	WHERE:		DIMENSION ARRAY(ISIZE)
			DIMENSION IK(2)
			IK(1) IS THE ARRAY ELEMENT WITH THE MINIMUM
				OF THE ARRAY
			IK(2) IS THE ARRAY ELEMENT WITH THE MAXIMUM
				OF THE ARRAY
 
	THE INTEGERS THAT ARE RETURNED CAN BE USED IN FFT ANALYSIS
TO FIND THE CENTER FREQUENCIES.


	ELMNTI
	THE SUBROUTINE ELMNTI WILL RETURN THE ARRAY ELEMENT
POSITION WHERE THERE IS THE MAXIMUM AND MINIMUM VALUES OF THE INTEGER
ARRAY.
 
	FORM:		CALL ELMNTI(IRRAY,ISIZE,IK)
 
	WHERE:		DIMENSION IRRAY(ISIZE)
			DIMENSION IK(2)
			IK(1) IS THE ARRAY ELEMENT WITH THE MINIMUM
				VALUE IN THE ARRAY
			IK(2) IS THE ARRAY ELEMENT WITH THE MAXIMUM
				VALUE IN THE ARRAY
 
	THE INTEGERS THAT ARE RETURNED CAN BE USED IN FFT ANALYSIS 
TO FIND THE CENTER FREQUENCY.


	GET
	THE SUBROUTINE GET WILL RETURN THE OUTSIDE LIMITS
IN THE FORM OF A FOUR ELEMENT ARRAY.
 
	FORM:	CALL GET(LIM)
 
	WHERE :		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
 
	A STANDARD SIZE PLOT WILL FILL A STANDARD SIZE PIECE OF
PRINTER PAPER. THE SUBROUTINE WILL ASK THE ENTERING TERMINAL IF 
A STANDARD SIZE PLOT IS DESIRED.  A Y RETURN WILL RETURN TO THE 
CALLING PROGRAM, THE STANDARD COORDINATES.  ANY OTHER ANSWER WILL 
ENABLE THE USER TO ENTER THE LIMITS VIA THE CALL BUTTON ON 
THE PLOTTER.


	GRID
	THE SUBROUTINE GRID WILL DRAW ON THE PLOTTER THE OUTSIDE
GRID TO BE USED BY THE OTHER SUBROUTINES.  
 
	FORM:	CALL GRID(LIM,NUMX,NUMY)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			NUMX ISTHE NUMBER OF DIVIDED OFF REGIONS
		IN THE X DIRECTION(TICKS IF NEGATIVE)
			NUMY IS THE NUMBER OF DIVIDED OFF REGIONS
		IN THE Y DIRECTION(TICKS IF NEG)
 	
	THE SIZE OF THE GRID IS DETERMINED BY LIM, WHICH CAN COME 
FROM THE GET SUBROUTINE.  IF NUMX IS NEGATIVE, TICK MARKS WILL
BE DRAWN AT THE TOP AND BOTTOM OF THE GRID.  IF POSITIVE,
THEN LINES WILL BE DRAWN ALL THE WAY ACROSS.  THE SAME OCCURS
FOR NUMY.
	NOTICE : NUMX AND NUMY ARE THE NUMBER OF REGIONS AND NO THE
NUMBER OF LINES.


	FLPLOT
	THE SUBROUTINE FLPLOT WILL PLOT AN ARRAY OF FLOATING POINT
NUMBERS ON THE PLOTTER ON THE PLOT AT A SPECIFIC LOCATION.
 
	FORM:		CALL FLPLOT(I,NUM,B,ARRAY,ISIZE,LIM,LIMITX,IXX,FX)
 
	WHERE:		I IS THE REGION NUMBER ON THE PLOT COUNTING DOWN.
			NUM IS THE TOTAL NUMBER OF REGIONS.
			DIMENSION B(2)
			B(1) IS THE LOWER SCALE LIMIT
			B(2) IS THE UPPER SCALE LIMIT.
			DIMENSION ARRAY(ISIZE)
			DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			DIMENSION LIMITX(2)
			LIMITX(1) IS THE LOWER INTEGER ARRAY ELEMENT TO USE IN PLOT
			LIMITX(2) IS THE UPPER INTEGER ARRAY ELEMENT TO USE IN PLOT
			IXX IS THE POSITION NUMBER ON THE X DIRECTION
				THE ARRAY IS PLOTTED AT.
			IXX=0	SETS ALL THE ARRAY ELEMENTS 
				OUTSIDE THE RANGE OF ISIZE TO 0
			FX IS THE FLOATING POINT NUMBER LAST USED
				IN THE PLOTFL ROUTINE(NEEDED TO CONNECT
				THE ARRAY ELEMENTS IN MULTI ARRAY
				PLOTS IN THE SAME PLOTTING REGION
 
	THE VALUE IN ARRAY WILL BE CONNECTED IN A PLOT THAT IS SCALED
SO THAT THE TOP OF THE PLOTTING REGION CORRESPONDS TO B(2) AND THE 
BOTTOM  TO B(1).  THE LOWER X LIMIT WILL BE LIMITX(1) AND THE UPPER X LIMIT
WILL BE LIMITX(2) AND THE POINTS WILL BE PLACED IN ASCENDING ORDER
AS INTEGERS.  MORE THAN ONE SET OF ARRAYS CAN BE PLOTTED IN THE
REGION IF THE IXX VALUE TELLS WHERE THEY ARE TO BE PLOTTED
AND FX IS USED SO THAT THE END OF ONE ARRAY WILL PROPERLY
CONNECT WITH THE FIRST OF THE NEXT ARRAY.


	LABELX
	THE SUBROUTINE LABELX WILL ENABLE THE USER TO PRINT THE LIMITS
OF THE PLOTTED DATA ON THE X AXIS.
 
	FORM:		CALL LABELX(LIM,VALUE,ITYPE,SCALE)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			DIMENSION VALUE(2)
			VALUE(1) IS THE LOWER VALUE TO BE PRINTED.
			VALUE(2) IS THE UPPER VALUE TO BE PRINTED.
			ITYPE IS THE FORMAT TO BE USED.
			ITYPE=1		INTEGER FORM
			ITYPE=2		FLOATING POINT FORM
			ITYPE=3		EXPONINTIAL FORM
			SCALE IS THE FRACTION OF THE DEFAULT SIZE
 
	THE VAULUES ARE PRINTED ON THE BOTTOM OF THE PLOT NEAR
THE LEFT SIDE FOR THE LOWER VALUE AND NEAR THE RIGHT SIDE FOR
THE UPPER VALUE.  THE FORMAT IS DETERMINED BY THE ITYPE VALUE.
IF THE INTEGER FORM IS CHOSEN THEN IT MUST BE LESS THAN 32000.
THE FLOATING POINT FORMAT IS CHOSEN TO MATCH THE NUMBER AND UNEXPECTED
RESULTS CAN HAPPEN IF IT IS TOO LARGE OR TOO SMALL.  IF THE RANGE IS
UNKNOWN OR IT IS KNOWN TO BE TOO LARGE THE EXPONITIAL FORMAT 
SHOULD BE CHOSEN.  THE DEFAULT SIZE FOR THE
LETTERS IS 56 WIDE BE 88 TALL.  A VALUE OF SCALE=1. WILL MAKE THE
THE NUMBERS THIS SIZE.


	LABELY
	THE SUBROUTINE LABELY WILL PRINT THE MAX AND MIN VALUES OF
THE PLOTS YOU DO.  IF MORE THAN ONE PLOT IS DONE IN THE VERTICAL 
DIRECTION THE LOCATION SHOULD BE SPECIFIED.
 
	FORM:		CALL LABELY(LIM,VALUE,ITYPE,NUM,I,SCALE)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) ISTHE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			DIMENSION VALUE(2)
			VALUE(1) IS THE LOWER VALUE TO BE PRINTED.
			VALUE (2) IS THE UPPER VALUE TO BE PRINTYED.
			ITYPE IS THE FORMAT TO BE USED.
			ITYPE=1	INTEGER FORMAT
			ITYPE=2	FLOATING POINT FORMAT
			ITYPE=3	EXPONITIAL FORMAT
			NUM IS THE TOTAL NUMBER OF VERTICAL PLOTS.
			I IS THE POSITION NUMBER OF THE PLOT BEING LABELED.
		COUNTING DOWN.
			SCALE IS THE FRACTION OF THE DEFAULT SIZE.
 
	THE VALUES ARE PRINTED ON THE LEFT SIDE OF THE PLOT. THE UPPER
VALUE IS PRINTED NEAR THE UPPER SIDE OF THE PLOT SELECTED.  THE 
LOWER VALUE IS PRINTED NEAR THE LOWER SIDE OF THE PLOT SELECTED.
THE FORMAT IS DETERMINED BY THE ITYPE VALUE.  AUTO SCALING OF NUMBER 
SIZE MAY TAKE OVER IF THEY WONT FIT IN THE SPACE PROVIDED.
IF THE INTEGER FORM IS CHOSEN THEN IT MUST BE LESS THAN 32000.
THE FLOATING POINT FORMAT IS CHOSEN TO MATCH THE NUMBER AND UNEXPECTED
RESULTS CAN HAPPEN IF IT IS TOO LARGE OR TOO SMALL.  IF THE RANGE IS
UNKNOWN OR IT IS KNOWN TO BE TOO LARGE THE EXPONITIAL FORMAT 
SHOULD BE CHOSEN.  THE DEFAULT SIZE FOR THE
LETTERS IS 56 WIDE BE 88 TALL.  A VALUE OF SCALE=1. WILL MAKE THE
THE NUMBERS THIS SIZE.


	LIMITF
	THE SUBROUTINE LIMITF WILL RETURN THE MAXIMUM AND MINIMUM
VALUES OF A REAL ARRAY.
 
	FORM:		CALL LIMITF(ARRAY,ISSIZE,B)
 
	WHERE:		DIMENSION ARRAY(ISIZE)
			DIMENSION B(2)
			B(1) IS THE MINUMUM VALUE OF THE ARRAY.
			B(2) IS THE MAXIMUM VALUE OF THE ARRAY.
 
	THE VALUES THAT ARE RETURNED CAN BE USED IN LABELY TO
CORRECTLY LABEL THE SCALING.


	LIMITI
	THE SUBROUTINE LIMITI WILL RETURN THE MAXIMUM AND MINIMUM
VALUES OF AN INTEGER ARRAY.
 
	FORM:		CALL LIMITI(IRRAY,ISIZE,K)
 
	WHERE:		DIMENSION IRRAY(ISIZE)
			DIMENSION K(2)
			K(1) IS THE MINIMUM VALUE OF THE IRRAY.
			K(2) IS THE MAXIMUM VALUE OF THE IRRAY.
 
	THE VALUES THAT ARE RETURNED CAN BE USED IN LABELX OR LABELY
TO CORRECTLY LABEL THE SCALING.


	LINEX
	THE SUBROUTINE LINEX WILL DRAW A HORIZONTAL LINE IN THE GIVEN
REGION SCALED TO THE RIGHT HEIGHT BETWEEN TWO GIVEN ARRAY ELEMENT NUMBERS.
 
	FORM:		CALL LINEX(LIM,NUM,I,B,Y,LIMITX,LL)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			NUM IS THE NUMBER OF PLOTTING REGIONS BEING USED
			I IS THE PLOTTING REGION BEING USED NOW
			DIMENSSION B(2)
			B(1) IS THE LOWER SCALE LIMIT
			B(2) IS THE UPPER SCALE LIMIT
			Y IS THE VALUE AT WHICH THE LINE IS THE BE DRAWN
			DIMENSION LIMITX(2)
			LIMITX(1) IS THE LOWER INTEGER X LIMIT USED IN THE
				PLOT
			LIMITX(2) IS THE UPPER INTEGER X LIMIT USED IN THE
				PLOT
			DIMENSION LL(2)
			LL(1) IS THE LOWER POSITION NUMBER TO START LINE AT
			LL(2) IS THE UPPER POSITION NUMBER TO STOP LINE AT


	LINEY
	THE SUBROUTINE LINEY WILL DRAW A VERTICAL LINE IN THE GIVEN
REGION SCALED TO THE RIGHT HEIGHT BETWEEN TWO GIVEN Y VALUES.
 
	FORM:		CALL LINEY(LIN,NUM,I,B,IPOS,LIMITX,YL)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			NUM IS THE NUMBER OF REGIONS BEING USED FOR
				THIS PLOT
			I IS THE REGION NUMBER BEING USED ON THIS CALL
			DIMENSION B(2)
			B(1) IS THE LOWER SCALE LIMIT
			B(2) IS THE UPPER SCALE LIMIT
			IPOS IS THE ARRAY ELEMENT AT WHICH THE LINE IS
				TO BE DRAWN
			DIMENSION LIMITX(2)
			LIMITX(1) IS THE LOWER INTEGER X LIMIT USED IN
				THE PLOT
			LIMITX(2) IS THE UPPER INTEGER X LIMIT USED IN
				THE PLOT
			DIMENSION YL(2)
			YL(1) IS THE LOWER Y VALUE TO START LINE AT
			YL(2) IS THE UPPER Y VALUE TO STOP AT


	LOAD
	THE SUBROUTINE LOAD WILL LOAD AN ARRAY WITH NUMBERS READ
IN FROM A DATA FILE.
 
	FORM:		CALL LOAD(ARRAY,ISIZE,FILE,ISTART,ILUN,ISTAT)
 
	WHERE:		DIMENSION ARRAY(ISIZE)
			BYTE FILE
			DIMENSION FILE(80)
			ISTART IS THE PLACE IN THE DATA FILE FOR ARRAY(1)
			ILUN IS THE LOGICAL UNIT NUMBER
			ISTAT IS THE STATUS WORD
			ISTAT=1	SUCCESSFUL
			ISTAT=0	ERROR IN READ
			ISTAT=I	EOF BEFORE ISTART AT ELEMENT I
			ISTAT=-I	EOF BEFORE ARRAY FILLED AT ELEMENT I
 
	THE DATA FILE WILL BE READ USING A F20.10 FORMAT.  FILE IS
A READONLY FILE.


	LOADC
	THE SUBROUTINE LOADC WILL LOAD A COMPLEX ARRAY WITH NUMBERS
READ IN FROM A GIVEN DATA FILE.
 
	FORM:		CALL LOADC(CRRAY,ISIZE,FILE,ISTART,ILUN,ISTAT)
 
	WHERE:		COMPLEX CRRAY
			DIMENSION CRRAY(ISIZE)
			BYTE FILE
			DIMENSION FILE(80)
			ISTART IS THE PLACE IN THE DATA FILE FOR CRRAY(1)
			ILUN IS THE LOGICAL UNIT NUMBER TO USE
			ISTAT IS THE STATUS WORD
			ISTAT=1 SUCCESSFUL
			ISTAT=0	ERROR IN READ
			ISTAT=I EOF BEFORE ISTART AT ELEMENT I
			ISTAT=-1 EOF BEFORE CRRAY FILLED AT ELEMENT I
 
	THE DATA FILE WILL BE READ USING A * FORMAT.  FILE IS TREATED
AS A READONLY FILE.


	LOADI
	THE SUBROUTINE LOADI WILL LOAD AN IRRAY WITH NUMBERS READ
IN FROM A DATA FILE.
 
	FORM:		CALL LOADI(IRRAY,ISIZE,FILE,ISTART,ILUN,ISTAT)
 
	WHERE:		DIMENSION IRRAY(ISIZE)
			BYTE FILE
			DIMENSION FILE(80)
			ISTART IS THE PLACE IN THE DATA FILE FOR IRRAY(1)
			ILUN IS THE LOGICAL UNIT NUMBER
			ISTAT IS THE STATUS WORD
			ISTAT=1	SUCCESSFUL
			ISTAT=0	ERROR IN READ
			ISTAT=I	EOF BEFORE ISTART AT ELEMENT I
			ISTAT=-I	EOF BEFORE ARRAY FILLED AT ELEMENT I
 
	THE DATA FILE WILL BE READ USING A F20.10 FORMAT.  FILE IS
A READONLY FILE.


	OFF
	THE SUBROUTINE OFF WILL TURN THE PLOTTER OFF AT THE CONCLUSION
OF THE PROGRAM.
 
	FORM:		CALL OFF


	ON
	THE SUBROUTINE ON WILL TURN THE PLOTTER ON AND WILL CONNECT
IT WITH A SPECIFIC LUN.
 
	FORM:		CALL ON(ILUN)
 
	WHERE:		ILUN IS THE LOGICAL UNIT NUMBER


	PLOTFL
	THE SUBROUTINE PLOTFL WILL PLOT AN ARRAY OF FLOATING POINT
NUMBERS ON THE PLOTTER ON THE PLOT AT A SPECIFIC LOCATION.
 
	FORM:		CALL PLOTFL(I,NUM,B,ARRAY,ISIZE,LIM,LIMITX)
 
	WHERE:		I IS THE REGION NUMBER ON THE PLOT COUNTING DOWN.
			NUM IS THE TOTAL NUMBER OF REGIONS.
			DIMENSSION B(2)
			B(1) IS THE LOWER SCALE LIMIT
			B(2) IS THE UPPER SCALE LIMIT.
			DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			DIMENSION LIMITX(2)
			LIMITX(1) IS THE LOWER INTEGER LIMIT TO USE IN PLOT
			LIMITX(2) IS THE UPPER INTEGER LIMIT TO USE IN PLOT
 
	THE VALUE IN ARRAY WILL BE CONNECTED IN A PLOT THAT IS SCALED
SO THAT THE TOP OF THE PLOTTING REGION CORRESPONDS TO B(2) AND THE 
BOTTOM  TO B(1).  THE LOWER X LIMIT WILL BE LIMITX(1) AND THE UPPER X LIMIT
WILL BE LIMITX(2) AND THE POINTS WILL BE PLACED IN ASCENDING ORDER
AS INTEGERS.


	PLOTIN
	THE SUBROUTINE PLOTIN WILL PLOT AN IRRAY OF INTEGER
NUMBERS ON THE PLOTTER ON THE PLOT AT A SPECIFIC LOCATION.
 
	FORM:		CALL PLOTIN(I,NUM,K,IRRAY,ISIZE,LIM,LIMITX)
 
	WHERE:		I IS THE REGION NUMBER ON THE PLOT COUNTING DOWN.
			NUM IS THE TOTAL NUMBER OF REGIONS.
			DIMENSION K(2)
			K(1) IS THE LOWER SCALE LIMIT
			K(2) IS THE UPPER SCALE LIMIT.
			DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			DIMENSION LIMITX(2)
			LIMITX(1) IS THE LOWER INTEGER LIMIT TO USE IN PLOT
			LIMITX(2) IS THE UPPER INTEGER LIMIT TO USE IN PLOT
 
	THE VALUE IN IRRAY WILL BE CONNECTED IN A PLOT THAT IS SCALED
SO THAT THE TOP OF THE PLOTTING REGION CORRESPONDS TO K(2) AND THE 
BOTTOM  TO K(1).  THE LOWER X LIMIT WILL BE LIMITX(1) AND THE UPPER X LIMIT
WILL BE LIMITX(2) AND THE POINTS WILL BE PLACED IN ASCENDING ORDER
AS INTEGERS.


	SIDE
	THE SUBROUTINE SIDE WILL WRITE A LITTLE LABEL ON THE PLOT TO
DESCRIBE THEM.
 
	FORM:		CALL SIDE(LIM,LABEL,ISIZE,NUM,I)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			BYTE LABEL
			DIMENSION LABEL(ISIZE)
			NUM IS THE NUMBER OF REGIONS TO BE PLOTTED.
			I IS THE REGION NUMBER COUNTING DOWN.
 
	THE LABEL WILL BE WRITTEN AT A 90 DEG ANGLE AND WILL
BE AUTO SCALED TO FIT THE SPACE GIVEN IF THE DEFAULT SIZE WON'T WORK.
THE LABEL WILL BE CENTERED IF THE DEFAULT WILL WORK.  THE LABEL
IS ADJUSTED NOT TO RUN INTO THE DEFAULT NUMBERS FROM LABELY.


	TOP
	THE SUBROUTINE TOP WILL ENABLE THE USER TO PRINT A STRING
ON THE TOP OF THE PLOT.
 
	FORM:		CALL TOP(LIM,ARRAY,ISIZE)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			BYTE ARRAY
			DIMENSION ARRAY(ISIZE)
 
	A STRING ARRAY IS WRITTEN ON THE TOP OF THE PLOT.
THERE ARE ISIZE CHARACTERS.  THE SIZE OF THE CHARACTERS IS 36
WIDE BY 60 TALL WHERE THE DEFAULT SIZE IS
56 BY 88.  IF THERE ARE TOO MANY CHARACTERS THEN AUTO SCALING 
WILL COME IN TO EFFECT MAKING THE LETTERS SMALLER UNTIL THEY FIT.


	WHERXY
	THE SUBROUTINE WHERXY WILL RETURN TO THE CALLING PROGRAM
THE X AND Y POSITIONS OF THE PEN (SCALED TO THE APPROPRIATE VALUES)
WHEN THE PLOTTER CALL BUTTON IS PUSHED.
 
	FORM:		CALL WHERXY(LIM,NUM,I,B,LIMITX,IXX,Y)
 
	WHERE:		DIMENSION LIIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			NUM IS THE TOTAL NUMBER OF PLOTTING REGIONS
			I IS THE REGION NUMBER OF THE PLOT COUNTING DOWN
			DIMENSION B(2)
			B(1) IS THE LOWER SCALE LIMIT
			B(2) IS THE UPPER SCALE LIMIT
			DIMENSION LIMITX(2)
			LIMITX(1) IS THE LOWER INTEGER LIMIT USED IN THE PLOT
			LIMITX(2) IS THE UPPER INTEGER LIMIT USED IN THE PLOT
			IXX IS THE ARRAY ELEMENT POSITION OF THE PEN WHEN 
				CALL WAS PRESSED
			Y IS THE Y VALUE SCALED TO THE LIMITS OF THE PLOT
				WHEN CALL WAS PRESSED
 
	THIS SUBROUTINE WILL PICK OUT AN ARRAY ELEMENT AND THE Y
VALUE THAT CORRESPONDS TO THE POSITION OF THE PEN WHEN THE PLOTTER
CALL BUTTON IS PRESSED.  IT CAN THEREFORE BE USED TO FIND AN ARRAY
ELEMENT OR THE Y VALUE IN A CERTAIN PLOT.


	ZTICK
	THE SUBROUTINE ZTICK WILL MARK ON THE PLOTS
A TICK MARK TO SHOW THE ZERO VALUE FOR PERSPECTIVE.
 
	FORM:		CALL ZTICK(LIM,NUM,I,B)
 
	WHERE:		DIMENSION LIM(4)
			LIM(1) IS THE RIGHT SIDE COOR.
			LIM(2) IS THE LEFT SIDE COOR.
			LIM(3) IS THE TOP COOR.
			LIM(4) IS THE BOTTOM COOR.
			NUM IS THE TOTAL NUMBER OF PLOTTING REGIONS
			I IS THE REGION USED ON THE PLOT COUNTING DOWN
			DIMENSION B(2)
			B(1) IS THE LOWER SCALE LIMIT
			B(2) IS THE UPPER SCALE LIMIT
 
	IF THE TOP AND BOTTOM VALUES OF THE PLOT ARE NOT BOTH
POSITIVE OR NEGATIVE A TICK MARK WILL MADE ON THE LEFT AND
RIGHT SIDE OF THE REGION SPECIFIED TO MARK THE ZERO POINT.