SESSION NOTES FOR RX016  ALTERNATE CLI'S UNDER RSX



	.TITLE lgocli - CLI THAT IMPLEMENTS rmd, who ... from logged out ttys
	.IDENT	/1.00/
	.enable	lc
;	author:		Edward Cetron
;			Center for Biomedical Design
;			Univ. of Utah
;			801-581-5304
;
;	creation date:	Sept. 1, 1982
;
; THIS TASK (TMCLI) ILLUSTRATES THE USE OF THE CLI CONTROL DIRECTIVES PRESENT 
; IN RSX-11M V4.0 AND RSX-11M-PLUS V2.0. 
;
; WHEN SET UP AS A TERMINAL'S CLI, IT PROVIDES THE FOLLOWING COMMANDS:
;
;	who	-> who
;	rmd	-> rmd
;	hel	-> hel
;	help	-> help
;
; Logged out users will see only the above commands. IF THE "DPR" SWITCH
; IS INCLUDED ON THE CLI /INIT COMMAND, USERS WILL KNOW IMMEDIATELY IF
; THEIR TERMINAL IS SET TO THIS CLI BY THE PRESENCE OF THE DOUBLE RIGHT
; ANGLE BRACKET AS THE PROMPT.
;
; IF IT IS INITIALIZED WITH THE SYSTEM MESSAGE OPTION ENABLED, IT WILL
; GREET USERS WHEN THEIR TERMINAL IS SET TO THE CLI, AND SAY GOODBYE
; TO THEM WHEN THEY SWITCH AWAY.
;
; IN ORDER TO BRING THIS CLI UP ON THE SYSTEM, ISSUE THE FOLLOWING
; COMMAND SEQUENCE:
;
; >MAC lgocli,lgocli/-SP=lgocli
; >TKB lgocli,lgocli/-SP=lgocli,[1,1]EXELIB/LB
; >INS lgocli/CLI=YES/TASK=...lgo
; >CLI /INIT=lgocli/MESSAGE/DPR="<15><12>/>>/"/TASK=...lgo
;
;	TO SET TERMINALS TO THIS CLI, ISSUE THE FOLLOWING COMMAND
;	WHERE TTN: IS REPLACED BY THE TERMINAL NUMBER OR TI:
;
; >SET /CLI=TTN:lgocli
;
; NOTE THAT THE PROMPT ISSUED IN RESPONSE TO A CONTROL/C DEFAULTS TO THE
; NAME OF THE CLI WHICH IS "lgocli>". 
;
; IT CAN BE ELIMINATED FROM THE SYSTEM BY THE FOLLOWING COMMANDS, ASSUMING
; NO TERMINALS ARE SET TO IT:
;
; >CLI /ELIM=lgocli
; >REM ...lgo
;





; EXPERIMENT WITH THE OTHER OPTIONS ON THE CLI /INIT COMMAND, THE ENABLE
; AND DISABLE CLI COMMANDS, AND LEAVING OFF THE /MESSAGE SWITCH ON THE /INIT
; COMMAND TO OBSERVE THE EFFECT THEY HAVE. ALSO TRY CHANGING THE /TASK=
; SWITCH ON THE INS AND CLI /INIT COMMAND TO "/TASK=lgocli" AND NOTICE
; THAT ONLY ONE COPY OF THE TASK WILL EXIST FOR ALL TERMINALS, RATHER THAN
; ONE PER COMMAND. IF THIS IS DONE, YOU SHOULD ALSO CHANGE THE OPTION
; ON THE GCCI$ DIRECTIVE FROM GC.CEX TO GC.CST SO THE TASK WILL STAY ACTIVE
; BUT STOPPED WHEN NO COMMANDS ARE OUTSTANDING FOR IT.
;
 
	.MCALL	GCCI$,RPOI$,EXIT$S,QIOW$,ALUN$,DIR$
;
; DIRECTIVE DPBS
;
GCCI:	GCCI$	CMDBUF,CBLEN,IBUF,IBLEN,0,GC.CEX
RPOI:	RPOI$	MCR...
QIOW:	QIOW$	IO.WVB,5,1,,,,<,,40>
ALUN:	ALUN$	5
 
;
; BUFFER AREAS
;
CMDBUF:	.BLKB	80.+G.CCBF	;LENGTH = HEADER PLUS COMMAND IN BYTES
				;NOTE THAT ON M-PLUS THE MAXIMUM COMMAND
				;LENGTH IS 255. BYTES, SO THE LENGTH SHOULD
				;BE <255.+G.CCBF> OR CHARACTERS MAY BE LOST.
 
CBLEN=.-CMDBUF			;CALCULATE LENGTH
	.EVEN
 
IBUF:	.BLKB	G.CCCA+2	;LONG ENOUGH TO CONTAIN ALL INFORMATION
IBLEN=.-IBUF			;CALCULATE LENGTH
	.EVEN
 
wnam:	.rad50	/...who/
wcmd:	.ascii	/who/		; who command
wlen=.-wcmd			; who command length
	.even

rnam:	.rad50	/...rmd/
rcmd:	.ascii	/rmd/		; rmd command
rlen=.-rcmd			; length of rmd command
	.even


hlbuf:	.blkb	80.		; buffer to generate commands in
	.even

hlpcmd:	.ascii	/help/		; basic part of hel...  command
hlplen=.-hlpcmd			; length of hel... command
hlpbuf:	.blkb	80.-hlplen	; buffer to generate commands in
	.even






;
; TEXT TO BE DISPLAYED UPON RECEIPT OF NEW TERMINAL LINKED OR
; TERMINAL REMOVED MESSAGES FROM SYSTEM.
;
LKT:	.ASCII	<15><12>/WELCOME TO THE LOGGED OUT TERMINAL CLI/<15><12>
LKTLEN=.-LKT
	.EVEN
 
RMT:	.ASCII	<15><12>/GOOD BYE FROM THE LOGGED OUT TERMINAL CLI/<15><12>
RMTLEN=.-RMT
	.EVEN
 
;
; CHARACTERS LOST DUE TO BUFFER BEING TO SMALL MESSAGE
;
CHLOST:	.ASCII	<15><12>/LGOCLI - SORRY, PART OF YOUR COMMAND WAS LOST/<15><12>
CLLEN=.-CHLOST
 
;
; ILLEGAL COMMAND MESSAGE
;
ILL:	.ASCII	<15><12>/LGOCLI - ILLEGAL COMMAND/<15><12>
ILLLEN=.-ILL
	.EVEN
 
;
; CLI CODE
;
 
	.ENABL	LSB
START:	DIR$	#GCCI		;GET A COMMAND FROM SYSTEM
	bcc	ok		; if cc, ok
	jmp	100$		;IF CS, DIRECTIVE ERROR
;
; IF THE GCCI$ DIRECTIVE HAD THE GC.CST OPTION SPECIFIED, WE MAY HAVE
; JUST BEEN UNSTOPPED, SO WE HAVE TO GET THE COMMAND.
;
ok:	CMP	#IS.CLR,$DSW	;WERE WE JUST UNSTOPPED?
	BEQ	START		;IF EQ YES
	MOV	#CMDBUF,R0	;POINT TO COMMAND BUFFER
	TST	(R0)		;IS THIS A SYSTEM MESSAGE?
	bne	nomsg		; no, it is not
	jmp	MSG		;IF EQ YES
;	BPT
nomsg:	CMPB	G.CCCT(R0),G.CCCL(R0) ;DID ENTIRE COMMAND FIT IN BUFFER
	beq	hioreq
	bhi	hioreq		; if hi yes
	jmp	150$		;IF LO NO
hioreq:	MOV	#RPOI,R5	;POINT TO DPB OF RPOI$ DIRECTIVE





;
; AT THIS POINT, THE CLI HAS A COMMAND TO BE PROCESSED. THE CODE FROM
; THE "START:" LABEL TO HERE SHOULD BE FAIRLY COMMON AMONG ALL CLIS.
; FROM THIS POINT ON, THE CODE WILL BE SPECIFIC TO THE PARTICULAR LANGUAGE
; THIS CLI IS IMPLEMENTING. COMMANDS CAN BE ADDED OR DELETED AT WILL
; BY MODIFYING CODE IN THIS SECTION. AS STATED ABOVE, THIS EXTREMELY
; SIMPLE CLI PROVIDES TWO COMMANDS, AND GIVES EVERYTHING ELSE TO MCR.
; THIS CREATES AN OPEN ENDED ENVIRONMENT. REJECTING UNRECOGNIZED COMMANDS
; INSTEAD OF PASSING THEM TO MCR WOULD LIMIT THE TERMINAL USER'S USE OF
; THE SYSTEM TO ONLY THOSE OPERATIONS ALLOWED BY THE CLI. THIS IS
; A SECURE WAY OF CONTROLLING SYSTEM USE, IN CASES WHEN IT IS NECESSARY.
; IN THIS EXAMPLE, CHANGING THE "BNE 50$" BELOW, TO A "BNE 60$"
; WOULD CREATE AN ENVIRONMENT WHERE THE ONLY OPERATION A USER COULD
; PERFORM WOULD BE TO TYPE FILES ON THE TERMINAL, OR SWITCH BACK TO MCR.
; ALL OF THE REST OF RSX IS TOTALLY INACCESSABLE. IF NO MEANS OF SWITCHING
; BACK TO MCR IS PROVIDED, IT WOULD BE IMPOSSIBLE FOR THE USER TO DO
; ANYTHING THE CLI DOES NOT EXPLICITLY LET HIM DO.
;
 
	cmp	#"wh,g.ccbf(r0)	; is it a who command?
	beq	10$		;  yes...
	cmp	#"WH,g.ccbf(r0)	; is it a WHO command?
	beq	10$		;  yes...
	cmp	#"rm,g.ccbf(r0)	; is it a rmd command?
	beq	20$		;  yes...
	cmp	#"RM,g.ccbf(r0)	; is it a RMD command?
	beq	20$		;  yes...
2$:	cmp	#"he,g.ccbf(r0)	; is it a he command?
	bne	3$		;  no...
	cmp	#"lp,g.ccbf+2(r0)	; is it help?
	beq	40$		;  yes
	cmpb	#'l,g.ccbf+2(r0);  no, so is it hel?
	beq	50$		;  yes...
3$:	cmp	#"HE,g.ccbf(r0)	; is it a HE command?
	bne	4$
	cmp	#"LP,g.ccbf+2(r0)	; is it HELP?
	beq	40$		;  yes, help.....
	cmpb	#'L,g.ccbf+2(r0);  no, so is it HEL?
	beq	50$		;  yes
4$:	BNE	60$		;IF NE NO command


10$:	mov	wnam,r.potk(r5)		; get word 1 of task name
	mov	wnam+2,r.potk+2(r5)	; get word 2 of task name
	mov	#wcmd,r.pobf(r5)	; put address of who command in dpb
	mov	#wlen,r.pobl(r5)	; put length of command in dpb
	br	isscmd			; issue command

20$:	mov	rnam,r.potk(r5)		; get word 1 of task name
	mov	rnam+2,r.potk+2(r5)	; get word 2 of task name
	mov	#rcmd,r.pobf(r5)	; put address of rmd command in dpb
	mov	#rlen,r.pobl(r5)	; put length of command in dpb
	br	isscmd			; issue command






40$:	MOV	R0,R1		;COPY ADDRESS OF BUFFER WITH COMMAND
	ADD	#G.CCBF+4,R1	;POINT TO SPACE AFTER THE help
	MOV	#hlpBUF,R2	;POINT TO BUFFER THAT WILL CONTAIN CMD
	MOV	#hlpLEN,R4	;GET LENGTH OF INITIAL PART OF COMMAND
42$:	MOVB	(R1)+,R3	;GET NEXT CHARACTER
	CMPB	#15,R3		;IS IT THE END OF THE COMMAND
	BEQ	44$		;IF EQ YES
	MOVB	R3,(R2)+	;PUT CHARACTER IN OUTPUT BUFFER
	INC	R4		;COUNT CHARACTER
	BR	42$		;GET NEXT CHARACTER
44$:	MOV	#hlpCMD,R.POBF(R5);PUT ADDRESS OF CMD TO ISSUE IN DPB
	MOV	R4,R.POBL(R5)	;INSERT LENGTH OF COMMAND
	br	isscmd
 
50$:	MOV	R0,R1		;COPY ADDRESS OF BUFFER WITH COMMAND
	ADD	#G.CCBF,R1	;POINT TO ENTIRE HEL??? COMMAND
	MOV	#hlBUF,R2	;POINT TO BUFFER THAT WILL CONTAIN CMD
	MOV	#0,R4		;SET LENGTH OF INITIAL PART OF COMMAND
52$:	MOVB	(R1)+,R3	;GET NEXT CHARACTER
	CMPB	#15,R3		;IS IT THE END OF THE COMMAND
	BEQ	54$		;IF EQ YES
	MOVB	R3,(R2)+	;PUT CHARACTER IN OUTPUT BUFFER
	INC	R4		;COUNT CHARACTER
	BR	52$		;GET NEXT CHARACTER
54$:	MOV	#hlbuf,R.POBF(R5);PUT ADDRESS OF CMD TO ISSUE IN DPB
	MOV	R4,R.POBL(R5)	;INSERT LENGTH OF COMMAND
 
;
; ISSUE RPOI$ DIRECTIVE TO EXECUTE COMMAND
;
ISSCMD:	MOV	(R0),R.PODV(R5)	;PUT NAME OF ISSUING DEVICE IN RPOI
	MOVB	G.CCUN(R0),R.POUN(R5) ;COPY UNIT NUMBER
	MOVB	IBUF+G.CCPU,R.POUM(R5)	;PROPOGATE UIC OF TERMINAL
	MOVB	IBUF+G.CCPU+1,R.POUG(R5)
	MOV	IBUF+G.CCOA,R.POOA(R5)	;COPY ID PARENT IN CASE WE WERE SPAWNED
	DIR$	#RPOI		;PASS COMMAND TO EXECUTOR TASK
	bcs	110$		; error
;	mov	r.pobf(r5),r1	;
;	mov	r.pobl(r5),r2
;	call	issmsg
	jmp	START		;IF CC, SUCCESS
 
;
; CONTROL IS TRANSFERED HERE IF UNKNOWN COMMANDS ARE TO BE REJECTED
; INSTEAD OF BEING PASSED TO MCR.
;
60$:	MOV	#ILL,R1		;POINT TO MESSAGE TO BE PRINTED
	MOV	#ILLLEN,R2	;GET LENGTH OF MESSAGE
	CALL	ISSMSG		;ISSUE MESSAGE
	jmp	START		;TRY FOR NEXT COMMAND
 





;
; ERROR HANDLING CODE
;
 
100$:	CLR	R0		;FATAL ERROR ON GCCI$
	BR	150$
110$:	MOV	#1,R0		;FATAL ERROR ON RPOI$
	mov	$dsw,r1
120$:	IOT			;FATAL
 
150$:	MOV	#CHLOST,R1	;POINT TO MESSAGE TO BE PRINTED
	MOV	#CLLEN,R2	;GET LENGTH OF MESSAGE
	CALL	ISSMSG		;ISSUE MESSAGE
	jmp	START
	.DSABL	LSB
 
;
; A SYSTEM MESSAGE WAS RECEIVED INSTEAD OF A COMMAND
;
 
MSG:	CMPB	#CM.LKT,G.CCUN(R0) ;IS IT A NEW TERMINAL LINKED TO US?
	BEQ	10$		;IF EQ YES
	CMPB	#CM.RMT,G.CCUN(R0) ;IS IT A TERMINAL BEING REMOVED
	BEQ	20$		;IF EQ YES
	CMPB	#CM.EXT,G.CCUN(R0) ;IS IT A ELIMINATE ALL PACKET
	BEQ	50$		;IF EQ YES
	CMPB	#CM.ELM,G.CCUN(R0) ;IS IT A CLI ELIMINATION MESSAGE
	BEQ	50$		;IF EQ YES
	jmp	START		;IGNORE ALL OTHER MESSAGES
;
; ISSUE WELCOME MESSAGE
;
10$:	MOV	#LKT,R1		;POINT TO MESSAGE TEXT
	MOV	#LKTLEN,R2	;GET LENGTH
	ADD	#G.CCBF,R0	;POINT TO TERMINAL THAT WAS SET
	BR	30$		;
 
;
; ISSUE GOOD BYE MESSAGE
;
20$:	MOV	#RMT,R1		;POINT TO MESSAGE TEXT
	MOV	#RMTLEN,R2	;GET LENGTH
	ADD	#G.CCBF,R0	;POINT TO TERMINAL NAME
30$:	CALL	ISSMSG		;ISSUE MESSAGE
	JMP	START		;GET NEXT COMMAND
;
; WHEN AN ELIMINATE ALL MESSAGE IS RECEIVED, EXIT IMMEDIATELY
;
50$:	EXIT$S
 





;
; ROUTINE TO PRINT TO TERMINAL
;
;
; INPUTS:
;
;	R0=ADDRESS OF NAME OF TERMINAL TO PRINT TO
;	R1=ADDRESS OF MESSAGE TO PRINT
;	R2=LENGTH OF MESSAGE
;
; OUTPUTS:
;
;	NONE
;
; THIS ROUTINE PRINTS THE SPECIFIED MESSAGE ON THE SPECIFIED TERMINAL.
; ALL ERRORS THAT MIGHT RESULT ARE IGNORED. IN GENERAL, CLIS SHOULD
; DO ASYNCHRONOUS I/O WITH COMPLETION AST'S, AND PROVIDE A TIMEOUT
; FACILITY TO KILL THE I/O IF IT HASN'T COMPLETED IN A CERTAIN
; AMOUNT OF TIME IN ORDER TO PREVENT TERMINAL I/O FROM HOLDING UP
; COMMAND PROCESSING. THIS IS NOT DONE HERE FOR SIMPLICITY.
;
 
ISSMSG:	MOV	(R0),ALUN+A.LUNA  ;SET UP DEVICE NAME
	MOVB	2(R0),ALUN+A.LUNU ;AND UNIT NUMBER
	CLRB	ALUN+A.LUNU+1	;CLEAR HIGH BYTE
	DIR$	#ALUN		;ASSIGN LUN 5 TO THE SPECIFIED DEVICE
	BCS	10$		;IF CS, SKIP I/O
	MOV	R1,QIOW+Q.IOPL	;SET ADDRESS OF MESSAGE
	MOV	R2,QIOW+Q.IOPL+2 ;INSERT LENGTH OF MESSAGE
	DIR$	#QIOW		;DO I/O AND WAIT FOR IT
10$:	RETURN
 
	.END	START
-------------------------
		command file to build lgocli

.xqt mac lgocli,lgocli=lgocli
set /cli=tt0:mcr
set /mcr=tt1:
set /mcr=tt2:
set /mcr=tt3:
set /mcr=tt4:
set /mcr=tt5:
set /mcr=tt6:
set /mcr=tt7:
set /mcr=tt10:
cli /elim=lgocli
rem ...lgo
.wait ...mac
tkb lgocli,lgocli=lgocli,lb:[1,1]exelib/lb,lb:[1,54]rsx11m.stb/ss
pur lgocli.*
ins lgocli/cli=yes/task=...lgo
cli /init=lgocli/lgo/task=...lgo/dpr="<15><12>/>>/"
-------------------------
-------------------------





	.TITLE rtcli - CLI THAT IMPLEMENTS rmd, who, run, abo, mcr, dcl
	.IDENT	/1.00/
	.enable	lc
;	author:		Edward Cetron
;			Center for Biomedical Design
;			Univ. of Utah
;			801-581-5304
;
;	creation date:	June 18, 1983
;
; WHEN SET UP AS A TERMINAL'S CLI, IT PROVIDES THE FOLLOWING COMMANDS:
;
;	who	-> who
;	rmd	-> rmd
;	run	-> run
;	abo	-> abo
;	mcr	-> switch back to mcr
;	dcl	-> switch back to dcl
;
; IF THE "DPR" SWITCH
; IS INCLUDED ON THE CLI /INIT COMMAND, USERS WILL KNOW IMMEDIATELY IF
; THEIR TERMINAL IS SET TO THIS CLI BY THE PRESENCE OF THE ? CHARACTER
; AS THE PROMPT.
;
; IF IT IS INITIALIZED WITH THE SYSTEM MESSAGE OPTION ENABLED, IT WILL
; GREET USERS WHEN THEIR TERMINAL IS SET TO THE CLI, AND SAY GOODBYE
; TO THEM WHEN THEY SWITCH AWAY.
;
; IN ORDER TO BRING THIS CLI UP ON THE SYSTEM, ISSUE THE FOLLOWING
; COMMAND SEQUENCE:
;
; >MAC rtcli,rtcli/-SP=rtcli
; >TKB rtcli,rtcli/-SP=rtcli,[1,1]EXELIB/LB
; >INS rtcli/CLI=YES/TASK=...rtm
; >CLI /INIT=rtcli/MESSAGE/DPR="<15><12>/?/"/CPR="<15><12>/rtmcli>/"/TASK=...rtm
;
;	TO SET TERMINALS TO THIS CLI, ISSUE THE FOLLOWING COMMAND
;	WHERE TTN: IS REPLACED BY THE TERMINAL NUMBER OR TI:
;
; >SET /CLI=TTN:rtcli
;
; NOTE THAT THE PROMPT ISSUED IN RESPONSE TO A CONTROL/C DEFAULTS TO THE
; NAME OF THE CLI WHICH IS "rtmcli>". 
;
; IT CAN BE ELIMINATED FROM THE SYSTEM BY THE FOLLOWING COMMANDS, ASSUMING
; NO TERMINALS ARE SET TO IT:
;
; >CLI /ELIM=rtcli
; >REM ...rtm
;





; EXPERIMENT WITH THE OTHER OPTIONS ON THE CLI /INIT COMMAND, THE ENABLE
; AND DISABLE CLI COMMANDS, AND LEAVING OFF THE /MESSAGE SWITCH ON THE /INIT
; COMMAND TO OBSERVE THE EFFECT THEY HAVE. ALSO TRY CHANGING THE /TASK=
; SWITCH ON THE INS AND CLI /INIT COMMAND TO "/TASK=rtcli" AND NOTICE
; THAT ONLY ONE COPY OF THE TASK WILL EXIST FOR ALL TERMINALS, RATHER THAN
; ONE PER COMMAND. IF THIS IS DONE, YOU SHOULD ALSO CHANGE THE OPTION
; ON THE GCCI$ DIRECTIVE FROM GC.CEX TO GC.CST SO THE TASK WILL STAY ACTIVE
; BUT STOPPED WHEN NO COMMANDS ARE OUTSTANDING FOR IT.
;
 
	.mcall	dcbdf$		; Device control block offsets
	.mcall	hwddf$		; Hardware registers
	.mcall	tcbdf$		; Terminal control block offsets
	.mcall	ucbdf$		; Unit control block offsets

	dcbdf$
	hwddf$
	tcbdf$
	ucbdf$
;
;
;	Directive macros from LB:[1,1]SYSLIB.OLB
;
	.mcall	alun$		; assign logical unit number
	.mcall	dir$		; execute directive
	.mcall	mrkt$		; mark time (wait)
	.mcall	qiow$		; queue i/o and wait
	.mcall	spwn$		; spawn task
	.mcall	stse$s		; stop for single event flag
	.mcall	gcci$		; get command interpreter information
	.mcall	rpoi$		; request and pass offspring information
	.mcall	exit$s
;
; DIRECTIVE DPBS
;
GCCI:	GCCI$	CMDBUF,CBLEN,IBUF,IBLEN,0,GC.CEX
RPOI:	RPOI$	MCR...
QIOW:	QIOW$	IO.WVB,5,1,,,,<,,40>
ALUN:	ALUN$	5
mcrspn:	spwn$	MCR...,,,,,3,,,runbuf,runlen
 
;
; BUFFER AREAS
;
CMDBUF:	.BLKB	80.+G.CCBF	;LENGTH = HEADER PLUS COMMAND IN BYTES
				;NOTE THAT ON M-PLUS THE MAXIMUM COMMAND
				;LENGTH IS 255. BYTES, SO THE LENGTH SHOULD
				;BE <255.+G.CCBF> OR CHARACTERS MAY BE LOST.
 





CBLEN=.-CMDBUF			;CALCULATE LENGTH
	.EVEN
 
IBUF:	.BLKB	G.CCCA+2	;LONG ENOUGH TO CONTAIN ALL INFORMATION
IBLEN=.-IBUF			;CALCULATE LENGTH
	.EVEN
 
wnam:	.rad50	/...who/
wcmd:	.ascii	/who/		; who command
wlen=.-wcmd			; who command length
	.even

rnam:	.rad50	/...rmd/
rcmd:	.ascii	/rmd/		; rmd command
rlen=.-rcmd			; length of rmd command
	.even


dclcmd:	.ascii	\set /dcl=ti:\
setcmd:	.ascii	\set /mcr=ti:\
setlen	=.-setcmd
	.even


abocmd:	.ascii	/abo/		; basic part of abo command
abolen=.-abocmd			; length of abo command
abobuf:	.blkb	80.-abolen	; buffer to generate commands in
	.even

runmsg:	.ascii	<15><12>/  Now starting to /
rnmsgl	= .-runmsg
runcmd:	.ascii	/run [/		; basic part of run command
rungrp:	.ascii	/000/
	.ascii	/,/
runmem:	.ascii	/000/
	.ascii	/]/
runlen=.-runcmd			; length of run command
runbuf:	.blkb	80.-runlen	; buffer to generate commands in
	.even


;
; TEXT TO BE DISPLAYED UPON RECEIPT OF NEW TERMINAL LINKED OR
; TERMINAL REMOVED MESSAGES FROM SYSTEM.
;
LKT:	.ASCII	<15><12>/Welcome to the realtime operating system./<15><12>
LKTLEN=.-LKT
	.EVEN
 
RMT:	.ASCII	<15><12>/Goodbye from the realtime operating system./<15><12>
RMTLEN=.-RMT
	.EVEN





 
;
; CHARACTERS LOST DUE TO BUFFER BEING TO SMALL MESSAGE
;
CHLOST:	.ASCII	<15><12>/RTCLI - SORRY, PART OF YOUR COMMAND WAS LOST/<15><12>
CLLEN=.-CHLOST
 
;
; ILLEGAL COMMAND MESSAGE
;
ILL:	.ASCII	<15><12>/RTCLI - ILLEGAL COMMAND/<15><12>
ILLLEN=.-ILL
	.EVEN
 
;
; CLI CODE
;
 
	.ENABL	LSB
START:	DIR$	#GCCI		;GET A COMMAND FROM SYSTEM
	bcc	ok		; if cc, ok
	jmp	100$		;IF CS, DIRECTIVE ERROR
;
; IF THE GCCI$ DIRECTIVE HAD THE GC.CST OPTION SPECIFIED, WE MAY HAVE
; JUST BEEN UNSTOPPED, SO WE HAVE TO GET THE COMMAND.
;
ok:	CMP	#IS.CLR,$DSW	;WERE WE JUST UNSTOPPED?
	BEQ	START		;IF EQ YES
	MOV	#CMDBUF,R0	;POINT TO COMMAND BUFFER
	TST	(R0)		;IS THIS A SYSTEM MESSAGE?
	bne	nomsg		; no, it is not
	jmp	MSG		;IF EQ YES
;	BPT
nomsg:	CMPB	G.CCCT(R0),G.CCCL(R0) ;DID ENTIRE COMMAND FIT IN BUFFER
	beq	hioreq
	bhi	hioreq		; if hi yes
	jmp	150$		;IF LO NO
hioreq:	MOV	#RPOI,R5	;POINT TO DPB OF RPOI$ DIRECTIVE
;
; AT THIS POINT, THE CLI HAS A COMMAND TO BE PROCESSED. THE CODE FROM
; THE "START:" LABEL TO HERE SHOULD BE FAIRLY COMMON AMONG ALL CLIS.
; FROM THIS POINT ON, THE CODE WILL BE SPECIFIC TO THE PARTICULAR LANGUAGE
; THIS CLI IS IMPLEMENTING. COMMANDS CAN BE ADDED OR DELETED AT WILL
; BY MODIFYING CODE IN THIS SECTION. AS STATED ABOVE, THIS EXTREMELY
; SIMPLE CLI PROVIDES TWO COMMANDS, AND GIVES EVERYTHING ELSE TO MCR.
; THIS CREATES AN OPEN ENDED ENVIRONMENT. REJECTING UNRECOGNIZED COMMANDS
; INSTEAD OF PASSING THEM TO MCR WOULD LIMIT THE TERMINAL USER'S USE OF
; THE SYSTEM TO ONLY THOSE OPERATIONS ALLOWED BY THE CLI. THIS IS
; A SECURE WAY OF CONTROLLING SYSTEM USE, IN CASES WHEN IT IS NECESSARY.
; IN THIS EXAMPLE, CHANGING THE "BNE 50$" BELOW, TO A "BNE 60$"





; WOULD CREATE AN ENVIRONMENT WHERE THE ONLY OPERATION A USER COULD
; PERFORM WOULD BE TO TYPE FILES ON THE TERMINAL, OR SWITCH BACK TO MCR.
; ALL OF THE REST OF RSX IS TOTALLY INACCESSABLE. IF NO MEANS OF SWITCHING
; BACK TO MCR IS PROVIDED, IT WOULD BE IMPOSSIBLE FOR THE USER TO DO
; ANYTHING THE CLI DOES NOT EXPLICITLY LET HIM DO.
;
 
	cmp	#"wh,g.ccbf(r0)	; is it a who command?
	beq	10$		;  yes...
	cmp	#"WH,g.ccbf(r0)	; is it a WHO command?
	beq	10$		;  yes...
	cmp	#"rm,g.ccbf(r0)	; is it a rmd command?
	beq	20$		;  yes...
	cmp	#"RM,g.ccbf(r0)	; is it a RMD command?
	beq	20$		;  yes...
2$:	cmp	#"ru,g.ccbf(r0)	; is it a run command?
	beq	50$		;  yes
3$:	cmp	#"RU,g.ccbf(r0)	; is it a RUN command?
	beq	50$		;  yes, help.....
	cmp	#"ab,g.ccbf(r0)	; is it an abo command?
	beq	40$
	cmp	#"AB,g.ccbf(r0)	; is it an ABO command?
	beq	40$		;  yes
	cmp	#"mc,g.ccbf(r0)	; is it an mcr command?
	beq	55$		; yes
	cmp	#"MC,g.ccbf(r0)	; is it an MCR command?
	beq	55$		; yes
	cmp	#"dc,g.ccbf(r0)	; is it an dcl command?
	beq	56$		; yes
	cmp	#"DC,g.ccbf(r0)	; is it an DCL command?
	beq	56$		; yes
4$:	jmp	60$		;IF NE NO command


10$:	mov	wnam,r.potk(r5)		; get word 1 of task name
	mov	wnam+2,r.potk+2(r5)	; get word 2 of task name
	mov	#wcmd,r.pobf(r5)	; put address of who command in dpb
	mov	#wlen,r.pobl(r5)	; put length of command in dpb
	br	isscmd			; issue command

20$:	mov	rnam,r.potk(r5)		; get word 1 of task name
	mov	rnam+2,r.potk+2(r5)	; get word 2 of task name
	mov	#rcmd,r.pobf(r5)	; put address of rmd command in dpb
	mov	#rlen,r.pobl(r5)	; put length of command in dpb
	br	isscmd			; issue command

40$:	MOV	R0,R1		;COPY ADDRESS OF BUFFER WITH COMMAND
	ADD	#G.CCBF+3,R1	;POINT TO space after 'abo '
	MOV	#aboBUF,R2	;POINT TO BUFFER THAT WILL CONTAIN CMD
	MOV	#abolen,R4		;GET LENGTH OF INITIAL PART OF COMMAND





42$:	MOVB	(R1)+,R3	;GET NEXT CHARACTER
	CMPB	#15,R3		;IS IT THE END OF THE COMMAND
	BEQ	44$		;IF EQ YES
	MOVB	R3,(R2)+	;PUT CHARACTER IN OUTPUT BUFFER
	INC	R4		;COUNT CHARACTER
	BR	42$		;GET NEXT CHARACTER
44$:	mov	#abocmd,r.pobf(r5)
	mov	#abolen,r.pobl(r5)
;	use next too if more than just 'abo ' is allowed
;	MOV	#abobuf,R.POBF(R5);PUT ADDRESS OF CMD TO ISSUE IN DPB
;	MOV	R4,R.POBL(R5)	;INSERT LENGTH OF COMMAND
	br	isscmd
 
50$:	MOV	R0,R1		;COPY ADDRESS OF BUFFER WITH COMMAND
	ADD	#G.CCBF+4,R1	;POINT TO space after 'run'
	MOV	#runBUF,R2	;POINT TO BUFFER THAT WILL CONTAIN CMD
	MOV	#0,R4		;SET LENGTH OF INITIAL PART OF COMMAND
52$:	MOVB	(R1)+,R3	;GET NEXT CHARACTER
	CMPB	#15,R3		;IS IT THE END OF THE COMMAND
	BEQ	54$		;IF EQ YES
	MOVB	R3,(R2)+	;PUT CHARACTER IN OUTPUT BUFFER
	INC	R4		;COUNT CHARACTER
	BR	52$		;GET NEXT CHARACTER
54$:	mov	r0,r3
	mov	#runmem,r0	;set uic member address
	clr	r1
	movb	ibuf+g.ccpu,r1	; get member
	mov	#7,r2		; set no zero suppression
	call	$cbtmg		; convert and place
	mov	#rungrp,r0	; set uic group address
	clr	r1
	movb	ibuf+g.ccpu+1,r1	;get group	
	mov	#7,r2
	call	$cbtmg
	mov	r3,r0
	add	#runlen,r4

	mov	#runmsg,r1
	mov	r4,r2
	add	#rnmsgl,r2
	call	issmsg

	mov	#mcrspn,r5
	MOV	#runcmd,s.pwca(R5);PUT ADDRESS OF CMD TO ISSUE IN DPB
	MOV	R4,s.pwcl(R5)	;INSERT LENGTH OF COMMAND
	MOV	$TKTCB,R1		;GET TASK CONTROL BLOCk
	MOV	T.UCB(R1),R2	;GET TI UCB ADDRESS
	BIS	#U2.PRV,U.CW2(R2) ;SET PRIVILEGED BIT
	dir$	#mcrspn		; start up desired task while privileged
;	bcs	545$
;	stse$s	#3.		; wait for spawn exit 
;545$:	MOV	$TKTCB,R1	;GET TASK CONTROL BLOCk
;	MOV	T.UCB(R1),R2	;GET TI UCB ADDRESS
;	BIC	#U2.PRV,U.CW2(R2) ;CLEAR PRIVILEGED BIT
	jmp	start





	
55$:	mov	#setcmd,r.pobf(r5)	; put address of rmd command in dpb
	br	57$
56$:	mov	#dclcmd,r.pobf(r5)	;
57$:	MOV	$TKTCB,R1	;GET TASK CONTROL BLOCK
	MOV	T.UCB(R1),R2	;GET TI UCB ADDRESS
	BIC	#U2.PRV,U.CW2(R2) ;CLEAR PRIVILEGED BIT
	mov	#setlen,r.pobl(r5)	; put length of command in dpb
	br	isscmd			; issue command
;
; ISSUE RPOI$ DIRECTIVE TO EXECUTE COMMAND
;
ISSCMD:	MOV	(R0),R.PODV(R5)	;PUT NAME OF ISSUING DEVICE IN RPOI
	MOVB	G.CCUN(R0),R.POUN(R5) ;COPY UNIT NUMBER
	MOVB	IBUF+G.CCPU,R.POUM(R5)	;PROPOGATE UIC OF TERMINAL
	MOVB	IBUF+G.CCPU+1,R.POUG(R5)
	MOV	IBUF+G.CCOA,R.POOA(R5)	;COPY ID PARENT IN CASE WE WERE SPAWNED
	DIR$	#RPOI		;PASS COMMAND TO EXECUTOR TASK
	bcs	110$		; error
;	mov	r.pobf(r5),r1	;
;	mov	r.pobl(r5),r2
;	call	issmsg
	jmp	START		;IF CC, SUCCESS
 
;
; CONTROL IS TRANSFERED HERE IF UNKNOWN COMMANDS ARE TO BE REJECTED
; INSTEAD OF BEING PASSED TO MCR.
;
60$:	MOV	#ILL,R1		;POINT TO MESSAGE TO BE PRINTED
	MOV	#ILLLEN,R2	;GET LENGTH OF MESSAGE
	CALL	ISSMSG		;ISSUE MESSAGE
	jmp	START		;TRY FOR NEXT COMMAND
 
;
; ERROR HANDLING CODE
;
 
100$:	CLR	R0		;FATAL ERROR ON GCCI$
	BR	150$
110$:	MOV	#1,R0		;FATAL ERROR ON RPOI$
	mov	$dsw,r1
120$:	IOT			;FATAL
 
150$:	MOV	#CHLOST,R1	;POINT TO MESSAGE TO BE PRINTED
	MOV	#CLLEN,R2	;GET LENGTH OF MESSAGE
	CALL	ISSMSG		;ISSUE MESSAGE
	jmp	START
	.DSABL	LSB





 
;
; A SYSTEM MESSAGE WAS RECEIVED INSTEAD OF A COMMAND
;
 
MSG:	CMPB	#CM.LKT,G.CCUN(R0) ;IS IT A NEW TERMINAL LINKED TO US?
	BEQ	10$		;IF EQ YES
	CMPB	#CM.RMT,G.CCUN(R0) ;IS IT A TERMINAL BEING REMOVED
	BEQ	20$		;IF EQ YES
	CMPB	#CM.EXT,G.CCUN(R0) ;IS IT A ELIMINATE ALL PACKET
	BEQ	50$		;IF EQ YES
	CMPB	#CM.ELM,G.CCUN(R0) ;IS IT A CLI ELIMINATION MESSAGE
	BEQ	50$		;IF EQ YES
	jmp	START		;IGNORE ALL OTHER MESSAGES
;
; ISSUE WELCOME MESSAGE
;
10$:	MOV	#LKT,R1		;POINT TO MESSAGE TEXT
	MOV	#LKTLEN,R2	;GET LENGTH
	ADD	#G.CCBF,R0	;POINT TO TERMINAL THAT WAS SET
	BR	30$		;
 
;
; ISSUE GOOD BYE MESSAGE
;
20$:	MOV	#RMT,R1		;POINT TO MESSAGE TEXT
	MOV	#RMTLEN,R2	;GET LENGTH
	ADD	#G.CCBF,R0	;POINT TO TERMINAL NAME
30$:	CALL	ISSMSG		;ISSUE MESSAGE
	JMP	START		;GET NEXT COMMAND
;
; WHEN AN ELIMINATE ALL MESSAGE IS RECEIVED, EXIT IMMEDIATELY
;
50$:	EXIT$S
 
;
; ROUTINE TO PRINT TO TERMINAL
;
;
; INPUTS:
;
;	R0=ADDRESS OF NAME OF TERMINAL TO PRINT TO
;	R1=ADDRESS OF MESSAGE TO PRINT
;	R2=LENGTH OF MESSAGE
;
; OUTPUTS:
;
;	NONE





;
; THIS ROUTINE PRINTS THE SPECIFIED MESSAGE ON THE SPECIFIED TERMINAL.
; ALL ERRORS THAT MIGHT RESULT ARE IGNORED. IN GENERAL, CLIS SHOULD
; DO ASYNCHRONOUS I/O WITH COMPLETION AST'S, AND PROVIDE A TIMEOUT
; FACILITY TO KILL THE I/O IF IT HASN'T COMPLETED IN A CERTAIN
; AMOUNT OF TIME IN ORDER TO PREVENT TERMINAL I/O FROM HOLDING UP
; COMMAND PROCESSING. THIS IS NOT DONE HERE FOR SIMPLICITY.
;
 
ISSMSG:	MOV	(R0),ALUN+A.LUNA  ;SET UP DEVICE NAME
	MOVB	2(R0),ALUN+A.LUNU ;AND UNIT NUMBER
	CLRB	ALUN+A.LUNU+1	;CLEAR HIGH BYTE
	DIR$	#ALUN		;ASSIGN LUN 5 TO THE SPECIFIED DEVICE
	BCS	10$		;IF CS, SKIP I/O
	MOV	R1,QIOW+Q.IOPL	;SET ADDRESS OF MESSAGE
	MOV	R2,QIOW+Q.IOPL+2 ;INSERT LENGTH OF MESSAGE
	DIR$	#QIOW		;DO I/O AND WAIT FOR IT
10$:	RETURN
 
	.END	START
-------------------------
		command file for rtcli

.xqt mac rtcli,rtcli=lb:[1,1]exemc/ml,lb:[11,10]rsxmc/pa:1,dl1:[2,1]rtcli
cli /elim=rtcli
rem ...rtm
.wait ...mac
tkb rtcli/pr,rtcli=rtcli,lb:[1,1]exelib/lb,lb:[1,54]rsx11m.stb/ss
pur rtcli.*
ins rtcli/cli=yes/task=...rtm
cli /init=rtcli/task=...rtm/dpr="<15><12>/?/"/cpr="<15><12>/rtcli>/"/message
-------------------------
-------------------------

	.TITLE cadcli - CLI THAT IMPLEMENTS INPUT STORAGE OR PRINTING
;			FOR COMPUTERVISION CONSOLE/PRINTER MONITORING
	.IDENT	/1.00/
	.enable	lc
;	author:		Edward Cetron
;			Center for Biomedical Design
;			Univ. of Utah
;			801-581-5304
;
;	creation date:	June 29, 1984
;
;
; IN ORDER TO BRING THIS CLI UP ON THE SYSTEM, ISSUE THE FOLLOWING
; COMMAND SEQUENCE:
;
; >MAC cadcli,cadcli/-SP=cadcli
; >TKB cadcli,cadcli/-SP=cadcli,[1,1]EXELIB/LB
; >INS cadcli/CLI=YES/TASK=...cad
; >CLI /INIT=cadcli/MESSAGE/DPR="<15><12>/>>/"/TASK=...cad





;
;	TO SET TERMINALS TO THIS CLI, ISSUE THE FOLLOWING COMMAND
;	WHERE TTN: IS REPLACED BY THE TERMINAL NUMBER OR TI:
;
; >SET /CLI=TTN:cadcli
;
; NOTE THAT THE PROMPT ISSUED IN RESPONSE TO A CONTROL/C DEFAULTS TO THE
; NAME OF THE CLI WHICH IS "cadcli>". 
;
; IT CAN BE ELIMINATED FROM THE SYSTEM BY THE FOLLOWING COMMANDS, ASSUMING
; NO TERMINALS ARE SET TO IT:
;
; >CLI /ELIM=cadcli
; >REM ...cad
;
; EXPERIMENT WITH THE OTHER OPTIONS ON THE CLI /INIT COMMAND, THE ENABLE
; AND DISABLE CLI COMMANDS, AND LEAVING OFF THE /MESSAGE SWITCH ON THE /INIT
; COMMAND TO OBSERVE THE EFFECT THEY HAVE. ALSO TRY CHANGING THE /TASK=
; SWITCH ON THE INS AND CLI /INIT COMMAND TO "/TASK=cadcli" AND NOTICE
; THAT ONLY ONE COPY OF THE TASK WILL EXIST FOR ALL TERMINALS, RATHER THAN
; ONE PER COMMAND. IF THIS IS DONE, YOU SHOULD ALSO CHANGE THE OPTION
; ON THE GCCI$ DIRECTIVE FROM GC.CEX TO GC.CST SO THE TASK WILL STAY ACTIVE
; BUT STOPPED WHEN NO COMMANDS ARE OUTSTANDING FOR IT.
;
 
	.MCALL	GCCI$,RPOI$,EXIT$S,QIOW$,ALUN$,DIR$
;
; DIRECTIVE DPBS
;
GCCI:	GCCI$	CMDBUF,CBLEN,IBUF,IBLEN,0,GC.CEX
RPOI:	RPOI$	MCR...
QIOW:	QIOW$	IO.WVB,5,1,,,,<,,40>
ALUN:	ALUN$	5
set1:	qiow$	sf.smc,5,1,,,,<onprt,2> 
set2:	qiow$	sf.smc,5,1,,,,<offprt,2>
chk1:	qiow$	sf.gmc,5,1,,,,<type,2>
;
; BUFFER AREAS
;
CMDBUF:	.BLKB	255.+G.CCBF	;LENGTH = HEADER PLUS COMMAND IN BYTES
				;NOTE THAT ON M-PLUS THE MAXIMUM COMMAND
				;LENGTH IS 255. BYTES, SO THE LENGTH SHOULD
				;BE <255.+G.CCBF> OR CHARACTERS MAY BE LOST.
 
CBLEN=.-CMDBUF			;CALCULATE LENGTH
	.EVEN
 
IBUF:	.BLKB	G.CCCA+2	;LONG ENOUGH TO CONTAIN ALL INFORMATION
IBLEN=.-IBUF			;CALCULATE LENGTH
	.EVEN





 
atnam:	.rad50	/...at./
	.even
atcmd:	.ascii	/@lb:[6,6]store /
atbuf:	.blkb	255.
	.even
;
prntr:	.ascii	/TT/
prntru:	.word	16
;
	.even

onprt:	.byte	tc.ttp
	.byte	1
offprt:	.byte	tc.ttp
	.byte	0
type:	.byte	tc.ttp
kind:	.byte	0
;
	.even
;
; CLI CODE
;
 
	.ENABL	LSB
START:	DIR$	#GCCI		;GET A COMMAND FROM SYSTEM
	bcc	ok		; if cc, ok
	jmp	100$		;IF CS, DIRECTIVE ERROR
;
; IF THE GCCI$ DIRECTIVE HAD THE GC.CST OPTION SPECIFIED, WE MAY HAVE
; JUST BEEN UNSTOPPED, SO WE HAVE TO GET THE COMMAND.
;
ok:	CMP	#IS.CLR,$DSW	;WERE WE JUST UNSTOPPED?
	BEQ	START		;IF EQ YES
	MOV	#CMDBUF,R0	;POINT TO COMMAND BUFFER
	TST	(R0)		;IS THIS A SYSTEM MESSAGE?
	bne	nomsg		; no, it is not
	jmp	start		; yes.... ignore messages....
;	BPT
nomsg:	CMPB	G.CCCT(R0),G.CCCL(R0) ;DID ENTIRE COMMAND FIT IN BUFFER
	beq	hioreq
	bhi	hioreq		; if hi yes
	jmp	150$		;IF LO NO
hioreq:	MOV	#RPOI,R5	;POINT TO DPB OF RPOI$ DIRECTIVE
;
; AT THIS POINT, THE CLI HAS A COMMAND TO BE PROCESSED. THE CODE FROM
; THE "START:" LABEL TO HERE SHOULD BE FAIRLY COMMON AMONG ALL CLIS.
; FROM THIS POINT ON, THE CODE WILL BE SPECIFIC TO THE PARTICULAR LANGUAGE
; THIS CLI IS IMPLEMENTING. COMMANDS CAN BE ADDED OR DELETED AT WILL
; BY MODIFYING CODE IN THIS SECTION. AS STATED ABOVE, THIS EXTREMELY





; SIMPLE CLI PROVIDES TWO COMMANDS, AND GIVES EVERYTHING ELSE TO MCR.
; THIS CREATES AN OPEN ENDED ENVIRONMENT. REJECTING UNRECOGNIZED COMMANDS
; INSTEAD OF PASSING THEM TO MCR WOULD LIMIT THE TERMINAL USER'S USE OF
; THE SYSTEM TO ONLY THOSE OPERATIONS ALLOWED BY THE CLI. THIS IS
; A SECURE WAY OF CONTROLLING SYSTEM USE, IN CASES WHEN IT IS NECESSARY.
; IN THIS EXAMPLE, CHANGING THE "BNE 50$" BELOW, TO A "BNE 60$"
; WOULD CREATE AN ENVIRONMENT WHERE THE ONLY OPERATION A USER COULD
; PERFORM WOULD BE TO TYPE FILES ON THE TERMINAL, OR SWITCH BACK TO MCR.
; ALL OF THE REST OF RSX IS TOTALLY INACCESSABLE. IF NO MEANS OF SWITCHING
; BACK TO MCR IS PROVIDED, IT WOULD BE IMPOSSIBLE FOR THE USER TO DO
; ANYTHING THE CLI DOES NOT EXPLICITLY LET HIM DO.
;
 
	cmp	#"#$,g.ccbf(r0)	; is it a print command?
	bne	40$		;  yes...
	cmp	#"%&,g.ccbf+2(r0)	; is it a print-on command?
	beq	10$		;  yes...
	cmp	#"%*,g.ccbf+2(r0)	; is it a print-off command?
	beq	20$
4$:	BNE	40$		;IF NE stuff it away (print or file)

;
;		print - on command
;

10$:	mov	#cmdbuf,r0
	MOV	(R0),ALUN+A.LUNA  ;SET UP DEVICE NAME
	MOV	2(R0),ALUN+A.LUNU ;AND UNIT NUMBER
	DIR$	#ALUN		;ASSIGN LUN 5 TO THE SPECIFIED DEVICE
	BCS	11$		;IF CS, SKIP I/O
	DIR$	#set1		;DO I/O AND WAIT FOR IT
11$:	jmp	start		; and go back for more
;
;	print - off command
;
20$:	mov	#cmdbuf,r0
	MOV	(R0),ALUN+A.LUNA  ;SET UP DEVICE NAME
	MOV	2(R0),ALUN+A.LUNU ;AND UNIT NUMBER
	DIR$	#ALUN		;ASSIGN LUN 5 TO THE SPECIFIED DEVICE
	BCS	21$		;IF CS, SKIP I/O
	DIR$	#set2		;DO I/O AND WAIT FOR IT
21$:	jmp	start		; and go back for more

40$:	dir$	#chk1		; file or print
	tstb	kind		; if zero, then file
	beq	42$		;    yep, file it
	mov	#prntr,r0	; no, print it
	MOV	(R0),ALUN+A.LUNA  ;SET UP DEVICE NAME
	MOV	2(R0),ALUN+A.LUNU ;AND UNIT NUMBER
	DIR$	#ALUN		;ASSIGN LUN 5 TO THE SPECIFIED DEVICE
	BCS	41$		;IF CS, SKIP I/O
	MOV	#cmdbuf+g.ccbf,QIOW+Q.IOPL	;SET ADDRESS OF MESSAGE
	MOV	cmdbuf+g.cccl,QIOW+Q.IOPL+2 ;INSERT LENGTH OF MESSAGE
	DIR$	#qiow		;DO I/O AND WAIT FOR IT
41$:	jmp	start		; and go back for more






42$:	MOV	#cmdbuf,R1		;COPY ADDRESS OF BUFFER WITH COMMAND
	ADD	#G.CCBF,R1	;POINT TO SPACE AFTER THE help
	MOV	#atbuf,R2	;POINT TO BUFFER THAT WILL CONTAIN CMD
	MOV	#15.,R4	;GET LENGTH OF INITIAL PART OF COMMAND
43$:	MOVB	(R1)+,R3	;GET NEXT CHARACTER
	CMPB	#15,R3		;IS IT THE END OF THE COMMAND
	BEQ	44$		;IF EQ YES
	MOVB	R3,(R2)+	;PUT CHARACTER IN OUTPUT BUFFER
	INC	R4		;COUNT CHARACTER
	BR	43$		;GET NEXT CHARACTER
44$:	MOV	#atcmd,R.POBF(R5);PUT ADDRESS OF CMD TO ISSUE IN DPB
	mov	atnam,r.potk(r5)		; get word 1 of task name
	mov	atnam+2,r.potk+2(r5)	; get word 2 of task name
	cmp	#70.,r4
	bgt	45$
	mov	#70.,r4
45$:	MOV	R4,R.POBL(R5)	;INSERT LENGTH OF COMMAND
	br	isscmd
 
;
; ISSUE RPOI$ DIRECTIVE TO EXECUTE COMMAND
;
ISSCMD:	mov	#cmdbuf,r0
	MOV	(R0),R.PODV(R5)	;PUT NAME OF ISSUING DEVICE IN RPOI
	MOVB	G.CCUN(R0),R.POUN(R5) ;COPY UNIT NUMBER
	MOVB	#6,R.POUM(R5)	;PROPOGATE UIC OF TERMINAL
	MOVB	#6,R.POUG(R5)
	MOV	IBUF+G.CCOA,R.POOA(R5)	;COPY ID PARENT IN CASE WE WERE SPAWNED
47$:	DIR$	#RPOI		;PASS COMMAND TO EXECUTOR TASK
	bcc	50$
	cmpb	$dsw,#-7.
	bne	110$		; error
	br	47$		; task still active, wait and try again
;	mov	r.pobf(r5),r1	;
;	mov	r.pobl(r5),r2
;	call	issmsg
50$:	jmp	START		;IF CC, SUCCESS
 
;
;
; ERROR HANDLING CODE
;
 
100$:	CLR	R0		;FATAL ERROR ON GCCI$
	BR	150$
110$:	MOV	#1,R0		;FATAL ERROR ON RPOI$
	mov	$dsw,r1
120$:	IOT			;FATAL
 
150$:	jmp	START
	.DSABL	LSB





 
;
;
; ROUTINE TO PRINT TO TERMINAL
;
;
; INPUTS:
;
;	R0=ADDRESS OF NAME OF TERMINAL TO PRINT TO
;	R1=ADDRESS OF MESSAGE TO PRINT
;	R2=LENGTH OF MESSAGE
;
; OUTPUTS:
;
;	NONE
;
; THIS ROUTINE PRINTS THE SPECIFIED MESSAGE ON THE SPECIFIED TERMINAL.
; ALL ERRORS THAT MIGHT RESULT ARE IGNORED. IN GENERAL, CLIS SHOULD
; DO ASYNCHRONOUS I/O WITH COMPLETION AST'S, AND PROVIDE A TIMEOUT
; FACILITY TO KILL THE I/O IF IT HASN'T COMPLETED IN A CERTAIN
; AMOUNT OF TIME IN ORDER TO PREVENT TERMINAL I/O FROM HOLDING UP
; COMMAND PROCESSING. THIS IS NOT DONE HERE FOR SIMPLICITY.
;
 
ISSMSG:	MOV	(R0),ALUN+A.LUNA  ;SET UP DEVICE NAME
	MOV	2(R0),ALUN+A.LUNU ;AND UNIT NUMBER
	DIR$	#ALUN		;ASSIGN LUN 5 TO THE SPECIFIED DEVICE
	BCS	10$		;IF CS, SKIP I/O
	MOV	R1,QIOW+Q.IOPL	;SET ADDRESS OF MESSAGE
	MOV	R2,QIOW+Q.IOPL+2 ;INSERT LENGTH OF MESSAGE
	DIR$	#QIOW		;DO I/O AND WAIT FOR IT
10$:	RETURN
 
	.END	START
-------------------------
	command file for cadcli

.xqt mac cadcli,cadcli=cadcli
set /cli=tt15:mcr
set /cli=tt23:mcr
cli /elim=cadcli
rem ...cad
.wait ...mac
tkb cadcli/pr:0,cadcli=cadcli,lb:[1,1]exelib/lb,lb:[1,54]rsx11m.stb/ss
pur cadcli.*
ins cadcli/cli=yes/task=...cad
cli /init=cadcli/lgo/task=...cad/dpr="<15><12>/*/"
-------------------------
-------------------------