QK-KERMIT: QUCS KERMIT FOR MS-DOS AND CP/M SYSTEMS

                                 VERSION: 2.5

          Kermit  is  a  protocol  for transferring files between com-
          puters over telecommunication lines.   It does  packetizing,
          checksumming,  and  retransmission to ensure data integrity.
          Microcomputer implementations of Kermit also provide  termi-
          nal  connection  at  any speed allowed by both the micro and
          the host.  Kermit is like many  other  such  protocols,  but
          with several differences:

             It's free.
             It's documented.
             It's well tested and in wide use.
             Implementations  exist  for  many different systems, in-
              cluding DEC and IBM mainframes and many  microcomputers.
              Each  implementation  is  written  in  the language best
              suited for a particular machine or operating system.

          Kermit was developed at the Columbia University  Center  for
          Computing Activities primarily to facilitate offline storage
          of  DECSYSTEM-20  files  on microcomputer floppy disks.  The
          Kermit specification has since served as the basis for  many
          implementations  of  Kermits  on  a wide variety of systems.
          Any Kermit can communicate with any other Kermit.

          Kermit does not rely on any host system software or servers.
          All actions are initiated explicitly by  the  user.    Typi-
          cally, the user:

             starts Kermit on a microcomputer,
             "connects" through Kermit to the remote host,
             logs on,
             starts Kermit on the remote host,
             "escapes" back to the micro,
             and  issues SEND and RECEIVE commands to send files back
              and forth between the two systems.

          Kermit can transfer files singly or in wildcard groups.

          QK-Kermit is a version of Kermit for MS-DOS and CP/M systems
          written at Queen's University in  Turbo-PASCAL.    The  CP/M
          versions  provide  ADM3A terminal emulation; the MS-DOS ver-
          sion emulates a VT-100 terminal.  When using the MS-DOS ver-
          sion with  Queen's  VM/CMS  system,  specify  terminal  type
          IBMPC.    For  the  KAYPRO  version,  specify  terminal type
          KAYPROK; for Apple IIe specify APPLE2E.



                                                                     1


KERMIT -----------------------------------------------------------------------|
        |-- Connect ----------------------|                                   |
        |             |-- <set options> --|                                   |
        |-- SENd <local-filespec> --------------------------------------------|
        |                           |-- AS <remote-filespec>------------------|
        |                                                     |-- RAW --|     |
        |-- RECeive <remote-filespec> ----------------------------------------|
        |                              |-- AS <local-filespec> ---------------|
        |                                                       |-- REPLACE --|
        |-- SET --------------------------------------------------------------|
        |        |-- <300|1200|2400|4800|9600> -----------|                   |
        |        |-- <Even|Odd|Mark|None> ----------------|                   |
        |        |-- <Full|Half> -------------------------|                   |
        |        |-- <STandard|Xon-xoff|SEries/1> --------|                   |
        |        |-- <A:|B:|C:|D:> -----------------------|                   |
        |        |-- <One|TWo> ---------------------------|                   |
        |        |-- <DIsk|PRinter> ----------------------|                   |
        |        |-- <PACketsize> ------------------------|
        |        |-- <TImeout> -----|                     |
        |        |-- <NUmpad> ------|                     |
        |        |-- <PAdchar> -----|                     |
        |        |-- <STartchar> ---|-- <decimal digit> --|
        |        |-- <ENdchar> -----|                     |
        |        |-- <CNtrlquote> --|                     |
        |        |                                        |
        |        |-- <BIt8quote> ---|-- <ASCII Char> -----|
        |        |-- <CHecktype> ---|
        |        |-- <Repchar> -----|
        |-- STatus -----------------------------------------------------------|
        |-- DIrectory --------------------------------------------------------|
        |               |-- <local-filespec> --|                              |
        |-- Erase <local-filespec> -------------------------------------------|
        |-- REName <local-filespec> <local-newfilespec> ----------------------|
        |-- TYpe <local-filespec> --------------------------------------------|
        |-- RUn <local-filespec> ---------------------------------------------|
        |-- MKdir -- <Directory name> ----------------------------------------|
        |-- CHdir -- <Directory name> ----------------------------------------|
        |-- RMdir -- <Directory name> ----------------------------------------|
        |-- REMote <any command supported by the remote Kermit> --------------|
        |-- Log --------------------------------------------------------------|
        |         |-- <filespec> --|                                          |
        |-- TAke <filespec> --------------------------------------------------|
        |-- DEfine -----------------------------------------------------------|
        |            |-- <define-word> ------------------------|              |
        |                                |-- <define-string> --|              |
        |-- Audio-------------------------------------------------------------|
        |-- Parms-------------------------------------------------------------|
        |-- Quit -------------------------------------------------------------|
                   |-- Local ---|
                   |-- Remote --|
                   |-- Discon --|
                   |-- All -----|


                                                           2


          QK-KERMIT COMMANDS

          The Kermit commands may be abbreviated to the minimum number
          of unique characters; i.e. CONNECT may be abbreviated  to  C
          and  STATUS  may be abbreviated to ST, but SET has no abbre-
          viation since there is a SEND command which also begins with
          SE.  Commands may be issued in a string as parameters to the
          Kermit startup  command  to  the  operating  system,  or  as
          internal commands once Kermit is running.

          All  parameter  specifications are optional.  If the command
          requires a parameter specification and one is not  supplied,
          then Kermit will prompt you for the required information.

          CONNECT < option settings>
                    This command causes the micro to simulate a termi-
                    nal  connected  to another computer.   This allows
                    one to sign on to the Host computer as a terminal.
                    The optional parameters specify the option setting
                    (See SET command for options).

                    To exit this terminal connect mode and  return  to
                    the Kermit command mode type in a CONTROL \ .

                    Note:  When  the connect command is issued, Kermit
                    checks the line for DTR and CTS signals and if  it
                    does  not  find  them  it assumes the modem is not
                    connected. It then issues a message

                                  'Please connect modem'

                    every few seconds until it finds the signal.    It
                    may  be,  however,  that  your particular computer
                    does not detect the presence of these signals even
                    when the modem is connected.  In this case we  can
                    by  pass the  signal checking by hitting the SPACE
                    bar on the keyboard.

          SEND <local-filename> AS <remote-filename> RAW
                    Sends a file to the remote host system.  Wild-card
                    characters  are  permitted to send multiple files.
                    Normally only the local filename is  specified  if
                    you  do not want a different file name on the host
                    system.

                    The RAW specification is only used if  the  remote
                    host  does  not have a Kermit, and we wish to send
                    the file as is (unpacketed).

                    For example:
                              SEND ABCD.FIL
                              SEND MYFILES.* AS YOURS.*
                              SEND A:WXYZ.DAT

                                                                     3


                    Several single-character  commands  may  be  given
                    while a file transfer is in progress:
                    ^Z  Stop  sending  this  file,  and don't send any
                        further files.
                    ^X  (Control-X) Stop sending the current file  and
                        go on to the next one, if any.
                    ^E  Like  ^C,  but send an Error packet to the re-
                        mote Kermit in an attempt to bring it back  to
                        server or interactive command level.
                    ^C  Return  to Kermit-MS command level immediately
                        without sending any kind  of  notification  to
                        the remote system.
                    Control-X  and  Control-Z send the proper protocol
                    messages to the remote Kermit to bring  it  grace-
                    fully  to the desired state.  Control-C leaves the
                    remote Kermit in whatever state it happens  to  be
                    in.   Control-E "aborts" any protocol that is tak-
                    ing place.

          RECEIVE <remote-filename> as <local-filename> REPLACE
                    Gets a file from the remote host system  and  puts
                    it  to  the destination device (usually the disk).
                    If the local-filename is not  specified  then  the
                    local filename is the same as the remote file name
                    with  the  remote  filetype  truncated  to 3 char-
                    acters.  If the local file name already exist  the
                    local  file name is modified with an '&'.  If how-
                    ever the REPLACE option is specified then the  old
                    file is replaced by the newly received file.

                    For example:
                              RECEIVE  MYPROG.PASCAL
                              REC      D:*.SCRIPT AS *.WS

                    Several  single-character  commands  may  be given
                    while a file transfer is in progress:
                    ^Z  Stop sending this file,  and  don't  send  any
                        further files.
                    ^X  (Control-X)  Stop sending the current file and
                        go on to the next one, if any.
                    ^E  Like ^C, but send an Error packet to  the  re-
                        mote  Kermit in an attempt to bring it back to
                        server or interactive command level.
                    ^C  Return to Kermit-MS command level  immediately
                        without  sending  any  kind of notification to
                        the remote system.
                    Control-X and Control-Z send the  proper  protocol
                    messages  to  the remote Kermit to bring it grace-
                    fully to the desired state.  Control-C leaves  the
                    remote  Kermit  in whatever state it happens to be
                    in.  Control-E "aborts" any protocol that is  tak-
                    ing place.


                                                                     4


          SET <option settings>
                    Set the various operational parameters.

                    Baud Rate      Baud  rate may be any standard rate
                                   from 300 to 9600 bps.  Normal maxi-
                                   mum baud rate for MS-DOS version is
                                   9600, and 2400 for CP/M systems.
                    Parity         May be Even, Odd,  Mark,  or  None.
                                   Use  even parity for Queen's VM/CMS
                                   system.
                                   Use parity none for VAX systems.
                    Duplex         May be Full or Half.  Use Full  du-
                                   plex if the remote system echos the
                                   characters,  Half duplex if it does
                                   not.
                    Protocol       May  be  STANDARD,   XON-XOFF,   or
                                   SERIES/1.    Use  SERIES/1 for port
                                   class VM (41), or VAX computers;
                                   use   XON-XOFF   for   port   class
                                   VMLINE(40 or 32);
                                   use  STANDARD  for  most other com-
                                   puters.
                    Disk Drive     Specify in the normal  MS-DOS  for-
                                   mat,  e.g. C:  The default drive is
                                   normally B:
                    Com Port       May be either One or Two.  Normally
                                   Port One is used.
                    Destination    May  be  either  DISK  or  PRINTER.
                                   Normally,  received files go to the
                                   disk, but they may be redirected to
                                   the printer.

          STATUS    This command show the current setting of the above
                    option settings.

          DIRECTORY display the local directory

          ERASE     erase a local file(s)

          RENAME    rename a local file(s)

          TYPE      display the contents of a local file

                    The above four commands are similar to the  MS-DOS
                    and  CP/M commands.   "Local" refers to the MS-DOS
                    or CP/M system which you are directly using.

          MKDIR     Makes a directory

          CHDIR     Changes the directory

          RMDIR     Removes a directory


                                                                     5


          (See MS-DOS Manual to see how to use the above  3  directory
          commands)

          RUN <file spec>
                    Run a program under Kermit. This is only available
                    on  the MS-DOS system and it is not implemented in
                    the CP/M systems.

          REMOTE <remote-commands>
                    Issue remote server request.   Although  QK-Kermit
                    is  able to issue all the remote server request as
                    documented in the Kermit standards, refer  to  the
                    Kermit  documentation  for  the  particular remote
                    version being used for supported commands.

                    Used as a remote Kermit, QK-Kermit  only  responds
                    to remote SEND and RECEIVE commands.

          LOG <logfile name>
                    This  command  causes  all incoming data to be re-
                    corded in a file as specified by the logfile name.
                    To close the current logfile  simply  reissue  the
                    LOG command. If no logfile name is specified, log-
                    ging  is  terminated.     If a new logfile name is
                    specified then the old logfile is closed and a new
                    logfile is opened.

          TAKE <takefilename>
                    This command enables a series of Kermit  commands,
                    which  are  stored in a file, to be executed.  For
                    example one might typically have to run  a  series
                    of  programs which create data which one wishes to
                    transfer to the other computer.

                              RUN PROG1
                              SEND DATA1.FIL
                              RUN PROG2
                              SEND DATA2.FIL
                              etc.

          DEFINE <define-word> <define-string>
                    This command enables one to define a word equal to
                    a string.   This  is  useful  in  alleviating  the
                    necessity  of typing in long command strings or it
                    can be used to provide a synonyms for  other  com-
                    mands.  For example:

                    DEFINE VM      CONNECT  9600 EVEN FULL SERIES/1 B:
                                   ONE DISK
                    DEFINE DELETE  ERASE
                    DEFINE BYE     QUIT ALL


                                                                     6


                    If no define-string is  specified,  the  specified
                    define-word  is deleted.  If DEFINE is issued with
                    no parameters, a list  of  all  define-words  cur-
                    rently in effect are displayed.

                    Note:    DEFINES are initialized from a file named
                    KERMIT.DEF when Kermit is initiated.   If any  new
                    DEFINES  are  specified during the Kermit session,
                    then at Kermit termination Kermit will attempt  to
                    write  a new Kermit.DEF file.  Note that the read-
                    ing and writing of this Kermit.DEF file is to  the
                    default  disk drive.  As a result, for new defines
                    to be created, the  default  disk  must  have  the
                    write-protect tab removed.

                    As  distributed,  the KERMIT.DEF file contains the
                    following define-words.

                    DEFINE-WORD    DEFINE-STRING
                    ___________    _____________
                    VM             Connect 9600 Even Full Series/1  B:
                                   One Disk
                    VM1200         Connect  1200 Even Full Series/1 B:
                                   One Disk
                    PC             Connect 9600 Even Full STANDARD  B:
                                   One Disk

          AUDIO     This  is a toggle command which when it is toggled
                    on will provide an audiable sound with each kermit
                    prompt.

          PARMS     This is a toggle command which when it is  toggled
                    on will display the setting of the packet parmeter
                    when a STATUS command is issued.

          QUIT <quit-option>
                    terminate the local and/or remote Kermit.

                    QUIT LOCAL or QUIT
                                   will terminate QK-Kermit.
                    QUIT REMOTE    will terminate the remote Kermit.
                    QUIT DISCON    will  terminate  the  remote Kermit
                                   and log off the  remote  host  com-
                                   puter.
                    QUIT ALL       will  terminate  the  remote Kermit
                                   and log off the  remote  host  com-
                                   puter and then terminates the local
                                   QK-Kermit.

          NOTE: "filespec" refers to a file specification in the form

                                   d:name.ext

          where 'd' is the disk drive designation, 'name' is the first
          level  file  name (the filename for CP/M, MS-DOS, and VM/CMS

                                                                     7


          systems), and 'ext' is the file  extension  (a  3  character
          extension  for  CP/M  or  MS-DOS  systems,  the  8 character
          filetype for VM/CMS systems).  If 'd:' is not specified, the
          default disk drive is assumed.

          APL CHARACTER SET

          For PC's equipped with the APL character ROM,  one  may  use
          the  APL character set.  To invoke APL character set send an
          ESC "{" sequence.  Use ESC "}" to return to normal Character
          set.















                                                                     8


          INSTALLING QK-KERMIT

          QK-Kermit may be obtained on diskette from the Micro  Infor-
          mation  Centre  in  Dupuis  Hall  or by downloading from the
          VM/CMS system using either another version  of  Kermit  sup-
          porting binary file transfer or YTERM.

          If you have the distribution diskette, simply copy the files

              KERMIT.COM
              KEYTABLE.DAT
              KERMIT.DEF

          to your working system disk.

          To  download  the  files from VM/CMS, first locate the files
          with the command

              LIST KERMIT COM* *

          and note the filemode of the disk (it will be  either  R  or
          Y).    There  are  three versions of the KERMIT.COM files on
          this disk.  They are as follows:

          KERMIT COMMSDOS        KERMIT.COM for MS-DOS
          KERMIT COMKAYPR        KERMIT.COM for Kaypro with CP/M
          KERMIT COMAPPLE        KERMIT.COM for  Apple  IIe  with  the
                                 CP/M card

          Download  the  appropriate Kermit file plus the KEYTABLE.DAT
          and KERMIT.DEF files to your system disk using either  YTERM
          or KERMIT.  Note that the KERMIT file MUST be downloaded us-
          ing a binary transfer facility (subcommand DOWNBIN in YTERM,
          SET  TRANSLATE  OFF in Kermit-CMS).  KEYTABLE DAT and KERMIT
          DEF must be downloaded as a normal file (subcommand DOWN  in
          YTERM, SET TRANSLATE ON in Kermit-CMS).







                                                                     9



          USING QK-KERMIT WITH KERMIT-CMS

          The  following  is  a suggested approach to do file transfer
          between a micro and the Queen's mainframe computer.

          Basic procedure:

          1.  Place the system disk created as above in  drive  A  and
              your data disk in drive B;
          2.  Type in "KERMIT" to start up QK-Kermit.
          3.  Type in "VM" which will configure Kermit at 9600 bps for
              the  VM/CMS system with files defaulting to the B: drive
              and place QK-Kermit into terminal mode.  The VM  command
              is  a define-word provided in the distributed KERMIT.DEF
              file.
          4.  Turn on the modem, and logon to  the  VM/CMS  system  as
              normal  using  terminal types IBMPC, KAYPROK  or APPLE2E
              as appropriate for the version of QK-Kermit that you are
              using.
          5.  After logging on, type "Kermit" on the VM/CMS system  to
              invoke  CMS-Kermit  and  issue the SERVER command.  This
              command will automatically return you  to  QK-Kermit  on
              the micro.
          6.  Issue  SEND or RECEIVE commands to send or get the files
              desired.
          7.  You may also wish to issue a DIRECTORY  command  to  see
              what  files  you  have on your floppy disk, or issue the
              REMOTE DIRECTORY command to list files on the  CMS  sys-
              tem.
          8.  If required, one can move back to terminal mode by issu-
              ing a "Connect" command to QK-Kermit.  When returning to
              back  to terminal mode from QK-Kermit command mode, with
              Kermit-CMS still in SERVER mode, the first  command  you
              issue  is not displayed.  Once the first command is exe-
              cuted, Kermit-CMS returns to normal mode  and  all  com-
              mands are displayed.
          9.  When  you  are finished you can issue a QUIT ALL command
              to logoff from the VM/CMS system and terminate your  re-
              mote Kermit.






                                                                    10



          SOME USEFUL HINTS:

          1.  Create  a  few  DEFINE  words for frequently used Kermit
              commands.  This will allow lengthy commands to be issued
              with a single word.  The following are some suggestions.

              DEFINE VM           Connect 9600 Even Full Series/1 B:
              DEFINE VMLINE       Connect 9600 Even Half Xon-Xoff B:
              DEFINE LIST         Remote Directory
              DEFINE PUSH         Run A:Command.Com
              DEFINE BYE          Set A: ; Quit All

              For example, using the VM define  above,  you  can  con-
              figure  Kermit  for  the  VM/CMS  system and be put into
              "connect" mode directly by simply issuing the command

                                     KERMIT VM

          2.  The Kermit protocol is designed to recover automatically
              from minor telecommunications  line  errors.    However,
              there are problems which may result in the file transfer
              being  "hung".  If Kermit hangs up in the middle of file
              transfer it may be necessary to issue  several  carriage
              returns  before  one  can  get  back  the  remote Kermit
              prompt.  It may occasionally be necessary to restart the
              remote and/or local Kermit after this.

          3.  In the above section describing  the  use  of  QK-Kermit
              with Kermit-CMS we basically issue QK-Kermit commands as
              opposed  to  Kermit-CMS  commands.   If desired, one can
              interact with Kermit-CMS by  issuing  SEND  and  RECEIVE
              commands from Kermit-CMS instead of from QK-Kermit.

          4.  QK-Kermit will act as a server Kermit whenever QK-Kermit
              is in the 'Connected ' mode; i.e. QK-Kermit does not re-
              quire  a  SERVER  command as does Kermit-CMS.  QK-Kermit
              will automatically assume  there  is  a  server  request
              whenever it see a SOH character.






                                                                    11



          KERMIT-CMS COMMANDS

          Although  Kermit-CMS  is  documented in a separate HELP file
          (type HELP KERMIT), the following summary of Kermit-CMS  re-
          mote  server commands is included for the convenience of the
          the QK-Kermit user.  Although QK-Kermit is able to issue all
          the remote server request as documented in the Kermit stand-
          ards, only   some have been implemented  on  the  Kermit-CMS
          system  here  at  Queen's.   Some of the useful commands are
          listed below.

REMOTE ---- DIRECTORY --------------------------------------------------------|
        |               |-- <remote-filespec> --|                             |
        |-- TYPE <remote-filespec> -------------------------------------------|
        |-- ERASE <remote-filespec> ------------------------------------------|
        |-- RENAME <remote-filespec> -----------------------------------------|
        |-- FINISH  ----------------------------------------------------------|
        |-- LOGOUT -----------------------------------------------------------|
        |-- HELP -------------------------------------------------------------|

where

          DIRECTORY      displays the VM/CMS directory
          TYPE           displays the contents of a VM/CMS file
          ERASE          erases a VM/CMS file
          RENAME         renames a VM/CMS file.  You will be  prompted
                         for the new filespec.
          FINISH         terminates Kermit-CMS
          LOGOUT         terminates  the  remote  Kermit  and  log off
                         VM/CMS
          HELP           displays help information








                                                                    12



          GENERAL COMMENTS

          QK-Kermit is written in Turbo Pascal  so  it  is  relatively
          easy  to  understand  and  modify if extensions are desired.
          The source code is distributed with the diskette.

          VERSION 2.5 IMPROVMENTS AND ADDITIONS

          1.  Automatic server mode.  QK-Kermit will automatically en-
              ter into server mode upon receipt of  a  SOH  character.
              This  feature was inadvertently disabled in the 2.4 ver-
              sion.

          2.  Insert Mode Indicator - When in insert mode  the  cursor
              changes from a thin line to a fat block.

          3.  Sub  directory  commands  -  MKDIR, CHDIR and RMDIR were
              added.  Also Kermit allows the use of subdirectories  in
              the file specification.

          4.  Audio  toggle  - Kermit will now run quietly without any
              audiable promp unless the audio toggle is turned on.

          5.  Packet parameters can now  be  specified  at  run  time.
              Note  however that QKKERMIT will still automatically ad-
              just the packet parameters to match the other Kermit  it
              connects with.

          6.  APL  character  set  can be selected by entering a ESC {
              character.

          7.  Fix bug-related to packet parameters when  running  with
              VAX Kermit.







                                                                    13


                   APPENDIX
                  -----------
              Code assignments for Keys specified by KEYTABLE.DAT.

              KEY                      ASCII     HEX
             -------                  -------   ------
              backspace                BS        08
              tab                      HT        09
              Return                   CR        0D

              F1                       ESC 1     1B 31
              F2                       ESC 2     1B 32
              F3                       ESC 3     1B 33
              F4                       ESC 4     1B 34
              F5                       ESC 5     1B 35
              F6                       ESC 6     1B 36
              F7                       ESC 7     1B 37
              F8                       ESC 8     1B 38
              F9                       ESC 9     1B 39
              F10                      ESC 0     1B 30
              NumLock                  ESC -     1B 2D
              ScrollLock               ESC =     1B 3D

              Shift F1                 ESC Q     1B 51
              Shift F2                 ESC W     1B 57
              Shift F3                 ESC E     1B 45
              Shift F4                 ESC R     1B 52
              Shift F5                 ESC T     1B 54
              Shift F6                 ESC Y     1B 59
              Shift F7                 ESC U     1B 55
              Shift F8                 ESC I     1B 49
              Shift F9                 ESC O     1B 4F
              Shift F10                ESC P     1B 50
              Shift NumLock            ESC [     1B 5B
              Shift ScrollLock         ESC \     1B 5C

              KeyPad  7   home         EM        19
              KeyPad  8   up arrow     US        1F
              KeyPad  9   PgUp         ESC 7     1B 37
              KeyPad  -   minus        VT        0B
              KeyPad  4   left arrow   BS        08
              KeyPad  5                ESC       1B
              KeyPad  6   right arrow  FS        1C
              KeyPad  +   plus         FF        0C
              KeyPad  1   end          SI        0F
              KeyPad  2   down arrow   LF        0A
              KeyPad  3   PgDn         ESC 8     1B 38
              KeyPad  0   Ins          GS        1D
              KeyPad  .   Del          DEL       7F

              Cntl \                   Escape back to Kermit
              Cntl ]                   Send a BREAK

              Alt   F09                Escape back to Kermit

                                                                    14


              Alt   F10                Send a BREAK



















                                                                    15



              QTEK10: A TEKTRONIX 4010 EMULATOR FOR ZENITH P.C.'S

          QTEK10  is  a  Tektronix  4010  emulator  designed to run on
          Zenith P.C.'s with a Zenith Graphics Card.  It is an  exten-
          sion to the file transfer facility Kermit, and all functions
          available  through  Kermit  are  available  through  QTEK10.
          These facilities  are  all  well  described  in  the  Kermit
          documentation.

          Five files are necessary for running QTEK10:

                        QTEK10.COM
                        4X6.FON
                        ERROR.MSG
                        KEYTABLE.DAT
                        KERMIT.DEF

          4X6.FON  and   ERROR.MSG   must  be available in the A drive
          when using QTEK10 to produce graphics output.

                                  USING QTEK10

             Boot your system and run QTEK10.  The Kermit prompt will
              be displayed.

             Enter the Kermit command CONNECT and press RETURN.   You
              will be prompted to turn on your modem.

             Turn on your modem, and press RETURN again.

             Log on to port class VM, specifying terminal type IBMPC.

          You may now run any  of  the  graphics  packages,  currently
          available  on  the IBM 3081, specifying the appropriate code
          for a device type of Tektronix 4010.   Graphics output  from
          these  programs will be displayed on your screen.   To clear
          the screen and continue on with the next graph, or to termi-
          nate your program, press the ENTER key.   You may  also  run
          any  non-graphics  programs  and  commands  as  you normally
          would.

          NOTE:  QTEK10 will not run with a monitor  level  less  than
          2.1.   Enter [CTRL ALT INS] to determine your monitor level.
          If it is less than 2.1, you must make arrangements  to  have
          it upgraded before running QTEK10.