MSKERMIT for the RMX Operating Systems


        INTRODUCTION

        MSKERMIT, the richest and most widely used implementation of KERMIT
        for  the small computer, has been ported  to iRMX86 and iRMX286.  A
        DOS emulator  provides enough of  the DOS environment  to allow the
        essentially unchanged  MSKERMIT code to  run under both  of the RMX
        Operating Systems.

        This document  discusses differences  between KERMIT  and MSKERMIT,
        where KERMIT  refers to the RMX version  and MSKERMIT refers to the
        DOS program.   Users unfamiliar  with MSKERMIT  may prefer  to read
        this in  conjunction  with  MSKERM.DOC.    KERMIT's  initialization
        command  file,   called  MSKERMIT.INI  in   MSKERM.DOC,  is  called
        KERMIT.INI  for RMX.   Wherever MSKERM.DOC refers  to the BACKSPACE
        key, the RUBOUT or DEL key is used in RMX.

        Directions  for installation and configuration  are included at the
        end of this document.


        FEATURES NOT IMPLEMENTED

        PUSH has  not been  implemented.   Unlike the  DOS implementations,
        there  is nothing that could  be done with PUSH  that can't be done
        with RUN.

        VT102 and Heath/Zenith-19 terminal emulation, as well as all of the
        SET TERMINAL  commands have not been implemented.   You can use the
        terminal of your choice and configure KERMIT to work with it.

        You  cannot transmit a break to the remote computer.  Although some
        serial  communication board's firmware supports sending breaks, the
        RMX Terminal Support Code does not.


        PATH AND FILE NAMES

        KERMIT will accept  any RMX path  or file name  with one exception.
        If  the right-most path  separator is ^,  it must be  followed by a
        redundant /.  For example: DIR ^/UNCLE.FILE and DIR ^UNCLE.FILE are
        the  same in RMX, but only the first will work in KERMIT.  MSKERMIT
        doesn't recognize ^ as a path separator, so we have to fool it.

        Wherever  KERMIT accepts a wild card  file specification, a list of
        file names may be used, as  long  as  they  are  all in the default
        directory.  For example:

        SEND READ.ME.FIRST,*X*.A*,*.OBJ,ETC.ETC

        works.  Try to say that in DOS.

        When KERMIT is in SERVER mode, operating as the "remote" KERMIT, it
        will respond to a GET file-name-list from the "local" KERMIT.

        KERMIT  will rename incoming files to match DOS naming rules.  It's
        still basically a DOS program.

        The command:
        SEND ,

        is an  extension to MSKERMIT that tells  KERMIT to send those files
        unsent from  the previous wild card batch.   If you are well into a
        SEND *,  when you lose your connection  to the remote computer, you
        can  "SEND ,", after you reestablish  your connection, and the SEND
        will be  resumed with the next file from  the wild card batch.  The
        interrupted file will have to be sent individually.


        USAGE NOTES

        The  KERMIT TYPE command is  the RMX COPY command.   The KERMIT DEL
        command  is the RMX DELETE command.  KERMIT will accept any RMX DIR
        command.  This applies to  SERVER  mode  response  to  REMOTE  DEL,
        REMOTE DIR, and REMOTE TYPE.  Examples:

        TYPE SAMPLE.FILE TO :LP:
        DEL * Q
        DIR $ FOR *.P86 L

        Continuation can be used with the RUN command.  For example:

                RUN ATTACHDEVICE T4 AS COM2 &
                RUN PHYSICAL

        is equivalent to:
                RUN ATTACHDEVICE T4 AS COM2 PHYSICAL

        If ^W  is used for a paging display  while in the command being RUN
        or in  DEL, DIR,  SPACE, or  TYPE, the  Terminal Support  Code will
        deadlock the system.

        SET DEFAULT-DISK will accomplish  nothing.    Use  the  KERMIT  CWD
        command  to change disk drives and/or directories.  The CWD command
        is not the  same as  the RMX  ATTACHFILE command.   Use  CWD :HOME:
        where  you would simply say ATTACHFILE.   Upon exit, KERMIT returns
        you to the same $ directory you were in when you called KERMIT.

        The  kermit action  verbs available  for SET  KEY are  \Kexit (exit
        connect   mode),  \Khelp  (connect  mode  help),  \Kstatus  (STATUS
        command), \Klogoff (suspend  logging),  \Klogon  (resume  logging),
        \Khangup  (HANGUP command), and \Knull (send the null character out
        the serial port).  These kermit action verbs are best bound to keys
        that send  characters in  the 80-0ffh  range or  control characters
        unused in your dialog with the remote computer.  The scan codes for
        keys whose codes are 80h through 0ffh are \X180 through \X1ff.

        While SET DESTINATION PRINTER  works, it  is very  slow.   The line
        printer driver  hogs  the  processor,  as  a  result,  simultaneous
        read/write/compute is not  possible.    It's  probably  quicker  to
        receive to disk and then copy to the printer.

        KERMIT is a  Human Interface  command.   When invoked  from another
        program,  it  should  be  by  sendcommand  rather  then  loadiojob.
        KERMIT's exit  status  is  returned  as  the  user  fault  code  of
        exitiojob  and is available as the command exception when KERMIT is
        invoked by sendcommand.  If non-zero, the high byte is 40h; the low
        byte   contains  the  values  mentioned   in  MSKERM.DOC,  with  an
        additional value of 0ffh meaning that KERMIT bombed gracefully.

        KERMIT has the appearance of being a CPU hog; the green light burns
        bright and steady.   Actually,  in the  default, KERMIT  has simply
        substituted itself for the idle task.

        KERMIT uses a scratch file  to  implement  wild  cards  and  REMOTE
        server commands  that return information.   Failure to exit KERMIT,
        such as hanging up in the Terminal Support Code or re-booting while
        in KERMIT, will  result  in  an  fnode  and  possibly  some  blocks
        becoming  allocated but unreferenced.  The  fnode and blocks can be
        freed using DISKVERIFY.


        SERIAL PORTS

        There  are ten serial  ports, 0 through  9.  Port  0 corresponds to
        :TERM:.   Port n, for n > 0,  corresponds to logical name :COMn: or
        :Tn:.  At startup, KERMIT looks for the first of ports 1 through 9.
        If none are found, a warning message is issued and port 0 is used.

        When  a port whose physical device name is the  same as :TERM:'s is
        selected, KERMIT changes the  display  mode  to  QUIET  to  prevent
        screen displays from conflicting with serial communication.  When a
        port  is selected that changes  from a one port  to two port state,
        the display mode is restored to its previous value.

        The RMX  Terminal Support Code hangs up  when a DTE configured port
        is active and you either plug or unplug the RS-232 cable.

        The RMX Terminal  Support  Code,  when  operating  with  unbuffered
        serial boards such as the 8251, can accept only a few characters at
        9600 baud before losing some.  KERMIT can send at 9600 baud through
        such boards, but receiving is limited to 4800 baud.  It can connect
        to a remote computer at 9600 baud, but will drop some characters if
        they  are sent faster than  fast typing speed.   There should be no
        baud rate problems up  to  19200  baud  with  buffered  serial  I/O
        boards, such as the 544 or 188/48.

        RMX86 R6 and RMX286 R1 Terminal Support Code Problems

        The Terminal  Support Code fails to wait  for I/O completion when a
        connection  is closed.   When  in SERVER  mode using  an unbuffered
        serial  board at lower baud rates,  the acknowledgement packet to a
        FINISH or BYE command from the Kermit at the other end gets chopped
        off  and the local  Kermit will report  a failure of  the FINISH or
        BYE.

        For  middle and higher baud  rates, 1200 and up  for the 86/30, the
        TSC doesn't  overlap read and  compute.  The  consequences are most
        noticeable  in connect mode, when nothing will appear on the screen
        until the either the remote host stops sending or is XOF'd.

        Serial I/O results in  system  clock  slow  down.    No,  it's  not
        relativity,  it's probably great yawning chasms of code enclosed in
        CLI/STI brackets in the TSC.

        To solve these problems, use a later release of RMX.


        SINGLE PORT OPERATION

        You  can use KERMIT  on a single  port system, if  you have another
        computer that you can connect directly to it.  For example, connect
        your RMX system to a PC's COM port in place of your terminal.  Call
        up KERMIT  on the PC, set  the baud rate to  match your RMX system,
        and connect  to it.  Use the PC as  the RMX terminal.  If there are
        no logical  names :COMn: and  :Tn:, where 0  < n <  10, KERMIT will
        automatically  select port 0 and change its default display mode to
        "quiet", which is necessary for one port operation.

        If your  system is an 8086 and you  want to receive files, SET BAUD
        4800 before  issuing the  SERVER command  (see above,  under serial
        ports).  The  baud rate change  won't take effect  until the SERVER
        command.

        After issuing  the SERVER command  escape back to  the PC's KERMIT,
        resetting it's baud rate,  if necessary,  and use  SEND or  GET for
        file  transfer.  When done, issue  the FINISH command, reconnect to
        KERMIT, and exit to the system.  The terminal's baud rate and other
        attributes will  be restored to their initial  values.  If you want
        to continue using the PC as a terminal, you may have to escape back
        to the PC to change its baud rate and reconnect.

        In one  port  operation,  KERMIT  refuses  to  CONNECT.    You  may
        alternate use of port  0 with  other ports  and KERMIT  will change
        display modes for you automatically.


        INSTALLATION

        KERMIT  and, if you  want to do  wild card sends,  the auxiliary WC
        command  should be copied to one of the default search directories.
        The logical  choice is :UTILS:, though they  both needn't be in the
        same  directory.  If all you have is the source for WC, WC.P86, its
        comment header  contains SUBMIT file contents  to make the command.
        The  WC command isn't otherwise totally  useless.  Try entering "WC
        ?able,movie*" as an alternative to "DIR $ FOR ?able,movie*".


        CONFIGURATION

        Configuration is optional.    The  configuration  file,  KERMIT.CFG
        (actually it's  '.CFG'  suffixed  to  whatever  you  call  KERMIT),
        follows the rules for KERMIT  TAKE  files  with  one  configuration
        command per line.   KERMIT  looks  for  KERMIT.CFG  first  in  your
        default directory, $.  If not found, it looks in the directory from
        which  KERMIT was loaded.  Suppose you install KERMIT by copying it
        to :UTILS:TOAD.  The search  would  be,  first  :$:TOAD.CFG,  then,
        :UTILS:TOAD.CFG.   A system  requiring configuration  for different
        brand  terminals or for  different remote hosts  can configure them
        all by using a different default directory for each.

        In  the following configuration command descriptions, upper case is
        used for literal keywords,  n refers  to a  decimal number,  and \n
        refers to a number in KERMIT backslash notation, i.e.  '\' followed
        by an optional  case  insensitive  radix  letter  followed  by  the
        number.   Radix letters are D for decimal, X for hexadecimal, and O
        for octal.  If omitted, the radix defaults to decimal.

        OSC string

        OSC is  used  to  configure  KERMIT  to  your  terminal  using  OSC
        sequences  (see RMX86 Release 6 or RMX286  Release 1, BIOS App.  F;
        or RMX86 Release 7 or  RMX286  Release  2,  Device  Drivers  User's
        Guide, Section  2.3).  If your terminal is  set to send space or no
        parity and is VT100  compatible or  you use  SET DISPLAY  SERIAL or
        QUIET, it is unnecessary.

        First you must decide  if  the  regular  screen  formatted  display
        during file  transfers is what you want.   The RMX Terminal Support
        Code is  reluctant to permit transparent  input when translation is
        enabled.  As  a consequence, you  have the choice  between a decent
        screen format during file transfer, or a fully functional keyboard.
        When  you choose  the acceptable  screen format,  RMX holds  up the
        escape key for one extra keystroke, and if ^E, ^X, or ^Z are needed
        for terminal configuration (several  terminals  use  ^Z  for  clear
        screen), they  won't work as  escapes during file  transfer.  Also,
        file  transfer is quicker with  a SERIAL or QUIET  display.  On the
        other hand, opting  for the  keyboard results  in a  hideous screen
        during file transfer, unless you SET DISPLAY SERIAL or QUIET.

        The  string is a valid and complete  OSC sequence WITHOUT the ESC [
        lead-in  or ESC \  terminator.  Any  number of OSC  commands may be
        used as long as each is complete and independent.

        If  your terminal sends even, odd, or mark parity, include T:R=0 in
        your  OSC to strip  parity from terminal  input.  In  this case you
        will  not be able to  use SET KEY for  characters greater than 7fh,
        but then, you couldn't anyway.

        The  following example  illustrates an  OSC command  sufficient for
        KERMIT  screen displays.  It configures KERMIT for the Qume QVT102,
        Televideo 910 Plus, 912, 920, 925, & 950, and Zentec Zephyr & Cobra
        terminals.  Let's look at it to see how OSC configuration works.

        OSC T:T=1,F=1,U=32,E6=93,E30=75,E31=116

        T=1     enables translation
        F=1     vertical cursor coordinate precedes horizontal
        U=32    value for cursor row or column 1.  32 is the code for space
        E6=93   translate cursor positioning to ESC =
        E30=75  translate clear screen to ESC +
        E31=116 translate clear to end of line to ESC T

        Referring to  the manual for your terminal  and BIOS Tables F-4 and
        F-5 or DD Tables  2-3  and  2-4,  edit  the  above  to  match  your
        terminal.

        TRANSLATE

        By default, KERMIT disables TSC translation when you connect to the
        remote  computer.  The TRANSLATE command enables TSC translation in
        connect mode.  It's possible to make your non-VT100 terminal behave
        like a VT100 if  your mainframe's  screen editor  uses a  subset of
        VT100 escapes that the TSC can translate or simulate.

        ESCC

        The  ESCC command causes KERMIT to send  an ESC c, the VT100 reset,
        to your  terminal on exit.  You may want  to use this if you have a
        VT100 compatible terminal  or if  you are  unjustifiably optimistic
        about the Terminal Support Code.    It's  use  has  been  known  to
        deadlock Release 6 when TSC translation is enabled.

        ECHO ON or OFF

        ECHO ON causes subsequent CFG  commands  and  TAKE  file  commands,
        including  those from KERMIT.INI, to be  displayed.  This is useful
        for associating cryptic CFG error messages with the offending line.
        ECHO OFF stops CFG and TAKE file echoing.

        BUFILL \n

        KERMIT's  serial input is  content paced against  a background fill
        whose  default value  is 0ffh.   Use  BUFILL to  change it  if your
        remote computer  can send 0ffh.  Values  to try include \X7f, \X80,
        and \0.   If  none of  these work,  you'll have  to find  a control
        character  never used by the remote computer.  The maximum value is
        255.

        CIFILL \n

        Terminal input is content paced against an 80h background.  If your
        terminal sends  80h, use  CIFILL to  change the  default.   See the
        paragraph above for suggested values.

        PRIORITY \n

        By default, KERMIT sets its  priority  to  254  to  guarantee  more
        (numerically  lower) priority for  its I/O tasks  regardless of how
        the system it's running on has been ICU'd.  This permits it to stay
        out  of the way in multi-user  systems and in background operation.
        The maximum value is  254.   If KERMIT  is included  in round-robin
        sheduling, it will use its full time slice.

        SUB-PACK n

        This  parameter tunes performance  for file sending.   Send packets
        are sent in bursts  of  default  size  60.    This  optimizes  send
        performance for an  86/30  at  19.6  KB  with  1000  byte  packets.
        Decreasing its value  increases RMX  overhead, while  increasing it
        reduces write/compute overlap.  Factors effecting the optimal value
        include the CPU  board, clock rate,  baud rate, and  packet size as
        well as the performance of  the  remote  host.    The  transmission
        time/sub-packet size function has a broad minimum.

        CO-DELAY n

        This parameter tunes connect  mode  performance.    Output  to  the
        terminal is allowed  to accumulate  and is  written every  n system
        clock  ticks.  The default value is 6, nominally 60 ms.  Increasing
        the value improves connect  mode  performance  at  the  expense  of
        herky-jerk terminal output.

        DTR-TIME n

        The duration, in milli-seconds, that DTR is held down by the HANGUP
        command.  The default is 500.

        For  the HANGUP command to work, all of the following must be true.
        The  port must  be configured  DTE, the  serial board  must support
        modem control, and the system  must  have  been  ICU'd  with  modem
        control enabled for the DTE port(s).  A null-modem cable with a DCE
        port will not permit DTR control.

        KILL \n

        Creates a  "kill KERMIT"  task associated  with the  terminal input
        character  specified by  the parameter,  usually an  unused control
        character.  Useful for developers, incorporators, and anyone trying
        to  figure out how to  connect a DTE port  to their remote computer
        for the first time.  This  will  not  solve  the  ^W  inspired  TSC
        deadlock.   Only killing the job from another terminal or warm boot
        will do.